## Slide 1
Jinfan Chen, Juan Gómez Luna, Izzat El Hajj, Yuxin Guo, Onur Mutlu
SimplePIM:
A Software Framework for Productive and Efficient Processing-in-Memory
https://arxiv.org/pdf/2310.01893.pdf
https://github.com/CMU-SAFARI/SimplePIM
juang@ethz.ch
2023 International Conference on Parallel Architectures and Compilation Techniques
Monday, October 23, 2023

## Slide 2: Executive Summary
Processing-in-Memory (PIM) promises to alleviate the data movement bottleneck
Real PIM hardware is now available, e.g., UPMEM PIM
However, programming real PIM hardware is challenging, e.g.:
  Distribute data across PIM memory banks,
  Manage data transfers between host cores and PIM cores, and between PIM cores,
  Launch PIM kernels on the PIM cores, etc.
SimplePIM is a high-level programming framework for real PIM hardware
  Iterators such as map, reduce, and zip
  Collective communication with broadcast, scatter, and gather
Implementation on UPMEM and evaluation with six different workloads
  Reduction, vector add, histogram, linear/logistic regression, K-means
  4.4x fewer lines of code compared to hand-optimized code
  Between 15% and 43% faster than hand-optimized code for three workloads
Source code: https://github.com/CMU-SAFARI/SimplePIM

## Slide 3: Outline
Processing-in-memory
and PIM programming
SimplePIM:
A high-level programming framework for processing-in-memory
Evaluation

## Slide 4: Processing-in-Memory (PIM)
PIM is a computing paradigm that advocates for memory-centric computing systems, where processing elements are placed near or inside the memory arrays
Real-world PIM architectures are becoming a reality
  UPMEM PIM, Samsung HBM-PIM, Samsung AxDIMM, SK Hynix AiM, Alibaba HB-PNM
These PIM systems have some common characteristics:
  There is a host processor (CPU or GPU) with access to (1) standard main memory, and (2) PIM-enabled memory
  PIM-enabled memory contains multiple PIM processing elements (PEs) with high bandwidth and low latency memory access
  PIM PEs run only at a few hundred MHz and have a small number of registers and small (or no) cache/scratchpad
  PIM PEs may need to communicate via the host processor

## Slide 5: A State-of-the-Art PIM System
In our work, we use the UPMEM PIM architecture
  General-purpose processing cores called DRAM Processing Units (DPUs)
    Up to 24 PIM threads, called tasklets
    32-bit integer arithmetic, but multiplication/division are emulated*, as well as floating-point operations
  64-MB DRAM bank (MRAM), 64-KB scratchpad (WRAM)
* 8-bit integer multiplication is natively supported

## Slide 6: Programming a PIM System (I)
Example: Hand-optimized histogram with UPMEM SDK
... // Initialize global variables and functions for histogram
int main_kernel() {
if (tasklet_id == 0)
mem_reset(); // Reset the heap
... // Initialize variables and the histogram
T *input_buff_A = (T*)mem_alloc(2048); // Allocate buffer in scratchpad memory
for (unsigned int byte_index = base_tasklet; byte_index < input_size; byte_index += stride) {
// Boundary checking
uint32_t l_size_bytes = (byte_index + 2048 >= input_size) ? (input_size - byte_index) : 2048;
// Load scratchpad with a DRAM block
mram_read((const __mram_ptr void*)(mram_base_addr_A + byte_index), input_buff_A, l_size_bytes);
// Histogram calculation
histogram(hist, bins, input_buff_A, l_size_bytes/sizeof(uint32_t));
}
...
barrier_wait(&my_barrier); // Barrier to synchronize PIM threads
... // Merging histograms from different tasklets into one histo_dpu
// Write result from scratchpad to DRAM
if (tasklet_id == 0)
if (bins * sizeof(uint32_t) <= 2048)
mram_write(histo_dpu, (__mram_ptr void*)mram_base_addr_histo, bins * sizeof(uint32_t));
else
for (unsigned int offset = 0; offset < ((bins * sizeof(uint32_t)) >> 11); offset++) {
mram_write(histo_dpu + (offset << 9), (__mram_ptr void*)(mram_base_addr_histo +
(offset << 11)), 2048);
}
return 0;
}

## Slide 7: Programming a PIM System (II)
PIM programming is challenging
  Manage data movement between host DRAM and PIM DRAM
    Parallel, serial, broadcast, and gather/scatter transfers
  Manage data movement between PIM DRAM bank and scratchpad
    8-byte aligned and maximum of 2,048 bytes
  Multithreaded programming model
  Inter-thread synchronization
    Barriers, handshakes, mutexes, and semaphores
Our Goal
Design a high-level programming framework that abstracts these hardware-specific complexities and provides a clean yet powerful interface for ease of use and high program performance

## Slide 8: Outline
Processing-in-memory
and PIM programming
SimplePIM:
A high-level programming framework for processing-in-memory
Evaluation

## Slide 9: The SimplePIM Programming Framework
SimplePIM provides standard abstractions to build and deploy applications on PIM systems
  Management interface
    Metadata for PIM-resident arrays
  Communication interface
    Abstractions for host-PIM and PIM-PIM communication
  Processing interface
    Iterators (map, reduce, zip) to implement workloads

## Slide 10: Management Interface
Metadata for PIM-resident arrays
  array_meta_data_t describes a PIM-resident array
  simple_pim_management_t for managing PIM-resident arrays
lookup: Retrieves all relevant information of an array
register: Registers the metadata of an array
free: Removes the metadata of an array
void simple_pim_array_free(const char* id, simple_pim_management_t* management);
array_meta_data_t* simple_pim_array_lookup(const char* id,
simple_pim_management_t* management);
void simple_pim_array_register(array_meta_data_t* meta_data,
simple_pim_management_t* management);

## Slide 11: The SimplePIM Programming Framework
SimplePIM provides standard abstractions to build and deploy applications on PIM systems
  Management interface
    Metadata for PIM-resident arrays
  Communication interface
    Abstractions for host-PIM and PIM-PIM communication
  Processing interface
    Iterators (map, reduce, zip) to implement workloads

## Slide 12: Host-to-PIM Communication: Broadcast
SimplePIM Broadcast
  Transfers a host array to all PIM cores in the system
void simple_pim_array_broadcast(char* const id, void* arr, uint64_t len,
uint32_t type_size, simple_pim_management_t* management);

## Slide 13: Host-to-PIM Communication: Scatter/Gather
SimplePIM Scatter
  Distributes an array to PIM DRAM banks
SimplePIM Gather
  Collects portions of an array from PIM DRAM banks
void* simple_pim_array_gather(char* const id, simple_pim_management_t* management);
void simple_pim_array_scatter(char* const id, void* arr, uint64_t len,
uint32_t type_size, simple_pim_management_t* management);

## Slide 14: PIM-PIM Communication: AllReduce
SimplePIM AllReduce
  Used for algorithm synchronization
  The programmer specifies an accumulative function
void simple_pim_array_allreduce(char* const id, handle_t* handle,
simple_pim_management_t* management);

## Slide 15: PIM-PIM Communication: AllGather
SimplePIM AllGather
  Combines array pieces and distributes the complete array to all PIM cores
void simple_pim_array_allgather(char* const id, char* new_id,
simple_pim_management_t* management);

## Slide 16: The SimplePIM Programming Framework
SimplePIM provides standard abstractions to build and deploy applications on PIM systems
  Management interface
    Metadata for PIM-resident arrays
  Communication interface
    Abstractions for host-PIM and PIM-PIM communication
  Processing interface
    Iterators (map, reduce, zip) to implement workloads

## Slide 17: Processing Interface: Map
Array Map
  Applies map_func to every element of the data array
void simple_pim_array_map(const char* src_id, const char* dest_id,
uint32_t output_type, handle_t* handle, simple_pim_management_t* management);

## Slide 18: Processing Interface: Reduction
Array Reduction
  The map_to_val_func function transforms an input element to an output value and an output index
  The acc_func function accumulates the output values onto the output array
void simple_pim_array_red(const char* src_id, const char* dest_id,
uint32_t output_type, uint32_t output_len, handle_t* handle,
simple_pim_management_t* management);

## Slide 19: Processing Interface: Zip
Array Zip
  Takes two input arrays and combines their elements into an output array
void simple_pim_array_zip(const char* src1_id, const char* src2_id,
const char* dest_id, simple_pim_management_t* management);

## Slide 20: SimplePIM’s UPMEM Implementation
Communication interface
  SimplePIM automatically handles alignment requirements and inserts padding as needed
Processing interface
  Array map
    Invokes PIM cores and PIM threads, and handles PIM DRAM-scratchpad transfers
  Array reduction
    Shared accumulator reduction
    Thread-private accumulator reduction
  Array zip
    Lazy approach to minimize data copying

## Slide 21: General Code Optimizations
Strength reduction
Loop unrolling
Avoiding boundary checks
Function inlining
Adjustment of data transfer sizes

## Slide 22: More in the Paper
Strength reduction
Loop unrolling
Avoiding boundary checks
Function inlining
Adjustment of data transfer sizes
https://arxiv.org/pdf/2310.01893.pdf

## Slide 23: Outline
Processing-in-memory
and PIM programming
SimplePIM:
A high-level programming framework for processing-in-memory
Evaluation

## Slide 24: Evaluation Methodology
Evaluated system
  UPMEM PIM system with 2,432 PIM cores with 159 GB of PIM DRAM
Real-world Benchmarks
  Vector addition
  Reduction
  Histogram
  K-Means
  Linear regression
  Logistic regression
Comparison to hand-optimized codes in terms of programming productivity and performance

## Slide 25: Productivity Improvement (I)
Example: Hand-optimized histogram with UPMEM SDK
... // Initialize global variables and functions for histogram
int main_kernel() {
if (tasklet_id == 0)
mem_reset(); // Reset the heap
... // Initialize variables and the histogram
T *input_buff_A = (T*)mem_alloc(2048); // Allocate buffer in scratchpad memory
for (unsigned int byte_index = base_tasklet; byte_index < input_size; byte_index += stride) {
// Boundary checking
uint32_t l_size_bytes = (byte_index + 2048 >= input_size) ? (input_size - byte_index) : 2048;
// Load scratchpad with a DRAM block
mram_read((const __mram_ptr void*)(mram_base_addr_A + byte_index), input_buff_A, l_size_bytes);
// Histogram calculation
histogram(hist, bins, input_buff_A, l_size_bytes/sizeof(uint32_t));
}
...
barrier_wait(&my_barrier); // Barrier to synchronize PIM threads
... // Merging histograms from different tasklets into one histo_dpu
// Write result from scratchpad to DRAM
if (tasklet_id == 0)
if (bins * sizeof(uint32_t) <= 2048)
mram_write(histo_dpu, (__mram_ptr void*)mram_base_addr_histo, bins * sizeof(uint32_t));
else
for (unsigned int offset = 0; offset < ((bins * sizeof(uint32_t)) >> 11); offset++) {
mram_write(histo_dpu + (offset << 9), (__mram_ptr void*)(mram_base_addr_histo +
(offset << 11)), 2048);
}
return 0;
}

## Slide 26: Productivity Improvement (II)
Example: SimplePIM histogram
// Programmer-defined functions in the file "histo_filepath"
void init_func (uint32_t size, void* ptr) {
char* casted_value_ptr = (char*) ptr;
for (int i = 0; i < size; i++)
casted_value_ptr[i] = 0;
}
void acc_func (void* dest, void* src) {
*(uint32_t*)dest += *(uint32_t*)src;
}
void map_to_val_func (void* input, void* output, uint32_t* key) {
uint32_t d = *((uint32_t*)input);
*(uint32_t*)output = 1;
*key = d * bins >> 12;
}
// Host side handle creation and iterator call
handle_t* handle = simple_pim_create_handle("histo_filepath", REDUCE, NULL, 0);
// Transfer (scatter) data to PIM, register as "t1"
simple_pim_array_scatter("t1", src, bins, sizeof(T), management);
// Run histogram on "t1" and produce "t2"
simple_pim_array_red("t1", "t2", sizeof(T), bins, handle, management);

## Slide 27: Productivity Improvement (III)
Lines of code (LoC) reduction
 | SimplePIM | Hand-optimized | LoC Reduction
Reduction | 14 | 83 | 5.93×
Vector Addition | 14 | 82 | 5.86×
Histogram | 21 | 114 | 5.43×
Linear Regression | 48 | 157 | 3.27×
Logistic Regression | 59 | 176 | 2.98×
K-Means | 68 | 206 | 3.03×
SimplePIM reduces the number of lines of effective code
by a factor of 2.98× to 5.93×

## Slide 28: Performance Evaluation (I)
Weak scaling analysis
SimplePIM achieves comparable performance for reduction, histogram, and linear regression
SimplePIM outperforms hand-optimized implementations for vector addition, logistic regression,
and k-means by 10%-37%

## Slide 29: Performance Evaluation (II)
Strong scaling analysis
SimplePIM scales better than hand-optimized implementations for reduction, histogram, and linear regression
SimplePIM outperforms hand-optimized implementations for vector addition, logistic regression,
and k-means by 15%-43%

## Slide 30: Variants of Array Reduction
Shared accumulator version versus thread-private version for histogram
The thread-private version is up to 70% faster than the shared accumulator version for histograms of 256-1024 bins
The number of active PIM threads of the thread-private version reduces after 1024 bins due to limited scratchpad size

## Slide 31: Discussion
SimplePIM is devised for PIM architectures with
  A host processor with access to standard main memory and PIM-enabled memory
  PIM processing elements (PEs) that communicate via the host processor
  The number of PIM PEs scales with memory capacity
SimplePIM emulates the communication between PIM cores via the host processor
Other parallel patterns can be incorporated in future work
  Prefix sum and filter can be easily added
  Stencil and convolution would require fine-grained scatter-gather for halo cells
  Random access patterns would be hard to support

## Slide 32: SimplePIM: arXiv Version
https://arxiv.org/pdf/2310.01893.pdf

## Slide 33: Source Code
https://github.com/CMU-SAFARI/SimplePIM

## Slide 34: Executive Summary
Processing-in-Memory (PIM) promises to alleviate the data movement bottleneck
Real PIM hardware is now available, e.g., UPMEM PIM
However, programming real PIM hardware is challenging, e.g.:
  Distribute data across PIM memory banks,
  Manage data transfers between host cores and PIM cores, and between PIM cores,
  Launch PIM kernels on the PIM cores, etc.
SimplePIM is a high-level programming framework for real PIM hardware
  Iterators such as map, reduce, and zip
  Collective communication with broadcast, scatter, and gather
Implementation on UPMEM and evaluation with six different workloads
  Reduction, vector add, histogram, linear/logistic regression, K-means
  4.4x fewer lines of code compared to hand-optimized code
  Between 15% and 43% faster than hand-optimized code for three workloads
Source code: https://github.com/CMU-SAFARI/SimplePIM

## Slide 35: Real PIM Tutorial (MICRO 2023)
October 29th: Lectures + Hands-on labs + Invited lectures
https://events.safari.ethz.ch/micro-pim-tutorial/doku.php?id=start
https://youtube.com/live/ohU00NSIxOI?feature=share

## Slide 36: PIM Review and Open Problems
Onur Mutlu, Saugata Ghose, Juan Gomez-Luna, and Rachata Ausavarungnirun, "A Modern Primer on Processing in Memory" Invited Book Chapter in Emerging Computing: From Devices to Systems - Looking Beyond Moore and Von Neumann, Springer, 2023
https://arxiv.org/pdf/1903.03988.pdf

## Slide 37
Jinfan Chen, Juan Gómez Luna, Izzat El Hajj, Yuxin Guo, Onur Mutlu
SimplePIM:
A Software Framework for Productive and Efficient Processing-in-Memory
https://arxiv.org/pdf/2310.01893.pdf
https://github.com/CMU-SAFARI/SimplePIM
juang@ethz.ch
2023 International Conference on Parallel Architectures and Compilation Techniques
Monday, October 23, 2023