## Slide 1: Slim NoC: A Low-Diameter On-Chip Network Topology for High Energy Efficiency and Scalability
Maciej Besta, Syed Minhaj Hassan, Sudhakar Yalamanchili, Rachata Ausavarungnirun, Onur Mutlu, Torsten Hoefler

## Slide 2: Massively Parallel Manycores
SW26010: 260 cores
PEZY-SC2: 2048 cores
Adapteva Epiphany: 1024 cores
?
...
Notes: Can I call a network` ’efficient’ ??
- can I add ‘using thorough mathematical optimization’ ??

## Slide 3: Networks in Compute Clusters
Notes: Can I call a network` ’efficient’ ??
- can I add ‘using thorough mathematical optimization’ ??

## Slide 4: Dragonfly, Slim Fly
diameter = 4
Fat tree [1]
Dragonfly [2]
TSUBAME2.0
Cray Cascade
diameter = 3
Slim Fly [3] based on the Hoffman-Singleton Graph [4]:
diameter = 2
> ~50% fewer routers than Fat tree
> ~30% fewer cables than Fat tree
[1] C. E. Leiserson. Fat-trees: Universal Networks for Hardware-Efficient Supercomputing. IEEE Transactions on Computers. 1985.
[2] J. Kim et al. Technology-Driven, Highly-Scalable Dragonfly Topology. ISCA’08.
[3] M. Besta and T. Hoefler. Slim Fly: A Cost Effective Low-Diameter Network Topology. SC14.
[4] A. J. Hoffman and R. R. Singleton. Moore graphs with diameter 2 and 3, IBM Journal of Research and Development. 1960.
Notes: Can I call a network` ’efficient’ ??
- can I add ‘using thorough mathematical optimization’ ??

## Slide 5: Inspiration: Diameter-2 Slim Fly
Key idea:
  Lower diameter and thus average path length: fewer needed links / routers.
routers
endpoints
Key method
Optimize towards the Moore Bound [1]: the upper bound on the number of vertices in a graph with given diameter D and radix k.
Thus, Slim Fly ensures the lowest radix (port count) for a given node count and for a fixed diameter... Sounds ideal for an on-chip setting?
[1] M. Miller, J. Siráň. Moore graphs and beyond: A survey of the degree/diameter problem, Electronic Journal of Combinatorics, 2005.
Notes: Can I call a network` ’efficient’ ??
- can I add ‘using thorough mathematical optimization’ ??

## Slide 6: Why not just use Slim Fly as an on-chip network?
Notes: What does “fewer groups/router” mean?
[fixed]

## Slide 7: Slim Fly on Chip – First Attempt
Example design for diameter = 2
A subgraph with
identical groups of routers
A subgraph with
identical groups of routers
Structure Intuition
Notes: What does “fewer groups/router” mean?
[fixed]

## Slide 8: Slim Fly on Chip – First Attempt
Groups form a fully-connected bipartite graph
Structure Intuition
Notes: What does “fewer groups/router” mean?
[fixed]

## Slide 9: Slim Fly on Chip – First Attempt
variant 1, variant 2
Flatt. Butterfly [1]
2D torus
Conc. mesh
Slim Fly on chip
Dragonfly on chip
variant 1, variant 2
Flatt. Butterfly [1]
2D torus
Conc. mesh
Slim Fly on chip
Dragonfly on chip
So how does it Fare?
Bad! No clear advantages from a topology that is close-to-optimal in the radix-size-diameter tradeoff
Why?
[1] J. Kim, W. J. Dally, D. Abts. Flattened butterfly: a cost-efficient topology for high-radix networks. ISCA’07

## Slide 10
What are the problems with the simple on-chip Slim Fly?

## Slide 12: Problems with Simple On-Chip Slim Fly, Part 1
Near-best radix-size-diameter tradeoff, but...
Long wire: traversing the whole die requires large input buffers for full link utilization
Short wire: small input buffers

## Slide 13: Problems with Simple On-Chip Slim Fly, Part 2
…number of nodes/routers being a power of two?
…equally many cores on each die side?
…equally many routers on each die side?
…equally many router groups on each die side?
There are few Slim Flies that satisfy various on-chip technological constraints
No need to pay attention to all these numbers 
Various Slim Fly configurations
Are there
configurations with…

## Slide 14
How to solve these problems?

## Slide 15: Solution: Slim NoC
Near-best radix-size-diameter tradeoff, but...
Long wire: traversing the whole die requires large input buffers for full link utilization
The model must be generic
to allow for arbitrary layouts.
Different mappings (“sets of arrows”) enable different layouts
Short wire: small input buffers
New cost and area models, new layouts
Part I

## Slide 16: Solution: Slim NoC
New cost and area models, new layouts
How to select a mapping?
Minimize the average wire length (M) :
Minimize the total buffer area (Δ):
ILP formulation: many more details for reproducibility and genericness, check the paper 
Part I

## Slide 17: Solution: Slim NoC
Let us see some layouts
New cost and area models, new layouts
What difference do they make for lengths of wires?
Part I

## Slide 18: Solution: Slim NoC
New cost and area models, new layouts
Let us see some layouts
What difference do they make for lengths of wires?
The “subgroup layout” (sn_subgr) is best for 200 nodes
The “group layout” (sn_gr) is best for 1296 nodes (it reduces wiring complexity)
Part I
Average wire length
sn_subgr

## Slide 19: Solution: Slim NoC
New cost and area models, new layouts
Let us see some layouts
What difference do they make for lengths of wires?
The “group layout” (sn_gr) is best for 1296 nodes The “subgroup layout” (sn_subgr) is best for 200 nodes
Part I

## Slide 20
Now let’s move to the second problem...

## Slide 21: Solution: Slim NoC
Are there
configurations with…
Non-Prime Finite Fields
…number of nodes/routers being a power of two?
…equally many cores on each die side?
…equally many routers on each die side?
…equally many router groups on each die side?
There are few Slim Flies that satisfy various on-chip technological constraints
Various Slim Fly configurations
Part II
How to develop such a finite field?
No need to pay attention to all these numbers 

## Slide 22: Solution: Slim NoC
Recap: a finite field
Assuming q is prime:
(with modular arithmetic).
Example:
50 routers
Assuming q is non-prime:
...with instruction tables that define operations on the field.
Example:
162 routers
How to develop such a finite field?
Non-Prime Finite Fields
Addition
Multiplication
Inverse
Check the paper for details 

## Slide 23
How do we optimize the router microarchitecture for Slim NoC
to provide high performance and high efficiency?

## Slide 24
Enhancement 1: Elastic Buffer links [1] + ElastiStore [2]
[1] G. Michelogiannakis et al. Elastic-Buffer Flow Control for On-Chip Networks. HPCA’09.
[2] I. Seitanidis et al. ElastiStore: An Elastic Buffer Architecture for Network-on-Chip Routers. DATE’14.
[3] C.-H. O. Chen et al. SMART: A Single-Cycle Reconfigurable NoC for SoC Applications. DATE’13.
[4] S. Hassan and S. Yalamanchili. Centralized Buffer Router: A Low Latency, Low Power Router for High Radix NoCs. NOCS’13.
Enhancement 2: SMART Links [3]
Slim NoC Router Microarchitecture Performance Optimizations
...
Provide deadlock-freedom
Drive links asynchronously and use repeaters
for single-cycle wires
Enhancement 3: Central Buffers [4]
Replace multi-flit input buffers with single-flit stating input buffers and add a central buffer
Let’s leave the details for the paper and just focus on the core aspects 
Part III
Notes: - Introduce cost model

## Slide 25
Let’s Summarize…
Notes: - Introduce cost model

## Slide 26: Evaluation

## Slide 27: Evaluation Methodology: Sensitivity Analyses
Topology:
Metrics:
Latency
Throughput
Buffer area
Buffer size
Static/dynamic power consumption
Throughput/power
Energy-delay product
[1] J. Kim, W. J. Dally, D. Abts. Flattened butterfly: a cost-efficient topology for high-radix networks. ISCA’07
Concentrated Mesh (CM)
Flattened Butterfly [1], A „Partitioned” Variant (PFBF)
2D Torus (T2D)
Flattened Butterfly [1] (FBF)
(Briefly) hierarchical NoCs
Traffic / workload:
Uniform Random
Bit Shuffle
Bit Reversal
Adversarial patterns
Parsec/Splash traces

## Slide 28: Evaluation Methodology: Sensitivity Analyses
Layout:
Group
Subgroup
Random
Naive
Concentration:
3
4
8
9
?
Router cycle time:
0.4ns
0.5ns
0.6ns
Technology node:
22nm
45nm
Injection rate:
0.01 – 0.95
Wire type:
Intermediate
Global
?
Microarchitecture enhancement:
SMART ON/OFF
Central Buffers ON/OFF
Buffer type:
Central
Edge
Network size (Node count):
200
1024
1296
Routing
Minimum static
Non-minimum adaptive

## Slide 29: Results: Performance
SMART links: ON
Central Buffers: ON
Node count: 192/200
Slim NoC provides the lowest latency
cm3: concentrated mesh, t2d3: torus,
pfbf3, pfbf4, fbf3: variants of Flattened Butterfly,
sn_subgr: Slim NoC (the subgroup layout)
in-house simulator [1]
[1] S. Hassan and S. Yalamanchili. Centralized Buffer Router: A Low Latency, Low Power Router for High Radix NoCs. NOCS’13.

## Slide 30: Results: Area and Power Consumption
SMART links: ON Central Buffers: ON
Node count: 192/200, Technology node: 45nm
Slim NoC is more efficient than high-radix designs
i-routers: routers (intermediate layer), a-routers: routers (active layer),
RRg-wires: router-router wires (global layer), RNg-wires: router-node wires (global layer).
Variants of
Flatt. Butterfly
2D torus
Conc. mesh
Slim NoC
Variants of
Flatt. Butterfly
2D torus
Conc. mesh
Slim NoC
Variants of
Flatt. Butterfly
2D torus
Conc. mesh
Slim NoC
DSENT power simulator [1]
[1] C. Sun et al. DSENT - A Tool Connecting Emerging Photonics with Electronics for Opto-Electronic Networks-on-Chip Modeling. NOCS’12.

## Slide 31: Results: Throughput / Power (PARSEC/SPLASH)
SMART links: ON
Central Buffers: ON
Node count: 192/200
Slim NoC provides a power-performance sweetspot
in-house simulator [1]
[1] S. Hassan and S. Yalamanchili. Centralized Buffer Router: A Low Latency, Low Power Router for High Radix NoCs. NOCS’13.

## Slide 32: Results: Scalability
Slim NoC is similarly advantageous
when we move
from 200 nodes to 1296 nodes
(check the paper for details )

## Slide 33: Other results
Notes: Say what these patterns are
Maybe show pictures ?

## Slide 34: What is Slim NoC?
Thank you
for your attention
A low-latency topology
An area- and energy-efficient topology
A power-performance-sweetspot topology
A highly-scalable topology
200 nodes
1296 nodes
Website:
http://spcl.inf.ethz.ch/ Research/
Scalable_Networking/
SlimNoC
Notes: - Where is the promised case study?

## Slide 35: Slim NoC: A Low-Diameter On-Chip Network Topology for High Energy Efficiency and Scalability
Maciej Besta, Syed Minhaj Hassan, Sudhakar Yalamanchili, Rachata Ausavarungnirun, Onur Mutlu, Torsten Hoefler

## Slide 36: Analysis: Diameter-2 Slim Fly
Lowest latency
Better throughput than Dragonfly
Almost-the-best throughput
~25-30% cost reduction vs. second-best topology (Dragonfly)
Notes: Say what these patterns are
Maybe show pictures ?

## Slide 37: Analysis: Diameter-2 Slim Fly
10
20
30
40
50
0
0
25
50
75
100
Number of endpoints [thousands]
Total cost [millions of $]
Cost of network construction
~25-30% cost reduction vs. second-best topology (Dragonfly)

## Slide 38: Analysis: Diameter-2 Slim Fly
Performance (Uniform Random)
Lowest latency
Better throughput than Dragonfly
Almost-the-best throughput
Notes: Say what these patterns are
Maybe show pictures ?

## Slide 39: Slim Fly on Chip – First Attempt
~50% fewer intra-group wires
One inter-group cable between
two groups
2(q-1) inter-group wires between two groups
Slim Fly:
Dragonfly:
~25% fewer routers
~33% higher endpoint density
Structure Intuition
“q”: the input parameter
that determines
the network structure. Formally, the base
of a finite field
(Slim Fly uses prime q; the corresponding field: {0, 1, …, q-1}.
Notes: What does “fewer groups/router” mean?
[fixed]

## Slide 40: Solution: Slim NoC
New cost and area models, new layouts
Let us see some layouts
What difference do they make for lengths of wires?
The “group layout” (sn_gr) is best for 1296 nodes The “subgroup layout” (sn_subgr) is best for 200 nodes

## Slide 41: Solution: Slim NoC
Recap: a finite field
Assuming q is prime:
(with modular arithmetic).
Example:
50 routers
Assuming q is non-prime:
...with instruction tables that define operations on the field.
Example:
162 routers
How to develop such a finite field?
Non-Prime Finite Fields
Addition
Multiplication
Inverse
Generate with
an exhaustive search, or use a construction based on polynomials

## Slide 42: Evaluation Methodology
4
1
2
3
Simulation Infrastructure
DSENT power simulator [5]
Considered elements for leakage: Router-router wires, Router-node wires, Routers.
Considered elements for dynamic power: Buffers, Crossbars, Wires.
[1] S. Hassan and S. Yalamanchili. Centralized Buffer Router: A Low Latency, Low Power Router for High Radix NoCs. NOCS’13.
[2] N. Jiang et al. A detailed and flexible cycle-accurate Network-on-Chip simulator. ISPASS’13.
[3] L. Valiant. A scheme for fast parallel communication. SIAM journal on computing, 1982.
[4] A. Singh. Load-Balanced Routing in Interconnection Networks. PhD thesis, Stanford University, 2005.
[5] C. Sun et al. DSENT - A Tool Connecting Emerging Photonics with Electronics for Opto-Electronic Networks-on-Chip Modeling. NOCS’12.
Performance
Cycle-accurate simulations (in-house simulator [1], Booksim [2])
Routing protocols:
  Minimum static routing
  Valiant routing [3]
  Universal Globally-Adaptive Load-Balancing routing [4]
    UGAL-L: each router has access to its local output queues
    UGAL-G: each router has access to the sizes of all the queues
Power consumption

## Slide 43: Results: Area and Power Consumption
SMART links: ON
Central Buffers: ON
Node count: 192/200
Slim NoC is more efficient than high-radix designs

## Slide 44: Results: Performance
SMART links: ON
Central Buffers: ON
Node count: 192/200
Slim NoC ensures the lowest latency

## Slide 45: Evaluation
SMART links: ON
Central Buffers: ON
Selected other insights
Node count: 192/200
Node count: 54

## Slide 46: Performance & routing
Minimum routing
Intra-group connections
1
Path of length 1 or 2 between two routers
Inter-group connections
(different types of groups)
2
Path of length 1 or 2 between two routers
Inter-group connections
(identical types of groups)
3
Path of length 2 between two routers

## Slide 47: Diameter-2 Slim Fly
A Slim Fly based on :
1
Construct a finite field .
2
Assuming q is prime:
with modular arithmetic.
Example:
E
Select a prime power q
50 routers
network radix: 7
Number of routers:
Network radix:

## Slide 48: Diameter-2 Slim Fly
3
Set of routers:
Label the routers
Routers (0,.,.)
Routers (1,.,.)
Example:
E
(0,1,.)
(0,2,.)
(0,3,.)
(0,4,.)
(0,0,.)
(1,1,.)
(1,2,.)
(1,3,.)
(1,4,.)
(1,0,.)
…
(0,0,0)
(0,0,1)
(0,0,2)
(0,0,3)
(0,0,4)
(1,4,0)
(1,4,1)
(1,4,2)
(1,4,3)
(1,4,4)

## Slide 49: Diameter-2 Slim Fly
Find primitive element
4
generates :
All non-zero elements of can be written as
Example:
E
Build Generator Sets
5

## Slide 50: Diameter-2 Slim Fly
Intra-group connections
6
Example:
E
Two routers in one group are connected iff their “vertical Manhattan distance” is an element from:
Take Routers
(0,0,0)
(0,0,1)
(0,0,2)
(0,0,3)
(0,0,4)
(for subgraph 0)
(for subgraph 1)

## Slide 51: Diameter-2 Slim Fly
Example:
E
Take Routers
Intra-group connections
6
Two routers in one group are connected iff their “vertical Manhattan distance” is an element from:
(for subgraph 0)
(for subgraph 1)

## Slide 52: Diameter-2 Slim Fly
Inter-group connections
7
Example:
E
Router
iff
Take Router
(1,0,0)
Take Router
(1,1,0)
Take Router

## Slide 53: Designing An Efficient Network Topology
Get load l per router-router channel (average number of routes per channel)
Make the network balanced, i.e.,:
each endpoint can inject at full capacity
Attaching endpoints: Diameter 2
1
2
concentration = 33% of router radix
network radix = 67% of router radix
Notes: - Equations without derivation ok?

## Slide 54: Deadlock Freedom
Assign two virtual channels (VC0 and VC1) to each link
For a 1-hop path use VC0
For a 2-hop path use VC0 (hop 1) and VC1 (hop 2)
One can also use the DFSSSP scheme [1]
Minimum Static Routing
[1] J. Domke, T. Hoefler, and W. Nagel. Deadlock-Free Oblivious Routing for Arbitrary Topologies. IPDPS’11
VC0
VC1
VC0

## Slide 55: Deadlock Freedom
Simple generalization of the previous scheme
Assign four virtual channels (VC0 – VC3) to each link
For hop k path use VCk, 0 <= k <= 3
Adaptive Routing
VC1
VC0
VC2
VC3

## Slide 56: Performance
Bit permutation traffic
01011
11010
11110
01111
Notes: Say what these patterns are
Maybe show pictures ?

## Slide 57: Performance
Shift traffic
dest id
source id
Notes: Say what these patterns are
Maybe show pictures ?

## Slide 58: Performance
Worst-case traffic
Notes: What is this d stuff?
[done]

## Slide 59: Performance
Buffer sizes (UGAL-L, worst-case traffic)
Oversubscription (64 flits)
p=16
p=18

## Slide 60: Structure Analysis
Average Distance
Uniform random traffic using minimum path routing
Notes: - check, fix

## Slide 61: Structure Analysis
Bisection Bandwidth (BB)
*
*BB approximated with
the Metis partitioner [1]
*
[1] G. Karypis, V. Kumar. A fast and high quality multilevel scheme for partitioning irregular graphs. ICPP’95

## Slide 62: Designing An Efficient Network Topology
Connecting routers: Diameter 2
Intra-group connections
6
Example:
E
Router
iff
Router
iff
Take Routers
(0,0,0)
(0,0,1)
(0,0,2)
(0,0,3)
(0,0,4)
(0,0,0), (0,0,1):
(0,0,0), (0,0,2):
(0,0,1), (0,0,2):
(0,0,0), (0,0,4):

## Slide 63: Designing An Efficient Network Topology
Connecting routers: Diameter 2
Intra-group connections
6
Example:
E
Router
iff
Router
iff
Take Routers
(0,0,0)
(0,0,1)
(0,0,2)
(0,0,3)
(0,0,4)
(1,4,0)
(1,4,1)
(1,4,2)
(1,4,3)
(1,4,4)
(1,4,0), (1,4,1):
(0,0,0), (0,0,2):
(0,0,1), (0,0,4):
(0,0,0), (0,0,4):

## Slide 64: Designing An Efficient Network Topology
Connecting routers: Diameter 2
Inter-group connections
7
Example:
E
Router
iff
Take Router
(0,0,0)
(0,1,1)
(1,1,0)
(0,0,0):
(0,1,1):
(0,2,2):
(0,4,4):
(0,2,2)
(0,3,3)
(0,4,4)