## Slide 1
Swordfish: A Framework for Evaluating
Deep Neural Network-based Basecalling
using Computation-in-Memory
with Non-Ideal Memristors
Taha Michael Shahroodi,
Gagandeep Singh, Mahdi Zahedi, Haiyu Mao,
Joel Lindegger, Can Firtina, Stephan Wong,
Onur Mutlu, Said Hamdioui
Notes: 1

## Slide 2: Executive Summary
Key Results: Across four real datasets of varying sizes, Swordfish realistically provides
  25.7 better average throughput compared to state-of-the-art basecalling on GPU
  12% mitigation in basecalling accuracy loss after hardware/software co-designed enhancement techniques
  Three new insights on future research directions for accuracy enhancement techniques
Key Contribution: Swordfish; the first framework for memristor-based CIM that uses characterized memories and accurate models to
1) accurately and realistically evaluate the effects of non-idealities on basecalling accuracy and throughput
2) comprehensively investigate the impact of accuracy enhancement techniques on basecalling accuracy and throughput
Goal: Enable accurate and realistic evaluation of accuracy and throughput for DNN-based basecalling on memristor-based CIM
Problem: Prior frameworks for memristor-based CIM accelerators targeting large DNNs either
overlook existing non-idealities,
overestimates achievable accuracy by studying non-idealities in isolation or using imprecise models/methodology
overlook the effects of non-idealities mitigation techniques on the achievable throughput
Context: Basecalling is the first step and a major throughput bottleneck
Basecallers use deep neural networks (DNNs)
DNN-based basecalling accuracy and throughput impact accuracy and throughput of next analysis
Prior research uses memristor-based Computation-in-Memory (CIM) to accelerate DNNs
Non-idealities in memristor-based CIM known to hinder accuracy

## Slide 3: Outline
Background & Motivation
Swordfish: Design & Implementation
Evaluation & Key Results
Takeaways & Summary

## Slide 4: Outline
Background & Motivation
Swordfish: Design & Implementation
Evaluation & Key Results
Takeaways & Summary

## Slide 5: Nanopore Genome Sequencing and Analysis Pipeline
Genome Sequencing: Determining DNA sequence order for
  Personalized medicine,
  Outbreak tracing,
  Understanding evolution
Nanopore Sequencing: A widely used sequencing technology
Basecalling
in GPU
A
T
G
C
Downstream Analysis
Examples:
Read Mapping
Variant Calling
…
Nanopore Sequencing
Current
Nanopore Genome Analysis Pipeline
Basecalling consumes up to 84.2% of the execution time [Bowden+ 2019]

## Slide 6: Nanopore Genome Sequencing and Analysis Pipeline
Genome Sequencing: Determining DNA sequence order for
  Personalized medicine,
  Outbreak tracing,
  Understanding evolution
Nanopore Sequencing: A widely used sequencing technology
Basecalling
in GPU
A
T
G
C
Downstream Analysis
Examples:
Read Mapping
Variant Calling
…
Nanopore Sequencing
Current
Nanopore Genome Analysis Pipeline
Basecalling consumes up to 84.2% of the execution time [Bowden+ 2019]
Basecalling is
Accuracy-critical
Performance Bottleneck
Basecallers are just large DNNs

## Slide 7: DNN Hardware Acceleration
DNN execution is dominated by:
Memristor-based crossbars support VMM
Vector-Matrix Multiplication (VMM)
Data movement between memory and accelerator
(e.g., GPU or TPU)
Computation in Memory (CIM) minimizes data movement

## Slide 8: DNN Hardware Acceleration
DNN execution is dominated by:
Memristor-based crossbars support VMM
Vector-Matrix Multiplication (VMM)
Data movement between memory and accelerator
(e.g., GPU or TPU)
Computation in Memory (CIM) minimizes data movement
Memristor-based CIM for DNN Acceleration
  [Ankit+, ASPLOS 2019], [Chi+, ISCA 2016], [Lou+, PACT2020], [Shafiee+, ISCA 2016]

## Slide 9: Memristor-based Crossbars

## Slide 10: VMM in Memristor-based Crossbars
Digital to Analog Converters (DACs)
Analog to Digital Converters (ADCs)

## Slide 11: VMM in Memristor-based Crossbars
VMM in Accelerators
VMM in Memristor-based Crossbars
In Accelerators
In Memory
Accurate

## Slide 12: Non-idealities in Memristor-based Crossbars
Digital to Analog Converters (DACs)
Analog to Digital Converters (ADCs)
Non-ideal DAC
Variation in
Synaptic Conductance
Wire Resistance
Non-ideal ADC
Non-idealities are everywhere

## Slide 13: VMM in Memristor-based Crossbars
VMM in Memristor-based Crossbars
In Memory

## Slide 14: VMM in Memristor-based Crossbars
VMM in Ideal Memristor-based Crossbars
In Memory
Accurate

## Slide 15: VMM in Memristor-based Crossbars
VMM in Real Memristor-based Crossbars
In Memory
In Memory
Accurate
Inaccurate
VMM in Ideal Memristor-based Crossbars
In Memory
Accurate

## Slide 16: Our Goal
To realistically evaluate end-to-end basecalling
accuracy and throughput for memristor-based CIM

## Slide 17: Key Idea
To account for the non-idealities in device, circuit and architecture of memristor-based CIM and the overhead of non-idealities mitigation techniques

## Slide 18: Outline
Background & Motivation
Swordfish: Design & Implementation
Evaluation & Key Results
Takeaways & Summary

## Slide 19: Swordfish vs Other Frameworks
Ideal Memristor-based CIM Frameworks for DNNs
User Input
DNN
Architecture
Weights
CIM Hardware
Architecture
Traditional ideal Frameworks
Partition & Map
Layer 1
Layer N
…
…
System Evaluator
Performance
Area
Kernel Chunks
(i.e., ideal VMMs)

## Slide 20: Swordfish Framework - Overview
Realistic Memristor-based CIM Frameworks for DNNs
Swordfish
User Input
DNN
Architecture
Weights
CIM Hardware
Architecture
Circuit Params
Device Params
Partition & Map
Layer 1
Layer N
…
…
System Evaluator
Performance
Area
Accuracy
Hyperparameters
Updated Weights
Kernel Chunks
Accuracy Enhancer
VMM Model Generator
Non-ideal
VMMs

## Slide 21: Swordfish Framework - Overview
Realistic Memristor-based CIM Frameworks for DNNs
Swordfish
User Input
DNN
Architecture
Weights
CIM Hardware
Architecture
Circuit Params
Device Params
Partition & Map
Layer 1
Layer N
…
…
System Evaluator
Performance
Area
Accuracy
Hyperparameters
Accuracy Enhancer
Updated Weights
Kernel Chunks
VMM Model Generator
Non-ideal
VMMs

## Slide 22: VMM Model Generator
Goal: Capture real output of VMM in presence of non-idealities
Swordfish supports two approaches:
Approach 1:
Real chip measurement and characterizations
Approach 2:
Analytical Modeling using component’s models
Model for
Non-Ideal ADC
Model for
Non-Ideal Crossbar
Model for
Non-Ideal DAC
Input Vector
Non-Ideal Input Voltages
Non-Ideal Output Currents
Non-Ideal Output Vector
© Copyright 2023, ArC INSTRUMENTS

## Slide 23: VMM Model Generator
Goal: Capture real output of VMM in presence of non-idealities
Swordfish supports two approaches:
Approach 1:
Real chip measurement and characterizations
Approach 2:
Analytical Modeling using component’s models
Model for
Non-Ideal ADC
Model for
Non-Ideal Crossbar
Model for
Non-Ideal DAC
Input Vector
Non-Ideal Input Voltages
Non-Ideal Output Currents
Non-Ideal Output Vector
Most Accurate
Less Flexible
More Flexible
Less Accurate
© Copyright 2023, ArC INSTRUMENTS

## Slide 24: Swordfish Framework - Overview
Realistic Memristor-based CIM Frameworks for DNNs
Swordfish
User Input
DNN
Architecture
Weights
CIM Hardware
Architecture
Circuit Params
Device Params
Partition & Map
Layer 1
Layer N
…
…
System Evaluator
Performance
Area
Accuracy
Hyperparameters
Kernel Chunks
VMM Model Generator
Non-ideal
VMMs
Accuracy Enhancer
Updated Weights

## Slide 25: Accuracy Enhancement
1. Analytical Variation Aware Training (VAT)
2. Knowledge Distillation-based (KD) VAT
Goal: Enhance the accuracy of a VMM by adapting input currents and resistance of memristors based on non-idealities
3. Read-Verify-Write (R-V-W) Training
4. Random Sparse Adaptation (RSA) Training
Swordfish supports four techniques:

## Slide 26: Example of Accuracy Enhancement
1. Analytical Variation Aware Training (VAT) [Offline]
2. Knowledge Distillation-based (KD) VAT [Offline]
Goal: Enhance the accuracy of a VMM by adapting input currents and resistance of memristors based on non-idealities
3. Read-Verify-Write (R-V-W) Training [Offline]
4. Random Sparse Adaptation (RSA) Training
Read more about
other techniques in the paper

## Slide 27: Accuracy Enhancement via Random Sparse Adaptation
Key idea?
Load Weights to Memristors + SRAM
VMM/Layer Output
Memristor Array
Digital Labeled Input Squiggle
SRAM
VMM Output
Initial Training
Retraining
In Software
e.g., using KD
Load Weights to SRAM
Key idea? Map the weights
Key idea? Map the weights that otherwise would map to error-prone memristor devices
Key idea? Map the weights that otherwise would map to error-prone memristor devices to reliable SRAM cells.
RSA in 3 Steps:
Initial Training (one-time, on GPU) and distribution of weights
VMM operation using both memories
Retraining all weights and reload those on SRAM (only)
+
1
2
3

## Slide 28: More in the Paper
Details of capturing non-idealities at VMM level
Implementation details of Swordfish components:
  Partition & Map
  Accuracy Enhancer
  VMM Model Generator
  System Evaluator
Elaborations on accuracy enhancement techniques
  Analytical Variation Aware Training (VAT)
  Knowledge Distillation-based (KD) using VAT
  Read-Verify-Write (R-V-W) Training
  Random Sparse Adaptation (RSA) Training

## Slide 29: Outline
Background & Motivation
Swordfish: Design & Implementation
Evaluation & Key Results
Takeaways & Summary

## Slide 30: Evaluation Methodology: Experimental Setup
We evaluate
  Basecaller: Bonito [Oxford Nanopore 2023]
  CIM Architecture: PUMA [Ankit+, ASPLOS 2019]
Infrastructure
  2x AMD EPYC 7742 CPU with 500 GB DDR4 DRAM
  8x NVIDIA V100
Datasets and Workloads [Wick+ 2019, Zook+ 2019, CADDE 2020]
  4 real read and reference genomes with various genome size (D1, D2, D3, and D4)

## Slide 31: Evaluated Non-idealities & Enhancement techniques
All
5
Non-idealities
Accuracy Enhancement Techniques
Combined
4
Synaptic+Wires
1
Sensing+ADC Circuitry
2
DAC+Driver Circuitry
3
Measured
5
Variation Aware Training (VAT)
1
Knowledge Distillation (KD)
2
Read-Verify-Write (R-V-W)
3
4
Random Sparse Adaptation (RSA) + KD
Analytical
Models
(Approach 2)
(Approach 1)

## Slide 32: Accuracy: All Non-idealities without Mitigation
Non-idealities
Accuracy (%)
D1
D2
Baseline
Baseline
Combined non-idealities leads to significant accuracy loss (>18%)

## Slide 33: Accuracy: Enhancement Techniques on All Non-idealities
Enhancement Technique
D1
Accuracy (%)
Baseline
Baseline
D3
Accuracy enhancement techniques mitigate non-idealities,
But differently.

## Slide 34: Accuracy: Enhancement Techniques on All Non-idealities
D1
Accuracy (%)
Baseline
Baseline
D3
Considerable accuracy loss (>6%) even with All
enhancement techniques.
Enhancement Technique

## Slide 35: Throughput Analysis
Ideal CIM implementation improves the basecalling throughput over Bonito-GPU by 413.6× on average
G-Bonito
Ideal-Swordfish
Realistic-Swordfish-RVW
Realistic-Swordfish-RSA
Realistic-Swordfish-RSA+KD

## Slide 36: Throughput Analysis
Ideal CIM implementation improves the basecalling throughput over Bonito-GPU by 413.6× on average
G-Bonito
Ideal-Swordfish
Realistic-Swordfish-RVW
Realistic-Swordfish-RSA
Realistic-Swordfish-RSA+KD
Throughput improvement at the high, unacceptable accuracy loss of 18%

## Slide 37: Throughput Analysis
Realistic CIM designs significantly underperform ideal design
G-Bonito
Ideal-Swordfish
Realistic-Swordfish-RVW
Realistic-Swordfish-RSA
Realistic-Swordfish-RSA+KD

## Slide 38: Throughput Analysis
Some realistic CIM designs degrade throughput compared to Bonito-GPU
G-Bonito
Ideal-Swordfish
Realistic-Swordfish-RVW
Realistic-Swordfish-RSA
Realistic-Swordfish-RSA+KD

## Slide 39: Throughput Analysis
Realistic CIM design using RSA+KD provides on average 25.7× higher throughput compared to Bonito-GPU
G-Bonito
Ideal-Swordfish
Realistic-Swordfish-RVW
Realistic-Swordfish-RSA
Realistic-Swordfish-RSA+KD

## Slide 40: More in the Paper
Details on evaluation methodology
  Datasets
  Array and devices
Evaluation results
  Individual non-idealities and architectural limitations on accuracy
  Accuracy enhancements on individual and combined non-idealities and architectural limitations
  Accuracy vs. Area analysis
  Observations and trends from the presented figures
  Results for 256x256 crossbar + comparison with 64x64 crossbars
Discussions, takeaways, and future work

## Slide 41: Outline
Background & Motivation
Swordfish: Design & Implementation
Evaluation & Key Results
Takeaways & Summary

## Slide 42: Takeaways
The target application for memristor-based CIM matters
Non-idealities are detrimental to both accuracy and performance
HW/SW co-designed techniques mitigate inaccuracy the most
Swordfish enables realistic evaluation of accuracy and performance for DNN-based applications on memristor-based CIM

## Slide 43: Summary
Many opportunities for
  Realistically evaluating accuracy and throughput other DNNs on memristor-based CIM
  Developing and evaluating novel accuracy enhancement techniques, on software, hardware, or both
  We should remain cautious applying known acceleration techniques to emerging technologies, architectures, and applications
Key Results: Across four real datasets of varying sizes, Swordfish realistically provides
  25.7 better average throughput compared to state-of-the-art basecalling on GPU
  12% mitigation in basecalling accuracy loss after hardware/software co-designed enhancement techniques
  Three new insights on future research directions for accuracy enhancement techniques
Key Contribution: Swordfish; the first framework for memristor-based CIM that uses characterized memories and accurate models to
1) accurately and realistically evaluate the effects of non-idealities on basecalling accuracy and throughput
2) comprehensively investigate the impact of accuracy enhancement techniques on basecalling accuracy and throughput

## Slide 44
Swordfish: A Framework for Evaluating
Deep Neural Network-based Basecalling
using Computation-in-Memory
with Non-Ideal Memristors
Questions?
Notes: 44