## Slide 1
SynCron
Efficient Synchronization Support
for Near-Data-Processing Architectures
Christina Giannoula
Nandita Vijaykumar, Nikela Papadopoulou, Vasileios Karakostas
Ivan Fernandez, Juan Gómez Luna, Lois Orosa
Nectarios Koziris, Georgios Goumas, Onur Mutlu

## Slide 2
NDP
Logic
CPU
DRAM
Graph Analytics
Neural Networks
Bioinformatics
Recommendation Systems
Near-Data-Processing (NDP) Systems

## Slide 3
Single Source Shortest Path (SSSP)
for v in Graph:
for u in neighbors[v]:
if distance[v] + edge_weight[v, u] < distance[u]
if distance[v] + edge_weight[v, u] < distance[u]
distance[u] = distance[v] + edge_weight[v, u]
Locks
Barriers
Graph Analytics
Bioinformatics
Concurrent
Data Structures
Databases
Image Processing
Synchronization is Necessary
lock_acquire(u)
lock_release(u)

## Slide 4
Main Memory
NDP Core
NDP Core
NDP Core
NDP Unit
Main Memory
NDP Core
NDP Core
NDP Core
NDP Unit
Programmable Core / Accelerator
Private
Cache
Expensive
Communication
No Shared Caches
No Hardware Cache Coherence
Challenge: Efficient Synchronization

## Slide 5
SynCron’s Benefits:
High System Performance
Low Hardware Cost
Programming Ease
General Synchronization Support
The first end-to-end synchronization solution for NDP architectures
SynCron

## Slide 6
NDP Synchronization Solution Space
Our Mechanism: SynCron
Evaluation
Outline

## Slide 7
Synchronization challenges in NDP systems:
(1) Lack of hardware cache coherence support
(2) Expensive communication across NDP units
(3) Lack of a shared level of cache memory
Main Memory
NDP Core
NDP Core
NDP Core
NDP Unit
Programmable Core / Accelerator
Private Cache
NDP System
Baseline NDP Architecture

## Slide 8
(1) Shared Memory
(2) Message-passing
Hardware Cache
Coherence
Remote
Atomics
Specialized Hardware Support
Software-based Schemes
Specialized Hardware Support
NDP Synchronization Solution Space

## Slide 9
(1) Shared Memory
(2) Message-passing
Hardware Cache
Coherence
Remote
Atomics
Specialized Hardware Support
Software-based Schemes
Specialized Hardware Support
NDP Synchronization Solution Space
Lack of hardware cache coherence support
CPUs:
Hierarchical CLH Locks [EuroPar’06]
Cohort Locks [TOPC’15]
Ticket Locks [TOCS’91] …
MPPs:
QOLB [ASPLOS’89]

## Slide 10
NDP Synchronization Solution Space
Expensive communication across NDP units
(1) Shared Memory
(2) Message-passing
Hardware Cache
Coherence
Remote
Atomics
Specialized Hardware Support
GPUs:
Fermi GF100 [IEEE Micro’10] …
MPPs:
SGI Origin [ISCA’97]
Cray T3E [ASPLOS’96] …
CPUs:
SSB [ISCA’07]
Lock Cache [CASES’01] …
MPPs:
Full/Empty Bits [ISCA’83] …
Software-based Schemes
Specialized Hardware Support
CPUs:
MiSAR [ISCA’15]
LCU [MICRO’10]
Glocks [IPDPS’11] …
GPUs:
HQL [IPDPS’13] …
NDPs:
Tesseract [ISCA’15]

## Slide 11
NDP Synchronization Solution Space
(1) Shared Memory
(2) Message-passing
Hardware Cache
Coherence
Remote
Atomics
Specialized Hardware Support
Software-based Schemes
Specialized Hardware Support
CPUs:
SSB [ISCA’07]
Lock Cache [CASES’01]
BarrierFilter [MICRO’06]
CPUs:
MiSAR [ISCA’15]
GPUs:
HQL [IPDPS’13]
NDPs:
Tesseract [ISCA’15], Near-Data Processing for In-memory Analytics [PACT’15]
Lack of a shared level of cache memory

## Slide 12
NDP Synchronization Solution Space
(1) Shared Memory
(2) Message-passing
Hardware Cache
Coherence
Remote
Atomics
Specialized Hardware Support
Software-based Schemes
Specialized Hardware Support
Prior schemes are not suitable or efficient
for NDP systems

## Slide 13
NDP Synchronization Solution Space
(1) Shared Memory
(2) Message-passing
Hardware Cache
Coherence
Remote
Atomics
Specialized Hardware Support
Software-based Schemes
Specialized Hardware Support
NDPs:
SynCron [HPCA’21]
Hardware Message-passing
to Avoid Synchronization via Shared Memory
Hierarchical Communication
to Eliminate Expensive Network Traffic
Specialized Cache Structure
to Minimize Latency Costs
SynCron’s Design Choices

## Slide 14
NDP Synchronization Solution Space
Our Mechanism: SynCron
Evaluation
Outline

## Slide 15
SynCron consists of four key techniques:
1. Hardware support for synchronization acceleration
2. Direct buffering of synchronization variables
3. Hierarchical message-passing communication
4. Integrated hardware-only overflow management
SynCron: Overview

## Slide 16
NDP Unit 0
Main Memory
NDP Core 0
Synchronization
Engine 0
NDP Core 1
NDP Unit 1
Main Memory
NDP Core 0
Synchronization
Engine 1
NDP Core 1
`````
ISA
  No Complex Cache Coherence Protocols
  No Expensive Atomic Operations
  Low Hardware Cost
1. Hardware Synchronization Support
Local
lock acquire

## Slide 17
NDP Unit 0
Main Memory
NDP Core 0
Synchronization
Engine 0
NDP Core 1
NDP Unit 1
Main Memory
NDP Core 0
Synchronization
Engine 1
NDP Core 1
Indexing Counters
Synchronization
Processing Unit
Address
…
--
…
--
…
--
…
--
…
Synchronization
Table
2. Direct Buffering of Variables
Local
lock acquire

## Slide 18
NDP Unit 0
Main Memory
NDP Core 0
Synchronization
Engine 0
NDP Core 1
NDP Unit 1
Main Memory
NDP Core 0
Synchronization
Engine 1
NDP Core 1
Indexing Counters
Synchronization
Processing Unit
Synchronization
Table
2. Direct Buffering of Variables
Local
lock acquire
Address
…
0x33A9
…
--
…
--
…
--
…
      No Costly Memory Accesses
      Low Latency

## Slide 19
NDP Unit 0
Main Memory
NDP Core 0
Synchronization
Engine 0
NDP Core 1
NDP Unit 2
Main Memory
NDP Core 0
Synchronization
Engine 2
NDP Core 1
NDP Unit 1
Main Memory
NDP Core 0
NDP Core 1
Synchronization
Engine 1
syncronVar
NDP Unit 3
Main Memory
NDP Core 0
NDP Core 1
Synchronization
Engine 3
3. Hierarchical Communication

## Slide 20
NDP Unit 1
Main Memory
NDP Core 0
NDP Core 1
Synchronization
Engine 1
NDP Unit 0
Main Memory
NDP Core 0
Synchronization
Engine 0
NDP Core 1
NDP Unit 2
Main Memory
NDP Core 0
Synchronization
Engine 2
NDP Core 1
syncronVar
Master
NDP Unit 3
Main Memory
NDP Core 0
NDP Core 1
Synchronization
Engine 3
3. Hierarchical Communication
Local
lock acquire

## Slide 21
NDP Unit 0
Main Memory
NDP Core 0
Synchronization
Engine 0
NDP Core 1
NDP Unit 2
Main Memory
NDP Core 0
Synchronization
Engine 2
NDP Core 1
NDP Unit 1
Main Memory
NDP Core 0
NDP Core 1
Synchronization
Engine 1
syncronVar
Master
NDP Unit 3
Main Memory
NDP Core 0
NDP Core 1
Synchronization
Engine 3
3. Hierarchical Communication
Global
lock acquire

## Slide 22
NDP Unit 0
Main Memory
NDP Core 0
Synchronization
Engine 0
NDP Core 1
NDP Unit 1
Main Memory
NDP Core 0
NDP Core 1
Synchronization
Engine 1
Master
Synchro-nization
Process-ing Unit
Indexing Counters
Synchronization Table 0
Address
Global
Waitlist
Local
Waitlist
…
0x33A9
0000
11
…
Synchro-nization
Process-ing Unit
Indexing Counters
Synchronization Table 1
Address
Global
Waitlist
Local
Waitlist
…
0x33A9
1101
11
…
3. Hierarchical Communication
Minimize Expensive Traffic
syncronVar

## Slide 23
NDP Unit 0
Main Memory
NDP Core 0
Synchronization
Engine 0
NDP Core 1
NDP Unit 1
Main Memory
NDP Core 0
Synchronization
Engine 1
NDP Core 1
syncronVar
Master
Synchronization
Processing Unit
Synchronization
Table
Indexing Counters
Counter0 = 0
Counter1 > 0
Counter2 = 0
Counter3 = 0
syncronVar
Address
4. Integrated Overflow Management
Address
…
0x33A9
…
0x2241
…
0x438C
…
0x6B4A
…
Fully Occupied

## Slide 24
NDP Unit 0
Main Memory
NDP Core 0
Synchronization
Engine 0
NDP Core 1
NDP Unit 1
Main Memory
NDP Core 0
Synchronization
Engine 1
NDP Core 1
syncronVar
Master
4. Integrated Overflow Management
Fully Occupied
Synchronization
Processing Unit
Synchronization
Table
Indexing Counters
Address
…
0x33A9
…
0x2241
…
0x438C
…
0x6B4A
…
      Low Performance Degradation
      High Programming Ease
Global
overflow
lock acquire

## Slide 25
Lock primitive
Barrier primitive
Semaphore primitive
Condition variable primitive
lock_acquire()
lock_release ()
barrier_wait_within_NDP_unit()
barrier_wait_across_NDP_units()
sem_wait()
sem_post()
cond_wait()
cond_signal()
cond_broadcast()
SynCron’s Supported Primitives

## Slide 26
All NDP cores compete for the same lock variable
NDP Unit 0
Main Memory
NDP Core 0
Synchronization
Engine 0
NDP Core 1
NDP Unit 1
Main Memory
NDP Core 0
Synchronization
Engine 1
NDP Core 1
syncronVar
Master
lock
acquire
lock
acquire
lock
acquire
lock
acquire
Lock Operation

## Slide 27: Lock Operation
NDP Unit 0
Main Memory
NDP Core 0
Synchronization
Engine 0
NDP Core 1
NDP Unit 1
Main Memory
NDP Core 0
Synchronization
Engine 1
NDP Core 1
syncronVar
Synchro-nization
Process-ing Unit
Indexing Counters
Synchronization Table 0
Address
Global
Waitlist
Local
Waitlist
…
0x33A9
00
11
…
Synchro-nization
Process-ing Unit
Indexing Counters
Synchronization Table 1
Address
Global
Waitlist
Local
Waitlist
…
0x33A9
00
11
…
Master
Local
lock acquire

## Slide 28: Lock Operation
NDP Unit 0
Main Memory
NDP Core 0
Synchronization
Engine 0
NDP Core 1
NDP Unit 1
Main Memory
NDP Core 0
Synchronization
Engine 1
NDP Core 1
syncronVar
Master
Synchro-nization
Process-ing Unit
Indexing Counters
Synchronization Table 0
Address
Global
Waitlist
Local
Waitlist
…
0x33A9
00
11
…
Synchro-nization
Process-ing Unit
Indexing Counters
Synchronization Table 1
Address
Global
Waitlist
Local
Waitlist
…
0x33A9
00
11
…
Global
lock acquire

## Slide 29: Lock Operation
NDP Unit 0
Main Memory
NDP Core 0
Synchronization
Engine 0
NDP Core 1
NDP Unit 1
Main Memory
NDP Core 0
Synchronization
Engine 1
NDP Core 1
syncronVar
Master
Synchro-nization
Process-ing Unit
Indexing Counters
Synchronization Table 0
Address
Global
Waitlist
Local
Waitlist
…
0x33A9
00
11
…
Synchro-nization
Process-ing Unit
Indexing Counters
Synchronization Table 1
Address
Global
Waitlist
Local
Waitlist
…
0x33A9
01
11
…
Global
lock acquire

## Slide 30: Lock Operation
NDP Unit 0
Main Memory
NDP Core 0
Synchronization
Engine 0
NDP Core 1
NDP Unit 1
Main Memory
NDP Core 0
Synchronization
Engine 1
NDP Core 1
syncronVar
Master
Synchro-nization
Process-ing Unit
Indexing Counters
Synchronization Table 0
Address
Global
Waitlist
Local
Waitlist
…
0x33A9
00
11
…
Synchro-nization
Process-ing Unit
Indexing Counters
Synchronization Table 1
Address
Global
Waitlist
Local
Waitlist
…
0x33A9
01
11
…
Local
lock grant

## Slide 31: Lock Operation
NDP Unit 0
Main Memory
NDP Core 0
Synchronization
Engine 0
NDP Core 1
NDP Unit 1
Main Memory
NDP Core 0
Synchronization
Engine 1
NDP Core 1
syncronVar
Master
Synchro-nization
Process-ing Unit
Indexing Counters
Synchronization Table 0
Address
Global
Waitlist
Local
Waitlist
…
0x33A9
00
11
…
Synchro-nization
Process-ing Unit
Indexing Counters
Synchronization Table 1
Address
Global
Waitlist
Local
Waitlist
…
0x33A9
01
00
…
Global
lock grant

## Slide 32: Lock Operation
NDP Unit 0
Main Memory
NDP Core 0
Synchronization
Engine 0
NDP Core 1
NDP Unit 1
Main Memory
NDP Core 0
Synchronization
Engine 1
NDP Core 1
syncronVar
Master
Synchro-nization
Process-ing Unit
Indexing Counters
Synchronization Table 0
Address
Global
Waitlist
Local
Waitlist
…
0x33A9
00
11
…
Synchro-nization
Process-ing Unit
Indexing Counters
Synchronization Table 1
Address
Global
Waitlist
Local
Waitlist
…
0x33A9
01
00
…
Local
lock grant

## Slide 33: Lock Operation
NDP Unit 0
Main Memory
NDP Core 0
Synchronization
Engine 0
NDP Core 1
NDP Unit 1
Main Memory
NDP Core 0
Synchronization
Engine 1
NDP Core 1
syncronVar
Master
Synchro-nization
Process-ing Unit
Indexing Counters
Synchronization Table 0
Address
Global
Waitlist
Local
Waitlist
…
0x33A9
00
00
…
Synchro-nization
Process-ing Unit
Indexing Counters
Synchronization Table 1
Address
Global
Waitlist
Local
Waitlist
…
0x33A9
01
00
…

## Slide 34: Lock Operation
NDP Unit 0
Main Memory
NDP Core 0
Synchronization
Engine 0
NDP Core 1
NDP Unit 1
Main Memory
NDP Core 0
Synchronization
Engine 1
NDP Core 1
syncronVar
Master
Synchro-nization
Process-ing Unit
Indexing Counters
Synchronization Table 0
Address
Global
Waitlist
Local
Waitlist
…
--
--
--
…
Synchro-nization
Process-ing Unit
Indexing Counters
Synchronization Table 1
Address
Global
Waitlist
Local
Waitlist
…
0x33A9
01
00
…
Global
lock release

## Slide 35: Lock Operation
NDP Unit 0
Main Memory
NDP Core 0
Synchronization
Engine 0
NDP Core 1
NDP Unit 1
Main Memory
NDP Core 0
Synchronization
Engine 1
NDP Core 1
syncronVar
Master
Synchro-nization
Process-ing Unit
Indexing Counters
Synchronization Table 0
Address
Global
Waitlist
Local
Waitlist
…
--
--
--
…
Synchro-nization
Process-ing Unit
Indexing Counters
Synchronization Table 1
Address
Global
Waitlist
Local
Waitlist
…
0x33A9
00
00
…
Global
lock release

## Slide 36: Lock Operation
NDP Unit 0
Main Memory
NDP Core 0
Synchronization
Engine 0
NDP Core 1
NDP Unit 1
Main Memory
NDP Core 0
Synchronization
Engine 1
NDP Core 1
syncronVar
Master
Synchro-nization
Process-ing Unit
Indexing Counters
Synchronization Table 0
Address
Global
Waitlist
Local
Waitlist
…
--
--
--
…
Synchro-nization
Process-ing Unit
Indexing Counters
Synchronization Table 1
Address
Global
Waitlist
Local
Waitlist
…
--
--
--
…

## Slide 37
NDP Unit 0
Main Memory
NDP Core 0
Synchronization
Engine 0
NDP Core 1
NDP Unit 1
Main Memory
NDP Core 0
Synchronization
Engine 1
NDP Core 1
syncronVar
Master
Synchro-nization
Process-ing Unit
Indexing Counters
Synchronization Table 0
Address
Global
Waitlist
Local
Waitlist
…
--
--
--
…
Synchro-nization
Process-ing Unit
Indexing Counters
Synchronization Table 1
Address
Global
Waitlist
Local
Waitlist
…
--
--
--
…
More details in the paper
Lock Operation

## Slide 38
NDP Synchronization Solution Space
Our Mechanism: SynCron
Evaluation
Outline

## Slide 39
Simulators:
  Zsim [Sanchez+, ISCA’13]
  Ramulator [Kim+, CAL’15]
System Configuration:
  4x NDP units of 16 in-order cores
  16KB L1 Data + Instr. Cache
  4GB HBM memory
SynCron’s Default Parameters:
  Synchronization Processing Unit @1GHz
  12-cycle worst-case latency for a message to be served [Aladdin]
  64 entries in Synchronization Table, 1-cycle latency [CACTI]
  256 entries in indexing counters 2-cycle latency [CACTI]
Workloads:
  9x Pointer-chasing Data Structures from ASCYLIB [David+, ASPLOS’15]
  6x Graph Applications from Crono [Ahmad+, IISWC’15]
  Time Series Analysis from Matrix Profile [Yeh+, ICDM’16]
Evaluation Methodology

## Slide 40
SynCron
Central [Ahn+, ISCA’15]:
  Synchronization Server: One NDP core of the NDP system
  Centralized hardware message-passing communication
Hier [Gao+, PACT’15 / Tang+, ASPLOS’19]:
  Synchronization Servers: One NDP core per NDP unit
  Hierarchical hardware message-passing communication
Ideal
  Zero overhead for synchronization
Comparison Points for SynCron

## Slide 41
Chart: 
| 15 | 30 | 45 | 60
Central | 4.72 | 6 | 6.9 | 7.92
Hier | 4.85 | 7.2 | 8.3 | 9.32
SynCron | 4.97 | 7.32 | 8.62 | 9.97
Ideal | 6.66 | 9.82 | 11.55 | 13.8
Operations / μs
Chart: 
| 15 | 30 | 45 | 60
Hier | 6.08 | 11.72 | 17.02 | 20.55
Central | 6.21 | 9.47 | 11.63 | 12.85
SynCron | 6.57 | 12.67 | 18.38 | 22.88
Ideal | 8.22 | 15.86 | 22.99 | 28.27
Number of NDP Cores
Hash Table – 1K
Operations / μs
Chart: 
| 15 | 30 | 45 | 60
Hier | 3.3 | 5.1 | 6.26 | 8.13
Central | 3.3 | 3.63 | 4.38 | 5.73
SynCron | 4.08 | 6 | 7.49 | 9.65
Ideal | 5.53 | 7.97 | 9.66 | 12.57
Linked List – 20K
Number of NDP Cores
Operations / ms
Stack – 100K
1.18x
1.26x
1.59x
1.78x
1.19x
1.68x
High Contention
Small # of Variables
Medium Contention
Medium # of Variables
Low Contention
High # of Variables
Throughput of Pointer Chasing
Number of NDP Cores

## Slide 42
Chart: 
| 15 | 30 | 45 | 60
Central | 4.72 | 6 | 6.9 | 7.92
Hier | 4.85 | 7.2 | 8.3 | 9.32
SynCron | 4.97 | 7.32 | 8.62 | 9.97
Ideal | 6.66 | 9.82 | 11.55 | 13.8
Chart: 
| 15 | 30 | 45 | 60
Hier | 6.08 | 11.72 | 17.02 | 20.55
Central | 6.21 | 9.47 | 11.63 | 12.85
SynCron | 6.57 | 12.67 | 18.38 | 22.88
Ideal | 8.22 | 15.86 | 22.99 | 28.27
Chart: 
| 15 | 30 | 45 | 60
Hier | 3.3 | 5.1 | 6.26 | 8.13
Central | 3.3 | 3.63 | 4.38 | 5.73
SynCron | 4.08 | 6 | 7.49 | 9.65
Ideal | 5.53 | 7.97 | 9.66 | 12.57
Operations / μs
Operations / μs
Operations / ms
Stack – 100K
Hash Table – 1K
Linked List – 20K
1.07x
1.11x
1.19x
Small # of Variables
Medium # of Variables
High # of Variables
Throughput of Pointer Chasing
Number of NDP Cores
Number of NDP Cores
Number of NDP Cores
SynCron achieves the highest throughput
under all scenarios

## Slide 43
Low Contention - High # of Variables
Chart: Speedup
| bfs.sl | cc.sx | sssp.co | pr.wk | tf.sl | tc.sx | ts.air | ts.pow | AVG
Central | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Hier | 1.09 | 1.11 | 1.07 | 1.25 | 1.09 | 1.12 | 1.67 | 1.63 | 1.19
SynCron | 1.38 | 1.37 | 1.21 | 1.5 | 1.38 | 1.41 | 2.16 | 2.29 | 1.48
Ideal | 1.46 | 1.43 | 1.42 | 1.61 | 1.48 | 1.49 | 2.88 | 2.63 | 1.58
Synchronization
Intensive
1.23x
-9.5%
Speedup in Real Applications
SynCron performs best across all real applications

## Slide 44
Chart: Energy Breakdown
| Central | Hier | SynCron | Ideal | Central | Hier | SynCron | Ideal | Central | Hier | SynCron | Ideal | Central | Hier | SynCron | Ideal | Central | Hier | SynCron | Ideal | Central | Hier | SynCron | Ideal | Central | Hier | SynCron | Ideal | Central | Hier | SynCron | Ideal | Central | Hier | SynCron | Ideal | bfs.sl | cc.sx | sssp.co | pr.wk | tf.sl | tc.sx | ts.air | ts.pow | AVG
Cache | 0.0473 | 0.0472 | 0.0427 | 0.0431 | 0.1523 | 0.1522 | 0.1411 | 0.1412 | 0.0514 | 0.0513 | 0.0504 | 0.0502 | 0.0432 | 0.0428 | 0.0425 | 0.0426 | 0.0562 | 0.0561 | 0.0546 | 0.0545 | 0.0465 | 0.0462 | 0.0449 | 0.0447 | 0.0174 | 0.0175 | 0.018 | 0.0176 | 0.0158 | 0.0158 | 0.0159 | 0.0158 | 0.060261 | 0.059413 | 0.055142 | 0.043096
Network | 0.1324 | 0.0645 | 0.0477 | 0.0335 | 0.1543 | 0.0831 | 0.0697 | 0.0571 | 0.1645 | 0.0714 | 0.0543 | 0.0382 | 0.1769 | 0.0874 | 0.0732 | 0.0596 | 0.1658 | 0.0867 | 0.0684 | 0.0524 | 0.17 | 0.086 | 0.071 | 0.0558 | 0.2784 | 0.0818 | 0.0604 | 0.0317 | 0.2441 | 0.0671 | 0.0474 | 0.0207 | 0.17129 | 0.079855 | 0.065467 | 0.038031
Memory | 0.8203 | 0.8112 | 0.3902 | 0.3891 | 0.6935 | 0.678 | 0.3501 | 0.3408 | 0.7841 | 0.7654 | 0.3409 | 0.3251 | 0.78 | 0.7275 | 0.3734 | 0.3628 | 0.778 | 0.7625 | 0.3055 | 0.298 | 0.7835 | 0.7349 | 0.3597 | 0.3371 | 0.7042 | 0.6917 | 0.1568 | 0.1565 | 0.7401 | 0.7247 | 0.2334 | 0.232 | 0.76845 | 0.74027 | 0.33961 | 0.32773
1.94x
System Energy in Real Applications
-6.2%
SynCron reduces system energy significantly

## Slide 45
 | Synchronization Engine | ARM Cortex A7
Technology | 40nm | 28nm
Area | Total: 0.0461mm2 | Total: 0.45mm2
Power | 2.7mW | 100mW
9.78%
2.70%
SynCron has low area and power overheads
Area and Power Overheads

## Slide 46
Different memory technologies (HBM, HMC, DDR4)
Various data placement techniques
Various transfer latencies on links across NDP units
Overflow management cost
Various sizes for the Synchronization Table
SynCron is effective for a wide variety
of configurations
Sensitivity Studies

## Slide 47
Synchronization is a major system challenge for NDP systems
Prior schemes are not suitable or efficient for NDP systems
SynCron is the first end-to-end synchronization solution for NDP architectures
Syncron consists of four key techniques:
i. Hardware support for synchronization acceleration
ii. Direct buffering of synchronization variables
iii. Hierarchical message-passing communication
iv. Integrated hardware-only overflow management
SynCron’s benefits: 90.5% and 93.8% of performance and energy of an Ideal zero-overhead scheme
SynCron is highly-efficient, low-cost, easy-to-use, and general to support many synchronization primitives
Summary & Conclusion

## Slide 48
SynCron
Efficient Synchronization Support
for Near-Data-Processing Architectures
Christina Giannoula
christina.giann@gmail.com
Nandita Vijaykumar, Nikela Papadopoulou, Vasileios Karakostas
Ivan Fernandez, Juan Gómez Luna, Lois Orosa
Nectarios Koziris, Georgios Goumas, Onur Mutlu

## Slide 49
Backup Slides

## Slide 50
Baseline NDP Architecture

## Slide 51
Low Scalability of Coherence-based Synchronization in Real System

## Slide 52
Low Scalability of Coherence-based Synchronization in NDP Simulated System

## Slide 53
SynCron’s Overview

## Slide 54
Lock Operation using SynCron

## Slide 55
SynCron’s API

## Slide 56
Message Encoding of SynCron

## Slide 57
Message Opcodes for All Primitives

## Slide 58
The Synchronization Engine

## Slide 59
Synchronization Table Entry

## Slide 60
Control Flow of Message in Synchronization Engine

## Slide 61
Synchronization Variable of SynCron

## Slide 62
Qualitative Comparison with Closely Related Works

## Slide 63
Simulated System

## Slide 64
Evaluated Workloads

## Slide 65
Speedup in Simple Microbenchmarks

## Slide 66
Throughput of Pointer Chasing

## Slide 67
Speedup in Real Applications

## Slide 68
Scalability in Real Applications using SynCron

## Slide 69
System Energy in Real Applications

## Slide 70
Data Movement in Real Applications

## Slide 71
Various Transfer Latencies on Links Across NDP Units – High Contention

## Slide 72
Various Transfer Latencies on Links Across NDP Units – Low Contention

## Slide 73
Speedup using Different Memory Technologies

## Slide 74
Speedup in Real Applications using two Different Data Placement Techniques

## Slide 75
Speedup of Syncron over its Flat Variant in a Low-contention and Synchronization Non-intensive Scenario

## Slide 76
Speedup of Syncron over its Flat Variant in a Low-contention and Synchronization Intensive Scenario
and in a High-contention Scenario

## Slide 77
Synchronization Table Occupancy in Real Applications

## Slide 78
Slowdown in Real Applications when Varying the Synchronization Table Size

## Slide 79
Overflow Management Cost of Different Overflow Schemes

## Slide 80
Area and Power Overheads of the Synchronization Engine