## Slide 1: Transparent Offloading and Mapping (TOM) Enabling Programmer-Transparent Near-Data Processing in GPU Systems
Kevin Hsieh
Eiman Ebrahimi, Gwangsun Kim, Niladrish Chatterjee,
Mike O’Connor, Nandita Vijaykumar,
Onur Mutlu, Stephen W. Keckler
Notes: Today I am going to talk about “Transparent Offloading and Mapping (TOM): Enabling Programmer-Transparent Near-Data Processing in GPU Systems”. This is a joint work with my collaborators in CMU, NVIDIA, KAIST, and ETH Zurich

## Slide 2: GPUs and Memory Bandwidth
Many GPU applications are bottlenecked by
off-chip memory bandwidth
GPU
MEM
MEM
MEM
MEM
Notes: GPUs are widely used today and have many applications. However, many GPU applications require much more off-chip memory bandwidth than currently supplied by pins. This limitation makes many GPU applications not able to fully utilize the computation power of GPUs.

## Slide 3: Opportunity: Near-Data Processing
GPU
Near-data processing (NDP) can significantly improve performance
3D-stacked memory (memory stack)
Logic layer
Logic layer SM
Crossbar switch
Mem Ctrl
….
SM (Streaming Multiprocessor)
MEM
MEM
MEM
MEM
Mem Ctrl
Notes: One promising solution to this problem is using the “near data processing” architecture. This architecture replaces GPU memory with 3D-stacked memories, and add a logic layer in each memory stack. In each logic layer, we can add streaming multiprocessors (or logic layer SM), which has similar functionality as the SMs in GPU. With this architecture, the GPU can offload memory intensive operations to these logic layer SMs, which can utilize the abundant internal memory bandwidth in 3D-stacked memories to improve GPU performance.

## Slide 4: Near-Data Processing: Key Challenges
Which operations should we offload?
How should we map data across multiple memory stacks?
Notes: There are two key challenges to enable the near data processing architecture. We need to determine which operations should we offload to memory stack. Also, we need to determine how to map data across multiple memory stacks.

## Slide 5: Key Challenge 1
?
Which operations should be executed on the logic layer SMs?
?
GPU
Logic layer SM
Crossbar switch
Mem Ctrl
….
Mem Ctrl
T = D0; D0 = D0 + D2; D2 = T - D2;
T = D1; D1 = D1 + D3; D3 = T - D3;
T = D0; d_Dst[i0] = D0 + D1;
d_Dst[i1] = T - D1;
?
Notes: For the first challenge, we need to determine which operations should be executed on the main GPUs, and which operations should be executed on the logic layer SMs. This is important because we want to execute compute intensive code in the GPU, and the memory intensive code in the logic layer SM.

## Slide 6: Key Challenge 2
How should data be mapped across multiple 3D memory stacks?
?
GPU
?
C = A + B
A
B
C
Notes: For the second challenge, we need to determine how to map data when a system consists of multiple memory stacks. For example, if we execute “C = A + B” in a logic layer SM, we want A, B, and C are all mapped to the same memory stack so we can fully utilize the internal memory bandwidth in memory stacks. If it’s not the case, we still need to go through off-chip memory channels to get the data, and loses the benefit of near data processing.

## Slide 7: The Problem
Solving these two key challenges requires significant programmer effort
Challenge 1: Which operations to offload?
  Programmers need to identify offloaded operations, and consider run time behavior
Challenge 2: How to map data across multiple memory stacks?
  Programmers need to map all the operands in each offloaded operation to the same memory stack
Notes: In state-of-art proposals, the major problem is that solving these two challenges requires significant programmer effort. For the first challenge, the programmer need to explicitly identify offloaded operations. Even programmers are willing to do that, they may not be able to make good decisions because the offloading efficiency also depends on run time variations. For the second challenge, programmers need to find all the operands in each offloaded operations and map them. Both are very difficult tasks for programmers. Also, only rewritten code can get the benefit of near-data processing architecture.

## Slide 8: Our Goal
Enable near-data processing in GPUs transparently to the programmer
Notes: Therefore, our goal of this work is to enable near-data processing in GPUs transparently, without any programmer intervention.

## Slide 9: Transparent Offloading and Mapping (TOM)
Component 1 - Offloading: A new programmer-transparent mechanism to identify and decide what code portions to offload
  The compiler identifies code portions to potentially offload based on memory profile.
  The runtime system decides whether or not to offload each code portion based on runtime characteristics.
Component 2 - Mapping: A new, simple, programmer-transparent data mapping mechanism to maximize data co-location in each memory stack
Notes: Read the slide

## Slide 10: Outline
Motivation and Our Approach
Transparent Offloading
Transparent Data Mapping
Implementation
Evaluation
Conclusion
Notes: I am going to talk about the first component, transparent offloading, to automatically determine what code portions to offload.

## Slide 11: TOM: Transparent Offloading
Static compiler analysis
Identifies code blocks as offloading candidate blocks
Uses run-time information to make the final offloading decision for each code block
Dynamic offloading control
Notes: As I just mentioned, our transparent offloading mechanism consists of two components. The first component is static compiler analysis, which identifies the code blocks that are potentially beneficial for offloading as the offloading candidates blocks. The second component is dynamic offloading control, which uses run-time information to decide whether these offloading candidates blocks should be really offloaded.

## Slide 12: TOM: Transparent Offloading
Static compiler analysis
Identifies code blocks as offloading candidate blocks
Uses run-time information to make the final offloading decision for each code block
Dynamic offloading control
Notes: Let’s talk about static compiler analysis first.

## Slide 13: Static Analysis: What to Offload?
Goal: Save off-chip memory bandwidth
GPU
Memory
Load
Addr
Data
GPU
Memory
Store
Addr +Data
Ack
GPU
Memory
Near-Data Processing
Live-in Reg
Live-out Reg
Offloading benefit: load & store instructions
Offloading cost: live-in & live-out registers
Conventional System
Offload
Compiler uses equations (in paper) for cost/benefit analysis
Notes: The static compiler analysis identifies what code portion to offload. As our goal is to save off-chip memory bandwidth, let’s take a look at the what we can save by offloading each operations. If we don’t offload a code block, each load instruction would need to send address to the memory, and get data back from the memory. Similarly, each store instruction would need to send address and data to the memory, and get the ack packet from the memory. These traffic can be saved if we offload this code block. However, there are costs to offload. We need to send live-in registers of this code block to memory. The live-in registers are the register values that are generated outside of the block. Similarly, we need to send the live-out registers back to GPU after the execution of a offloaded code block. Therefore, the offloading benefit comes from load/store instructions, and the offloading cost comes from live-in / live-out registers. We derive a equation to determine whether a code block could be beneficial to offload, and the details on in the paper.

## Slide 14: Offloading Candidate Block Example
...
float D0 = d_Src[i0];
float D1 = d_Src[i1];
float D2 = d_Src[i2];
float D3 = d_Src[i3];
float T;
T = D0; D0 = D0 + D2; D2 = T - D2;
T = D1; D1 = D1 + D3; D3 = T - D3;
T = D0; d_Dst[i0] = D0 + D1;
d_Dst[i1] = T - D1;
T = D2; d_Dst[i2] = D2 + D3;
d_Dst[i3] = T - D3;
Code block in Fast Walsh Transform (FWT)
Notes: Let’s use a real code block as an example

## Slide 15: Offloading Candidate Block Example
...
float D0 = d_Src[i0];
float D1 = d_Src[i1];
float D2 = d_Src[i2];
float D3 = d_Src[i3];
float T;
T = D0; D0 = D0 + D2; D2 = T - D2;
T = D1; D1 = D1 + D3; D3 = T - D3;
T = D0; d_Dst[i0] = D0 + D1;
d_Dst[i1] = T - D1;
T = D2; d_Dst[i2] = D2 + D3;
d_Dst[i3] = T - D3;
Offloading benefit outweighs cost
Cost: Live-in registers
Benefit: Load/store inst
Code block in Fast Walsh Transform (FWT)
Notes: In this example, the variables that are marked as red are the live-in registers, which are the cost of offloading. The code portions that are circles as green are load/store instructions, which are the benefit of offloading. By applying the equation of cost/benefit analysis, we determine the amount of data moved by load/store instructions is higher than the amount of live-in/live-outs, so the compiler marks it as an offloading candidate block

## Slide 16: Conditional Offloading Candidate Block
The cost of a loop is fixed, but the benefit of a loop is determined by the loop trip count.
The compiler marks the loop as a conditional offloading candidate block, and provides the offloading condition to hardware (e.g., loop trip count > N)
...
for (n = 0; n < Nmat; n++){ L_b[n] = −v ∗ delta /( 1.0 + delta ∗ L[n]);
}
...
Cost: Live-in registers
Benefit: Load/store inst
Code block in LIBOR Monte Carlo (LIB)
Notes: Sometimes, the decision can not be made statically. For example this code block is a loop. If the compiler just apply the simple cost / benefit analysis, it would have determined it is not an offloading candidate block. However, the cost of offloading a loop is fixed, but the benefit is determined by its loop trip count. The more iterations it executes, the more benefits we can get. Therefore in this case, the compiler marks it as a conditional offloading candidate block, and provides the offloading condition to hardware. The condition can be loop trip count needs to larger than certain number.

## Slide 17: TOM: Transparent Offloading
Static compiler analysis
Identifies code blocks as offloading candidate blocks
Uses run-time information to make the final offloading decision for each code block
Dynamic offloading control
Notes: As I just mentioned, our transparent offloading mechanism consists of two components. The first component is static compiler analysis, which identifies the code blocks that are potentially beneficial for offloading as the offloading candidates blocks. The second component is dynamic offloading control, which uses run-time information to decide whether these offloading candidates blocks should be really offloaded.

## Slide 18: When Offloading Hurts: Bottleneck Channel
RX
TX
Main GPU
Memory stack
Data
Transmit channel becomes full,
leading to slowdown with offloading.
Data
Data
Data
TX
Bottlenecked!
Reg
Reg
Reg
Notes: We need to make offloading decision dynamically because offloading hurt performance in two situations. In the first case, we can have a code block that need to get two data packets from the memory, and send two data packets to the memory. Offloading this block needs to send three register packets to the memory. For illustration purpose, the size of register and data is the same. Assuming now there is too much traffic on the TX channel and it becomes the bottleneck. Offloading this block will make the TX channel worse, and slowdowns the system.

## Slide 19
TX
SM capacity
Full
Memory stack SM becomes full,
leading to slowdown with offloading.
Main GPU
Memory stack
RX
When Offloading Hurts: Memory Stack Computational Capacity
Too many warps!
Notes: Another situation is the offloaded blocks reach the capacity limit of the logic layer SM. When that happens, more offloading simply waste the compute bandwidth of main GPU and leads to slowdown with offloading

## Slide 20: Dynamic Offloading Control: When to Offload?
Key idea: offload only when doing so is estimated to be beneficial
Mechanism:
  The hardware does not offload code blocks that increase traffic on a bottlenecked channel
  When the computational capacity of a logic layer’s SM is full, the hardware does not offload more blocks to that logic layer
Notes: Therefore, the key idea of our dynamic offloading control is to ensure the offloading is beneficial. First, we do not introduce more traffic on the bottleneck channel. The hardware monitor each channel and does not offload the candidate blocks that do not save memory bandwidth on the bottleneck channels. Second, the hardware monitors how many offloaded blocks are executed in each logic layer SM, and does not offload more when it reaches the limit of the SM.

## Slide 21: Outline
Motivation and Our Approach
Transparent Offloading
Transparent Data Mapping
Implementation
Evaluation
Conclusion
Notes: Now that we have introduced transparent offloading, let’s talk about the second component of TOM: transparent data mapping. This mechanism is designed to tackle the challenge of mapping data into multiple memory stacks.

## Slide 22: TOM: Transparent Data Mapping
Goal: Maximize data co-location for offloaded operations in each memory stack
Key Observation: Many offloading candidate blocks exhibit a predictable memory access pattern: fixed offset
Notes: The goal of transparent data mapping is to maximize data co-location in each memory stack for offloaded operations. We make a key observation that may offloading candidate blocks exhibit a predictable pattern: fixed offset. This is a very useful access pattern for our goal. Let’s use an example to explain.

## Slide 23: Fixed Offset Access Patterns: Example
...
for (n = 0; n < Nmat; n++){ L_b[n] = −v ∗ delta /( 1.0 + delta ∗ L[n]);
}
...
L_b base
n
L base
n
Some address bits are always the same:
Use them to decide memory stack mapping
85% of offloading candidate blocks exhibit fixed offset access patterns
Notes: In this code block, there are two accesses go to two arrays. Interestingly, they are always accessed with the same index. If we decompose their addresses, we will find that part of them is the base address of the array, and part of them is the index. As the index is always the same, their offset is always the same. Therefore, there will be always some address bits that are always the same. If we use these address bits to determine which memory stack we should map to, we can maximize the co-location of these two operands.

## Slide 24: Transparent Data Mapping: Approach
Key idea: Within the fixed offset bits, find the memory stack address mapping bits so that they maximize data co-location in each memory stack
Approach: Execute a tiny fraction (e.g, 0.1%) of the offloading candidate blocks to find the best mapping among the most common consecutive bits
Problem: How to avoid the overhead of data remapping after we find the best mapping?
Notes: Therefore, our transparent data mapping mechanism is based on the key observation that may offloading candidate blocks exhibit a predictable pattern: fixed offset. So we execute a tiny fraction of the offloading candidate blocks to find out the best mapping, and use it to map data into multiple memory stacks. However, we could introduce excessive data remapping overhead. So the problem is how to avoid the overhead of data remapping.

## Slide 25: Conventional GPU Execution Model
GPU
CPU
GPU Memory
CPU Memory
GPU Data
Launch Kernel
Notes: We can take advantage of GPU execution model to solve this problem. In conventional GPU execution model, the CPU needs to copy the GPU data from CPU memory to GPU memory. The CPU then launch kernel in GPU, and the GPU accesses GPU memory directly to finish the task.

## Slide 26: Transparent Data Mapping: Mechanism
GPU
CPU
GPU Memory
CPU Memory
GPU Data
Delay Memory Copy and Launch Kernel
Learn the best mapping among the most common consecutive bits
Memory copy happens only after the best mapping is found
There is no remapping overhead
Notes: In our transparent data mapping, the GPU data also starts at CPU memory. The difference is when CPU wants to copy memory from CPU to GPU, we delay the memory copy. Instead, we just launch the kernel in GPU, and the GPU executes on CPU memory for a tiny fraction of the code. This can be achieved by the GPU virtual memory system. Once the GPU learns the best mapping, it copies the memory to GPU memory with this mapping, and executes as usual. With this mechanism, we don’t’ pay remapping overhead, and only pay minimal initial learning overhead.

## Slide 27: Outline
Motivation and Our Approach
Transparent Offloading
Transparent Data Mapping
Implementation
Evaluation
Conclusion
Notes: After introduction of both mechanisms of TOM. Let’s talk about how TOM can be realized in a GPU pipeline.

## Slide 28: TOM: Putting It All Together
Fetch/
I-Cache/
Decode
Scoreboard
Instruction Buffer
Offload Controller
Issue
Operand Collector
ALU
MEM
Data Cache
Memory Port / MSHR
Channel Busy Monitor
Shared
Mem
Makes offloading decision
Sends offloading request
Monitors TX/RX
memory bandwidth
Notes: This is a typical GPU pipeline. Let’s focus on what we need to add into it for TOM. First, we need a offload controller, which makes offloading decision and sends offloading request to memory stacks. Second, we need a channel busy monitor, to monitor the TX/RX memory bandwidth and report bottlenecked channel. When a warp is issued to pipeline, it will first go to instruction buffer. When the instruction buffer detects it is a beginning of an offloading candidate block, it will send this warp to the offload controller. The offload controller makes a dynamic offloading decision based on runtime information, and send this warp to memory stack if it decides to offload.

## Slide 29: Outline
Motivation and Our Approach
Transparent Offloading
Transparent Data Mapping
Implementation
Evaluation
Conclusion
Notes: I am going to talk about our evaluation results of TOM.

## Slide 30: Evaluation Methodology
Simulator: GPGPU-Sim
Workloads:
  Rodinia, GPGPU-Sim workloads, CUDA SDK
System Configuration:
  68 SMs for baseline, 64 + 4 SMs for NDP system
  4 memory stacks
  Core: 1.4 GHz, 48 warps/SM
  Cache: 32KB L1, 1MB L2
  Memory Bandwidth:
    GPU-Memory: 80 GB/s per link, 320 GB/s total
    Memory-Memory: 40 GB/s per link
    Memory Stack: 160 GB/s per stack, 640 GB/s total
Notes: This is our evaluation methodology, We use GPGPU-sim and make sure the number of SMs are the same between baseline and our proposed system.

## Slide 31: Results: Performance Speedup
Chart: Speedup
| TOFF | TOM | TOFF | TOM | TOFF | TOM | TOFF | TOM | TOFF | TOM | TOFF | TOM | TOFF | TOM | TOFF | TOM | TOFF | TOM | TOFF | TOM | TOFF | TOM | BP | BFS | KM | CFD | HW | LIB | RAY | FWT | SP | RD | AVG
NDP | 0.99994 | 1.0238 | 1.2875 | 1.2081 | 1.0334 | 1.394 | 1.254 | 1.2401 | 1.0524 | 1.0521 | 1.3024 | 1.5212 | 1.0314 | 1.0198 | 1.1309 | 1.2778 | 1.4197 | 1.512 | 1.5147 | 1.7557 | 1.2026 | 1.3004
30% average (76% max)
performance improvement
1.20
1.30
Notes: We first look at performance. In this chart, Y-axis is the speedup, normalized to baseline. We illustrate two results for each workloads. One is “TOFF”, which stands for transparent offloading, the first component of TOM. Another is “TOM”, which have both components of TOM. As we can see, only using transparent offloading can give us 20% average speedup, and using both components of TOM can give us 30% average speedup, up to 76%.

## Slide 32: Results: Off-chip Memory Traffic
Chart: Memory Traffic
| TOFF | TOM | TOFF | TOM | TOFF | TOM | TOFF | TOM | TOFF | TOM | TOFF | TOM | TOFF | TOM | TOFF | TOM | TOFF | TOM | TOFF | TOM | TOFF | TOM | BP | BFS | KM | CFD | HW | LIB | RAY | FWT | SP | RD | AVG
GPU-Memory RX | 0.37847 | 0.37255 | 0.57684 | 0.60546 | 0.77841 | 0.55817 | 0.40912 | 0.40733 | 0.61558 | 0.61127 | 0.3426 | 0.36004 | 0.22314 | 0.22169 | 0.3369 | 0.34412 | 0.58182 | 0.58148 | 0.56294 | 0.56282 | 0.48058 | 0.46249
GPU-Memory TX | 0.58945 | 0.58921 | 0.21528 | 0.2228 | 0.086801 | 0.062518 | 0.55467 | 0.557 | 0.021214 | 0.021305 | 0.41577 | 0.4335 | 0.66665 | 0.69834 | 0.49603 | 0.50005 | 0.29003 | 0.29141 | 0.063856 | 0.063843 | 0.33998 | 0.344
Memory-Memory | 0.18227 | 0.019979 | 0.21262 | 0.1724 | 0.29642 | 0.055718 | 0.1502 | 9.881e-05 | 0.0066019 | 0.0065505 | 0.19328 | 0.17036 | 0.39714 | 0.18526 | 0.058573 | 0.010136 | 9.0275e-05 | 9.2467e-05 | 0.28348 | 0 | 0.17807 | 0.06206
13% average (37% max) memory traffic reduction
2.5X memory-memory traffic reduction
Notes: Next, we look at off-chip memory traffic. The Y-axis in this chart is the memory traffic, normalized to the baseline. We segment the traffic into three categories, which are GPU-memory RX channel, GPU-memory TX channel, and memory-memory channel. As we can see, using bmap can reduce memory traffic between GPU and memory, but overall does not save much due to extra memory-to-memory traffic. With tmap, we significantly reduce memory-to-memory traffic. Overall, we reduce 13% memory traffic (up to 37%), and more importantly, we reduce 2.5X memory-memory traffic with tmap. For some workloads, transparent data mapping can even reduce the memory-to-memory traffic to almost 0.

## Slide 33: More in the Paper
Other design considerations
  Cache coherence
  Virtual memory translation
Effect on energy consumption
Sensitivity studies
  Computational capacity of logic layer SMs
  Internal and cross-stack bandwidth
Area estimation (0.018% of GPU area)
Notes: There are more details in the paper. We discuss how we handle cache coherence and virtual memory translation in logic layer SM. We also provide our evaluation on energy consumption. Also, we do sensitivity study on the computational capacity of logic layer SMs, and different internal and cross-stack memory bandwidth. We also provide our area estimation in the paper.

## Slide 34: Conclusion
Near-data processing is a promising direction to alleviate the memory bandwidth bottleneck in GPUs
Problem: It requires significant programmer effort
  Which operations to offload?
  How to map data across multiple memory stacks?
Our Approach: Transparent Offloading and Mapping
  A new programmer-transparent mechanism to identify and decide what code portions to offload
  A programmer-transparent data mapping mechanism to maximize data co-location in each memory stack
Key Results: 30% average (76% max) performance improvement in GPU workloads
Notes: To conclude, near data processing is a promising direction to tackle the off-chip memory bandwidth bottleneck in GPU. The major problem of enabling near data processing is it requires a lot of programmer effort. The programmer needs to decide which operations to be offloaded, and how to map data to multiple memory stacks. We propose transparent offloading and mapping, TOM, that using compiler to identify code portions to potentially offload, and using the run-time system to make the offloading decision. We also introduce a programmer transparent data mapping mechanism to maximize offloaded data co-location. Our evaluation shows TOM can achieve 30% average performance improvement, up to 76%, in existing workloads without any program change.

## Slide 35: Transparent Offloading and Mapping (TOM) Enabling Programmer-Transparent Near-Data Processing in GPU Systems
Kevin Hsieh
Eiman Ebrahimi, Gwangsun Kim, Niladrish Chatterjee,
Mike O’Connor, Nandita Vijaykumar,
Onur Mutlu, Stephen W. Keckler
Notes: Today I am going to talk about “Transparent Offloading and Mapping (TOM): Enabling Programmer-Transparent Near-Data Processing in GPU Systems”. This is a joint work with my collaborators in CMU, NVIDIA, KAIST, and ETH Zurich

## Slide 36: Observation on Access Pattern
85% of offloading candidate blocks exhibit fixed offset pattern
Chart: Percent of offloading candidate blocks
| BP | BFS | KM | CFD | HW | LIB | RAY | FWT | SP | RD | AVG
All accesses fixed offset | 0.5 | 0 | 0 | 0.5 | 0 | 0.44444 | 0.25 | 0.5 | 0 | 1 | 0.31944
75%-99% fixed offset | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
50%-75% fixed offset | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
25%-50% fixed offset | 0 | 0.5 | 0 | 0.25 | 0.33333 | 0 | 0.5 | 0 | 0 | 0 | 0.15833
0%-25% fixed offset | 0.5 | 0.5 | 1 | 0.25 | 0.095238 | 0.33333 | 0 | 0 | 1 | 0 | 0.36786
No access fixed offset | 0 | 0 | 0 | 0 | 0.57143 | 0.22222 | 0.25 | 0.5 | 0 | 0 | 0.15437

## Slide 37: Bandwidth Change Equations

## Slide 38: Best memory mapping search space
We only need 2 bits to determine the memory stack in a system with 4 memory stacks. The result of the sweep starts from bit position 7 (128B GPU cache line size) to bit position 16 (64 KB).
Based on our results, sweeping into higher bits does not make a noticeable difference.
This search is done by a small hardware (memory mapping analyzer), which calculates how many memory stacks would be accessed by each offloading candidate instance for all different potential memory stack mappings (e.g., using bits 7:8, 8:9, ..., 16:17 in a system with four memory stacks)

## Slide 39: Best Mapping From Different Fraction of Offloading Candidate Blocks
Chart: Probability of accessing one memory stack in an offloading candidate instance
| BP | BFS | KM | CFD | HW | LIB | RAY | FWT | SP | RD | AVG
Baseline mapping | 3e-05 | 0.38869 | 0 | 0 | 0.06341 | 0.01896 | 0.85938 | 0.83261 | 1 | 1 | 0.41631
Best mapping in first 0.1% NDP blocks | 0.66108 | 0.44427 | 0.18962 | 1 | 0.32997 | 1 | 0.85829 | 1 | 1 | 1 | 0.74832
Best mapping in first 0.5% NDP blocks | 0.66108 | 0.44427 | 0.18962 | 1 | 0.44058 | 1 | 0.85829 | 1 | 1 | 1 | 0.75938
Best mapping in first 1% NDP blocks | 0.66108 | 0.44427 | 0.18962 | 1 | 0.44058 | 1 | 0.85829 | 1 | 1 | 1 | 0.75938
Best mapping in all NDP blocks | 0.71006 | 0.44429 | 0.18962 | 1 | 0.5187 | 1 | 0.8615 | 1 | 1 | 1 | 0.77242

## Slide 40: Energy Consumption Results
Chart: Normalized Energy
| no-ctrl | ctrl | no-ctrl | ctrl | no-ctrl | ctrl | no-ctrl | ctrl | no-ctrl | ctrl | no-ctrl | ctrl | no-ctrl | ctrl | no-ctrl | ctrl | no-ctrl | ctrl | no-ctrl | ctrl | no-ctrl | ctrl | no-ctrl | ctrl | no-ctrl | ctrl | no-ctrl | ctrl | no-ctrl | ctrl | no-ctrl | ctrl | no-ctrl | ctrl | no-ctrl | ctrl | no-ctrl | ctrl | no-ctrl | ctrl | no-ctrl | ctrl | no-ctrl | ctrl | bmap | tmap | bmap | tmap | bmap | tmap | bmap | tmap | bmap | tmap | bmap | tmap | bmap | tmap | bmap | tmap | bmap | tmap | bmap | tmap | bmap | tmap | BP | BFS | KM | CFD | HW | LIB | RAY | FWT | SP | RD | AVG
SMs | 1.0252 | 1.0138 | 0.92381 | 0.91837 | 0.45557 | 0.4557 | 0.36417 | 0.37939 | 0.62174 | 0.54197 | 0.53949 | 0.40265 | 0.85489 | 0.81871 | 0.73655 | 0.74179 | 0.89974 | 0.89912 | 0.89978 | 0.8998 | 1.2212 | 1.2221 | 0.8343 | 0.81272 | 0.93227 | 0.92763 | 0.92895 | 0.93444 | 0.58715 | 0.5934 | 0.60354 | 0.57016 | 0.72345 | 0.69703 | 0.65351 | 0.63106 | 0.7014 | 0.66836 | 0.54614 | 0.50506 | 0.80226 | 0.78379 | 0.70302 | 0.67954
Off-chip Links | 0.060601 | 0.053545 | 0.043817 | 0.040764 | 0.071418 | 0.07107 | 0.057119 | 0.059602 | 0.10639 | 0.068782 | 0.09295 | 0.061903 | 0.10896 | 0.088612 | 0.08215 | 0.079156 | 0.034838 | 0.034814 | 0.038339 | 0.038317 | 0.095702 | 0.095961 | 0.039055 | 0.035933 | 0.044708 | 0.041676 | 0.044035 | 0.043095 | 0.056893 | 0.055319 | 0.065463 | 0.059274 | 0.079848 | 0.075653 | 0.074011 | 0.070618 | 0.087848 | 0.064645 | 0.067933 | 0.054783 | 0.074721 | 0.065008 | 0.060487 | 0.054344
DRAM Devices | 0.054418 | 0.046925 | 0.043169 | 0.042497 | 0.55562 | 0.55861 | 0.51843 | 0.50237 | 0.49132 | 0.45027 | 0.4073 | 0.42276 | 0.087049 | 0.087252 | 0.076936 | 0.074353 | 0.00053786 | 0.00048563 | 0.00050478 | 0.00050353 | 0.098267 | 0.066541 | 0.1111 | 0.073355 | 0.015955 | 0.016864 | 0.016069 | 0.017117 | 0.25096 | 0.24856 | 0.27105 | 0.26504 | 0.093682 | 0.094122 | 0.084401 | 0.084207 | 0.34111 | 0.066976 | 0.54384 | 0.067106 | 0.19889 | 0.16366 | 0.20728 | 0.15493

## Slide 41: Sensitivity to Computational Capacity of memory stack SMs
Chart: Speedup
| BP | BFS | KM | CFD | HW | LIB | RAY | FWT | SP | RD | AVG
no-ctrl-1X-warp | 0.66245 | 0.97935 | 1.0693 | 1.0144 | 1.0513 | 0.36421 | 1.045 | 1.1683 | 1.2673 | 1.0792 | 0.97007
ctrl-1X-warp | 1.0238 | 1.2081 | 1.394 | 1.2401 | 1.0521 | 1.5212 | 1.0198 | 1.2778 | 1.512 | 1.7557 | 1.3004
ctrl-2X-warp | 1.018 | 1.3773 | 1.3492 | 1.3209 | 1.042 | 1.5374 | 1.0304 | 1.3233 | 1.539 | 1.4573 | 1.2995
ctrl-4X-warp | 1.0143 | 1.4308 | 1.3373 | 1.4907 | 1.0395 | 1.5298 | 1.0365 | 1.3446 | 1.6142 | 1.0953 | 1.2933
Chart: Normalized Memory Traffic
| BP | BFS | KM | CFD | HW | LIB | RAY | FWT | SP | RD | AVG
no-ctrl-1X-warp | 0.83668 | 1.0984 | 0.24434 | 0.83933 | 0.091904 | 0.80355 | 1.0305 | 0.56169 | 0.65547 | 0.0043893 | 0.61662
ctrl-1X-warp | 0.98174 | 1.0007 | 0.67641 | 0.96443 | 0.63912 | 0.9639 | 1.1053 | 0.8543 | 0.87298 | 0.62666 | 0.86855
ctrl-2X-warp | 0.96539 | 0.93806 | 0.57676 | 0.95691 | 0.15186 | 0.95932 | 1.084 | 0.76255 | 0.84111 | 0.25325 | 0.74892
ctrl-4X-warp | 0.96075 | 0.97605 | 0.12373 | 0.93858 | 0.09966 | 0.96102 | 1.0665 | 0.68659 | 0.7411 | 0.004259 | 0.65582

## Slide 42: Sensitivity to Internal Memory Bandwidth
Chart: Speedup
| BP | BFS | KM | CFD | HW | LIB | RAY | FWT | SP | RD | AVG
2X-internal-BW | 1.0238 | 1.2081 | 1.394 | 1.2401 | 1.0521 | 1.5212 | 1.0198 | 1.2778 | 1.512 | 1.7557 | 1.3004
1X-internal-BW | 1.01 | 1.2188 | 1.3333 | 1.2629 | 0.99884 | 1.5302 | 1.0234 | 1.3257 | 1.4594 | 1.619 | 1.2782