## Slide 1
ThyNVM: Enabling Software-Transparent Crash Consistency in Persistent Memory Systems
Jinglei Ren (Tsinghua University) Jishen Zhao (UC, Santa Cruz) Samira Khan (University of Virginia) Jongmoo Choi (Dankook University) Yongwei Wu (Tsinghua University) Onur Mutlu (CMU)
NVM provides an opportunity to manipulate persistent data directly
Problem: System crash can result in permanent data corruption in NVM
Current Solution: Explicit interfaces to manage consistency NV-Heaps [ASPLOS’11], BPFS [SOSP’09], Mnemosyne [ASPLOS’11]
Idea: Periodic checkpointing of data managed by hardware
Insight: A tradeoff between checkpointing latency and metadata storage overhead
void hashtable_update(hashtable_t* ht,
void *key, void *data)
{
list_t* chain = get_chain(ht, key);
pair_t* pair;
pair_t updatePair;
updatePair.first = key;
pair = (pair_t*) list_find(chain,
&updatePair);
pair->second = data;
}
void TMhashtable_update(TMARCGDECL
hashtable_t* ht, void *key, void*data){
list_t* chain = get_chain(ht, key);
pair_t* pair;
pair_t updatePair;
updatePair.first = key;
pair = (pair_t*) TMLIST_FIND(chain,
&updatePair);
pair->second = data;
}
Need a new implementation
Third party code
can be inconsistent
Prohibited
Operation
GOAL: Software transparent consistency in persistent memory systems
Execute legacy apps, No burden on programmers, Enable easier integration of NVM
1. Link to next
2. Link to prev
Checkpointing granularity
  Small granularity: large metadata
  Large granularity: small metadata
Latency and location
  Writeback from DRAM: long latency
  Remap in NVM: short latency
DRAM
NVM
High write locality pages in DRAM,
low write locality pages in NVM
Page Writeback
in DRAM
Block Remapping
in NVM
GOOD FOR
STREAMING WRITES
GOOD FOR
RANDOM WRITES
time
Epoch 0
Epoch 1
Epoch 2
Epoch 0
Epoch 1
Running
Checkpointing
Running
Checkpointing
Running
Checkpointing
Hides the long latency of Page Writeback
PAGE
CACHE BLOCK
One Entry Per Page
Small Metadata
One Entry Per Block
Huge Metadata
PAGE GRANULARITY
BLOCK GRANULARITY
Working location
Checkpoint location
X
X’
Y
Y’
W
Long latency of writing back data to NVM
DRAM
NVM
DRAM-BASED WRITEBACK
NVM-BASED REMAPPING
Short latency in NVM-based remapping
DRAM
NVM
No Copy during checkpointing,
remap in a new location during a write
1. DUAL GRANULARITY CHECKPOINTING
2. OVERLAPPING CHECKOINTING AND EXECUTION
ADAPTIVITY TO ACCESS PATTERN
Chart: Normalized Write Traffic To NVM
| Journal | Shadow | ThyNVM
Series 1 | 1 | 3.7057 | 1.1221
Chart: Normalized Write Traffic To NVM
| Journal | Shadow | ThyNVM
Series 1 | 1 | 0.39546 | 0.6687
RANDOM SEQUENTIAL
ThyNVM adapts to both access patterns
Journaling is better for Random and
Shadow paging is better for Sequential
LOW
LOW
LOW
LOW
PERFORMANCE OF
LEGACY CODE
Chart: Normalized IPC
| gcc | bwaves | milc | leslie. | soplex | Gems | lbm | omnet
Ideal DRAM | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Ideal NVM | 0.97621 | 0.88199 | 0.93493 | 0.8921 | 0.98908 | 0.99999 | 0.87038 | 0.99448
ThyNVM | 0.98469 | 0.92343 | 0.96227 | 0.94344 | 0.99253 | 0.99994 | 0.92862 | 0.99935
Provides consistency without
significant performance overhead
Within -4.9%/+2.7% of an
idealized DRAM/NVM system
Ideal DRAM: DRAM-based, no cost for consistency,
Lowest latency system
Ideal NVM: NVM-based, no cost for consistency, NVM has higher latency than DRAM
Journaling: Hybrid, commit dirty cache blocks, Leverages DRAM to buffer dirty blocks
Shadow Paging: Hybrid, copy-on-write pages, Leverages DRAM to buffer dirty pages
RANDOM SEQUENTIAL
Chart: Percentage of Execution Time
| Journal | Shadow | ThyNVM
Series 1 | 12.8221 | 45.2162 | 2.4662
Chart: Percentage of Execution Time
| Journal | Shadow | ThyNVM
Series 1 | 35.2552 | 9.6103 | 5.6131
Stalls the application for a negligible time
ThyNVM spends only 2.4%/5.5% of the execution time on checkpointing
45%
35%
Can spend 35-45% of the execution
on checkpointing
OVERLAPPING CHECKPOINTING AND EXECUTION
ThyNVM
Writeback data in NVM during checkpointing