## Slide 1: Enabling Software-Transparent Crash Consistency In Persistent Memory Systems
ThyNVM
Jinglei Ren, Jishen Zhao, Samira Khan,
Jongmoo Choi, Yongwei Wu, and Onur Mutlu

## Slide 2: TWO-LEVEL STORAGE MODEL
CPU
MEMORY
STORAGE
VOLATILE
FAST
BYTE ADDR
NONVOLATILE
SLOW
BLOCK ADDR
Ld/St
FILE
I/O
DRAM

## Slide 3: TWO-LEVEL STORAGE MODEL
CPU
MEMORY
STORAGE
VOLATILE
FAST
BYTE ADDR
NONVOLATILE
SLOW
BLOCK ADDR
Ld/St
FILE
I/O
DRAM
PCM, STT-RAM
NVM
Non-volatile memories combine characteristics of memory and storage

## Slide 4: PERSISTENT MEMORY
CPU
PERSISTENTMEMORY
Provides an opportunity to manipulate persistent data directly
Ld/St
NVM

## Slide 5: CHALLENGE: CRASH CONSISTENCY
System crash can result in
permanent data corruption in NVM
Persistent Memory System

## Slide 6: CURRENT SOLUTIONS
Explicit interfaces to manage consistency
  NV-Heaps [ASPLOS’11], BPFS [SOSP’09], Mnemosyne [ASPLOS’11]
AtomicBegin {
Insert a new node;
} AtomicEnd;
Limits adoption of NVM
Have to rewrite code with clear partition
between volatile and non-volatile data
Burden on the programmers

## Slide 7: OUR APPROACH: ThyNVM
Goal:
Software transparent consistency in
persistent memory systems

## Slide 8: ThyNVM: Summary
Checkpoints at multiple granularities to reduce both checkpointing latency and metadata overhead
Overlaps checkpointing and execution to reduce checkpointing latency
Adapts to DRAM and NVM characteristics
Performs within 4.9% of an idealized DRAM with zero cost consistency
A new hardware-based
checkpointing mechanism

## Slide 9: OUTLINE
Crash Consistency Problem
Current Solutions
ThyNVM
Evaluation
Conclusion

## Slide 10: CRASH CONSISTENCY PROBLEM
Add a node to a linked list
1. Link to next
2. Link to prev
System crash can result in
inconsistent memory state

## Slide 11: OUTLINE
Crash Consistency Problem
Current Solutions
ThyNVM
Evaluation
Conclusion

## Slide 12: CURRENT SOLUTIONS
void hashtable_update(hashtable_t* ht,
void *key, void *data)
{
list_t* chain = get_chain(ht, key);
pair_t* pair;
pair_t updatePair;
updatePair.first = key;
pair = (pair_t*) list_find(chain,
&updatePair);
pair->second = data;
}
Example Code
update a node in a persistent hash table
Explicit interfaces to manage consistency
  NV-Heaps [ASPLOS’11], BPFS [SOSP’09], Mnemosyne [ASPLOS’11]

## Slide 13: CURRENT SOLUTIONS
void TMhashtable_update(TMARCGDECL
hashtable_t* ht, void *key, void*data){
list_t* chain = get_chain(ht, key);
pair_t* pair;
pair_t updatePair;
updatePair.first = key;
pair = (pair_t*) TMLIST_FIND(chain,
&updatePair);
pair->second = data;
}

## Slide 14: CURRENT SOLUTIONS
void TMhashtable_update(TMARCGDECL
hashtable_t* ht, void *key, void*data){
list_t* chain = get_chain(ht, key);
pair_t* pair;
pair_t updatePair;
updatePair.first = key;
pair = (pair_t*) TMLIST_FIND(chain,
&updatePair);
pair->second = data;
}
Manual declaration of persistent components

## Slide 15: CURRENT SOLUTIONS
void TMhashtable_update(TMARCGDECL
hashtable_t* ht, void *key, void*data){
list_t* chain = get_chain(ht, key);
pair_t* pair;
pair_t updatePair;
updatePair.first = key;
pair = (pair_t*) TMLIST_FIND(chain,
&updatePair);
pair->second = data;
}
Manual declaration of persistent components
Need a new implementation

## Slide 16: CURRENT SOLUTIONS
void TMhashtable_update(TMARCGDECL
hashtable_t* ht, void *key, void*data){
list_t* chain = get_chain(ht, key);
pair_t* pair;
pair_t updatePair;
updatePair.first = key;
pair = (pair_t*) TMLIST_FIND(chain,
&updatePair);
pair->second = data;
}
Manual declaration of persistent components
Need a new implementation
Third party code
can be inconsistent

## Slide 17: CURRENT SOLUTIONS
void TMhashtable_update(TMARCGDECL
hashtable_t* ht, void *key, void*data){
list_t* chain = get_chain(ht, key);
pair_t* pair;
pair_t updatePair;
updatePair.first = key;
pair = (pair_t*) TMLIST_FIND(chain,
&updatePair);
pair->second = data;
}
Manual declaration of persistent components
Need a new implementation
Third party code
can be inconsistent
Prohibited
Operation
Burden on the programmers

## Slide 18: OUTLINE
Crash Consistency Problem
Current Solutions
ThyNVM
Evaluation
Conclusion

## Slide 19: OUR GOAL
Software transparent consistency
in persistent memory systems
Execute legacy applications
Reduce burden on programmers
Enable easier integration of NVM

## Slide 20
NO MODIFICATION
IN THE CODE
void hashtable_update(hashtable_t* ht,
void *key, void *data)
{
list_t* chain = get_chain(ht, key);
pair_t* pair;
pair_t updatePair;
updatePair.first = key;
pair = (pair_t*) list_find(chain,
&updatePair);
pair->second = data;
}

## Slide 21: RUN THE EXACT SAME CODE…
Persistent Memory System
Software transparent
memory crash consistency
void hashtable_update(hashtable_t* ht,
void *key, void *data){
list_t* chain = get_chain(ht, key);
pair_t* pair;
pair_t updatePair;
updatePair.first = key;
pair = (pair_t*) list_find(chain,
&updatePair);
pair->second = data;
}

## Slide 22: ThyNVM APPROACH
Running
Epoch 0
Epoch 1
time
Checkpointing
Running
Checkpointing
Periodic checkpointing of data
managed by hardware
Transparent to application and system

## Slide 23: CHECKPOINTING OVERHEAD
Running
Epoch 0
Epoch 1
time
Checkpointing
Running
Checkpointing
1. Metadata overhead
Working location
Checkpoint location
X
X’
Y
Y’
Metadata Table
2. Checkpointing latency
STALLED
STALLED

## Slide 24: 1. METADATA AND CHECKPOINTING GRANULARITY
PAGE
CACHE BLOCK
One Entry Per Page
Small Metadata
One Entry Per Block
Huge Metadata
PAGE GRANULARITY
BLOCK GRANULARITY
Working location
Checkpoint location
X
X’
Y
Y’

## Slide 25: 2. LATENCY AND LOCATION
W
DRAM-BASED WRITEBACK
Long latency of writing back data to NVM
DRAM
NVM
Working location
Checkpoint location
X
X’
1. Writeback data from DRAM
2. Update the metadata table

## Slide 26: 2. LATENCY AND LOCATION
NVM-BASED REMAPPING
Short latency in NVM-based remapping
DRAM
NVM
Working location
Checkpoint location
Y
X
No copying
of data
2. Update the metadata table
3. Write in a
new location

## Slide 27: ThyNVM KEY MECHANISMS
Checkpointing granularity
  Small granularity: large metadata
  Large granularity: small metadata
Latency and location
  Writeback from DRAM: long latency
  Remap in NVM: short latency
Based on these we propose two key mechanisms
1. Dual granularity checkpointing
2. Overlap of execution and checkpointing

## Slide 28: 1. DUAL GRANULARITY CHECKPOINTING
DRAM
NVM
High write locality pages in DRAM,
low write locality pages in NVM
Page Writeback
in DRAM
Block Remapping
in NVM
GOOD FOR
STREAMING WRITES
GOOD FOR
RANDOM WRITES

## Slide 29: 2. OVERLAPPING CHECKOINTING AND EXECUTION
Running
time
Checkpointing
Running
Checkpointing
time
Epoch 0
Epoch 1
Epoch 2
Epoch 0
Epoch 1
Running
Checkpointing
Running
Checkpointing
Running
Checkpointing
Epoch 0
Epoch 1
Hides the long latency of Page Writeback

## Slide 30: OUTLINE
Crash Consistency Problem
Current Solutions
ThyNVM
Evaluation
Conclusion

## Slide 31: METHODOLOGY
Cycle accurate x86 simulator Gem5
Comparison Points:
Ideal DRAM: DRAM-based, no cost for consistency
  Lowest latency system
Ideal NVM: NVM-based, no cost for consistency
  NVM has higher latency than DRAM
Journaling: Hybrid, commit dirty cache blocks
  Leverages DRAM to buffer dirty blocks
Shadow Paging: Hybrid, copy-on-write pages
  Leverages DRAM to buffer dirty pages

## Slide 32: ADAPTIVITY TO ACCESS PATTERN
Chart: Normalized Write Traffic To NVM
| Journal | Shadow | ThyNVM
Series 1 | 1 | 3.7057 | 1.1221
Chart: Normalized Write Traffic To NVM
| Journal | Shadow | ThyNVM
Series 1 | 1 | 0.39546 | 0.6687
RANDOM SEQUENTIAL
ThyNVM adapts to both access patterns
Journaling is better for Random and
Shadow paging is better for Sequential
LOW
LOW
LOW
LOW
BETTER

## Slide 33: OVERLAPPING CHECKPOINTING AND EXECUTION
RANDOM SEQUENTIAL
Chart: Percentage of Execution Time
| Journal | Shadow | ThyNVM
Series 1 | 12.8221 | 45.2162 | 2.4662
Chart: Percentage of Execution Time
| Journal | Shadow | ThyNVM
Series 1 | 35.2552 | 9.6103 | 5.6131
Stalls the application for a negligible time
ThyNVM spends only 2.4%/5.5% of the execution time on checkpointing
45%
35%
Can spend 35-45% of the execution
on checkpointing
BETTER

## Slide 34: PERFORMANCE OF LEGACY CODE
Chart: Normalized IPC
| gcc | bwaves | milc | leslie. | soplex | Gems | lbm | omnet
Ideal DRAM | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
Ideal NVM | 0.97621 | 0.88199 | 0.93493 | 0.8921 | 0.98908 | 0.99999 | 0.87038 | 0.99448
ThyNVM | 0.98469 | 0.92343 | 0.96227 | 0.94344 | 0.99253 | 0.99994 | 0.92862 | 0.99935
Provides consistency without
significant performance overhead
Within -4.9%/+2.7% of an
idealized DRAM/NVM system

## Slide 35: OUTLINE
Crash Consistency Problem
Current Solutions
ThyNVM
Evaluation
Conclusion

## Slide 36: ThyNVM
Checkpoints at multiple granularities to minimize both latency and metadata
Overlaps checkpointing and execution
Adapts to DRAM and NVM characteristics
Can enable widespread adoption
of persistent memory
A new hardware-based
checkpointing mechanism,
with no programming effort

## Slide 37: Enabling Software-transparent Crash Consistency In Persistent Memory Systems
ThyNVM
Jinglei Ren, Jishen Zhao, Samira Khan,
Jongmoo Choi, Yongwei Wu, and Onur Mutlu
Available at
http://persper.com/thynvm