## Slide 1
Yahya Can Tugrul Jeremie S. Kim Victor van der Veen Kaveh Razavi Onur Mutlu
U-TRR Uncovering in-DRAM RowHammer Protection Mechanisms: A New Methodology, Custom RowHammer Patterns, and Implications
Hasan Hassan
Notes: Hi, my name is Hasan.
I will be presenting our work on uncovering the operation of in-DRAM RowHammer Protection mechanisms.

## Slide 2: The RowHammer Vulnerability
Row 0
Row 1
Row 2
Row 3
Row 4
Repeatedly opening (activating) and closing (precharging)
a DRAM row causes RowHammer bit flips in nearby cells
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 0
Row 4
Row 2
open
Row 2
closed
DRAM Chip
Notes: The RowHammer vulnerability of modern DRAM is a critical reliability and security threat.
[CLICK] When a DRAM row is repeatedly activated and precharged many times, nearby rows may experience RowHammer bit flips.

## Slide 3: Current RowHammer Protection Mechanisms
DRAM vendors implement in-DRAM Target Row Refresh (TRR)
Key Idea: TRR refreshes nearby rows upon detecting an aggressor row
Row 0
Row 1
Row 2
Row 3
Row 4
DRAM Chip
TRR
Aggressor detected: Row 2
closed
open
Refresh neighbor rows
TRR-induced REF
TRR-induced REF
Notes: [CLICK] To protect their DRAM chips against RowHammer, DRAM vendors currently implement RowHammer mitigation mechanisms typically called Target Row Refresh or (TRR)
[CLICK] The key idea of TRR is to refresh nearby rows upon detecting an aggressor row

## Slide 4: Problem
TRR is obscure, undocumented, and proprietary
We cannot easily study the security properties of TRR
Notes: However, different vendors implement TRR differently and the exact operation of these TRR mechanisms is unknown. Therefore, TRR is obscure, undocumented, and proprietary
[CLICK] Because of this, today, we cannot easily study the security properties of TRR and make sure it is fully secure

## Slide 5: Goal
Study in-DRAM TRR mechanisms to
understand how they operate
1
assess their security
2
secure DRAM completely against RowHammer
3
Notes: Our goal is to study in-DRAM TRR mechanisms to [CLICK] understand how they operate, [CLICK] asses their security, [CLICK] and enable fully-secure DRAM against RowHammer

## Slide 6: U-TRR (Uncovering TRR)
U-TRR: A new methodology to
uncover the inner workings of TRR
Key idea: Use data retention failures as a side channel
to detect when a row is refreshed by TRR
Notes: To this end, we propose U-TRR, a new methodology to uncover the inner workings of TRR.
[CLICK] The key idea of U-TRR is to use data retention failures in DRAM as a side channel to detect when a certain row is refreshed by TRR

## Slide 7: U-TRR: Experimental Setup
* SoftMC [Hassan+, HPCA’17] enhanced for DDR4
Notes: We implement U-TRR using SoftMC, an FPGA-based infrastructure with precise temperature control which we enhanced for DDR4

## Slide 8: U-TRR Analysis Summary
15x Vendor A DDR4 DRAM modules
U-TRR
new RowHammer access patterns
that circumvent TRR
15x Vendor B DDR4 DRAM modules
15x Vendor C DDR4 DRAM modules
Notes: Using U-TRR, [CLICK] we analyze 45 DDR4 modules from three major DRAM vendors. [CLICK] Based on the understanding we develop from our analysis, we craft new RowHammer access patterns that circumvent the TRR mechanisms implemented today.

## Slide 9: Key Takeaways
All 45 modules we test are vulnerable
99.9% of rows in a DRAM bank experience at least one RowHammer bit flip
Up to 7 RowHammer bit flips in an 8-byte dataword, making ECC ineffective
Notes: In summary, we find that all 45 modules we test are vulnerable to our new RowHammer access patterns
[CLICK] almost all rows in a DRAM bank experience at least one RowHammer bit flip
[CLICK] a single 8-byte dataword experiences up to 7 Rowhammer bit flips, making ECC ineffective against our RowHammer access patterns.
[CLICK] Our paper has detailed descriptions and analyses of each of the 45 modules and we encourage you to read it and attend our full talk

## Slide 10
Yahya Can Tugrul Jeremie S. Kim Victor van der Veen Kaveh Razavi Onur Mutlu
U-TRR Uncovering in-DRAM RowHammer Protection Mechanisms: A New Methodology, Custom RowHammer Patterns, and Implications
Hasan Hassan
Notes: Thank you for your time. I invite you to listen to our full talk and read our paper for more details.