## Slide 1: Fast and Efficient Address Translation via Hybrid Restrictive & Flexible Virtual-to-Physical Address Mappings
Konstantinos Kanellopoulos
Rahul Bera, Kosta Stojiljkovic, Nisa Bostanci, Can Firtina,
Rachata Ausavarungnirun, Rakesh Kumar, Nastaran Hajinazar,
Mohammad Sadrosadati, Nandita Vijaykumar, and Onur Mutlu
UTOPIA

## Slide 2: Executive Summary
Problem: Conventional virtual memory (VM) frameworks enable a virtual address to flexibly map to any physical address. This flexibility necessitates large translation structures leading to:
(1) high translation latency and (2) large translation-induced interference in the memory hierarchy
Motivation: Restricting the address mapping leads to compact translation structures and reduces the overheads of address translation. Doing so across the entire memory has two major drawbacks:
Limits core VM functionalities (e.g., data sharing)
Increases swapping activity in the presence of free physical memory
Key Idea: Utopia is a new hybrid virtual-to-physical address mapping scheme that allows both flexible and restrictive hash-based address mappings to harmoniously co-exist in the system
Utopia manages physical memory using two types of physical memory segments:
Flexible Segment
Page
Table
Page
X86-64 Radix PT
Restrictive Segment
Page
Hash Function
Modulo Hash
Fast Translation
Limited VM features
Supports all VM features
Slow Translation
Key Results: Outperforms (i) the state-of-the-art contiguity-aware translation scheme by 13%, and (ii) achieves 95% of the performance of an ideal perfect-TLB
https://github.com/CMU-SAFARI/Utopia

## Slide 3: Talk Outline
Virtual Memory Background
Address Translation Overheads
Utopia: Hybrid Address Mappings
Utopia: Key Challenges
Evaluation Results

## Slide 4: Talk Outline
Virtual Memory Background
Address Translation Overheads
Utopia: Hybrid Address Mappings
Utopia: Key Challenges
Evaluation Results

## Slide 5: Virtual Memory Basics
A core feature of virtual memory management is that the mapping between virtual-to-physical pages is fully-associative
Virtual Address Space
Physical Address Space
Page Table
Perform Page Table Walk (PTW) to retrieve the mapping

## Slide 6: Page Table Walk in x86-64
9 bits
Virtual Address
9 bits
9 bits
9 bits
CR3
Physical Frame Number
PL4
PL3
PL2
PL1

## Slide 7: Page Table Walk in x86-64
9 bits
Virtual Address
9 bits
9 bits
9 bits
Physical Frame Number
12 bits
12 bits
1
2
3
4
Four sequential memory accesses
during a page table walk in x86-64

## Slide 8: Architectural Support for VM
To send a memory request to the memory hierarchy, the processor needs to translate the virtual address to the corresponding physical
Resolving an address translation request requires accessing the Page Table
Modern processors employ a specialized hardware unit called Memory Management Unit (MMU) to accelerate address translation

## Slide 9: Address Translation Flow (I)
Memory Hierarchy
Core
Page Table
Memory
Management Unit
Virtual
Address

## Slide 10: Address Translation Flow (II)
L1 I-TLB
L1 D-TLB
Unified
L2 TLB
Page Walk Caches
Page Table Walker
Miss
Miss
Miss
Virtual
Address
Miss
Memory Hierarchy
Memory Management Unit
Page Table
Notes: [1] There is a two level TLB-hierarchy.
[2] If we miss in the TLB, we trigger the page table walk
[3] We search in the page walk caches for intermediate levels

## Slide 11: Address Translation Flow (III)
DRAM
Memory
Management Unit
Swap
Space
Physical Address Space
Page Table Entry
Swap in
Notes: [1] If the physical page resides in the swap space, then it first needs be to be swapped into the DRAM before fetching it inside the cache hierarchy

## Slide 12: Address Translation Flow (IV)
Memory
Management Unit
Memory Hierarchy
Core
Physical
Address

## Slide 13: Talk Outline
Virtual Memory Background
Address Translation Overheads
Utopia: Hybrid Address Mappings
Utopia: Key Challenges
Evaluation Results

## Slide 14: Data-Intensive Workloads
Graph Analytics
Bioinformatics
High address translation overheads
Generative AI

## Slide 15: Address Translation Overhead
Frequent page table walks
High-latency page table walks

## Slide 16: Address Translation Overhead
High latency
PTWs
Frequent
PTWs
High performance overheads
High interference in memory hierarchy
+

## Slide 17: High Performance Overhead
Completely avoiding address translation
leads on average to 31% higher performance
Chart: Speedup over Radix
| BC | BFS | CC | DLRM | GEN | GC | PR | RND | SSSP | TC | XS | GMEAN
ECH | 1.1257 | 1.0372 | 1.0279 | 1.0349 | 1.0477 | 1.0473 | 1.0653 | 1.3565 | 1.0431 | 1.0337 | 1.1103 | 1.0811
P-TLB | 1.5355 | 1.188 | 1.1735 | 1.1857 | 1.2866 | 1.2858 | 1.1391 | 1.938 | 1.2867 | 1.1545 | 1.4004 | 1.3087
State-of-the-art Page Table1
Perfect TLB
31%
[1] Skarlatos et al. “Elastic Cuckoo Page Tables: Rethinking Virtual Memory
Translation for Parallelism” ASPLOS 2020

## Slide 18: High Interference in Main Memory
Chart: Normalized Row Buffer Conflicts
| BC | BFS | CC | DLRM | GEN | GC | PR | RND | SSSP | TC | XS | GMEAN
ECH | 1.4877 | 1.6327 | 1.668 | 1.6362 | 1.66 | 1.6603 | 1.4457 | 1.0172 | 1.7301 | 1.4864 | 1.2625 | 1.5012
P-TLB | 0.64564 | 0.73619 | 0.73233 | 0.73771 | 0.66306 | 0.66325 | 0.76381 | 0.57416 | 0.6642 | 0.77614 | 0.81311 | 0.7031
Completely avoiding address translation
leads to 30% fewer DRAM row buffer conflicts
30%
[1] Skarlatos et al. “Elastic Cuckoo Page Tables: Rethinking Virtual Memory
Translation for Parallelism” ASPLOS 2020

## Slide 19: Idea: Restricting VA-to-PA Mapping
Restrict the VA-to-PA mapping to
perform fast address translation1,2
..
0 0 1 0 1
0 0 1 1 0
0 0 1 1 1
..
0 0 0 0 0
0 0 0 0 0
0 0 0 1 0
..
..
Hash Function
Virtual Address Space
Physical Address Space
Hash Mask 11100
[1] Picorel et al. “Near-Memory Address Translation” PACT 2017
[2] Gosakan et al. “Mosaic Pages: Big TLB Reach with Small Pages” ASPLOS 2023

## Slide 20: Idea: Restricting VA-to-PA Mapping
..
0 0 1 0 1
0 0 1 1 0
0 0 1 1 1
..
0 0 0 1 0
Hash Function
Virtual Address Space
Physical Address Space
Hash Mask 11100
Restrict the VA-to-PA mapping to
perform fast address translation1,2
[1] Picorel et al. “Near-Memory Address Translation” PACT 2016
[2] Gosakan et al. “Mosaic Pages: Big TLB Reach with Small Pages” ASPLOS 2023

## Slide 21: Drawbacks of Restricting VA-to-PA Mapping
Employing a restrictive mapping across the entire memory comes with two key drawbacks:
Limits core VM functionalities such as data sharing
Increases swapping activity since the system cannot map virtual pages to free physical pages

## Slide 22: Effect on Swapping Activity
Chart: Normalized Accesses to Swap Space
| BC | BFS | CC | DLRM | GEN | GC | PR | RND | SSSP | TC | XS | GMEAN
Only Restrictive Mapping | 1.4545 | 3.9205 | 4.8 | 2.3435 | 3.2 | 1.5 | 2.7712 | 1.5 | 2.3542 | 1.125 | 1.8114 | 2.3684
Sole use of restrictive mapping leads to 2.37x higher swapping activity over the baseline

## Slide 23: Our Goal
Design a virtual-to-physical address mapping scheme that:
Provides fast and efficient translation using a restrictive hash-based address mapping
Enjoys the benefits of the conventional fully-flexible address mapping

## Slide 24: Talk Outline
Virtual Memory Background
Address Translation Overheads
Utopia: Hybrid Address Mappings
Utopia: Key Challenges
Evaluation Results

## Slide 25: Utopia: Key Idea
We propose Utopia, a new virtual-to-physical mapping scheme that enables both:
Flexible Mapping
Restrictive Mapping
Harmoniously co-exist in the system

## Slide 26: Utopia: Key Idea
Manage physical memory using two types of
physical memory segments:
Flexible Segments
Restrictive Segments

## Slide 27: Utopia: Key Idea (I)
Restrictive Segments
Flexible Segments
Fast address translation
Limited VM functionalities
Page
Virtual Page Number
Hash function
Restrictive Segment (RestSeg)
Page
Page
Page

## Slide 28: Utopia: Key Idea (II)
Flexible Segments
Restrictive Segments
High-latency
address translation
Supports all conventional VM features
Flexible Segment (FlexSeg)
Page
Page
Page
Page
Virtual Page Number
Page Table

## Slide 29: RestSeg Properties
Structural Properties
Address Translation for Data in RestSeg

## Slide 30: RestSeg Properties
Structural Properties
RestSeg is organized in
a set-associative manner
similar to how hardware caches operate

## Slide 31: RestSeg: Structural Properties
Example: 2-way associative RestSeg with 2 sets
4KB
Page
4KB
Page
4KB
Page
4KB
Page
Set 0
Way 0
Way 1
Way 0
Way 1
Set 1
Set-associative design offers high flexibility

## Slide 32: Multiple RestSegs in the System
4KB
Page
4KB
Page
4KB
Page
4KB
Page
2MB
Page
2MB
Page
RestSeg #1
RestSeg #2
Backward compatible with
large page mechanisms

## Slide 33: RestSeg Properties
Structural Properties
Address Translation for Data in RestSeg

## Slide 34: Restrictive Segment Walk (RSW)
RestSeg
Page
Page
Page
Page
Set 0
Way 0
Way 1
Way 0
Way 1
Set 1
Virtual Page

## Slide 35: Restrictive Segment Walk (RSW)
RestSeg
Page
Page
Page
Page
Set 0
Way 0
Way 1
Way 0
Way 1
Set 1
Virtual Page
How can we find out the physical location of the virtual page?

## Slide 36: RSW Operations
Tag Matching
1
Set Filtering
2

## Slide 37: RestSeg: Tag Matching
Virtual Address
Hash Function
Tag
Tag matching requires comparing the tags of all ways with the tag of the virtual page
Tag Array (TAR): Array that stores the tag of each entry
TAR
TAG
N/A
N/A
N/A
Set 0
Set 1
Set #
Do we always have to do tag matching?

## Slide 38: RestSeg: Set Filtering
Set Filtering: quickly discover if a set in the RestSeg is empty or not and filter tag mismatches
Set Filter (SF): Array of counters that keep track of the number of pages inside each set
Virtual Address
Hash Function
SF
1
0
Set 0
Set 1
Set #
Tag Matching

## Slide 39: Address Translation in Utopia
System employs:
2 RestSegs, one for 4KB and one for 2MB pages
1 FlexSeg
L1 TLB Miss
RestSeg Walks
L2 TLB Access
Page Table Walk

## Slide 40: Talk Outline
Virtual Memory Background
Address Translation Overheads
Utopia: Hybrid Address Mappings
Utopia: Key Challenges
Evaluation Results

## Slide 41: Utopia: Key Challenges
Which data should be placed in the RestSeg?
How to maintain RestSegs in the system
How to integrate Utopia in the address translation pipeline

## Slide 42: Utopia: Key Challenges
Which data should be placed in the RestSegs?
How to maintain RestSegs in the system
How to integrate Utopia in the address translation pipeline

## Slide 43: Page Placement in RestSeg
Our goal is to place costly-to-translate pages into a RestSeg
We propose two techniques to perform data placement in Utopia:
  Page-Fault-based Allocation Policy
  PTW-Tracking-based Migration Policy

## Slide 44: Page-Fault-Based Allocation Policy
On a page fault
the page is directly allocated in a RestSeg
RestSeg
Allocate
Page Fault
What about costly-to-translate pages
that reside in a FlexSeg?

## Slide 45: PTW-Tracking-Based Migration Policy
Use unused bits of each PTE as a counter that tracks the number and cost of PTWs for each page
Physical Frame #
Page Table Entry
Metadata
PTE Counters
> Threshold
RestSeg
Migrate
Unused bits

## Slide 46: Utopia: Three Key Challenges
Which data should be placed in the RestSegs?
How to maintain RestSegs in the system
How to integrate Utopia in the address translation pipeline

## Slide 47: OS Support for Utopia
OS supports Utopia in three ways by handling:
Allocations in a RestSeg
Replacements in a RestSeg
Migrations to/from a RestSeg
Detailed description in the paper

## Slide 48: Utopia: 3 Key Challenges
Which data should be placed in the RestSegs?
How to maintain RestSegs in the system
How to integrate Utopia in the address translation pipeline

## Slide 49: RestSeg Walker in MMU
TAR Cache
SF Cache
RestSeg Walker
FSM
Memory
Hierarchy

## Slide 50: MMU: Page inside RestSeg (I)
L1 TLB
TAR Cache
SF Cache
RestSeg Walker
FSM
Miss

## Slide 51: MMU: Page inside RestSeg (I)
L1 TLB
TAR Cache
SF Cache
RestSeg Walker
FSM
Miss
L2
Unified
TLB

## Slide 52: MMU: Page inside RestSeg (I)
L1 TLB
TAR Cache
SF Cache
RestSeg Walker
FSM
Miss
L2
Unified
TLB
Stall

## Slide 53: MMU: Page inside RestSeg (I)
L1 TLB
TAR Cache
SF Cache
RestSeg Walker
FSM
Miss
Data in RestSeg
Stall

## Slide 54: MMU: Page inside RestSeg (I)
L1 TLB
TAR Cache
SF Cache
RestSeg Walker
FSM
Miss
Data in RestSeg
Stall
PWCs
FlexSeg Walker
FSM

## Slide 55: MMU: Page inside RestSeg (I)
L1 TLB
TAR Cache
SF Cache
RestSeg Walker
FSM
Miss
Data in RestSeg
Stall
PWCs
FlexSeg Walker
FSM

## Slide 56: MMU: Page inside FlexSeg (II)
L1 TLB
TAR Cache
SF Cache
RestSeg Walker
FSM
Miss

## Slide 57: MMU: Page inside FlexSeg (II)
L1 TLB
TAR Cache
SF Cache
RestSeg Walker
FSM
Miss
L2
Unified
TLB

## Slide 58: MMU: Page inside FlexSeg (II)
L1 TLB
TAR Cache
SF Cache
RestSeg Walker
FSM
Miss
L2
Unified
TLB
Stall

## Slide 59: MMU: Page inside FlexSeg (II)
L1 TLB
TAR Cache
SF Cache
RestSeg Walker
FSM
Miss
L2
Unified
TLB
Stall
Data is not here

## Slide 60: MMU: Page inside FlexSeg (II)
L1 TLB
TAR Cache
SF Cache
RestSeg Walker
FSM
Miss
L2
Unified
TLB
Stall
Data is not here
PWCs
FlexSeg Walker
FSM

## Slide 61: MMU: Page inside FlexSeg (II)
L1 TLB
TAR Cache
SF Cache
RestSeg Walker
FSM
Miss
L2
Unified
TLB
Data is not here
PWCs
Page Table Walker
FSM
Data is in FlexSeg

## Slide 62: Area & Power Overhead
Area and power overhead evaluation using McPat
Comparison to a high-end Intel Raptor Lake
Utopia incurs 0.64% area and 0.72% power overhead per core

## Slide 63: Talk Outline
Virtual Memory Background
Address Translation Overheads
Utopia: Hybrid Address Mappings
Utopia: Key Challenges
Evaluation Results

## Slide 64: Evaluation Methodology
Sniper Multicore Simulator extended with:
  Page table walker & page walk caches
  Buddy allocator
  Migration Latency
Our poster at MICRO 2023 SRC introduces
a new open-source simulation
framework for VM research
https://github.com/CMU-SAFARI/Virtuoso

## Slide 65: Evaluation Methodology
Sniper Multicore Simulator extended with:
  Page table walker & page walk caches
  Buddy allocator
  Migration Latency
Workloads: Executed for 500M instructions
  GraphBIG: PR, BFS, BC, GC, CC
  HPCC: Randacc
  XSBench: Particle Simulation with 15K grid
  DLRM: SLS-like
  GenomicsBench: k-mer count

## Slide 66: Evaluated Mechanisms
  Baseline with Radix PT and Transparent Huge Pages enabled
  POM-TLB1: State-of-the art large software-managed TLB
  ECH2: State-of-the-art hash-based page table
  RMM3: Contiguity-aware address translation
  Utopia: 512MB RestSegs (one for 4KB and one for 2MB pages)
  P-TLB: Perfect L1 TLB (translation requests always hit in L1 TLB)
[2] Skarlatos et al. “Elastic Cuckoo Page Tables: Rethinking Virtual Memory Translation for Parallelism” ASPLOS ‘20
[1] Ryoo et al. “Rethinking TLB designs in virtualized environments: A very large part-of-memory TLB” ISCA ’17
[3] Karakostas et al. “Redundant memory mappings for fast access to large memories” ISCA ’15

## Slide 67: Performance Results
Chart: Speedup over Radix
| BC | BFS | CC | DLRM | GEN | GC | PR | RND | SSSP | TC | XS | GMEAN
POM-TLB | 1.0184 | 1.0427 | 1.0325 | 1.0409 | 1.0299 | 1.0293 | 1.0384 | 1.018 | 1.0441 | 1.0412 | 1.0744 | 1.0372
ECH | 1.1257 | 1.0372 | 1.0279 | 1.0349 | 1.0477 | 1.0473 | 1.0653 | 1.3565 | 1.0431 | 1.0337 | 1.1103 | 1.0811
RMM | 1.1456 | 1.0454 | 1.0365 | 1.0437 | 1.1504 | 1.1492 | 1.0307 | 1.5613 | 1.1852 | 1.0401 | 1.1945 | 1.1358
Utopia | 1.3174 | 1.1432 | 1.1158 | 1.141 | 1.2379 | 1.2373 | 1.1111 | 1.9353 | 1.1914 | 1.1073 | 1.386 | 1.2491
P-TLB | 1.5355 | 1.188 | 1.1735 | 1.1857 | 1.2866 | 1.2858 | 1.1391 | 1.938 | 1.2867 | 1.1545 | 1.4004 | 1.3087
Utopia outperforms the second-best performing scheme (RMM) by 13% and Radix by 24%
13%

## Slide 68: Performance Results
Utopia outperforms the second-best performing scheme (RMM) by 13% and Radix by 24%
Utopia’s performance is within 95% of P-TLB
Chart: Speedup over Radix
| BC | BFS | CC | DLRM | GEN | GC | PR | RND | SSSP | TC | XS | GMEAN
POM-TLB | 1.0184 | 1.0427 | 1.0325 | 1.0409 | 1.0299 | 1.0293 | 1.0384 | 1.018 | 1.0441 | 1.0412 | 1.0744 | 1.0372
ECH | 1.1257 | 1.0372 | 1.0279 | 1.0349 | 1.0477 | 1.0473 | 1.0653 | 1.3565 | 1.0431 | 1.0337 | 1.1103 | 1.0811
RMM | 1.1456 | 1.0454 | 1.0365 | 1.0437 | 1.1504 | 1.1492 | 1.0307 | 1.5613 | 1.1852 | 1.0401 | 1.1945 | 1.1358
Utopia | 1.3174 | 1.1432 | 1.1158 | 1.141 | 1.2379 | 1.2373 | 1.1111 | 1.9353 | 1.1914 | 1.1073 | 1.386 | 1.2491
P-TLB | 1.5355 | 1.188 | 1.1735 | 1.1857 | 1.2866 | 1.2858 | 1.1391 | 1.938 | 1.2867 | 1.1545 | 1.4004 | 1.3087

## Slide 69: Translation Latency
Chart: Reduction in Address Translation Latency
| BC | BFS | CC | DLRM | GEN | GC | PR | RND | SSSP | TC | XS | GMEAN
POM-TLB | 0.23937 | 0.13931 | 0.11813 | 0.13508 | 0.12934 | 0.12978 | 0.14795 | 0.16296 | 0.11577 | 0.30159 | 0.33041 | 0.1651
ECH | 0.44818 | 0.24228 | 0.21974 | 0.23678 | 0.32492 | 0.32504 | 0.35545 | 0.87967 | 0.30038 | 0.36847 | 0.45134 | 0.34888
RMM | 0.42221 | 0.46175 | 0.42538 | 0.45833 | 0.67499 | 0.67467 | 0.50742 | 0.44805 | 0.48162 | 0.42393 | 0.50157 | 0.49135
Utopia | 0.55588 | 0.55969 | 0.41664 | 0.55732 | 0.78996 | 0.79001 | 0.57167 | 0.99977 | 0.60669 | 0.47155 | 0.8548 | 0.63088
Utopia reduces average translation latency by 63% over Radix and 14% over RMM

## Slide 70: Main Memory Interference
Chart: Normalized DRAM Row Buffer Conflicts
| BC | BFS | CC | DLRM | GEN | GC | PR | RND | SSSP | TC | XS | GMEAN
POM-TLB | 0.97855 | 0.95768 | 0.96 | 0.95961 | 0.94638 | 0.94647 | 0.98576 | 0.95154 | 0.94905 | 0.96387 | 0.93954 | 0.95795
ECH | 1.4877 | 1.6327 | 1.668 | 1.6362 | 1.66 | 1.6603 | 1.4457 | 1.0172 | 1.7301 | 1.4864 | 1.2625 | 1.5012
RMM | 0.81986 | 0.87708 | 0.88672 | 0.87884 | 0.77632 | 0.7765 | 0.88246 | 0.80774 | 0.84443 | 0.88801 | 0.90716 | 0.84834
Utopia | 0.75756 | 0.84554 | 0.98936 | 0.84715 | 0.73176 | 0.73191 | 0.8646 | 0.57516 | 0.79884 | 0.99067 | 0.81539 | 0.80522
P-TLB | 0.64564 | 0.73619 | 0.73233 | 0.73771 | 0.66306 | 0.66325 | 0.76381 | 0.57416 | 0.6642 | 0.77614 | 0.81311 | 0.7031
Utopia reduces row buffer conflicts by 20%
over Radix and 9% less than P-TLB

## Slide 71: More Results and Details in the Paper
Sensitivity across different hash functions
Sensitivity to parallel/serial TLB access and RSW
Sensitivity to RestSeg size
Reuse-level distribution of 4KB pages
Effect of migration to memory requests
TAR & SF cache hit rate
Overhead across different context-switch quanta
https://arxiv.org/abs/2211.12205

## Slide 72: More Results and Details in the Paper
Sensitivity across different hash functions
Sensitivity to parallel/serial TLB access and RSW
Sensitivity to RestSeg size
Reuse-level distribution of 4KB pages
Effect of migration to memory requests
TAR & SF cache hit rate
Overhead across different context-switch quanta
https://arxiv.org/abs/2211.12205

## Slide 73: Conclusion
We propose Utopia, a new virtual-to-physical mapping scheme that enables both:
Flexible Mapping
Restrictive Mapping
Harmoniously co-exist in the system
https://github.com/CMU-SAFARI/Utopia
Utopia is open source
Utopia achieves (i) 13% higher performance than the state-of-the-art contiguity-aware translation scheme and (ii) 95% of the performance of an ideal perfect-TLB

## Slide 74: Fast and Efficient Address Translation via Hybrid Restrictive & Flexible Virtual-to-Physical Address Mappings
Konstantinos Kanellopoulos
Rahul Bera, Kosta Stojiljkovic, Nisa Bostanci, Can Firtina,
Rachata Ausavarungnirun, Rakesh Kumar, Nastaran Hajinazar,
Mohammad Sadrosadati, Nandita Vijaykumar, and Onur Mutlu
UTOPIA
https://github.com/CMU-SAFARI/Utopia

## Slide 75: Address Translation Flow (III)
Memory Hierarchy
Core
Page Table
Memory
Management Unit
Virtual
Address
Translation Latency
Hit in TLBs

## Slide 76: Virtual Memory Basics
Virtual Memory (VM) is one of the cornerstones
of most modern computing systems
Conventional VM designs provide :
  Application-transparent memory management
  Data sharing
  Process isolation

## Slide 77: Address Translation Flow (III)
Memory Hierarchy
Core
Page Table
Memory
Management Unit
Virtual
Address
Cache/DRAM Access
TLB Miss
Translation Latency

## Slide 78: High Latency PTWs
Irregular Memory Access Patterns
Large
Datasets
Large and costly-to-access PT

## Slide 79: Frequent PTWs
Chart: L2 TLB MPKI
| BC | BFS | CC | DLRM | GEN | GC | PR | RND | SSSP | TC | XS | GMEAN
L2 TLB 1.5K entries | 11.2052 | 71.5791 | 85.9922 | 71.6073 | 63.2478 | 63.2599 | 38.5931 | 71.1073 | 65.9952 | 6.7839 | 14.7529 | 39.43
2K | 11.1365 | 71.0632 | 85.3552 | 71.0736 | 61.6872 | 61.6964 | 38.3017 | 70.7726 | 65.7936 | 6.7514 | 14.5471 | 39.0287
4K | 10.8264 | 69.4259 | 83.4785 | 69.1341 | 57.334 | 57.3375 | 37.2204 | 69.6028 | 64.3837 | 6.6372 | 13.9013 | 37.7126
8K | 10.3654 | 64.9105 | 79.6102 | 65.8375 | 52.2626 | 52.238 | 35.4915 | 67.491 | 61.5506 | 6.4387 | 12.9254 | 35.6478
16K | 9.71 | 60.9531 | 73.19 | 60.9574 | 46.6056 | 46.6111 | 32.9895 | 63.6663 | 56.9297 | 6.1056 | 11.4453 | 32.8412
32K | 8.7933 | 53.377 | 64.454 | 53.5648 | 40.8714 | 40.86 | 29.6321 | 57.0056 | 50.9111 | 5.5919 | 9.3105 | 28.9818
64K | 7.5502 | 44.8016 | 54.7485 | 44.8208 | 35.3419 | 35.3484 | 26.132 | 46.2758 | 44.4765 | 4.9003 | 6.4744 | 24.3314
Even the largest 64K-entry L2 TLB
experiences 24 MPKI on average

## Slide 80: High Latency PTWs
Chart: PTW Latency (cycles)
| BC | BFS | CC | DLRM | GEN | GC | PR | RND | SSSP | TC | XS | GMEAN
Radix | 166.0465 | 128.9498 | 130.0739 | 128.5451 | 153.0084 | 153.0189 | 119.7282 | 135.7275 | 168.6697 | 142.3543 | 103.97 | 137.7941
ECH | 117.1476 | 107.3377 | 108.3602 | 107.4408 | 108.8615 | 108.8361 | 96.6544 | 13.3398 | 123.6753 | 111.3735 | 62.5574 | 86.0973
86 cycles on average to access
the state-of-the-art hash-based PT

## Slide 81: OS: Allocation in RestSeg
VPN
Hash Function
Tag Array
There is a free way!
Store data there

## Slide 82: OS: Allocation in RestSeg
VPN
Hash Function
Tag Array
Discover if there is a
free way in the set

## Slide 83: OS: Replacement in RestSeg
VPN
Hash Function
Tag Array
No way is free!
If no page-fault,
evict a page!

## Slide 84: OS: Migration to/from RestSeg
RestSeg
Migration
FlexSeg
DMA engine is responsible for migrating data between RestSegs and FlexSegs
DMA Engine

## Slide 85: Architectural Support for Utopia
New hardware components to support Utopia:
Specialized hardware circuitry to perform the tag matching and the set filtering
  - Avoid expensive software-based accesses to translation structures
Small caches for the the Tag Array and Set Filter
  - Accesses to Permissions Filter and Tag Array may exhibit high spatial and temporal locality
Minor modifications in the address translation pipeline:
  - RSW occurs in parallel with L2 TLB access