## Slide 1: What Your DRAM Power Models Are Not Telling You: Lessons from a Detailed Experimental Study
Saugata Ghose, A. Giray Yağlıkçı, Raghav Gupta, Donghyuk Lee, Kais Kudrolli, William X. Liu, Hasan Hassan, Kevin K. Chang, Niladrish Chatterjee, Aditya Agrawal, Mike O’Connor, Onur Mutlu
June 21, 2018

## Slide 2: DRAM Power Is Becoming a Major Design Concern
Main memory in computers consists of DRAM modules
DRAM consumes up to half of total system power
State-of-the-art DRAM power models are not adequate
  Based on IDD values: standard current measurements provided by vendors
  Often have a high mean absolute percentage error
    32% for DRAMPower
    161% for Micron power model
Chart: 
| Ware+ HPCA '10 | David+ ICAC '11 | Malladi+ ISCA '12 | Yoon ISCA '12 | Paul+ ISCA '15 | Elmore+ Report '16
Fraction of DRAM in System Energy Consumption | 0.46 | 0.19 | 0.25 | 0.435 | 0.4 | 0.243
OUR GOAL
Measure and analyze the power used by real DRAM, and build an accurate DRAM power model
Fraction of Total System Energy

## Slide 3: Background: DRAM Organization & Operation Characterization Methodology New Findings on DRAM Power Consumption VAMPIRE: A Variation-Aware DRAM Power Model Conclusion
Outline

## Slide 4: Simplified DRAM Organization and Operation
Fundamental DRAM commands: activate, read, write, precharge
One row of DRAM: 8 kB
One cache line of data: 64 B
DRAM Chip
Bank 0
. . .
. . .
Processor Chip
Memory Controller
Column Select
Bank Select
I/O Drivers
I/O Drivers
memory channel
DRAM Cell Array
Row Buffer
Bank 7
activation
Core
. . .
Core
Shared Last-Level Cache

## Slide 5: Background: DRAM Organization & Operation Characterization Methodology New Findings on DRAM Power Consumption VAMPIRE: A Variation-Aware DRAM Power Model Conclusion
Outline

## Slide 6: Power Measurement Platform
Keysight 34134A
DC Current Probe
DDR3L SO-DIMM
JET-5467A Riser Board
Virtex 6 FPGA
Notes: 50 SO-DIMMs -> 200 DRAM chips

## Slide 7: Methodology Details
SoftMC: an FPGA-based memory controller [Hassan+ HPCA ’17]
  Modified to repeatedly loop commands
  Open-source: https://github.com/CMU-SAFARI/SoftMC
Measure current consumed by a module during a SoftMC test
Tested 50 DDR3L DRAM modules (200 DRAM chips)
  Supply voltage: 1.35 V
  Three major vendors: A, B, C
  Manufactured between 2014 and 2016
For each experimental test that we perform
  10 runs of each test per module
  At least 10 current samples per run

## Slide 8: Background: DRAM Organization & Operation Characterization Methodology New Findings on DRAM Power Consumption VAMPIRE: A Variation-Aware DRAM Power Model Conclusion
Outline

## Slide 9: 1. Real DRAM Power Varies Widely from IDD Values
Different vendors have very different margins (i.e., guardbands)
Low variance among different modules from same vendor
Chart: Current (mA)
| Datasheet | Measured | Datasheet | Measured | Datasheet | Measured
Datasheet | 91.9098 | 0 | 65.0187 | 0 | 48.015 | 0
Q1 | 34.1322 | 44.5656 | 25.8025
MED-Q1 | 1.9511 | 1.3092 | 0.31631
Measured | 0.55097 | 14.628 | 1.204
Chart: Current (mA)
| Datasheet | Measured | Datasheet | Measured | Datasheet | Measured
Datasheet | 179.7895 | 0 | 165.0187 | 0 | 128.015 | 0
Q1 | 71.4976 | 69.6723 | 57.8985
MED-Q1 | 2.6486 | 1.1448 | 1.7217
Measured | 0.88936 | 2.6694 | 0.46656
Chart: Current (mA)
| Datasheet | Corrected | Datasheet | Corrected | Datasheet | Corrected
Datasheet | 735.4887 | 0 | 325.2622 | 0 | 308.2247 | 0
Q1 | 301.6832 | 238.3117 | 293.1429
MED-Q1 | 52.6622 | 20.8321 | 8.1341
Corrected | 10.7978 | 14.6474 | 2.7533
IDD2N
Idle
IDD0
Activate–Precharge
IDD4R
Read
Current consumed by real DRAM modules varies significantly for all IDD values that we measure
Notes: Replace IDD4R with corrected data

## Slide 10: 2. DRAM Power is Dependent on Data Values
Some variation due to infrastructure – can be subtracted
Without infrastructure variation: up to 230 mA of change
Toggle affects power consumption, but < 0.15 mA per bit
Chart: Number of Ones in a Cache Line
| 0 | 64 | 128 | 192 | 256 | 320 | 384 | 448 | 512
Vendor A | 255.83 | 308.66 | 358.24 | 415.28 | 468.42 | 530.35 | 588.1 | 627.56 | 689.65
Vendor B | 224.3 | 253.13 | 289.44 | 326.84 | 364.05 | 399.06 | 433.93 | 467.81 | 502.42
Vendor C | 227.35 | 258.53 | 294.27 | 329.21 | 364.33 | 398.02 | 431.3 | 463.66 | 496.92
Chart: Number of Ones in a Cache Line
| 0 | 64 | 128 | 192 | 256 | 320 | 384 | 448 | 512
Vendor A | 693.7869 | 655.8656 | 617.6723 | 577.6228 | 539.3236 | 498.4462 | 458.2978 | 419.7948 | 382.6493
Vendor B | 647.5426 | 608.896 | 571.9929 | 534.7461 | 497.4559 | 462.1276 | 424.2128 | 385.9581 | 350.5481
Vendor C | 542.4039 | 512.241 | 479.2756 | 449.3385 | 419.0288 | 389.3001 | 358.2096 | 327.4338 | 297.4687
DRAM power consumption depends strongly on the data value, but not on bit toggling
Notes: Replace graphs

## Slide 11: 3. Structural Variation Affects DRAM Power Usage
Vendor C: variation in idle current across banks
All vendors: variation in read current across banks
All vendors: variation in activation based on row address
Chart: 
| Vendor A | Vendor B | Vendor C
 | 1 | 1 | 1
 | 1.0134 | 1.0037 | 1.112
 | 1.0008 | 1.0004 | 1.1894
 | 1.0002 | 0.99869 | 1.179
 | 1.0039 | 1.0024 | 1.2359
 | 1.0038 | 1.0015 | 1.2249
 | 1.0056 | 1.0009 | 1.1166
 | 0.999 | 0.99824 | 1.1704
Chart: 
| Vendor A | Vendor B | Vendor C
 | 1 | 1 | 1
 | 0.99756 | 1.0339 | 1.0451
 | 1.0498 | 1.0205 | 1.0467
 | 1.0621 | 1.0244 | 1.0123
 | 1.0053 | 1.0317 | 1.0087
 | 1.0114 | 1.0249 | 1.0465
 | 1.0469 | 1.0194 | 1.0041
 | 1.0578 | 1.0448 | 1.0385
Chart: Number of Ones in Row Address
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15
Vendor A | 1 | 1.0097 | 1.02 | 1.0337 | 1.0449 | 1.0436 | 1.0552 | 1.065 | 1.0411 | 1.0776 | 1.0872 | 1.0654 | 1.0758 | 1.0718 | 1.0826 | 1.093
Vendor B | 1 | 1.0047 | 1.0092 | 1.0145 | 1.0181 | 1.0239 | 1.0705 | 1.0774 | 1.0265 | 1.0432 | 1.0456 | 1.0417 | 1.0508 | 1.0485 | 1.091 | 1.1456
Vendor C | 1 | 1.0053 | 1.0102 | 1.0207 | 1.0283 | 1.0301 | 1.0426 | 1.0149 | 1.0229 | 1.0354 | 1.0192 | 1.0273 | 1.023 | 1.0497 | 1.0447 | 1.0603
1.20
1.15
1.10
1.05
1.00
0.95
Significant structural variation: DRAM power varies systematically by bank and row
Notes: Fix bank number alignment

## Slide 12: 4. Generational Savings Are Smaller Than Expected
Similar trends for idle and read currents
IDD0
Activate–Precharge
IDD4W
Write
Actual power savings of newer DRAM is much lower than the savings indicated in the datasheets
Notes: Find sources and fix

## Slide 13: Summary of New Observations on DRAM Power
Real DRAM modules often consume less power than vendor-provided IDD values state
DRAM power consumption is dependent on the data value that is read/written
Across banks and rows, structural variation affects power consumption of DRAM
Newer DRAM modules save less power than indicated in datasheets by vendors
Detailed observations and analyses in the paper

## Slide 14: Background: DRAM Organization & Operation Characterization Methodology New Findings on DRAM Power Consumption VAMPIRE: A Variation-Aware DRAM Power Model Conclusion
Outline

## Slide 15: A New Variation-Aware DRAM Power Model
VAMPIRE: Variation-Aware model of Memory Power Informed by Real Experiments
VAMPIRE and raw characterization data will be open-source: https://github.com/CMU-SAFARI/VAMPIRE (August 2018)
VAMPIRE
Read/Write and Data-Dependent Power Modeling
Idle/Activate/Precharge Power Modeling
Structural Variation Aware Power Modeling
Inputs
(from memory system simulator)
Trace of DRAM commands, timing
Data that is being written
Outputs
Per-vendor power consumption
Range for each vendor (optional)

## Slide 16: VAMPIRE Has Lower Error Than Existing Models
Validated using new power measurements: details in the paper
VAMPIRE has very low error for all vendors: 6.8%
Much more accurate than prior models
Chart: Mean Absolute Percentage Error
| Vendor A | Vendor B | Vendor C | GMean
Micron Model | 2.4103 | 1.4924 | 0.91445 | 1.6057
DRAMPower | 0.74515 | 0.15087 | 0.076757 | 0.32426
VAMPIRE | 0.071432 | 0.068536 | 0.062684 | 0.067551

## Slide 17: VAMPIRE Enables Several New Studies
Taking advantage of structural variation to perform variation-aware physical page allocation to reduce power
Smarter DRAM power-down scheduling
Reducing DRAM energy with data-dependency-aware cache line encodings
  23 applications from the SPEC 2006 benchmark suite
  Traces collected using Pin and Ramulator
We expect there to be many other new studies in the future
Chart: Normalized DRAM Energy
| Vendor A | Vendor B | Vendor C | GMean
Baseline | 1 | 1 | 1 | 1
BDI | 1.0002 | 1.0004 | 1.0002 | 1.0003
Optimized | 1.0091 | 1.0101 | 1.0061 | 1.0084
OWI | 0.87621 | 0.87104 | 0.88807 | 0.87841

## Slide 18: Background: DRAM Organization & Operation Characterization Methodology New Findings on DRAM Power Consumption VAMPIRE: A Variation-Aware DRAM Power Model Conclusion
Outline

## Slide 19: Conclusion
DRAM consumes up to half of total system power: need to develop new low-power solutions
State-of-the-art DRAM power models are based only on IDD values, and have a high error
We make four new observations on DRAM power consumption using 50 real DRAM modules from three major vendors
  Real DRAM modules often consume less power than IDD values state
  Power consumption is dependent on the data value being read/written
  Across banks and rows, structural variation affects power consumption
  Newer DRAM modules save less power than indicated in datasheets
VAMPIRE: a new DRAM power model built on our observations
  Mean absolute percentage error of only 6.8%
  Case study: dependency-aware data encoding reduces DRAM power by 12%
More information: https://github.com/CMU-SAFARI/VAMPIRE

## Slide 20: What Your DRAM Power Models Are Not Telling You: Lessons from a Detailed Experimental Study
Saugata Ghose, A. Giray Yağlıkçı, Raghav Gupta, Donghyuk Lee, Kais Kudrolli, William X. Liu, Hasan Hassan, Kevin K. Chang, Niladrish Chatterjee, Aditya Agrawal, Mike O’Connor, Onur Mutlu
More information: https://github.com/CMU-SAFARI/VAMPIRE

## Slide 21: Backup Slides

## Slide 22: More Information in the Paper…
Full characterization analysis
Application-level comparison to existing power models
Case study: dependency-aware data encoding
Paper available at https://github.com/CMU-SAFARI/VAMPIRE
Chart: Normalized Energy
| Vendor A | Vendor B | Vendor C
Baseline | 1 | 1 | 1
BDI | 1.0002 | 1.0004 | 1.0002
Optimized | 1.0091 | 1.0101 | 1.0061
OWI | 0.87621 | 0.87104 | 0.88807

## Slide 23: Today’s Models Leave a Lot to Be Desired
Most models reliant on JEDEC-based IDD values
  Micron power calculator
  DRAMPower
  gem5/GPGPU-Sim
Some rely on circuit-level models
  Vogelsang model for memory scaling
  CACTI
None are all that accurate
  One value for each DRAM
  Does not capture any inherent variation (e.g., data, structure)

## Slide 24: How Do We Measure Current?
VDD
FPGA
SoftMC [1]
PCI-e IF
Host PC
PCI-e
DRAM Module
Rank
. . .
Chip
Chip
memory
channel
USB
Probe
Cmd Buffer
Hassan et al. “SoftMC: A Flexible and Practical Open-Source Infrastructure for Enabling Experimental DRAM Studies,” HPCA, 2017.
[1]

## Slide 25: Foundation of Current Power Models
Just how bad are current models?
JEDEC defines a set of IDD values
IDD0 | Activation and Precharge | 
IDD1 | Activation – 1 Column Read – Precharge | 
IDD2N | Precharge Standby (all banks are precharged/closed) | ✔ clk enabled
IDD3N | Active Standby (all banks are active/opened) | ✔ clk enabled
IDD2P | Precharge Power-Down (all banks are precharged/closed) | ✘clk disabled
IDD3P | Active Power-Down (all banks are active/opened) | ✘clk disabled
IDD4R/W | Burst mode Read/Write | 
IDD5B | Burst mode Refresh | 
IDD7 | Activate – Column Read w/ Auto Precharge | 

## Slide 26: What’s So Bad About That?
JEDEC defined IDD measurement loops cover:
  Average power consumption of all banks
    missing variation across banks
  Average power consumption of only two rows: 00 and F0
    missing variation across rows in a subarray
    missing variation across subarrays
  Average power consumption of only two data patterns: 00 and 33
    missing effect of number of ones/zeros in data
    missing effect of toggling bits

## Slide 27: IDD0: Activation and Precharge Energy
time
ACT
PRE
ACT
tRAS
tRP
PRE
tRAS
DRAM Array
Row Buffer
0x00
0xF0

## Slide 28: IDD1: Activation, Read, and Precharge Energy
Row Buffer
DRAM Array
0x00
0xF0
time
ACT
PRE
ACT
tRCD
tRP
RD
tRAS

## Slide 29: IDD2N: Precharged Standby
Row Buffer
DRAM Array
Bank 0
Bank 1
Bank 7
(1) Precharge All Banks (Close Row Buffers)
(2) Wait
Row Buffer
DRAM Array
Row Buffer
DRAM Array

## Slide 30: IDD3N: Active Standby
Row Buffer
DRAM Array
Row Buffer
DRAM Array
Row Buffer
DRAM Array
Bank 0
Bank 1
Bank 7
Activate All Banks
(Open Row Buffers)
(2) Wait

## Slide 31: IDD2P: Precharged Power Down
Row Buffer
DRAM Array
Bank 0
Bank 1
Bank 7
(1) Precharge All Banks (Close Row Buffers)
(2) Wait
Row Buffer
DRAM Array
Row Buffer
DRAM Array
CLK is Disabled

## Slide 32: IDD4R: Burst Read Current
Row Buffer
DRAM Array
Row Buffer
DRAM Array
Row Buffer
DRAM Array
Bank 0
Bank 1
Bank 7
Activate All Banks
(Open Row Buffers)
(2) Read one column at a time
(3) Interleave across banks after each read
0
1
7
8
9
15
0x00 0x33
0x00 0x33
0x00 0x33

## Slide 33: IDD4W: Burst Write Current
Row Buffer
DRAM Array
Row Buffer
DRAM Array
Row Buffer
DRAM Array
Bank 0
Bank 1
Bank 7
Activate All Banks
(Open Row Buffers)
(2) Write one column at a time
(3) Interleave across banks after each read
0
1
7
8
9
15
0x00 0x33
0x00 0x33
0x00 0x33

## Slide 34: IDD5B: Refresh in Burst Mode
Chart: 
 | 0 | 0 | 0 | 0 | 0 | 1 | 0.93333 | 0.86667 | 0.84444 | 0.83333 | 0.82667 | 0.82222 | 0.81905 | 0.81667 | 0.81481 | 0.81333 | 0.81212 | 1 | 0.93333 | 0.86667 | 0.84444 | 0.83333 | 0.82667 | 0.82222 | 0.81905 | 0.81667 | 0.81481 | 0.81333 | 0.81212 | 1 | 0.93333 | 0.86667 | 0.84444 | 0.83333 | 0.82667 | 0.82222 | 0.81905 | 0.81667 | 0.81481 | 0.81333 | 0.81212 | 1 | 0.93333 | 0.86667 | 0.84444 | 0.83333 | 0.82667 | 0.82222 | 0.81905 | 0.81667 | 0.81481
tREFI (64ms)
tRFC
time
REF
REF
tRFC
Burst Mode:
REF
tRFC

## Slide 35: IDD7: Read, Auto-Precharge
ACT-RDA
time
ACT-RDA
tRRD
tRRD
ACT-RDA
tRRD

## Slide 36: Impact of Bit Toggling on DRAM Power
0000 1010 1111 … 0011
Bank 0 Row Buffer
0
1
column
number
2
c – 1
1011 0010 1011 … 0110
Bank 1 Row Buffer
0
1
2
c – 1
1011 0010 1011 … 0110
Bank 7 Row Buffer
0
1
2
c – 1
1
2
. . .
. . .
. . .
. . .
. . .
. . .
. . .
Column Select
Column Select
Column Select
Bank Select
global bitlines
peripheral bus
to I/O drivers
global bitlines
Notes: Replace toggle figure

## Slide 37: Data Dependency Model
 | Read |  |  | Write |  | 
 | F (mA) | G (mA) | H (mA) | F (mA) | G (mA) | H (mA)
Vendor A | 246.44 | 0.433 | 0.0515 | 531.18 | -0.246 | 0.0461
Vendor B | 217.42 | 0.157 | 0.0947 | 466.84 | -0.215 | 0.0166
Vendor C | 234.42 | 0.154 | 0.0856 | 368.29 | -0.116 | 0.0229
y = F + Gn + Ht
Additional current per bit toggle
Additional current per logic-1
Chart: Number of Ones in a Cache Line
| 0 | 64 | 128 | 192 | 256 | 320 | 384 | 448 | 512
Vendor A | 255.83 | 308.66 | 358.24 | 415.28 | 468.42 | 530.35 | 588.1 | 627.56 | 689.65
Vendor B | 224.3 | 253.13 | 289.44 | 326.84 | 364.05 | 399.06 | 433.93 | 467.81 | 502.42
Vendor C | 227.35 | 258.53 | 294.27 | 329.21 | 364.33 | 398.02 | 431.3 | 463.66 | 496.92
Chart: Number of Ones in a Cache Line
| 0 | 64 | 128 | 192 | 256 | 320 | 384 | 448 | 512
Vendor A | 693.7869 | 655.8656 | 617.6723 | 577.6228 | 539.3236 | 498.4462 | 458.2978 | 419.7948 | 382.6493
Vendor B | 647.5426 | 608.896 | 571.9929 | 534.7461 | 497.4559 | 462.1276 | 424.2128 | 385.9581 | 350.5481
Vendor C | 542.4039 | 512.241 | 479.2756 | 449.3385 | 419.0288 | 389.3001 | 358.2096 | 327.4338 | 297.4687

## Slide 38: Models
https://github.com/CMU-SAFARI/VAMPIRE
Notes: Update tables

## Slide 39: Structural Variation
Normalized
Read Burst Energy across Banks
Normalized
Active Standby Energy
across Banks
Normalized
Write Burst Energy across Banks
Notes: Standby is upto 23%

## Slide 40: Evaluated System Configuration
Application traces collected using Pin
DRAM command timings generated using Ramulator: https://github.com/CMU-SAFARI/ramulator
Processor | x86-64 ISA, one core 3.2 GHz, 128-entry instruction window
Cache | L1: 64 kB, 4-way associative; L2: 2 MB, 16-way associative
Memory Controller | 64/64-entry read/write request queues, FR-FCFS [119, 149]
DRAM | DDR3L-800 [57], 1 channel, 1 rank/8 banks per channel
Notes: Make bigger

## Slide 41: Trends Across Generations
Basically, if you’re building a system, you aren’t getting the kinds of savings you were promised
Activation Energy
Precharge Standby Energy
Read Energy
Write Energy

## Slide 42: Data Encoding
Baseline: No coding
BDI: Base Delta Immediate
Optimized: Minimize the number of ones
OWI: Minimize ones for reads, maximize ones for writes
Chart: Normalized Energy
| Vendor A | Vendor B | Vendor C
Baseline | 1 | 1 | 1
BDI | 0.99637 | 0.99984 | 0.99568
Optimized | 0.96929 | 0.98504 | 0.97792
OWI | 0.72661 | 0.71389 | 0.74259
12.5%
Energy
Reduction
Notes: Update graph

## Slide 43: Validating Our DRAM Power Models
New tests run on 22 of our DDR3L DRAM SO-DIMMs
Validation command sequence
  Activate
  n reads
    Sweep n from 0 to 764
    All reads contain data value 0xAA
    All reads to Bank 0, Row 128
    Column interleaved
  Precharge
Error metric: mean absolute percentage error (MAPE)
Best prior model (DRAMPower): 32.4% MAPE
VAMPIRE: 6.8% MAPE