## Slide 1
The Virtual Block Interface: A Flexible Alternative
to the Conventional Virtual Memory Framework
Nastaran Hajinazar , Pratyush Patel , Minesh Patel , Konstantinos Kanellopoulos , Saugata Ghose ,
Rachata Ausavarungnirun , Geraldo F. Oliveira , Jonathan Appavoo , Vivek Seshadri , Onur Mutlu
7: Example Use Case: Address Translation
5: VBI Design Overview
2: Example Challenges of the Conventional Virtual Memory Framework
3: Our Goal
1
1: Motivation
8: Conclusion
  Design an alternative virtual memory framework that
  Efficiently and flexibly supports increasingly diverse system configurations
  Provides the key features of conventional virtual memory framework while eliminating its key inefficiencies
Modern computing systems continue to diversify with respect to system architecture, memory technologies, and applications’ memory needs
Continually adapting the conventional virtual memory framework to each possible system configuration is challenging
VBI is a promising new virtual memory framework
Can enable several important optimizations
Increases design flexibility for virtual memory
A new direction for future work in novel virtual memory frameworks
Page tables need to be shared between, and understood by both the hardware and the OS, resulting in rigid page table structures
Challenging to implement the page table flexibility that applications can benefit from
Key Takeaways
1. VBI-full improves the performance, by 2.4X on average compared to Native
2. VBI-full enables significant performance improvement in virtualized environments (4.3X on average compared to Virtual)
3. VBI-full outperforms Perfect TLB (by 49% on average) as the optimizations that VBI enables are not limited to only reducing the address translation overhead
https://www.youtube.com/watch?v=7c6LgVrCwPo
https://people.inf.ethz.ch/omutlu/pub/VBI-virtual-block-interface_isca20.pdf
Full Paper
Full Talk Video
2
3
4
5
6
7
1,2
3
1
1
4
5
1
6
7
1,4
Applications
Virtual Memory
managed by the operating system
Hardware
Cannot adapt
efficiently
Virtual Address Space (VAS)
P1
VAS 1
P2
Pn
Page Tables
managed by the OS
Physical Memory
VAS 2
VAS n
. . .
Processes
Guest OS
Host Virtual Address Space
Host OS
Host Page Tables
Physical Memory
---- virtualization layer ----
Guest Virtual Address Space
g VAS
Guest Page Tables
VAS 1
VAS 2
guest virtual – to – host virtual
host virtual – to – host physical
P2
P1
In virtual machines, both the guest and host OS perform address translation, resulting in an extra level of indirection
Challenging to perform computation in virtualized environments, efficiently
Virtual Address Space (VAS)
VAS 1
Page Tables
managed by the OS
Slow Mem.
Fast Mem.
P1
OS that defines and manages the address mapping, has low visibility into fine-grained runtime memory behavior information
Challenging in heterogenous memories to make timely migration decisions based on quickly changing memory access patterns or other dynamic behavior
Globally-visible VBI address space
Consists of a set of virtual blocks (VBs) of different sizes
Provides system-wide unique VBI addresses
VBI addresses are directly used to access on-chip caches
Pros: Enables inherently virtual caches
All VBs are visible to all processes
OS controls which processes access which VBs
Each process has its own permissions (read/write/execute) when attaching to a VB
OS maintains a list of VBs attached to each process used to perform permission checks
Processes map each semantically meaningful unit of information to a separate VB
e.g., a data structure, a shared library
Memory management is delegated to the Memory Translation Layer (MTL) in the memory controller
Address translation and Physical memory allocation
Translation structures are not shared with the OS
Per-VB translation structure tuned to the VB’s characteristics
Pros: many benefits, including
  Address translation overhead for the processes running inside a virtual machine, is no different than the processes running natively on system
  Enabling flexible translation structures
Virtual Address Space (VAS)
P1
VAS 1
P2
Pn
Page Tables
managed by the OS
Physical Memory
VAS 2
VAS n
. . .
Processes
VBI
Conventional Virtual Memory
one-to-one
mapping (OS)
fixed-size (256 TB)
VBI Address Space
P1
VB 1
P2
Pn
Memory Translation Layer
in the memory controller
Physical Memory
VB 2
VB 3
VB 4
. . .
Processes
many-to-many
mapping (OS)
variable-size (4 KB – 128 TB)
VBI-to-physical translation
virtual-to-physical translation
Key idea: Delegate physical memory management to dedicated hardware in the memory controller
Guiding Principles:
Size virtual address spaces appropriately for processes
- Mitigates translation overheads of unnecessarily large address spaces
Decouple address translation from access protection
- Defers address translation until necessary to access memory
- Enables the flexibility of managing translation and protection using separate structures
Communicate data semantics to the hardware
- Enables intelligent resource management
4: Virtual Block Interface (VBI)
  Achieving the guiding principles:
  A process’ VBs define its address space, i.e., determined by the actual needs of the process
  Address mapping is dedicated to the MTL, while OS retains full control over managing the access permissions
  Each VB is associated with a set of information:
  A System-wide unique ID
  Size of the VB
  Enable bit
  Reference counter: number of processes attached to the VB
  Properties bit vector: semantic information about VB contents, such as access pattern, latency sensitive vs. bandwidth sensitive
6: Optimizations Enabled by VBI
Chart: 
| astar | bzip2 | GemsFDTD | mcf | milc | namd | sjeng | bwaves-17 | deepsjeng-17 | lbm-17 | omnetpp-17 | img-dnn | moses | Graph500 | AVG
Virtual | 0.2606 | 0.3532 | 0.3538 | 0.1726 | 0.6883 | 0.9799 | 0.6527 | 0.8699 | 0.74598 | 0.8131 | 0.40677 | 0.66991 | 0.25863 | 0.75242 | 0.56984
Perfect TLB | 1.5738 | 1.4731 | 1.6118 | 8.9041 | 2.1443 | 1.1 | 1.1559 | 1.2328 | 1.146 | 1.2689 | 1.3625 | 1.2982 | 1.9246 | 1.2554 | 1.9608
VBI-Full | 1.6116 | 1.4734 | 1.8074 | 13.3753 | 2.1034 | 1.1033 | 1.1757 | 1.7194 | 1.2013 | 1.8486 | 1.7323 | 1.6141 | 2.1654 | 1.4239 | 2.4539
Speedup
13.3
8.9
  Native: applications run natively on an x86-64 system
  Virtual: applications run inside a virtual machine (accelerated using 2D page walk cache [Bhargava+, ASPLOS’08])
  Perfect TLB: an unrealistic version of Native with no translation overhead
  VBI-Full: VBI with all the optimizations that it enables
  Naturally enabled by VBI and not easily attainable before:
  Appropriately sized process address space
  Flexible address translation structures
  Communicating data semantics to the hardware
  Inherently virtual caches
  Eliminating 2D page walks in virtual machines
  Delayed physical memory allocation
  Early memory reservation mechanism
VB
Enable
Reference Counter
Properties
Size
X
Inherent to VBI design
Covered in the paper