## Slide 1: The Virtual Block Interface: A Flexible Alternative to the Conventional Virtual Memory Framework
Nastaran Hajinazar Pratyush Patel Minesh Patel Konstantinos Kanellopoulos Saugata Ghose Rachata Ausavarungnirun Geraldo F. Oliveira Jonathan Appavoo Vivek Seshadri Onur Mutlu

## Slide 2: Executive Summary
  Motivation: Modern computing systems continue to diversify with respect to system architecture, memory technologies, and applications’ memory needs
  Problem: Continually adapting the conventional virtual memory framework to each possible system configuration is challenging
  Results in performance loss or requires non-trivial workarounds
Goal: Design an alternative virtual memory framework that
(1) Efficiently supports a wide variety of new system configurations
(2) Provides the key features and eliminates the key inefficiencies of the conventional virtual memory framework
Virtual Block Interface (VBI): Delegates memory management to dedicated hardware in the memory controller
  Efficiently adapts to diverse system configurations
  Reduces overheads and complexities associated with conventional virtual memory
  Enables many optimizations (e.g., low-overhead page walks in virtual machines, virtual caches)
Evaluation: Two example use cases
  VBI significantly improves performance for both native execution (2.4x) and virtual machine environments (4.3x)
    VBI significantly improves heterogeneous memory architecture effectiveness
2

## Slide 3: Outline
Motivation
3
VBI: Virtual Block Interface
Key Idea & Guiding Principles
Design Overview
Optimizations Enabled by VBI
Methodology
Results
Summary

## Slide 4: Outline
Motivation
4
VBI: Virtual Block Interface
Key Idea & Guiding Principles
Design Overview
Optimizations Enabled by VBI
Methodology
Results
Summary

## Slide 5: Virtual Memory
5
Application
Hardware
Virtual Memory
managed by the operating system

## Slide 6: Computing Systems Are Diversifying
6
Application
Virtual Memory
managed by the operating system
Hardware
Cannot adapt
efficiently

## Slide 7: Computing Systems Are Diversifying
7
Application
Virtual Memory
managed by the operating system
Hardware
Cannot adapt
efficiently
Continually adapting the conventional virtual memory framework is challenging

## Slide 8: Conventional Virtual Memory Framework
8
Virtual Address Space (VAS)
P1
VAS 1
P2
Pn
Page Tables
managed by the OS
Physical Memory
VAS 2
VAS n
. . .
Processes

## Slide 9: Conventional Virtual Memory Framework
9
Virtual Address Space (VAS)
P1
VAS 1
P2
Pn
Page Tables
managed by the OS
Physical Memory
VAS 2
VAS n
. . .
Processes
each process is mapped to a fixed-size virtual address space
e.g., 256 TB in Intel x86-64

## Slide 10: Conventional Virtual Memory Framework
10
Virtual Address Space (VAS)
P1
VAS 1
P2
Pn
Page Tables
managed by the OS
Physical Memory
VAS 2
VAS n
. . .
Processes
one-to-one mapping
managed by the OS

## Slide 11: Conventional Virtual Memory Framework
11
Virtual Address Space (VAS)
P1
VAS 1
P2
Pn
Page Tables
managed by the OS
Physical Memory
VAS 2
VAS n
. . .
Processes
per-process page tables to map each VAS to physical memory
managed by the OS
read by hardware

## Slide 12: Challenges
Three examples of the challenges in adapting conventional virtual memory frameworks for increasingly-diverse systems:
  Requiring a rigid page table structure
  High address translation overhead in virtual machines
  Inefficient heterogeneous memory management
12

## Slide 13: Challenge 1: Rigid Page Table Structures
Flexibly customized page tables can reduce the address translation overhead
  Customized to the application’s memory behavior
    e.g., larger granularities for more densely
    allocated memory regions
Con:
  Requires a rigid page table structure
    e.g., fixed-granularity 4-level page table in Intel x86
13
Virtual Address Space (VAS)
P1
VAS 1
P2
Pn
Page Tables
managed by the OS
Physical Memory
VAS 2
VAS n
. . .
Processes
accessed by both OS and hardware

## Slide 14: Challenges
Three examples of the challenges in adapting conventional virtual memory frameworks for increasingly-diverse systems:
  Requiring a rigid page table structure
  High address translation overhead in virtual machines
  Inefficient heterogeneous memory management
14

## Slide 15: Challenge 2: Overheads in Virtual Machines
15
Host Virtual Address Space
Host OS
Host Page Tables
Physical Memory
Process 1
VAS 1

## Slide 16: Challenge 2: Overheads in Virtual Machines
16
In virtual machines, processes go through an extra level of indirection
Con:
  2D page table walks
Guest OS
Host Virtual Address Space
Host OS
Process 2
Host Page Tables
Physical Memory
---- virtualization layer ----
Guest Virtual Address Space
g VAS
Guest Page Tables
Process 1
VAS 1
VAS 2
guest virtual – to – host virtual
host virtual – to – host physical

## Slide 17: Challenges
Three examples of the challenges in adapting conventional virtual memory frameworks for increasingly-diverse systems:
  Requiring a rigid page table structure
  High address translation overhead in virtual machines
  Inefficient heterogeneous memory management
17

## Slide 18: Challenge 3: Managing Heterogeneous Memory
Page Tables
managed by the OS
Enhancing performance with heterogenous memories requires:
  Data mapping
18
Virtual Address Space (VAS)
P1
VAS 1
Slow Mem.
Fast Mem.

## Slide 19: Challenge 3: Managing Heterogeneous Memory
19
Virtual Address Space (VAS)
P1
VAS 1
Page Tables
managed by the OS
Slow Mem.
Fast Mem.
Enhancing performance with
heterogenous memories requires:
  Data mapping
  Data migration
Con:
  OS has low visibility into runtime memory behavior
    Timely reaction to the changes is challenging

## Slide 20: Prior Works
Optimizations that alleviate the overheads of the conventional virtual memory framework
Shortcomings:
Based on specific system or workload characteristics
  Are applicable to only limited problems or applications
Require specialized and not necessarily compatible changes to both the OS and hardware
  Implementing all in a system is a daunting prospect
20

## Slide 21: Prior Works
Optimizations that alleviate the overheads of the conventional virtual memory framework
Shortcomings:
Based on specific system or workload characteristics
  Are applicable to only limited problems or applications
Require specialized and not necessarily compatible changes to both the OS and hardware
  Implementing all in a system is a daunting prospect
21
We need a holistic solution that efficiently supports increasingly diverse system configurations

## Slide 22: Our Goal
Design an alternative virtual memory framework that
  Efficiently and flexibly supports increasingly diverse system configurations
  Provides the key features of conventional virtual memory framework while eliminating its key inefficiencies
22

## Slide 23: Outline
Motivation
23
VBI: Virtual Block Interface
Key Idea & Guiding Principles
Design Overview
Optimizations Enabled by VBI
Methodology
Results
Summary

## Slide 24: Virtual Block Interface (VBI)
VBI is an alternative virtual memory framework
  Key idea:
  Delegate physical memory management to dedicated hardware in the memory controller
24

## Slide 25: VBI: Guiding Principles
Size virtual address spaces appropriately for processes
  Mitigates translation overheads of unnecessarily large address spaces
Decouple address translation from access protection
  Defers address translation until necessary to access memory
  Enables the flexibility of managing translation and protection using separate structures
Communicate data semantics to the hardware
  Enables intelligent resource management
25
Addresses the rigidness and lack of information in current frameworks, to reduce large overheads

## Slide 26: Outline
Motivation
26
VBI: Virtual Block Interface
Key Idea & Guiding Principles
Design Overview
Optimizations Enabled by VBI
Methodology
Results
Summary

## Slide 27: VBI: Overview
27
Virtual Address Space (VAS)
P1
VAS 1
P2
Pn
Page Tables
managed by the OS
Physical Memory
VAS 2
VAS n
. . .
Processes
VBI
Conventional Virtual Memory
VBI Address Space
P1
VB 1
P2
Pn
Memory Translation Layer
in the memory controller
Physical Memory
VB 2
VB 3
VB 4
. . .
Processes

## Slide 28: Virtual Blocks
VBI Address Space
P1
VB 1
P2
Pn
Memory Translation Layer
in the memory controller
Physical Memory
VB 2
VB 3
VB 4
. . .
Processes
Globally-visible VBI address space
28

## Slide 29: Virtual Blocks
VBI Address Space
P1
VB 1
P2
Pn
Memory Translation Layer
in the memory controller
Physical Memory
VB 2
VB 3
VB 4
. . .
Processes
Globally-visible VBI address space
  Consists of a set of virtual blocks (VBs) of different sizes
    Example size classes: 4 KB, 128 KB, 4 MB, 128 MB, 4 GB, 128 GB, 4 TB, 128 TB
29

## Slide 30: Virtual Blocks
VBI Address Space
P1
VB 1
P2
Pn
Memory Translation Layer
in the memory controller
Physical Memory
VB 2
VB 3
VB 4
. . .
Processes
Globally-visible VBI address space
  Consists of a set of virtual blocks (VBs) of different sizes
    Example size classes: 4 KB, 128 KB, 4 MB, 128 MB, 4 GB, 128 GB, 4 TB, 128 TB
All VBs are visible to all processes
30

## Slide 31: Virtual Blocks
VBI Address Space
P1
VB 1
P2
Pn
Memory Translation Layer
in the memory controller
Physical Memory
VB 2
VB 3
VB 4
. . .
Processes
Globally-visible VBI address space
  Consists of a set of virtual blocks (VBs) of different sizes
    Example size classes: 4 KB, 128 KB, 4 MB, 128 MB, 4 GB, 128 GB, 4 TB, 128 TB
All VBs are visible to all processes
Processes map each semantically meaningful unit of information
to a separate VB
  e.g., a data structure, a shared library
31

## Slide 32: Inherently Virtual Caches
VBI address space provides system-wide unique VBI addresses
VBI addresses are directly used to access on-chip caches
  No longer require address translation
Pros:
  Enables inherently virtual caches
    no synonyms and homonyms
32
VBI Address Space
P1
VB 1
P2
Pn
Memory Translation Layer
in the memory controller
Physical Memory
VB 2
VB 3
VB 4
. . .
Processes

## Slide 33: Hardware-Managed Memory
Memory management is delegated to the Memory Translation Layer (MTL) in the memory controller
  Address translation
  Physical memory allocation
Pros: Many benefits, including
  Physical memory is allocated only when the location needs to be written to memory
  No need for 2D page walks in virtual machines
  Enabling flexible translation structures
33
VBI Address Space
P1
VB 1
P2
Pn
Memory Translation Layer
in the memory controller
Physical Memory
VB 2
VB 3
VB 4
. . .
Processes

## Slide 34: OS-Managed Access Permissions
VBI Address Space
P1
VB 1
P2
Pn
Memory Translation Layer
in the memory controller
Physical Memory
VB 2
VB 3
VB 4
. . .
Processes
OS controls which processes access which VBs
Each process has its own permissions (read/write/execute) when attaching to a VB
OS maintains a list of VBs attached to each process
  Stored in a per-process table
  Used during permission checks
34

## Slide 35: Process Address Space in VBI
Virtual Address Space (VAS)
P1
VAS 1
P2
Pn
Page Tables
managed by the OS
Physical Memory
VAS 2
VAS n
. . .
Processes
VBI Address Space
P1
VB 1
P2
Pn
Memory Translation Layer
in the memory controller
Physical Memory
VB 2
VB 3
VB 4
. . .
Processes
Any process can attach to any VB
A process' VBs define its address space
  Address space size is determined by the actual needs of the process
the address space of process P1
35

## Slide 36: Process Address Space in VBI
VBI Address Space
P1
VB 1
P2
Pn
Memory Translation Layer
in the memory controller
Physical Memory
VB 2
VB 3
VB 4
. . .
Processes
Any process can attach to any VB
A process' VBs define its address space
  Address space size is determined by the actual needs of the process
the address space of process P1
36
First guiding principle:
Appropriately-sized virtual address spaces

## Slide 37: Decoupled Protection and Translation
Address mapping
managed by OS
37
Virtual Address Space (VAS)
P1
VAS 1
P2
Pn
Page Tables
managed by the OS
Physical Memory
VAS 2
VAS n
. . .
Processes
Access permissions
managed by OS
VBI Address Space
P1
VB 1
P2
Pn
Memory Translation Layer
in the memory controller
Physical Memory
VB 2
VB 3
VB 4
. . .
Processes
Access permissions
managed by OS
Address mapping
managed by the MTL
Conventional virtual memory
VBI

## Slide 38: Decoupled Protection and Translation
Address mapping
managed by OS
38
Access permissions
managed by OS
VBI Address Space
P1
VB 1
P2
Pn
Memory Translation Layer
in the memory controller
Physical Memory
VB 2
VB 3
VB 4
. . .
Processes
Access permissions
managed by OS
Address mapping
managed by the MTL
Second guiding principle:
Decoupling address translation from access protection
VBI

## Slide 39: Address Translation Structures in VBI
VBI Address Space
P1
VB 1
P2
Pn
Memory Translation Layer
in the memory controller
Physical Memory
VB 2
VB 3
VB 4
. . .
Processes
39
Translation structures are not shared with the OS
  Separate structures for translation
  and permission information
  Allows flexible translation structures
  Per-VB translation structure tuned to the VB’s characteristics e.g., single-level tables for small VBs
Pros:
  Lowers overheads and allows for customization

## Slide 40: VB Information
VBI Address Space
P1
VB 1
P2
Pn
Memory Translation Layer
in the memory controller
Physical Memory
VB 2
VB 3
VB 4
. . .
Processes
VB
Enable
Reference Counter
Properties
Size
Each VB is associated with
  System-wide unique ID
  Size i.e., which size class
  Enable bit
  Reference counter number of processes attached to the VB
  Properties bit vector
  semantic information about VB contents, e.g., access pattern, latency sensitive vs. bandwidth sensitive
X
40

## Slide 41: VB Information
VBI Address Space
P1
VB 1
P2
Pn
Memory Translation Layer
in the memory controller
Physical Memory
VB 2
VB 3
VB 4
. . .
Processes
VB
Enable
Reference Counter
Properties
Size
Each VB is associated with
  System-wide unique ID
  Size i.e., which size class
  Enable bit
  Reference counter number of processes attached to the VB
  Properties bit vector
  semantic information about VB contents, e.g., access pattern, latency sensitive vs. bandwidth sensitive
X
41
Third guiding principle:
Communicating data semantics to the hardware

## Slide 42: Implementing VBI
Please refer to our paper
  Detailed reference implementation and microarchitecture
42
Memory Controller
Memory Translation Layer (MTL)
L1
miss
VBUID offset
L2
Last-Level Cache (LLC)
index = request_vb(...);
x = malloc(index, size);
.
.
.
y = (*x);
Virtual
Address
Application
index offset
miss
VBI
Address
CPU
Physical Memory
VITs
CVTs
enable_vb
attach
CVT (Client–VB Table) Cache
Translation Structures
Data
Translation Walker
Physical Address
TLB
miss
hit
VIT (VB Info Table) Cache

## Slide 43: Outline
Motivation
43
VBI: Virtual Block Interface
Key Idea & Guiding Principles
Design Overview
Optimizations Enabled by VBI
Methodology
Results
Summary

## Slide 44: Optimizations Naturally Enabled by VBI
Many optimizations not easily attainable before
Examples:
  Appropriately sized process address space
  Flexible address translation structures
  Communicating data semantics to the hardware
  Inherently virtual caches
  Delayed physical memory allocation
  Eliminating 2D page walks in virtual machines
  Early memory reservation mechanism
44
Achieved through guiding principles
Covered in our paper
Covered next

## Slide 45: Example Optimizations
  Inherently virtual caches
  Delayed physical memory allocation
  Eliminating 2D page walks in virtual machines
45

## Slide 46: Inherently Virtual Caches
In VBI
In Conventional Virtual Memory
virtually-indexed virtually-tagged
(VIVT)
46
VIPT
Cache
Core
Physical Memory
TLB
virtual address
miss
hit
physical address
VIVT
Cache
Core
Physical Memory
TLB
virtual address
physical address
VBI
Cache
Core
Physical Memory
MTL
VBI address
physical address
permission check
page walk
miss
VIVT
Cache
Synonyms
&
homonyms
miss
miss
permission check
VBI
Cache
No
Synonyms
&
homonyms
physical address
page walk
system-wide
unique
virtually-indexed physically-tagged
(VIPT)

## Slide 47: Inherently Virtual Caches
In Conventional Virtual Memory
In VBI
virtually-indexed virtually-tagged
(VIVT)
caches in VBI
47
VIPT
cache
Core
Physical Memory
TLB
virtual address
miss
hit
physical address
VIVT
cache
Core
Physical Memory
TLB
virtual address
physical address
VBI
cache
Core
Physical Memory
MTL
VBI address
physical address
permission check
page walk
miss
VIVT
Cache
Synonyms
&
homonyms
miss
miss
permission check
VBI
Cache
No
Synonyms
&
homonyms
physical address
page walk
system-wide
unique
virtually-indexed physically-tagged
(VIPT)
VBI reduces address translation overhead by enabling benefits akin to VIVT caches

## Slide 48: Example Optimizations
  Inherently virtual caches
  Delayed physical memory allocation
  Eliminating 2D page walks in virtual machines
48

## Slide 49: Delayed Physical Memory Allocation
miss
page walk
In VBI
virtually-indexed physically-tagged (VIPT)
In Conventional Virtual Memory
49
VIPT
Cache
Core
Physical Memory
TLB
virtual address
hit
physical address
VBI
Cache
Core
Physical Memory
MTL
VBI address
miss
no memory
allocated
miss
zeroed
cache line
actual
cache line

## Slide 50: Delayed Physical Memory Allocation
miss
page walk
50
VIPT
cache
Core
Physical Memory
TLB
virtual address
hit
physical address
VBI
Cache
Core
Physical Memory
MTL
VBI address
write
back
allocates
memory
actual
cache line
miss
virtually-indexed physically-tagged (VIPT)
In Conventional Virtual Memory
In VBI

## Slide 51: Delayed Physical Memory Allocation
51
VBI
Cache
Core
Physical Memory
MTL
VBI address
write
back
allocates
memory
No address translation for accesses to regions with no allocation
No memory accesses to regions with no allocation yet
No memory allocation for VBs that never leave the cache during their lifetime
In VBI

## Slide 52: Delayed Physical Memory Allocation
In VBI
52
VBI
Cache
Core
Physical Memory
MTL
VBI address
write
back
Allocates
memory
No address translation for accesses to regions with no allocation
No memory access to regions with no allocation yet
No memory allocation for VBs that never leave the cache during their lifetime
VBI reduces address translation overhead, improves overall performance,
and reduces memory consumption

## Slide 53: Example Optimizations
  Inherently virtual caches
  Inherently virtual caches
  Eliminating 2D page walks in virtual machines
53

## Slide 54: Eliminating 2D Page Walks in Virtual Machines
Guest OS
54
Host Virtual Address Space
Host OS
Process 2
Host Page Tables
Physical Memory
---- virtualization layer ----
Guest Virtual Address Space
g VAS
Guest Page Tables
Process 1
VAS 1
VAS 2
Process running on a virtual machine (VM)
guest virtual – to – host virtual
host virtual – to – host physical
Conventional virtual memory

## Slide 55: Eliminating 2D Page Walks in Virtual Machines
Guest OS
55
Host Virtual Address Space
Host OS
Process 2
Host Page Tables
Physical Memory
---- virtualization layer ----
Guest Virtual Address Space
g VAS
Guest Page Tables
Process 1
VAS 1
VAS 2
Process running on a virtual machine (VM)
guest virtual – to – host virtual
host virtual – to – host physical
Guest OS
VBI Address Space
Host OS
Process 1
VB 1
Process 2
Memory Translation Layer
in Memory Controller
Physical Memory
VB 2
VB 3
---- virtualization layer ----
Conventional virtual memory

## Slide 56: Eliminating 2D Page Walks in Virtual Machines
Guest OS and host OS interact once to attach Process 1 to its VBs
56
MTL is the only component in the system that manages address mapping
Guest OS
VBI Address Space
Host OS
Process 1
VB 1
Process 2
Memory Translation Layer
in Memory Controller
Physical Memory
VB 2
VB 3
---- virtualization layer ----
VBI

## Slide 57: Eliminating 2D Page Walks in Virtual Machines
Guest OS and host OS interact once to attach Process 1 to its VBs
57
MTL performs address translation and memory allocation
Guest OS
VBI Address Space
Host OS
Process 2
VB 1
Process 1
Memory Translation Layer
in Memory Controller
Physical Memory
VB 2
VB 3
---- virtualization layer ----
By eliminating 2D page walks, VBI reduces address translation overhead in virtualized environments

## Slide 58: Outline
Motivation
58
VBI: Virtual Block Interface
Key Idea & Guiding Principles
Design Overview
Optimizations Enabled by VBI
Methodology
Results
Summary

## Slide 59: Methodology
Simulator: heavily-modified version of Ramulator
  Models virtual memory components (e.g., TLBs, page tables)
  Available at https://github.com/CMU-SAFARI/Ramulator-VBI
Workloads: SPECspeed 2017, SPEC CPU 2006, TailBench, Graph 500
System parameters:
  Core: 4-wide issue, OOO, 128-entry ROB
  L1 Cache: 32 KB, 8-way associative, 4 cycles
  L2 Cache: 256 KB, 8-way associative, 8 cycles
  L3 Cache: 8 MB (2 MB per-core), 16-way associative, 31 cycles
  L1 DTLB: - 4 KB pages: 64-entry, fully associative
  - 2 MB pages: 32-entry, fully associative
  L2 DTLB: 4 KB and 2 MB pages: 512-entry, 4-way associative
  Page Walk Cache: 32-entry, fully associative
  DRAM: DDR3-1600, 1 channel, 1 rank/channel, 8 banks/rank
  PCM: PCM-800, 1 channel, 1 rank/channel, 8 banks/rank
59

## Slide 60: Outline
Motivation
60
VBI: Virtual Block Interface
Key Idea & Guiding Principles
Design Overview
Optimizations Enabled by VBI
Methodology
Results
Summary

## Slide 61: Use Case 1: Address Translation
The impact of VBI on reducing the address translation overhead in both native execution and virtual machines
Evaluated systems:
  Three baselines:
    Native: applications run natively on an x86-64 system
    Virtual: applications run inside a virtual machine (accelerated using 2D page walk cache [Bhargava+, ASPLOS’08])
    Perfect TLB: an unrealistic version of Native with no translation overhead
  One VBI configuration:
    VBI-Full: VBI with all the optimizations that it enables
See our paper for results on more system configurations
61

## Slide 62: Use Case 1: Address Translation
Chart: 
| astar | bzip2 | GemsFDTD | mcf | milc | namd | sjeng | bwaves-17 | deepsjeng-17 | lbm-17 | omnetpp-17 | img-dnn | moses | Graph500 | AVG
Virtual | 0.2606 | 0.3532 | 0.3538 | 0.1726 | 0.6883 | 0.9799 | 0.6527 | 0.8699 | 0.74598 | 0.8131 | 0.40677 | 0.66991 | 0.25863 | 0.75242 | 0.56984
Perfect TLB | 1.5738 | 1.4731 | 1.6118 | 8.9041 | 2.1443 | 1.1 | 1.1559 | 1.2328 | 1.146 | 1.2689 | 1.3625 | 1.2982 | 1.9246 | 1.2554 | 1.9608
VBI-Full | 1.6116 | 1.4734 | 1.8074 | 13.3753 | 2.1034 | 1.1033 | 1.1757 | 1.7194 | 1.2013 | 1.8486 | 1.7323 | 1.6141 | 2.1654 | 1.4239 | 2.4539
62
Speedup
Normalized to Native
0.7x
13.3
8.9

## Slide 63: Use Case 1: Address Translation
Chart: 
| astar | bzip2 | GemsFDTD | mcf | milc | namd | sjeng | bwaves-17 | deepsjeng-17 | lbm-17 | omnetpp-17 | img-dnn | moses | Graph500 | AVG
Virtual | 0.2606 | 0.3532 | 0.3538 | 0.1726 | 0.6883 | 0.9799 | 0.6527 | 0.8699 | 0.74598 | 0.8131 | 0.40677 | 0.66991 | 0.25863 | 0.75242 | 0.56984
Perfect TLB | 1.5738 | 1.4731 | 1.6118 | 8.9041 | 2.1443 | 1.1 | 1.1559 | 1.2328 | 1.146 | 1.2689 | 1.3625 | 1.2982 | 1.9246 | 1.2554 | 1.9608
VBI-Full | 1.6116 | 1.4734 | 1.8074 | 13.3753 | 2.1034 | 1.1033 | 1.1757 | 1.7194 | 1.2013 | 1.8486 | 1.7323 | 1.6141 | 2.1654 | 1.4239 | 2.4539
63
Speedup
13.3
8.9
Normalized to Native
1.9x

## Slide 64: Use Case 1: Address Translation
Chart: 
| astar | bzip2 | GemsFDTD | mcf | milc | namd | sjeng | bwaves-17 | deepsjeng-17 | lbm-17 | omnetpp-17 | img-dnn | moses | Graph500 | AVG
Virtual | 0.2606 | 0.3532 | 0.3538 | 0.1726 | 0.6883 | 0.9799 | 0.6527 | 0.8699 | 0.74598 | 0.8131 | 0.40677 | 0.66991 | 0.25863 | 0.75242 | 0.56984
Perfect TLB | 1.5738 | 1.4731 | 1.6118 | 8.9041 | 2.1443 | 1.1 | 1.1559 | 1.2328 | 1.146 | 1.2689 | 1.3625 | 1.2982 | 1.9246 | 1.2554 | 1.9608
VBI-Full | 1.6116 | 1.4734 | 1.8074 | 13.3753 | 2.1034 | 1.1033 | 1.1757 | 1.7194 | 1.2013 | 1.8486 | 1.7323 | 1.6141 | 2.1654 | 1.4239 | 2.4539
64
Speedup
Normalized to Native
2.4x
13.3
8.9

## Slide 65: Use Case 1: Address Translation
Chart: 
| astar | bzip2 | GemsFDTD | mcf | milc | namd | sjeng | bwaves-17 | deepsjeng-17 | lbm-17 | omnetpp-17 | img-dnn | moses | Graph500 | AVG
Virtual | 0.2606 | 0.3532 | 0.3538 | 0.1726 | 0.6883 | 0.9799 | 0.6527 | 0.8699 | 0.74598 | 0.8131 | 0.40677 | 0.66991 | 0.25863 | 0.75242 | 0.56984
Perfect TLB | 1.5738 | 1.4731 | 1.6118 | 8.9041 | 2.1443 | 1.1 | 1.1559 | 1.2328 | 1.146 | 1.2689 | 1.3625 | 1.2982 | 1.9246 | 1.2554 | 1.9608
VBI-Full | 1.6116 | 1.4734 | 1.8074 | 13.3753 | 2.1034 | 1.1033 | 1.1757 | 1.7194 | 1.2013 | 1.8486 | 1.7323 | 1.6141 | 2.1654 | 1.4239 | 2.4539
65
Speedup
Normalized to Native
4.3x
13.3
8.9

## Slide 66: Use Case 1: Address Translation
Chart: 
| astar | bzip2 | GemsFDTD | mcf | milc | namd | sjeng | bwaves-17 | deepsjeng-17 | lbm-17 | omnetpp-17 | img-dnn | moses | Graph500 | AVG
Virtual | 0.2606 | 0.3532 | 0.3538 | 0.1726 | 0.6883 | 0.9799 | 0.6527 | 0.8699 | 0.74598 | 0.8131 | 0.40677 | 0.66991 | 0.25863 | 0.75242 | 0.56984
Perfect TLB | 1.5738 | 1.4731 | 1.6118 | 8.9041 | 2.1443 | 1.1 | 1.1559 | 1.2328 | 1.146 | 1.2689 | 1.3625 | 1.2982 | 1.9246 | 1.2554 | 1.9608
VBI-Full | 1.6116 | 1.4734 | 1.8074 | 13.3753 | 2.1034 | 1.1033 | 1.1757 | 1.7194 | 1.2013 | 1.8486 | 1.7323 | 1.6141 | 2.1654 | 1.4239 | 2.4539
66
Speedup
Normalized to Native
13.3
8.9
49%

## Slide 67: Use Case 1: Address Translation
Chart: 
| astar | bzip2 | GemsFDTD | mcf | milc | namd | sjeng | bwaves-17 | deepsjeng-17 | lbm-17 | omnetpp-17 | img-dnn | moses | Graph500 | AVG
Virtual | 0.2606 | 0.3532 | 0.3538 | 0.1726 | 0.6883 | 0.9799 | 0.6527 | 0.8699 | 0.74598 | 0.8131 | 0.40677 | 0.66991 | 0.25863 | 0.75242 | 0.56984
Perfect TLB | 1.5738 | 1.4731 | 1.6118 | 8.9041 | 2.1443 | 1.1 | 1.1559 | 1.2328 | 1.146 | 1.2689 | 1.3625 | 1.2982 | 1.9246 | 1.2554 | 1.9608
VBI-Full | 1.6116 | 1.4734 | 1.8074 | 13.3753 | 2.1034 | 1.1033 | 1.1757 | 1.7194 | 1.2013 | 1.8486 | 1.7323 | 1.6141 | 2.1654 | 1.4239 | 2.4539
67
Speedup
Normalized to Native
13.3
8.9
VBI significantly improves performance
in both native execution and virtual machines
49%

## Slide 68: Use Case 2: Memory Heterogeneity
The benefits of VBI in harnessing the full potential of heterogeneous memory architectures
  Hybrid PCM–DRAM memory architecture
Evaluated systems:
  Two baselines:
    Hotness-Unaware PCM–DRAM: unaware of the data hotness
    IDEAL: always maps frequently-accessed data to DRAM
  One VBI configuration:
    VBI PCM–DRAM: VBI maps and migrates frequently-accessed VBs to the DRAM
68

## Slide 69: Use Case 2: Memory Heterogeneity
More in our paper:
Similar performance improvement for Tiered-Latency-DRAM [Lee+, HPCA’13]
69
Chart: 
| astar | bzip2 | GemsFDTD | hmmer | mcf | milc | soplex | sphinx3 | bwaves-17 | lbm-17 | omnetpp-17 | xalancbmk-17 | img-dnn | moses | Graph500 | AVG
VBI PCM-DRAM | 1.3611 | 1.1938 | 1.6155 | 1.3747 | 1.7064 | 1.4929 | 1.4155 | 1.6518 | 1.3466 | 1.5283 | 1.6886 | 1.2631 | 1.1415 | 1.2104 | 1.378 | 1.3344
IDEAL | 1.3879 | 1.21 | 1.7281 | 1.3797 | 2.087 | 1.547 | 1.5089 | 1.6765 | 1.3925 | 1.733 | 1.8192 | 1.2986 | 1.1628 | 1.2592 | 1.4838 | 1.5116
Normalized to Hotness-Unaware PCM–DRAM
Speedup
33%

## Slide 70: Use Case 2: Memory Heterogeneity
70
Chart: 
| astar | bzip2 | GemsFDTD | hmmer | mcf | milc | soplex | sphinx3 | bwaves-17 | lbm-17 | omnetpp-17 | xalancbmk-17 | img-dnn | moses | Graph500 | AVG
VBI PCM-DRAM | 1.3611 | 1.1938 | 1.6155 | 1.3747 | 1.7064 | 1.4929 | 1.4155 | 1.6518 | 1.3466 | 1.5283 | 1.6886 | 1.2631 | 1.1415 | 1.2104 | 1.378 | 1.3344
IDEAL | 1.3879 | 1.21 | 1.7281 | 1.3797 | 2.087 | 1.547 | 1.5089 | 1.6765 | 1.3925 | 1.733 | 1.8192 | 1.2986 | 1.1628 | 1.2592 | 1.4838 | 1.5116
Normalized to Hotness-Unaware PCM–DRAM
Speedup
33%
VBI enables efficient data mapping and data migration for heterogeneous memory systems

## Slide 71: Outline
Motivation
71
VBI: Virtual Block Interface
Key Idea & Guiding Principles
Design Overview
Optimizations Enabled by VBI
Methodology
Results
Summary

## Slide 72: Summary
Virtual Block Interface (VBI): A new virtual memory framework
  Addresses the challenges in adapting conventional virtual memory to increasingly diverse system configurations and workloads
Key Idea: Delegate physical memory management to dedicated hardware in the memory controller
Benefits: Not easily attainable in conventional virtual memory (e.g., inherently virtual caches , delaying physical memory allocation, and avoiding 2D page walks in virtual machines)
Evaluation:
  VBI significantly improves performance in both native execution and virtual machines
  Increases the effectiveness of managing heterogeneous memory architectures
Conclusion: VBI is a promising new virtual memory framework
  Can enable several important optimizations
  Increases design flexibility for virtual memory
  A new direction for future work in novel virtual memory frameworks
72

## Slide 73: The Virtual Block Interface: A Flexible Alternative to the Conventional Virtual Memory Framework
Nastaran Hajinazar Pratyush Patel Minesh Patel Konstantinos Kanellopoulos Saugata Ghose Rachata Ausavarungnirun Geraldo F. Oliveira Jonathan Appavoo Vivek Seshadri Onur Mutlu