## Slide 1: Variable Read Disturbance (VRD) An Experimental Analysis of Temporal Variation in DRAM Read Disturbance
Ataberk Olgun, F. Nisa Bostancı, İsmail Emir Yüksel Oğuzhan Canpolat, Haocong Luo, Geraldo F. Oliveira A. Giray Yağlıkçı, Minesh Patel, Onur Mutlu
https://arxiv.org/pdf/2502.13075
Notes: Hello everyone. I am Ataberk and I am very happy to present our work: “Variable Read Disturbance: An Experimental Analysis of Temporal Variation in DRAM Read Disturbance”

## Slide 2: A Typical DRAM-Based Computing System
CPU
DRAM Module
DRAM Chip
Notes: This is a typical DRAM-based computing system with a CPU [CLICK] and a DRAM module with multiple DRAM chips.

## Slide 3: DRAM Organization
DRAM Chip
Bank
Chip I/O
DRAM Bank
Subarray
. . .
DRAM Subarray
Row Buffer
Bitline
…
…
Wordline
…
…
…
…
DRAM Cell
DRAM Row
Notes: Each DRAM chip contains multiple banks
Each bank is composed of many subarrays [CLICK]
And within each subarray, there is a two dimensional array of DRAM cells. [CLICK]
These cells are organized into rows that are selected using wordlines [CLICK]
And the cells are connected to a row buffer via bitlines [CLICK]
To access data in a row, you need to activate the row and too many repeated activations can lead to

## Slide 4: Read Disturbance in DRAM (I)
Read disturbance in DRAM breaks memory isolation
Prominent example: RowHammer
Row 1
Row 2
Row 3
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 2
open
Row 2
closed
DRAM Subarray
Victim Row
Victim Row
Aggressor Row
Repeatedly opening (activating) and closing a DRAM row many times causes RowHammer bitflips in adjacent rows
[Kim+, ISCA’14]
Notes: … read disturbance bitflips. Read disturbance bitflips have significant system-level implications because they break memory isolation.
[CLICK] A prominent example of read disturbance is RowHammer.
[CLICKx9] Repeatedly activating and closing a DRAM row many times causes RowHammer bitflips in adjacent rows
We call the repeatedly activated row the aggressor row and the rows that have bitflips victim rows.
That’s RowHammer…

## Slide 5: Read Disturbance in DRAM (II)
Read disturbance in DRAM breaks memory isolation
A new read disturbance phenomenon: RowPress
Row 1
Row 2
Row 3
Row 2
open
Row 1
Row 3
Row 2
closed
Row 2
open
Row 1
Row 3
Row 2
open
Row 2
keep open
Victim Row
Victim Row
Aggressor Row
[Luo+, ISCA’23]
Keeping a DRAM row open for a long time causes bitflips in adjacent rows
DRAM Subarray
Notes: …, but there is also RowPress.
[Click]
RowPress induces bitflips by keeping the aggressor row open for a very long time.

## Slide 6: Read Disturbance Solutions
There are many solutions to mitigate read disturbance bitflips
More robust DRAM chips and/or error-correcting codes
Increased refresh rate
Physical isolation
Row remapping
Preventive refresh
Proactive throttling
Each solution offers a different system design point in reliability, performance, energy, and area tradeoff space
Notes: [CLICKx6 as you talk] Prior works proposed many techniques to mitigate read disturbance bitflips and maintain system robustness and security.
[CLICK] Many different techniques are valuable as each technique comes with a different reliability, performance, energy, and area tradeoff.

## Slide 7: The Read Disturbance Threshold (RDT)
Many secure read disturbance solutions take a preventive action before a bitflip manifests
  E.g., preventively refresh a victim row
Must accurately quantify the amount of disturbance that a row can withstand before experiencing a bitflip
  Typically identified by testing for read disturbance failures
Read Disturbance Threshold (RDT): The number of aggressor row activations needed to induce the first bitflip
Notes: Regardless, a *common* operation pattern across many different solutions is that they take *an action* before a bitflip manifests. For example, refreshing a victim row.
[CLICK] To do so, they *must accurately quantify* the amount of disturbance a row can withstand before it experiences a bitflip. [CLICK] This is typically quantified by time-intensive testing for read disturbance failures.
[CLICK] The read disturbance threshold, or RDT for short, quantifies the amount of disturbance a row can withstand before it experiences a bitflip. This metric is typically expressed in terms of an activation count.

## Slide 8: Accurate Identification of Read Disturbance Threshold is Critical for System Security and Performance
Configured RDT for the Mitigation Technique
Performance and Energy Overhead
RDT overestimated Insecure Low overhead (e.g., 10,000)
RDT underestimated High overhead Secure
(e.g., 20)
Ground truth RDT (e.g., 1,000)
To securely prevent bitflips at low overhead RDT must be accurately identified and carefully configured
Notes: Now I will try to illustrate [CLICK] why it is important to *accurately identify RDT*.
[CLICK] The x-axis shows increasing RDT values in arbitrary units
[CLICK] and the y-axis shows performance and energy overheads in arbitrary units.
[CLICK] This is a curve you’d expect to see: as the RDT becomes smaller, read disturbance solutions induce more performance and energy overheads, for example by more frequently performing time- and energy-intensive preventive refresh operations.
[CLICK] If you have this ground truth RDT value for the row, you want to configure your solution with that exact RDT value, why?
[CLICK] because if you configure it with a higher value you cannot mitigate bitflips and your system is no longer secure
[CLICK] and if you are overly conservative you incur unnecessary performance and energy overheads
[CLICK] In summary, we must accurately identify RDT to securely prevent bitflips at low overhead

## Slide 9: Variable Read Disturbance (VRD) Summary
Research Question
How accurately and efficiently can we measure the read disturbance threshold (RDT) of each DRAM row?
Experimental Characterization
Record >100M RDT measurements across 3750 rows and many test parameters (e.g., temperature, data pattern) in 160 DDR4 and 4 HBM2 chips
Key Observations
RDT changes significantly and unpredictably over time: VRD
Maximum observed RDT is 3.5X higher than minimum (for a row)
Smallest RDT (for a row) may appear after 94,467 measurements
Implications for System Security and Robustness
RDT cannot be accurately identified quickly
Given our limited dataset, guardbands (>10%) and ECC (SECDED or Chipkill) may prevent VRD-induced bitflips at significant performance cost
  More data and analyses needed to make definitive conclusion
Call for future work on understanding and efficiently mitigating VRD
Notes: [CLICK] Our work tries to answer a key question about the read disturbance threshold: “How accurately and efficiently can we measure the read disturbance threshold of each DRAM row?”
[CLICK] We record more than a hundred million read disturbance threshold measurements across many rows in many DRAM chips
[CLICK] We find that the read disturbance threshold of a DRAM row varies significantly and unpredictably over time.
[CLICK] The largest RDT observed for a DRAM row can be 3.5 times the smallest observed for the same row, and
[CLICK] a row’s smallest RDT may appear after 94 thousand measurements We call this new phenomenon Variable Read Disturbance.
[CLICK] Variable read disturbance has implications for system security and robustness because the RDT of a row cannot be quickly and accurately identified.
[CLICK] We evaluate using guardbands for RDT and error-correcting codes as a solution for VRD-induced bitflips: **Given our limited dataset of bitflip locations** we find that relatively large guardbands and ECC could prevent VRD-induced bitflips at significant performance cost.
[CLICK] But more data and analyses are needed to make a definitive conclusion
[CLICK] Our results call for future work on understanding and efficiently mitigating VRD.

## Slide 10: Talk Outline
Motivation
Experimental Characterization Methodology
Foundational Results
In-Depth Analysis of VRD
Implications for System Security and Robustness
Conclusion
Notes: Here is the outline for the rest of the talk

## Slide 11: Talk Outline
Motivation
Experimental Characterization Methodology
Foundational Results
In-Depth Analysis of VRD
Implications for System Security and Robustness
Conclusion
Notes: I will continue by motivating our study

## Slide 12: Motivation
DRAM chips are increasingly more vulnerable to read disturbance with technology scaling
Technology Scaling
Chart: 
| The Min. ACT Count to Observe Bit Flips
2020 | 9.6
2014 | 139.2
[Yaglikci+, HPCA’24]
Notes: Read disturbance bitflips happen in more DRAM cells with fewer activations as DRAM technology scales to smaller sizes to satisfy our memory requirements.
[CLICK] We see more than 10X reduction in the read disturbance threshold between chips manufactured approximately 7 years apart.
[CLICK] Thus, DRAM chips become more vulnerable to read disturbance with technology scaling.

## Slide 13: Motivation
DRAM read disturbance worsens as DRAM chip density increases
Existing solutions become more aggressive
Aggressive preventive actions make existing solutions prohibitively expensive
Notes: Reducing read disturbance thresholds, or, worsening read disturbance [CLICK] causes existing mitigations to become more aggressive, [CLICK] and in turn, induce higher overheads

## Slide 14: Motivation
Configured RDT for the Mitigation Technique
Performance and Energy Overhead
RDT overestimated Insecure Low overhead (e.g., 10,000)
RDT underestimated High overhead Secure
(e.g., 20)
Ground truth RDT (e.g., 1,000)
Prior works assume that the ground truth Read Disturbance Threshold (RDT) can be identified
Notes: Moreover [CLICKx2], prior works assume that the ground truth read disturbance threshold can be identified
In our work, we challenge this assumption…

## Slide 15: Problem
No prior work rigorously studies
temporal variation of
DRAM read disturbance threshold
&
implications for future solutions
Notes: And we see that no prior work studies the temporal variation of DRAM read disturbance
and its implications for future solutions

## Slide 16: Our Goal
Answer two research questions:
Analyze implications for read disturbance solutions
1
Does RDT change over time?
2
How reliably and efficiently can RDT be measured?
Notes: Our goal is twofold:
First we’d like to answer two research questions: [CLICK] Does the read disturbance threshold change over time? [CLICK] If so, how reliably and efficiently can we measure it?
[CLICK] Second, we’d like to analyze implications of temporal variation of read disturbance threshold for read disturbance solutions.

## Slide 17: Talk Outline
Motivation
Experimental Characterization Methodology
Foundational Results
In-Depth Analysis of VRD
Implications for System Security and Robustness
Conclusion
Notes: To achieve our goals, we experimentally characterize DRAM chips

## Slide 18: DDR4 DRAM Testing Infrastructure
  DRAM Bender on a Xilinx Virtex UltraScale+ XCU200
Xilinx Alveo U200 FPGA Board (programmed with DRAM Bender*)
DRAM Module with Heaters
MaxWell FT200 Temperature Controller
PCIe
Host Interface
*Olgun et al., "DRAM Bender: An Extensible and Versatile FPGA-Based Infrastructure to Easily Test State-of-the-Art DRAM Chips,” TCAD, 2023. [GitHub: https://github.com/CMU-SAFARI/DRAM-Bender]
Fine-grained control over DRAM commands,
timing parameters (±1.5ns), and temperature (±0.5°C )
Notes: We use DRAM Bender to test DDR4 DRAM modules [CLICK]
This infrastructure provides us with fine-grained control over DRAM commands, timing parameters, and temperature

## Slide 19: HBM2 DRAM Testing Infrastructure
*Olgun et al., "DRAM Bender: An Extensible and Versatile FPGA-Based Infrastructure to Easily Test State-of-the-Art DRAM Chips,” TCAD, 2023. [GitHub: https://github.com/CMU-SAFARI/DRAM-Bender]
Fine-grained control over DRAM commands,
timing parameters (±1.67ns), and temperature (±0.5°C )
  DRAM Bender on a Bittware XUPVVH
Notes: This is another version of the same infrastructure we use to test HBM2 DRAM chips.

## Slide 20: Tested DRAM Chips
160 DDR4 and 4 HBM2 Chips from SK Hynix, Micron, Samsung
Notes: We test many DRAM chips from three major DRAM manufacturers spanning
[CLICK] various die density and die revisions and chip organizations.

## Slide 21: Testing Methodology
To characterize our DRAM chips at worst-case conditions:
Prevent sources of interference during core test loop
  No DRAM refresh: to avoid refreshing victim row
  No read disturbance mitigation mechanisms: to observe circuit-level effects
  No error correcting codes (ECC): to observe all bitflips
  Test for less than a refresh window (32ms) to avoid retention failures
Worst-case read disturbance access sequence
We use worst-case read disturbance access sequence based on prior works’ observations
Double-sided read disturbance: repeatedly access the two physically-adjacent rows
Record bitflips in victim
Victim Row
Aggressor Row 1
Aggressor Row 2
1 hammer
Open-close
Open-close
Notes: [CLICK x7 as you say below]
We carefully re-use the rigorous read disturbance characterization methodology as done by prior work where we prevent sources of interference and use the worst-case double-sided read disturbance access patterns.
The bottom figure depicts [CLICK] one hammer. Opening and closing the two neighbors of a victim row constitutes one hammer.

## Slide 22: Talk Outline
Motivation
Experimental Characterization Methodology
Foundational Results
In-Depth Analysis of VRD
Implications for System Security and Robustness
Conclusion
Notes: Now, I will describe our major results…

## Slide 23: Foundational Results: Key Takeaway
The Read Disturbance Threshold (RDT) of a row changes randomly and unpredictably over time
Accurately identifying RDT is challenging
Key Takeaway
Notes: … starting with this takeaway message.
We find that the read disturbance threshold of a row changes randomly and unpredictably over time.
This makes accurately identifying RDT very challenging.

## Slide 24: Read Disturbance Threshold Changes Over Time
Chart: 
| 1
Y-Values | 37630
Measurement Number
Read Disturbance Threshold
37360 hammers
Notes: [CLICKx2] We plot the read disturbance threshold values observed
[CLICK] across many read disturbance threshold measurements (or samples, or observations) for one DRAM row
[CLICK] Here is an example point in the plot describing a measurement [CLICK] that yields a read disturbance threshold value of 37K hammers

## Slide 25: Read Disturbance Threshold Changes Over Time
Chart: 
| 1 | 2 | 3 | 4 | 5
Y-Values | 37630 | 38704 | 38346 | 37630 | 38704
Measurement Number
Read Disturbance Threshold
Notes: Here are the RDT values across 5 measurements

## Slide 26: Read Disturbance Threshold Changes Over Time
Chart: 
Measurement Number
Read Disturbance Threshold
Notes: Here is across 1000. To expand the x-axis further and still make sense out of the plot…

## Slide 27: Read Disturbance Threshold Changes Over Time
Chart: 
| 1
Y-Values | 37866.638
Measurement Number
Read Disturbance Threshold
Maximum
Minimum
Average
Notes: We “compress” a series of 1000 measurements into this form: circle shows the average across 1000 measurements and error bars show the range of values

## Slide 28: Read Disturbance Threshold Changes Over Time
Chart: 
Measurement Number
Read Disturbance Threshold
Notes: Now, here is RDT across one hundred thousand measurements for one DRAM row.

## Slide 29: Read Disturbance Threshold Changes Over Time
Chart: 
Measurement Number
Read Disturbance Threshold
Minimum RDT at 16926th measurement
Notes: We observe that for this series of RDT measurements, the minimum RDT appears at around 17 thousand measurements.

## Slide 30: Read Disturbance Threshold Changes Over Time
Chart: 
Read Disturbance Threshold
Read Disturbance Threshold of a DRAM row varies over time: Variable Read Disturbance (VRD)
Notes: This is a key result that demonstrates the variable read disturbance phenomenon

## Slide 31: The RDT of a Row Has Multiple States
Read Disturbance Threshold
# of Measurements
The RDT of a row takes various different values across 100,000 measurements
Notes: We also investigate the distribution of observed RDT values: [CLICK] Here we show a [CLICK] histogram of the RDT values where a bar’s height indicates the number of measurements that yield the RDT value shown on the x-axis.
[CLICK] We observe that [CLICK] the read disturbance threshold of a row takes various different values across one hundred thousand measurements

## Slide 32: Variable Read Disturbance Across DRAM Chips
Read Disturbance Threshold
# of Measurements
RDT consistently varies over time across all tested DRAM chips
Notes: Here we show data for one tested row each from 6 tested chips [CLICK].
This observation is consistent across all tested chips…

## Slide 33: Variable Read Disturbance Across DRAM Chips
RDT
# of Measurements
RDT consistently varies over time across all tested DRAM chips
https://arxiv.org/pdf/2502.13075
Notes: … and I refer you to our paper for results for other chips that we couldn’t fit in that previous slide

## Slide 34: VRD is (Likely) Unpredictable
The outcome of the next read disturbance threshold (RDT) measurement cannot be predicted given past measurements
1
RDT histograms well resemble* random probability distributions e.g., normal distribution
* Resemblance quantified using statistical tests in the paper
2
Analyze and find no repeating patterns in the series of consecutively measured RDT values using the autocorrelation function
Notes: We analyze the predictability of the next RDT value given past RDT measurements and we find that it is likely unpredictable.
[CLICK] First, we find that the RDT histograms well resemble prominent random probability distributions
[CLICK] Second, we use the autocorrelation function to try and identify repeating patterns in a series of 100000 measurements and we cannot identify any repeating patterns

## Slide 35: VRD is (Likely) Unpredictable
The outcome of the next RDT measurement cannot be predicted given past measurements
1
RDT histograms well resemble* random probability distributions e.g., normal distribution
2
Analyze and find no repeating patterns using the autocorrelation function
https://arxiv.org/pdf/2502.13075
Notes: For more details on our methodology, please check the paper

## Slide 36: Talk Outline
Motivation
Experimental Characterization Methodology
Foundational Results
In-Depth Analysis of VRD
Implications for System Security and Robustness
Conclusion
Notes: Now we take an in-depth look at VRD in many DRAM rows by sweeping various test parameters

## Slide 37: In-Depth Analysis: Parameter Space
Four data patterns
Three temperature levels: 50°C, 65°C, 80°C
Three aggressor row on time values (RowPress):
  Minimum tRAS = ~35ns
  Interval between two periodic refresh commands tREFI = 7.8µs (DDR4)
  Maximum interval between two refresh 9 ⨉ tREFI = 70.2µs (DDR4)
Test 3750 rows and measure RDT 1000 times per row
  Aside: what would happen if we measure >1M times?
Notes: We use four data patterns
[CLICK] Three temperature levels
[CLICK] Three aggressor row on time values (to investigate RowPress and VRD)
[CLICK] and we test many rows in total across all chips and measure RDT 1000 times for each tested row
[CLICK] We test 1000 times for time constraints. It is good to think about what you’d see if you did 1 million or 10 million or more measurements.

## Slide 38: In-Depth Analysis: Key Takeaways
All tested DRAM rows exhibit VRD
Takeaway 1
Relatively few (<500) RDT measurements are unlikely to yield the minimum RDT of a row
Takeaway 2
Data patterns, temperature, and aggressor row on time affect VRD
Takeaway 3
Notes: Here are the three key takeaways from our in-depth study

## Slide 39: In-Depth Analysis: Key Takeaways
All tested DRAM rows exhibit VRD
Takeaway 1
Relatively few (<500) RDT measurements are unlikely to yield the minimum RDT of a row
Takeaway 2
Data patterns, temperature, and aggressor row on time affect VRD
Takeaway 3
Notes: First, all tested DRAM rows exhibit variable read disturbance, to *varying* degrees

## Slide 40: VRD Across DRAM Rows
DRAM Rows Sorted by Increasing Coefficient of Variation of RDT
Across 1000 RDT Measurements
Coefficient of Variation
A row with small variance in RDT distribution across 1000 measurements
Notes: Here we show the coefficient of variation in the distribution of 1000 read disturbance threshold measurements for each tested row.
[CLICK] The circled tiny pink dot stands for the DRAM row with the smallest coefficient of variation in its RDT distribution. Another way to look at this is that this row’s RDT values are very close to each other.
[CLICK] We show the rows sorted in increasing coefficient of variation on the x-axis

## Slide 41: VRD Across DRAM Rows
DRAM Rows Sorted by Increasing Coefficient of Variation of RDT
Across 1000 RDT Measurements
Coefficient of Variation
Median row
Row with the greatest variance in RDT distribution
All tested rows exhibit VRD
Notes: We observe that all tested rows exhibit VRD: no row has 0 variation in its RDT measurements
[CLICKx2] We highlight two points in this plot: the median row, and the row with the greatest variance in its read disturbance threshold distribution

## Slide 42: VRD in Two Example Rows
1.2⨉
3.5⨉
Variation in read disturbance threshold can reach 3.5⨉
Notes: Here is a look at those two rows. We see their RDT values across 1000 successive measurements on the x-axis
[CLICK] For the median row, we see that the maximum observed RDT is 1.2 times higher than the minimum
[CLICK] and we observe that the variation in RDT can reach a high factor: it is 3.5 times for the row with the greatest RDT variation

## Slide 43: In-Depth Analysis: Key Takeaways
All tested DRAM rows exhibit VRD
Takeaway 1
Relatively few (<500) RDT measurements are unlikely to yield the minimum RDT of a row
Takeaway 2
Data patterns, temperature, and aggressor row on time affect VRD
Takeaway 3
Notes: Now moving onto the second takeaway: Relatively few measurements are unlikely to yield the minimum read disturbance threshold of a row

## Slide 44: Probability of Identifying the Minimum RDT
How likely is it that N < 1000 measurements yield the minimum RDT value across 1000 measurements?
N = 1, 3, 5, 10, 50, and 500
Monte Carlo simulations for 10K iterations
Notes: We try to answer this question: how likely is it for us to find the minimum observed RDT across 1000 measurements, using
[CLICK] only N measurements where N is smaller than 1000? [CLICK]
We use monte carlo simulations and [CLICK] plot the probability of identifying the minimum RDT value over varying N [CLICK] for all tested rows

## Slide 45: Probability of Identifying the Minimum RDT
Very unlikely to find the minimum RDT of a DRAM row with N = 1 measurement
only 0.2% for the median row
Notes: [CLICK] N = 1 measurement has a very low probability of yielding the minimum RDT across 1000 measurements, only 0.2%... and

## Slide 46: Probability of Identifying the Minimum RDT
Probability of finding the minimum read disturbance threshold increases with N (i.e., with more and more testing)
0.2%
0.7%
1.1%
2.1%
10.0%
75.3%
Probability values for the median row
Notes: (SLOWLY) we observe that the probability increases with N
goes up to 75% for the median row - but does not reach 100% -, for N = 500 measurements
====
TODO: spend more time here

## Slide 47: Expected Value of the Minimum RDT
With only N < 1000 RDT measurements how far are we from the minimum RDT across 1000 measurements
Chart: 
Measurement Number
Read Disturbance Threshold
Minimum across 1000 measurements
Notes: To gain more insight into VRD, we devise another metric called the expected value of the minimum RDT to quantify how higher of an RDT value we expect to find with N smaller than 1000 measurements.
[CLICK] I’ll describe this pictorially. [CLICK] This line depicts the minimum RDT value across 1000 measurements

## Slide 48: Expected Value of the Minimum RDT
With only N < 1000 RDT measurements how far are we from the minimum RDT across 1000 measurements
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24 | 25 | 26 | 27 | 28 | 29 | 30 | 31 | 32 | 33 | 34 | 35 | 36 | 37 | 38 | 39 | 40 | 41 | 42 | 43 | 44 | 45 | 46 | 47 | 48 | 49 | 50 | 51 | 52 | 53 | 54 | 55 | 56 | 57 | 58 | 59 | 60 | 61 | 62 | 63 | 64 | 65 | 66 | 67 | 68 | 69 | 70 | 71 | 72 | 73 | 74 | 75 | 76 | 77 | 78 | 79 | 80 | 81 | 82 | 83 | 84 | 85 | 86 | 87 | 88 | 89 | 90 | 91 | 92 | 93 | 94 | 95 | 96 | 97 | 98 | 99 | 100 | 101 | 102 | 103 | 104 | 105 | 106 | 107 | 108 | 109 | 110 | 111 | 112 | 113 | 114 | 115 | 116 | 117 | 118 | 119 | 120 | 121 | 122 | 123 | 124 | 125 | 126 | 127 | 128 | 129 | 130 | 131 | 132 | 133 | 134 | 135 | 136 | 137 | 138 | 139 | 140 | 141 | 142 | 143 | 144 | 145 | 146 | 147 | 148 | 149 | 150 | 151 | 152 | 153 | 154 | 155 | 156 | 157 | 158 | 159 | 160 | 161 | 162 | 163 | 164 | 165 | 166 | 167 | 168 | 169 | 170 | 171 | 172 | 173 | 174 | 175 | 176 | 177 | 178 | 179 | 180 | 181 | 182 | 183 | 184 | 185 | 186 | 187 | 188 | 189 | 190 | 191 | 192 | 193 | 194 | 195 | 196 | 197 | 198 | 199 | 200 | 201 | 202 | 203 | 204 | 205 | 206 | 207 | 208 | 209 | 210 | 211 | 212 | 213 | 214 | 215 | 216 | 217 | 218 | 219 | 220 | 221 | 222 | 223 | 224 | 225 | 226 | 227 | 228 | 229 | 230 | 231 | 232 | 233 | 234 | 235 | 236 | 237 | 238 | 239 | 240 | 241 | 242 | 243 | 244 | 245 | 246 | 247 | 248 | 249 | 250 | 251 | 252 | 253 | 254 | 255 | 256 | 257 | 258 | 259 | 260 | 261 | 262 | 263 | 264 | 265 | 266 | 267 | 268 | 269 | 270 | 271 | 272 | 273 | 274 | 275 | 276 | 277 | 278 | 279 | 280 | 281 | 282 | 283 | 284 | 285 | 286 | 287 | 288 | 289 | 290 | 291 | 292 | 293 | 294 | 295 | 296 | 297 | 298 | 299 | 300 | 301 | 302 | 303 | 304 | 305 | 306 | 307 | 308 | 309 | 310 | 311 | 312 | 313 | 314 | 315 | 316 | 317 | 318 | 319 | 320 | 321 | 322 | 323 | 324 | 325 | 326 | 327 | 328 | 329 | 330 | 331 | 332 | 333 | 334 | 335 | 336 | 337 | 338 | 339 | 340 | 341 | 342 | 343 | 344 | 345 | 346 | 347 | 348 | 349 | 350 | 351 | 352 | 353 | 354 | 355 | 356 | 357 | 358 | 359 | 360 | 361 | 362 | 363 | 364 | 365 | 366 | 367 | 368 | 369 | 370 | 371 | 372 | 373 | 374 | 375 | 376 | 377 | 378 | 379 | 380 | 381 | 382 | 383 | 384 | 385 | 386 | 387 | 388 | 389 | 390 | 391 | 392 | 393 | 394 | 395 | 396 | 397 | 398 | 399 | 400 | 401 | 402 | 403 | 404 | 405 | 406 | 407 | 408 | 409 | 410 | 411 | 412 | 413 | 414 | 415 | 416 | 417 | 418 | 419 | 420 | 421 | 422 | 423 | 424 | 425 | 426 | 427 | 428 | 429 | 430 | 431 | 432 | 433 | 434 | 435 | 436 | 437 | 438 | 439 | 440 | 441 | 442 | 443 | 444 | 445 | 446 | 447 | 448 | 449 | 450 | 451 | 452 | 453 | 454 | 455 | 456 | 457 | 458 | 459 | 460 | 461 | 462 | 463 | 464 | 465 | 466 | 467 | 468 | 469 | 470 | 471 | 472 | 473 | 474 | 475 | 476 | 477 | 478 | 479 | 480 | 481 | 482 | 483 | 484 | 485 | 486 | 487 | 488 | 489 | 490 | 491 | 492 | 493 | 494 | 495 | 496 | 497 | 498 | 499 | 500 | 501 | 502 | 503 | 504 | 505 | 506 | 507 | 508 | 509 | 510 | 511 | 512 | 513 | 514 | 515 | 516 | 517 | 518 | 519 | 520 | 521 | 522 | 523 | 524 | 525 | 526 | 527 | 528 | 529 | 530 | 531 | 532 | 533 | 534 | 535 | 536 | 537 | 538 | 539 | 540 | 541 | 542 | 543 | 544 | 545 | 546 | 547 | 548 | 549 | 550 | 551 | 552 | 553 | 554 | 555 | 556 | 557 | 558 | 559 | 560 | 561 | 562 | 563 | 564 | 565 | 566 | 567 | 568 | 569 | 570 | 571 | 572 | 573 | 574 | 575 | 576 | 577 | 578 | 579 | 580 | 581 | 582 | 583 | 584 | 585 | 586 | 587 | 588 | 589 | 590 | 591 | 592 | 593 | 594 | 595 | 596 | 597 | 598 | 599 | 600 | 601 | 602 | 603 | 604 | 605 | 606 | 607 | 608 | 609 | 610 | 611 | 612 | 613 | 614 | 615 | 616 | 617 | 618 | 619 | 620 | 621 | 622 | 623 | 624 | 625 | 626 | 627 | 628 | 629 | 630 | 631 | 632 | 633 | 634 | 635 | 636 | 637 | 638 | 639 | 640 | 641 | 642 | 643 | 644 | 645 | 646 | 647 | 648 | 649 | 650 | 651 | 652 | 653 | 654 | 655 | 656 | 657 | 658 | 659 | 660 | 661 | 662 | 663 | 664 | 665 | 666 | 667 | 668 | 669 | 670 | 671 | 672 | 673 | 674 | 675 | 676 | 677 | 678 | 679 | 680 | 681 | 682 | 683 | 684 | 685 | 686 | 687 | 688 | 689 | 690 | 691 | 692 | 693 | 694 | 695 | 696 | 697 | 698 | 699 | 700 | 701 | 702 | 703 | 704 | 705 | 706 | 707 | 708 | 709 | 710 | 711 | 712 | 713 | 714 | 715 | 716 | 717 | 718 | 719 | 720 | 721 | 722 | 723 | 724 | 725 | 726 | 727 | 728 | 729 | 730 | 731 | 732 | 733 | 734 | 735 | 736 | 737 | 738 | 739 | 740 | 741 | 742 | 743 | 744 | 745 | 746 | 747 | 748 | 749 | 750 | 751 | 752 | 753 | 754 | 755 | 756 | 757 | 758 | 759 | 760 | 761 | 762 | 763 | 764 | 765 | 766 | 767 | 768 | 769 | 770 | 771 | 772 | 773 | 774 | 775 | 776 | 777 | 778 | 779 | 780 | 781 | 782 | 783 | 784 | 785 | 786 | 787 | 788 | 789 | 790 | 791 | 792 | 793 | 794 | 795 | 796 | 797 | 798 | 799 | 800 | 801 | 802 | 803 | 804 | 805 | 806 | 807 | 808 | 809 | 810 | 811 | 812 | 813 | 814 | 815 | 816 | 817 | 818 | 819 | 820 | 821 | 822 | 823 | 824 | 825 | 826 | 827 | 828 | 829 | 830 | 831 | 832 | 833 | 834 | 835 | 836 | 837 | 838 | 839 | 840 | 841 | 842 | 843 | 844 | 845 | 846 | 847 | 848 | 849 | 850 | 851 | 852 | 853 | 854 | 855 | 856 | 857 | 858 | 859 | 860 | 861 | 862 | 863 | 864 | 865 | 866 | 867 | 868 | 869 | 870 | 871 | 872 | 873 | 874 | 875 | 876 | 877 | 878 | 879 | 880 | 881 | 882 | 883 | 884 | 885 | 886 | 887 | 888 | 889 | 890 | 891 | 892 | 893 | 894 | 895 | 896 | 897 | 898 | 899 | 900 | 901 | 902 | 903 | 904 | 905 | 906 | 907 | 908 | 909 | 910 | 911 | 912 | 913 | 914 | 915 | 916 | 917 | 918 | 919 | 920 | 921 | 922 | 923 | 924 | 925 | 926 | 927 | 928 | 929 | 930 | 931 | 932 | 933 | 934 | 935 | 936 | 937 | 938 | 939 | 940 | 941 | 942 | 943 | 944 | 945 | 946 | 947 | 948 | 949 | 950 | 951 | 952 | 953 | 954 | 955 | 956 | 957 | 958 | 959 | 960 | 961 | 962 | 963 | 964 | 965 | 966 | 967 | 968 | 969 | 970 | 971 | 972 | 973 | 974 | 975 | 976 | 977 | 978 | 979 | 980 | 981 | 982 | 983 | 984 | 985 | 986 | 987 | 988 | 989 | 990 | 991 | 992 | 993 | 994 | 995 | 996 | 997 | 998 | 999 | 1000
Y-Values | 38346 | 37272 | 37988 | 36198 | 37272
Measurement Number
Read Disturbance Threshold
Minimum across 1000 measurements
5 random samples
Minimum across 5 samples
Expected value of the minimum RDT
Notes: Here are 5 random samples from the set of 1000 measurements
[CLICK] and the minimum across those 5 samples
[CLICK] this metric quantifies the distance between the two minimums

## Slide 49: Expected Value of the Minimum RDT
Expected Normalized Value of the Minimum RDT
Notes: We plot the new metric on the [CLICK] y-axis and the probability of finding the minimum RDT on x-axis.

## Slide 50: Expected Value of the Minimum RDT
Expected Normalized Value of the Minimum RDT
RDT found by 1 measurement 3.21⨉ greater than minimum RDT across 1000 measurements
Notes: Each point on this plot stands for one row [CLICK]. [CLICK] This point shows you that there is a row where we expect to find an RDT value using one measurement 3.21 times greater than the one we would find if we were to test for 1000 times

## Slide 51: Expected Value of the Minimum RDT
Expected Normalized Value of the Minimum RDT
“Better” for testing
Plot interpretation
“Better” for testing == as tight an RDT distribution as possible
tight RDT distribution
Notes: A good way to interpret this plot is that we want to have small y-axis values. Small y-axis values indicate *tighter* RDT distributions and you want RDT distributions as tight as possible.

## Slide 52: Expected Value of the Minimum RDT
Expected Normalized Value of the Minimum RDT
The minimum RDT is significantly smaller than the one expected to be found with N = 1 measurement
RDT expected to be found by 1 measurement is 1.9⨉ greater than minimum RDT across 1000 measurements
Notes: This is the full plot.
[CLICK] Now we highlight the rows with smaller than 0.1% probability of finding the minimum RDT: for these rows the minimum RDT appears only once in the series of 1000 measurements
[CLICK] They can have up to 1.9 times expected normalized value of the minimum RDT
[CLICK] We conclude that the minimum RDT across 1000 measurements is significantly smaller than the one expected to be found by N = 1 measurement

## Slide 53: Expected Value of the Minimum RDT
Expected Normalized Value of the Minimum RDT
With increasing N (number of measurements) we expect to identify an RDT value closer to the minimum across 1000 measurements
Notes: With increasing N, we expect to identify an RDT value closer to the minimum value across 1000 measurements

## Slide 54: In-Depth Analysis: Key Takeaways
All tested DRAM rows exhibit VRD
Takeaway 1
Relatively few (<500) RDT measurements are unlikely to yield the minimum RDT of a row
Takeaway 2
Data patterns, temperature, and aggressor row on time affect VRD
Takeaway 3
Notes: Finally, data patterns, temperature, and aggressor row on time all affect VRD and you can find the detailed analyses in the paper, but I am not going to cover these details in the presentation.

## Slide 55: Talk Outline
Motivation
Experimental Characterization Methodology
Foundational Results
In-Depth Analysis of VRD
Implications for System Security and Robustness
Conclusion
Notes: The observations I presented have implications for system security and robustness

## Slide 56: Implications Summary
Security guarantees provided by mitigation techniques rely on accurately identified minimum read disturbance threshold (RDT)
Accurate identification of minimum RDT (for each row) is extremely challenging (even with 1000s measurements) because RDT unpredictably changes over time
We analyze the use of a guardband and ECC
  May prevent VRD-induced bitflips
  Large guardbands induce performance overhead
Call for future work on online RDT profiling and runtime configurable read disturbance mitigations
Notes: Security guarantees provided by read disturbance mitigation techniques or solutions rely on an accurately identified RDT
[CLICK] Our results show that accurate identification of RDT is extremely challenging
[CLICK] We evaluate a short-term solution: combining a guardband for RDT and error-correcting codes. [CLICK] Given our limited empirical bitflip dataset, we show that this combined solution could prevent VRD-induced bitflips at performance cost.
[CLICK] Our results call for future work on online read disturbance profiling and runtime configurable read disturbance mitigations

## Slide 57: Important Caveat
VRD solution analysis based on 1K or 10K read disturbance threshold measurements per row
More measurements could yield worse results
  Read disturbance threshold distribution tail could expand
What results would millions or billions of RDT measurements yield?
Notes: I’d like to stress an important caveat. The results I presented in the last slide and that I am going to present next are based on only a limited number of read disturbance threshold measurements.
[CLICK] More RDT measurements could yield worse results
[CLICK] and it is good to think about what millions of or billions of or more RDT measurements would yield.

## Slide 58: Challenges of Accurately Identifying RDT
Variation in read disturbance threshold across 1000 measurements can reach 3.5⨉ and may not be bounded
3.5⨉
RDT
Measurement Number
VRD is affected by data pattern, temperature, aggressor row on time
Comprehensive RDT profiling is time-intensive
Measuring RDT of each row only once with 8000 hammers using four data patterns, at three temperature levels takes 39 minutes in a bank of 256K rows
Notes: That, was a summary. I will do a deep dive by explaining why it’s challenging to accurately identify the minimum RDT
[CLICK] The variation in RDT can reach 3.5X and it may not be bounded.
[CLICK] RDT distribution is affected by many parameters and comprehensive RDT testing is time intensive
[CLICK] Measuring the RDT of each row in a bank of 256K rows *only once* can take 39 minutes

## Slide 59: RDT Profiling is Time-Intensive
Comprehensive RDT testing can take tens of hours (only 1000 measurements, one data pattern, one temperature level, one aggressor row on time)
Notes: In fact, we show that comprehensive read disturbance threshold testing for a DRAM chip can take tens of hours to complete if you want to measure RDT multiple times

## Slide 60: RDT Profiling is Time-Intensive
Comprehensive RDT testing can take hours (1000 measurements, one data pattern, one temperature level, one aggressor row on time)
https://arxiv.org/pdf/2502.13075
Notes: I refer you to our paper for more details on that

## Slide 61: Making Do With Few RDT Measurements
A system designer might measure RDT a few times and apply a safety margin (guardband) to the minimum observed value
Notes: Because it is so time consuming to comprehensively test for read disturbance bitflips, a system designer might measure RDT a few times, take the minimum across those few measurements, and apply a guardband to it with the hope of covering a not yet observed minimum RDT value
[CLICK] This plot shows you the probability that N measurements displayed on the x-axis + the guardband shown above will cover the minimum RDT value across 1,000 measurements.

## Slide 62: Making Do With Few RDT Measurements
A system designer might measure RDT a few times and apply a safety margin (guardband) to the minimum observed value
Average across all tested rows
Minimum across all tested rows
Notes: We show both the average value across all tested rows using circles and the minimum across all tested rows using bars.
What that pink bar means is there is a row where you *don’t* expect to find the minimum read disturbance threshold across 1K measurements with 100% probability, even with 500 measurements.
[CLICK] Here is the full plot.

## Slide 63: Making Do With Few RDT Measurements
A large guardband does not guarantee that the minimum RDT is always identified
Using guardbands alone is likely not effective
Notes: We observe that a large guardband does not guarantee that the minimum RDT is always identified and conclude that guardbands alone are likely not effective.

## Slide 64: RDT Guardband Increases Performance Overheads
50% RDT safety margin can induce 45% additional overhead (over no margin)
Relying solely on guardbands not recommended
45%
35%
Notes: Moreover, large guardbands can [CLICK] introduce significant performance overhead.
[CLICK] Thereby we do not recommend relying solely on guardbands.

## Slide 65: Combining ECC and Guardbands (I)
Single-error correcting double-error detecting (SECDED) or Chipkill ECC combined with guardbands could mitigate VRD-induced bitflips
Unique bitflips when 10% RDT guardband applied
10% guardband combined w/ ECC is likely unsafe
Notes: We evaluate error-correcting codes as a complementary technique to using a guardband for RDT
[CLICK] The plot shows you a histogram of the number of unique bitflips in a row when we use a 10% RDT guardband.
[CLICK] The bitflip rate we observe suggests that widely-used ECC schemes combined with 10% guardband for RDT is likely unsafe, depending on how the bitflips are located.

## Slide 66: Combining ECC and Guardbands (II)
RDT guardbands ≥20% yield 1 unique bitflip in a row
Given our limited measurement dataset (10K measurements) RDT guardbands ≥20% combined with ECC may prevent VRD-induced read disturbance bitflips
More detailed analysis (following a large-scale study) needed to make a definitive conclusion
Notes: However, guardbands greater than or equal to 20% yield only 1 unique bitflip in a row
[CLICK] The bitflip patterns *we* observe could be prevented with larger than or equal to 20% guardband combined with widely-used ECC schemes.
[CLICK] But more detailed analysis likely following a large-scale study is needed to make a definitive conclusion about the effectiveness of guardbands and ECC.

## Slide 67: More in the Paper
Hypothetical explanation for VRD
Effect of True- and Anti-Cell Layout
  Presence of true- and anti-cells in the victim row does not significantly affect the RDT distribution
Read disturbance mitigation evaluation methodology
Probability of errors at the worst observed bitflip rate for 10% RDT guardband
  SEC, SECDED, and Chipkill-like (SSC)
Read disturbance testing time and energy consumption
Detailed information on tested modules and chips
Notes: There are many more things in the paper that I cannot talk about now
In the interest of time, I’ll refer you to…

## Slide 68: More in the Paper
Hypothetical explanation for VRD
Effect of True- and Anti-Cell Layout
  Presence of true- and anti-cells in the victim row does not significantly affect the RDT distribution
Read disturbance mitigation evaluation methodology
Probability of errors at the worst observed bitflip rate for 10% safety margin
  SEC, SECDED, and Chipkill-like (SSC)
Read disturbance testing time and energy consumption
Detailed information on tested modules and chips
https://arxiv.org/pdf/2502.13075
Notes: … our paper for those details

## Slide 69: Talk Outline
Motivation
Experimental Characterization Methodology
Foundational Results
In-Depth Analysis of VRD
Implications for System Security and Robustness
Conclusion
Notes: I’ll quickly conclude my talk

## Slide 70: VRD Conclusion
Minimum RDT (of a row) may appear after many measurements
Variable Read Disturbance (VRD)
The read disturbance threshold changes unpredictably over time
RDT for a DRAM row can vary by 3.5X
Given our limited read disturbance bitflip dataset, guardbands combined with error-correcting codes may be a solution for VRD-induced bitflips. More data and analyses needed to make definitive conclusion
Future work could alleviate the shortcomings of existing mitigations & develop better understanding of inner workings of VRD
Identifying the minimum RDT is challenging and time-intensive
Notes: We demonstrate Variable Read Disturbance, showing that the read disturbance threshold of a row changes unpredictably over time.
[CLICK] We show VRD’s interesting characteristics through detailed experimental characterization.
[CLICK] VRD has implications for system robustness and security. Thus, we evaluate short-term solutions for VRD induced bitflips. *Given our limited bitflip dataset*, relatively large guardbands and ECC may prevent VRD-induced failures. However, more data and analyses are necessary to make a definitive conclusion
[CLICK] We call for future work on efficient solutions for VRD and future work that will develop our understanding of inner workings of VRD.

## Slide 71: Extended Version on arXiv
https://arxiv.org/pdf/2502.13075
Notes: An extended version of our conference paper is on arXiv.

## Slide 72: Variable Read Disturbance (VRD) An Experimental Analysis of Temporal Variation in DRAM Read Disturbance
Ataberk Olgun, F. Nisa Bostancı, İsmail Emir Yüksel Oğuzhan Canpolat, Haocong Luo, Geraldo F. Oliveira A. Giray Yağlıkçı, Minesh Patel, Onur Mutlu
https://arxiv.org/pdf/2502.13075
Notes: And that’s all. I am happy to take your questions.

## Slide 73: Variable Read Disturbance Backup Slides

## Slide 74: Is this Experiment Noise?
Short answer: no
Hypothetical explanation for VRD: Randomly changing charge trap state in the active region
Long answer: We cannot identify any independent variables within our control that allow reliably predicting the minimum RDT despite extensive testing
Device-level studies should confirm our hypotheses

## Slide 75: Hypothetical Explanation for VRD
No device-level study shows temporal variations in read disturbance vulnerability
Electron migration and injection into victim cell is a major read disturbance failure mechanism
This mechanism is assisted by charge traps in the shared active region of the victim and aggr. cell
Temporal variation attributed to randomly changing occupied/unoccupied states of charge traps

## Slide 76: RDT Distribution Across Chips

## Slide 77: # of Consecutive Measurements That Yield the Same RDT Value

## Slide 78: Autocorrelation Function Tests

## Slide 79: Expected Value of the Minimum RDT
Expected Normalized Value of the Minimum RDT

## Slide 80: Expected Value of the Minimum RDT
Expected Normalized Value of the Minimum RDT
Min. RDT found by 1 measurement 3.21⨉ greater than min. RDT found by 1000 measurements

## Slide 81: Expected Value of the Minimum RDT
Expected Normalized Value of the Minimum RDT

## Slide 82: Effect of Die Density and Die Revision (I)
Expected Normalized Value of the Minimum RDT
Number of Measurements (N)
RDT distribution worsens with increasing die density and with advanced DRAM technology
Notes: We plot the expected normalized value of the minimum RDT [CLICK] for three die revision and die density combinations
[CLICK] We observe that the RDT distribution worsens: that is, we expect to find a larger RDT with N < 1000 measurements, with increasing die density

## Slide 83: Effect of Die Density and Die Revision (II)
The effect of die density and die revision is consistent across all tested modules
Notes: [CLICK] We consistently make this observation across all tested modules

## Slide 84: Effect of Data Pattern (I)
Expected Normalized Value of the Minimum RDT
Number of Measurements (N)
Notes: Here we show the expected normalized value of the minimum RDT for four tested data patterns

## Slide 85: Effect of Data Pattern (I)
Expected Normalized Value of the Minimum RDT
Number of Measurements (N)
RDT distribution changes with data pattern
1.04⨉
1.06⨉
expected normalized value for the median row
Notes: We observe that the RDT distribution [CLICK] changes with the data pattern. Here we show the y-axis values for the median rows to quantify the change.

## Slide 86: Effect of Data Pattern (II)
Expected Normalized Value of the Minimum RDT
Number of Measurements (N)
No single data pattern causes the worst RDT distribution across all tested DRAM chips
Notes: We look at the effect of data pattern across all tested modules. We observe that [CLICK] no single data pattern causes the worst RDT distribution across all tested DRAM chips

## Slide 87: Effect of Aggressor Row On Time
Expected Normalized Value of the Minimum RDT
RDT distribution changes with aggressor row on time
RDT distribution can become better or worse with increasing row on time
Notes: This shows the effect of aggressor row on time.
[CLICK] We see that the RDT distribution changes with aggressor row on time
[CLICK] It can become better or worse with increasing row on time

## Slide 88: Effect of Temperature
Expected Normalized Value of the Minimum RDT
RDT distribution tends to change with temperature
Number of Measurements (N) = 1
Notes: We look at the effect of temperature
[CLICK] and we see that the RDT distribution tends to change with temperature

## Slide 89: Effect of True- and Anti-Cell Layout
The presence of true- and anti-cells in the victim row does not significantly affect the RDT distribution

## Slide 90: Error Probability Analysis

## Slide 91: DRAM Operation: Activate and Precharge
Row 1
Row 2
Row 3
Row Buffer
Row 1
Access data in Row 1
Row 1 is closed
DRAM Subarray
Notes: To access a cell we use activate and precharge operations.
[CLICK] If we want to access data in Row 1, [CLICK] we must first activate Row 1, or open it

## Slide 92: DRAM Operation: Activate and Precharge
Row 1
Row 2
Row 3
Row Buffer
Activate command
Row 1
Access data in Row 1
Row 1 is open
Row 1 is closed
DRAM Subarray
Notes: We do that [CLICK] using an ACTIVATE [CLICK] command.

## Slide 93: DRAM Operation: Activate and Precharge
Row 1
Row 2
Row 3
Row Buffer
Row 1
Precharge command
Access data in Row 3
Row 3 is closed
DRAM Subarray
Notes: If, in this opened state, we [CLICK] want to access data in Row 3, [CLICK] we close the open row [CLICK] using the PREcharge command.

## Slide 94: DRAM Operation: Activate and Precharge
Row 1
Row 2
Row 3
Row Buffer
Activate command
Access data in Row 3
Row 3
Row 3 is open
Row 3 is closed
DRAM Subarray
Notes: [CLICK] Now we can activate Row 3 and access data in Row 3.
Repeatedly performing activate and precharge operations can lead to…

## Slide 95: DRAM Cell Leakage
Each cell encodes information in leaky capacitors
wordline
capacitor
access
transistor
bitline
Stored data is corrupted if too much charge leaks (i.e., the capacitor voltage degrades too much)
charge
leakage
paths
[Patel+, ISCA’17]
Notes: Each cell encodes data in fundamentally leaky capacitors [CLICK] Here is a simplified diagram of a DRAM cell, where the capacitor in red stores the data and the access transistor gates access to the data
[CLICK]
There are a number of leakage paths by which charge can enter or exit the capacitor.
[CLICK]
The important thing to note is that stored data can be corrupted if too much charge leaks
Which is the same as saying if the capacitor voltage degrades too much
[END]

## Slide 96: DRAM Refresh
Periodic refresh operations preserve stored data
Capacitor voltage (Vdd)
100%
0%
Vmin
Refresh Window
Refresh Operations
time
REF
REF
REF
[Kim+, ISCA’20]
Notes: Here, we have a simplified diagram of the capacitor voltage over time
We see that the voltage decreases over time in an exponential decay.
There’s a threshold Vmin under which we can no longer guarantee that we will correctly read the data that was originally stored in the cell.
[CLICK]
As long as a cell’s voltage remains above this line, we consider this a retention success.
[CLICK]
However, as soon as the voltage drops below Vmin, we consider this a retention failure
In order to prevent charge leakage failures, also known as retention failures, [CLICK] we issue periodic refresh operations to restore the charge in the cell. [CLICK] The interval between refresh commands are referred to as the refresh window.

## Slide 97: Read Disturbance Bitflips
Capacitor voltage (Vdd)
100%
0%
Vmin
time
REF
REF
REF
Accesses to nearby row
Read Disturbance
Bitflip
[Kim+, ISCA’20]
Notes: Now lets take a look at this diagram in the context of a read disturbance access pattern.
[CLICK] If enough activations are issued to a nearby row within a refresh window, the charge leakage rate can be accelerated such that we end up with a bitflip.