## Slide 1: Venice Improving Solid-State Drive Parallelism at Low Cost via Conflict-Free Accesses
Rakesh Nadig*, Mohammad Sadrosadati*, Haiyu Mao, Nika Mansouri Ghiasi, Arash Tavakkol, Jisung Park, Hamid Sarbazi-Azad, Juan Gómez Luna, and Onur Mutlu
Session 3B: Monday 19 June, 4:00 PM EDT
Notes: Hello. I am Rakesh Nadig, a PhD student in the SAFARI Research Group at ETH Zurich.
In this lightning talk, I will give a brief preview of our work, Venice: Improving Solid-State Drive Parallelism at Low Cost via Conflict-Free Accesses

## Slide 2: Key Problem: Path Conflicts in Modern SSDs
Multiple flash memory chips are connected to the SSD Controller using a shared channel
I/O requests attempt to simultaneously access the flash chips using a single path Path Conflict
Path Conflicts cause I/O requests to be transferred serially on the shared channel
Limits SSD parallelism and overall performance
1
Notes: Lets look at the key problem we address in this work [CLICK]
In a commodity SSD, multiple flash chips are connected to the SSD controllers using a shared channel [CLICK]
So, multiple I/O requests may attempt to simultaneously access flash chips connected to the same shared channel [CLICK] which causes Path Conflict in SSDs [CLICK] The i/o requests that experience path conflicts are transferred serially on the shared channel [CLICK]
Path conflicts limit the SSD parallelism and overall performance of the SSD

## Slide 3: Delay Caused by Path Conflicts
Case 1: Same Channel
Case 2: Different Channels
FC0
F0
F1
F2
F3
Channel 0
CMD
RD Operation
Data Transfer
Flash chip 0
Flash chip 1
Channel 0:
CMD
RD Operation
Data Transfer
Read Request 1
Read Request 2
Served serially
Path conflict!
time
2
Channel 0
Flash chip 0
time
Flash chip 4
Channel 0:
Channel 1:
CMD
RD Operation
Data Transfer
CMD
RD Operation
Data Transfer
Channel 1
FC0
FC1
F0
F1
F2
F3
F4
F5
F6
F7
Read Request 1
Read Request 2
Served in parallel
Saved Cycles

## Slide 4: Performance Impact of Path Conflicts
Path conflicts increase the average I/O latency by 57% in our experiments on a performance-optimized SSD
The performance overhead of path conflicts increases by 1.6x in our experiments for high-I/O-intensity workloads
3

## Slide 5: Prior Approaches
Shared Channel
FC
FC
FC
FC
Flash Chip
Baseline SSD
FC
FC
FC
FC
Flash Chip
2x Wider Shared Channel
Packetized SSD (pSSD) [1]
4
[1] Kim+, “Networked SSD: Flash Memory Interconnection Network for High-Bandwidth SSD”, MICRO 2022 [2] Tavakkol+, “Network-on-SSD: A Scalable and High-Performance Communication Design Paradigm for SSDs”, IEEE CAL 2012

## Slide 6: Prior Approaches
Shared Channel
FC
FC
FC
FC
Flash Chip
Baseline SSD
FC
FC
FC
FC
Flash Chip
2x Wider Shared Channel
Packetized SSD (pSSD) [1]
4
[1] Kim+, “Networked SSD: Flash Memory Interconnection Network for High-Bandwidth SSD”, MICRO 2022 [2] Tavakkol+, “Network-on-SSD: A Scalable and High-Performance Communication Design Paradigm for SSDs”, IEEE CAL 2012
Baseline SSD and Packetized SSD do not provide path diversity to flash chips

## Slide 7: Prior Approaches
Shared Channel
FC
FC
FC
FC
Flash Chip
Baseline SSD
FC
FC
FC
FC
Flash Chip
2x Wider Shared Channel
Packetized SSD (pSSD) [1]
4
[1] Kim+, “Networked SSD: Flash Memory Interconnection Network for High-Bandwidth SSD”, MICRO 2022 [2] Tavakkol+, “Network-on-SSD: A Scalable and High-Performance Communication Design Paradigm for SSDs”, IEEE CAL 2012
Baseline SSD and Packetized SSD do not provide path diversity to flash chips
Packetized Network SSD (pnSSD) [1]
FC
FC
FC
FC
Horizontal Channel
Vertical Channel
Network-on-SSD (NoSSD) [2]
FC
FC
FC
FC
Flash Chip
Link

## Slide 8: Prior Approaches
Shared Channel
FC
FC
FC
FC
Flash Chip
Baseline SSD
FC
FC
FC
FC
Flash Chip
2x Wider Shared Channel
Packetized SSD (pSSD) [1]
4
[1] Kim+, “Networked SSD: Flash Memory Interconnection Network for High-Bandwidth SSD”, MICRO 2022 [2] Tavakkol+, “Network-on-SSD: A Scalable and High-Performance Communication Design Paradigm for SSDs”, IEEE CAL 2012
Baseline SSD and Packetized SSD do not provide path diversity to flash chips
Packetized Network SSD (pnSSD) [1]
FC
FC
FC
FC
Horizontal Channel
Vertical Channel
Network-on-SSD (NoSSD) [2]
FC
FC
FC
FC
Flash Chip
Link
Packetized Network SSD and Network-on-SSD
do not effectively utilize the path diversity
incur large area & cost overheads

## Slide 9: Our Goal
To fundamentally address the path conflict problem in SSDs by
5
increasing the number of paths to each flash chip (i.e., path diversity) at low cost
effectively utilizing the increased path diversity for communication between the SSD controller and flash chips

## Slide 10: Our Proposal
Venice
Named after the network of canals in the city of Venice
https://en.wikipedia.org/wiki/Venice
A low-cost interconnection network of flash chips in the SSD
Conflict-free path reservation for each I/O request
A non-minimal fully-adaptive routing algorithm for path identification
6

## Slide 11: Venice: Architecture (I)
FC
Flash Node
…
…
…
…
…
…
…
…
…
FC
FC
FC
7
Flash
Chip
Router
Chip
Links
I/O bus
Bi-directional Link
Venice provides increased path diversity at low cost
No modifications to existing flash chips in Venice
Notes: We first look at the low-cost interconnection network in Venice
[CLICK] In our design, there are many flash nodes interconnected using a 2D mesh topology. Venice can work with any network topology in principle.
Each Flash controller manages a row of flash nodes similar to the typical SSD shared bus architecture
[CLICK] Two flash nodes are connected using a bidirectional link
[CLICK] lets look at the design of a flash node
[click] each flash node consists of a flash chip and a [click] separate router chip
[click] the links are connected to the router chip and not to the flash chip
[click] each flash chip is connected to its corresponding router chip using the typical I/O data pins
[click] The interconnection network is low-cost because of
[click] separation of router chip from the flash chip
[click] no additional pins or circuitry added to the flash chip. The flash chip remains untouched

## Slide 12: Venice: Architecture (II)
FC
…
…
…
…
…
…
…
…
…
FC
FC
FC
7
Target Flash Node
Scout Packet
Reserved Path for I/O Request
Venice uses a small scout packet to reserve a conflict-free path for each I/O request
Path reservation eliminates path conflicts by enabling conflict-free I/O transfer

## Slide 13: Venice: Summary
Mitigates path conflicts by efficiently utilizing the path diversity of the SSD interconnection network
Improves performance by 1.9x/1.5x over the best-performing prior work on performance-optimized/cost-optimized SSD
8
Speedup over Baseline SSD
Chart: 
| MSR Cambridge | YCSB | Slacker | SYSTOR '17 | YCSB RocksDB | GMEAN
pSSD | 1.3679 | 1.2429 | 1.2388 | 1.1785 | 1.0461 | 1.2725
pnSSD | 1.4195 | 1.2253 | 1.1857 | 1.1314 | 1.0626 | 1.2835
NoSSD | 1.4886 | 1.2888 | 1.0869 | 1.2025 | 1.1324 | 1.3325
Venice | 2.876 | 2.2293 | 1.7454 | 2.6821 | 2.2193 | 2.5567
Baseline SSD
2.7x
Chart: 
| MSR Cambridge | YCSB | Slacker | SYSTOR '17 | YCSB RocksDB | GMEAN
pSSD | 1.156 | 1.0407 | 1.0331 | 1.042 | 1.027 | 1.0977
pnSSD | 1.1122 | 1.0417 | 1.0348 | 1.034 | 1.0866 | 1.081
NoSSD | 1.2028 | 1.1266 | 1.0321 | 1.0545 | 1.0933 | 1.1398
Venice | 1.8719 | 1.5594 | 1.4117 | 1.3082 | 1.7317 | 1.6707
1.7x
1.9x
1.5x

## Slide 14: Venice: Summary
Mitigates path conflicts by efficiently utilizing the path diversity of the SSD interconnection network
Improves performance by 1.9x/1.5x over the best-performing prior work on performance-optimized/cost-optimized SSD
8
Reduces energy consumption by 46% on average over the most efficient prior work
Chart: 
| MSR Cambridge | YCSB | Slacker | SYSTOR '17 | YCSB RocksDB | AVG
pSSD | 0.76814 | 0.88721 | 0.91754 | 0.90269 | 1.0222 | 0.84439
pnSSD | 0.7415 | 0.89584 | 0.95561 | 0.93297 | 1.0152 | 0.83932
NoSSD | 0.66591 | 0.7343 | 0.86453 | 0.81963 | 0.76217 | 0.72842
Venice | 0.36364 | 0.42215 | 0.53647 | 0.36947 | 0.38174 | 0.39082
61%
Energy Consumption (Norm. to Baseline SSD)
46%

## Slide 15: Venice: Summary
Mitigates path conflicts by efficiently utilizing the path diversity of the SSD interconnection network
Improves performance by 1.9x/1.5x over the best-performing prior work on performance-optimized/cost-optimized SSD
Reduces energy consumption by 46% on average over the most efficient prior work
8
Low-cost and requires no changes to commodity flash chips

## Slide 16: Venice Improving Solid-State Drive Parallelism at Low Cost via Conflict-Free Accesses
Session 3B: Monday 19 June, 4:00 PM EDT
https://arxiv.org/abs/2305.07768
Notes: To know more about Venice, please visit us at Session 3B on 19th June at 4 PM or read our paper. Thank you.