## Slide 1: Venice Improving Solid-State Drive Parallelism at Low Cost via Conflict-Free Accesses
Rakesh Nadig*, Mohammad Sadrosadati*, Haiyu Mao, Nika Mansouri Ghiasi, Arash Tavakkol, Jisung Park, Hamid Sarbazi-Azad, Juan Gómez Luna, and Onur Mutlu

## Slide 2: Talk Outline
Motivation
Venice
Evaluation
Summary
2

## Slide 3: Overview of a Modern Solid-State Drive
Host Interface Layer
DRAM
Flash Controller
Flash Controller
Flash Controller
Flash Chip
Flash Chip
Flash Chip
…
Flash Chip
Flash Chip
Flash Chip
…
…
SSD
SSD Controller
Flash Translation Layer
Shared Channel
…
…
Flash Chip
Flash Chip
Flash Chip
…
…
3

## Slide 4: Key Problem: Path Conflicts in Modern SSDs
Multiple flash memory chips are connected to the SSD Controller using a shared channel
I/O requests attempt to simultaneously access the flash chips using a single path Path Conflict
Path Conflicts cause I/O requests to be transferred serially on the shared channel
Limits SSD parallelism and reduces performance
4

## Slide 5: Delay Caused by Path Conflicts
Case 1: Same Channel
Case 2: Different Channels
FC0
F0
F1
F2
F3
Channel 0
CMD
RD Operation
Data Transfer
Flash chip 0
Flash chip 1
Channel 0:
CMD
RD Operation
Data Transfer
Read Request 1
Read Request 2
Served serially
Path conflict!
time
5
Channel 0
Flash chip 0
time
Flash chip 4
Channel 0:
Channel 1:
CMD
RD Operation
Data Transfer
CMD
RD Operation
Data Transfer
Channel 1
FC0
FC1
F0
F1
F2
F3
F4
F5
F6
F7
Read Request 1
Read Request 2
Served in parallel
Saved Cycles

## Slide 6: Performance Impact of Path Conflicts
Path conflicts increase the average I/O latency by 57% in our experiments on a performance-optimized SSD
The performance overhead of path conflicts increases by 1.6x in our experiments for high-I/O-intensity workloads
6

## Slide 7: Prior Approaches
Shared Channel
FC
FC
FC
FC
Flash Chip
Baseline SSD
FC
FC
FC
FC
Flash Chip
2x Wider Shared Channel
Packetized SSD (pSSD) [1]
7
[1] Kim+, “Networked SSD: Flash Memory Interconnection Network for High-Bandwidth SSD”, MICRO 2022 [2] Tavakkol+, “Network-on-SSD: A Scalable and High-Performance Communication Design Paradigm for SSDs”, IEEE CAL 2012

## Slide 8: Prior Approaches
Shared Channel
FC
FC
FC
FC
Flash Chip
Baseline SSD
FC
FC
FC
FC
Flash Chip
2x Wider Shared Channel
Packetized SSD (pSSD) [1]
8
[1] Kim+, “Networked SSD: Flash Memory Interconnection Network for High-Bandwidth SSD”, MICRO 2022 [2] Tavakkol+, “Network-on-SSD: A Scalable and High-Performance Communication Design Paradigm for SSDs”, IEEE CAL 2012
Baseline SSD and Packetized SSD do not provide path diversity to flash chips

## Slide 9: Prior Approaches
Shared Channel
FC
FC
FC
FC
Flash Chip
Baseline SSD
FC
FC
FC
FC
Flash Chip
2x Wider Shared Channel
Packetized SSD (pSSD) [1]
9
[1] Kim+, “Networked SSD: Flash Memory Interconnection Network for High-Bandwidth SSD”, MICRO 2022 [2] Tavakkol+, “Network-on-SSD: A Scalable and High-Performance Communication Design Paradigm for SSDs”, IEEE CAL 2012
Packetized Network SSD (pnSSD) [1]
FC
FC
FC
FC
Horizontal Channel
Vertical Channel
Network-on-SSD (NoSSD) [2]
FC
FC
FC
FC
Flash Chip
Link
Baseline SSD and Packetized SSD do not provide path diversity to flash chips

## Slide 10: Prior Approaches
Shared Channel
FC
FC
FC
FC
Flash Chip
Baseline SSD
FC
FC
FC
FC
Flash Chip
2x Wider Shared Channel
Packetized SSD (pSSD) [1]
10
[1] Kim+, “Networked SSD: Flash Memory Interconnection Network for High-Bandwidth SSD”, MICRO 2022 [2] Tavakkol+, “Network-on-SSD: A Scalable and High-Performance Communication Design Paradigm for SSDs”, IEEE CAL 2012
Packetized Network SSD (pnSSD) [1]
FC
FC
FC
FC
Horizontal Channel
Vertical Channel
Network-on-SSD (NoSSD) [2]
FC
FC
FC
FC
Flash Chip
Link
Packetized Network SSD and Network-on-SSD
do not effectively utilize the path diversity
incur large area & cost overheads
Baseline SSD and Packetized SSD do not provide path diversity to flash chips

## Slide 11: Our Goal
To fundamentally address the path conflict problem in SSDs by
11
increasing the number of paths to each flash chip (i.e., path diversity) at low cost
effectively utilizing the increased path diversity for communication between the SSD controller and flash chips

## Slide 12: Talk Outline
Motivation
Venice
Evaluation
Summary
12

## Slide 13: Our Proposal
Venice
Named after the network of canals in the city of Venice
https://en.wikipedia.org/wiki/Venice
A low-cost interconnection network of flash chips in the SSD
Conflict-free path reservation for each I/O request
A non-minimal fully-adaptive routing algorithm for path identification
13

## Slide 14: Our Proposal
Named after the network of canals in the city of Venice
https://en.wikipedia.org/wiki/Venice
A low-cost interconnection network of flash chips in the SSD
Conflict-free path reservation for each I/O request
A non-minimal fully-adaptive routing algorithm for path identification
14
Venice

## Slide 15: Venice: Architecture
FC
Flash Node
…
…
…
…
…
…
…
…
…
FC
FC
FC
15
Flash
Chip
Router
Chip
Links
I/O bus
Bi-directional Link
Venice provides increased path diversity at low cost
No modifications to existing flash chips in Venice

## Slide 16: Our Proposal
Named after the network of canals in the city of Venice
https://en.wikipedia.org/wiki/Venice
A low-cost interconnection network of flash chips in the SSD
Conflict-free path reservation for each I/O request
A non-minimal fully-adaptive routing algorithm for path identification
16
Venice

## Slide 17: Venice: Path Reservation (I)
Venice uses a small scout packet to reserve a conflict-free path for each I/O request
F0
F5
F1
F6
F2
F7
F3
F8
FC0
FC1
FC2
FC3
F4
F9
F10
F11
F12
F13
F14
F15
F16
F17
F18
F19
Scout Packet
Router of F5
Crossbar
Packet ID | Entry Port | Exit Port | Valid bit
Router Reservation Table
1
Left
Right
Valid
Target Flash Node
Reserved Path
17

## Slide 18: Venice: Path Reservation (II)
Venice uses a small scout packet to reserve a conflict-free path for each I/O request
F0
F5
F1
F6
F2
F7
F3
F8
FC0
FC1
FC2
FC3
F4
F9
F10
F11
F12
F13
F14
F15
F16
F17
F18
F19
Target Flash Node
Reserved Path
18
Scout Packet
Reserved Path

## Slide 19: Venice: Path Reservation
Venice uses a small scout packet to reserve a conflict-free path for each I/O request
F0
F5
F1
F6
F2
F7
F3
F8
FC0
FC1
FC2
FC3
F4
F9
F10
F11
F12
F13
F14
F15
F16
F17
F18
F19
Reserved Path
19
Reserved Path
The overhead of path reservation is negligible due to the small size of the scout packet
Path reservation eliminates path conflicts by enabling conflict-free I/O transfer
Notes: We look at another request whose target flash node is F9.
[click] in a shared bus SSD architecture, this request would face path conflict due to ongoing transfer of the previous request in the same channel. In Venice's interconnection network, the target flash node can be reached using a different path.
[click] Flash controller FC2 initiates the path reservation process by sending the scout packet
[click] the router of each flash node updates its router reservation table as the scout packet traverses the network
[click] a path is reserved for the second request now.

## Slide 20: Our Proposal
Named after the network of canals in the city of Venice
https://en.wikipedia.org/wiki/Venice
A low-cost interconnection network of flash chips in the SSD
Conflict-free path reservation for each I/O request
A non-minimal fully-adaptive routing algorithm for path identification
20
Venice

## Slide 21: Venice: Non-Minimal Fully Adaptive Routing
Venice uses a non-minimal fully-adaptive routing algorithm to route scout packets when a minimal path is unavailable
Effectively utilizes the idle links in the interconnection network to find a conflict-free path
F0
F5
F1
F6
F2
F7
F3
F8
FC0
FC1
FC2
FC3
F4
F9
F10
F11
F12
F13
F14
F15
F16
F17
F18
F19
21
Reserved Minimal Paths
Non-minimal Path
Req to F2
Req to F8
Req to F6
Req to F7
Target Flash Node

## Slide 22: More in the Paper
Venice’s non-minimal fully-adaptive routing algorithm
Handling deadlock and livelock scenarios
Overhead of exercising a non-minimal path
Analysis of prior architectures proposed to mitigate the path conflict problem
Detailed background on modern SSD architecture
22

## Slide 23: Talk Outline
Motivation
Venice
Evaluation
Summary
23

## Slide 24: Evaluation Methodology
Using MQSim [Tavakkol+, FAST’18], a state-of-the-art SSD simulator
Two SSD configurations
  Performance-Optimized (Samsung Z-NAND SSD)
  Cost-Optimized (Samsung PM9A3)
Nineteen data-intensive workloads from
  MSR Cambridge, YCSB, Slacker, SYSTOR ‘17 and RocksDB
Prior Approaches
  Baseline SSD: A typical multi-channel shared bus SSD
  Packetized SSD (pSSD) [Kim+, MICRO’22]: Uses packetization to double the flash channel bandwidth
  Packetized Network SSD (pnSSD) [Kim+, MICRO’22]: Increases path diversity by introducing vertical channels
  Network-on-SSD (NoSSD) [Tavakkol+, CAL 2012]: Proposes an interconnection network of flash chips with simple deterministic routing
  Path-conflict-free SSD: An ideal SSD with no path conflicts
24

## Slide 25: Results: Performance Analysis (I)
Performance-Optimized SSD
25
Chart: 
| MSR Cambridge | YCSB | Slacker | SYSTOR '17 | YCSB RocksDB | GMEAN
pSSD | 1.3679 | 1.2429 | 1.2388 | 1.1785 | 1.0461 | 1.2725
pnSSD | 1.4195 | 1.2253 | 1.1857 | 1.1314 | 1.0626 | 1.2835
NoSSD | 1.4886 | 1.2888 | 1.0869 | 1.2025 | 1.1324 | 1.3325
Venice | 2.876 | 2.2293 | 1.7454 | 2.6821 | 2.2193 | 2.5567
Path-conflict-free SSD | 4.785 | 2.9899 | 2.0677 | 3.2899 | 3.5978 | 3.8133
Speedup over Baseline SSD
2.7x
2.1x
2.0x
1.9x
45%
Baseline SSD
Venice improves SSD performance by 1.9x on average over the best-performing prior work
Venice’s performance is within 45% of the performance of a Path-conflict-free SSD

## Slide 26: Results: Performance Analysis (II)
Cost-Optimized SSD
26
Chart: 
| MSR Cambridge | YCSB | Slacker | SYSTOR '17 | YCSB RocksDB | GMEAN
pSSD | 1.156 | 1.0407 | 1.0331 | 1.042 | 1.027 | 1.0977
pnSSD | 1.1122 | 1.0417 | 1.0348 | 1.034 | 1.0866 | 1.081
NoSSD | 1.2028 | 1.1266 | 1.0321 | 1.0545 | 1.0933 | 1.1398
Venice | 1.8719 | 1.5594 | 1.4117 | 1.3082 | 1.7317 | 1.6707
Path-conflict-free SSD | 2.1548 | 1.7412 | 1.588 | 1.4372 | 2.0132 | 1.9003
Speedup over Baseline SSD
25%
1.7x
1.5x
1.6x
1.5x
Baseline SSD
Venice improves SSD performance by 1.5x on average over the best-performing prior work
Venice’s performance is within 25% of the performance of a Path-conflict-free SSD

## Slide 27: Results: Performance Analysis (III)
Performance-Optimized SSD
Cost-Optimized SSD
27
Chart: 
| MSR Cambridge | YCSB | Slacker | SYSTOR '17 | YCSB RocksDB | GMEAN
pSSD | 1.3679 | 1.2429 | 1.2388 | 1.1785 | 1.0461 | 1.2725
pnSSD | 1.4195 | 1.2253 | 1.1857 | 1.1314 | 1.0626 | 1.2835
NoSSD | 1.4886 | 1.2888 | 1.0869 | 1.2025 | 1.1324 | 1.3325
Venice | 2.876 | 2.2293 | 1.7454 | 2.6821 | 2.2193 | 2.5567
Path-conflict-free SSD | 4.785 | 2.9899 | 2.0677 | 3.2899 | 3.5978 | 3.8133
Speedup over Baseline SSD
Chart: 
| MSR Cambridge | YCSB | Slacker | SYSTOR '17 | YCSB RocksDB | GMEAN
pSSD | 1.156 | 1.0407 | 1.0331 | 1.042 | 1.027 | 1.0977
pnSSD | 1.1122 | 1.0417 | 1.0348 | 1.034 | 1.0866 | 1.081
NoSSD | 1.2028 | 1.1266 | 1.0321 | 1.0545 | 1.0933 | 1.1398
Venice | 1.8719 | 1.5594 | 1.4117 | 1.3082 | 1.7317 | 1.6707
Path-conflict-free SSD | 2.1548 | 1.7412 | 1.588 | 1.4372 | 2.0132 | 1.9003
Speedup over Baseline SSD
Venice provides significant improvement in performance over all prior approaches

## Slide 28: Results: Reduction in Path Conflicts
Chart: 
| MSR Cambridge | YCSB | Slacker | SYSTOR '17 | YCSB RocksDB | AVG
Baseline SSD | 0.0016682 | 0.0032304 | 0.0029128 | 0.0034716 | 0.0027341 | 0.0023606
pSSD | 0.0014535 | 0.0028722 | 0.0028419 | 0.0033009 | 0.0025218 | 0.0021531
pnSSD | 0.0015103 | 0.0028989 | 0.0028616 | 0.0034562 | 0.0025133 | 0.0022115
NoSSD | 0.0014302 | 0.0026048 | 0.0024786 | 0.0025528 | 0.0023217 | 0.0019353
Venice | 3e-05 | 0.00014 | 0.00050562 | 0.00043 | 0.00013 | 0.00019114
% of I/O Requests
Venice mitigates path conflicts by using path reservation and effective utilization of path diversity
99.98% of I/O requests do not experience path conflicts
28

## Slide 29: Results: SSD Energy Consumption
Chart: 
| MSR Cambridge | YCSB | Slacker | SYSTOR '17 | YCSB RocksDB | AVG
pSSD | 0.76814 | 0.88721 | 0.91754 | 0.90269 | 1.0222 | 0.84439
pnSSD | 0.7415 | 0.89584 | 0.95561 | 0.93297 | 1.0152 | 0.83932
NoSSD | 0.66591 | 0.7343 | 0.86453 | 0.81963 | 0.76217 | 0.72842
Venice | 0.36364 | 0.42215 | 0.53647 | 0.36947 | 0.38174 | 0.39082
Energy Consumption (Norm. to Baseline SSD)
Venice reduces the SSD energy consumption by 46% on average over the most efficient prior work
Baseline SSD
61%
29
46%

## Slide 30: More in the Paper
Power and area overhead analysis
Tail latency analysis
Sensitivity to interconnection network configurations
Performance on mixed workloads
Detailed evaluation methodology
30

## Slide 31: More in the Paper
https://arxiv.org/abs/2305.07768
31

## Slide 32: Talk Outline
Motivation
Venice
Evaluation
Summary
32

## Slide 33: Venice: Summary
Mitigates path conflicts by efficiently utilizing the path diversity of the SSD interconnection network
Improves performance by 1.9x/1.5x over the best-performing prior work on performance-optimized/cost-optimized SSD
Reduces energy consumption by 46% on average over the most efficient prior work
33
Low-cost and requires no changes to commodity flash chips

## Slide 34: Venice Improving Solid-State Drive Parallelism at Low Cost via Conflict-Free Accesses
Rakesh Nadig*, Mohammad Sadrosadati*, Haiyu Mao, Nika Mansouri Ghiasi, Arash Tavakkol, Jisung Park, Hamid Sarbazi-Azad, Juan Gómez Luna, and Onur Mutlu
https://arxiv.org/abs/2305.07768

## Slide 35: FAQ
Scout Packet Structure
Power Overhead
Area Overhead
Evaluated Configurations
Workload Characteristics
Mixed Workloads
Results
  Throughput Analysis
  Tail Latency
  Power Consumption
  Performance on Mixed Workloads
  Sensitivity to Interconnection Network Configuration

## Slide 36: Structure of a Scout Packet
A scout packet consists of two 8 bit flits, a header flit and a tail flit
The flash controller sends a scout packet to identify a conflict-free path for the I/O request
Type
Type
Destination Flash Chip ID
Source Flash
Controller ID
Unused Bits
2 bits
2 bits
6 bits
3 bits
3 bits
Scout Packet
8 bits
2-bit Type Info
1st
Bit
2nd
Bit
0: Cancel
1: Reserve
0: Header Flit
1: Tail Flit
1
2
Header
Flit
Tail
Flit

## Slide 37: Power Consumption (I)
Router
  We implement the HDL and synthesize it using UMC 65nm technology node
  Router consumes 0.241mW for a 4KB page transfer
Network Link
  ORION 3.0 power model tool
  Each network link consumes about 1.08mW for a 4KB page transfer
  Link capacitance is lower than bus capacitance -> 90% less power than that of the shared channel bus
    Links are shorter and thinner than a shared bus
    Two drivers in links compared to several drivers in a bus

## Slide 38: Area Overhead
Router
  Area overhead estimated using router’s HDL model
  Each router has
    an area of 614 m2 + 40 I/O
    A total area of 8mm2 -> 8% of a typical 100mm2 flash chip
Network Link
  ORION 3.0 model for area analysis of network links
  112 network links for a 8x8 flash array configuration
  44% lower area than a baseline multi-channel shared bus architecture
  Links are thinner and require lower pitch sizes

## Slide 39: Evaluated Configurations

## Slide 40: Workload Characteristics

## Slide 41: Mixed Workloads

## Slide 42: SSD Throughput Analysis
Performance-Optimized SSD
Cost-Optimized SSD
Chart: 
| MSR Cambridge | YCSB | Slacker | SYSTOR '17 | YCSB RocksDB | AVG
Baseline SSD | 0.23211 | 0.33764 | 0.4853 | 0.31351 | 0.27903 | 0.28766
pSSD | 0.31557 | 0.42151 | 0.59916 | 0.36517 | 0.29154 | 0.36188
pnSSD | 0.33148 | 0.41495 | 0.57344 | 0.35282 | 0.29585 | 0.36536
NoSSD | 0.33523 | 0.43841 | 0.52788 | 0.38942 | 0.31704 | 0.37301
Venice | 0.61262 | 0.74687 | 0.84568 | 0.82164 | 0.61772 | 0.68482
SSD Throughput (Norm. to Path-conflict-free SSD)
Chart: 
| MSR Cambridge | YCSB | Slacker | SYSTOR '17 | YCSB RocksDB | AVG
Baseline SSD | 0.49191 | 0.57677 | 0.62973 | 0.69824 | 0.50105 | 0.54889
pSSD | 0.56125 | 0.60055 | 0.65056 | 0.72841 | 0.51416 | 0.59622
pnSSD | 0.54002 | 0.60044 | 0.6518 | 0.72173 | 0.54141 | 0.58699
NoSSD | 0.57855 | 0.64863 | 0.64996 | 0.73606 | 0.54894 | 0.61519
Venice | 0.87032 | 0.8957 | 0.88952 | 0.91096 | 0.86024 | 0.88037
SSD Throughput (Norm. to Path-conflict-free SSD)
176%
120%
113%
102%
76%
58%
61%
51%

## Slide 43: SSD Throughput Analysis
Performance-Optimized SSD
Cost-Optimized SSD
Chart: 
| MSR Cambridge | YCSB | Slacker | SYSTOR '17 | YCSB RocksDB | AVG
Baseline SSD | 0.23211 | 0.33764 | 0.4853 | 0.31351 | 0.27903 | 0.28766
pSSD | 0.31557 | 0.42151 | 0.59916 | 0.36517 | 0.29154 | 0.36188
pnSSD | 0.33148 | 0.41495 | 0.57344 | 0.35282 | 0.29585 | 0.36536
NoSSD | 0.33523 | 0.43841 | 0.52788 | 0.38942 | 0.31704 | 0.37301
Venice | 0.61262 | 0.74687 | 0.84568 | 0.82164 | 0.61772 | 0.68482
SSD Throughput (Norm. to Path-conflict-free SSD)
Chart: 
| MSR Cambridge | YCSB | Slacker | SYSTOR '17 | YCSB RocksDB | AVG
Baseline SSD | 0.49191 | 0.57677 | 0.62973 | 0.69824 | 0.50105 | 0.54889
pSSD | 0.56125 | 0.60055 | 0.65056 | 0.72841 | 0.51416 | 0.59622
pnSSD | 0.54002 | 0.60044 | 0.6518 | 0.72173 | 0.54141 | 0.58699
NoSSD | 0.57855 | 0.64863 | 0.64996 | 0.73606 | 0.54894 | 0.61519
Venice | 0.87032 | 0.8957 | 0.88952 | 0.91096 | 0.86024 | 0.88037
SSD Throughput (Norm. to Path-conflict-free SSD)
176%
120%
113%
102%
76%
58%
61%
51%
Venice improves SSD throughput over prior approaches by effectively mitigating path conflicts

## Slide 44: Tail Latency
Comparison of tail latencies in the 99th percentile of I/O requests
32% reduction
22% reduction

## Slide 45: Tail Latency
Comparison of tail latencies in the 99th percentile of I/O requests
32% reduction
22% reduction
Venice reduces tail latencies by effectively mitigating path conflicts

## Slide 46: Power Consumption (II)
Venice reduces the average power consumption by 4% over Baseline SSD
Chart: 
| MSR Cambridge | YCSB | Slacker | SYSTOR '17 | YCSB RocksDB | AVG
pSSD | 1.0441 | 1.1016 | 1.1324 | 1.0639 | 1.1605 | 1.0748
pnSSD | 1.0349 | 1.097 | 1.1302 | 1.0562 | 1.1605 | 1.068
NoSSD | 0.97515 | 0.9458 | 0.93967 | 0.97314 | 0.92749 | 0.96299
Venice | 0.97154 | 0.93714 | 0.92635 | 0.96658 | 0.9113 | 0.95604
Power Consumption (Norm. to Baseline SSD)
Baseline SSD
1.07x
1.06x
0.96x
0.95x

## Slide 47: Performance on Mixed Workloads
Chart: 
| mix1 | mix2 | mix3 | mix4 | mix5 | mix6 | GMEAN
pSSD | 1.0069 | 0.98108 | 1.0333 | 1.0236 | 0.99455 | 1.009 | 1.0079
pnSSD | 1.0146 | 1.0111 | 1.0187 | 1.0049 | 1.0166 | 1.0125 | 1.013
NoSSD | 1.0424 | 1.0558 | 1.1593 | 1.2882 | 1.0527 | 1.1358 | 1.1192
Venice | 1.3442 | 1.2915 | 1.7827 | 2.5522 | 1.5266 | 3.0915 | 1.8277
Path-conflict-free SSD | 1.937 | 1.5575 | 2.5341 | 3.3683 | 2.1389 | 4.1472 | 2.4724
Speedup over Baseline SSD
Venice outperforms prior approaches on high-intensity mixed workloads by effectively mitigating path conflicts
Baseline SSD
1.01x
1.01x
1.12x
1.83x
2.47x

## Slide 48: Sensitivity to Network Configurations
Chart: 
| 4x16 | 8x8 | 16x4
pSSD | 1.2232 | 1.2725 | 1.0474
NoSSD | 1.3428 | 1.3325 | 1.107
Venice | 2.0319 | 2.5567 | 1.905
Path-conflict-free SSD | 5.2207 | 3.8133 | 2.1437
Speedup over Baseline SSD
Venice provides higher performance improvement for 8x8 compared to 4x16 and 16x4
Baseline SSD
1.22x
1.34x
2.03x
5.22x
1.27x
1.33x
2.56x
1.05x
1.11x
1.90x
2.14x
3.81x

## Slide 49: Prior Approaches to Address Path Conflicts
Network-On-SSD [2]
  Replaces a multi-channel shared bus architecture with an interconnection network of flash chips
  Significantly increases path diversity than a typical SSD
Links
F0
F1
F2
F3
F4
F5
F6
F7
F8
F9
F10
F11
F12
F13
F14
F15
FC0
FC1
FC2
FC3
5
[2] Tavakkol+, “Network-on-SSD: A Scalable and High-Performance Communication Design Paradigm for SSDs”, IEEE CAL 2012

## Slide 50: Prior Approaches to Address Path Conflicts
Network-On-SSD [2]
  Replaces a multi-channel shared bus architecture with an interconnection network of flash chips
  Significantly increases path diversity than a typical SSD
Ongoing I/O request
F0
F1
F2
F3
F4
F5
F6
F7
F8
F9
F10
F11
F12
F13
F14
F15
FC0
FC1
FC2
FC3
Target Chip
I/O Request to F2
Path Conflict
[2] Tavakkol+, “Network-on-SSD: A Scalable and High-Performance Communication Design Paradigm for SSDs”, IEEE CAL 2012
Network-On-SSD’s simple routing algorithm fails to mitigate path conflicts in SSDs