## Slide 1: VICTIMA Drastically Increasing Address Translation Reach by Leveraging Underutilized Cache Resources
Konstantinos Kanellopoulos
Hong Chul Nam, Nisa Bostanci, Rahul Bera, Mohammad Sadrosadati,
Rakesh Kumar, Davide Basilio Bartolini and Onur Mutlu

## Slide 2: Executive Summary
Problem: Address translation is a major performance bottleneck in data-intensive workloads
Large datasets and irregular memory access patterns lead to frequent L2 TLB misses (e.g., 20-50 MPKI) and frequent high-latency (e.g., 100-150 cycles) page table walks (PTW)
Motivation: Increasing the translation reach (i.e., memory covered by the TLBs) reduces PTWs. However, employing large TLBs leads to increased area, power and latency overheads.
Victima: New software-transparent scheme that drastically increases the address translation reach of the processor’s TLB hierarchy by leveraging the underutilized cache resources
https://github.com/CMU-SAFARI/Victima
Key Results: Victima (i) outperforms by 5.1% a state-of-the-art large TLB design and (ii) achieves similar performance to an optimistically fast 128K-entry L2 TLB
Key Idea:
Key Benefits:
+ Efficient in native/virtualized environments
+ Fully transparent to application/OS software
+ Compatible with huge page schemes
Transform L2 cache blocks that store PTEs into blocks that store TLB entries
PTEs
TLB Entries
L2 Cache
Opportunity: Increase the translation reach of the TLB hierarchy by storing the existing TLB entries within the existing cache hierarchy
Notes: [1] Let’s discuss quickly the problem:
Data intensive workloads experience high address translation overheads:
Many data-intensive workloads use large datasets and experience irregular memory access patterns
Frequent L2 TLB misses and frequent high-latency PTW overheads.

## Slide 3: Talk Outline
Background & Motivation
Opportunity: Leverage Caches
Victima: Overview
Victima: Detailed Design
Evaluation Results
Notes: No need to discuss the whole outline – it took 25 seconds

## Slide 4: Talk Outline
Background & Motivation
Opportunity: Leverage Caches
Victima: Overview
Victima: Detailed Design
Evaluation Results

## Slide 5: Virtual Memory Basics
The Page Table (PT) stores all virtual-to-physical address mappings
The x86-64 PT is organized as a 4/5-level radix tree
To access the PT, the system performs a Page Table Walk (PTW)
Notes: Align and add more space.

## Slide 6: Page Table Walk in x86-64
9 bits
Virtual Address
9 bits
9 bits
9 bits
CR3
Physical Frame Number
PL4
PL3
PL2
PL1

## Slide 7: Page Table Walk in x86-64
9 bits
Virtual Address
9 bits
9 bits
9 bits
CR3
Physical Frame Number
PL4
PL3
PL2
PL1
Four sequential memory accesses
during a page table walk in x86-64

## Slide 8: Address Translation Flow (I)
Memory Hierarchy
Core
Page Table
Memory
Management Unit
Virtual
Address

## Slide 9: Address Translation Flow (II)
L1 I-TLB
L1 D-TLB
Unified
L2 TLB
Page Walk Caches
Page Table Walker
Miss
Miss
Miss
Virtual
Address
Miss
Memory Hierarchy
Memory Management Unit
Page Table

## Slide 10: Address Translation Overhead
Chart: PTW Latency (cycles)
| 20-30 | 30-40 | 40-50 | 50-60 | 60-70 | 70-80 | 80-90 | 90-100 | 100-110 | 110-120 | 120-130 | 130-140 | 140-150 | 150-160 | 160-170 | 170-180 | 180-190
Occurences | 3.046 | 0.443 | 0.467 | 1.108 | 2.639 | 3.056 | 2.209 | 2.156 | 2.482 | 2.896 | 4.061 | 3.99 | 4.476 | 2.872 | 0.714 | 0.225 | 0.146
Core spends 137 cycles on average
to perform a PTW
Mean: 137 cycles
Notes: Number of occurences of different page table walk latencies across 500M instructions
The average page table walk latency is 137 cycles

## Slide 11: Address Translation Overhead
High latency
PTWs
Frequent
PTWs
High performance overheads
+

## Slide 12: Potential Solution
High latency
PTWs
Frequent
PTWs
High performance overheads
+
Reduce PTW frequency by
increasing address translation reach

## Slide 13: Address Translation Reach: Definition
4KB
4KB
4KB
2MB
4KB
2MB
2MB
4KB
Amount of VA-to-PA mappings
stored by the processor’s TLB hierarchy
Example Modern Processors:
Maximum 3-4GB
Increase Reach
Reduce PTWs

## Slide 14: Increasing Address Translation Reach
Large Hardware TLBs

## Slide 15: Scaling Hardware L2 TLB (I)
Employing a 64K-entry L2 TLB
reduces MPKI from 39 to 24
Chart: L2 TLB MPKI
| BC | BFS | CC | DLRM | GEN | GC | PR | RND | SSSP | TC | XS | GMEAN
L2 TLB 1.5K entries | 11.2052 | 70.5749 | 85.9961 | 71.5893 | 63.2432 | 63.2465 | 38.5931 | 71.1067 | 65.9778 | 6.7839 | 14.7529 | 39.3766
64K | 7.5502 | 45.073 | 54.5346 | 44.9912 | 35.3586 | 35.3472 | 26.1325 | 46.268 | 44.6049 | 4.9003 | 6.4744 | 24.3515
1.5K-Entry L2 TLB
64K-Entry L2 TLB
Notes: - Baseline config with 1.5 K entries L2 TLB and a much larger 64K-entry L2 TLB

## Slide 16: Scaling Hardware L2 TLB (II)
64K-entry L2 TLB with optimistic access latency provides 5.4% speedup over baseline
Chart: Speedup over Baseline
| BC | BFS | CC | DLRM | GEN | GC | PR | RND | SSSP | TC | XS | GMEAN
64K-12 | 1.0611 | 1.0408 | 1.033 | 1.0401 | 1.0546 | 1.0549 | 1.0551 | 1.0437 | 1.056 | 1.0576 | 1.0994 | 1.0541
5.4%
64K-Entry L2 TLB Optimistic 12-cycle access latency
Notes: - We assume the 64K entry L2 TLB has an optimistic access latency of 12 cycles – same as the baseline system

## Slide 17: Scaling Hardware L2 TLB (II)
64K-entry L2 TLB with optimistic access latency provides 5.4% speedup over baseline
Benefits come for free?
Chart: Speedup over Baseline
| BC | BFS | CC | DLRM | GEN | GC | PR | RND | SSSP | TC | XS | GMEAN
64K-12 | 1.0611 | 1.0408 | 1.033 | 1.0401 | 1.0546 | 1.0549 | 1.0551 | 1.0437 | 1.056 | 1.0576 | 1.0994 | 1.0541
5.4%
64K-Entry L2 TLB Optimistic 12-cycle access latency

## Slide 18: Scaling Hardware L2 TLB (III)
64K-entry L2 TLB with realistic access latency provides only 0.8% speedup over baseline
Chart: Speedup over Baseline
| BC | BFS | CC | DLRM | GEN | GC | PR | RND | SSSP | TC | XS | GMEAN
64K-39 | 1.0191 | 1.0004 | 0.99795 | 1.0011 | 1.005 | 1.0048 | 0.99723 | 1.0121 | 1.0074 | 1.0314 | 1.0149 | 1.0083
64K-Entry L2 TLB Realistic 39-cycle access latency
0.8%
Notes: [1] We tuned the latency of the same large 64K L2 TLB, based on CACTI, to 39 cycles which represents a more realistic scenario

## Slide 19: Increasing Translation Reach
Large Hardware TLBs
Large Software-Managed TLBs

## Slide 20: Large Software-Managed L3 TLB
L2 TLB
Miss
Software L3 TLB
Main Memory
MMU
Contiguous

## Slide 21: Drawbacks of Software-Managed TLB
High Latency
Contiguous Physical Allocations
OS Modifications
1
2
3
Notes: L3 TLB to L2 TLB??

## Slide 22: Increasing Translation Reach
Large
Hardware
TLBs
Large
Software-Managed TLBs
Both approaches come with
major drawbacks
Notes: [1] Large hardware TLBs come with increased access latency area and power overheads
[2] Software managed TLBs complicate memory management while incurring high latency – similar to the PTW latency – in native execution environments
[3] Both approaches come with major drawbacks which hinder their adoption

## Slide 23: Talk Outline
Background & Motivation
Opportunity: Leverage Caches
Victima: Overview
Victima: Detailed Design
Evaluation Results

## Slide 24: Opportunity: Leverage Caches
Store TLB entries in hardware caches
Notes: Make everything appear

## Slide 25: Leverage Cache Hierarchy
L2 TLB
MMU
TLB Entry
L2 Cache
PT
Walker
Miss
TLB Entry

## Slide 26: Where is the Benefit?
1.5K entries
12-cycle latency
2MB L2 Cache
Fits 36x more
TLB entries
Low latency
(e.g., 16 cycles)
L2 TLB
PTW takes 137 cycles on average

## Slide 27
Interference with Program Data?
Chart: Breakdown of L2 Data Block Reuse
| BC | BFS | CC | DLRM | GEN | GC | PR | RND | SSSP | TC | XS | GMEAN
Reuse 0 | 0.86066 | 0.94635 | 0.94805 | 0.94547 | 0.91946 | 0.91943 | 0.95482 | 0.86622 | 0.93767 | 0.92594 | 0.91907 | 0.93296
1-5 | 0.13582 | 0.046948 | 0.045221 | 0.047729 | 0.07396 | 0.073981 | 0.042333 | 0.12212 | 0.05891 | 0.07355 | 0.074329 | 0.061195
5-10 | 0.002249 | 0.0029149 | 0.0027119 | 0.0031217 | 0.003474 | 0.0034728 | 0.001051 | 0.0098158 | 0.0016732 | 0.00032699 | 0.0046164 | 0.0030027
10-20 | 0.00075122 | 0.0022842 | 0.0022708 | 0.0023415 | 0.0017419 | 0.0017418 | 0.0010278 | 0.0017382 | 0.00076282 | 5.0653e-05 | 0.0012267 | 0.0016777
>20 | 0.00051974 | 0.0014992 | 0.0017451 | 0.0013334 | 0.0013664 | 0.0013709 | 0.00076343 | 0.00010279 | 0.00098398 | 0.00012888 | 0.00076284 | 0.0011654
L2 cache is heavily underutilized

## Slide 28: Talk Outline
Background & Motivation
Opportunity: Leverage Caches
Victima: Overview
Victima: Detailed Design
Evaluation Results

## Slide 29: Our Goal
Drastically increase
the address translation reach of the processor
Leverage cache resources
to store TLB entries

## Slide 30: Victima: Key Idea
Repurpose L2 cache blocks
to store clusters of TLB entries
  Low-latency and high-capacity component
  to back up the L2 TLB

## Slide 31: Victima: Overview
L2 TLB
MMU
PTW Cost
Estimator
L2 Cache
Low latency
PTE Block
TLB Block
Miss
Miss
Eviction
Transform
Costly-to-translate page?

## Slide 32
Victima Benefits
+ Drastic increase in address translation reach
+ Fully transparent to application/OS software
+ No need for contiguous physical allocations
+ Compatible with huge pages

## Slide 33: Talk Outline
Background & Motivation
Opportunity: Leverage Caches
Victima: Overview
Victima: Detailed Design
Evaluation Results

## Slide 34
Victima: Detailed Design
  L2 Cache Modifications
  Allocation of TLB Entries in L2 Cache
  Page Table Walk Cost Predictor
1
2
3

## Slide 35
Victima: L2 Cache Modifications
  Access TLB blocks using virtual address
  Perform tag matching for TLB blocks
1
2

## Slide 36: Example: Cache Configuration
1MB
16-way associative
L2 Cache
10 bits
Set index
Notes: [1] We are going to be using an example cache configuration where the L2 cache is 1MB large and 16-way associative
[2] Thus, the set index is 10 bits large

## Slide 37
Data Blocks vs. TLB Blocks in Caches
36 bits
0
Tag
64 bytes
TLB Entry
Data Block
Data
52-bit Physical Address
36 bits
Tag
1
TLB Entry
TLB Block
0
1
2
3
4
5
6
7
PTEs (8 bytes per PTE)
23 bits
23 bits
36-bit Virtual Page Number (4KB)
Tag
Tag
13 bits
ASID/Size
10 bits
Set index
6 bits
Offset
10 bits
Set index
3 bits
Offset
Notes: First, let’s see the structure of a conventional data block
We extend the metadata of the Data Block with an additional bit to distinguish between Data Blocks and TLB Blocks. In the Data Block, the TLB Entry bit is set to 0.
The conventional data block stores 64 bytes – we need 6 bits for the offset
As we showed before, the set index is 10 bits, and the rest 36 bits of the physical address constitute the tag.
Now, let’s see the structure of a TLB block – The TLB entry bit is set to 1. We use a virtual page number to access the TLB Block. The TLB block contains 8 page table entries from the last level of the page table – these correspond to 8 contiguous virtual pages – Thus 3 bits constitute the offset with which we can select onf of the 8 PTEs inside the cache line.
Set index remains the same and we see that the remaining bits for the tag are 23 – 13 less compared to the physical address tag.
Hence, we use the additional bits to store the ASID of the process and the page size of the TLB entries in the block

## Slide 38
Tag Matching for TLB Block
23 bits
1
Tag
TLB
Entry
TLB Block
Virtual
Address
23 bits
9 bits
ASID
Tag
9 bits
ASID
=
=
3 bits
Offset
0
1
2
3
4
5
6
7
PTEs

## Slide 39
Victima: L2 Cache Modifications
  L2 Cache Modifications
  Allocation of TLB Entries in L2 Cache
  Page Table Walk Cost Predictor
1
2
3

## Slide 40: Allocation of TLB Entries in L2 Cache
  On L2 TLB Miss
  On L2 TLB Eviction
1
2

## Slide 41: Allocation of TLB Entries in L2 Cache
  On L2 TLB Miss
  On L2 TLB Eviction
1
2

## Slide 42: Allocating TLB Blocks – L2 TLB Miss
L2 TLB
MMU
PTW Cost
Estimator
L2 Cache
TLB Block
PTE Block
Miss
Page Table
Walker
Transform

## Slide 43: Allocation of TLB Entries in L2 Cache
  On L2 TLB Miss
  On L2 TLB Eviction
1
2

## Slide 44: Allocating TLB Blocks – L2 TLB Eviction
L2 TLB
MMU
PTW Cost
Estimator
L2 Cache
TLB Block
Eviction
Page Table
Walker
Transform
PTE Block

## Slide 45: Address Translation in Victima (I)
L2 TLB
MMU
L2 Cache
TLB Block
Miss
Page Table
Walker
Hit

## Slide 46: Address Translation in Victima (II)
L2 TLB
MMU
L2 Cache
Miss
Page Table
Walker
Miss

## Slide 47
Victima: Detailed Design
  L2 Cache Modifications
  Allocation of TLB Blocks in L2 Cache
  Page Table Walk Cost Predictor
1
2
3

## Slide 48
PTW Cost Predictor: Objective
  Predict which pages are costly-to-translate
  Insert only those TLB blocks in L2 cache
Notes: Add banner explaining the benefits it brings

## Slide 49
Tracking Costly-to-Translate Pages
Page Table Entry
..
..
Frequency
Cost
Counters
Page Table Walker
Update Counters

## Slide 50
PTW Cost Predictor (PTW-CP)
PTW Frequency
PTW Cost
Comparator Tree
Bypassing Logic
based on L2 cache MPKI
Costly-to-translate
page ?
Costly-to-translate
page !
Notes: If MPKI is smaller than X, just fetch all inside the cache

## Slide 51: PTW-CP Details in the Paper
Feature engineering to find
minimal set of useful features
2-feature comparator predicts costly-to-translate pages with 82% accuracy

## Slide 52: Talk Outline
Background & Motivation
Opportunity: Leverage Caches
Victima: Overview
Victima: Detailed Design
Evaluation Results

## Slide 53
Sniper Multicore Simulator extended with:
  TLB Hierarchy with multiple page sizes
  Radix page table walker
  Page walk caches
Workloads: Executed for 500M instructions
  GraphBIG: PR, BFS, BC, GC, CC
  HPCC: Randacc
  XSBench: Particle Simulation
  DLRM: Sparse-length sum
  GenomicsBench: k-mer counting
Evaluation Methodology
https://github.com/CMU-SAFARI/Victima
Notes: Add description of workloads from the paper
Add correct configurations

## Slide 54: Configurations – Native Execution
  Radix: Baseline system with 1.5K-entry L2 TLB and Transparent Huge pages enabled
  Optimistic L2 TLB-64K: System with 64K-entry L2 TLB (optimistic 12-cycle access latency)
  Optimistic L2 TLB-128K: System with 128K-entry L2 TLB (optimistic 12-cycle access latency)
  POM-TLB1: System with 64K-entry software-managed L3 TLB
  Victima
[1] Ryoo et al. “Rethinking TLB designs in virtualized environments: A very large part-of-memory TLB” ISCA 2017

## Slide 55: Performance Speedup
Victima achieves similar performance to the optimistically fast 128K-entry L2 TLB
Chart: Speedup over Baseline
| BC | BFS | CC | DLRM | GEN | GC | PR | RND | SSSP | TC | XS | GMEAN
POM-TLB 64K | 1.0238 | 1.02 | 1.0131 | 1.0175 | 1.0251 | 1.0252 | 1.0168 | 1.0013 | 1.0256 | 1.0412 | 1.051 | 1.0236
Opt. L2 TLB 64K | 1.0611 | 1.0408 | 1.033 | 1.0401 | 1.0546 | 1.0549 | 1.0551 | 1.0437 | 1.056 | 1.0576 | 1.0994 | 1.0541
Opt. L2 TLB 128K | 1.0705 | 1.0636 | 1.049 | 1.0632 | 1.0663 | 1.0665 | 1.0586 | 1.0484 | 1.074 | 1.0761 | 1.1553 | 1.0716
Victima | 1.0089 | 1.0641 | 1.0477 | 1.0637 | 1.0181 | 1.0184 | 1.0553 | 1.2824 | 1.0371 | 1.0537 | 1.1927 | 1.0738
1.28x
Notes: Rewrite this..

## Slide 56: Reduction of Page Table Walks
Victima reduces PTWs by 50%
on average compared to the baseline
Chart: Reduction of PTWs
| BC | BFS | CC | DLRM | GEN | GC | PR | RND | SSSP | TC | XS | GMEAN
POM-TLB 64K | 0.33085 | 0.38073 | 0.36989 | 0.37668 | 0.44462 | 0.44392 | 0.32563 | 0.35661 | 0.32855 | 0.28156 | 0.56858 | 0.37587
L2 TLB 64K | 0.32619 | 0.37372 | 0.36746 | 0.37558 | 0.44151 | 0.44124 | 0.32288 | 0.34916 | 0.32545 | 0.27766 | 0.56115 | 0.37175
L2 TLB 128K | 0.45347 | 0.46242 | 0.45193 | 0.46168 | 0.52201 | 0.5218 | 0.38511 | 0.56317 | 0.41976 | 0.38605 | 0.77434 | 0.48174
Victima | 0.34656 | 0.51862 | 0.50641 | 0.51856 | 0.47849 | 0.47826 | 0.53353 | 0.91662 | 0.34603 | 0.34172 | 0.90343 | 0.50662
50%

## Slide 57: Effect of L2 Cache Size on Victima
Chart: Reduction of PTWs
| BC | BFS | CC | DLRM | GEN | GC | PR | RND | SSSP | TC | XS | GMEAN
2MB | 0.34656 | 0.51647 | 0.50624 | 0.51849 | 0.47856 | 0.47838 | 0.53353 | 0.91662 | 0.34591 | 0.34172 | 0.90343 | 0.50641
4MB | 0.41747 | 0.54274 | 0.53523 | 0.54545 | 0.56034 | 0.56059 | 0.55543 | 0.99871 | 0.41105 | 0.44548 | 0.97637 | 0.56993
8MB | 0.49421 | 0.58476 | 0.58077 | 0.58651 | 0.64077 | 0.64079 | 0.59507 | 0.99953 | 0.48947 | 0.55052 | 0.98182 | 0.63142
Employing an 8MB L2 cache with Victima
reduces PTWs by 63%
63%

## Slide 58: Performance in Virtualized Environments
Chart: Speedup over NP
| BC | BFS | CC | DLRM | GEN | GC | PR | RND | SSSP | TC | XS | GMEAN
POM-TLB | 1.0477 | 1.1046 | 1.0813 | 1.105 | 1.0836 | 1.0856 | 1.0792 | 1.0158 | 1.0794 | 1.0666 | 1.1526 | 1.0815
Victima | 1.2523 | 1.2059 | 1.1844 | 1.2026 | 1.2063 | 1.2082 | 1.2713 | 1.1288 | 1.1791 | 1.1195 | 1.2931 | 1.2036
Victima outperforms 64K-entry
software-managed TLB by 12%
Notes: Add discussion about performance results

## Slide 59: Area & Power Overhead
Area and power overhead evalution using McPAT
Comparison to a high-end Intel Raptor Lake
Victima incurs 0.04% area and 0.08% power overheads

## Slide 60: More in the paper
Victima integration in virtualized environments
Maintenance operations to handle TLB shootdowns
TLB-Block-aware replacement policy
Implementation details of PTW cost estimator
Translation reach provided by Victima
https://arxiv.org/abs/2310.04158

## Slide 61: More in the paper
Victima integration in virtualized environments
Maintenance operations to handle TLB shootdowns
TLB-Block-aware replacement policy
Implementation details of PTW cost estimator
Translation reach provided by Victima
https://arxiv.org/abs/2310.04158

## Slide 62: Victima is Open Source
https://github.com/CMU-SAFARI/Victima

## Slide 63: Victima is Open Source
Documentation is available

## Slide 64: Conclusion
We present Victima, a new software-transparent scheme that drastically increases the translation reach of the processor’s TLB hierarchy by leveraging the underutilized cache resources
https://github.com/CMU-SAFARI/Victima
Key Results: Victima (i) outperforms by 5.1% a state-of-the-art software-managed TLB and (ii) achieves similar performance to an optimistically fast 128K-entry L2 TLB design without the associated area and power overheads
Key idea: Transform L2 cache blocks that store PTEs into blocks that store TLB entries
PTEs
TLB Entries
L2 Cache
Notes: Translation reach = memory coverage
Check the paper to see the right number of percents

## Slide 65: VICTIMA Drastically Increasing Translation Reach by Leveraging Underutilized Cache Resources
Konstantinos Kanellopoulos
Hong Chul Nam, Nisa Bostanci, Rahul Bera, Mohammad Sadrosadati,
Rakesh Kumar, Davide Basilio Bartolini and Onur Mutlu
https://github.com/CMU-SAFARI/Victima

## Slide 66: Adding Hardware-based L3 TLB
High access latency offsets the potential performance gains of hardware L3 TLB
Chart: Speedup over Baseline
| BC | BFS | CC | DLRM | GEN | GC | PR | RND | SSSP | TC | XS | GMEAN
L3 TLB 64K entries 15-cycle latency | 1.0318 | 1.0235 | 1.0165 | 1.0213 | 1.029 | 1.0291 | 1.0241 | 1.0106 | 1.0303 | 1.0439 | 1.0599 | 1.029
64K-20 | 1.0294 | 1.02 | 1.015 | 1.0186 | 1.0249 | 1.025 | 1.0199 | 1.0105 | 1.0253 | 1.0421 | 1.0522 | 1.0257
64K-25 | 1.0262 | 1.0166 | 1.0099 | 1.0146 | 1.0209 | 1.0212 | 1.0166 | 1.0105 | 1.0201 | 1.04 | 1.0454 | 1.0219
64K-30 | 1.0242 | 1.0099 | 1.0063 | 1.0111 | 1.0171 | 1.017 | 1.0124 | 1.0103 | 1.0151 | 1.0378 | 1.0387 | 1.0181
64K-35 | 1.0218 | 1.0069 | 1.0054 | 1.0096 | 1.0129 | 1.0131 | 1.0083 | 1.0103 | 1.0025 | 1.0356 | 1.0319 | 1.0143
64K-40 | 1.0189 | 1.0021 | 0.99979 | 1.0013 | 1.009 | 1.0091 | 1.0043 | 1.0102 | 0.99806 | 1.0331 | 1.0247 | 1.01
Cacti7.0 Estimation

## Slide 67: Reuse of TLB Blocks in L2 Cache
Chart: Breakdown of TLB Block Reuse in L2 Cache
| BC | BFS | CC | DLRM | GEN | GC | PR | RND | SSSP | TC | XS | GMEAN
Reuse 0 | 0.40789 | 0.40512 | 0.4077 | 0.40524 | 0.38962 | 0.38964 | 0.39206 | 0.34996 | 0.39704 | 0.39882 | 0.32688 | 0.38733
Reuse 1-5 | 0.01996 | 0.012008 | 0.012595 | 0.012016 | 0.021132 | 0.021129 | 0.0089985 | 0.0058321 | 0.018196 | 0.0099202 | 0.0064628 | 0.012319
Reuse 5-10 | 0.0012678 | 0.00013991 | 0.00014468 | 0.00013031 | 0.0015035 | 0.0015048 | 0.00073409 | 0.0026809 | 0.00054659 | 0.00059247 | 0.0010637 | 0.00061919
Reuse 10-20 | 0.00033762 | 3.3008e-05 | 3.4726e-05 | 2.7899e-05 | 0.00059048 | 0.0005872 | 1.0283e-05 | 0.0031905 | 0.00028419 | 0.00020962 | 0.0010116 | 0.00018233
Reuse >20 | 0.57055 | 0.5827 | 0.57953 | 0.58259 | 0.58716 | 0.58714 | 0.5982 | 0.63834 | 0.58393 | 0.59046 | 0.66458 | 0.59624
More than 60% of TLB blocks
experience reuse higher than 20
Notes: Add area comparisons and remove this plot

## Slide 68: Sensitivity to L2 Cache Replacement Policy
Employing the TLB-aware DRRIP leads to 1.8% higher performance compared to the conventional DDRIP
Chart: Speedup over DRRIP
| BC | BFS | CC | DLRM | GEN | GC | PR | RND | SSSP | TC | XS | GMEAN
TLB-Aware DRRIP | 1.0211 | 1.0229 | 1.0131 | 1.0233 | 1.0255 | 1.0165 | 1.0001 | 1.0289 | 1.0425 | 0.99615 | 1.0148 | 1.0185

## Slide 69: Page Table Walk in X86-64
9-bit
VIRTUAL ADDRESS
9-bit
9-bit
9-bit
CR3
Physical Frame Number
Four sequential memory accesses
during a page table walk in x86-64
Up to 24 memory accesses in
virtualized environments
Notes: Remove virtualized environments banner

## Slide 70: Virtualized Environments
  Two-level address translation
Guest
Virtual
Host
Virtual
Host
Physical
1
2

## Slide 71: Virtualized Environments
L2 TLB
Nested
TLB
Guest-Virtual
Host-Physical
Guest-Virtual
Host-Virtual

## Slide 72: Virtualized Environments
L2 TLB
MMU
TLB Entry
L2 Cache
Nested
TLB
Nested TLB Entry
Notes: - Remove discussion about virtualized environments

## Slide 73
PTW-CP Feature Set
Feature (per PTE) | Bits | Description
Page Size | 1 | The size of the page (4KB or 2MB)
Page Table Walk Cost | 3 | DRAM accesses during a PTW
Page Table Walk Frequency | 3 | The number of PTWs
LLPWC Hits | 5 | The number of third-level PWC hits
L1 TLB Misses | 5 | The number of L1 TLB misses
L2 TLB Misses | 5 | The number of L2 TLB hits
L2 Cache Hits | 5 | The number of L2 cache hits
L1 TLB Evictions | 5 | The number of L1 TLB evictions
L2 TLB Evictions | 6 | The number of L2 TLB evictions
Accesses | 6 | The number of accesses to the page
Feature engineering to find
minimal set of useful features
Notes: Make the table more visible

## Slide 74
PTW-CP Exploration
 | NN-10 | NN-5 | NN-2 | Comparator
Feature Size | 10 | 5 | 2 | 2
Number of Layers | 4 | 4 | 6 | N/A
Size of Hidden Layers | 16 | 64 | 4 | N/A
Number of Neurons | 737 | 8769 | 97 | N/A
Size (B) | 5896 | 70152 | 776 | 24
Recall | 0.9334 | 0.9244 | 0.8962 | 0.8961
Accuracy | 0.9213 | 0.9172 | 0.8290 | 0.8290
Precision | 0.8768 | 0.8747 | 0.7333 | 0.7334
F1-score | 0.9042 | 0.8989 | 0.8066 | 0.8066
2-feature comparator predicts costly-to-translate pages with 82% accuracy
Notes: Move to backup slides

## Slide 75: Configurations in Virtualized Environments
Nested Paging1: Baseline system that performs Nested PTWs
POM-TLB2: System with 64K-entry software-managed L3 TLB
Ideal Shadow Paging3: System that employs an ideal version of Shadow Paging
Victima: Caching both TLB and Nested TLB entries in the L2 cache
[2] Ryoo et al. “Rethinking TLB designs in virtualized environments: A very large part-of-memory TLB” ISCA 2017
[1] Bhargava et al. “Accelerating two-dimensional page walks for virtualized systems” ASPLOS 2008
[3] “Agile paging: Exceeding the best of Nested and Shadow Paging” ISCA 2016

## Slide 76: Reduction in Host and Guest PTWs
Chart: Reduction of PTWs
| BC | BFS | CC | DLRM | GEN | GC | PR | RND | SSSP | TC | XS | GMEAN
POM-TLB Guest PTW | 0.31829 | 0.37731 | 0.36841 | 0.37892 | 0.43104 | 0.43792 | 0.29793 | 0.36636 | 0.3205 | 0.28338 | 0.57301 | 0.37035
POM-TLB Host PTW | 0.28099 | 0.3449 | 0.33738 | 0.34633 | 0.35958 | 0.36145 | 0.29733 | 0.366 | 0.2401 | 0.26819 | 0.52093 | 0.33184
Victima Guest PTW | 0.32505 | 0.45525 | 0.45913 | 0.45014 | 0.40104 | 0.40795 | 0.48645 | 0.58113 | 0.28958 | 0.334 | 0.66249 | 0.42902
Victima Host PTW | 0.98292 | 0.99678 | 0.99695 | 0.99654 | 0.99044 | 0.99057 | 0.99657 | 1 | 0.98322 | 0.99651 | 0.99925 | 0.9936