## Slide 1: Virtuoso
Konstantinos Kanellopoulos Konstantinos Sgouras F. Nisa Bostanci
Andreas Kosmas Kakolyris Berkin Kerim Konar Rahul Bera
Mohammad Sadrosadati Rakesh Kumar Nandita Vijaykumar Onur Mutlu
Enabling Fast and Accurate Virtual Memory Research with an Imitation-based Operating System Simulation Methodology
https://github.com/CMU-SAFARI/Virtuoso

## Slide 2
GPUs
CPUs
NICs
Virtual
Memory

## Slide 3
GPUs
CPUs
NICs
Accelerator
Virtual Memory
is a cornerstone of
modern computing systems

## Slide 4: Does Virtual Memory come for free?

## Slide 5: Memory Allocation
Virtual memory causes high performance overheads
Address
Translation
1
2

## Slide 6: Memory Allocation Overheads
Emerging Workloads
Short Running (<1s)
Function-as-a-Service
Short-input Short-output
Large Language Model Inference
OS Memory
Allocation Routines
High spawning throughput
Time
Execution
Time spent in OS cannot be amortized due to short execution
1

## Slide 7: Physical Memory Allocation Overheads
On average 32% of execution time (measured
in a real system) spent on physical memory allocation
Chart: Fraction of total execution time (%)
| JSON | AES | IMG-RES | WCNT | DB | Llama | Bagel | Mistral | 3D Transp | Hadamard | 2D-Sum | GMEAN
Physical Memory Allocation | 81.5188 | 49.9586 | 45.7742 | 38.2381 | 92.3539 | 21.6697 | 12.5163 | 25.7039 | 12.5647 | 19.9799 | 35.9464 | 32.408

## Slide 8: Address Translation Overheads
Sparse Machine
Learning
Bioinformatics
Graph Analytics
Databases
Emerging Workloads
Long Running (>100s)
Irregular Memory Accesses
Data Fetching
TLB Miss
Page Table Walk
High Latency Address Translation
Time
2

## Slide 9: Address Translation Overheads
On average 26% of execution time (measured
in a real system) is spent on address translation
Chart: Fraction of total execution time (%)
| BC | BFS | CC | KCORE | GC | PR | SSSP | TC | XS | RND | GMEAN
Address Translation | 31.05 | 18.76 | 18.8 | 18.23 | 39.9 | 17.68 | 30.6 | 17.52 | 24.71 | 59.18 | 25.3688

## Slide 10: High VM Overheads
Chart: Fraction of execution time (%)
| AES | IMG-RES | WCNT | DB | Llama | Bagel | Mistral | Transpose | Hadamard | Mmap | Page Cache | GMEAN | BC | BFS | CC | KCORE | GC | PR | SSSP | TC | XS | RND | GMEAN | Short Running | Long Running
Address Translation | 0.81 | 1.14 | 1.58 | 1.47 | 2.02 | 0.9 | 2.47 | 0.15 | 0.18 | 0.31 | 1.19 | 0.80807 | 31.05 | 18.76 | 18.8 | 18.23 | 39.9 | 17.68 | 30.6 | 17.52 | 24.71 | 59.18 | 25.3688
Minor Page Faults | 49.9586 | 45.7742 | 38.2381 | 92.3539 | 21.6697 | 12.5163 | 25.7039 | 19.8529 | 19.9799 | 12.5023 | 50.1505 | 29.3654 | 1.6765 | 9.8911 | 12.0897 | 9.851 | 0.28334 | 9.0575 | 1.5088 | 9.0078 | 8.8042 | 14.7194 | 4.9553
VM causes high overheads
in diverse emerging workloads

## Slide 11
Virtual Memory overheads are
expected to increase as we transition
to larger physical address spaces

## Slide 12: Going into the Future
GPU Memory
CPU Memory
Unified Virtual Memory
High Bandwidth
Limited Capacity
High Capacity
Low cost/bit
1

## Slide 13: Going into the Future
GPU Memory
CPU Memory
Unified Virtual Memory
High Bandwidth
Limited Capacity
High Capacity
Low cost/bit
Direct Storage Access
High-end SSD
Byte-addressable interface
1
2

## Slide 14: Going into the Future
GPU Memory
CPU Memory
Unified Virtual Memory
High Bandwidth
Limited Capacity
High Capacity
Low cost/bit
Memory Disaggregation
Direct Storage Access
High-end SSD
Byte-addressable interface
Access to both local and remote memory modules
1
2
3

## Slide 15: Researchers try to save the day

## Slide 16
Co-design the hardware and the OS
to reduce VM overheads
Software-managed TLB Subsystem
Nagle+ ISCA 1993
Ryoo+ ISCA 2017
Marathe+ MICRO 2017
Jaleel+ TACO 2019

## Slide 17
Co-design the hardware and the OS
to reduce VM overheads
Leveraging VA-to-PA Contiguity
Software-managed TLB Subsystem
Pham+ MICRO 2012
Karakostas*,Ghandhi*+ ISCA 2015
Zhao+ ISCA 2022
Ausavarungnirun+ MICRO 2017

## Slide 18
Co-design the hardware and the OS
to reduce VM overheads
Software-managed TLB Subsystem
Accelerating Memory Allocation
Wang+ MICRO 2023
Lee+ ISCA 2020
Tirumalasetty+ TACO 2022
Leveraging VA-to-PA Contiguity

## Slide 19
Co-design the hardware and the OS
to reduce VM overheads
Leverage VA-to-PA Contiguity
Software-managed TLB Subsystem
Alternative Address Mappings
Picorel+ PACT 2016
Gosakan+ ASPLOS 2023
Kanellopoulos+ MICRO 2023
Accelerating Memory Allocation

## Slide 20
Co-design the hardware and the OS
to reduce VM overheads
Leverage VA-to-PA Contiguity
Software-managed TLB Subsystem
Accelerating Memory Allocation
Alternative Address Mappings
Rethinking the Page Table Design
Employing Multiple Page Sizes
and more...

## Slide 21
Co-design the hardware and the OS
to reduce VM overheads
Leverage VA-to-PA Contiguity
Software-managed TLB Subsystem
Accelerate Memory Allocation
Alternative Address Mappings
Rethinking the Page Table Design
Employing multiple page sizes
Wide range of hardware-OS co-design
techniques that aim to improve virtual memory

## Slide 22
Effectively evaluating VM techniques is crucial for progress in the domain

## Slide 23: Challenges in Evaluation
Interplay between system components
Hardware MMU
Software-level Memory Management
System Components

## Slide 24: Example: Page Table and Large Pages
Page Table
Size
OS Allocation Policy
Size of the page table depends on the number of large pages provided by the OS

## Slide 25: Example: Page Table and Large Pages
”I can provide plenty
of large pages”
2MB Pages
Page Table
# Entries
OS Kernel
Free

## Slide 26: Example: Page Table and Large Pages
“Fragmentation is rising so
I cannot allocate 2MB pages”
4KB Pages
Page Table
# Entries
OS Kernel

## Slide 27: Page Table and Memory Interference
DRAM Bank
Rows
Row Buffer
App 1
App 2
App 2
Page Table Entries
Program
Data
Program
Data
.
.
.
.
.
.

## Slide 28: Page Table and Memory Interference
DRAM Bank
Rows
Row Buffer
App 1
App 2
App 2
.
.
.
.
.
.
Conflict

## Slide 29: Page Table and Memory Interference
DRAM Bank
Rows
Row Buffer
App 1
App 2
App 1
.
.
.
.
.
.

## Slide 30: Page Table and Memory Interference
DRAM Bank
Rows
Row Buffer
App 1
App 2
App 1
.
.
.
.
.
.
Conflict

## Slide 31: Page Table and Memory Interference
DRAM Bank
Rows
Row Buffer
App 1
App 2
App 1
.
.
.
.
.
.
Conflict
Frequent accesses
to page table entries cause
high interference in main memory

## Slide 32: Challenges in Evaluation
Hardware MMU
Software-level Memory Management
System Components

## Slide 33: Challenges in Evaluation
Hardware MMU
Software-level Memory Management
System Components
Evaluating the interplay between components is critical when assessing current and new VM techniques

## Slide 34: Researchers have architectural simulators at their disposal

## Slide 35: Existing Architectural Simulators
Emulation-based
Full-system
1
2
Two main classes of simulators

## Slide 36: Emulation-based Simulators
Ramulator
Sniper
ChampSim
Limited support for OS primitives
ZSim
Analytically estimate
VM Overheads
High simulation speed with a focus on modeling microarchitectural features

## Slide 37: Analytical Estimation of VM Overheads
Page Table Walk Latency = 100 cycles (fixed)
Minor Page Fault Latency = 2000 cycles (fixed)
Example
First-order Models
Is this good enough?
Simple mathematical or algorithmic approximation

## Slide 38: Variable PTW Latency
Average PTW Latency (measured in a real system) ranges from 33 up to 184 cycles
Chart: 53 Benchmarks with Varying Memory Intensity Levels
 | 33.4185 | 33.5939 | 41.4149 | 43.1872 | 43.3386 | 44.0845 | 44.2789 | 45.1341 | 45.5405 | 45.8632 | 46.7314 | 46.9314 | 48.3119 | 48.9222 | 48.9642 | 50.0474 | 51.1853 | 51.4607 | 51.5388 | 53.309 | 53.347 | 53.5019 | 55.1829 | 56.0908 | 58.848 | 59.0667 | 60.4439 | 60.8051 | 62.9218 | 64.2463 | 65.4819 | 67.7023 | 68.4531 | 69.4164 | 71.7254 | 73.6908 | 76.0648 | 77.757 | 79.362 | 80.0731 | 80.1896 | 84.1811 | 93.5784 | 94.9767 | 96.3801 | 96.6924 | 99.293 | 144.4437 | 151.81 | 152.0026 | 159.2114 | 163.558 | 184.5915
High Memory
Intensity
Low Memory Intensity

## Slide 39: Variable Memory Allocation Latency
THP
Enabled
THP
Disabled
Physical Memory Allocation Latency (μs) in Log Scale
Contribution of outliers to total minor page fault latency: 25%
Contribution of outliers to total memory allocation latency: 67%
Median
25th
percentile
75th percentile
Notes: In this experiment, we measured the memory allocation latency using ftrace with THP disabled and enabled.

## Slide 40: Variable Memory Allocation Latency
The latency of handling memory allocation
(measured in a real system)
exhibits high variability
THP
Enabled
THP
Disabled
Physical Memory Allocation Latency (μs) in Log Scale
Contribution of outliers to total minor page fault latency: 25%
Contribution of outliers to total memory allocation latency: 67%
Notes: The contribution of the outlier values (above seventy-fifth percentile) is 67% of the total latency.

## Slide 41: Variable Memory Allocation Latency
The latency of handling memory allocation
(measured in a real system)
exhibits high variability
THP
Enabled
THP
Disabled
Physical Memory Allocation Latency (μs) in Log Scale
Contribution of outliers to total minor page fault latency: 25%
Contribution of outliers to total memory allocation latency: 67%
Notes: In contrast, outliers with THP disabled, contribute only by 25% to the total latency.

## Slide 42: Analytical Estimation of VM Overheads
Use of First-order Models
First-order models do not accurately
capture the dynamic nature of VM overheads

## Slide 43: Full-System Simulators
gem5-FS
QFlex
PTLsim
Enable the execution of a full-blown OS
on top of a hardware simulator
Low simulation speed
Hard to develop

## Slide 44: Existing Architectural Simulators
Emulation-based
Full-System
1
2
Two main classes of simulators

## Slide 45: Existing Architectural Simulators
Dichotomy
Emulation-based
Simulation Speed
Accuracy in Estimating VM overheads
Full-System

## Slide 46: Existing Architectural Simulators
Emulation-based
Simulation Speed
Accuracy in Estimating VM overheads
Our goal
Full-System

## Slide 47: Enabling Fast and Accurate VM Research
New simulation framework that enables
fast and accurate prototyping and evaluation of
the software and hardware components of VM
Virtuoso

## Slide 48: Imitation-based Simulation Methodology
Lightweight Userspace Kernel
written in a high-level programming language
Choose OS modules only related
to the desired research
“I will try to imitate
the full-blown OS”

## Slide 49: Imitation-based Simulation Methodology
Full-blown Kernel
Thread Scheduler
Data Sharing Support
Managing NUMA
Virtual Memory Area Handling
Block device driver
Protection
Transparent Huge Pages
hugetlbfs
Cgroups
SLAB Allocator
Swapping
Interrupts
Monitoring
Boot process

## Slide 50: Imitation-based Simulation Methodology
Lightweight Userspace Kernel
Virtual Memory Area Handling
Transparent Huge Pages
Swapping

## Slide 51: Imitation-based Simulation Methodology
Rapid development and prototyping
High simulation speed by executing
only the desired OS kernel functionality
Accurate evaluation by integrating
Virtuoso with an architectural simulator
1
2
3

## Slide 52: Imitation-based Simulation Methodology
add R1, R1 ,R2
load R1, [0xA]
Lightweight Userspace Kernel
Desired Memory Management modules written in a high-level language
Simulator
Binary Instrumentation
Core Model
Userspace Kernel Instruction Stream
+ Imitates the OS-level
Overhead

## Slide 53: Imitation-based Simulation Methodology
add R1, R1 ,R2
load R1, [0xA]
Lightweight Userspace Kernel
Desired Memory Management modules written in a high-level language
Simulator
Binary Instrumentation
Core Model
Userspace Kernel Instruction Stream
Functional Outcome
+ Enables emulation of kernel modules

## Slide 54: Workflow: Page Fault Handling Example
Example Userspace Kernel
Page Fault Handler
Transparent Huge Pages
Buddy Allocator

## Slide 55: Workflow: Page Fault Handling Example
Core
Model
Example: Sniper Simulator [Carlson+ TACO 12]
MMU
Model
Translation Request
Example Userspace Kernel
Workload
2
Memory
Access
3
4
5
Page Fault Handler
1
Binary Instrumentation
Page Fault
6
7
8

## Slide 56: Workflow: Page Fault Handling Example
Core
Model
Example: Sniper Simulator [Carlson+ TACO 12]
MMU
Model
Translation Request
Example Userspace Kernel
Workload
Memory
Access
Page Fault Handler
Page Fault
Outcome

## Slide 57: MimicOS: Imitating the Linux Kernel
MimicOS modules written in C++
Transparent Huge Pages
Buddy Allocator
Radix-based page table
hugetlbfs
Swap Space
Page Cache
More details in the paper
https://arxiv.org/pdf/2403.04635

## Slide 58: VirTool: State-of-the-art VM techniques
Nested MMU
Support
4 page table designs
2 THP Policies
2 Hash-based address mapping schemes
2 Memory Tagging Schemes
Software-Managed TLB
2 Contiguity-aware Schemes
Page-Size Prediction
2 Intermediate Address Space Schemes
Toolset encompassing the HW/SW components
of multiple state-of-the-art VM techniques
Speculative Translation
TLB Prefetching

## Slide 59: VirTool: State-of-the-art VM techniques
Nested MMU
Support
4 page table designs
2 THP Policies
2 Hash-based mapping schemes
2 Memory Tagging Schemes
Software-Managed TLB
2 Contiguity-aware Schemes
Page-Size Prediction
2 Intermediate Address Space Schemes
Toolset encompassing multiple state-of-the-art VM techniques
Enables researchers to evaluate
and prototype current and
brand new VM techniques

## Slide 60: VirTool: State-of-the-art VM techniques
Nested MMU
Support
4 page table designs
2 THP Policies
2 Hash-based mapping schemes
2 Memory Tagging Schemes
Software-Managed TLB
2 Contiguity-aware Schemes
Page-Size Prediction
2 Intermediate Address Space Schemes
Toolset encompassing multiple state-of-the-art VM techniques
Virtuoso is a highly versatile
simulation framework

## Slide 61
Integrated Virtuoso with 5 Diverse
Architectural Simulators
gem5-SE
System-call emulation
mode of gem5
http://gem5.org/
[Lowe-Power+ arXiv 2020]
[Binkert+ SIGARCH News 2011]

## Slide 62
Integrated Virtuoso with 5 Diverse
Architectural Simulators
gem5-SE
Ramulator
Focus on main memory subsystem
https://github.com/CMU-SAFARI/ramulator2
[Luo+ CAL 2023]

## Slide 63
Integrated Virtuoso with 5 Diverse
Architectural Simulators
gem5-SE
Ramulator
Sniper
Focus on
multicore systems
[Carlson+ TACO 2012]
https://github.com/snipersim/snipersim

## Slide 64
Integrated Virtuoso with 5 Diverse
Architectural Simulators
gem5-SE
Ramulator
Sniper
ChampSim
Focus on
microarchitecture
https://github.com/ChampSim/ChampSim
[Gober+ arXiv 2022]

## Slide 65
Integrated Virtuoso with 5 Diverse
Architectural Simulators
gem5-SE
Ramulator
Sniper
ChampSim
MQSim
Focus on
storage devices
[Tavakkol+ FAST 2018]
https://github.com/CMU-SAFARI/MQSim

## Slide 66: Validation against a Real System
Virtuoso
Sniper
High-end
Server-grade
CPU
Against
Linux Kernel

## Slide 67: Validation: Instructions Per Cycle (IPC)
Virtuoso integrated with Sniper improves
IPC modeling accuracy by 21%
compared to baseline Sniper
Chart: IPC Modeling Accuracy
| BC | BFS | CC | KCORE | GC | PR | SSSP | TC | XS | GMEAN
Baseline Sniper | 0.32663 | 0.50198 | 0.95992 | 0.84968 | 0.60465 | 0.56965 | 0.74747 | 0.86354 | 0.78095 | 0.6583
Virtuoso + Sniper | 0.69304 | 0.42896 | 0.76148 | 0.97236 | 0.76519 | 0.85278 | 0.83465 | 0.94964 | 0.96474 | 0.78237
gem5-FS | 0.91 | 0.88 | 0.895 | 0.86 | 0.875 | 0.905 | 0.855 | 0.89 | 0.85 | 0.87976

## Slide 68: Validation: Instructions Per Cycle (IPC)
Virtuoso integrated with Sniper achieves IPC modeling accuracy within 9% of gem5-FS
Chart: IPC Modeling Accuracy
| BC | BFS | CC | KCORE | GC | PR | SSSP | TC | XS | GMEAN
Baseline Sniper | 0.32663 | 0.50198 | 0.95992 | 0.84968 | 0.60465 | 0.56965 | 0.74747 | 0.86354 | 0.78095 | 0.6583
Virtuoso + Sniper | 0.69304 | 0.42896 | 0.76148 | 0.97236 | 0.76519 | 0.85278 | 0.83465 | 0.94964 | 0.96474 | 0.78237
gem5-FS | 0.91 | 0.88 | 0.895 | 0.86 | 0.875 | 0.905 | 0.855 | 0.89 | 0.85 | 0.87976

## Slide 69: Validation: Page Fault Handling Latency
Virtuoso integrated with Sniper models the
page fault handling latency with 66% accuracy,
within 15% of gem5-FS
Chart: Page Fault Modeling Accuracy
| JSON | AES | DB | WCNT | IMG-RES | LLMs | 3D Transp | Hadamard | 2D Sum | GMEAN
Virtuoso+Sniper | 0.65494 | 0.68976 | 0.60379 | 0.59682 | 0.70254 | 0.5735 | 0.80392 | 0.70863 | 0.67864 | 0.66478
gem5-FS | 0.84 | 0.78 | 0.86 | 0.8 | 0.82 | 0.81 | 0.85 | 0.79 | 0.83 | 0.81959

## Slide 70: Simulation Speed Comparison
Chart: Slowdown over Baseline Simulators
| ChampSim | Sniper | Ramulator | Gem5-SE | AVG
with MimicOS | 0.13 | 0.35 | 0.02 | 0.28 | 0.195
ChampSim
Sniper
Ramulator
gem5
GMEAN
MimicOS leads to an average 20% simulation time overhead over the baseline version of the simulator

## Slide 71: Simulation Speed Comparison
Chart: Slowdown over Baseline Simulators
| ChampSim | Sniper | Ramulator | Gem5-SE | AVG
with MimicOS | 0.13 | 0.35 | 0.02 | 0.28 | 0.195
with Full-blown Linux Kernel | 0.77
ChampSim
Sniper
Ramulator
gem5
GMEAN
Enabling full-system execution mode in gem5
leads to 77% simulation time overhead

## Slide 72: Virtuoso’s Versatility
We showcase Virtuoso’s
versatility by evaluating multiple
different use cases
5 use cases in the paper
https://arxiv.org/pdf/2403.04635
Demonstrate new insights on
state-of-the-art VM techniques

## Slide 73: Virtuoso Example Use Cases
Evaluating Different
Page Table Designs
Evaluating Physical Memory
Allocation Policies

## Slide 74: Virtuoso Example Use Cases
Evaluating Different
Page Table Designs
Evaluating Physical Memory
Allocation Policies

## Slide 75: Evaluation Methodology
Radix: Baseline radix-based page table
ECH1: Elastic Cuckoo Hash-based Page Table
Fragmentation: Number of available 2MB pages
compared to the total number of 2MB pages
[1] Skarlatos et al. “Elastic Cuckoo Page Tables: Rethinking Virtual Memory Translation for Parallelism” ASPLOS 2020
Workloads: GraphBIG, XSBench, HPCC

## Slide 76: Reduction in PTW Latency
As memory fragmentation decreases, the PTW
latency reduction of ECH compared to Radix increases
Chart: Memory Fragmentation Level
| 1 | 0.98 | 0.96 | 0.94 | 0.92 | 0.9
Radix | 0 | 0.1121 | 0.14623 | 0.17665 | 0.20205 | 0.22241
ECH | 0.060588 | 0.19541 | 0.2358 | 0.27035 | 0.30218 | 0.33282
11%
6%

## Slide 77: Main Memory Interference
Chart: Normalized DRAM Row Buffer Conflicts
| BC | BFS | CC | GC | KC | PR | RND | SP | TC | XS | GMEAN
ECH | 1.3289 | 1.4017 | 1.3797 | 1.6951 | 1.2466 | 1.2638 | 2.5032 | 2.7943 | 1.4331 | 1.0078 | 1.5279
ECH leads to an average 52% increase
in DRAM row buffer conflicts over Radix
2.5x
2.7x
52%

## Slide 78: Virtuoso Example Use Cases
Evaluating Different
Page Table Designs
Evaluating Physical Memory
Allocation Policies

## Slide 79: Evaluation Methodology
Buddy: Baseline allocator with the buddy system
Utopia:1 Part of memory is organized using a hash-based mapping
Workloads: Short-input Short-output LLM inference
[1] Kanellopoulos et al. “Utopia: Fast and Efficient Address Translation via Hybrid Restrictive & Flexible Virtual-to-Physical Address Mappings” MICRO 2023
Mistral-7B
Llama-2-7B
Bagel-2.8B

## Slide 80: Accelerating Memory Allocation
Chart: Physical Memory Allocation Speedup
| Llama-2-7B | Mistral-7B | Bagel-2.8B
Utopia - 32MB Hash-based Segment | 2.0419 | 2.179 | 2.1783
Restricting the virtual-to-physical mapping speeds up memory allocation by up to 2.17x

## Slide 81: More Details in the Paper
- Detailed description of communication primitives
- Detailed description of MimicOS modules
- Integration methodology with different simulators
- Integration with heterogeneous system simulation
- Evaluation of intermediate address space schemes
- Evaluation of swapping activity and translation latency in hash-based address mapping schemes
- Evaluation of two additional hash-based page tables
and more to come …

## Slide 82: More Details in the Paper
- Detailed description of communication primitives
- Detailed description of MimicOS modules
- Integration methodology with different simulators
- Evaluation of intermediate address space schemes
- Evaluation of swapping activity and translation latency in hash-based address mapping schemes
- Evaluation of two additional hash-based page tables
https://arxiv.org/pdf/2403.04635

## Slide 83: Virtuoso is Open-Source
https://github.com/CMU-SAFARI/Virtuoso

## Slide 84: Virtuoso Website – Getting Started
https://github.com/CMU-SAFARI/Virtuoso/website

## Slide 85: Virtuoso Website - Documentation
https://safari.ethz.ch/virtuoso

## Slide 86: Virtuoso Website – Incoming Features
https://safari.ethz.ch/virtuoso

## Slide 87: Conclusion

## Slide 88
VM causes high overheads
in emerging workloads

## Slide 89
New simulation framework that enables
fast and accurate prototyping and evaluation of
the software and hardware components of VM
Virtuoso
https://github.com/CMU-SAFARI/Virtuoso

## Slide 90: Imitation-based Simulation Methodology
Rapid development and versatility
High simulation speed
Accurate simulation
1
2
3

## Slide 91
Validation against high-end server-grade CPU
Implemented 5 diverse use cases to
showcase Virtuoso’s versatility
VirTool
Integration with 5 simulators
Toolset encompassing multiple state-of-the-art VM techniques
gem5-SE
Ramulator
Sniper
ChampSim
MQSim
https://github.com/CMU-SAFARI/Virtuoso

## Slide 92
We hope Virtuoso establishes a
common ground for VM research

## Slide 93: Virtuoso
Konstantinos Kanellopoulos Konstantinos Sgouras F. Nisa Bostanci
Andreas Kosmas Kakolyris Berkin Kerim Konar Rahul Bera
Mohammad Sadrosadati Rakesh Kumar Nandita Vijaykumar Onur Mutlu
Enabling Fast and Accurate Virtual Memory Research with an Imitation-based Operating System Simulation Methodology
https://github.com/CMU-SAFARI/Virtuoso
Github
arXiv

## Slide 94: Why do we need Virtual Memory?

## Slide 95
Programmer-transparent
memory management
Process isolation
Data sharing between processes
1
2
3
Virtual Memory Benefits

## Slide 96: How does Virtual Memory work?

## Slide 97
Physical Address Space (e.g., physical memory)
Virtual Address Space #1
Virtual Address Space #2
App 1
App 2

## Slide 98
Page
Page
Physical Address Space (e.g., physical memory)
Virtual Address Space #1
Virtual Address Space #2
App 1
App 2
Page
Page
Page
Page
Page
Page
Page
(e.g., 4KB)

## Slide 99
Physical Address Space
Virtual Address Space #1
Virtual Address Space #2
App 1
App 2

## Slide 100
Physical Address Space
Virtual Address Space #1
Virtual Address Space #2
App 1
App 2
Virtual-to-Physical Address Mapping

## Slide 101: Who establishes virtual-to-physical address mappings?

## Slide 102
Physical Memory
Virtual Address Space
App
Map virtual addresses
to physical memory

## Slide 103
Virtual Address Space
Physical Address Space
Fault
Virtual address
not mapped to
physical memory

## Slide 104
Operating
System
Physical Memory
Handles memory allocation
Virtual Address Space
App

## Slide 105
Operating System
Finds free space in
physical memory
Fetches data
from the disk
Application is stalled
Minor Fault
Major Fault

## Slide 106
Virtual Address Space
Operating
System
Physical Memory
Page Table
Store/Update the
virtual-to-physical address mapping

## Slide 107: How does the CPU discover the virtual-to-physical mapping?

## Slide 108
Memory Hierarchy
Core
Memory
Management Unit
Virtual
Address
Address Translation
Page
Table
Hardware unit responsible
for address translation

## Slide 109
TLB Hierarchy
Page Table Walker
Miss
Memory Hierarchy
Memory Management Unit
Page
Table
Address Translation
Notes: [1] There is a two level TLB-hierarchy.
[2] If we miss in the TLB, we trigger the page table walk
[3] We search in the page walk caches for intermediate levels

## Slide 110: Validation against a Real System
MMU Performance
Validation Metrics
InstructionsPer Cycle
Page Fault Latency
Virtuoso
Sniper
High-end
Server-grade
CPU

## Slide 111: Validation: L2 TLB MPKI
Virtuoso integrated with Sniper models
the L2 TLB misses per kilo instructions
of a real high-end CPU with 82% accuracy
Chart: L2 TLB MPKI Modelling Accuracy
| BC | BFS | CC | KCORE | GC | PR | SSSP | TC | XS | GMEAN
 | 0.86568 | 0.72775 | 0.78091 | 0.99927 | 0.83869 | 0.55912 | 0.76774 | 0.99996 | 0.9526 | 0.82053
82%

## Slide 112: Validation: Page Table Walk Latency
Chart: PTW Latency Modelling Accuracy
| BC | BFS | CC | KCORE | GC | PR | SSSP | TC | XS | GMEAN
Accuracy | 0.7143 | 0.889 | 0.80202 | 0.99204 | 0.92742 | 0.93685 | 0.95403 | 0.89357 | 0.65841 | 0.85586
86%
Virtuoso integrated with Sniper models the
Page Table Walk latency of a real high-end CPU
with 86% accuracy

## Slide 113: Instructions vs Simulation Time
Chart: 
| 5.0156460211174103 | 16.2252377409507 | 22.302859914450568 | 44.333219208898193
Execution time | 1.1488 | 1.5717 | 1.796 | 2.612
Fraction of Instructions Executed by MimicOS
Normalized
Simulation Time
y=1.5x
y
x
Linear relationship between instructions
executed by MimicOS and simulation time