## Slide 1: A Case for Richer Cross-layer Abstractions: Bridging the Semantic Gap with Expressive Memory
Nandita Vijaykumar
Abhilasha Jain, Diptesh Majumdar, Kevin Hsieh, Gennady Pekhimenko
Eiman Ebrahimi, Nastaran Hajinazar, Phillip B. Gibbons, Onur Mutlu

## Slide 2
HW-SW Interfaces
(ISA & Virtual Memory)
Software
Hardware
Functionality
Performance?
SW Optimization
HW Optimization

## Slide 3: Higher-level information is not visible to HW
Data Structures
Code Optimizations
Access Patterns
Integer
Float
Char
Data Type
Instructions
Memory Addresses
100011111…
101010011…
Hardware
Software

## Slide 4
ISA
Virtual Memory
Expressive
Memory
“XMem”
Higher-level
Program
Semantics
Performance
Functionality
Software
Hardware

## Slide 5: Outline
Why do we need a richer cross-layer abstraction?
Designing Expressive Memory (XMem)
Evaluation (with a focus on one use case)

## Slide 6: Performance optimization in hardware

## Slide 7: What we do today: We design hardware to infer and predict program behavior to optimize for performance
Caches
Memory Controllers
Prefetchers

## Slide 8: With a richer abstraction: SW can provide program information can significantly help hardware
Data Structures
Access Patterns
Integer
Float
Char
Data Type/Layout
Hardware
Software
Prefetcher
Data Compression
Data Placement

## Slide 9: Benefits of a richer abstraction:
Optimizations:
Cache Management
Data Placement in DRAM
Data Compression
Approximation
DRAM Cache Management
NVM Management
NUCA/NUMA Optimizations
….
Express:
Data structures
Access semantics
Data types
Working set
Reuse
Access frequency
…..

## Slide 10: Optimizing for performance in software

## Slide 11: What we do today: Use platform-specific optimizations to tune SW
Example: SW-based cache optimizations
Tune working set
8MB cache
6MB cache
SW optimizations make assumptions regarding HW resources
Significant portability and programmability challenges

## Slide 12: With a richer interface: HW can alleviate burden on SW
Working set
Reuse
SW only expresses program information
System/HW handles
optimizing for specific system details
e.g. exact cache size, memory organization,
NUMA organization

## Slide 13: Benefits of a richer abstraction:
Optimizations:
Cache Management
Data Placement in DRAM
Data Compression
Approximation
DRAM Cache Management
NVM Management
NUCA/NUMA Optimizations
….
Performance
Express:
Data structures
Access semantics
Data types
Working set
Reuse
Access frequency
…..
HW optimizations
Programmability
Portability
SW optimizations

## Slide 14: SW information in HW is proven to be useful, but..
Lots of research on hints/directives to hardware and HW-SW co-designs
Cache hints, Prefetcher hints, Annotations for data placement, …
Downsides:
Not scalable – can’t add new instructions for each optimization
Not portable – make assumptions about underlying resources
These downsides significantly limit adoption of otherwise useful approaches

## Slide 15
Design a rich, general, unifying abstraction
between HW and SW for performance
Our Goal:

## Slide 16: Outline
Why do we need a richer cross-layer abstraction?
Designing Expressive Memory (XMem)
Evaluation (with a focus on one use case)

## Slide 17: Key design goals
Supplemental and hint-based only
General and extensible
Architecture-agnostic
Low overhead

## Slide 18: An Overview of Expressive Memory
Interface to Application
Interface to System/Architecture
DRAM Cache
OS
. . .
Prefetcher
Memory Controller
Caches
Application
Expressive
Memory
System to summarize and save program information

## Slide 19: Challenge 1: Generality and architecture-agnosticism
Interface to Application
Interface to System/Architecture
DRAM Cache
OS
. . .
Prefetcher
Memory Controller
Caches
Application
Expressive
Memory
Data structures,
data type, access patterns, …
What to prefetch?
Which data to cache?
General,
High-level
Architecture-specific, Low-level

## Slide 20: Challenge 2: Tracking changing program properties with low overhead
Application
Expressive Memory
System/Architecture
Program behavior keeps changing:
Data structures are accessed differently in different phases
New data structures are allocated
We want to convey lots of information!
Dynamic interface that continually tracks program behavior
Potentially very high storage/communication overhead at run time

## Slide 21: A new HW-SW abstraction
Software
Hardware
Atom:1
Application
Atom: 2
Atom: 3
System/Architecture
Memory
Region
Memory
Region
Memory
Region

## Slide 22: The Atom: A closer look
A hardware-software abstraction to convey program semantics
Atom: X
Program
Attributes
Mapping
State
Valid/invalid at current execution point
Unique Atom ID
Atom
Data Value Properties:
  INT, FLOAT, CHAR,…
  COMPRESSIBLE, APPROXIMABLE
Access Properties:
  Read-Write Characteristics
  Access Pattern
  Access Intensity (“Hotness”)
3) Data Locality:
Working Set
Reuse
4) ….

## Slide 23: The three Atom operators
Atom
Atom
Program
Attributes
Mapping
State
1) CREATE
2) MAP/UNMAP
3) ACTIVATE/DEACTIVATE

## Slide 24: Using Atoms to express program semantics
A = malloc ( size );
Atom1 = CreateAtom( “INT”, “Regular”, …);
MapAtom( Atom1, A, size );
ActivateAtom(Atom1);
….
….
Atom2 = CreateAtom( “INT”, “Irregular”, …);
UnMapAtom( Atom1, A, size);
MapAtom( Atom2, A, size );
ActivateAtom(Atom2);
Memory Region A
(3D Array)
Atom: 1
Attributes cannot be changed
Atom: 2

## Slide 25: Implementing the Atom
Compile Time (CREATE)
Load Time (CREATE)
Run Time (MAP and ACTIVATE)

## Slide 26: Compile Time (CREATE)
Atom: 1
Program
Attributes 1
Atom Segment
in Object File
Atom: 2
Program
Attributes 2
Compiler
A = malloc ( size );
Atom1 = CreateAtom( “INT”, “Regular”, …);
MapAtom( Atom1, A, size );
ActivateAtom(Atom1);
….
….
Atom2 = CreateAtom( “INT”, “Irregular”, …);
UnMapAtom( Atom1, A, size);
MapAtom( Atom2, A, size );
ActivateAtom(Atom2);
Compiler
High overhead operations are handled at compile time

## Slide 27: Load Time (CREATE)
Atom Segment
in Object File
Atom ID
Attributes
OS
Cache
Controllers
Attribute Translator
Prefetcher
Memory Controller
…
Architecture-agnostic,
general
Architecture-specific,
low-level

## Slide 28: Run Time (MAP and ACTIVATE)
A = malloc ( size );
Atom1 = CreateAtom( “INT”, “Regular”, …);
MapAtom( Atom1, A, size );
ActivateAtom(Atom1);
….
….
Atom2 = CreateAtom( “INT”, “Irregular”, …);
UnMapAtom( Atom1, A, size);
MapAtom( Atom2, A, size );
ActivateAtom(Atom2);
New insts in ISA
DRAM Cache
OS
. . .
Prefetcher
Memory Controller
Caches
Application
Expressive
Memory
Design challenge:
How to do this with low overhead?

## Slide 29: Outline
Why do we need a richer cross-layer abstraction?
Designing Expressive Memory (XMem)
Evaluation (with a focus on one use case)

## Slide 30: A fresh approach to traditional optimizations
Optimizations:
Cache Management
Data Placement in DRAM
Data Compression
Approximation
DRAM Cache Management
NVM Management
NUCA/NUMA Optimizations
….
Performance
Express:
Data structures
Access semantics
Data types
Working set
Reuse
Access frequency
…..
HW optimizations
Programmability
Portability
SW optimizations

## Slide 31: Use Case 1: Improving portability of SW cache optimization
SW-based cache optimizations try to fit the working set in the cache
Examples: hash-join partitioning, cache tiling, stencil pipelining
machine learning, computer vision, numerical analysis, etc.)
A
B
C

## Slide 32: Methodology (Use Case 1)
Evaluation Infrastructure: Zsim, DRAMSim2
Workloads: Polybench
System Parameters:
Core: 3.6 GHz, Westmere-like OOO, 4-wide issue, 128-entry ROB
L1 Cache: 32KB Inst and 32KB Data, 8 ways, 4 cycles, LRU
L2 Cache: 128KB private per core, 8 ways, 8 cycles, DRRIP
L3 Cache: 8MB (1MB/core, partitioned), 16 ways, 27 cycles, DRRIP
Prefetcher: Multi-stride prefetcher at L3, 16 strides
Memory: DRAM DDR3-1066, 2 channels, 1 rank/channel, 8 banks/rank, 17GB/s
(2.1GB/s/core), FR-FCFS, open-row policy

## Slide 33: Correctly sizing the working set is critical
Chart: 
| 256 | 2048 | 8192 | 16384
Baseline | 1 | 0.6971 | 0.71265 | 1.2117
Gemm
Tile Size (kB)
Execution
Time
Bigger is better
(more reuse)
71%
Cache Thrashing
Optimal tile size depends on available cache space:
This causes portability and programmability challenges

## Slide 34: Leveraging Expressive Memory for cache tiling
Map tile to an atom, specifying high reuse and tile size
If tile size < available cache space: default policy
If tile size > available cache space: pin a part of the tile, prefetch the rest (avoid thrashing)
SW expresses program-level semantic information
HW manages cache space to optimize for performance

## Slide 35: Cache tiling with Expressive Memory
Chart: 
| 256 | 2048 | 8192 | 16384
Baseline | 1 | 0.6971 | 0.71265 | 1.2117
XMem | 1.0052 | 0.69645 | 0.70306 | 0.81824
Gemm
Tile Size (kB)
Execution
Time
Knowledge of locality semantics enables more intelligent cache management
Improves portability and programmability
47%

## Slide 36: Results across more workloads
Chart: 
| 64 | 8192 | 65536 | 131072
 | 1 | 0.78587 | 0.82754 | 1.2066
 | 0.8476 | 0.78304 | 0.81794 | 0.8606
Chart: 
| 256 | 32768 | 65536 | 131072
 | 1 | 0.81678 | 0.84687 | 1.1092
 | 0.58184 | 0.56653 | 0.56332 | 0.5692
Chart: 
| 1024 | 4096 | 16384 | 65536
 | 1 | 1.5871 | 1.6052 | 1.6596
 | 0.89366 | 1.1122 | 1.1475 | 1.1591
Chart: 
| 8 | 64 | 65536 | 131072
 | 1 | 0.81419 | 0.88466 | 1.4674
 | 0.97774 | 0.79743 | 0.85046 | 1.1604
Chart: 
| 16384 | 262144 | 524288 | 1048576
 | 1 | 0.92845 | 0.9753 | 0.99602
 | 0.96025 | 0.80498 | 0.79473 | 0.79346
Chart: 
| 256 | 16384 | 262144 | 524288
 | 1 | 0.81797 | 2.9036 | 6.1878
 | 0.83116 | 0.77962 | 1.7668 | 3.6194
Chart: 
| 128 | 8192 | 16384 | 32768
 | 1 | 0.4985 | 0.48915 | 0.72669
 | 0.76425 | 0.48802 | 0.48014 | 0.56707
Normalized Exec. Time
Tile Size in kB
Expressive Memory
Baseline
Chart: 
| 256 | 65536 | 131072 | 262144
 | 1 | 0.84076 | 0.84649 | 1.1042
 | 1.0006 | 0.85473 | 0.84927 | 0.87974
Chart: 
| 256 | 2048 | 8192 | 16384
Baseline | 1 | 0.6971 | 0.71265 | 1.2117
XMem | 1.0052 | 0.69645 | 0.70306 | 0.81824
Chart: 
| 8192 | 16384 | 32768 | 65536
Baseline | 1 | 1.4246 | 1.516 | 1.5312
XMem | 0.98877 | 1.1219 | 1.1455 | 1.2302
Chart: 
| 64 | 512 | 1024 | 4096
 | 1 | 0.68184 | 0.88819 | 1.0205
 | 0.80846 | 0.58166 | 0.41872 | 0.38926
Chart: 
| 8192 | 16384 | 32768 | 65536
 | 1 | 0.9608 | 0.95357 | 0.9767
 | 0.7045 | 0.70865 | 0.70859 | 0.70932

## Slide 37: More in the paper
Use Case 2: Leveraging data structure semantics to enable more intelligent OS-based page placement
More details on the implementation
Overhead analysis
Other use cases of XMem

## Slide 38: Conclusion
ISA
Virtual Memory
Expressive
Memory
“XMem”
Higher-level
Program
Semantics
Software
Hardware
General and architecture-agnostic interface to SW to express program semantics
Key program information to aid system/HW components in optimization

## Slide 39: A Case for Richer Cross-layer Abstractions: Bridging the Semantic Gap with Expressive Memory
Nandita Vijaykumar
Abhilasha Jain, Diptesh Majumdar, Kevin Hsieh, Gennady Pekhimenko
Eiman Ebrahimi, Nastaran Hajinazar, Phillip B. Gibbons, Onur Mutlu