## Slide 1: Optimizing DRAM Timing for the Common-Case
Donghyuk Lee
Yoongu Kim, Gennady Pekhimenko, Samira Khan,
Vivek Seshadri, Kevin Chang, Onur Mutlu
Adaptive-Latency DRAM
Notes: Hello, my name is Donghyuk Lee.
Today, I will talk about “Adaptive-Latency DRAM which optimizes DRAM timings for the common-case”.
This work is done in collaboration with my co-authors from Carnegie Mellon University.

## Slide 2
(11 – 11 – 28)
Timing Parameters
DRAM Module
x86 CPU
DDR3 1600MT/s (11-11-28)
SPEC
mcf
Runtime: 527min
Runtime: 477min
-10.5% (no error)
(8 – 8 – 19)
MemCtrl
Parsec
GUPS
Memcached
Apache
Notes: A system consists of a processor and DRAM based-memory system that are connected by memory channel.
DRAM has many timing parameters as minimum number of clock cycles between commands.
Memory controller follows these timing parameters when accessing DRAM.
We execute a benchmark with using the standard timing parameters.
Then, we intentionally reduce the timing parameters and execute same benchmark again.
When comparing these two cases, we observe significant performance improvement by reducing timing parameters, for example, 10% performance improvement for spec mcf benchmark.
Without any errors.-----

## Slide 3: Reducing DRAM Timing
Why can we reduce DRAM timing parameters without any errors?
Notes: I will mostly talk about reducing DRAM timing parameters.
Before explaining the details of our work, I would provide high level questions and our answers.
First question is why reducing DRAM timing parameters works?
Our observation is that DRAM timing parameters are overly conservative and
dictated by the slowest DRAM chip at the highest operating temperature.
Second question is how much we can reduce DRAM timing parameters?
Our DRAM latency characterization shows that it depends on the operating temperature and DRAM chip.
Third question is whether this approach is safe?
Our answer is Yes.
We exploit only the extra margin in timing parameters.
We perform 33 day long evaluation with reduced timing parameters and observed no errors.
Let me explain details about our work.

## Slide 4
Executive Summary
Observations
  DRAM timing parameters are dictated by the worst-case cell (smallest cell across all products at highest temperature)
  DRAM operates at lower temperature than the worst case
Idea: Adaptive-Latency DRAM
  Optimizes DRAM timing parameters for the common case (typical DIMM operating at low temperatures)
Analysis: Characterization of 115 DIMMs
  Great potential to lower DRAM timing parameters (17 – 54%) without any errors
Real System Performance Evaluation
  Significant performance improvement (14% for memory-intensive workloads) without errors (33 days)
Notes: Let me conclude
DRAM timing parameters are dictated by the worst case cell.
We propose Adaptive-Latency DRAM that optimizes DRAM timing parameters for common cases
Our characterization shows the significant potential to lower DRAM timing parameters.
Our real system evaluation shows that our mechanism provides significant performance improvement without introducing errors.

## Slide 5
1. DRAM Operation Basics
2. Reasons for Timing Margin in DRAM
4. Adaptive-Latency DRAM
5. DRAM Characterization
6. Real System Performance Evaluation
3. Key Observations
Notes: This is the outline. I will first briefly explain DRAM operation and two reasons of timing margin in DRAM.
Then, we will talk about our three key mechanisms and propose our mechanism, Adaptive-Latency DRAM.
Then, we will provide the DRAM latency characterization results and real system performance evaluation results.
Let me start from DRAM operation.

## Slide 6
DRAM Stores Data as Charge
1. Sensing
2. Restore
3. Precharge
DRAM Cell
Sense-Amplifier
Three steps of charge movement
Notes: The right figure shows DRAM organization which is consists of DRAM cells and sense-amplifiers.
There are three steps for accessing DRAM.
First, when DRAM selects one of rows in its cell array, the selected cells drive their charge to sense-amplifiers.
Then, sense-amplifiers detect the charge, recognizing data of cells.
We call this operation as sensing.
Second, after sensing data from DRAM cells, sense-amplifiers drive charge to the cells for reconstructing original data.
We call this operation as restore.
Third, after restoring the cell data, DRAM deselects the accessed row and puts the sense-amplifiers to original state for next access.
We call this operation as precharge.
As shown in these three steps, DRAM operation is charge movement between cell and sense-amplifier.

## Slide 7
Data 0
Data 1
Cell
time
charge
Sense-Amplifier
DRAM Charge over Time
Sensing
Restore
Why does DRAM need the extra timing margin?
Timing Parameters
In theory
In practice
margin
Cell
Sense-Amplifier
Notes: Timing parameters exist to ensure sufficient movement of charge.
The figure shows the timeline for accessing DRAM in X-axis and Y-axis shows the charge amount in DRAM cell and sense-amplifier.
When selecting a row of cells, each cell drives their charge toward to the corresponding sense-amplifier.
If driven charge is more than enough to detect the data, the sense-amplifier starts to restore data by driving charge toward the cell.
This restore operation finishes when the cell is fully charged.
Ideally, DRAM timing parameters are just enough for the sufficient movement of charge.
However, in practice, there are large margin in DRAM timing parameters.
Why are these margin required?

## Slide 8
1. DRAM Operation Basics
2. Reasons for Timing Margin in DRAM
4. Adaptive-Latency DRAM
5. DRAM Characterization
6. Real System Performance Evaluation
3. Key Observations
Notes: This is the outline. I will first briefly explain DRAM operation and two reasons of timing margin in DRAM.
Then, we will talk about our three key mechanisms and propose our mechanism, Adaptive-Latency DRAM.
Then, we will provide the DRAM latency characterization results and real system performance evaluation results.
Let me start from DRAM operation.

## Slide 9
1. Process Variation
  DRAM cells are not equal
  Leads to extra timing margin for cell that can store small amount of charge
`
2. Temperature Dependence
  DRAM leaks more charge at higher temperature
  Leads to extra timing margin when operating at low temperature
Two Reasons for Timing Margin
1. Process Variation
  DRAM cells are not equal
  Leads to extra timing margin for a cell that can store a large amount of charge
1. Process Variation
  DRAM cells are not equal
  Leads to extra timing margin for a cell that can store a large amount of charge
Notes: There are two reasons for the margin in DRAM timing parameters.
First is process variation and second is temperature dependence.
Let me introduce the first factor, process variation.

## Slide 10
DRAM Cells are Not Equal
Real
Ideal
Same Size 
Same Charge 
Different Size 
Different Charge 
Largest Cell
Smallest Cell
Same Latency
Different Latency
Large variation in cell size 
Large variation in charge 
Large variation in access latency
Notes: Ideally, DRAM would have uniform cells which have same size, thereby having same access latency.
Unfortunately, due to process variation, each cell has different size, thereby having different access latency.
Therefore, DRAM shows large variation in both charge amount in its cell and access latency to its cell.

## Slide 11
Contact
Process Variation
Access Transistor
Bitline
Capacitor
Small cell can store small charge
Small cell capacitance
High contact resistance
Slow access transistor
❶ Cell Capacitance
❷ Contact Resistance
❸ Transistor Performance
ACCESS
DRAM Cell
 High access latency
Notes: Ideally, DRAM would have uniform cells which have same size, thereby having same access latency.
Unfortunately, due to process variation, each cell has different size, thereby having different access latency.
Therefore, DRAM shows large variation in both charge amount in its cell and access latency to its cell.

## Slide 12
Two Reasons for Timing Margin
1. Process Variation
  DRAM cells are not equal
  Leads to extra timing margin for a cell that can store a large amount of charge
`
2. Temperature Dependence
  DRAM leaks more charge at higher temperature
  Leads to extra timing margin for cells that operate at the high temperature
2. Temperature Dependence
  DRAM leaks more charge at higher temperature
  Leads to extra timing margin for cells that operate at the high temperature
2. Temperature Dependence
  DRAM leaks more charge at higher temperature
  Leads to extra timing margin for cells that operate at the low temperature
Notes: Let me introduce the second factor temperature dependence.

## Slide 13
Charge Leakage Temperature
Room Temp.
Hot Temp. (85°C)
Small Leakage
Large Leakage
Cells store small charge at high temperature
and large charge at low temperature
 Large variation in access latency
Notes: DRAM leakage increases the variation.
DRAM loses their charge over time and loses more charge at higher temperature.
Therefore, DRAM cell has smallest charge when operating at hot temperature, for example 85C which is the highest temperature guaranteed by DRAM standard.
This temperature dependence increases the variation in DRAM cell charge.

## Slide 14
DRAM Timing Parameters
DRAM timing parameters are dictated by the worst-case
  The smallest cell with the smallest charge in all DRAM products
  Operating at the highest temperature
Large timing margin for the common-case

## Slide 15
Our Approach
We optimize DRAM timing parameters for the common-case
  The smallest cell with the smallest charge in a DRAM module
  Operating at the current temperature
Common-case cell has extra charge than the worst-case cell
Can lower latency for the common-case

## Slide 16
1. DRAM Operation Basics
2. Reasons for Timing Margin in DRAM
4. Adaptive-Latency DRAM
5. DRAM Characterization
6. Real System Performance Evaluation
3. Key Observations
Notes: This is the outline. I will first briefly explain DRAM operation and two reasons of timing margin in DRAM.
Then, we will talk about our three key mechanisms and propose our mechanism, Adaptive-Latency DRAM.
Then, we will provide the DRAM latency characterization results and real system performance evaluation results.
Let me start from DRAM operation.

## Slide 17
Key Observations
1. Sensing
2. Restore
3. Precharge
Sense cells with extra charge faster
 Lower sensing latency
No need to fully restore cells with extra charge
 Lower restore latency
No need to fully precharge bitlines for cells with extra charge
 Lower precharge latency
Notes: Remember there are three steps in DRAM operation, sensing, restore, and precharge.
In all these steps, the excessive charge enables potential timing parameter reduction.
Let me introduce these three scenarios in order.

## Slide 18
Typical DIMM at
Low Temperature
Observation 1. Faster Sensing
More Charge
Strong Charge
Flow
Faster Sensing
Typical DIMM at Low Temperature
 More charge  Faster sensing
Timing
(tRCD)
17% ↓
No Errors
115 DIMM
Characterization
Notes: First step in DRAM operation is sensing.
In typical case, there are more charge in DRAM cell compared to the worst case.
The excessive charge enables stronger charge drive to sense-amplifier.
Then, sense-amplifier can detect data of DRAM cell fast, thereby complete sensing operation fast.
In our DRAM latency profiling results of 115 DRAM modules,
we observe that 17% potential reduction for the corresponding timing parameters of sensing.
As a result, more charge in typical cases lead to fast sensing.

## Slide 19
Observation 2. Reducing Restore Time
Larger Cell &
Less Leakage 
Extra Charge
No Need to Fully
Restore Charge
Typical DIMM at lower temperature
 More charge  Restore time reduction
Typical DIMM at
Low Temperature
Read (tRAS)
37% ↓
Write (tWR)
54% ↓
No Errors
115 DIMM
Characterization
Notes: Second step in DRAM operation is restore.
Due to larger size and less leakage, typical DRAM cells have more charge than the worst cell.
Even though typical DRAM does not restore the excessive charge during restore operation,
eventually the typical cell has more charge than the worst case cell, guaranteeing reliable operations.
By reducing this restore time in DRAM read/write, our DRAM latency characterization shows significant potential to reduce corresponding timing parameters. For example, 37% for read and 54% for write.
As a result, more charge in typical cases enables restore time reduction.

## Slide 20
Empty (0V)
Full (Vdd)
Half
Observation 3. Reducing Precharge Time
Bitline
Sense-Amplifier
Sensing
Precharge
Precharge ?
– Setting bitline to half-full charge
Typical DIMM at Lower Temperature
Notes: Third step is precharge. Previously we explained the precharge simply as going back to original state.
Let me introduce more details about precharge.
To detect data in DRAM cell, DRAM has sense-amplifier and wire connection to the bitline.
DRAM preserve their a bit of data in two charge state, empty and fully charged.
During sensing and restore, the bitline moves to either of these two states.
After finishing the access, the bitline should be go back to the half of these two state.
We call this precharge. Unfortunately, bitline is usually long by connecting hundred of cells such that it takes long time for precharge.

## Slide 21
Empty (0V)
Full (Vdd)
Half
bitline
Not Fully Precharged
More Charge
 Strong Sensing
Access Empty Cell
Access Full Cell
Timing
(tRP)
35% ↓
No Errors
115 DIMM
Characterization
Typical DIMM at Lower Temperature
 More charge  Precharge time reduction
Observation 3. Reducing Precharge Time
Notes: Let us observe the impact of reducing precharge with a simple example.
The sense-amplifier first accesses an empty cell then not fully precharged by reducing corresponding timing parameter.
Then DRAM next access a fully charged cell.
Due to the bias in the bitline, it takes longer time to access the fully charged cell.
However, if the cell has much excessive charge, the strong charge flow overcomes the bias in the bitline, leading to reliable access.
Our DRAM latency evaluation shows that in typical case, we can reduce corresponding timing parameter by 35% without errors.
Therefore, more charge in typical cases enables precharge time reduction.

## Slide 22
Key Observations
1. Sensing
2. Restore
3. Precharge
Sense cells with extra charge faster
 Lower sensing latency
No need to fully restore cells with extra charge
 Lower restore latency
No need to fully precharge bitlines for cells with extra charge
 Lower precharge latency
Notes: Remember there are three steps in DRAM operation, sensing, restore, and precharge.
In all these steps, the excessive charge enables potential timing parameter reduction.
Let me introduce these three scenarios in order.

## Slide 23
1. DRAM Operation Basics
2. Reasons for Timing Margin in DRAM
4. Adaptive-Latency DRAM
5. DRAM Characterization
6. Real System Performance Evaluation
3. Key Observations
Notes: This is the outline. I will first briefly explain DRAM operation and two reasons of timing margin in DRAM.
Then, we will talk about our three key mechanisms and propose our mechanism, Adaptive-Latency DRAM.
Then, we will provide the DRAM latency characterization results and real system performance evaluation results.
Let me start from DRAM operation.

## Slide 24: Adaptive-Latency DRAM
Key idea
  Optimize DRAM timing parameters online
Two components
  DRAM manufacturer profiles multiple sets of reliable DRAM timing parameters at different temperatures for each DIMM
  System monitors DRAM temperature & uses appropriate DRAM timing parameters
reliable DRAM timing parameters
DRAM temperature

## Slide 25
1. DRAM Operation Basics
2. Reasons for Timing Margin in DRAM
4. Adaptive-Latency DRAM
5. DRAM Characterization
6. Real System Performance Evaluation
3. Key Observations
Notes: This is the outline. I will first briefly explain DRAM operation and two reasons of timing margin in DRAM.
Then, we will talk about our three key mechanisms and propose our mechanism, Adaptive-Latency DRAM.
Then, we will provide the DRAM latency characterization results and real system performance evaluation results.
Let me start from DRAM operation.

## Slide 26: DRAM Temperature
DRAM temperature measurement
  Server cluster: Operates at under 34°C
  Desktop: Operates at under 50°C
  DRAM standard optimized for 85°C
Previous works – DRAM temperature is low
  El-Sayed+ SIGMETRICS 2012
  Liu+ ISCA 2007
Previous works – Maintain DRAM temperature low
  David+ ICAC 2011
  Liu+ ISCA 2007
  Zhu+ ITHERM 2008
DRAM operates at low temperatures in the common-case

## Slide 27: DRAM Testing Infrastructure
Temperature
Controller
PC
Heater
FPGAs
FPGAs
Notes: This is the photo of our infrastructure, that we built mostly from scratch.
For higher throughput, we employ eight FPGAs, all of which are enclosed in thermally-regulated environment.

## Slide 28
Test Pattern
Write
time
Access
Verify
Refresh Interval: 64–512ms
Single cache line test (Read/Write)
Overlapping multiple single cache line tests to simulate power noise and coupling
Write
Access
Verify
time
Refresh Interval: 64–512ms
Access
Access
Verify
. . .
. . .
. . .

## Slide 29
Control Factors
Timing parameters
  Sensing: tRCD
  Restore: tRAS (read), tWR(write)
  Precharge: tRP
Temperature: 55 – 85°C
Refresh interval: 64 – 512ms
  Longer refresh interval leads to smaller charge
  Standard refresh interval: 64ms

## Slide 30
Chart: 
| 15.0ns | 12.5ns | 10.0ns | 7.5ns
64ms | 1 | 1 | 1 | 30648
Chart: 
| 35.0ns | 32.5ns | 30.0ns | 27.5ns | 25.0ns | 22.5ns | 20.0ns
64ms | 1 | 1 | 1 | 1 | 1 | 1 | 1
Chart: 
| 15.0ns | 12.5ns | 10.0ns | 7.5ns
64ms | 1 | 1 | 1 | 31042
Chart: 
| 15.0ns | 12.5ns | 10.0ns | 7.5ns | 5.0ns
64ms | 1 | 1 | 1 | 1 | 1
10
102
103
104
105
0
Errors
Temperature: 85°C/Refresh Interval: 64, 128, 256, 512ms
1. Timings ↔ Charge
More charge enables
more timing parameter reduction
Sensing
Restore
(Read)
Precharge
Restore
(Write)
Chart: 
| 15.0ns | 12.5ns | 10.0ns | 7.5ns
64ms | 1 | 1 | 1 | 30648
Chart: 
| 35.0ns | 32.5ns | 30.0ns | 27.5ns | 25.0ns | 22.5ns | 20.0ns
64ms | 1 | 1 | 1 | 1 | 1 | 1 | 1
Chart: 
| 15.0ns | 12.5ns | 10.0ns | 7.5ns
64ms | 1 | 1 | 1 | 31042
Chart: 
| 15.0ns | 12.5ns | 10.0ns | 7.5ns | 5.0ns
64ms | 1 | 1 | 1 | 1 | 1
Chart: 
| 15.0ns | 12.5ns | 10.0ns | 7.5ns
64ms | 1 | 1 | 1 | 30648
128ms | 1 | 1 | 1 | 31752
Chart: 
| 35.0ns | 32.5ns | 30.0ns | 27.5ns | 25.0ns | 22.5ns | 20.0ns
64ms | 1 | 1 | 1 | 1 | 1 | 1 | 1
128ms | 1 | 1 | 1 | 1 | 1 | 1 | 1
Chart: 
| 15.0ns | 12.5ns | 10.0ns | 7.5ns
64ms | 1 | 1 | 1 | 31042
128ms | 1 | 1 | 1 | 32021
Chart: 
| 15.0ns | 12.5ns | 10.0ns | 7.5ns | 5.0ns
64ms | 1 | 1 | 1 | 1 | 1
128ms | 1 | 1 | 1 | 1 | 1
Chart: 
| 15.0ns | 12.5ns | 10.0ns | 7.5ns
64ms | 1 | 1 | 1 | 30648
128ms | 1 | 1 | 1 | 31752
256ms | 2 | 3 | 6 | 33703
Chart: 
| 35.0ns | 32.5ns | 30.0ns | 27.5ns | 25.0ns | 22.5ns | 20.0ns
64ms | 1 | 1 | 1 | 1 | 1 | 1 | 1
128ms | 1 | 1 | 1 | 1 | 1 | 1 | 1
256ms | 2 | 2 | 2 | 3 | 3 | 5 | 6
Chart: 
| 15.0ns | 12.5ns | 10.0ns | 7.5ns
64ms | 1 | 1 | 1 | 31042
128ms | 1 | 1 | 1 | 32021
208ms | 1 | 2 | 2 | 33876
256ms | 1 | 2 | 2 | 33876
Chart: 
| 15.0ns | 12.5ns | 10.0ns | 7.5ns | 5.0ns
64ms | 1 | 1 | 1 | 1 | 1
128ms | 1 | 1 | 1 | 1 | 1
256ms | 8 | 8 | 12 | 13 | 16
Chart: 
| 15.0ns | 12.5ns | 10.0ns | 7.5ns
64ms | 1 | 1 | 1 | 30648
128ms | 1 | 1 | 1 | 31752
256ms | 2 | 3 | 6 | 33703
512ms | 529 | 815 | 873 | 34001
Chart: 
| 35.0ns | 32.5ns | 30.0ns | 27.5ns | 25.0ns | 22.5ns | 20.0ns
64ms | 1 | 1 | 1 | 1 | 1 | 1 | 1
128ms | 1 | 1 | 1 | 1 | 1 | 1 | 1
256ms | 2 | 2 | 2 | 3 | 3 | 5 | 6
512ms | 730 | 831 | 914 | 1051 | 1050 | 1077 | 1096
Chart: 
| 15.0ns | 12.5ns | 10.0ns | 7.5ns
64ms | 1 | 1 | 1 | 31042
128ms | 1 | 1 | 1 | 32021
208ms | 1 | 2 | 2 | 33876
256ms | 1 | 2 | 2 | 33876
512ms | 504 | 744 | 765 | 34508
Chart: 
| 15.0ns | 12.5ns | 10.0ns | 7.5ns | 5.0ns
64ms | 1 | 1 | 1 | 1 | 1
128ms | 1 | 1 | 1 | 1 | 1
256ms | 8 | 8 | 12 | 13 | 16
512ms | 3174 | 4957 | 6007 | 6424 | 6822

## Slide 31
Chart: 
| 15.0ns | 12.5ns | 10.0ns | 7.5ns
64ms | 1 | 1 | 1 | 20361
Chart: 
| 15.0ns | 12.5ns | 10.0ns | 7.5ns
64ms | 1 | 1 | 1 | 30648
Chart: 
| 35.0ns | 32.5ns | 30.0ns | 27.5ns | 25.0ns | 22.5ns | 20.0ns
64ms | 1 | 1 | 1 | 1 | 1 | 1 | 1
Chart: 
| 15.0ns | 12.5ns | 10.0ns | 7.5ns | 5.0ns
64ms | 1 | 1 | 1 | 1 | 1
Chart: 
| 15.0ns | 12.5ns | 10.0ns | 7.5ns
64ms | 1 | 1 | 1 | 30648
128ms | 1 | 1 | 2 | 31752
Chart: 
| 35.0ns | 32.5ns | 30.0ns | 27.5ns | 25.0ns | 22.5ns | 20.0ns
64ms | 1 | 1 | 1 | 1 | 1 | 1 | 1
128ms | 1 | 2 | 3 | 3 | 3 | 4 | 5
Chart: 
| 15.0ns | 12.5ns | 10.0ns | 7.5ns
64ms | 1 | 1 | 1 | 20361
128ms | 2 | 2 | 4 | 21261
Chart: 
| 15.0ns | 12.5ns | 10.0ns | 7.5ns | 5.0ns
64ms | 1 | 1 | 1 | 1 | 1
128ms | 12 | 21 | 32 | 42 | 54
Chart: 
| 15.0ns | 12.5ns | 10.0ns | 7.5ns | 5.0ns
64ms | 1 | 1 | 1 | 1 | 1
128ms | 12 | 21 | 32 | 42 | 54
256ms | 425 | 777 | 931 | 942 | 1030
Chart: 
| 15.0ns | 12.5ns | 10.0ns | 7.5ns
64ms | 1 | 1 | 1 | 30648
128ms | 1 | 1 | 2 | 31752
256ms | 15 | 22 | 24 | 33703
Chart: 
| 35.0ns | 32.5ns | 30.0ns | 27.5ns | 25.0ns | 22.5ns | 20.0ns
64ms | 1 | 1 | 1 | 1 | 1 | 1 | 1
128ms | 1 | 2 | 3 | 3 | 3 | 4 | 5
256ms | 25 | 35 | 42 | 44 | 57 | 65 | 70
Chart: 
| 15.0ns | 12.5ns | 10.0ns | 7.5ns
64ms | 1 | 1 | 1 | 20361
128ms | 2 | 2 | 4 | 21261
256ms | 27 | 29 | 33 | 34243
Temperature: 55, 65, 75, 85°C/Refresh Interval: 512ms
Chart: 
| 15.0ns | 12.5ns | 10.0ns | 7.5ns
64ms | 1 | 1 | 1 | 30648
128ms | 1 | 1 | 2 | 31752
256ms | 15 | 22 | 24 | 33703
512ms | 529 | 815 | 873 | 34001
Chart: 
| 35.0ns | 32.5ns | 30.0ns | 27.5ns | 25.0ns | 22.5ns | 20.0ns
64ms | 1 | 1 | 1 | 1 | 1 | 1 | 1
128ms | 1 | 2 | 3 | 3 | 3 | 4 | 5
256ms | 25 | 35 | 42 | 44 | 57 | 65 | 70
512ms | 730 | 831 | 914 | 1051 | 1050 | 1077 | 1096
Chart: 
| 15.0ns | 12.5ns | 10.0ns | 7.5ns
64ms | 1 | 1 | 1 | 20361
128ms | 2 | 2 | 4 | 21261
256ms | 27 | 29 | 33 | 34243
512ms | 504 | 744 | 765 | 34508
Chart: 
| 15.0ns | 12.5ns | 10.0ns | 7.5ns | 5.0ns
64ms | 1 | 1 | 1 | 1 | 1
128ms | 12 | 21 | 32 | 42 | 54
256ms | 425 | 777 | 931 | 942 | 1030
512ms | 3174 | 4957 | 6007 | 6424 | 6822
10
102
103
104
105
0
Errors
2. Timings ↔ Temperature
Lower temperature enables
more timing parameter reduction
Chart: 
| 15.0ns | 12.5ns | 10.0ns | 7.5ns
64ms | 1 | 1 | 1 | 20361
Chart: 
| 15.0ns | 12.5ns | 10.0ns | 7.5ns
64ms | 1 | 1 | 1 | 30648
Chart: 
| 35.0ns | 32.5ns | 30.0ns | 27.5ns | 25.0ns | 22.5ns | 20.0ns
64ms | 1 | 1 | 1 | 1 | 1 | 1 | 1
Chart: 
| 15.0ns | 12.5ns | 10.0ns | 7.5ns | 5.0ns
64ms | 1 | 1 | 1 | 1 | 1
Sensing
Restore
(Read)
Precharge
Restore
(Write)

## Slide 32
3. Summary of 115 DIMMs
Latency reduction for read & write (55°C)
  Read Latency: 32.7%
  Write Latency: 55.1%
Latency reduction for each timing parameter (55°C)
  Sensing: 17.3%
  Restore: 37.3% (read), 54.8% (write)
  Precharge: 35.2%

## Slide 33
1. DRAM Operation Basics
2. Reasons for Timing Margin in DRAM
4. Adaptive-Latency DRAM
5. DRAM Characterization
6. Real System Performance Evaluation
3. Key Observations
Notes: This is the outline. I will first briefly explain DRAM operation and two reasons of timing margin in DRAM.
Then, we will talk about our three key mechanisms and propose our mechanism, Adaptive-Latency DRAM.
Then, we will provide the DRAM latency characterization results and real system performance evaluation results.
Let me start from DRAM operation.

## Slide 34
Real System Evaluation Method
System
  CPU: AMD 4386 ( 8 Cores, 3.1GHz, 8MB LLC)
  DRAM: 4GByte DDR3-1600 (800Mhz Clock)
  OS: Linux
  Storage: 128GByte SSD
Workload
  35 applications from SPEC, STREAM, Parsec, Memcached, Apache, GUPS

## Slide 35
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
1.4%
6.7%
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
5.0%
Single-Core Evaluation
AL-DRAM improves performance on a real system
Performance Improvement
Average
Improvement
all-35-workload

## Slide 36
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
14.0%
2.9%
Chart: 
| soplex | mcf | milc | libq | lbm | gems | copy | s.cluster | gups | non-intensive | intensive | all-workloads
Single Core | 0.06639 | 0.10482 | 0.094576 | 0.13158 | 0.13835 | 0.144 | 0.12463 | 0.018974 | 0.184 | 0.013864 | 0.066838 | 0.050088
Multi Core | 0.15438 | 0.12305 | 0.14558 | 0.13499 | 0.15581 | 0.15723 | 0.20029 | 0.14045 | 0.18578 | 0.029225 | 0.14039 | 0.10518
10.4%
Multi-Core Evaluation
AL-DRAM provides higher performance for
multi-programmed & multi-threaded workloads
Performance Improvement
Average
Improvement
all-35-workload

## Slide 37
Conclusion
Observations
  DRAM timing parameters are dictated by the worst-case cell (smallest cell across all products at highest temperature)
  DRAM operates at lower temperature than the worst case
Idea: Adaptive-Latency DRAM
  Optimizes DRAM timing parameters for the common case (typical DIMM operating at low temperatures)
Analysis: Characterization of 115 DIMMs
  Great potential to lower DRAM timing parameters (17 – 54%) without any errors
Real System Performance Evaluation
  Significant performance improvement (14% for memory-intensive workloads) without errors (33 days)
Notes: Let me conclude
DRAM timing parameters are dictated by the worst case cell.
We propose Adaptive-Latency DRAM that optimizes DRAM timing parameters for common cases
Our characterization shows the significant potential to lower DRAM timing parameters.
Our real system evaluation shows that our mechanism provides significant performance improvement without introducing errors.

## Slide 38: Optimizing DRAM Timing for the Common-Case
Donghyuk Lee
Yoongu Kim, Gennady Pekhimenko, Samira Khan,
Vivek Seshadri, Kevin Chang, Onur Mutlu
Adaptive-Latency DRAM
Notes: Thank you.

## Slide 39
Backup Slides

## Slide 40
Overhead
DRAM Manufacturer
  Additional tests: can be integrated into existing test process (i.e., TCSR test)
DRAM (DIMM)
  Already have in-DRAM temperature sensor (i.e., Low Power DDR)
  Multiple sets of timing parameters can be stored in SPD (Serial Presence Detect)
System Support for AL-DRAM
  Already have ability to change DRAM timing online

## Slide 41
Chart: 
| A | B | C
35.0ns | 0 | 0 | 0
32.5ns | 0 | 0 | 1
30.0ns | 0 | 0 | 1
27.5ns | 0 | 0 | 2
25.0ns | 0 | 1 | 3
22.5ns | 0 | 2 | 7
20.0ns | 1 | 2 | 9
Errors
tRAS:
tRCD:
tRP:
Ref. Interval:
10.0ns
12.5ns
200ms
12.5ns
10.0ns
200ms
10.0ns
10.0ns
200ms
Reducing a timing parameter
 Reduces potential reduction of other parameters
Multiple Timing Parameters

## Slide 42
Temperature (°C)
Chart: 
| a | b | c | d
Refresh Interval | 640 | 448 | 288 | 192
Maximum error-free refresh interval (ms)
55°C
65°C
75°C
85°C
64ms SPEC
More charge than required
Need for reliable operation from other fail mechanisms (i.e., VRT)
Safety-margin  Safe refresh interval
Extra charge that can be used for latency reduction
Temperature ↔ Refresh Interval

## Slide 43
Cell capacitor
Bitline capacitor
Sense-amplifier
Access transistor
Bitline
DRAM Cell Organization

## Slide 44
Access transistor
Bitline capacitor
Cell capacitor
Charge-sharing
Sense
Amplify
Precharge
Leakage
Sense-amplifier
Bitline
Turn-on access transistor
1
Ready to access data
2
Fully charged
3
Precharged to Vdd/2
4
DRAM Cell Operation

## Slide 45
Largest
charge
Smallest
charge
Typical cell
Worst cell
Worst temp.
Typical temp.
Fast restore
Slow restore
Slowly
leak
Fast leak
DRAM Cell Charge Variations