## Slide 1
Today, DRAM is just a storage device

## Slide 2
Today, DRAM is just a storage device
RowClone: Bulk Data Copy and Initialization Using DRAM
MICRO 2013

## Slide 3
Today, DRAM is just a storage device
RowClone: Bulk Data Copy and Initialization Using DRAM
MICRO 2013
Gather-Scatter DRAM: Accelerating Strided Accesses Using DRAM
MICRO 2015

## Slide 4
Today, DRAM is just a storage device
RowClone: Bulk Data Copy and Initialization Using DRAM
MICRO 2013
Gather-Scatter DRAM: Accelerating Strided Accesses Using DRAM
MICRO 2015
Ambit: Accelerating Bulk Bitwise Operations Using DRAM
MICRO 2017

## Slide 5
Bulk Bitwise Operations
Database indices
Search filters
Database scans
Cryptography
Genome analysis
...

## Slide 6
Throughput of bulk bitwise operations limited
by available memory bandwidth
Processor
Memory
Channel
Bulk Bitwise Operations
Database indices
Search filters
Database scans
Cryptography
Genome analysis
...

## Slide 7
Ambit
Perform bitwise operations completely inside DRAM chips
Bitwise AND/OR: Simultaneous activation of three rows
Bitwise NOT: Inverters already present in sense amplifiers

## Slide 8
Ambit
Perform bitwise operations completely inside DRAM chips
Bitwise AND/OR: Simultaneous activation of three rows
Bitwise NOT: Inverters already present in sense amplifiers
1% area cost over existing DRAM chips
improvement in
raw throughput
32X
reduction in
energy consumed
35X

## Slide 9
Ambit
Perform bitwise operations completely inside DRAM chips
Bitwise AND/OR: Simultaneous activation of three rows
Bitwise NOT: Inverters already present in sense amplifiers
1% area cost over existing DRAM chips
improvement in
raw throughput
32X
reduction in
energy consumed
35X
performance improvement
in real-world applications
3X-7X

## Slide 10
Ambit In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology
Vivek Seshadri, Donghyuk Lee, Thomas Mullins, Hasan Hassan, Amirali Boroumand,
Jeremie Kim, Michael A. Kozuch, Onur Mutlu, Phillip B. Gibbons, Todd C. Mowry
Session 3A – Tuesday, 11 AM