## Slide 1: Ambit In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology
Vivek Seshadri
Donghyuk Lee, Thomas Mullins, Hasan Hassan, Amirali Boroumand, Jeremie Kim, Michael A. Kozuch, Onur Mutlu, Phillip B. Gibbons, Todd C. Mowry

## Slide 2: Executive Summary
Problem: Bulk bitwise operations
  present in many applications, e.g., databases, search filters
  existing systems are memory bandwidth limited
Our Proposal: Ambit
  perform bulk bitwise operations completely inside DRAM
  bulk bitwise AND/OR: simultaneous activation of three rows
  bulk bitwise NOT: inverters already in sense amplifiers
  less than 1% area overhead over existing DRAM chips
Results compared to state-of-the-art baseline
  average across seven bulk bitwise operations
    32X performance improvement, 35X energy reduction
  3X-7X performance for real-world data-intensive applications
Notes: Talk about energy more
Explicitly state the performance improvement numbers
Range for throughput and energy?
Color more? Bulk AND/OR or NOT
Mechanism for NOT – fix the description. (use inverters already in sense amplifiers}?
Cost not coming out – mention the area cost

## Slide 3
[1] Li and Patel, BitWeaving, SIGMOD 2013
[2] Goodwin+, BitFunnel, SIGIR 2017
Bulk Bitwise Operations
BitWeaving
(database queries)
BitFunnel
(web search)
Bitmap indices
(database indexing)
Set operations
Encryption algorithms
DNA
sequence mapping
...
Notes: Add … (signify more applications)
Add references to some works (bitweaving, bitfunnel)

## Slide 4: Today, DRAM is just a storage device!
Processor
(CPU, GPU, FPGA)
DRAM
Channel
Write
Read
Throughput of bulk bitwise operations limited by available memory bandwidth

## Slide 5: Our Approach
Processor
(CPU, GPU, FPGA or PiM)
DRAM
Channel
Use analog operation of DRAM to perform bitwise operations completely inside memory!

## Slide 6: Outline of the talk
1. DRAM Background
3. Ambit-NOT: Bitwise NOT in DRAM
2. Ambit-AND-OR: Bitwise AND/OR in DRAM
4. Ambit Implementation
5. Applications and Evaluation

## Slide 7: Inside a DRAM Chip
…
…
…
…
…
…
2D Array
of DRAM Cells
Sense amplifiers
8KB

## Slide 8: DRAM Cell Operation
Sense Amp
enable
bitline
wordline
capacitor
access transistor
bitline

## Slide 9: DRAM Cell Operation
½ VDD + δ
enable
bitline
wordline
capacitor
access transistor
0
½ VDD
0
1
1
VDD
raise wordline
enable sense amp
connects cell to bitline
cell loses charge to bitline
cell regains charge
Sense Amp
deviation in bitline voltage
½ VDD
0
bitline

## Slide 10: Outline of the talk
1. DRAM Background
3. Bitwise NOT in DRAM
2. Bitwise AND/OR in DRAM
4. Ambit Implementation
5. Applications and Evaluation

## Slide 11: Triple-Row Activation: Majority Function
½ VDD + δ
0
½ VDD
0
1
1
VDD
enable sense amp
Sense Amp
activate
all three rows
0
1
0
1

## Slide 12: Bitwise AND/OR Using Triple-Row Activation
1
1
1
1
VDD
Sense Amp
A
B
C

## Slide 13: Bitwise AND/OR Using Triple-Row Activation
1
1
1
1
VDD
Sense Amp
A
B
C
Output = AB + BC + CA
= C (A OR B) +
~C (A AND B)
Control the value of C to perform bitwise OR or bitwise AND of A and B
38X improvement in raw throughput
44X reduction in energy consumption
for bulk bitwise AND/OR operations

## Slide 14: Potential Concerns with Triple-Row Activation
With three cells, bitline deviation may not be enough
Process variation: all cells are not equal
Cells leak charge
Memory controller may have to send three addresses
Source data gets destroyed
Spice simulations put these concerns to rest.
(Section 6 in paper)
Address these challenges through implementation
(next slide)
Notes: *

## Slide 15: Bulk Bitwise AND/OR in DRAM
Copy data of row A to row t1
Copy data of row B to row t2
Initialize data of row t3 to 0/1
Activate rows t1/t2/t3 simultaneously
Copy data of row t1/t2/t3 to Result row
Copy data of row A to row t1
Copy data of row B to row t2
Initialize data of row t3 to 0/1
Activate rows t1/t2/t3 simultaneously
Copy data of row t1/t2/t3 to Result row
Result = row A AND/OR row B
Statically reserve three designated rows t1, t2, and t3
MICRO 2013
Notes: * each copy operation takes only 80ns

## Slide 16: Bulk Bitwise AND/OR in DRAM
Copy RowClone data of row A to row t1
Copy RowClone data of row B to row t2
Initialize RowClone data of row t3 to 0/1
Activate rows t1/t2/t3 simultaneously
Copy RowClone data of row t1/t2/t3 to Result row
Result = row A AND/OR row B
Use RowClone to perform copy and initialization operations completely in DRAM!
Statically reserve three designated rows t1, t2, and t3
Copy data of row A to row t1
Copy data of row B to row t2
Initialize data of row t3 to 0/1
Activate rows t1/t2/t3 simultaneously
Copy data of row t1/t2/t3 to Result row
Notes: Replace copies with rowclone once it is mentioned
Tie back to the concerns.
Reiterate speedup numbers
strike copy and make it rowclone

## Slide 17: Outline of the talk
1. DRAM Background
3. Bitwise NOT in DRAM
2. Bitwise AND/OR in DRAM
4. Ambit Implementation
5. Applications and Evaluation

## Slide 18: Negation Using the Sense Amplifier
Sense Amp
bitline
bitline
enable
Can we copy the negated value from bitline to a DRAM cell?
Notes: Mark the enable signal to the sense amplifier
Before introducing the dual contact cell, state the key idea

## Slide 19: Negation Using the Sense Amplifier
Sense Amp
Dual Contact Cell
Regular wordline
Negation wordline
bitline
bitline
enable
Notes: Mark the enable signal to the sense amplifier
Before introducing the dual contact cell, state the key idea

## Slide 20: Negation Using the Sense Amplifier
enable sense amp
Sense Amp
½ VDD + δ
½ VDD
VDD
½ VDD
0
activate source
activate
negation wordline
bitline
bitline
source
Notes: Provide the result for NOT
Present all the results after this slide?

## Slide 21: Ambit vs. DDR3: Performance and Energy
Chart: 
| not | and/or | nand/nor | xor/xnor | mean
Performance Improvement | 51.6251 | 38.3193 | 30.6965 | 21.8566 | 32
Energy Reduction | 59.5 | 43.9 | 35.1 | 25.1 | 35
32X
35X

## Slide 22: Outline of the talk
1. DRAM Background
3. Bitwise NOT in DRAM
2. Bitwise AND/OR in DRAM
4. Ambit Implementation
5. Applications and Evaluation

## Slide 23: Ambit – Implementation
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
…
…
…
Sense
Amplifiers
Dual Contact Cells
Designated Rows
for Triple Activation
Regular
Data Rows
Pre-initialized Rows
Notes: Make it clear that this is a subarray
Activate -> activation

## Slide 24: Ambit – Implementation
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
…
…
…
Sense
Amplifiers
Dual Contact Cells
Temporary Rows
for Triple Activate
Regular
Data Rows
Pre-initialized Rows
Bitwise Decoder
Regular Row Decoder
Notes: * Command sequence to perform bitwise AND operation?

## Slide 25: Integrating Ambit with the System
PCIe device
  Similar to other accelerators (e.g., GPU)
System memory bus
  Ambit uses the same DRAM command/address interface
Pros and cons discussed in paper (Section 5.4)
Notes: Make it simpler
Two approaches.

## Slide 26: Outline of the talk
1. DRAM Background
3. Bitwise NOT in DRAM
2. Bitwise AND/OR in DRAM
4. Ambit Implementation
5. Applications and Evaluation

## Slide 27: Real-world Applications
Methodology (Gem5 simulator)
  Processor: x86, 4 GHz, out-of-order, 64-entry instruction queue
  L1 cache: 32 KB D-cache and 32 KB I-cache, LRU policy
  L2 cache: 2 MB, LRU policy
  Memory controller: FR-FCFS, 8 KB row size
  Main memory: DDR4-2400, 1 channel, 1 rank, 8 bank
Workloads
  Database bitmap indices
  BitWeaving –column scans using bulk bitwise operations
  Set operations – comparing bitvectors with red-black trees
Notes: Add color
Fix workloads – add set operation workload as well

## Slide 28: Bitmap Indices: Performance
Consistent reduction in execution time. 6X on average
Chart: Execution Time of Query
| w = 2 | w = 3 | w = 4 | w = 2 | w = 3 | w = 4 | n = 8m | n = 16m
Baseline | 27.92 | 41.72 | 54.84 | 58 | 85.44 | 112.92
Ambit | 5.16 | 6.88 | 8.64 | 10.2 | 13.68 | 17.16
5.4X
6.1X
6.3X
5.7X
6.2X
6.6X
Notes: Add color
Remove “week” and “users”

## Slide 29: Speedup offered by Ambit for BitWeaving
Chart: Number of bits for each column value
| 4 | 8 | 12 | 16 | 20 | 24 | 28 | 32
1m | 1.8 | 2.7 | 3.5 | 4.1 | 9.6 | 10.6 | 11 | 11.6
2m | 1.8 | 2.8 | 7.6 | 9 | 9.8 | 10.8 | 11.2 | 11.7
4m | 1.8 | 6 | 7.8 | 9.2 | 9.9 | 10.9 | 11.3 | 11.8
8m | 3.9 | 6.1 | 7.9 | 9.2 | 10 | 11 | 11.4 | 11.9
Number of rows in the database table
select count(*) where c1 < field < c2
12X
Notes: Reference bitweaving again
Add color
Fix the tag

## Slide 30: Other Details and Results in Paper
Detailed implementation of Ambit
  Changes to DRAM chips
  Optimizations to improve performance
  Error correction codes (open problem)
Detailed SPICE simulation analysis
Comparison to 3D-stacked DRAM
Other applications
  Set operations
  BitFunnel: Web search document filtering
  Masked initialization
  Cryptography
  DNA sequence mapping
Notes: Add reference to the bitfunnel
Add …
Other details in the paper
  Compared to 3D stacking

## Slide 31: Conclusion
Problem: Bulk bitwise operations
  present in many applications, e.g., databases, search filters
  existing systems are memory bandwidth limited
Our Proposal: Ambit
  perform bulk bitwise operations completely inside DRAM
  bulk bitwise AND/OR: simultaneous activation of three rows
  bulk bitwise NOT: inverters already in sense amplifiers
  less than 1% area overhead over existing DRAM chips
Results compared to state-of-the-art baseline
  average across seven bulk bitwise operations
    32X performance improvement, 35X energy reduction
  3X-7X performance for real-world data-intensive applications

## Slide 32: Ambit In-Memory Accelerator for Bulk Bitwise Operations Using Commodity DRAM Technology
Vivek Seshadri
Donghyuk Lee, Thomas Mullins, Hasan Hassan, Amirali Boroumand, Jeremie Kim, Michael A. Kozuch, Onur Mutlu, Phillip B. Gibbons, Todd C. Mowry

## Slide 34: Backup Slides

## Slide 35: Data movement consumes high energy
src: Bill Dally Keynote, “Challenge for Future Computer Systems,” HIPEAC 2015.

## Slide 36: RowClone: In-DRAM Bulk Data Copy (MICRO 2013)
½ VDD + δ
0
½ VDD
0
1
1
VDD
enable sense amp
Sense Amp
0
1
activate
source
activate
destination
data gets copied source to destination
source
destination
MICRO 2013
Notes: Add MICRO 2013 to the title
Mark source and destination on the slide
Mention the speedup of RowClone mechanism

## Slide 37: Today, DRAM is just a storage device!
Processor
DRAM
Channel
Write (64B)
Read (64B)
Can we do more with DRAM?

## Slide 38: Ambit – Implementation
0
0
0
0
0
0
0
0
1
1
1
1
1
1
1
1
…
…
…
Sense
Amplifiers
Dual Contact Cells
Temporary Rows
for Triple Activate
Regular
Data Rows
Pre-initialized Rows
Bitwise Decoder
Regular Row Decoder
Reserved
Address 0
Notes: * Command sequence to perform bitwise AND operation?

## Slide 39: Summary of operations
…
…
…
…
…
…
Sense amplifiers
Copy
AND
OR
NOT

## Slide 40: Ambit Throughput
Chart: Throughput (GOps/sec)
| not | and/or | nand/nor | xor/xnor | mean
Skylake | 8.5742 | 5.7757 | 5.7757 | 5.7757 | 6.105
GTX 745 | 12.042 | 8.1117 | 8.1117 | 8.1117 | 8.5742
HMC 2.0 | 159.7863 | 106.8913 | 106.8913 | 106.8913 | 112.986
Ambit | 621.6678 | 310.8339 | 248.9997 | 177.294 | 274.374
Ambit-3D | 2486.6711 | 1243.3356 | 995.9987 | 709.176 | 1097.496

## Slide 41: Error Correction Code
Need ECC that is homomorphic over bitwise operations
  ECC(A and B) = ECC(A) and ECC(B)
  ECC(A or B) = ECC(A) or ECC(B)
  ECC(not A) = not ECC(A)
Triple Modular Redundancy
  trivially satisfies the above condition
  2X capacity overhead
  Better performance and energy efficiency
  Lower overall cost