## Slide 1
Lavanya Subramanian, Vivek Seshadri, Arnab Ghosh, Samira Khan, Onur Mutlu
Carnegie Mellon University, Intel Labs, University of Virginia
Application Slowdown Model:
Quantifying and Controlling Impact of Interference at
Shared Caches and Main Memory
Problem:
Shared Resource Interference
Chart: Slowdown
| leslie3d (core 0) | gcc (core 1)
Slowdown | 1.9 | 1.1
Chart: Slowdown
| leslie3d (core 0) | mcf (core 1)
Slowdown | 5.4 | 2.1
gcc
(core 1)
mcf
(core 1)
Impact of
Shared Resource Interference
2. Unpredictable application slowdowns
1. High application slowdowns
Application Slowdown Model (ASM)
Leveraging the Application Slowdown Model
Main Memory
Shared
Cache
Core
Core
Core
Core
Our Goal
Provide high and predictable performance in the presence of
shared resource interference
Our Approach
Build a model to estimate slowdowns
Leverage our model for slowdown-aware resource management
Slowdown
Slowdown
Chart: Shared Cache Access Rate Alone/ Shared Cache Access Rate Shared
| 1.9566398593094234 | 1.4244011693845886 | 1.2634952603669136 | 1.2398817773717179 | 1.2327504382395447 | 1.1866685232301462 | 1.1281807279586349 | 1.1240581612633374 | 1.0852248306002077 | 1.049730923564083 | 1.0308963402118512 | 1
astar | 2.0976 | 1.4098 | 1.2836 | 1.2286 | 1.2286 | 1.1781 | 1.1316 | 1.0886 | 1.075 | 1.0238 | 1.0118 | 1
lbm | 1.9524 | 1.5769 | 1.268 | 1.2178 | 1.1714 | 1.1604 | 1.0982 | 1
bzip2 | 1.5672 | 1.448 | 1.3189 | 1.2404 | 1.11 | 1
Observation: Proxy for Performance
For a memory bound application,
Performance α Cache access rate
Challenge: Estimating Cache Access Rate Alone
Minimize memory bandwidth contention:
Using priority (Subramanian et al., HPCA 2013)
Request Buffer State
Main Memory
1. Run alone
Time units
Service order
Main Memory
1
2
Request Buffer State
Main Memory
2. Run with another application
Main Memory
1
2
3
Request Buffer State
Main Memory
3. Run with another application: highest priority
Main Memory
1
2
3
3
Time units
Service order
Time units
Service order
Highest priority  Little interference
(almost as if application were run alone)
Enables estimation of miss service time
Quantify shared cache capacity contention:
Using auxiliary tag stores (Pomerene et al., 1989)
Main Memory
Shared
Cache
Auxiliary Tag Store
Priority
Core
Core
Auxiliary Tag Store
Auxiliary tag store counts #contention misses
From auxiliary tag store
when given high priority
Measured when given high priority
#Contention Misses x
Average Miss Service Time
Remove contention cycles when estimating CARAlone
Average error of ASM: 10%; Average error of previous models: 30%
Main Memory
Shared
Cache
Core
Core
Slowdown-aware cache capacity partitioning
Previous work: Reduce miss counts;
Our proposal: Reduce slowdowns
Slowdown-aware memory bandwidth partitioning
Main Memory
Shared
Cache
Core
Core
Allocation memory bandwidth
proportional to slowdowns
Coordinated Resource
Allocation Schemes
Main Memory
Shared
Cache
Core
Core
Core
Core
16-core system 100 workloads
Significant fairness benefits across different channel counts
Chart: Number of Channels
FRFCFS-NoPart | 10.498 | 6.9257
FRFCFS+UCP | 9.4748 | 6.0393
TCM+UCP | 10.4292 | 6.592
PARBS+UCP | 9.3348 | 6.033
ASM-Cache-Mem | 7.9617 | 5.5061
Chart: Number of Channels
FRFCFS-NoPart | 0.212 | 0.30811
FRFCFS+UCP | 0.20694 | 0.30879
TCM+UCP | 0.19336 | 0.28617
PARBS+UCP | 0.21259 | 0.31157
ASM-Cache-Mem | 0.20928 | 0.30633
Providing
Slowdown Guarantees
Cache allocation with the goal of meeting a slowdown bound
Allocate just enough cache space to critical application
Allocate remaining cache space to other applications
Chart: Slowdown
| h264ref | mcf | sphinx3 | soplex
Naive-QoS | 2.1735 | 2.395 | 3.7317 | 3.2826
ASM-QoS-2.5 | 2.3009 | 2.0314 | 3.2274 | 2.8803
ASM-QoS-3 | 2.4396 | 1.9874 | 3.2151 | 2.7853
ASM-QoS-3.5 | 2.576 | 1.9762 | 3.1915 | 2.7442
ASM-QoS-4 | 2.6616 | 1.9711 | 3.1823 | 2.6657