## Slide 1: Quantifying and Controlling Impact of Interference at Shared Caches and Main Memory
Lavanya Subramanian, Vivek Seshadri,
Arnab Ghosh, Samira Khan, Onur Mutlu
Application Slowdown Model

## Slide 2: Problem: Interference at Shared Resources
Main Memory
Shared
Cache
Core
Core
Core
Core

## Slide 3: Impact of Shared Resource Interference
Chart: Slowdown
| leslie3d (core 0) | gcc (core 1)
Slowdown | 1.9 | 1.1
Chart: Slowdown
| leslie3d (core 0) | mcf (core 1)
Slowdown | 5.4 | 2.1
2. Unpredictable application slowdowns
1. High application slowdowns
gcc (core 1)
mcf (core 1)
Our Goal: Achieve High and Predictable Performance
Notes: This graph shows two applications from the SPEC CPU 2006 suite, leslie3d and gcc. These applications are run on either core of a two core system and share main memory. The y-axis shows each application’s slowdown as compared to when the application is run standalone on the same system.
Now, let’s look at leslie3d. It slows down by 2x when run with gcc.
Let’s look at another case when leslie3d is run with another application, mcf. Leslie now slows down by 5.5x, while it slowed down by 2x when run with gcc. Leslie experiences different slowdowns when run with different applications.
More generally, an application’s performance depends on which applications it is running with. Such performance unpredictability is undesirable….

## Slide 4: Outline
Quantify Impact of Interference - Slowdown
  Key Observation
  Estimating Cache Access Rate Alone
  ASM: Putting it All Together
  Evaluation
Control Slowdown
  Slowdown-aware Cache Capacity Allocation
  Slowdown-aware Memory Bandwidth Allocation
  Coordinated Cache/Memory Management

## Slide 5: Quantifying Impact of Shared Resource Interference
Alone
(No interference)
time
Execution time
Shared
(With interference)
time
Execution time
Impact of Interference

## Slide 6: Slowdown: Definition
Slowdown
Notes: Slowdown of an application is its performance when it is run stand alone on a system to its performance when it is sharing the system with other applications.
An application’s performance when it is sharing the system with other applications can be measured in a straightforward manner. However, measuring an application’s alone performance, without actually running it alone is harder.
This is where are first observation comes in.

## Slide 7: Approach: Impact of Interference on Performance
Alone
(No interference)
time
Execution time
Shared
(With interference)
time
Execution time
Impact of Interference
Previous Approach: Estimate impact of interference at a per-request granularity
Difficult to estimate due to request overlap
Our Approach: Estimate impact of interference aggregated over requests

## Slide 8: Outline
Quantify Slowdown
  Key Observation
  Estimating Cache Access Rate Alone
  ASM: Putting it All Together
  Evaluation
Control Slowdown
  Slowdown-aware Cache Capacity Allocation
  Slowdown-aware Memory Bandwidth Allocation
  Coordinated Cache/Memory Management

## Slide 9: Observation: Shared Cache Access Rate is a Proxy for Performance
Performance  Shared Cache Access rate
Chart: Shared Cache Access Rate Alone/ Shared Cache Access Rate Shared
| 1.9566398593094234 | 1.4244011693845886 | 1.2634952603669136 | 1.2398817773717179 | 1.2327504382395447 | 1.1866685232301462 | 1.1281807279586349 | 1.1240581612633374 | 1.0852248306002077 | 1.049730923564083 | 1.0308963402118512 | 1
astar | 2.0976 | 1.4098 | 1.2836 | 1.2286 | 1.2286 | 1.1781 | 1.1316 | 1.0886 | 1.075 | 1.0238 | 1.0118 | 1
lbm | 1.9524 | 1.5769 | 1.268 | 1.2178 | 1.1714 | 1.1604 | 1.0982 | 1
bzip2 | 1.5672 | 1.448 | 1.3189 | 1.2404 | 1.11 | 1
Slowdown
Intel Core i5, 4 cores
Difficult
Easy
Slowdown
Shared Cache Access Rate Alone
Shared Cache Access Rate Shared

## Slide 10: Outline
Quantify Slowdown
  Key Observation
  Estimating Cache Access Rate Alone
  ASM: Putting it All Together
  Evaluation
Control Slowdown
  Slowdown-aware Cache Capacity Allocation
  Slowdown-aware Memory Bandwidth Allocation
  Coordinated Cache/Memory Management

## Slide 11: Estimating Cache Access Rate Alone
Main Memory
Shared
Cache
Core
Core
Core
Core
Challenge 1:
Main memory
bandwidth interference
Challenge 2:
Shared cache
capacity interference

## Slide 12: Estimating Cache Access Rate Alone
Main Memory
Shared
Cache
Core
Core
Core
Core
Challenge 1:
Main memory
bandwidth interference

## Slide 13: Highest Priority Minimizes Memory Bandwidth Interference
Can minimize impact of main memory interference by giving the application highest priority at the memory controller
(Subramanian et al., HPCA 2013)
Highest priority  Little interference
(almost as if the application were run alone)
Highest priority minimizes interference
Enables estimation of miss service time
(used to account for shared cache interference)
Notes: We observe that an application’s alone request service rate can be estimated by giving the application highest priority in accessing memory.
Because, when an application has highest priority, it receives little interference from other applications, almost as though the application were run alone.

## Slide 14: Estimating Cache Access Rate Alone
Main Memory
Shared
Cache
Core
Core
Core
Core
Challenge 2:
Shared cache
capacity interference

## Slide 15: Cache Capacity Contention
Main Memory
Shared
Cache
Cache
Access Rate
Priority
Core
Core
Applications evict each other’s blocks
from the shared cache

## Slide 16: Shared Cache Interference is Hard to Minimize Through Priority
Main Memory
Shared
Cache
Priority
Core
Core
Priority
Takes effect instantly
Many blocks of the blue core
Takes a long time for red core to benefit
from cache priority
Long warmup
Lots of interference to other applications

## Slide 17: Our Approach: Quantify and Remove Cache Interference
Quantify impact of shared cache interference
Remove impact of shared cache interference on CARAlone estimates

## Slide 18: 1. Quantify Shared Cache Interference
Main Memory
Shared
Cache
Cache
Access Rate
Auxiliary Tag Store
Priority
Core
Core
Still in auxiliary tag store
Auxiliary Tag Store
Count number of such contention misses

## Slide 19: 2. Remove Cycles to Serve Contention Misses from CARAlone Estimates
From auxiliary tag store
when given high priority
Measured when application is given high priority
Remove cache contention cycles when estimating
Cache Access Rate Alone (CAR Alone)
#Contention Misses x
Average Miss Service Time

## Slide 20: Accounting for Memory and Shared Cache Interference
Accounting for memory interference
CAR Alone
Accounting for memory and cache interference
CAR Alone

## Slide 21: Outline
Quantify Slowdown
  Key Observation
  Estimating Cache Access Rate Alone
  ASM: Putting it All Together
  Evaluation
Control Slowdown
  Slowdown-aware Cache Capacity Allocation
  Slowdown-aware Memory Bandwidth Allocation
  Coordinated Cache/Memory Management

## Slide 22: Application Slowdown Model (ASM)
Slowdown

## Slide 23: ASM: Interval Based Operation
time
Interval
Estimate
slowdown
Interval
Estimate
slowdown
Measure CARShared
Estimate CARAlone
Measure CARShared
Estimate CARAlone
Notes: MISE operates on an interval basis.
Execution time is divided into intervals. During an interval, each application’s shared request service rate and alpha are measured.
And alone request service rate is estimated.
At the end of the interval, slowdown is estimated as a function of these three quantities.
This repeats during every interval.
Now, let us look at how each of these quantities is measured/estimated.

## Slide 24: A More Accurate and Simple Model
More accurate: Takes into account request overlap behavior
  Implicit through aggregate estimation of cache access rate and miss service time
  Unlike prior works that estimate per-request interference
Simpler hardware: Amenable to set sampling in the auxiliary tag store
  Need to measure only contention miss count
  Unlike prior works that need to know if each request is a contention miss or not

## Slide 25: Outline
Quantify Slowdown
  Key Observation
  Estimating Cache Access Rate Alone
  ASM: Putting it All Together
  Evaluation
Control Slowdown
  Slowdown-aware Cache Capacity Allocation
  Slowdown-aware Memory Bandwidth Allocation

## Slide 26: Previous Work on Slowdown Estimation
Previous work on slowdown estimation
  STFM (Stall Time Fair Memory) Scheduling [Mutlu et al., MICRO ’07]
  FST (Fairness via Source Throttling) [Ebrahimi et al., ASPLOS ’10]
  Per-thread Cycle Accounting [Du Bois et al., HiPEAC ’13]
Basic Idea:
Count interference cycles experienced by each request
Slowdown
Notes: The most relevant previous works on slowdown estimation are STFM, stall time fair memory scheduling and FST, fairness via source throttling.
FST employs similar mechanisms as STFM for memory-induced slowdown estimation, therefore, I will focus on STFM for the rest of the evaluation.
STFM estimates slowdown as the ratio of alone to shared stall times.
Stall time shared is easy to measure, analogous to shared request service rate
Stall time alone is harder and STFM estimates it by counting the number of cycles an application receives interference from other applications.

## Slide 27: Methodology
Configuration of our simulated system
  4 cores
  1 channel, 8 banks/channel
  DDR3 1333 DRAM
  2MB shared cache
Workloads
  SPEC CPU2006 and NAS
  100 multiprogrammed workloads
Notes: Next, I will quantitatively compare MISE and STFM. Before that, let me present our methodology.
We carry out our evaluations on a 4-core, 1-channel DDR3 1066 DRAM system.
Our workloads are composed of SPEC CPU 2006 applications. We build 300 multiprogrammed workloads from these applications.

## Slide 28: Model Accuracy Results
Select applications
Chart: Slowdown Estimation Error (in %)
| calculix | povray | tonto | namd | dealII | sjeng | perlbench | gobmk | xalancbmk | sphinx3 | GemsFDTD | omnetpp | lbm | leslie3d | soplex | milc | libq | mcf | NPBbt | NPBft | NPBis | NPBua | Average
FST | 0.41045 | 2.0079 | 5.1953 | 1.8752 | 31.7637 | 3.9164 | 5.0801 | 5.7555 | 10.2045 | 28.8548 | 53.2408 | 33.9099 | 85.5316 | 23.7095 | 78.2879 | 28.8525 | 21.6335 | 144.5315 | 0 | 29.7229 | 45.8772 | 32.1654 | 29.737 | 0 | 29.3729
PTCA | 1.9106 | 3.68 | 7.5351 | 4.5745 | 32.2882 | 10.317 | 35.1831 | 16.1571 | 27.705 | 6.4247 | 32.3625 | 22.1458 | 33.7427 | 19.2084 | 81.8627 | 11.1493 | 104.3351 | 108.3397 | 0 | 3.1958 | 133.656 | 9.1995 | 69.8224 | 0 | 40.3875
ASM | 11.8215 | 1.6467 | 5.8829 | 3.6925 | 9.8046 | 7.3422 | 10.7283 | 6.569 | 6.5517 | 7.5311 | 11.4907 | 12.3207 | 13.0691 | 5.7255 | 9.5044 | 8.1542 | 2.8033 | 23.1982 | 0 | 2.5694 | 14.7302 | 7.6906 | 4.199 | 0 | 9.8567
Average error of ASM’s slowdown estimates: 10%
Previous models have 29%/40% average error

## Slide 29: Outline
Quantify Slowdown
  Key Observation
  Estimating Cache Access Rate Alone
  ASM: Putting it All Together
  Evaluation
Control Slowdown
  Slowdown-aware Cache Capacity Allocation
  Slowdown-aware Memory Bandwidth Allocation
  Coordinated Cache/Memory Management

## Slide 30: Outline
Quantify Slowdown
  Key Observation
  Estimating Cache Access Rate Alone
  ASM: Putting it All Together
  Evaluation
Control Slowdown
  Slowdown-aware Cache Capacity Allocation
  Slowdown-aware Memory Bandwidth Allocation
  Coordinated Cache/Memory Management

## Slide 31: Cache Capacity Partitioning
Main Memory
Shared
Cache
Core
Core
Previous partitioning schemes mainly focus on miss count reduction
Problem: Does not directly translate to performance and slowdowns

## Slide 32: ASM-Cache: Slowdown-aware Cache Capacity Partitioning
Goal: Achieve high fairness and performance through slowdown-aware cache partitioning
Key Idea: Allocate more cache space to applications whose slowdowns reduce the most with more cache space

## Slide 33: Outline
Quantify Slowdown
  Key Observation
  Estimating Cache Access Rate Alone
  ASM: Putting it All Together
  Evaluation
Control Slowdown
  Slowdown-aware Cache Capacity Allocation
  Slowdown-aware Memory Bandwidth Allocation
  Coordinated Cache/Memory Management

## Slide 34: Memory Bandwidth Partitioning
Main Memory
Shared
Cache
Core
Core
Goal: Achieve high fairness and performance through slowdown-aware bandwidth partitioning

## Slide 35: ASM-Mem: Slowdown-aware Memory Bandwidth Partitioning
Key Idea: Prioritize an application proportionally to its slowdown
Application i’s requests prioritized at the memory controller for its fraction

## Slide 36: Outline
Quantify Slowdown
  Key Observation
  Estimating Cache Access Rate Alone
  ASM: Putting it All Together
  Evaluation
Control Slowdown
  Slowdown-aware Cache Capacity Allocation
  Slowdown-aware Memory Bandwidth Allocation
  Coordinated Cache/Memory Management

## Slide 37: Coordinated Resource Allocation Schemes
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Core
Main Memory
Shared
Cache
Cache capacity-aware
bandwidth allocation
1. Employ ASM-Cache to partition cache capacity
2. Drive ASM-Mem with slowdowns from ASM-Cache

## Slide 38: Fairness and Performance Results
16-core system 100 workloads
14%/8% unfairness reduction on 1/2 channel systems compared to PARBS+UCP with similar performance
Chart: Number of Channels
FRFCFS-NoPart | 10.498 | 6.9257
FRFCFS+UCP | 9.4748 | 6.0393
TCM+UCP | 10.4292 | 6.592
PARBS+UCP | 9.3348 | 6.033
ASM-Cache-Mem | 7.9617 | 5.5061
Chart: Number of Channels
FRFCFS-NoPart | 0.212 | 0.30811
FRFCFS+UCP | 0.20694 | 0.30879
TCM+UCP | 0.19336 | 0.28617
PARBS+UCP | 0.21259 | 0.31157
ASM-Cache-Mem | 0.20928 | 0.30633

## Slide 39: Other Results in the Paper
Distribution of slowdown estimation error
Sensitivity to system parameters
  Core count, memory channel count, cache size
Sensitivity to model parameters
Impact of prefetching
Case study showing ASM’s potential for providing slowdown guarantees

## Slide 40: Summary
Problem: Uncontrolled memory interference cause high and unpredictable application slowdowns
Goal: Quantify and control slowdowns
Key Contribution:
  ASM: An accurate slowdown estimation model
  Average error of ASM: 10%
Key Ideas:
  Shared cache access rate is a proxy for performance
  Cache Access Rate Alone can be estimated by minimizing memory interference and quantifying cache interference
Applications of Our Model
  Slowdown-aware cache and memory management to achieve high performance, fairness and performance guarantees
Source Code Release by January 2016

## Slide 41: Quantifying and Controlling Impact of Interference at Shared Caches and Main Memory
Lavanya Subramanian, Vivek Seshadri,
Arnab Ghosh, Samira Khan, Onur Mutlu
Application Slowdown Model

## Slide 42: Backup

## Slide 43: Highest Priority Minimizes Memory Bandwidth Interference
Request Buffer State
Main Memory
1. Run alone
Time units
Service order
Main Memory
1
2
Request Buffer State
Main Memory
2. Run with another application
Service order
Main Memory
1
2
3
Request Buffer State
Main Memory
3. Run with another application: highest priority
Service order
Main Memory
1
2
3
Time units
Time units
3
Notes: Here is an example.
An application, let’s call it the red application, is run by itself on a system. Two of its requests are queued at the memory controller request buffers. Since these are the only two requests queued up for main memory at this point, the memory controller schedules them back to back and they are serviced in two time units.
Now, the red application is run with another application, the blue application. The blue application’s request makes its way between two of the red application’s requests. A naïve memory scheduler could potentially schedule the requests in the order in which they arrived, delaying the red application’s second request by one time unit, as compared to when the application was run alone.
Next, let’s consider running the red and blue applications together, but give the red application highest priority. In this case, the memory scheduler schedules the two requests of the red application back to back, servicing them in two time units. Therefore, when the red application is given highest priority, its requests are serviced as though the application were run alone.

## Slide 44: Accounting for Queueing
A cycles is a queueing cycle if
  a request from the highest priority application is outstanding and
  the previously scheduled request was from another application
CAR Alone

## Slide 45: Impact of Cache Capacity Contention
Cache capacity interference causes high application slowdowns
Shared Main Memory
Shared Main Memory and Caches
Chart: Slowdown
| bzip2 (core 0) | soplex (core 1)
Slowdown | 1.36 | 1.1
Chart: Slowdown
| bzip2 (core 0) | soplex (core 1)
Slowdown | 1.86 | 1.48

## Slide 46: Error with No Sampling

## Slide 47: Error Distribution

## Slide 48: Miss Service Time Distributions

## Slide 49: Impact of Prefetching

## Slide 50: Sensitivity to Epoch and Quantum Lengths

## Slide 51: Sensitivity to Core Count

## Slide 52: Sensitivity to Cache Capacity

## Slide 53: Sensitivity to Auxiliary Tag Store Sampling

## Slide 54: ASM-Cache: Fairness and Performance Results
Significant fairness benefits across different systems
Chart: Number of Cores
| 4 | 8 | 16
NoPart | 2.0956 | 4.7684 | 13.7536
UCP | 1.8479 | 4.3221 | 12.1485
ASM-Cache | 1.8346 | 3.7867 | 10.2182
Chart: Number of Cores
| 4 | 8 | 16
NoPart | 0.60539 | 0.35515 | 0.16049
UCP | 0.64109 | 0.36832 | 0.17
ASM-Cache | 0.63244 | 0.36993 | 0.18

## Slide 55: ASM-Cache: Fairness and Performance Results

## Slide 56: ASM-Mem: Fairness and Performance Results
Chart: Number of Cores
| 4 | 8 | 16
FRFCFS | 2.0956 | 4.5308 | 13.7536
TCM | 2.1267 | 4.8042 | 17.3192
PARBS | 2.0376 | 4.5488 | 18.5194
ASM-Mem | 2.0046 | 4.3129 | 12.0891
Chart: Number of Cores
| 4 | 8 | 16
FRFCFS | 0.60539 | 0.36787 | 0.16049
TCM | 0.58838 | 0.34883 | 0.14305
PARBS | 0.61121 | 0.3704 | 0.14866
ASM-Mem | 0.60238 | 0.3609 | 0.16044
Significant fairness benefits across different systems

## Slide 57: ASM-QoS: Meeting Slowdown Bounds
Chart: Slowdown
| h264ref | mcf | sphinx3 | soplex
Naive-QoS | 2.1735 | 2.395 | 3.7317 | 3.2826
ASM-QoS-2.5 | 2.3009 | 2.0314 | 3.2274 | 2.8803
ASM-QoS-3 | 2.4396 | 1.9874 | 3.2151 | 2.7853
ASM-QoS-3.5 | 2.576 | 1.9762 | 3.1915 | 2.7442
ASM-QoS-4 | 2.6616 | 1.9711 | 3.1823 | 2.6657

## Slide 58: Previous Approach: Estimate Interference Experienced Per-Request
Shared
(With interference)
time
Execution time
Req A
Req B
Req C
Request Overlap Makes Interference Estimation Per-Request Difficult

## Slide 59: Estimating PerformanceAlone
Shared
(With interference)
Execution time
Req A
Req B
Req C
Request Queued
Request Served
Difficult to estimate impact of interference per-request due to request overlap

## Slide 60: Impact of Interference on Performance
Alone
(No interference)
time
Execution time
Shared
(With interference)
time
Execution time
Impact of Interference
Previous Approach: Estimate impact of interference at a per-request granularity
Difficult to estimate due to request overlap