## Slide 1: RFVP: Rollback-Free Value Prediction with Safe to Approximate Loads
Amir Yazdanbakhsh,
Bradley Thwaites,
Hadi Esmaeilzadeh
Gennady Pekhimenko, Onur Mutlu,
Todd C. Mowry
Georgia Institute of Technology
Carnegie Mellon University

## Slide 2: Executive Summary
Problem: Performance of modern GPUs significantly limited by the available off-chip bandwidth
Observations:
  Many GPU applications are amenable to approximation
  Data value similarity allows to efficiently predict values of cache misses
Key Idea: Use simple value prediction mechanisms to avoid accesses to main memory when it is safe
Results:
  Higher speedup (36% on average) with less than 10% quality loss
  Lower energy consumption (27% on average)

## Slide 3
Virtual Reality
Data Analytics
Robotics
Multimedia
GPU

## Slide 4
Virtual Reality
Data Analytics
Robotics
Multimedia
Many GPU applications are limited by the off-chip bandwidth

## Slide 5: Motivation: Bandwidth Bottleneck
Chart: Speedup
0.5x | 0.78 | 0 | 0 | 0 | 0.61 | 0 | 0 | 0 | 0.93 | 0 | 0 | 0 | 0.97587 | 0 | 0 | 0 | 0.98 | 0 | 0 | 0 | 0.89 | 0 | 0 | 0 | 0.99228 | 0 | 0 | 0 | 0.99 | 0 | 0 | 0 | 0.76 | 0 | 0 | 0 | 0.99 | 0.88526
1x | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
1x | 0 | 0 | 0 | 0 | 0
2x | 0 | 1.06 | 0 | 1.49 | 1.07 | 1.1226 | 1.48 | 1.25 | 1.4877 | 1.03 | 1.78 | 1.2 | 1.2583
4x | 0 | 0 | 1.07 | 1.72 | 1.1 | 1.1864 | 1.82 | 1.36 | 1.7889 | 1.05 | 2 | 1.29 | 1.3725
8x | 0 | 0 | 0 | 1.07 | 1.75 | 1.11 | 1.2042 | 1.94 | 1.4 | 1.8932 | 1.05 | 2.03 | 1.33 | 1.4045
Perfect Memory | 0 | 0 | 0 | 0 | 1.1408 | 0 | 0 | 0 | 0 | 1.9542 | 0 | 0 | 0 | 0 | 1.8978 | 0 | 0 | 0 | 0 | 1.2412 | 0 | 0 | 0 | 0 | 13.6465 | 0 | 0 | 0 | 0 | 0 | 2.4722 | 0 | 0 | 0 | 0 | 13.5378 | 0 | 0 | 0 | 0 | 1.3811 | 0 | 0 | 0 | 0 | 2.5864 | 0 | 0 | 0 | 0 | 0 | 4.0094 | 0 | 0 | 0 | 0 | 2.6488
13.7
2.5
13.5
2.6
4.0
2.6
backprop
fastwalsh
gaussian
heartwall
matrixmul
particlefilter
similarityscore
s.reduce
s.srad2
stringmatch
geomean
Off-chip bandwidth is a major performance bottleneck
Notes: GPGPU applications from Rodinia, MapReduce, Nvidia CUDA SDK.

## Slide 6: Only Few Loads Matters
Chart: 
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10
backprop | 0.31531 | 0.62872 | 0.93712 | 0.97008 | 0.99999 | 1 | 1 | 1 | 1 | 1
fastwalsh | 0.19565 | 0.3913 | 0.58696 | 0.78261 | 0.91304 | 0.95652 | 1 | 1 | 1 | 1
gaussian | 0.2957 | 0.54585 | 0.7728 | 0.99976 | 1 | 1 | 1 | 1 | 1 | 1 | 1
heartwall | 0.11412 | 0.22738 | 0.32484 | 0.42015 | 0.51342 | 0.60457 | 0.69273 | 0.77199 | 0.85043 | 0.92524 | 1
matrixmul | 0.33106 | 0.55177 | 0.77248 | 0.8699 | 0.93696 | 0.99534 | 0.99855 | 0.9996 | 0.99981 | 1 | 1
particlefilter | 0.26923 | 0.43376 | 0.58333 | 0.71688 | 0.85043 | 0.96154 | 0.97329 | 0.98291 | 0.99145 | 0.99679 | 1
reduce | 0.49965 | 0.99908 | 0.99954 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
similarityscore | 0.69141 | 0.78986 | 0.86863 | 0.90802 | 0.94375 | 0.97344 | 0.99084 | 0.99379 | 0.99645 | 0.99839 | 1
srad2 | 0.1657 | 0.33141 | 0.49711 | 0.66281 | 0.82852 | 0.98715 | 0.9944 | 0.9956 | 0.99657 | 0.99692 | 1
stringmatch | 0.46394 | 0.86136 | 0.87275 | 0.88287 | 0.89299 | 0.89418 | 0.89426 | 0.89426 | 0.89426 | 0.89426 | 1
Percentage of Load Misses
Number of Loads
Few GPU instructions generate most of the cache misses

## Slide 7
Virtual Reality
Data Analytics
Robotics
Multimedia
Many GPU applications are also amenable to approximation

## Slide 8: Rollback-Free Value Prediction
Key idea:
Predict values for safe-to-approximate loads when they miss in the cache
Design principles:
No rollback/recovery, only value prediction
Drop rate is a tuning knob
Other requests are serviced normally
Providing safety guarantees

## Slide 9: RFVP: Diagram
GPU
Memory
Hierarchy
Cores
L1 Data Cache
RFVP
Value Predictor

## Slide 10: Code Example to Support Intuition
float newVal = 0;
for (int i=0; i<N; i++) {
float4 v1 = matrix1[i];
float4 v2 = matrix2[i];
newVal += v1.x * v2.x;
newVal += v1.y * v2.y;
newVal += v1.z * v2.z;
newVal += v1.w * v2.w;
}
Matrixmul:

## Slide 11: Code Example to Support Intuition (2)
int d_cN, d_cS, d_cW, d_cE;
d_cN = d_c[ei];
d_cS = d_c[d_iS[row] + d_Nr * col];
d_cW = d_c[ei];
d_cE = d_c[row + d_Nr * d_jE[col]];
s.srad2:

## Slide 12: Outline
Motivation
Key Idea
RFVP Design and Operation
Evaluation
Conclusion

## Slide 13: RFVP Architecture Design
Instruction annotations by the programmer
ISA changes
  Approximate load instruction
  Instruction for setting the drop rate
Defining approximate load semantics
Microarchitecture Integration

## Slide 14: Programmer Annotations
Safety is a semantic property of the program
We rely on the programmer to annotate the code

## Slide 15: ISA Support
Approximate Loads
load.approx Reg<id>, MEMORY<address>
is a probabilistic load - can assign precise or imprecise value to Reg<id>
Drop rate
set.rate DropRateReg
sets the fraction (e.g., 50%) of the approximate cache misses that do not initiate memory requests

## Slide 16: Microarchitecture Integration
Memory
Hierarchy
Cores
RFVP
Value Predictor
L1 Data Cache
Cores
RFVP
Value Predictor
L1 Data Cache
Cores
RFVP
Value Predictor
L1 Data Cache
Cores
RFVP
Value Predictor
L1 Data Cache
SM

## Slide 17: Microarchitecture Integration
Memory
Hierarchy
Cores
RFVP
Value Predictor
L1 Data Cache
Cores
RFVP
Value Predictor
L1 Data Cache
Cores
RFVP
Value Predictor
L1 Data Cache
Cores
RFVP
Value Predictor
L1 Data Cache
Memory Request
All the L1 misses are sent to the memory subsystem
DATA
SM

## Slide 18: Microarchitecture Integration
Memory
Hierarchy
Cores
RFVP
Value Predictor
L1 Data Cache
Cores
RFVP
Value Predictor
L1 Data Cache
Cores
RFVP
Value Predictor
L1 Data Cache
Cores
RFVP
Value Predictor
L1 Data Cache
Memory Request
A fraction of the requests will be handled by RFVP
DATA
SM

## Slide 19: Language and Software Support
Targeting performance critical loads
  Only a few critical instructions matter for value prediction
Providing safety guarantees
  Programmer annotations and compiler passes
Drop-rate selection
  A new knob that allows to control quality vs. performance tradeoffs

## Slide 20: Base Value Predictor: Two-Delta Stride
+
Last Value
Stride1
Stride2
Hash (PC)
Predicted Value

## Slide 21: Designing RFVP predictor for GPUs
+
Last Value
Stride1
Stride2
Hash (PC)
Predicted Value
How to design a predictor for GPUs with,
for example, 32 threads per warp?

## Slide 22: GPU Predictor Design and Operation
+
Last Value
Stride1
Stride2
Hash (PC)
+
+
+
1
2
…
16
17
18
…
32
Last Value
Stride1
Stride2
Predicted Value
Predicted Value
warp
(32 threads)

## Slide 23: Outline
Motivation
Key Idea
RFVP Design and Operation
Evaluation
Conclusion

## Slide 24: Methodology
Simulator
GPGPU-Sim simulator (cycle-accurate) ver. 3.1
Workloads
GPU benchmarks from Rodinia, Nvidia SDK, and Mars benchmark suites
System Parameters
GPU with 15 SMs, 32 threads/warp, 6 memory channels,
48 warps/SM, 32KB shared memory, 768KB LLC, GDDR5
177.4 GB/sec off-chip bandwidth

## Slide 25: RFVP Performance
backprop
fastwalsh
gaussian
heartwall
matrixmul
particlefilter
similarityscore
s.reduce
s.srad2
stringmatch
geomean
Speedup
Chart: 
| backprop | fastwalshtransform | gaussian | heartwall | matrixmul | particle filter | similarity score | s.reduce | s.srad2 | stringmatch | average
Error < 1% | 1.03 | 1.11 | 1 | 1.05 | 1 | 1.22 | 1.11 | 1.01 | 1.09 | 1 | 1.0599
Error < 3% | 1.06 | 1.11 | 1 | 1.05 | 1.1 | 1.22 | 1.28 | 1.01 | 1.09 | 1 | 1.0886
Error < 5% | 1.06 | 1.13 | 1.13 | 1.05 | 1.21 | 1.22 | 1.59 | 1.01 | 1.32 | 1 | 1.1609
Error < 10% | 1.08 | 1.13 | 1.44 | 1.06 | 2.2 | 1.47 | 2.36 | 1.12 | 1.37 | 1 | 1.3611
2.2
2.4
Significant speedup for various acceptable quality rates

## Slide 26: RFVP Bandwidth Consumption
Chart: 
| backprop | fastwalshtransform | gaussian | heartwall | matrixmul | particle filter | similarity score | s.reduce | s.srad2 | stringmatch | average
Error < 1% | 1.12 | 1.34 | 1 | 1.18 | 1 | 1.09 | 1.14 | 1.7 | 1.09 | 1 | 1.1509
Error < 3% | 1.34 | 1.34 | 1 | 1.18 | 1.14 | 1.09 | 1.14 | 1.7 | 1.09 | 1 | 1.1872
Error < 5% | 1.34 | 1.44 | 1.09 | 1.18 | 1.32 | 1.09 | 1.67 | 1.7 | 1.34 | 1 | 1.2981
Error < 10% | 1.48 | 1.44 | 1.37 | 1.25 | 1.86 | 1.22 | 1.96 | 2.29 | 1.32 | 1 | 1.476
backprop
fastwalsh
gaussian
heartwall
matrixmul
particlefilter
similarityscore
s.reduce
s.srad2
stringmatch
geomean
BW Consumption Reduction
1.9
2.0
Reduction in consumed bandwidth (up to 1.5X average)
2.3

## Slide 27: RFVP Energy Reduction
Chart: 
| backprop | fastwalshtransform | gaussian | heartwall | matrixmul | particle filter | similarity score | s.reduce | s.srad2 | stringmatch | average
Error < 1% | 1.03 | 1.12 | 1 | 1.04 | 1 | 1.2 | 1.1 | 1.05 | 1.06 | 1 | 1.0583
Error < 3% | 1.05 | 1.12 | 1 | 1.04 | 1.1 | 1.2 | 1.1 | 1.05 | 1.06 | 1 | 1.0705
Error < 5% | 1.05 | 1.13 | 1.06 | 1.04 | 1.21 | 1.2 | 1.57 | 1.05 | 1.21 | 1 | 1.1425
Error < 10% | 1.06 | 1.13 | 1.15 | 1.05 | 1.94 | 1.37 | 1.98 | 1.13 | 1.23 | 1 | 1.266
backprop
fastwalsh
gaussian
heartwall
matrixmul
particlefilter
similarityscore
s.reduce
s.srad2
stringmatch
geomean
Energy Reduction
1.9
2.0
Reduction in consumed energy (27% on average)
1.6

## Slide 28: Sensitivity to the Value Prediction
Two-Delta predictor was the best option
Chart: 
| backprop | fastwalsh | gaussian | heartwall | matrixmul | particlefilter | similarityscore | s.reduce | s.srad2 | stringmatch | geomean
Null Predictor | 1 | 1 | 1.02 | 1.01 | 1.06 | 1.02 | 1.04 | 1.01 | 1 | 1 | 1.0158
Last-Value Predictor | 1.02 | 1.11 | 1.32 | 1.05 | 1.56 | 1.12 | 1.58 | 1.05 | 1.28 | 1 | 1.1926
Two-Delta Predictor | 1.08 | 1.13 | 1.44 | 1.06 | 2.2 | 1.47 | 2.36 | 1.12 | 1.37 | 1 | 1.3611
Speedup
2.2
2.4

## Slide 29: Other Results and Analyses in the Paper
Sensitivity to the drop rate (energy and quality)
Precise vs. imprecise value distributions
RFVP for memory latency wall
  CPU performance
  CPU energy reduction
  CPU quality vs. performance tradeoff

## Slide 30: Conclusion
Problem: Performance of modern GPUs significantly limited by the available off-chip bandwidth
Observations:
  Many GPU applications are amenable to approximation
  Data value similarity allows to efficiently predict values of cache misses
Key Idea: Use simple rollback-free value prediction mechanism to avoid accesses to main memory
Results:
  Higher speedup (36% on average) with less than 10% quality loss
  Lower energy consumption (27% on average)

## Slide 31: RFVP: Rollback-Free Value Prediction with Safe to Approximate Loads
Amir Yazdanbakhsh,
Bradley Thwaites,
Hadi Esmaeilzadeh
Gennady Pekhimenko, Onur Mutlu,
Todd C. Mowry
Georgia Institute of Technology
Carnegie Mellon University

## Slide 32: Sensitivity to the Drop Rate
Chart: 
| backprop | gaussian | srad2 | fastwalsh | heartwall | matrixmul | dwt | particlefilter | similarityscore | reduce | stringnmatch | geomean
Drop Rate = 12.5% | 1.02 | 1.06 | 1.06 | 1.05 | 1.1 | 1.11 | 1.11 | 1.01 | 1.09 | 1.07 | 1.0675
Drop Rate = 25% | 1.03 | 1.09 | 1.13 | 1.06 | 1.21 | 1.22 | 1.28 | 1.01 | 1.16 | 1.61 | 1.1697
Drop Rate = 50% | 1.05 | 1.11 | 1.27 | 1.09 | 1.56 | 1.38 | 1.59 | 1.01 | 1.32 | 1.78 | 1.2934
Drop Rate = 75% | 1.08 | 1.17 | 1.44 | 1.13 | 3.29 | 1.47 | 3.77 | 1.12 | 1.43 | 2 | 1.6142
Drop Rate = 80% | 1.09 | 1.19 | 1.49 | 1.15 | 4.18 | 1.51 | 4.73 | 1.13 | 1.47 | 2.2 | 1.7317
Drop Rate = 90% | 1.1 | 1.22 | 1.58 | 1.19 | 8.25 | 1.65 | 9.12 | 1.15 | 1.57 | 3.49 | 2.1357
backprop
fastwalsh
gaussian
heartwall
matrixmul
particlefilter
similarityscore
s.reduce
s.srad2
stringmatch
geomean
Speedup
Speedup varies significantly with different drop rates

## Slide 33: Pareto Analysis
Pareto-optimal is the configuration with 192 entries and 2 independent predictors for 32 threads