## Slide 1: Rollback-Free Value Prediction with Approximate Loads
Georgia Institute of Technology
Carnegie Mellon University
Hadi Esmaeilzadeh | Onur Mutlu | Todd Mowry
Bradley Thwaites | Gennady Pekhimenko | Amir Yazdanbakhsh
Jongse Park | Girish Mururu

## Slide 2: Mitigating Memory Wall with Approximation
Rollback-Free Value Prediction
  Microarchitecturally-triggered approximation
  Predict the value of an approximate load when it misses in the cache
  Do not check for mispredictions
  Do not rollback from mispredictions
  Mitigate long latency memory accesses

## Slide 3: Rollback Free Value Prediction

## Slide 4: Design Principles
Maximize opportunities for performance and energy benefits
Minimize the adverse effects of approximation on quality degradation

## Slide 5: Design Challenges and Solutions
Target Performance-Critical Safe Loads
  Profile-directed compilation
  Usually, < 32 loads cause 80% of cache misses
Utilize Fast-Learning Predictors
  Two-delta stride predictor
  Prediction: table lookup plus an addition
Integrate RFVP with existing architecture
Notes: Predictor keeps track of the previous values and just by a simple table lookup and then addition
For the microarchitecture integration we refer you to the paper

## Slide 6: Experimental Results with a Modern OoO Processor
8%
19%
Average
Maximum
0.8%
1.8%
Average
Maximum
More CPU configurations and value predictors are in the paper
Chart: Two-Delta Value Prediction - Quality Loss
| swim | fma3d | bwaves | mcf | cactusadm | soplex | gemsfdtd | geomean
 | 0.002 | 0.016 | 0.018 | 0 | 0.003 | 0.0175 | 0
Chart: 2MB LLC, 4-Wide, Performance Results
| swim | fma3d | bwaves | mcf | cactusadm | soplex | gemsfdtd | geomean
 | 1.1924 | 1.045 | 1.1024 | 0.99991 | 1.0787 | 1.0827 | 1.073
Notes: The quality loss and the benefits are one order magnitude different

## Slide 7: Ongoing Work
Extend rollback-free value prediction to GPUs
Drop a fraction of the missed requests
Preliminary results: Up to 2x improvement in energy and performance with only 10% quality degradation
Mitigate both Memory Wall and Bandwidth Wall