## Slide 1
Rollback-Free Value Prediction with Approximate Loads
Bradley Thwaites, Gennady Pekhimenko, Amir Yazdanbakhsh, Jongse Park, Girish Mururu
Hadi Esmaeilzadeh, Onur Mutlu, Todd C. Mowry
RFVP Overview
Design Principles
Design Challenges
Key Experimental Results
Ongoing Work
Motivation
  Mitigate long latency memory accesses
  Microarchitecturally-triggered approximation
  Predict the value of an approximate load when it misses in the cache
  Do not check for mispredictions
  Do not rollback from mispredictions
Chart: Performance Benefit
| swim | fma3d | bwaves | mcf | cactusADM | soplex | GemsFDTD | geomean
 | 1.2663 | 1.0841 | 1.8532 | 5.0604 | 1.2831 | 3.8765 | 4.7564
Perfect Prediction
Maximize opportunities for performance and energy benefits
Minimize the adverse effects of approximation on quality degradation
(0%, 0%, 0%)
(1.06x, 1.03x, 2%)
(1.13x, 1.06x, 6%)
(1.27x, 1.10x, 11%)
Extend rollback-free value prediction to GPUs
Drop a fraction of the missed requests
Preliminary results: Up to 2x improvement in
energy and performance
with only 10% quality degradation
Mitigate both Memory Wall and Bandwidth Wall
Chart: Performance Benefit
| swim | fma3d | bwaves | mcf | cactusADM | soplex | GemsFDTD | geomean
 | 1.1924 | 1.045 | 1.1024 | 0.99991 | 1.0787 | 1.0827 | 1.073
2MB LLC, 4-Wide, Performance Results
Target Performance-Critical Safe Loads
  Profile-directed compilation
  Usually, < 32 loads cause 80% of cache misses
Utilize Fast-Learning Predictors
  Two-delta stride predictor
  Prediction: table lookup plus an addition
Integrate RFVP with existing architecture
Chart: Value Prediction - Quality Loss
| swim | fma3d | bwaves | mcf | cactusADM | soplex | GemsFDTD
Stride | 0.177 | 0.154 | 0.028 | 0 | 0.183 | 0.195 | 0.021
TwoDelta | 0.002 | 0.016 | 0.018 | 0 | 0.003 | 0.0175 | 0
(Performance Gain, Energy Gain, Quality Loss)