## Slide 1
Lois Orosa, Rodolfo Azevedo and Onur Mutlu
AVPP:
Address-first Value-next Predictor
with Value Prefetching for Improving the Efficiency of Load Value Prediction

## Slide 2
  Motivation: single-thread performance is critical for many applications
  Problem: improving single-thread performance in modern processors requires techniques that significantly increase the hardware cost
  Goal: revisit Load Value Prediction as an efficient way to improve single-thread performance
  Contributions:
  We propose optimizations for reducing the hardware cost of load value prediction
  We propose a new taxonomy of Value Prediction Policies
  AVPP:
    New load value predictor that predicts the address first and the value next.
    Increases the coverage of the predictor by prefetching the value of a future instance of the load instruction
Results:
AVPP outperforms all state-of-the-art value predictors in the context of load value prediction, and it is less complex than predicting all instructions
AVPP provides 11.2% system performance improvement and 3.7% energy savings compared to no value prediction.
Executive Summary
Notes: To begin, I will give a brief overview. [CLICK] many applications are limited by the single thread performance. [CLICK] The problem is that achieving performance benefits require significant hardware cost [CLICK] The goal is to revisit load value prediction as a low cost alternative to improve single-thread performance. We propose [CLICK] AVPP, a mechanism

## Slide 3
Motivation and Goal
Motivation and Goal
Background
Reducing Hardware Complexity
Taxonomy of Value Prediction
Mechanism: AVPP
Evaluation and Results
Conclusion
AVPP Outline
Notes: Here is the outline for the talk today [CLICK]

## Slide 4
Motivation and Goal
Motivation and Goal
Background
Reducing Hardware Complexity
Taxonomy of Value Prediction
Mechanism: AVPP
Evaluation and Results
Conclusion
AVPP Outline
Notes: Here is the outline for the talk today [CLICK]

## Slide 5: Motivation and Goal
True data dependencies limit single-thread performance significantly
We simulate an oracle predictor that predicts the output of instructions correctly:
We observe that an oracle predictor achieves almost the same performance predicting load instructions as predicting all instructions
Predicting all instructions requires large predictors
Our goal is revisit Load Value Prediction as a low-cost alternative to improve single-thread performance
32%
28%

## Slide 6
Motivation and Goal
Motivation and Goal
Background
Reducing Hardware Complexity
Taxonomy of Value Prediction
Mechanism: AVPP
Evaluation and Results
Conclusion
AVPP Outline
Notes: Here is the outline for the talk today [CLICK]

## Slide 7
Background: Value Prediction
True Data Dependency:
Value Prediction breaks true data dependencies by predicting values and performing speculative execution
  Prediction: the output value of instr_0 (A)
  Speculation: executes instr_1 using the predicted value of A
  instr_0 and instr_1 are executed in parallel
Requires a Rollback mechanism to recover from mispredictions
instr_0: A = B + 1
instr_1: C = A + 3
Read-After-Write (RAW)
Depends on the result of the previous instruction

## Slide 8
State-of-the-art Value Predictors
Last Value Predictor (LVP) [Lipasti+ MICRO’96]
  The predicted value is the last value
Stride Predictor (Stride) [Mendelson+ TR’96]
  The predicted value is the last value + stride
  2D-Stride [Eickemeyer+ IBM Journal’93]: variant that improves performance in loops
Finite Context Method (FCM) predictor [Sazeides+ TR’97]
  Context based predictor
  Large prediction tables
  D-FCM [Goeman+ HPCA’01]: variant that uses strides
VTAGE [Perais+ HPCA’14]
  Uses global branch history
  D-VTAGE [Perais+ HPCA’15]: variant that uses strides
Notes: Add figure to explain one of then

## Slide 9
Motivation and Goal
Motivation and Goal
Background
Reducing Hardware Complexity
Taxonomy of Value Prediction
Mechanism: AVPP
Evaluation and Results
Conclusion
AVPP Outline
Notes: Here is the outline for the talk today [CLICK]

## Slide 10
Reducing Hardware Complexity
Predicting only load instructions instead of predicting all instructions has some advantages:
  Decrease the hardware cost: we show that load value predictors have a smaller area footprint
  Less pressure over shared resources (e.g., Physical Register File): we show how to reduce the number of ports in the paper
  We leverage the Load Queue for implementing load value prediction
Load Instructions are 25% of all instructions on average
Small modifications to support Load Value Prediction
Notes: Add figure to explain one of then

## Slide 11
Previous Works on Reducing Complexity of Value Prediction
AVPP
512
11.2%
Minimal hardware Modifications to an OoO processor
Load Value Prediction:
Main contribution for reducing complexity
Work
[Perais+ HPCA’14]
EOLE [Perais+ ISCA’14]
BeBOP
[Perais+ HPCA’15]
[Perais+ MICRO’16]
Predictor Entries
8192
8192
2048
2048
Speedup
~10%
~10%
11.2%
5%
- Introduces Confidence
Counters
-
Reduces the extra ports
required on the PRF
-
Increases the
complexity of the in-order
front-end and back-end
Single predictor entry for a
cache line
-
Register reuse
-
Low hardware cost
- Simple mechanism to
recover from
value mispredictions
Value prediction for all instructions:
Notes: Add figure to explain one of then

## Slide 12
Motivation and Goal
Motivation and Goal
Background
Reducing Hardware Complexity
Taxonomy of Value Prediction
Mechanism: AVPP
Evaluation and Results
Conclusion
AVPP Outline
Notes: Here is the outline for the talk today [CLICK]

## Slide 13
Taxonomy of Value Prediction Policies
We propose a new taxonomy for analyzing value prediction design choices
  Predictor update
  Prediction availability
  In-flight pending updates

## Slide 14
Taxonomy: Predictor Update Policies
  Where is the predictor updated in the pipeline?
  Correct update:
    The predictor is updated at the commit stage
  Speculative update:
    The predictor is updated at the fetch stage

## Slide 15
Taxonomy: Prediction Availability Policies
  What happens when the prediction is not ready at dispatch time?
  Delay dispatch
    The pipeline is stalled waiting for the prediction
  Not-delay dispatch
    The prediction is discarded

## Slide 16
Taxonomy: In-flight Pending Update Policies
  What happens with back-to-back predictions?
  In-flight ignore
    The predictor ignores previous in-flight instructions
  In-flight wait
    The predictor waits for previous in-flight instructions to update the predictor

## Slide 17
Taxonomy
  We evaluate different combinations of these policies for all predictors we evaluate

## Slide 18
Motivation and Goal
Motivation and Goal
Background
Reducing Hardware Complexity
Taxonomy of Value Prediction
Mechanism: AVPP
Evaluation and Results
Conclusion
AVPP Outline
Notes: Here is the outline for the talk today [CLICK]

## Slide 19
AVPP: Address-first Value-next Value Predictor
with Data Prefetching
Observations:
  Predicting load instructions has almost the same potential performance benefits as predicting all instructions
  Addresses are usually more predictable than values
Key Ideas:
  Predict only load instructions to reduce hardware cost
  Leverage the better predictability of addresses on load instructions to improve performance

## Slide 20
AVPP: Predictor Overview
Two main hardware structures:
Address Table (AT):
  Implemented with any predictor
  Indexed by the load instruction address
  Calculates the predicted address
AT
VT
1
2
3
Predicted
address
LD instruction
address
Predicted
value
Confidence
3bits
pdis
3bits
1bit
2. Value Table (VT):
  Indexed by the predicted address
  Returns the predicted value
d
AT predictor entry
AT entry
VT entry
value
tag

## Slide 21
AVPP: Prediction Overview (II)
AVPP predicts the output of every load instruction
The prediction happens in the front-end of the pipeline
Confidence mechanism to improve accuracy [Perais+ HPCA’14]
If the prediction is confident, write the result in the target register
Speculatively execute all the dependent instructions
Front-end
Exec. (OoO)
Commit
Load
1
2
3
AT
VT
1
2
3
Predicted
address
LD Instruction
address
Predicted
value
1
2
3
3
Front-end
Exec. (OoO)
Commit
Dependent
instruction
TIME
4
4

## Slide 22
AVPP: Update Overview
Update the AT at commit of every load instruction
Update the VT:
  At the commit of every store instruction. Keeps the VT coherent with memory
  At the commit of every load instruction?
Front-end
Exec. (OoO)
Commit
Load
7
6
5
Front-end
Exec. (OoO)
Commit
Store
TIME
AT
VT
7
LD instruction
address
Load Address
Load Address
Value
9
8
Store Address
7
Store Address
9
Store Value
9
TIME
Should we update the VT
at the commit of every load instruction ?

## Slide 23
40
4
tag
Last value
-
Stride
8
12
16
4
AVPP: Updating the VT at Each Load Instruction
40: LD [4]
40: LD [8]
40: LD [12]
40: LD [16]
AT
4
10
8
3
12
9
16
13
addr
value
VT
PC
Instruction
4
10
8
3
12
9
16
13
tag
val
L1 Cache
Correct
predictions :
0
MISS
MISS
VT always misses
No valid predictions
Last addr
Stride
Predictor
HIT
HIT
MISS
HIT
8+4=12
12+4=16
Predictor stage: predicting
Predictor stage: updating

## Slide 24
AVPP: Prefetching Overview
Idea: Prefetch values from the memory hierarchy into VT to increase the VT hit ratio
The prefetch address is calculated at each address prediction
  Generated when the prediction is confident
  Predicted to be accessed by future instances of the same load instruction
  Dynamic prefetch distance (details in the paper)
The VT is updated with the prefetched values
Prefetch
address
VT
Prefetch
Value
AT
1
2
Predicted
address
LD Instruction
address
3
Prefetch
address
4
4
3
The goal of prefetching is to increase the predictor coverage, not to hide memory latency

## Slide 25
40
4
tag
Last value
-
Stride
8
12
16
4
AVPP: Updating the VT with Prefetching
40: LD [4]
40: LD [8]
40: LD [12]
40: LD [16]
AT
12
9
16
13
20
2
addr
value
VT
PC
Instruction
4
10
8
3
12
9
16
13
tag
val
L1 Cache
Correct
predictions :
0
MISS
HIT
Last addr
Stride
Predictor
HIT
HIT
HIT
HIT
8+4=12
12+4=16
Predictor stage: predicting
Predictor stage: updating
20
2
1
2
Valid Predictions
VT hits because we prefetch the right values into it

## Slide 26
AVPP: Putting All Together
  Leverages the better predictability of addresses on load instructions to improve performance
  Two basic hardware structures:
    AT: predicts the address first
    VT: predicts the value next
  Prefetches future instances of the load instruction to improve the VT hit rate

## Slide 27
Motivation and Goal
Motivation and Goal
Background
Reducing Hardware Complexity
Taxonomy of Value Prediction
Mechanism: AVPP
Evaluation and Results
Conclusion
AVPP Outline
27
Notes: Here is the outline for the talk today [CLICK]

## Slide 28
Experimental Setup
Simulation platform:
  ZSIM [Sanchez+ ISCA’13] : 4-issue OoO cores, TAGE branch predictor, 128-entry ROB, 32KB L1 caches, 256KB L2s, Stream prefetchers
  McPAT [Li+ MICRO’09] for estimating the energy consumption
  Predictors evaluated:
    LVP, 2D-Stride, DFCM, VTAGE, DVTAGE, AVPP-DVTAGE, AVPP-Stride
    512 entries
23 selected benchmarks from
  SPEC2000
  SPEC2006
  PARSEC/SPLASH2

## Slide 29
Evaluation: Speedup
AVPP outperforms the state-of-the-art predictors
11.2% speedup over no value prediction
11.2%
5.9%

## Slide 30
Evaluation: Energy
AVPP outperforms the state-of-the-art predictors
3.7% energy savings over no value prediction
2.6%
3.7%

## Slide 31
Coverage of a predictor: percentage of loads for which a prediction is used for speculation
Coverage of the Load Value Predictors
AVPP covers more load instructions than the state-of-the-art
AVPP covers 44% of the load instructions
44%
36%

## Slide 32
Evaluation: Accuracy
Accuracy is higher than 99.8% in all predictors
because of the use of the confidence counters

## Slide 33
Where are the Benefits Coming from?
AVPP prefetching alone does not provide significant performance improvement
AVPP prediction alone provides only 4.8% speedup
The full AVPP achieves 10.6% speedup
1.8%
4.8%
10.6%

## Slide 34
More Results in the Paper
Multi-core simulations
Cache hit distribution
Distribution of the prefetch request that hits in L1, L2 and main memory
Sensitivity studies on
  Memory hierarchy (larger caches)
  Load Queue size
Impact of different load value prediction implementation policies

## Slide 35
Motivation and Goal
Motivation and Goal
Background
Reducing Hardware Complexity
Taxonomy of Value Prediction
Mechanism: AVPP
Evaluation and Results
Conclusion
AVPP Outline
Notes: Here is the outline for the talk today [CLICK]

## Slide 36
  Motivation: single-thread performance is critical for many applications
  Problem: improving single-thread performance in modern processors requires techniques that significantly increase the hardware cost
  Goal: revisit Load Value Prediction as an efficient way to improve single-thread performance
  Contributions:
  We propose optimizations for reducing the hardware cost of load value prediction
  We propose a new taxonomy of Value Prediction Policies
  AVPP:
    New load value predictor that predicts the address first and the value next.
    Increases the coverage of the predictor by prefetching the value of a future instance of the load instruction
Results:
AVPP outperforms all state-of-the-art value predictors in the context of load value prediction, and it is less complex than predicting all instructions
AVPP provides 11.2% system performance improvement and 3.7% energy savings compared to no value prediction.
Executive Summary
Notes: To begin, I will give a brief overview. [CLICK] many applications are limited by the single thread performance. [CLICK] The problem is that achieving performance benefits require significant hardware cost [CLICK] The goal is to revisit load value prediction as a low cost alternative to improve single-thread performance. We propose [CLICK] AVPP, a mechanism

## Slide 37
Lois Orosa, Rodolfo Azevedo and Onur Mutlu
AVPP:
Address-first Value-next Predictor
with Value Prefetching for Improving the Efficiency of Load Value Prediction

## Slide 38
BACKUP

## Slide 39
Cache Hit Distribution
of the predicted load instructions
Most of the predicted load instructions
hit into L1 cache

## Slide 40
Cache Hit Distribution
of AVPP-DVTAGE prefetch requests
Most of the AVPP prefetch requests hit into L1 cache

## Slide 41
Coverage of AVPP-DVTAGE
with and without prefetching
The coverage of the predictor
largely improves with prefetching

## Slide 42
VT hit rate with and without prefetching
Prefetching increases the VT hit rate

## Slide 43
Impact of the Prediction Policies
The best policy depends on the microarchitecture

## Slide 44
Impact of the Predictor Size
512 entries is a sweet spot

## Slide 45
Impact of the VT Table Size
64 VT entries is a sweet spot

## Slide 46
Impact of Cache Configurations
The speedup of load value prediction does not depend much on the cache configuration

## Slide 47
Store Set Prediction
and L2 Prefetching
The L2 Prefetcher and Load Value Prediction (LVP) are complementary

## Slide 48
L1 prefetching VS AVPP
When AVPP and L1 prefetcher are used together
the performance is additive in many benchmarks

## Slide 49
Multithreaded and Multiprogram Mixes
AVPP outperforms previous predictors