## Slide 1
Banshee: Bandwidth-Efficient DRAM Caching via Software/Hardware Cooperation
Xiangyao Yu1, Christopher Hughes2, Nadathur Satish2, Onur Mutlu3, Srinivas Devadas1
1MIT 2 Intel Labs 3ETH Zürich
Motivation
In-package DRAM has
  5X higher bandwidth than off-package DRAM
  Similar latency as off-package DRAM
  Limited capacity (up to 16 GB)
In-package DRAM can be used as a cache
Banshee Contribution
Bandwidth efficiency as a first-class design constraint
High Bandwidth efficiency without degrading latency
Evaluations
Core
SRAM
Cache Hierarchy
Memory Controller
In-Package
DRAM
Off-Package
DRAM
On-Chip
In-Package
> 400 GB/s
90 GB/s
384 GB
16 GB
* Numbers from Intel Knights Landing
Bandwdith Inefficiency in Existing DRAM Caches
Chart: Bytes per Instruction
| Unison Cache | Alloy Cache | BEAR | Tagless |
Hit | 2.0357 | 1.4663 | 1.4367 | 2.0141
Metadata | 2.1489 | 1.5358 | 1.3562 | 0
Replacement | 0.99297 | 0.63307 | 0.11723 | 0.99217
DRAM Cache Traffic Breakdown
Coarse-Granularity
Fine-Granularity
Drawback 1: Metadata traffic (e.g., tags, LRU bits, frequency counters, etc.)
Drawback 2: Replacement traffic
  Especially for coarse-granularity (e.g., page-granularity) DRAM cache designs
Idea 1: Efficient TLB coherence for Page-Table-Based DRAM Caches
* Assuming 4-way set-associative DRAM cache
Translation Lookaside Buffer (TLB)
TLB Entry
…
VPN
PPN
Core
SRAM Cache Hierarchy
Memory Controller
In-Package
DRAM
Off-Package
DRAM
Hardware
Software
Cached
(1 bit)
Way
(2 bits)
Mapping
Tag Buffer
PPN
V
Mapping
Page Table
Page Table Entry
…
PPN
Mapping
Reverse
Mapping
(Find all PTEs that map to a given PPN)
Track DRAM cache contents using page tables and TLBs
Maintain latest mapping for recently remapped pages in the Tag Buffer
Enforce TLB coherence lazily when the Tag Buffer is full to amortize the cost
Idea 2: Bandwidth-Aware Cache Replacement
Memory Controller
In-
Package
DRAM
Off-Package
DRAM
Cache Hits
(64 B)
Cache Misses
(64 B)
Limited Cache
Replacements
Sampled
Frequency
Counter
Accesses
DRAM cache replacement incurs significant DRAM traffic
  Cache replacement traffic
  Metadata traffic
Limit cache replacement rate
  Replace only when the incoming page’s frequency counter is greater than the victim pages’s counter by a threshold
Reduce metadata traffic
  Access frequency counters for a randomly sampled fraction of memory accesses
Banshee improves performance by 15% on average over the best-previous (i.e., BEAR) latency-optimized DRAM cache design
Banshee reduces 36% in-package DRAM traffic over the best-previous design
Banshee reduces 3% off-package DRAM traffic over the best-previous design