## Slide 1: Boyi: A Systematic Framework for Automatically Deciding the Right Execution Model of OpenCL Applications on FPGAs
Jiantong Jiang (Northeastern University, China),
Zeke Wang (Zhejiang University, China),
Xue Liu (Northeastern University, China),
Juan Gómez-Luna (ETH Zürich, Switzerland),
Nan Guan (Hong Kong Polytechnic University),
Qingxu Deng (Northeastern University, China),
Wei Zhang (Hong Kong University of Science and Technology),
Onur Mutlu (ETH Zürich , Switzerland)

## Slide 2: Outline
Background and Motivations
Our Solution
Experiment
Conclusion

## Slide 3: What is OpenCL?
OpenCL stands for Open Computing Language.
OpenCL has been developed for heterogeneous computing environments with a host-accelerator execution model.
  The CPU runs the control task.
  The GPU/ FPGA runs the computing kernel.
Notes: What is OpenCL? OpenCL stands for Open Computing Language.
OpenCL has been developed for heterogeneous computing environments with a host-accelerator execution model. In particular, CPU runs the host code and GPU/FPGA runs the kernel code.

## Slide 4: OpenCL on FPGA
External DDR
FPGA
Memory blocks
Software-centric  FPGA as a parallel architecture.
Users can program with OpenCL.
DSP blocks
Memory blocks
Logic blocks
Hardware-centric  fine-gained parallelism
Users need to program with HDL.
OpenCL
SDK
Notes: Originally, the FPGA has distributed resource features, as shown in the left figure, logic blocks, DSP blocks and memory blocks.
From the hardware centric point of view, FPGA can be used to achieve fine-grained parallelism.
However, users need to program FPGA with HDL, which is cycle-sensitive and error-prone.
With the end-to-end Intel OpenCL SDK, the FPGA resources are organized in the OpenCL hierarchy, as shown in the right figure.
From the software centric point of view, the FPGA is viewed as a parallel architecture. The global memory is implemented with external DDR. Local memory is implemented with memory blocks, and pipeline is implemented with dsp blocks, memory blocks and logic blocks.
And now users can program FPGA with OpenCL for a much better programmability.

## Slide 5: Conventional OpenCL: NDRange Kernel
How conventional OpenCL performs on an FPGA?
Core2
Core1
Core0
Explicit multi-threaded  executing the same operation on multiple data concurrently
Load
Compute
store
Load
Compute
store
Load
Compute
store
Data 0
Data 1
Data 2
Notes: The conventional NDRange kernel is the default OpenCL kernel model, which is originally designed for GPUs. So how does it work?
Usually OpenCL divides a problem into equal partitions, with the granularity of a work-item. Work-item is the basic unit of execution.
As shown in the figure, each work-item will go into the kernel pipeline and operate on different subset of data according to its id.
So the execution is just similar to GPU processing, parallel threads can be executed on different GPU cores.
And it achieves the explicit multi-threaded parallelism by executing the same operation on multiple data concurrently.
And how conventional OpenCL performs on an FPGA?

## Slide 6: Issue of Conventional OpenCL
Conventional OpenCL cannot always represent FPGA architecture in an efficient manner.
1.6x 12.1x 4.1x 3.0x 4.7x 11.3x 21.0x
Notes: Due to the architecture differences between GPU and FPGA, conventional OpenCL cannot always represent FPGA architecture in an efficient manner.
The figure shows the performance ratio over baseline for seven OpenCL applications. The left bar represents the speedup of the best conventional OpenCL kernel which already employs the best-effort optimizations. And the right bar represents the speedup of the optimal optimization combinations. We can see that the performance difference can reach up to 21x.
So conventional OpenCL cannot fully harvest the performance potential of FPGAs. However, things are changed with two new features of Opencl.

## Slide 7
The optimal performance is enabled by two OpenCL features!

## Slide 8: OpenCL Feature 1: SWI Kernel
The SWI model executes the kernel in only one CU that contains only one work-item.
Load
Compute
store
Pipelined parallelism No conflict among work items.
D0
D1
D2
D3
D7
D6
D5
D4
8 Data Points
Notes: First we talk about SWI kernel.
The SWI model executes the kernel in only one CU that contains only one work-item.
The different operations are performed one after the other as shown in the figure.
The OpenCL SDK analyses loops and determines pipelined parallelism at the compilation time.
So it closely matches the traditional deep-pipelined nature of FPGA and achieves parallelism from the loops by executing multiple operations on different data concurrently.

## Slide 9: OpenCL Feature 2: OpenCL Channel
OpenCL
channel
OpenCL channel can be used to pass data between two OpenCL kernels (typically SWI).
  Synchronizing the kernels
  Reducing the number of global memory accesses
Global memory
FPGA
Producer kernel
Consumer kernel
Notes: Next we talk about OpenCL channel.
OpenCL channel can be used to pass data between two OpenCL kernels via on-chip FIFO buffers instead of global memory accessing.
So there are two advantages.
First, it can synchronize the kernels with high efficiency and low latency.
Second, the number of global memory accesses is significantly reduced.

## Slide 10: Challenges
Two OpenCL features exponentially increase design space.
  Enabled by two features, we have four OpenCL execution models:
  For each execution model, we have at least six optimization methods:
  For each optimization method, we have different pragmas.
NDRange
SWI
NDRange+Channel
SWI+Channel
SM
MC
PM
UL
SIMD
CU
The compilation time is extremely long!
Notes: Despite the great performance potential of two emerging OpenCL features, we still identify two challenges.
First, The two features increase the design space.
Enabled by the two features, we have four high-level OpenCL execution models. Because the OpenCL application can be executed in NDRange or SWI kernels, with or without OpenCL channels.
Then for each execution model, we can apply a number of conventional optimization methods to improve the performance.
And each optimization method may have different pragmas.
So we need to explore a huge design space for each execution model.
The second challenge is that the current Intel tool takes extremely long time to synthesize a single solution.

## Slide 11: Effect of Four Execution Models
Different execution models can significantly affect the performance.
NDRange
SWI
NDRange+Channel
SWI+Channel
Execution model should be decided first.
Notes: We observe that different execution models can significantly affect the performance.
The figure shows the performance of the most suitable and unsuitable execution models for eight applications over baseline.
Then we argue that the execution model should be decided first, as it determines the potential of other conventional optimizations.

## Slide 12
Can we explicitly determine the most suitable execution model (i.e., whether or not to use two OpenCL features) to optimize OpenCL programs on FPGAs?
We provide a systematic framework Boyi to automatically determine the most suitable execution model.

## Slide 13: Outline
Background and Motivations
Our Solution
  OpenCL Pattern Recognition
  Execution Model Prediction
Experiment
Conclusion

## Slide 14: Architecture of Boyi
Boyi explicitly determines the most suitable execution model to optimize OpenCL programs on FPGAs.
  OpenCL Pattern Recognition
  Execution Model Prediction
Clang Frontend
LLVM IR
Direct Prediction
Potential Evolution
Four Execution Models
NDR
SWI
NDR + C
SWI + C
SWI
OpenCL Channel
OpenCL Pattern Recognition
Execution Model Prediction
OpenCL Kernel Source Code
Host C/C++ Source Code
Most Suitable Execution Model
KKC Recognition
MPS Recognition
AO Recognition
AO: Atomic Operation
MPS: Multi-Pass Scheme
KKC: Kernel-to-Kernel Communication
Notes: The figure shows our framework. It consists of two components: OpenCL pattern recognition and execution model prediction.
First, the OpenCL pattern recognition component analyzes the input OpenCL kernel and host code, to automatically identify three typical OpenCL patterns:
Atomic Operation (AO), Multi-Pass Scheme (MPS) and Kernel-to- Kernel Communication (KKC).
They often occur on GPUs and are worth to revisit on FPGAs, as their performance can be significantly improved with the help of two emerging OpenCL features.
Then it can output the presence and absence of three OpenCL patterns to the next component.
The execution model prediction component then predicts the most suitable execution model based on the presence or absence of three patterns.
In the following, we will talk about the two component respectively.

## Slide 15: Outline
Background and Motivations
Our Solution
  OpenCL Pattern Recognition
  Execution Model Prediction
Experiment
Conclusion

## Slide 16: OpenCL Pattern: Atomic Operation
5
Issues on FPGAs:
Input data
Hash function
Histogram
0
1
2
3
1
0
6
1
4
2
7
3
2
4
5
5
9
6
0
7
Hash index
1
2
0
3
2
1
1
0
8 work-items
Conflict
Noticeable resource overhead
Long latency and low bandwidth
Low frequency
 AO is not a good fit on FPGAs.
1
6
4
7
2
9
0
Notes: Before talking about the first component OpenCL pattern recognition, we first discuss the three OpenCL pattern.
First we talk about the atomic operations.
In NDR kernels, when multiple work items try to update the same memory location, AOs are required to guarantee the memory consistency.
Take as an example the simplified histogram, as shown in the figure. Each work item update the shared histogram atomically.
AO provides improved programmability for GPUs. But there are three issues on FPGAs.
First, the mechanism of AOs is complex, so a large amount of FPGA resources is required.
Second, with AOs in our kernel, all the memory transactions, including both atomic and normal memory transactions, have to enter the atomic module to guarantee the correct execution, leading to longer memory access latency and lower memory bandwidth.
Third, the frequency of the kernel is lower, leading to lower performance.
We conclude that AO is not a good fit on FPGAs.

## Slide 17: OpenCL Pattern: Atomic Operation
5
Potential on FPGAs:
Input data
Hash function
Histogram
0
1
2
3
1
0
6
1
4
2
7
3
2
4
5
5
9
6
0
7
Hash index
1
2
0
3
2
1
1
0
1
6
4
7
2
9
0
Notes: To eliminate the need of AO, we can use SWI kernel.
Because it uses one single work-item, so it can avoid conflicts among multiple work-items.
The histogram application using SWI kernel is shown in the figure, it only needs normal memory operations.

## Slide 18: OpenCL Pattern: Multi-Pass Scheme
in
6
0
2
3
1
4
3
5
2
8
9
0
1
6
4
7
0
6
6
8
0
1
5
8
0
2
10
19
0
1
7
11
out
11
13
19
18
local_sum
Step 1: 4 work-groups
50
37
18
0
pre_sum
50
56
56
58
37
38
42
45
18
20
28
37
0
1
7
11
out
Step 2: 1 work-group
in
6
0
2
3
1
4
3
5
2
8
9
0
1
6
4
7
0
6
6
8
0
1
5
8
0
2
10
19
0
1
7
11
out
Step 3: 4 work-groups
11
13
19
18
local_sum
Notes: Next we talk about the multi-pass scheme.
MPS is widely adopted to use many cores in CPUs/GPUs to increase the overall parallelism at the cost of more memory traffic.
Take as an example the simplified prefix sum, as shown in the figure. We perform the prefix sum on the input array of size 16.
In Step 1, four WGs execute concurrently. Each WG performs the prefix sum on its own part of data and stores its local sum.
In Step 2, one WG to computes the prefix sum on local sum and store.
In Step 3, each WG performs vector addition and produces the final prefix sum.

## Slide 19: OpenCL Pattern: Multi-Pass Scheme
Issues on FPGAs:
Potential on FPGAs:
6
0
2
3
1
4
3
5
2
8
9
0
1
6
4
7
50
56
56
58
37
38
42
45
18
20
28
37
0
1
7
11
out
in
More memory traffic
 MPS is not a good fit on FPGAs.
Notes: We observe that MPS requires more memory traffic to implement an algorithm.
It works pretty well on GPUs, because the memory bandwidth of GPUs is high.
But we predict that MPS is not a good fit on FPGAs due to their low memory bandwidth.
To avoid MPS, we can use SWI kernel, which means the multiple-pass algorithm can be implemented in a single-pass approach, as shown in the figure.
Then the memory traffic is reduced.

## Slide 20: OpenCL Pattern: Kernel-to-Kernel Communication
Issues on FPGAs:
The communication via global memory is expensive.
Global memory
FPGA
Producer kernel
Consumer kernel
Notes: Next we talk about kernel-to-kernel communication.
On GPUs, the communication between producer/consumer kernels is done via global memory: after the producer kernel writes some data to the global memory, the consumer kernel reads the data from global memory, as shown in the figure.
There is no physical communication path between any two GPU cores, but GPUs have massive thread-level parallelism and high memory bandwidth, so this method works well on GPUs.
However, the memory bandwidth is low on FPGAs, so the communication via external memory is expensive.

## Slide 21: OpenCL Pattern: Kernel-to-Kernel Communication
Potential on FPGAs
Reducing the number of memory accesses
Inter-kernel parallelism (i.e., concurrent kernel execution)
OpenCL
channel
Global memory
FPGA
Producer kernel
Consumer kernel
Notes: But we can use the OpenCL channel in a way that the producer kernel directly send data to the consumer kernel, thus reducing the number of memory accesses.
Besides, both kernels can execute concurrently.
That is to say, we can achieve not only intra-kernel parallelism (i.e., pipelined) but also inter-kernel parallelism (i.e., concurrent kernel execution).

## Slide 22: OpenCL Pattern Recognition
We develop nine LLVM passes to recognize three OpenCL patterns.
  AO recognition
  KKC recognition
  MPS recognition
The implementation details can be found in our paper!
Notes: Then we propose an LLVM-based OpenCL pattern recognition mechanism, in order to automatically identify AO, KKC and MPS.
The recognition of the pattern AO is quite straightforward, as each atomic instruction is converted to an LLVM IR instruction.
We develop an LLVM pass HasAO to recognize AO instructions in the OpenCL kernel code.
Next we will talk about more complicated patterns, KKC and MPS.

## Slide 23: Outline
Background and Motivations
Our Solution
  OpenCL Pattern Recognition
  Execution Model Prediction
Experiment
Conclusion

## Slide 24: Execution Model Prediction
Direct prediction
Kernels with AO and MPS benefit from the SWI kernel.
Kernels with KKC benefit from the OpenCL channel.
AO | MPS | KKC
N | N | N
Y | N | N
N | Y | N
Y | Y | N
N | N | Y
Y | N | Y
N | Y | Y
Y | Y | Y
Direct prediction
NDR
SWI
SWI
SWI
NDR+C
SWI+C
SWI+C
SWI+C
Notes: The goal of this component is to predict the most suitable execution model based on the presence or absence of three OpenCL pattern.
Our prediction has two parts. The first part is a direct prediction, as shown in the table.
Intuitively, an OpenCL application with AO and MPS benefits from the SWI kernel, while an OpenCL kernel with KKC benefits from the OpenCL channel.

## Slide 25: Execution Model Prediction
Potential evolution of SWI
  Conditions:
AO | MPS | KKC | Direct prediction
N | N | N | NDR
Y | N | N | SWI
N | Y | N | SWI
Y | Y | N | SWI
N | N | Y | NDR+C
Y | N | Y | SWI+C
N | Y | Y | SWI+C
Y | Y | Y | SWI+C
Potential evolution
NDR
SWI+C
SWI+C
SWI+C
NDR+C
SWI+C
SWI+C
SWI+C
Sufficient FPGA resource.
The SWI kernel is compute-bound.
Notes: The second part is the potential evolution of SWI.
When the original prediction is SWI execution model, we may potentially evolve the SWI execution model to the SWI+C execution model for higher computing parallelism, if the following two conditions are satisfied.
First, Sufficient FPGA Resources.
SWI+C needs more than one SWI kernel, thus requiring more FPGA resources to implement.
Second, The SWI Kernel is Compute-Bound.
The evolution happens only when the original SWI kernel is compute-bound. For memory-bound kernels, further replication cannot alleviate the existing memory bottleneck. We also present an analytical model in order to determine whether or not the targeted SWI kernel is compute-bound.

## Slide 26: Outline
Background and Motivations
Our Solution
Experiment
  Experimental Setup
  Effect of Execution Model
  Prediction of Execution Model
Conclusion

## Slide 27: Experimental Setup
Platform: Terasic DE5a-Net board: Altera Arria 10 GX FPGA and 8GB 2-bank DDR3, with Altera OpenCL SDK version 16.1.
Workloads:
Benchmark | Source | Description | AO | MPS | KKC | Datasets
BFS | Chai | Breadth-First Search | Y | N | N | NY, NE, UT
RSCD |  | RANSAC | Y | N | Y | 2000 iterations
TQH |  | Task Queue System | Y | N | N | Basket
HSTO |  | Histogram | Y | N | N | 256bins
SC |  | Stream Compaction | Y | N | N | 50%
PAD |  | Padding | Y | N | N | 1000*999
CEDD |  | Canny Edge Detection | N | N | Y | Peppa, Maradona, Paw
KM | Rodinia | K-Means | N | N | N | 25600 points, 8 features
MM | Intel demo | Matrix Multiplication | N | N | N | A: 2k*1k, B: 1k*1k
MS |  | Mandelbrot Set | N | N | N | 640*800, 2000 iterations
PS | CUDA demo | Prefix Sum | N | Y | N | 262144 points
Notes: Here is our platform and benchmarks.
We use 11 OpenCL applications, where seven applications are from Chai benchmark suite. They are highly optimized for GPUs. They serve as our baseline in this paper.

## Slide 28: Comparison Methodology
Hypothesis 1: Different execution models lead to significant performance differences.
  Quantitative comparison among execution models
  Exploring optimization combinations
Hypothesis 2: Boyi can predict the most suitable execution model for each OpenCL application.
Notes: Comparison Methodology.
Our evaluations mainly validate the following two hypotheses.
First, different execution models lead to significant performance differences
In particular, we first explore the optimization combinations for each execution model of each OpenCL application,
second quantitatively compare the highest speedup that each execution model can achieve,
Second, we validate that Boyi can predict the most suitable execution model for each OpenCL application.

## Slide 29: Hypothesis 1: Different execution model --> different performance
App | Number of combinations |  |  |  | Maximum speedup |  |  | 
 | NDR | SWI | NDR+C | SWI+C | NDR | SWI | NDR+C | SWI+C
BFS | 17 | 7 | 7 | 9 | 1.9 | 3.1 | 1.2 | 3.1
RSCD | 25 | 10 | 24 | 46 | 15.8 | 4.6 | 73.8 | 39.7
TQH | 9 | 15 |  | 23 | 1.1 | 1.3 |  | 21.0
HSTO | 13 | 37 | 11 | 29 | 2.7 | 5.1 | 16.9 | 32.4
SC | 15 | 34 |  | 10 | 1.5 | 4.5 |  | 17.1
PAD | 10 | 10 |  | 14 | 1.2 | 1.6 |  | 4.8
CEDD | 57 | 15 | 22 | 7 | 2.7 | 0.3 | 2.7 | 0.4
KM | 33 | 11 | 10 | 18 | 147.7 | 32.8 | 136.4 | 31.4
MM | 25 | 9 |  | 6 | 837.1 | 13.3 |  | 6.6
MS | 7 | 6 |  | 7 | 34.7 | 0.02 |  | 3.2
PS | 26 | 20 |  | 12 | 15.8 | 44.4 |  | 46.2
Quantitative comparison among execution models
Different execution models result in significant performance differences.
Different applications require different execution models to achieve the best performance.
It is critical to decide the most suitable execution model when optimizing OpenCL applications on FPGAs.
Notes: Now we validate the first hypothesis, different execution model leads to significantly different performance.
First, we quantitatively compare the highest speedup that each execution model can achieve.
The table shows for each execution model the number of optimization combinations we have tried and the maximum speedup over the baseline. Empty slot indicates that the particular execution model cannot be successfully implemented due to the limitation of OpenCL channel.
We make two observations.
First, different execution models result in significant performance differences.
Second, different OpenCL applications require different execution models to achieve the best performance.
We conclude that it is critical to decide the most suitable execution model when optimizing OpenCL applications on FPGA.

## Slide 30: Hypothesis 1: Exploring optimization combinations for Each Execution Model
We manually implement sufficient number of optimization combinations (subset) for KM, such that we reach the near-to-optimal optimization combination for each execution model.
Most suitable execution model
Most unsuitable execution model
Notes: For each application, we explore sufficient number of optimization combinations for each execution model, such that the near-to-optimal optimization combination is included for each execution model.
We take KM as an example. The figure shows the speedup of each optimization combination over the baseline for each execution model.
The baseline is GPU code from Rodinia.
The X-axis shows optimization combinations under four execution models. The figure just shows a subset of optimization combinations for each optimization combination due to space limit.

## Slide 31: Hypothesis 2: Boyi Predicts the Right Execution Model
Application | AO | MPS | KKC | Actual | Predicted
BFS | Y | N | N | SWI | SWI
RSCD | Y | N | Y | NDR+C | SWI+C
TQH | Y | N | N | SWI+C | SWI+C ※
HSTI | Y | N | N | SWI+C | SWI+C ※
SC | Y | N | N | SWI+C | SWI+C ※
PAD | Y | N | N | SWI+C | SWI+C ※
CEDD | N | N | Y | NDR+C | NDR+C
KM | N | N | N | NDR | NDR
MM | N | N | N | NDR | NDR
MS | N | N | N | NDR | NDR
PS | N | Y | N | SWI | SWI
SWI+C ※ indicates the potential evolution of SWI
N
NDR+C
The actual and predicted execution models roughly match.
Notes: Now we validate the second hypothesis. For each OpenCL application, the prediction of execution model matches the experimental result.
The table shows the predicted execution model, and the actual execution model that achieves the best performance in our experiments.
We can observe that the prediction of execution model almost matches the real experimental result, except for RSCD.
For RSCD, its AO is executed after one loop whose trip count is 5922, so it has trivial impact on the overall performance. From the performance’s perspective, we can consider RSCD does not contain AO. As such, the predicted execution model match the actual execution model.

## Slide 32: End-to-end Performance Comparison
Performance comparison to existing works
Application | Ours (ms) | Existing work (ms) | Our/Existing Speedup
RSCD [1] | 0.8 | 28.9 | 38.3
TQH [1] | 66.9 | 150.6 | 2.3
HSTO [1] | 38.8 | 487.9 | 12.6
CEDD [1] | 161.9 | 237.8 | 1.5
MM [2] | 9.1 | 34.3 | 3.8
MS [2] | 27.2 | 944.1 | 34.7
[1] S. Huang et al., “Analysis and modeling of collaborative execution strategies for heterogeneous cpu-fpga architectures”, ICPE, 2019.
[2] Intel. Intel SDK for OpenCL Design Examples. 2018
Notes: To validate the efficiency of Boyi, we also compare the performance of our optimal implementation to existing works that are state-of-the-art.
The table shows the execution time of six applications under the optimal optimization combination and the comparison to the existing implementations on FPGAs. In particular, one work in ICPE’19 runs the first four applications in Chai benchmark using a CPU-FPGA co-processing approach. We re-implement their best optimization combination on our platform. And our code achieves 1.5-38.3x higher throughput than their work, indicating the efficiency of Boyi.

## Slide 33: Outline
Background and Motivations
Our Solution
Experiment
Conclusion

## Slide 34: Conclusion
We need to leverage two OpenCL features to exploit the performance potential of FPGAs, since the architecture of FPGA is significantly different from that of GPUs.
We propose Boyi, a systematic framework for deciding the most suitable execution model of an OpenCL application.
Boyi is able to automatically predict the right execution model which can match the real experimental results.

## Slide 35: Boyi: A Systematic Framework for Automatically Deciding the Right Execution Model of OpenCL Applications on FPGAs
Jiantong Jiang (Northeastern University, China),
Zeke Wang (Zhejiang University, China),
Xue Liu (Northeastern University, China),
Juan Gómez-Luna (ETH Zürich, Switzerland),
Nan Guan (Hong Kong Polytechnic University),
Qingxu Deng (Northeastern University, China),
Wei Zhang (Hong Kong University of Science and Technology),
Onur Mutlu (ETH Zürich , Switzerland)

## Slide 36: OpenCL Pattern Recognition
An LLVM-based OpenCL pattern recognition mechanism
  AO recognition
  KKC recognition
  MPS recognition
HasAO
#AOTrue
Notes: Then we propose an LLVM-based OpenCL pattern recognition mechanism, in order to automatically identify AO, KKC and MPS.
The recognition of the pattern AO is quite straightforward, as each atomic instruction is converted to an LLVM IR instruction.
We develop an LLVM pass HasAO to recognize AO instructions in the OpenCL kernel code.
Next we will talk about more complicated patterns, KKC and MPS.

## Slide 37: KKC Recognition
R1: the OpenCL application has two or more OpenCL kernels.
R2: the consumer kernel reads from the same buffer object (in global memory) as a producer kernel writes to.
R3: the producer and the consumer kernels access the buffer object with the same memory access pattern (MAP).
R1: NumKernels
#Kernels>1?
#Kernels
R2: IsSameBuf
Y
R2: IsRdWr
#R2Triplets>0?
#R2Triplets
R3: IsSameMAP
Y
#KKCTrue
R2BufferTriplets
#KKCTrue=0
N
#KKCTrue=0
N
Notes: We need to consider three conditions R1 R2 R3 for KKC recognition.
Accordingly, we design four LLVM passes to analysis the input OpenCL kernel and host code, as shown in the figure.
The blue squares represent the LLVM passes that run over the OpenCL kernel code, while the green ones represent the passes that run over the host code.
The first condition R1 is that The OpenCL Application Has Two or More OpenCL Kernels.
And the pass NumOfKernels is designed to determine the value of #Kernels.
R2: The Second Kernel Reads from the Same Buffer Object (in Global Memory) as the First Kernel Writes to.
The pass IsSameBuf runs over the input host code to determine each triplet (buffer, k1, k2) satisfying the condition: two kernels k1 and k2 access the same buffer object buffer.
The pass IsRdWr runs over the input kernel code to determine whether k1 writes data to the buffer object buffer while k2 reads data from buffer.
R3: Two Kernels Access the Buffer Object Following the Same Memory Access Pattern (MAP).
The pass IsSameMAP takes all the BufferTriplets as input to determine R3.

## Slide 38: MPS Recognition
R5: the intermediate buffer objects are not needed when the OpenCL application is mapped to one work-group
R4: two kernels access the same buffer object with different MAPs
R1: NumKernels
#Kernels>1?
#Kernels
R2: IsSameBuf
Y
R2: IsRdWr
#R2Triplets>0?
#R2Triplets
R2BufferTriplets
#MPSTrue=0
N
Y
R4: IsSequential
R5: VarBuffHost
R5: VarInKernel
#R4Triplets
R4SeqTriplets
Args, ArgVals
#R4Triplets>0?
#MPSTrue=0
N
#MPSTrue=0
#MPSTrue=0
N
Y
R5: BuffInKernel
Vars, VarVals
Buffs
Notes: KKC recognition is more complicated, we need to consider four conditions R1 R2 R4 R5.
Accordingly, we design six passes to analysis the input OpenCL kernel and host code.
Just like the pattern KKC, MPS can exist only when R1 and R2 are met. So we adopt the same three passes from KKC recognition and obtain the BufferTriplets.
Then R4 is that Two Kernels Execute Sequentially.
R4 is opposite to R3. so we get SeqTriplets which are these triplets that do not satisfy R3.
R5:The Intermediate Buffer Objects are Not Needed when the OpenCL Application is Mapped to One Work-Group.
The key idea is to examine the situation of each of the R4SeqTriplets when the number of work-groups becomes one.

## Slide 39: Four Execution Models
 | NDR | SWI | NDR+C | SWI+C
Programmability | Moderate | High | Low | Low
Computing parallelism | High | Low | High | Moderate/High
Memory traffic | High | Low | Moderate | Low
General comparison of four execution models:
NDR can achieve higher computing parallelism.
SWI is more easy to program and requires a lower memory traffic.
OpenCL channel will increase the programming difficulty, reduce the memory traffic and lead to higher computing parallelism.
Notes: Then we move to the second component execution model prediction.
So before that, we revisit the four execution models.
we analyze their programmability, computing parallelism and memory traffic respectively for each execution model. The table shows a general comparison results.
Generally, we can see that
NDR can achieve higher computing parallelism.
SWI is more easy to program and requires a lower memory traffic.
OpenCL channel increases the programming difficulty, reduce the memory traffic and lead to a higher computing parallelism.