## Slide 1: Carpool: A Bufferless On-Chip Network
Xiyue Xiang
Wentao Shi, Saugata Ghose, Peng Lu,
Onur Mutlu, Nian-Feng Tzeng
Supporting Adaptive Multicast and Hotspot Alleviation

## Slide 2
Executive Summary
Problem: bufferless NoCs lack of efficient support for multicast (MC) and hotspot (HS) traffic
Our Goal: reduce the contention caused by MC and HS traffic in a bufferless NoC with low cost
Observation: MC flits increase serialization latency and HS flits waste network bandwidth
Key Idea: fork MC flits adaptively when NoC is not congested and merge HS flits opportunistically
  Carpool is the first bufferless NoC providing support for multicast and hotspot traffic
    Results
      43% lower latency and 8% lower power than conventional bufferless NoC
      26% lower latency, 50% lower power, and 64% less area than the buffered NoC with MC/HS support
Notes: Bufferless on-chip networks, known as bufferless NoCs, are considered as a good design option for multicore processor because of their low hardware complexity and high energy-efficiency. However, the current bufferless NoC lacks of efficient support for multicast and hotspot traffic.
A multicast packet can be a request from one nodes to many other nodes forming a 1-to-M pattern. The other is hotspot where M senders may send the packets to the same destinations, forming M-to-1 traffic.
So, in the following presentation, I will begin with highlighting two important observations. First, MC flit can create near-end congestion at the source NI. Second, the HS flit can create far-end congestion at the destinations.
We propose Carpool which was inspire by Carpooling in our real life where passengers can ride the same car sharing the road infrastructure to alleviate the traffic congestion. In this work, the basic idea of Carpool is to fork the multicast flits adaptively when the NoC is not congested and merge the hs flit in the network with low cost. The basic principle is to reduce the amount of traffic in the network to avoid contention caused by multicast and hotspot packets.
With these two simple mechanisms, Carpool can reduce the latency and power significantly, compared with the conventional bufferless NoC with no special support and its buffered counterpart with similar support. Also, it enjoys 64% of less area than its buffered NoC counterpart.

## Slide 3
2. Key Observations
4. Hardware Implementation
5. Evaluation
3. Our Approach
1. Network-on-Chips Basics
1. Network-on-Chips Basics

## Slide 4
NoCs in the Silicons
Notes: Network on chip has been extensively studied in the academia over the past 20 years or so. Lately, NoC has been widely adopted by a large number of leading SoC firms in their latest silicon or prototypes.

## Slide 5
Network-on-Chips
Node
Core
L1
Router
Shared LLC Slice
NI
12
13
14
15
8
9
10
11
4
5
6
7
0
1
2
3
NoCs carry the communication among nodes on the same die
Router is the pivots of NoCs, moving traffic from node to node
Notes: In a multicore processor, NoC has been considered as an efficient interconnection substrate carrying communication among nodes on the same die. Each node may contain an out-of-order core, a private L1 instruction and data cache, a shared L2 cache slice, a Network Interface (or NI), and a router. In the context of SoC, a node can also be any processing element, such as FPGA, GPU, Memory controller, on-chip storage, and other I/O component.

## Slide 6
Buffer Write
VC Arbitration
Switch Arbitration
Switch Traversal
Virtual Channel
North
West
South
East
East
South
West
North
Port Allocation
Switch Traversal
North
West
South
East
East
South
West
North
Sorting
Network
Buffered router
Bufferless router
Buffered vs. Bufferless Router
 | Buffered NoCs | Bufferless NoCs
Performance |  | 
Power |  | 
Area |  | 
Bufferless NoCs is a compelling design option for future multicore processor due to its simplicity and power-efficiency
Notes: Routers serves as the pivots of NoC, moving traffic from node to node. There are two stereotypes. A buffered router and a bufferless router.
For buffered router, there are a number of buffers at each input port, which are partitioned into multiple virtual channels. However, buffers tends to take a significant amount of chip area and power budget. Lots of work have studied the amount of buffers to make tradeoff among performance, area and power. The simplest alternative would be bufferless router, where each input port only contain a single buffer, which is able to hold a single flit. Bufferless NoC has much lower hardware complexity and better power efficiency than buffered NoCs. However, this has also led to a completely different set of challenges to ensure bufferless NoCs to deliver competitive performance as its buffered counterpart.
Nonetheless, bufferless NoC has been deemed as a compelling design option for future multicore processor due to its simplicity and power-efficiency.

## Slide 7
Bufferless NoCs Basics
Contention
❶ Flit Ranking
❷ Port Allocation
❸ Forward/Deflect
High network latency & power
Deflect low priority flits
Bufferless Router
Flit A
Flit B
Simple Operations
Bufferless NoCs rely on deflection to resolve flits contention, but avoid deflection as much as possible
Deflected
Notes: Since bufferless noc removes the input buffers, the operation is much simpler. Usually, a sorting network is used to find out the flit ranking. Then port allocation takes place sequentially based on the flit priority. The crossbar then directs the traffic based on the allocation result. All the flits must move down the pipeline at each cycle. When a lower priority flit fails to claim its desired port, it will be deflected, which often leads to increased network latency and power consumption.
Other variant of bufferless NoC is to drop the lower-priority flit during contention. This will require adding a separate network to handle retransimission. In this work, we will focus on discussing deflection based bufferless NoC.
So, the key of bufferless NoC is to use deflection to resolve flit contention, but avoid deflection as much as possible.

## Slide 8: Current bufferless NoCs lack of efficient support for multicast and hotspot traffic
Notes: Although a lots of works are then proposed to optimize bufferless NoC for unicast traffic, there is no work existed to provide efficient support for handling multicast and hotspot traffic for bufferless NoC.

## Slide 9
2. Key Observations
4. Hardware Implementation
5. Evaluation
3. Our Approach
1. Network-on-Chips Basics
2. Key Observations
Notes: So, what are the multicast and hotspot flits? And what causes them?

## Slide 10
Multicast
Originate from one node destined to multiple nodes
Occur: invalidation
Issue: long serialization latency
Multicast and Hotspot in NoCs
4
6
7
8
3
5
0
1
2
4
6
7
8
3
5
0
1
2
Hotspot
Originate from multiple nodes with the same destination and payload
Occur: acknowledgement, shared lock variables access
Issue: waste network bandwidth
Providing support for MC and HS is very important for
a bufferless NoC to deliver high performance
Notes: A multicast packet can be a request from one nodes to many other nodes forming a 1-to-M pattern. The special case is broadcast, where a single node is sending packet to all the rest of nodes in the system. Multicast is very common in the processor. For example, with a directory-based coherence protocol, evicting a shared cache line often involves sending a sequence of invalidation packets to the home node, forming multicast traffic.
The other is hotspot where M senders may send the packets to the same destinations, forming M-to-1 traffic. The hotspot traffic occurs when multiple nodes send acknowledgements associated with the same request or access the shared lock variable for entering the critical section during synchronization. These packets are often on the critical path of execution, directly determine the application runtime.
Conventionally, both MC and HS flits involve injecting M separate flits causing network congestion
Therefore, providing support for multicast and hotspot traffic can be very useful to improve the performance and reduce the power consumption of the shared memory system.

## Slide 11
Impact of MC and HS Traffic
In Bufferless NoCs
Chart: Injection Rate (packet/cycle)
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32
mc_r=0 | 113.12 | 114.52 | 116.06 | 117.81 | 119.91 | 122.29 | 125.3 | 128.66 | 133.14 | 138.11 | 144.9 | 154.07 | 167.37 | 190.19 | 399.28 | 9150.82
mc_r=0.1 | 239.6286 | 269.3905 | 364.4613 | 19334.2921 | 48604.2495 | 71602.9494
Chart: Injection Rate (packet/cycle)
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34
hs_r=0 | 113.12 | 114.52 | 116.06 | 117.81 | 119.91 | 122.29 | 125.3 | 128.66 | 133.14 | 138.11 | 144.9 | 154.07 | 167.37 | 190.19 | 399.28 | 9150.82
hs_r=0.1 | 149.4368 | 152.4339 | 157.1735 | 162.4707 | 170.4862 | 180.0351 | 196.9722 | 227.7099 | 291.6945 | 542.5448 | 1754.7672
Our Goal: reduce the contention caused by multicast and hotspot traffic in bufferless NoCs with low complexity
10% multicast
No multicast
10% hotspot
No hotspot
Saturate at 5% of capacity
Saturate at 17%
of capacity
3× latency increase
39% latency increase
Multicast and Hotspot Traffic Impact:
Increase network latency & saturate NoCs prematurely
Notes: Since MC and HS are quite common and there is no efficient support in the bufferless NoC, it is naturally to have a question in mind “are these two types of traffic harmful to bufferless NoC?”
We did experiment to study the impact of MC and HS traffic in a 8x8 bufferless NoC. And in the experiment, the multicast is handled in a naïve approach such that each multicast flit with M destinations involves M unicast flit being injected sequentially. And there is no special treatment for hotspot traffic.
As we can see, with only 10% of multicast traffic, the average latency increases almost 3X, causing network saturate at 5% of its capacity.
On the right hand side, 10% of hotspot traffic rises latency by 39%, causing network saturate at 17% of its capacity.
So, the multicast and hotspot traffic can increase the latency and saturate the network prematurely.
Out goal is to reduce the contention caused by multicast and hotspot traffic in bufferless NoCs with low complexity.

## Slide 12
2. Key Observations
4. Hardware Implementation
5. Evaluation
3. Our Approach
1. Network-on-Chips Basics
3. Our Approach

## Slide 13
Our Approach – Carpool
Multicast Flit Forking
  Source NI injects single multicast request
  Adaptively fork multicast flits when NoCs is not congested
  Congestion measure: starvation rate
Hotspot Flit Merging
  Tagged at the originating nodes
  Intermediate routers detect hotspot flits
  Some hotspot flits are quietly dropped
Notes: Carpool contains two simple mechanisms: mc flit forking and hs flit merging
For a multicast flits with M destinations, the conventional approach creates M flits, stores in a queue, and injects them one by one, which takes M cycles to just for injecting all the flits replicas. Carpool allows a multicast flit to enter the network with a single cycle latency and forks new multicast flit replicas adaptively as they travel toward their destinations. As forking new flit replica can increase the network load, we use starvation rate measured at each NI to indicate network congestion and only enable the flit forking mechanism when the network is not congested. The created flit replica and the original flit carry distinct destination lists and are transferred across the network independently. This approach can significantly reduce the serialization latency, and allow the multicast flits to explore the path diversity.
Then, as the hotspot flits are essentially carrying the same payload, they are tagged at the originating nodes and are merged in the intermediate nodes opportunistically. Similar to multicast flits, each hotspot flit carries a list identifying the source of senders, which is updated if being merged. The other hotspot flits being merged are quietly dropped. Merging hotspot flits can effectively resolve the contention when it happens, leading to reduced network load and improved bandwidth utilization.

## Slide 14
D1
D4
D2
D5
D3
D6
S
S
D1
D4
D2
D5
D3
D6
6
3
2
1
2
1
1
1
1
1
1
1
15 transfers, 10 cycles
6 transfers, 5 cycles
Forking multicast flits reduces the serialization latency at the source network interface
Naïve bufferless
Carpool
Multicast Flit Forking
Notes: Next I will use an example to give you an intuitive view about the potential of Carpool. For the naïve approach on the left hand side, a multicast flits with 6 destinations involves 6 independence flits injected sequentially. It entails 15 transfers and takes 10 cycles to deliver all the flits because of the near-end congestion at the source NI.
On the contrary, the multicast flit in Carpool takes a single cycle to enter the network, and fork new flit replica in the network along the way to the destination. As a result, only 6 flit transfers and 5 cycles are needed.
So, forking multicast flits removes the near-end contention at the source node, leading to reduced latency.

## Slide 15
R2
R3
SA
R1
D
SB
SA
R1
D
SB
Naïve bufferless
Carpool
A
A
B
A
B
A
B
A
AB
6 transfers, 5 cycles
3 transfers, 2 cycles
Merging hotspot flits reduces network load and
improves network bandwidth utilization
dst
dst
Hotspot Flit Merging
Notes: In another example, there are two hotspot flits having the same destination. For the naïve approach, as they encounter at the router in the middle, one of them is deflected, taking additional two hops before arriving at the destination. It takes 6 transfers and 5 cycles.
For Carpool, they are merged and delivered to their destination without deflection, which only need 3 transfers and 2 cycles.
So merging hotspot flits resolve the contention when it happens, reducing network load and improving the bandwidth utilization.

## Slide 16
Deadlock-free
  Efficient & scalable encoding
  Two-level hierarchical representation
  {clusterID, nodeList}
  No wire overhead
    nodeList shares half of payload channels (64-bit)
    Tradeoff: sending more flits
Low-cost hotspot flit merging (11.5% of router area)
  Only compare flits on higher-numbered ports
Design Features
Notes: Although forking and merging mechanisms appear to be very straightforward, there are a couple of issues which cannot be ignored. In a bufferless router, all flits that arrive at the same cycle must be sent out on their assigned output ports simultaneously. As a result, we can avoid deadlock by simply guaranteeing that the number of flits (including replicas) that request output ports at any given cycle is less than or equal to the total number of output ports in the router.
To enable Carpool, each flit needs to carry a list to identify either multiple destinations for a multicast flit or multiple senders for a hotspot flits. Directly representing N nodes with a bit-vector will cause channel width to increase linearly when the number of nodes scales. Instead, Carpool follows a two-level hierarchical representation.
A network is partitioned into multiple virtual clusters, indexed by clusterID. All nodes within a cluster are encoded with a bit-vector, called nodeList. With a 4-bit clusterID and a 64-bit nodeList, we can uniquely identify up to 1024 nodes. Now, instead of scaling linearly with respect to the number of nodes in the network, Carpool scales in terms of the number of clusters, which is much more scalable. To avoid adding additional wires, Carpool allows nodeList to use half of the links that were previously for the payload, sharing physical channels. This can avoid using dedicated channel to carry the nodelist, at the cost of sending more multicast flits. So, each MC flit involves sending 2 multicast flits.
When a hotspot flit arrives at one of the input ports, the router check if there are any hotspot flits at other input port can be merged with this flit. Instead of checking all the rest of input ports, Carpool numbers the input port in sequence in the order of N E S W and Local, and only check the flits on the higher-numbered port. This will enable merging operations with extremely low hardware cost. According to our RTL synthesis, the logic to support merging only accounts for 11.5% of router area.

## Slide 17
2. Key Observations
4. Hardware Implementation
5. Evaluation
3. Our Approach
1. Network-on-Chips Basics
4. Hardware Implementation

## Slide 18
MEI: Merge, Eject, and Inject
N
E
S
W
Eject
Ejector Tree
Kill Logic
Merge Logic
Injector
Muxes
Inject
RC: Route Computation
PS: Permutation Sort
PA: Port Allocation
ST: Switch Traversal (Crossbar)
DM: Destination Management
N
E
S
W
APV
APV
sorted DPV
flit timestamps
destination list
DPV
Router Microarchitecture
Carpool router is very simple and efficient
 RC: Find out desired port vector (DPV)
 MEI: Merge HS flits, eject a local-destined flit, and inject new flit
 PS: Find flit with the highest rank
 PA: Compute allocated port vector (APV) based on sorted DPV
 ST: Mux the flit to output ports
 DM: Update nodeList of MC flit
Notes: Here is the proposed router microarchitecture of Carpool. It has 2-stage pipelines and includes 6 major modules, performing router computation, permutation sort, merge/eject/inject, port allocation, switch traversal and destinations management.
Talk about each module.
Next, we will discuss some of the major operations. For more detail, please refer to our paper.

## Slide 19
Route Computation
Partition the network into NE/SE/SW/NW quadrant, mapping to N/E/S/W port
  Each port has a bit-vector (i.e., MASK) to indicate nodes assigned to the mapped quadrant
X-Y Routing
dst
dstList
&&
MASKN
&
&&
&
&&
&
&&
&
MASKE
MASKS
MASKW
DPV
1
0
multicast
For MC flits, outputs are assigned based on which quadrant contains its destinations.
For UC/HS flits, use X-Y routing
Notes: To compute the desired output port at each hop, we first partition the network into four quadrants as NE, SE, SW, and NW, and maps them to N, W, S, W respectively. Each port has a bit-vector to indicate the nodes assigned to the mapped quadrant.
For MC flit, the output are assigned if the corresponding quadrant contains any destinations.
For UC/HS, we still use the conventional dimension-order routing.

## Slide 20
Naïve Port Allocation
Flit 0
Flit 1
Flit 2
Flit 3
PE
Desired Port Vector
DPV0
PW
PN
PS
D
APV0
Allocated Port
Vector
DPV1
PW
APV1
PE
PN
PS
D
DPV2
PW
APV2
PE
PN
PS
D
DPV3
PW
APV3
PE
PN
PS
D
Long latency: 7.0ns
Reasons for sequential allocation
  Enforce strict priority
  Avoid deadlock due to multicast
Sequential port allocation is over-provisioned
and creates long critical path latency
Not necessary
Notes: In a bufferless router, in order to enforce a strict priority, a port request from a low-priority flit cannot be processed until requests from all higher-priority flits are resolved. Also, due to the existence of multicast flit, the output ports must be allocated one at a time to avoid deadlock. We found that enforcing strict priority often leads to a very long latency, slowing down the router clock rate. However, this is often overkilled as the bufferless router is normally operated under low-to-medium load so that some channels will remain idle most of the time.

## Slide 21
Flit 0
unicast
0
0
0
1
Pending
Desired
Port Vector
DPV0
Initial Allocated
Port Vector
0
0
0
0
IAPV0
0
0
0
1
PDPV0
FPA
0
0
0
1
APV0
1
0
1
1
DPV1
IPA
1
0
1
0
IAPV1
PPD
0
0
0
0
PDPV1
FPA
1
0
1
0
APV1
0
0
0
1
DPV2
IPA
0
0
0
0
IAPV2
PPD
0
0
0
1
PDPV2
FPA
0
1
0
0
APV2
0
0
0
0
DPV3
IPA
0
0
0
0
IAPV3
PPD
0
0
0
0
PDPV3
FPA
0
0
0
0
APV3
Flit 1
multicast
Flit 2
unicast
Flit 3
no flit
E W N S
E W N S
PPD
IPA
Parallel Port Allocation
Initial Port Allocation (IPA)
Pending Port Determination
(PPD)
Final Port Allocation (FPA)
IPA, PPD, and FPA occurs in par
Shortens the latency by 54% and improves the clock rate by 25%
Notes: So we proposed a parallel port allocation mechanism that significantly reduce the latency of port allocation in the presence of multicast traffic. The key idea is to divide the port allocation into multiple stages and perform the operation in each stage in parallel. In initial port allocation, only uncontended ports are initially assigned to each flits. The second stage simply calculates the pending port request. And the final port allocation performs fix priority allocation in parallel on each channel. With this, Carpool shortens the latency of port allocation by 54% and improves the router clock rate by 25%, which directly translate to boosted network bandwidth.

## Slide 22
2. Key Observations
4. Hardware Implementation
5. Evaluation
3. Our Approach
1. Network-on-Chips Basics
5. Evaluation

## Slide 23
Methodology
Emulate the injection rate, multicast, and hotspot behavior of real system
Generated packets have the probability of mc_rate/hs_rate to be a multicast/hotspot packet
  probability: 0.01(Low), 0.05(Mid), 0.1(High)
Area and latency are obtained through RTL synthesis based on 35nm standard cell library

## Slide 24
Chart: 
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4 | 0.42 | 0.44 | 0.46 | 0.48
Carpool | 100.1495 | 103.883 | 108.075 | 113.1185 | 118.3585 | 124.6465 | 132.1135 | 141.6765 | 154.2525 | 168.204 | 177.1775 | 184.5135 | 214.1195 | 411.1435 | 1191.707 | 1732.0165 | 2231.6505 | 2706.7875 | 3123.826 | 3568.3745 | 4041.612 | 4425.9005 | 4896.78 | 5394.711
Chart: 
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4 | 0.42 | 0.44 | 0.46 | 0.48
FANI/O | 161.3624 | 161.966 | 162.5696 | 163.3744 | 164.7828 | 165.5876 | 167.0966 | 169.008 | 171.6236 | 175.1446 | 181.2812 | 195.8682 | 850.8748 | 2622.642 | 5056.7596 | 7395.2066 | 10451.0322 | 13678.3808 | 16542.0604 | 19063.0964 | 22116.91 | 25229.0716 | 28014.2832 | 30737.1228
Chart: Injection Rate (packets/cycle/node)
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4 | 0.42 | 0.44 | 0.46 | 0.48
Carpool | 100.1495 | 103.883 | 108.075 | 113.1185 | 118.3585 | 124.6465 | 132.1135 | 141.6765 | 154.2525 | 168.204 | 177.1775 | 184.5135 | 214.1195 | 411.1435 | 1191.707 | 1732.0165 | 2231.6505 | 2706.7875 | 3123.826 | 3568.3745 | 4041.612 | 4425.9005 | 4896.78 | 5394.711
Chart: 
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4 | 0.42 | 0.44 | 0.46 | 0.48
BLESS | 149.0186 | 151.5278 | 155.9189 | 159.4039 | 164.3526 | 170.2074 | 179.1987 | 191.2568 | 209.5879 | 246.9471 | 420.5001 | 9803.2353 | 22248.5885 | 35063.9093 | 44377.8506 | 52659.047 | 60610.5624 | 67513.4413 | 73787.905 | 78923.5404 | 83553.9205 | 84867.6261 | 93795.2203 | 97253.3161
Chart: 
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4 | 0.42 | 0.44 | 0.46 | 0.48
FIFO | 159.6522 | 160.457 | 161.3624 | 162.5696 | 163.8774 | 165.8894 | 167.9014 | 171.02 | 175.3458 | 182.086 | 193.152 | 236.3094 | 1580.6272 | 3540.9188 | 6538.6982 | 9712.5276 | 12219.0772 | 16041.8772 | 19386.9278 | 23052.0876 | 26060.7318 | 29592.0936 | 32606.2708 | 35959.5706
Sweep MC and HS rate for BLESS, FANI/O, Carpool
Latency
Carpool resolves network congestion caused by multicast and hotspot traffic, reducing latency
Chart: Injection Rate (packets/cycle/node)
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4 | 0.42 | 0.44 | 0.46 | 0.48
FIFO | 159.6522 | 160.457 | 161.3624 | 162.5696 | 163.8774 | 165.8894 | 167.9014 | 171.02 | 175.3458 | 182.086 | 193.152 | 236.3094 | 1580.6272 | 3540.9188 | 6538.6982 | 9712.5276 | 12219.0772 | 16041.8772 | 19386.9278 | 23052.0876 | 26060.7318 | 29592.0936 | 32606.2708 | 35959.5706
Chart: 
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4 | 0.42 | 0.44 | 0.46 | 0.48
BLESS | 240.3953 | 272.1088 | 398.1961 | 17812.3229 | 50257.3244 | 71902.3109 | 88734.4427 | 104480.6485 | 108733.6031 | 116542.7214 | 125226.1565 | 129041.1163 | 130408.7 | 132427.212 | 134550.3437 | 136379.2717 | 134457.5033 | 138087.8278 | 135180.9893 | 136567.392 | 137422.0534 | 137553.7167 | 136937.9172 | 136955.621
Chart: 
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4 | 0.42 | 0.44 | 0.46 | 0.48
Carpool | 93.2065 | 117.5725 | 181.697 | 315.9065 | 730.456 | 2545.1335 | 3990.129 | 5183.0805 | 6317.5405 | 7477.742 | 8584.2335 | 9902.552 | 10885.838 | 11954.9945 | 13151.614 | 14034.161 | 15357.5885 | 16542.418 | 17308.1785 | 18564.4685 | 19938.855 | 20577.218 | 21829.9055 | 23008.447
LowMC-LowHS(0.01)
HighMC-HighHS(0.1)
Carpool vs. BLESS: -43%
Carpool vs. FANI/O: -26%
FANI/O requires 2.7X more area
Notes: This slide shows the average packet latency as we vary the injection rate. On the left-hand side, both multicast and hotspot rate are low, and on the right-hand side, both multicast and hotspot rate are high. We compare Carpool with BLESS and FANI/O. BLESS is a conventional bufferless NoC with no special support for MC and HS traffic, while FANI/O is a buffered design counterpart providing similar support.
On the left-hand side, we can see that Carpool constantly outperforms BLESS and FANI/O. The latency reduction over BLESS is mainly due to the removal of long serialization latency for injecting the multicast flits, and merging hotspot flits.
Although lacks of buffers, Carpool consistently outperforms FANI/O, as Carpool uses deflection to explore the path diversity of the network.
For the high mc and hs rate, Carpool still consistently enjoy much lower latency. FANI/O is more successful at handling the heavy congestion in this case. However, to achieve this, it consumes 2.7X more area. With the same area budget, we can replicate Carpool to multiple physical network, with each network running independently below the saturation to deliver lower latency.
So, in general, prior to saturation, Carpool has 43% and 26% lower latency compared to BLESS and FANI/O.
So Carpool resolves the network congestion caused by multicast and hotspot traffic, reducing the network latency.

## Slide 25
Chart: Injection Rate (packets/cycle/node)
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4 | 0.42 | 0.44 | 0.46 | 0.48
BLESS | 50.29 | 36.23 | 36.81 | 41.3 | 47.7 | 55.35 | 64.72 | 75.77 | 89.37 | 107.18 | 134.7 | 160.46 | 161.54 | 161.99 | 163.35 | 164.02 | 164.45 | 165.71 | 166.7 | 165.57 | 168.09 | 167.77 | 169.84 | 169.85
Chart: 
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4 | 0.42 | 0.44 | 0.46 | 0.48
BLESS | 35.88 | 56.51 | 97.87 | 152.48 | 153.28 | 154.98 | 156.74 | 154.56 | 156.07 | 157.12 | 158.46 | 160.2 | 162.06 | 163.72 | 164.77 | 165.04 | 166.18 | 167.25 | 167.83 | 168.8 | 169.58 | 169.75 | 170.63 | 171.56
Chart: 
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4 | 0.42 | 0.44 | 0.46 | 0.48
Carpool | 31.86 | 46.22 | 78.42 | 96.28 | 68.32 | 53.39 | 55.24 | 56.47 | 58.67 | 60.78 | 63.45 | 66.83 | 70.8 | 71.79 | 77.08 | 78.25 | 84.94 | 86.73 | 87.67 | 96.08 | 97.81 | 98.81 | 99.89 | 111.63
Chart: Injection Rate (packets/cycle/node)
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4 | 0.42 | 0.44 | 0.46 | 0.48
BLESS | 50.29 | 36.23 | 36.81 | 41.3 | 47.7 | 55.35 | 64.72 | 75.77 | 89.37 | 107.18 | 134.7 | 160.46 | 161.54 | 161.99 | 163.35 | 164.02 | 164.45 | 165.71 | 166.7 | 165.57 | 168.09 | 167.77 | 169.84 | 169.85
Chart: 
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4 | 0.42 | 0.44 | 0.46 | 0.48
FIFO | 104.78 | 86.17 | 94.94 | 110.63 | 129.02 | 148.79 | 169.29 | 190.25 | 211.59 | 233 | 254.54 | 276.16 | 291.83 | 306.18 | 318.73 | 332.86 | 346.25 | 359.31 | 373.63 | 387.15 | 401.01 | 414.96 | 428.81 | 442.27
Chart: 
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4 | 0.42 | 0.44 | 0.46 | 0.48
BLESS | 50.29 | 36.23 | 36.81 | 41.3 | 47.7 | 55.35 | 64.72 | 75.77 | 89.37 | 107.18 | 134.7 | 160.46 | 161.54 | 161.99 | 163.35 | 164.02 | 164.45 | 165.71 | 166.7 | 165.57 | 168.09 | 167.77 | 169.84 | 169.85
Chart: 
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4 | 0.42 | 0.44 | 0.46 | 0.48
FANI/O | 107.46 | 86.03 | 93.23 | 107.61 | 124.94 | 143.52 | 162.98 | 183.02 | 203.3 | 223.97 | 244.53 | 265.51 | 283.79 | 298.39 | 311.98 | 325.26 | 338.94 | 352.34 | 365.99 | 379.96 | 393.97 | 408.12 | 421.16 | 434.91
Chart: 
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4 | 0.42 | 0.44 | 0.46 | 0.48
Carpool | 55.81 | 38.83 | 38.54 | 42.97 | 49.62 | 57.71 | 67.39 | 78.52 | 91.68 | 104.02 | 110.18 | 109.37 | 99.03 | 68.49 | 62.17 | 65.12 | 66.09 | 67.3 | 68.52 | 70.01 | 71.1 | 72.13 | 72.87 | 75.13
Sweep MC and HS rate for BLESS, FANI/O, Carpool
Power
Carpool reduces power due to fewer packet injection and reduced hardware complexity
LowMC-LowHS(0.01)
HighMC-HighHS(0.1)
Carpool vs BLESS: 8%
Carpool vs. FANI/O: -51%
Notes: Compared to BLESS, Carpool has similar power consumption prior to saturation, despite requiring a greater circuit area to support multicast flit forking and hotspot flit merging.
For High MC-HS, Carpool consume less power than BLESS because it injects fewer packets into the network and deliver the packet much faster, reducing the network congestion.
Carpool reduces the power significantly compared with FANI/O. These power saving are mainly contributed by the reduced circuit complexity.

## Slide 26
Chart: 
| Carpool | CarpoolSPA | BLESS | FANI/O
Latency | 1 | 1.32 | 1.06 | 1.53
Critical Path Latency
Carpool increases the router clock rate and
lifts up the network bandwidth
1.32X
1.53X
Carpool
CarpoolSPA
BLESS
FANI/O
1.06X
1.00X
Synthesis using Cadence Encounter based on 35nm standard cell library
Notes: Using Cadence Encounter, we perform the RTL synthesis. We found out that Carpool reduces the router critical path latency by 24% at the expense of 2.4% of the area. Although Carpool consume a little more area than BLESS, it reduce the critical path by 5.7%.
Carpool has much lower critical path latency and area than FANI/O. It is mainly due to removed buffered and simplified control. Desipte this, Carpool still perform competitively with FANI/O. We conclude that Carpool deliver significant performance improvement with low hardware complexity.

## Slide 27
Chart: 
Area | 1 | 0.98 | 0.84 | 2.74
Area
Carpool requires much smaller area than the buffered counterpart
1.00X
0.98X
2.74X
Carpool
CarpoolSPA
BLESS
FANI/O
0.84X
Carpool vs. BLESS: 43% lower latency and 8% lower power
Carpool vs. FANI/O: 26% lower latency and 51% lower power
Notes: Using Cadence Encounter, we perform the RTL synthesis. We found out that Carpool reduces the router critical path latency by 24% at the expense of 2.4% of the area. Although Carpool consume a little more area than BLESS, it reduce the critical path by 5.7%.
Carpool has much lower critical path latency and area than FANI/O. It is mainly due to removed buffered and simplified control. Desipte this, Carpool still perform competitively with FANI/O. We conclude that Carpool deliver significant performance improvement with low hardware complexity.

## Slide 28
Summary
Problem: bufferless NoCs lack of efficient support for multicast (MC) and hotspot (HS) traffic
Our Goal: reduce the contention caused by MC and HS traffic in a bufferless NoC with low cost
Observation: MC flits increase serialization latency and HS flits waste network bandwidth
Key Idea: fork MC flits adaptively when NoC is not congested and merge HS flits opportunistically
  Carpool is the first bufferless NoC providing support for multicast and hotspot traffic
    Results
      43% lower latency and 8% lower power than conventional bufferless NoC
      26% lower latency, 50% lower power, and 64% less area than the buffered NoC with MC/HS support
Notes: Bufferless on-chip networks, known as bufferless NoCs, are considered as a good design option for multicore processor because of their low hardware complexity and high energy-efficiency. However, the current bufferless NoC lacks of efficient support for multicast and hotspot traffic.
A multicast packet can be a request from one nodes to many other nodes forming a 1-to-M pattern. The other is hotspot where M senders may send the packets to the same destinations, forming M-to-1 traffic.
So, in the following presentation, I will begin with highlighting two important observations. First, MC flit can create near-end congestion at the source NI. Second, the HS flit can create far-end congestion at the destinations.
We propose Carpool which was inspire by Carpooling in our real life where passengers can ride the same car sharing the road infrastructure to alleviate the traffic congestion. In this work, the basic idea of Carpool is to fork the multicast flits adaptively when the NoC is not congested and merge the hs flit in the network with low cost. The basic principle is to reduce the amount of traffic in the network to avoid contention caused by multicast and hotspot packets.
With these two simple mechanisms, Carpool can reduce the latency and power significantly, compared with the conventional bufferless NoC with no special support and its buffered counterpart with similar support. Also, it enjoys 64% of less area than its buffered NoC counterpart.

## Slide 29: Carpool: A Bufferless On-Chip Network
Xiyue Xiang
Wentao Shi, Saugata Ghose, Peng Lu,
Onur Mutlu, Nian-Feng Tzeng
Supporting Adaptive Multicast and Hotspot Alleviation

## Slide 30: Backup Slides

## Slide 31
Related Work
Bufferless NoCs
  Deflection-based: [Moscibroda+ ISCA’09], [Fallin+ HPCA’11], [Fallin+ NOCS’12], [Kim+ CAL’13], [Rachata+ SBAC-PAD’14], [Kim+ NOCS’14], [Xiang+ IPDPS’16]
  Drop-based: [Hayenga+ MICRO’09]
  Source-throttling: [Chang+ SBAC-PAD’12], [Nychis+ SIGCOMM’12], [Daya+ DAC’16]
Buffered NoCs with Multicast Support
  Path-based: [Goossens+ IEEE D&T’05], [Lu+ ISVLSI’06]
  Tree-based: [Jin+ HPCA’07], [Jerger+ ISCA’08], [Samman+ DATE’08], [Rodrigo+ MICRO’08], [Wang+ NOCS’09], [Krishna+ MICRO’11]
  Hybrid: [Abad+ HPCA’09]

## Slide 32
Flit Format
pkt
type
reqID
mshrID
timestamp
size
seq#
dst
payload
2
6
6
8
3
3
6
128
Field
Size
Unicast
pkt
type
reqID
mshrID
timestamp
size
seq#
cluster
ID
payload
2
6
6
8
4
4
4
64
Field
Size
nodeList
64
Multicast
pkt
type
dst
mshrID
timestamp
size
seq#
cluster
ID
payload
2
6
6
8
4
4
4
64
Field
Size
nodeList
64
Hotspot

## Slide 33
Sweep MC and HS rate for BLESS, FANI/O, Carpool
Throughput
Carpool delivers much better throughput prior network saturation than both BLESS and FANI/O
LowMC-LowHS(0.01)
HighMC-HighHS(0.1)
Chart: Injection Rate (packets/cycle/node)
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4 | 0.42 | 0.44 | 0.46 | 0.48
BLESS | 0.24103 | 0.48207 | 0.72597 | 0.967 | 1.208 | 1.4433 | 1.6915 | 1.9354 | 2.1793 | 2.4175 | 2.6557 | 2.7317 | 2.7274 | 2.7073 | 2.7217 | 2.7274 | 2.7073 | 2.7073 | 2.7073 | 2.6801 | 2.7202 | 2.7432 | 2.6901 | 2.6815
FANI/O | 0.12922 | 0.25845 | 0.38867 | 0.51789 | 0.64712 | 0.77634 | 0.90457 | 1.0348 | 1.162 | 1.2942 | 1.4195 | 1.5507 | 1.6342 | 1.6471 | 1.6421 | 1.6362 | 1.6342 | 1.6262 | 1.6233 | 1.6292 | 1.6342 | 1.6412 | 1.6272 | 1.6272
Carpool | 0.31908 | 0.63817 | 0.96031 | 1.2809 | 1.6015 | 1.9084 | 2.2366 | 2.5542 | 2.8916 | 3.1679 | 3.316 | 3.2687 | 2.9298 | 1.6473 | 0.68244 | 0.64122 | 0.64427 | 0.68244 | 0.72366 | 0.76947 | 0.77405 | 0.82595 | 0.82901 | 0.8916
Chart: Injection Rate (packets/cycle/node)
| 0.02 | 0.04 | 0.06 | 0.08 | 0.1 | 0.12 | 0.14000000000000001 | 0.16 | 0.18 | 0.2 | 0.22 | 0.24 | 0.26 | 0.28000000000000003 | 0.3 | 0.32 | 0.34 | 0.36 | 0.38 | 0.4 | 0.42 | 0.44 | 0.46 | 0.48
BLESS | 0.75753 | 1.5294 | 2.2826 | 2.693 | 2.6944 | 2.7245 | 2.7202 | 2.6141 | 2.7102 | 2.7059 | 2.6786 | 2.7059 | 2.7389 | 2.7518 | 2.7446 | 2.7231 | 2.7547 | 2.7217 | 2.7561 | 2.7446 | 2.7346 | 2.7159 | 2.7245 | 2.736
FIFO | 0.14911 | 0.2992 | 0.44831 | 0.59841 | 0.74851 | 0.89662 | 1.0487 | 1.1948 | 1.3469 | 1.493 | 1.6431 | 1.7903 | 1.827 | 1.835 | 1.8131 | 1.8191 | 1.8111 | 1.7982 | 1.8082 | 1.8022 | 1.8052 | 1.8042 | 1.8042 | 1.8012
Carpool | 1.4305 | 2.8397 | 4.2855 | 4.7969 | 3.2092 | 1.1038 | 1.1008 | 1.1847 | 1.2794 | 1.3878 | 1.5145 | 1.6672 | 1.8366 | 1.8504 | 2.0687 | 2.0794 | 2.3511 | 2.3771 | 2.3756 | 2.7267 | 2.771 | 2.7725 | 2.774 | 3.2519

## Slide 34
Chart: Normalized Value
| Normalized Latency | Normalized Deflection Rate | Normalized Fork Count
Carpool | 1 | 1 | 1
CarpoolSPA | 1.0587 | 1.4614 | 1.1629
Effect of Parallel Port Allocation
Carpool forks flits only when desired outputs are not contended, therefore reducing both deflection rate and latency

## Slide 35
Performance Breakdown
Chart: Normalized Value
| Normalized Latency | Normalized Throughput | Normalized Deflection Rate
Carpool | 1 | 1 | 1
ForkOnly | 1.93 | 0.99819 | 1.8321
MergeOnly | 2.5512 | 0.66376 | 1.5497
1.9X
2.6X
Forking and merging in Carpool significantly reduce the deflection and improve performance
Notes: To understand the individual benefits of enabling multicast flit forking and hotspot flit merging separately, we compare the performance of Carpool with a bufferless NoC with only forking or merging capability. This figures shows that with both multicast flit forking and hotspot flits merging, Carpool can deliver much lower latency, higher throughput thanks to the reduced deflection rate.

## Slide 36
Chart: Injection Rate (packets/cycle/node)
| 0.01 | 0.02 | 0.03 | 0.04 | 0.05 | 0.06 | 7.0000000000000007E-2 | 0.08 | 0.09 | 0.1 | 0.11 | 0.12 | 0.13 | 0.14000000000000001
Carpool without Adaptive Forking | 88.506 | 92.994 | 98.076 | 104.148 | 111.144 | 119.988 | 129.954 | 144.672 | 162.624 | 195.426 | 251.724 | 381.018 | 1230.438
Carpool with Adaptive Forking | 88.506 | 92.994 | 98.076 | 104.148 | 111.144 | 119.922 | 129.888 | 144.54 | 162.822 | 187.242 | 212.652 | 238.722 | 262.482 | 304.194 | 402.006 | 637.098 | 920.568
Effect of Adaptive Forking
Adaptive forking prevents NoCs being saturated prematurely by replicated multicast flits

## Slide 37: Carpool: A Bufferless On-Chip Network
Xiyue Xiang
Wentao Shi, Saugata Ghose, Peng Lu,
Onur Mutlu, Nian-Feng Tzeng
Supporting Adaptive Multicast and Hotspot Alleviation