## Slide 1: HAT: Heterogeneous Adaptive Throttling for On-Chip Networks
Kevin Kai-Wei Chang
Rachata Ausavarungnirun
Chris Fallin
Onur Mutlu
Notes: collaborative work done with rachata, chris, and my advisor Onur Mutlu
We are all from Carnegie Mellon University.

## Slide 2: Executive Summary
Problem: Packets contend in on-chip networks (NoCs), causing congestion, thus reducing system performance
Approach: Source throttling (temporarily delaying packet injections) to reduce congestion
1) Which applications to throttle? Observation: Throttling network-intensive applications leads to higher system performance Key idea 1: Application-aware source throttling
2) How much to throttle? Observation: There is no single throttling rate that works well for every application workload Key idea 2: Dynamic throttling rate adjustment
Result: Improves both system performance and energy efficiency over state-of-the-art source throttling policies
Notes: Here is a one slide summary of my talk today
The major problem is that packets contend in on-chip networks, which causes congestion.
As a result, system performance reduces due to increased network latency.
To address the problem of network congestion, we take the approach of source throttling,
which temporarily delays packet injections into the network.
There are two key questions that need to be answered when using source throttling.
First, which applications do we throttle?
We observe that throttling network-intensive applications leads to higher system performance.
Based on this observation, we develop our first key idea, application-aware source throttling, which
selectively throttles certain applications based on their network intensities.
The second key question is how much do we throttle selected applications?
We observe that there is no single throttling rate works well for every application workload.
Therefore, we develop our second key idea, dynamic throttling rate adjustment, to adapt to different workloads and program phases.
X:which adapts throttling to different workloads to achieve high perf.
X:which uses different throttling rate for different workloads.
Our evaluation shows we improve both system performance and energy efficiency over state-of-the-art source throttling policies.

## Slide 3: Outline
Background and Motivation
Mechanism
Comparison Points
Results
Conclusions
Notes: Here is the outline of the talk.
Next I’ll talk about the background and motivation of our work.

## Slide 4: On-Chip Networks
PE
Processing Element
(Cores, L2 Banks, Memory Controllers, etc)
PE
Connect cores, caches, memory controllers, etc.
  Buses and crossbars are not scalable
PE
PE
PE
…
IInterconnect
Notes: In a multi-core processor, an interconnect serves as a communication substrate for cores, caches, ….
However as core count continues to increase, conventional interconnects such as busses and crossbards no longer scale adequately.
<FLIP>

## Slide 5: On-Chip Networks
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
Router
Processing Element
(Cores, L2 Banks, Memory Controllers, etc)
PE
Connect cores, caches, memory controllers, etc
  Buses and crossbars are not scalable
Packet switched
2D mesh: Most commonly used topology
Primarily serve cache misses and memory requests
Notes: One commonly proposed solution is on-chip network (NoC), which allows cores to communicate with a packet switched substrate.
Here is a figure showing an on-chip network that uses a 2d-mesh topology which
is commonly used due to its low layout complexity.
This is also the topology we used for our evaluations, but our mechanism is also applicable to other topologies.
In most multi-core systems, NoC primarily serves cache misses and memory requests.

## Slide 6: Network Congestion Reduces Performance
Network congestion:
system performance
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
R
PE
P
P
P
P
P
Congestion
R
Router
Processing Element
(Cores, L2 Banks, Memory Controllers, etc)
PE
P
Packet
Limited shared resources (buffers and links)
due to design constraints: Power, chip area, and timing
Notes: Typically, a network has limited shared resources due to various design constraints, such as power, chip area and timing.
Therefore, a network will sometimes experience network congestion when there is a large amount of traffic.
Network congestion reduces network throughput, and hence system performance.
Here is a quick illustration on showing how congestion can occur in a network. Four different nodes send their packets (the red packets) to a central node.
Since multiple packets are contending in the central router, causing congestion, the yellow packet’s injection is delayed.
------------

## Slide 7: Goal
Improve system performance in a highly congested network
Observation: Reducing network load (number of packets in the network) decreases network congestion, hence improves system performance
Approach: Source throttling (temporarily delaying new traffic injection) to reduce network load
Notes: Our goal in this work is to improve application performance in a highly congested network.
To achieve this, we observe that reducing network load (defined as…) decreases network congestion, hence it improves performance as I will show later.
To reduce network load, we take the approach of source throttling, which temporarily delays new traffic injection.
Let me show an example on how throttling can improve system performance.

## Slide 8: Source Throttling
PE
PE
PE
…
I
Network
Processing Element
(Cores, L2 Banks, Memory Controllers, etc)
PE
P
Packet
I
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
Long network latency when the network is congested
Notes: Here is a figure showing a network that has multiple nodes connected to it.
When there is a large amount of packets in the network, which causes congestion, the network latency significantly increases for every packet.

## Slide 9: Source Throttling
PE
PE
PE
…
I
Network
Processing Element
(Cores, L2 Banks, Memory Controllers, etc)
PE
P
Packet
I
P
P
P
P
P
P
P
P
P
P
P
P
P
P
P
Throttle
Throttle
Throttle
P
Throttling makes some packets wait longer to inject
Average network throughput increases, hence higher
system performance
P
P
P
P
P
P
Notes: When we apply source throttling on the nodes, which delays their packet injections
<CLICK>
The network load reduces with more packets waiting at the sources to be injected.
Even though throttling makes some packets wait longer at the sources, the average network throughput actually increases due to less number of in-flight packets.
As a result, source throttling leads to higher system performance.

## Slide 10: Key Questions of Source Throttling
Every cycle when a node has a packet to inject, source throttling blocks the packet with probability P
  We call P “throttling rate” (ranges from 0 to 1)
Throttling rate can be set independently on every node
Two key questions:
Which applications to throttle?
How much to throttle?
Naïve mechanism: Throttle every single node with a constant throttling rate
Notes: Then how exactly do we throttle packet injections?
In every cycle, when a node has a packet to inject, we block that packet with a probability P,
We call this probability P “throttling rate”, which ranges from 0 to 1.
This throttling rate can be set independently on every node.
Given this tunable knob, throttling rate, we need to answer two key questions.
1. First, which applications do we throttle?
2. Second, how much do we throttle these applications?
A naïve way of source throttling is to block injection of every node with a constant throttling rate. However, this does not work well.
And we will explain why this is the case by going through some key observations on answering these two questions.

## Slide 11: Key Observation #1
Throttling network-intensive applications leads to higher system performance
Configuration: 16-node system, 4x4 mesh network,
8 gromacs (network-non-intensive), and 8 mcf (network-intensive)
gromacs
…
mcf
I
P
P
P
P
P
P
P
P
P
P
Throttle
Throttling gromacs decreases system performance by 2% due to minimal network load reduction
Notes: Our first key observation is that throttling network-intensive…..
To illustrate this point, we set up an experiment on a 16-node system running 8 copies of gromacs, which is a network-non-intensive spec benchmark,
and 8 copies of mcf, which is a network-intensive spec benchmark.
Here I am showing an abstracted view of the system with gromacs and mcf connected to the same network.
Since mcf is an network-intensive application, a large fraction of the network is occupied by packets from mcf.
Let’s consider different throttling scenarios.
First, when ONLY gromacs applications are throttled,
the network load reduces minimally without changing much.
The system performance averaged across all applications actually decreases
by 2% due to minimal network load reduction and increased network latency on gromacs.
<FLIP>

## Slide 12: Key Observation #1
Throttling mcf increases system performance by 9% (gromacs: +14% mcf: +5%) due to reduced congestion
gromacs
…
Throttling network-intensive applications leads to higher system performance
Configuration: 16-node system, 4x4 mesh network,
8 gromacs (network-non-intensive), and 8 mcf (network-intensive)
mcf
I
P
P
P
P
P
P
P
P
P
P
Throttle
Notes: On the other hand, when mcf is throttled <CLICK> the network load reduces significantly.
<CLICK>
As a result, throttling mcf increases average system performance by 9%.
It allows gromacs to make much faster progress with less network latency.
Thus, gromacs’ performance increases by 14%.
Even though mcf is throttled, mcf’s performance still increases due to reduced network congestion.

## Slide 13: Key Observation #1
gromacs
…
Throttling network-intensive applications leads to higher system performance
Configuration: 16-node system, 4x4 mesh network,
8 gromacs (network-non-intensive), and 8 mcf (network-intensive)
mcf
I
P
P
P
P
P
Throttle
Throttling mcf reduces congestion
gromacs benefits more from less network latency
Throttling network-intensive applications reduces congestion
Benefits both network-non-intensive and network-intensive applications
Notes: The reason network-non-intensive applications, such as gromacs, benefit more from reduced network latency is that
serving each packet injected by network–non-intensive apps allows these applications to make greater forward progress
than when serving a packet from a network-intensive app.
This b/c network-non-int. apps inject fewer packets overall.
In sum, BULLET

## Slide 14: Key Observation #2
mcf
There is no single throttling rate that works well for every application workload
Network runs best at or below a certain network load
Dynamically adjust throttling rate to avoid overload and under-utilization
…
mcf
I
P
P
P
P
P
P
P
P
gromacs
gromacs
I
P
P
P
Throttle 0.8
…
Throttle 0.8
Throttle 0.8
Throttle 0.8
Notes: Our second key observation is that there is no single throttling rate that works well for every application workload
Let me show a quick example on applying the same throttling rate on different workloads.
First, here is a figure showing a system with only gromacs running. As described before, gromacs is a network-non-intensive application, so there are ONLY a few packets in the network. Say that we apply a throttling rate of 0.8 on every node. The network will STILL REMAIN lightly loaded as before,
* so throttling gromacs is unnecessary and can reduce system performance.
On the other hand, here is a system running only mcf. Since mcf is a network-intensive application,
the network is heavily congested with a large amount of packets. With the same throttling rate applied to mcf,
the network load reduces more than throttling gromacs.
* Since throttling reduces congestion, it can increase performance for mcf.
As a result, applying the same throttling rate to different workloads can yield very different network loads.
Why is this an issue?
<CLICK>
We observe that the network runs ….
So, we NEED to dynamically adjust the throttling rate for different workloads to avoid overloading the network.
--------------LONG------------------
So we need to adjust the throttling rate differently depending on the workloads running in the system.
Otherwise, if we simply throttle every workload with the same throttling rate, then we can get very different results in the network.
In some workloads, we can be over-throttling applications with a too aggressive throttling rate if the network is only lightly loaded to begin with.
On the other hand, we can be under-throttling applications if the throttling rate is not high enough.
<CLICK>
Therefore, we NEED to dynamically adjust throttling rate for each workload to avoid overloading the network.

## Slide 15: Outline
Background and Motivation
Mechanism
Comparison Points
Results
Conclusions
Notes: Next I will talk about our mechanism-> flip through the slide

## Slide 16: Heterogeneous Adaptive Throttling (HAT)
Application-aware throttling: Throttle network-intensive applications that interfere with network-non-intensive applications
Network-load-aware throttling rate adjustment: Dynamically adjust throttling rate to adapt to different workloads and program phases
Notes: Previous slide -> called Heterogeneous Adaptive Throttling (HAT), a new source throttling mechanism built on top of the two key observations I just described.
HAT has two key components :
The first component is app-aware throttling.
HAT throttles network-intensive apps that interfere with network-non-intensive applications
to reduce network congestion and allow network-non-intensive applications to send their packets through the network more quickly.
2.The second component is network-load….
HAT …BULLET, so that it provides high performance

## Slide 17: Heterogeneous Adaptive Throttling (HAT)
Application-aware throttling: Throttle network-intensive applications that interfere with network-non-intensive applications
Network-load-aware throttling rate adjustment: Dynamically adjust throttling rate to adapt to different workloads and program phases
Notes: Let’s take a look at how HAT performs application-aware throttling.

## Slide 18: Application-Aware Throttling
Measure applications’ network intensity
Throttle network-intensive applications
Network-non-intensive
(Unthrottled)
How to select unthrottled applications?
Σ MPKI < Threshold
Higher L1 MPKI
Use L1 MPKI (misses per thousand instructions) to estimate network intensity
Leaving too many applications unthrottled overloads the network
Select unthrottled applications so that their total network
intensity is less than the total network capacity
Network-intensive
(Throttled)
App
Notes: First, HAT measures each application’s network intensity.
Since NoC primarily serves L1 cache misses in our evaluated system, we use L1 MPKI as a proxy to intensity.
  Once applications’ intensity is measured.
  HAT will pick some network-non-intensive applications to be unthrottled while throttling the remaining network-intensive applications.
  Then, how do we select these untthrottled applications?
  <CLICK>
  The unthrottled apps burden the network since their packet injections are not delayed
  so we want to make sure that we don’t leave too many applications unthrottled such that they overload the network.
  <CLICK>
  Therefore, we want to select unthrottled applications so that their total network intensity is less less the ….
  To do so, HAT first sorts apps by their measured L1 MPKI. Next starting from the least mpki app,
  the applications are classified as network non intensive until their sum of MPKI exceeds a pre-set threshold.
  All remaining applications are then classified as network intensive.
  After applications have been classified, HAT applies throttling to network-intensive applications.
  -------------------------------------------REMOVED---------------------------------------------
  HAT throttles intensive application
  Again, the reason to throttle them is to reduce congestion and allow non-intensive app,
  which are more sensitive to network latency, to send packets through the network more quickly.
  CAP ensures that the traffic of non-intensive applications provides sufficient load without causing severe network congestion.
  So it should be scaled with network capacity and tuned for the particular network design.

## Slide 19: Heterogeneous Adaptive Throttling (HAT)
Application-aware throttling: Throttle network-intensive applications that interfere with network-non-intensive applications
Network-load-aware throttling rate adjustment: Dynamically adjust throttling rate to adapt to different workloads and program phases
Notes: Now let’s talk about the second component of HAT.

## Slide 20: Dynamic Throttling Rate Adjustment
Different workloads require different throttling rates to avoid overloading the network
But, network load (fraction of occupied buffers/links) is an accurate indicator of congestion
Key idea: Measure current network load and dynamically adjust throttling rate based on load
  if network load > target:
  Increase throttling rate
  else:
  Decrease throttling rate
If network is congested, throttle more
If network is not congested, avoid unnecessary throttling
Notes: In the previous slide, our second key observation shows that different workloads require different throttling rates to avoid overloading the network.
But, network load (concretely defined as fraction of occupied buffers/links) is an accurate indicator of congestion.
Based on this observation, our key idea is to measure the current network load and dynamically adjust throttling rate to
make sure the network load stay below an empirically observed target without applying any unnecessary throttling.
Our algorithm works as the following:
If the current network load is greater than the target, we increase the throttling rate to reduce congestion.
otherwise if the load is below the target, we decrease the throttling rate to avoid unnecessary throttling.

## Slide 21: Heterogeneous Adaptive Throttling (HAT)
Application-aware throttling: Throttle network-intensive applications that interfere with network-non-intensive applications
Network-load-aware throttling rate adjustment: Dynamically adjust throttling rate to adapt to different workloads and program phases
Notes: Now I have told you about two components of HAT. Let me tell you how HAT operates in time.

## Slide 22: Epoch-Based Operation
Application classification and throttling rate adjustment are expensive if done every cycle
Solution: recompute at epoch granularity
Time
Current Epoch
(100K cycles)
Next Epoch
(100K cycles)
During epoch:
Every node:
Measure L1 MPKI
Measure network load
Beginning of epoch:
All nodes send measured info to a central controller, which:
Classifies applications
Adjusts throttling rate
Sends new classification and throttling rate to each node
Notes: Application classification and throttling rate….. If done at a per-cycle basis is expensive,
we want to reduce the computation overhead by recomputing at epoch gran.
In this work, we set an epoch to 100K cycles.
During an epoch, every node measures its L1 MPKI and the network load.
Once an epoch finishes, all nodes send measured information to a central controller, which classifies
applications, and adjusts throttling rate.
Then, the central controller sends the new application classification and throttling rate to each node.

## Slide 23: Putting It Together: Key Contributions
1. Application-aware throttling
  Throttle network-intensive applications based on applications’ network intensities
2. Network-load-aware throttling rate adjustment
  Dynamically adjust throttling rate based on network load to avoid overloading the network
HAT is the first work to combine application-aware throttling and network-load-aware rate adjustment
Notes: Let me put together everything now by explaining what our key contributions are.
First, we propose application-aware throttling which throttles network-intensive applications to reduce congestion
and allow network-non-intensive applications to make faster progress.
Second, we propose network-load-aware throttling rate adjustment.
We observe that different workloads require different throttling rates to avoid overloading the network.
So we dynamically ….
To our knowledge, HAT is the first work to combine these two key principles to perform source throttling.
--------------OLD-----------
we observe that there is no single throttling rate that works well for every application workload
and network runs best at or below a certain network load.
Therefore we dynamically adjusting throttling rate…

## Slide 24: Outline
Background and Motivation
Mechanism
Comparison Points
Results
Conclusions
Notes: Now let’s take a look at our comparison points.

## Slide 25: Comparison Points
Source throttling for bufferless NoCs [Nychis+ Hotnets’10, SIGCOMM’12]
  Throttle network-intensive applications when other applications cannot inject
  Does not take network load into account
  We call this “Heterogeneous Throttling”
Source throttling for buffered networks [Thottethodi+ HPCA’01]
  Throttle every application when the network load exceeds a dynamically tuned threshold
  Not application-aware
  Fully blocks packet injections while throttling
  We call this “Self-Tuned Throttling”
Notes: The first work by Nychis et al. proposes source throttling for bufferless networks.
In particular, they propose throttling network….
However, their mechanism does not take network load into account when adjusting throttling rate,
hence can over- or under-throttle applications.
We call this work heterogeneous throttling in the results I’ll present.
The second work by thottethodi proposes source throttling for off-chip
It dynamically triggers throttling based on buffer occupancy.
There are two major disadvantages:
First, it is not application aware. It throttles every node, which can lose performance improvement opportunity by throttling network-non-intensive apps.
Second, it fully blocks the packet injections without any throttling rate adjustment, which can over-throttle applications.
We will call this work self-tuned in the results I’ll present.

## Slide 26: Outline
Background and Motivation
Mechanism
Comparison Points
Results
Conclusions
Notes: I will now show some results.

## Slide 27: Methodology
Chip Multiprocessor Simulator
  64-node multi-core systems with a 2D-mesh topology
  Closed-loop core/cache/NoC cycle-level model
  64KB L1, perfect L2 (always hits to stress NoC)
Router Designs
  Virtual-channel buffered router: 4 VCs, 4 flits/VC [Dally+ IEEE TPDS’92]
    Input buffers to hold contending packets
  Bufferless deflection router: BLESS [Moscibroda+ ISCA’09]
    Misroute (deflect) contending packets
Notes: First, we use a 64-node cycle-level simulator with a 2D-mesh topology on-chip network.
The CPU cores model stalls, and interact with the caches and network in a closed-loop way.
Each core has a private L1 and there is a shared L2 cache to stress the network.
Routers:
We eval our throttling mechanism on top of different router designs.
The first design is a conventional virtual channel router, which has input buffers to hold contending packets
The second design is BLESS, a bufferless deflection router, that doesn’t have these buffers and instead deflect contending packets to different links.

## Slide 28: Methodology
Workloads
  60 multi-core workloads of SPEC CPU2006 benchmarks
  4 network-intensive workload categories based on the network intensity of applications (Low/Medium/High)
Metrics System performance: Fairness: Energy efficiency:
Notes: Workloads:
We form 60 multi-core workloads using spec cpu 2006 benchmarks. We divide the workload into 4 intensive workload categories based on the intensity of applications.
The intensity varies from low, medium and high based on L1 MPKI
Metrics:
We evaluate system performance using weighted speedup which is a measure of system throughput normalized to when running alone.
We also evaluate fairness using maximum slowdown to show that the algorithm doesn’t unfairly penalize any application.
Finally, we measure energy efficiency as performance per watt.

## Slide 29: Performance: Bufferless NoC (BLESS)
Chart: Workload Categories
| HL | HML | HM | H | AVG
No Throttling | 39.5123 | 38.9303 | 25.2614 | 15.0946 | 29.2127
Heterogeneous | 40.5786 | 40.1135 | 26.1258 | 15.3219 | 30.0343
HAT | 43.2522 | 43.3974 | 28.1143 | 16.3917 | 32.2514
1. HAT provides better performance improvement than state-of-the-art throttling approaches
2. Highest improvement on heterogeneous workloads
- L and M are more sensitive to network latency
+ 7.4%
+ 9.4%
+ 11.5%
+ 11.3%
+ 8.6%
Notes: I will first present performance results on BUFFERLESS networks USING BLESS
Y-axis
X-axis different workload categories and each category has 15 workloads.
Again, the letter stands for intensity level. For example H stands for high intensity.
Each category is a combination of different intensity applications, except for the one that contains all high intensity applications.
In each bar group, the blue bar is for the baseline system without any throttling.
The second red bar uses heterogeneous throttling proposed by Nychis et al..
The last green bar is HAT.
I want to draw two conclusions.
First, HAT CONSISTENLY provides…BLUE. On average it achieve 7.4% performance improvement over hetero.
Second, HAT provides highest …. OVER the baseline compared to homogeneous workloads with all high intensity apps
b/c L & M intensity applications are more sensitive to network latency and can benefit more from reduced congestion.

## Slide 30: Performance: Buffered NoC
Chart: Workload Categories
| HL | HML | HM | H | AVG
No Throttling | 43.4324 | 42.8599 | 30.7187 | 20.7078 | 33.8653
Self-Tuned | 43.3173 | 42.7665 | 29.9213 | 20.454 | 33.5555
Heterogeneous | 43.7044 | 43.061 | 30.6928 | 20.9577 | 34.0367
HAT | 44.8544 | 44.8571 | 32.3874 | 20.9946 | 35.1869
HAT provides better performance improvement than prior approaches
+ 3.5%
Notes: Now, I’ll show the performance results on buffered network.
Y-axis, again shows the weighted speedup and x-axis shows different workload categories
For each bar group, in addition to HAT and hetero., we also show perf of self-tuned by thottethodi
A few conclusions:
First, we see similar perf trend as in bufferless noc. HAT provides better perf improvement than prior works. On average, system performance improves by 3.5% over heterogeneous throttling
Second, although congestion is much lower in a buffered network, HAT still provides performance benefits.
3. Third, we observe that self-tuned throttling does not improve system performance because prior work shows that self-tuned benefits in terms of network latency when network becomes saturated without examining the application performance.
------------------------------------
evaluates
it based on network performance metric (such as network latency) without examining the application performance.
X: b/c it performs hard throttling by completely blocking traffic injection until congestion is cleared.
X: This will only temporarily reduces congestion, but congestion will return soon once packet injections are allowed again.

## Slide 31: Application Fairness
Chart: 
| Buffered
No Throttling | 1
Self-Tuned | 1.0066
Heterogeneous | 0.9967
HAT | 0.95261
HAT provides better fairness than prior works
- 15%
- 5%
Chart: Normalized Maximum Slowdwon (Lower is better)
| BLESS
No Throttling | 1
Heterogeneous | 1.1176
HAT | 0.85144
Notes: To show that HAT does not unfairly penalize any application through throttling, we evaluate the application fairness by using max slowdown.
The Y-axis shows the max slowdown normalized to the baseline.
NOTE that lower value is better for maximum slowdown.
The bar group on the left shows the results on bufferless networks and the bar group on the right shows results on buffered networks.
On average HAT provides better fairness than prior works.
This is b/c the most slowed down apps tend to be latency-sensitive applications.
Therefore, HAT is able to improve the performance of these applications by using application-aware throttling

## Slide 32: Network Energy Efficiency
Chart: Normalized Perf. per Watt
| BLESS | Buffered
No Throttling | 1 | 1
HAT | 1.085 | 1.05
+ 8.5%
+ 5%
HAT increases energy efficiency by reducing network load by 4.7% (BLESS) or 0.5% (buffered)
Notes: In addition, we evaluate HAT’s effect on network energy efficiency
Y:
X:
On average, HAT increases energy efficiency for both network designs.
This is because HAT allows packets to traverse through the network more quickly with less congestion, thus reducing dynamic energy consumption.
-----------
SHORT: On average, HAT increases energy efficiency because it reduces network load by 4.7% for BLESS or 0.5% for buffered networks.
LONG: On average, HAT increases energy efficiency by 8.5% and 5% for BLESS and buffered networks, respectively.
This is because HAT reduces network load by 4.7% for bless or 0.5% for buffered network.

## Slide 33: Other Results in Paper
Performance on CHIPPER [Fallin+ HPCA’11]
  HAT improves system performance
Performance on multithreaded workloads
  HAT is not designed for multithreaded workloads, but it slightly improves system performance
Parameter sensitivity sweep of HAT
  HAT provides consistent system performance improvement on different network sizes
Notes: Here’s a highlight of other results in the paper.
We evaluate the performance of HAT on another bufferless router design called CHIPPER. HAT still improves system performance.
Second, although HAT.. BULLET
Finally, we evaluate parameter sensitivity sweep of HAT.
HAT provides …
I encourage you to read the paper.

## Slide 34: Conclusions
Problem: Packets contend in on-chip networks (NoCs), causing congestion, thus reducing system performance
Approach: Source throttling (temporarily delaying packet injections) to reduce congestion
1) Which applications to throttle? Observation: Throttling network-intensive applications leads to higher system performance Key idea 1: Application-aware source throttling
2) How much to throttle? Observation: There is no single throttling rate that works well for every application workload Key idea 2: Dynamic throttling rate adjustment
Result: Improves both system performance and energy efficiency over state-of-the-art source throttling policies
Notes: Here is a one slide summary of my talk today
The major problem is that packets contend in on-chip networks, which causes congestion.
As a result, system performance reduces due to increased network latency.
To address the problem of network congestion, we take the approach of source throttling,
which temporarily delays packet injections into the network.
There are two key questions that need to be answered when using source throttling.
First, which applications do we throttle?
We observe that throttling network-intensive applications leads to higher system performance.
Based on this observation, we develop our first key idea, application-aware source throttling, which
selectively throttles certain applications based on their network intensities.
The second key question is how much do we throttle selected applications?
We observe that there is no single throttling rate works well for every application workload.
Therefore, we develop our second key idea, dynamic throttling rate adjustment,
Which uses different throttling rate for different workloads.
which adapts throttling to different workloads to achieve high perf.
Our evaluation shows we improve both system performance and energy efficiency over state-of-the-art source throttling policies.

## Slide 35: HAT: Heterogeneous Adaptive Throttling for On-Chip Networks
Kevin Kai-Wei Chang
Rachata Ausavarungnirun
Chris Fallin
Onur Mutlu
Notes: Name: … phd student from CMU
Ttitle
collaborative work done with rachata, chris, and my advisor, Onur Mutlu

## Slide 36: Throttling Rate Steps

## Slide 37: Network Sizes

## Slide 38: Performance on CHIPPER/BLESS
Injection rate (number of injected packets / cycle):
+8.5% (BLESS) or +4.8% (CHIPPER)

## Slide 39: Multithreaded Workloads

## Slide 40: Motivation
Chart: Throttling Rate (%)
| 80.0 | 82.0 | 84.0 | 86.0 | 88.0 | 90.0 | 92.0 | 94.0 | 96.0 | 98.0 | 100.0
Workload 1 | 9.6783 | 9.6962 | 9.7273 | 9.7829 | 9.8607 | 9.9987 | 10.286 | 10.713 | 9.5421 | 7.5361
Workload 2 | 14.5502 | 14.5837 | 14.6565 | 14.7872 | 15.0076 | 15.2556 | 15.1927 | 14.4139 | 12.8768 | 10.7685
90%
94%

## Slide 41: Sensitivity to Other Parameters
Network load target: WS peaks at b/w 50% and 65% network utilization
  Drops more than 10% beyond that
Epoch length: WS varies by less than 1% b/w 20K and 1M cycles
Low-intensity workloads: HAT does not impact system performance
Unthrottled network intensity threshold:

## Slide 42: Implementation
L1 MPKI: One L1 miss hardware counter and one instruction hardware counter
Network load: One hardware counter to monitor the number of flits routed to neighboring nodes
Computation: Done at one central CPU node
  At most several thousand cycles (a few percent overhead for 100K-cycle epoch)