## Slide 1: Exploiting Compressed Block Size as an Indicator of Future Reuse
Gennady Pekhimenko,
Tyler Huberty, Rui Cai,
Onur Mutlu, Todd C. Mowry
Phillip B. Gibbons,
Michael A. Kozuch

## Slide 2: Executive Summary
In a compressed cache, compressed block size is an additional dimension
Problem: How can we maximize cache performance utilizing both block reuse and compressed size?
Observations:
  Importance of the cache block depends on its compressed size
  Block size is indicative of reuse behavior in some applications
Key Idea: Use compressed block size in making cache replacement and insertion decisions
Results:
  Higher performance (9%/11% on average for 1/2-core)
  Lower energy (12% on average)
Notes: Traditional cache replacement and insertion policies mainly focus on block reuse.
But in a compressed caches, compressed block size is an additional dimension.
In this work, we aim to answer a question on: How can we maximize cache performance utilizing both block reuse and compressed size?
We make two observations:
…
We then apply this observation in two new cache management mechanisms that use compressed block size in making cache replacement and insertion decisions.
Our evaluation shows that these mechanisms are effective in improving both the performance (11% increase on average) and energy efficiency (
12% on average) of the modern systems.

## Slide 3: Potential for Data Compression
Compression Ratio
Latency
0.5
1.5
1.0
2.0
FPC
X
C-Pack
X
BDI
X
SC2
X
Frequent Pattern
Compression (FPC)
[Alameldeen+, ISCA’04]
C-Pack [Chen+,
Trans. on VLSI’10]
Base-Delta-Immediate (BDI)
[Pekhimenko+, PACT’12]
Statictical Compression
(SC2) [Arelakis+, ISCA’14]
5 cycles
9 cycles
1-2 cycles
8-14 cycles
Can we do better?
All use LRU replacement policy
All these works showed significant performance improvements
Notes: Several recent works showed the potential of data compression for on-chip caches.
The proposed algorithms offer different tradeoffs by providing higher effective cache capacities but with increase in access latency due to decompression.
For example, FPC compression algorithm provides almost 1.5X ratio with 5 cycles decompression latency.
C-Pack, offers 1.64X but with 9 cycles decompression.
More recently, BDI: 1.53X with 1-2 cycles decompression
SC^2 – 2X but with 8-14 cycles decompression.
While all these works demonstrate significant potential for on-chip data compression, they still use conventional LRU replacement policy.
The question we ask in this work: How can we do better if we use compression block size in cache management decisions?

## Slide 4: Size-Aware Cache Management
Compressed block size matters
Compressed block size varies
Compressed block size can indicate reuse
Notes: In order to answer this question we make three major observations.
#1. Compressed block size matters in cache management decisions
#2. Compressed block size varies (both within and between applications). Which makes the block size a new dimension in cache management.
#3. And probably the most surprising result is that compressed block size can sometimes indicate block’s reuse.

## Slide 5: #1: Compressed Block Size Matters
A
Y
B
Cache:
X
miss
hit
A
Y
hit
B
miss
C
miss
C
time
X
miss
hit
B
C
time
A
Y
miss
hit
hit
Belady’s OPT Replacement
Size-Aware Replacement
saved cycles
Size-aware policies could yield fewer misses
X A Y B C
Access stream:
large
small
Notes: Our first observation is that compressed block size matters.
I will demonstrate this by showing that Size-aware replacement can outperform Belady’s OPT algorithm.
We have small cache, and expected access stream in the steady state. We assume that the cache initially has large block Y, and three small blocks:
A,B,C.

## Slide 6: #2: Compressed Block Size Varies
Chart: Cache Coverage, %
| mcf | lbm | astar | tpch2 | calculix | h264ref | wrf | povray | gcc
size: 0-7 | 95747 | 74979 | 2102620 | 375881841 | 50813 | 2233065 | 12892190 | 1907038 | 5443123
size: 8-15 | 591 | 12817602 | 1006006 | 419865 | 5819 | 2888878 | 994569 | 745306 | 329320
size: 16-23 | 1286278 | 879730 | 16461026 | 14614264 | 119491 | 11576435 | 317339 | 5062854 | 15140710
size: 24-31 | 101237209 | 1202307 | 169424087 | 34810743 | 84860 | 1509034 | 309028 | 3195618 | 86700988
size: 32-39 | 438661822 | 793833 | 670753253 | 50533937 | 194054 | 97922655 | 518059 | 6346086 | 60228812
size: 40-47 | 1596238818 | 828881 | 281444015 | 72471798 | 191533 | 2363534 | 690912 | 15479836 | 62365042
size: 48-55 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
size: 56-63 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
size: 64 | 208129457 | 1192267355 | 240781337 | 500266655 | 574276 | 4743877 | 2242311 | 14040601 | 5767781
Compressed block size varies within and between applications
Block size, bytes
BDI compression algorithm [Pekhimenko+, PACT’12]
Notes: Our second observation is that compressed block size varies both within and between applications.
We show this by demonstrating the block size distribution for a representative set of our applications. In this experiment, and for the rest of the talk we use BDI compression, but observations are true for other compression algorithms as well.
First, there are applications with …
Second, there are applications with a single dominant compressed size.

## Slide 7: #3: Block Size Can Indicate Reuse
bzip2
Block size, bytes
Different sizes have different dominant reuse distances
Notes: But probably the most surprising observation is the observation #3.
What we found is that compressed block size can sometimes be an indicator of data reuse.
To show this, we perform a special experiment for our applications. Here I’m showing one representative application called bzip2.
For every compressed cache block size with BDI we show the distribution of the reuse distances (measured in the # of memory accesses).
As you can see, some sizes … have short reuse distance, while others, e.g., 34-byte blocks have long reuse distance.
Out of 23 memory-intensive applications total, 15 apps have some correlation between the size and reuse.

## Slide 8: Code Example to Support Intuition
int A[N]; // small indices: compressible
double B[16]; // FP coefficients: incompressible
for (int i=0; i<N; i++) {
int idx = A[i];
for (int j=0; j<N; j++) {
sum += B[(idx+j)%16];
}
}
long reuse, compressible
short reuse, incompressible
Compressed size can be an indicator of reuse distance
Notes: Simple code example to support intuition.

## Slide 9: Size-Aware Cache Management
Compressed block size matters
Compressed block size varies
Compressed block size can indicate reuse
Notes: In order to answer this question we make three major observations.
#1. Compressed block size matters in cache management decisions
#2. Compressed block size varies (both within and between applications). Which makes the block size a new dimension in cache management.
#3. And probably the most surprising result is that compressed block size can sometimes indicate block’s reuse.

## Slide 10: Outline
Motivation
Key Observations
Key Ideas:
  Minimal-Value Eviction (MVE)
  Size-based Insertion Policy (SIP)
Evaluation
Conclusion

## Slide 11: Compression-Aware Management Policies (CAMP)
CAMP
MVE:
Minimal-Value Eviction
SIP:
Size-based
Insertion Policy
Notes: Our design consists of two new ideas: MVE and SIP that altogether joined into CAMP.

## Slide 12: Minimal-Value Eviction (MVE): Observations
Define a value (importance) of the block to the cache
Evict the block with the lowest value
Block #0
Block #1
Block #N
…
Highest priority: MRU
Lowest priority: LRU
Set:
Block #X
Block #X
…
Importance of the block depends on both the likelihood of reference and the compressed block size
Highest value
Lowest value
Notes: The first idea we propose is called MVE …
In the conventional cache management, from the replacement policy point of view, all blocks within a set are logically ordered based on priority (usually defined based on expected reuse distance in the future).
When we want to put a new line in the $, we usually remove a block with the lowest priority.

## Slide 13: Minimal-Value Eviction (MVE): Key Idea
Value =
Probability of reuse
Compressed block size
Probability of reuse:
Can be determined in many different ways
Our implementation is based on re-reference interval prediction value (RRIP [Jaleel+, ISCA’10])
Notes: We define the value function of the block to the cache based on both … as shown in this formula.
Can be determined in many different ways,
Our implementation is based on RRIP …

## Slide 14: Compression-Aware Management Policies (CAMP)
CAMP
MVE:
Minimal-Value Eviction
SIP:
Size-based
Insertion Policy
Notes: This was MVE and now I will present SIP.

## Slide 15: Size-based Insertion Policy (SIP): Observations
Sometimes there is a relation between the compressed block size and reuse distance
compressed
block size
data structure
This relation can be detected through the compressed block size
Minimal overhead to track this relation (compressed block information is a part of design)
reuse distance

## Slide 16: Size-based Insertion Policy (SIP): Key Idea
Insert blocks of a certain size with higher priority if this improves cache miss rate
Use dynamic set sampling [Qureshi, ISCA’06] to detect which size to insert with higher priority
set A
set B
set C
set D
set E
set G
set H
set F
set I
Main Tags
set A
8B
Auxiliary Tags
set D
64B
set F
8B
set I
64B
set A
set F
+ CTR8B -
…
miss
set F
8B
set A
8B
…
miss
decides policy
for steady state

## Slide 17: Outline
Motivation
Key Observations
Key Ideas:
  Minimal-Value Eviction (MVE)
  Size-based Insertion Policy (SIP)
Evaluation
Conclusion

## Slide 18: Methodology
Simulator
  x86 event-driven simulator (MemSim [Seshadri+, PACT’12])
Workloads
  SPEC2006 benchmarks, TPC, Apache web server
  1 – 4 core simulations for 1 billion representative instructions
System Parameters
  L1/L2/L3 cache latencies from CACTI
  BDI (1-cycle decompression) [Pekhimenko+, PACT’12]
  4GHz, x86 in-order core, cache size (1MB - 16MB)
Notes: In our experiments, we used MemSim event-driven simulator based on Simics as a front-end.

## Slide 19: Evaluated Cache Management Policies
Design | Description
LRU | Baseline LRU policy - size-unaware
RRIP | Re-reference Interval Prediction [Jaleel+, ISCA’10] - size-unaware
Notes: Size-aware

## Slide 20: Evaluated Cache Management Policies
Design | Description
LRU | Baseline LRU policy - size-unaware
RRIP | Re-reference Interval Prediction [Jaleel+, ISCA’10] - size-unaware
ECM | Effective Capacity Maximizer [Baek+, HPCA’13] + size-aware

## Slide 21: Evaluated Cache Management Policies
Design | Description
LRU | Baseline LRU policy - size-unaware
RRIP | Re-reference Interval Prediction [Jaleel+, ISCA’10] - size-unaware
ECM | Effective Capacity Maximizer [Baek+, HPCA’13] + size-aware
CAMP | Compression-Aware Management Policies (MVE + SIP)
Notes: Size-aware

## Slide 22: Size-Aware Replacement
Effective Capacity Maximizer (ECM)
[Baek+, HPCA’13]
  Inserts “big” blocks with lower priority
  Uses heuristic to define the threshold
Shortcomings
  Coarse-grained
  No relation between block size and reuse
  Not easily applicable to other cache organizations

## Slide 23: CAMP Single-Core
Chart: Normalized IPC
| astar | cactusADM | gcc | gobmk | h264ref | soplex | zeusmp | bzip2 | GemsFDTD | gromacs | leslie3d | perlbench | sjeng | sphinx3 | xalancbmk | milc | omnetpp | libquantum | lbm | mcf | tpch2 | tpch6 | apache | GMeanIntense | GMeanAll
RRIP | 1.1359 | 1.1822 | 1.0085 | 1.0102 | 1.0013 | 1.2166 | 0.96715 | 1.0362 | 0.92631 | 1.0075 | 1.0303 | 1.0056 | 1.0038 | 1.1624 | 1.0379 | 1.0003 | 0.95642 | 1.0021 | 1.0008 | 1.0918 | 1.0293 | 0.99622 | 1.0028 | 1.0532 | 1.0329
ECM | 1.1234 | 1.1422 | 1.0065 | 1.0071 | 0.99131 | 1.2538 | 0.9726 | 1.0324 | 0.92879 | 1.009 | 1.0455 | 1.0042 | 1.0063 | 1.1854 | 1.0483 | 1.0014 | 0.98478 | 1.0031 | 0.99943 | 1.097 | 1.0304 | 1.0015 | 1.0147 | 1.059 | 1.0362
MVE | 1.1663 | 1.1822 | 1.0124 | 1.0172 | 1.0026 | 1.2189 | 0.96722 | 1.0443 | 0.92631 | 1.0169 | 1.041 | 1.0085 | 1.0051 | 1.2072 | 1.0709 | 1.0057 | 0.96821 | 1.0022 | 0.98551 | 1.1059 | 1.0327 | 0.99581 | 1.011 | 1.063 | 1.0405
SIP | 1.136 | 1.1821 | 1.0174 | 1.0108 | 1.0013 | 1.3126 | 0.99881 | 1.0394 | 0.99843 | 1.0089 | 1.0504 | 1.0056 | 1.0037 | 1.1815 | 1.0394 | 1.0006 | 0.96152 | 1.0021 | 1.0008 | 1.0955 | 1.0303 | 0.99892 | 1.0061 | 1.072 | 1.0442
CAMP | 1.1633 | 1.1821 | 1.0208 | 1.0179 | 1.0027 | 1.3149 | 0.99882 | 1.0434 | 0.99843 | 1.017 | 1.051 | 1.0086 | 1.0052 | 1.2272 | 1.0736 | 1.0115 | 0.9704 | 1.0025 | 0.99667 | 1.1076 | 1.0342 | 0.99855 | 1.0131 | 1.0816 | 1.0516
SPEC2006, databases, web workloads, 2MB L2 cache
CAMP improves performance over LRU, RRIP, ECM
31%
8%
5%

## Slide 24: Multi-Core Results
Classification based on the compressed block size distribution
  Homogeneous (1 or 2 dominant block size(s))
  Heterogeneous (more than 2 dominant sizes)
We form three different 2-core workload groups (20 workloads in each):
  Homo-Homo
  Homo-Hetero
  Hetero-Hetero

## Slide 25: Multi-Core Results (2)
Chart: Normalized Weighted Speedup
| Homo-Homo | Homo-Hetero | Hetero-Hetero | GeoMean
RRIP | 1.0136 | 1.0324 | 1.0529 | 1.0328
ECM | 1.0172 | 1.0444 | 1.0669 | 1.0426
MVE | 1.0192 | 1.0442 | 1.0739 | 1.0455
SIP | 1.0228 | 1.039 | 1.0749 | 1.0453
CAMP | 1.0314 | 1.0659 | 1.0816 | 1.0594
CAMP outperforms LRU, RRIP and ECM policies
Higher benefits with higher heterogeneity in size

## Slide 26: Effect on Memory Subsystem Energy
Chart: Normalized Energy
| astar | cactusADM | gcc | gobmk | h264ref | soplex | zeusmp | bzip2 | GemsFDTD | gromacs | leslie3d | perlbench | sjeng | sphinx3 | xalancbmk | milc | omnetpp | libquantum | lbm | mcf | tpch2 | tpch6 | apache | GMeanIntense | GMeanAll
RRIP | 0.91445 | 0.77376 | 0.98478 | 0.98594 | 1.0063 | 0.83878 | 1.044 | 0.94293 | 1.113 | 0.9923 | 1.0315 | 0.97103 | 0.9932 | 0.84952 | 0.8629 | 0.99861 | 1.0608 | 0.99879 | 1.0013 | 0.95106 | 0.97716 | 1.0052 | 1.0265 | 0.95011 | 0.96744
ECM | 0.91857 | 0.80075 | 0.97786 | 0.98732 | 0.99691 | 0.81331 | 1.0404 | 0.91982 | 1.1114 | 0.98096 | 1.0161 | 0.95417 | 0.99036 | 0.81866 | 0.83857 | 0.99805 | 1.0281 | 0.99864 | 1.0045 | 0.95812 | 0.97735 | 1.0057 | 1.0166 | 0.94296 | 0.95991
CAMP | 0.89718 | 0.79128 | 0.97016 | 0.97735 | 0.99074 | 0.81071 | 1.0022 | 0.91683 | 1.0021 | 0.96585 | 1.0117 | 0.95638 | 0.98796 | 0.79316 | 0.77993 | 0.99677 | 1.002 | 0.99874 | 1.0036 | 0.93621 | 0.96631 | 0.99778 | 1.0193 | 0.91797 | 0.94341
CAMP reduces energy consumption in the memory subsystem
5%
L1/L2 caches, DRAM, NoC, compression/decompression

## Slide 27: CAMP for Global Replacement
G-CAMP
G-MVE:
Global Minimal-Value Eviction
G-SIP:
Global Size-based
Insertion Policy
CAMP with V-Way [Qureshi+, ISCA’05] cache design
Reuse Replacement instead of RRIP
Set Dueling instead of Set Sampling
Notes: Explain what global replacement means …
Details are in the paper …

## Slide 28: G-CAMP Single-Core
SPEC2006, databases, web workloads, 2MB L2 cache
G-CAMP improves performance over LRU, RRIP, V-Way
Chart: Normalized IPC
| astar | cactusADM | gcc | gobmk | h264ref | soplex | zeusmp | bzip2 | GemsFDTD | gromacs | leslie3d | perlbench | sjeng | sphinx3 | xalancbmk | milc | omnetpp | libquantum | lbm | mcf | tpch2 | tpch6 | apache | GMeanIntense | GMeanAll
RRIP | 1.1359 | 1.1822 | 1.0085 | 1.0102 | 1.0013 | 1.2166 | 0.96715 | 1.0362 | 0.92631 | 1.0075 | 1.0303 | 1.0056 | 1.0038 | 1.1624 | 1.0379 | 1.0003 | 0.95642 | 1.0021 | 1.0008 | 1.0918 | 1.0293 | 0.99622 | 1.0028 | 1.0532 | 1.0329
V-WAY | 1.0886 | 1.2038 | 1.0061 | 1.0097 | 0.97356 | 1.6372 | 1.0152 | 1.0432 | 1.007 | 1.0045 | 1.0257 | 1.004 | 1.002 | 1.0491 | 1.0522 | 1.0015 | 1.0328 | 1.0012 | 1.0041 | 1.1194 | 1.0222 | 1.0122 | 1.0159 | 1.0868 | 1.0514
G-MVE | 1.1737 | 1.2038 | 1.0337 | 1.1072 | 1.0058 | 1.9266 | 1.0152 | 1.0509 | 1.007 | 0.96924 | 1.0371 | 1.0151 | 1.0063 | 1.2517 | 0.87169 | 1.0281 | 0.89181 | 1.0117 | 0.95666 | 1.2421 | 0.86677 | 1.0127 | 0.994 | 1.0861 | 1.0576
G-SIP | 1.1713 | 1.2038 | 1.001 | 1.0017 | 0.98823 | 1.7116 | 1.0152 | 1.0415 | 1.007 | 1.0054 | 1.0221 | 1.0085 | 1.0013 | 1.0917 | 1.0816 | 0.99971 | 1.0365 | 1.0012 | 1.0091 | 1.226 | 1.0348 | 1.0129 | 1.0165 | 1.1116 | 1.0651
G-CAMP | 1.1697 | 1.2038 | 1.0355 | 1.1031 | 1.0058 | 1.9757 | 1.0152 | 1.0504 | 1.007 | 1.0047 | 1.0586 | 1.0103 | 1.0058 | 1.2513 | 1.0556 | 1.015 | 1.0333 | 1.0125 | 1.0161 | 1.2687 | 1.0247 | 1.0131 | 1.0168 | 1.1401 | 1.0888
14%
9%

## Slide 29: Storage Bit Count Overhead
Designs (with BDI) | LRU | CAMP | V-Way | G-CAMP
tag-entry | +14b | +14b | +15b | +19b
data-entry | +0b | +0b | +16b | +32b
total | +9% | +11% | +12.5% | +17%
Over uncompressed cache with LRU
2%
4.5%
Notes: Change color
Show deltas and arrows

## Slide 30: Cache Size Sensitivity
Chart: Normalized IPC
| 1M | 2M | 4M | 8M | 16M
LRU | 1 | 1.0656 | 1.1157 | 1.2521 | 1.3885
RRIP | 1.011 | 1.1007 | 1.1534 | 1.2954 | 1.3995
ECM | 1.0196 | 1.1043 | 1.1621 | 1.3066 | 1.4111
CAMP | 1.0276 | 1.1217 | 1.1704 | 1.3132 | 1.4233
V-WAY | 1.0248 | 1.1204 | 1.2304 | 1.3996 | 1.4487
G-CAMP | 1.0527 | 1.1603 | 1.271 | 1.4423 | 1.4873
CAMP/G-CAMP outperforms prior policies for all $ sizes
G-CAMP outperforms LRU with 2X cache sizes

## Slide 31: Other Results and Analyses in the Paper
Block size distribution for different applications
Sensitivity to the compression algorithm
Comparison with uncompressed cache
Effect on cache capacity
SIP vs. PC-based replacement policies
More details on multi-core results

## Slide 32: Conclusion
In a compressed cache, compressed block size is an additional dimension
Problem: How can we maximize cache performance utilizing both block reuse and compressed size?
Observations:
  Importance of the cache block depends on its compressed size
  Block size is indicative of reuse behavior in some applications
Key Idea: Use compressed block size in making cache replacement and insertion decisions
Two techniques: Minimal-Value Eviction and Size-based Insertion Policy
Results:
  Higher performance (9%/11% on average for 1/2-core)
  Lower energy (12% on average)
Notes: Traditional cache replacement and insertion policies mainly focus on block reuse.
But in a compressed caches, compressed block size is an additional dimension.
In this work, we aim to answer a question on: How can we maximize cache performance utilizing both block reuse and compressed size?
We make two observations:
…
We then apply this observation in two new cache management mechanisms that use compressed block size in making cache replacement and insertion decisions.
Our evaluation shows that these mechanism are effective in improve both the performance (11% increase on average) and energy efficiency (
12% on average) of the modern systems.

## Slide 33: Exploiting Compressed Block Size as an Indicator of Future Reuse
Gennady Pekhimenko,
Tyler Huberty, Rui Cai,
Onur Mutlu, Todd C. Mowry
Phillip B. Gibbons,
Michael A. Kozuch

## Slide 34: Backup Slides

## Slide 35: Potential for Data Compression
Compression algorithms for on-chip caches:
Frequent Pattern Compression (FPC) [Alameldeen+, ISCA’04]
  performance: +15%, comp. ratio: 1.25-1.75
C-Pack [Chen+, Trans. on VLSI’10]
  comp. ratio: 1.64
Base-Delta-Immediate (BDI) [Pekhimenko+, PACT’12]
  performance: +11.2%, comp. ratio: 1.53
Statistical Compression [Arelakis+, ISCA’14]
  performance: +11%, comp. ratio: 2.1

## Slide 36: Potential for Data Compression (2)
Better compressed cache management
  Decoupled Compressed Cache (DCC) [MICRO’13]
  Skewed Compressed Cache [MICRO’14]

## Slide 37: # 3: Block Size Can Indicate Reuse
soplex
Block size, bytes
Different sizes have different dominant reuse distances
Notes: Explain this graph better. Maybe replace with simpler version.

## Slide 38: Conventional Cache Compression
Tag0
Tag1
…
…
…
…
Tag Storage:
Set0
Set1
Way0
Way1
Data0
…
…
Set0
Set1
Way0
Way1
…
Data1
…
32 bytes
Data Storage:
Conventional 2-way cache with 32-byte cache lines
Compressed 4-way cache with 8-byte segmented data
Tag0
Tag1
…
…
…
…
Tag Storage:
Way0
Way1
Way2
Way3
…
…
Tag2
Tag3
…
…
Set0
Set1
Twice as many tags
C - Compr. encoding bits
C
Set0
Set1
…
…
…
…
…
…
…
…
S0
S0
S1
S2
S3
S4
S5
S6
S7
…
…
…
…
…
…
…
…
8 bytes
Tags map to multiple adjacent segments

## Slide 39: CAMP = MVE + SIP
Minimal-Value eviction (MVE)
  Probability of reuse based on RRIP [ISCA’10]
Size-based insertion policy (SIP)
  Dynamically prioritizes blocks based on their compressed size (e.g., insert into MRU position for LRU policy)
Value Function =
Probability of reuse
Compressed block size

## Slide 40: Overhead Analysis

## Slide 41: CAMP and Global Replacement
CAMP with V-Way cache design
Tag0
Tag1
…
…
…
…
…
…
Tag2
Tag3
…
…
Set0
Set1
Data0
…
…
64 bytes
…
Data1
…
status
tag
fptr
R0
R1
rptr
comp
…
…
…
8 bytes
v+s
R2
R3

## Slide 42: G-MVE
Two major changes:
Probability of reuse based on Reuse Replacement policy
  On insertion, a block’s counter is set to zero
  On a hit, the block’s counter is incremented by one indicating its reuse
Global replacement using a pointer (PTR) to a reuse counter entry
  Starting at the entry PTR points to, the reuse counters of 64 valid data entries are scanned, decrementing each non-zero counter

## Slide 43: G-SIP
Use set dueling instead of set sampling (SIP) to decide best insertion policy:
  Divide data-store into 8 regions and block sizes into 8 ranges
  During training, for each region, insert blocks of a different size range with higher priority
  Count cache misses per region
In steady state, insert blocks with sizes of top performing regions with higher priority in all regions

## Slide 44: Size-based Insertion Policy (SIP): Key Idea
Insert blocks of a certain size with higher priority if this improves cache miss rate
Highest priority
Lowest priority
64
32
16
64
16
32
…
Set:
16
32
Notes: Remove animation

## Slide 45: Evaluated Cache Management Policies
Design | Description
LRU | Baseline LRU policy
RRIP | Re-reference Interval Prediction[Jaleel+, ISCA’10]
ECM | Effective Capacity Maximizer[Baek+, HPCA’13]
V-Way | Variable-Way Cache[ISCA’05]
CAMP | Compression-Aware Management (Local)
G-CAMP | Compression-Aware Management (Global)

## Slide 46: Performance and MPKI Correlation
Mechanism | LRU | RRIP | ECM
CAMP | 8.1%/-13.3% | 2.7%/-5.6% | 2.1%/-5.9%
Performance improvement / MPKI reduction
CAMP performance improvement correlates with MPKI reduction

## Slide 47: Performance and MPKI Correlation
Mechanism | LRU | RRIP | ECM | V-Way
CAMP | 8.1%/-13.3% | 2.7%/-5.6% | 2.1%/-5.9% | N/A
G-CAMP | 14.0%/-21.9% | 8.3%/-15.1% | 7.7%/-15.3% | 4.9%/-8.7%
Performance improvement / MPKI reduction
CAMP performance improvement correlates with MPKI reduction

## Slide 48: Multi-core Results (2)
G-CAMP outperforms LRU, RRIP and V-Way policies
Chart: Normalized Weighted Speedup
| Homo-Homo | Homo-Hetero | Hetero-Hetero | GeoMean
RRIP | 1.0136 | 1.0324 | 1.0529 | 1.0328
V-WAY | 1.0228 | 0.9972 | 1.0434 | 1.0209
G-MVE | 1.0312 | 1.0944 | 1.134 | 1.0857
G-SIP | 1.0264 | 1.0669 | 1.0889 | 1.0604
G-CAMP | 1.0638 | 1.1195 | 1.1585 | 1.1133

## Slide 49: Effect on Memory Subsystem Energy
Chart: Normalized Energy
| astar | cactusADM | gcc | gobmk | h264ref | soplex | zeusmp | bzip2 | GemsFDTD | gromacs | leslie3d | perlbench | sjeng | sphinx3 | xalancbmk | milc | omnetpp | libquantum | lbm | mcf | tpch2 | tpch6 | apache | GMeanIntense | GMeanAll
RRIP | 0.91445 | 0.77376 | 0.98478 | 0.98594 | 1.0063 | 0.83878 | 1.044 | 0.94293 | 1.113 | 0.9923 | 1.0315 | 0.97103 | 0.9932 | 0.84952 | 0.8629 | 0.99861 | 1.0608 | 0.99879 | 1.0013 | 0.95106 | 0.97716 | 1.0052 | 1.0265 | 0.95011 | 0.96744
ECM | 0.91857 | 0.80075 | 0.97786 | 0.98732 | 0.99691 | 0.81331 | 1.0404 | 0.91982 | 1.1114 | 0.98096 | 1.0161 | 0.95417 | 0.99036 | 0.81866 | 0.83857 | 0.99805 | 1.0281 | 0.99864 | 1.0045 | 0.95812 | 0.97735 | 1.0057 | 1.0166 | 0.94296 | 0.95991
CAMP | 0.89718 | 0.79128 | 0.97016 | 0.97735 | 0.99074 | 0.81071 | 1.0022 | 0.91683 | 1.0021 | 0.96585 | 1.0117 | 0.95638 | 0.98796 | 0.79316 | 0.77993 | 0.99677 | 1.002 | 0.99874 | 1.0036 | 0.93621 | 0.96631 | 0.99778 | 1.0193 | 0.91797 | 0.94341
V-WAY | 0.95295 | 0.74487 | 0.99538 | 0.98425 | 1.1616 | 0.58808 | 0.98568 | 0.91737 | 0.99146 | 1.0034 | 1.0357 | 0.98151 | 0.99591 | 0.95284 | 0.83683 | 0.99882 | 0.9723 | 0.99989 | 0.99943 | 0.92687 | 0.98161 | 0.98325 | 1.0092 | 0.91104 | 0.94931
G-CAMP | 0.88587 | 0.71913 | 0.93578 | 0.89979 | 0.94982 | 0.50651 | 0.96377 | 0.86489 | 0.9879 | 0.95885 | 1.0116 | 0.84713 | 0.90208 | 0.83151 | 0.71186 | 0.9827 | 0.9141 | 0.95279 | 0.98143 | 0.80969 | 0.94483 | 0.97585 | 0.95572 | 0.84967 | 0.88213
CAMP/G-CAMP reduces energy consumption in the memory subsystem
15.1%
L1/L2 caches, DRAM, NoC, compression/decompression