## Slide 1: Concurrent Data Structures for Near-Memory Computing
Zhiyu Liu (Brown)
Irina Calciu (VMware Research)
Maurice Herlihy (Brown)
Onur Mutlu (ETH)

## Slide 2: Concurrent Data Structures
Are used everywhere: kernel, libraries, applications
Issues:
Difficult to design and implement
Data layout and memory/cache hierarchy
play crucial role in performance
Cache
Memory
Notes: Hot path vs cold path – caches matter

## Slide 3: The Memory Wall
CPU
L1 cache
L2 cache
L3 cache
Memory
< 10 ns
Tens of ns
Hundreds
of ns
2.2 GHz = 220K cycles during this time
Data
movement
Notes: Data movement is expensive
CPUs have been getting faster for a long time, while memory has not
Although CPUs are not getting actually getting faster anymore, memory seems to be getting even slower (e.g. NVM), as vendors
Have been prioritizing bandwidth and scaling over speed.
Minimize data movement move computation to where the data is

## Slide 4: Near Memory Computing
Also called Processing In Memory (PIM)
Avoid data movement by doing computation in memory
Old idea
New advances in 3D integration and die-stacked memory
Viable in the near future
Notes: Becoming feasible
3D stacking technologies

## Slide 5: Near Memory Computing: Architecture
  Vaults: memory partitions
  PIM cores: lightweight
    Fast access to its own vault
  Communication
    Between a CPU and a PIM
    Between PIMs
    Via messages sent to buffers
CPU
Crossbar Network
CPU
PIM core
Vault
PIM memory
PIM core
PIM core
CPU
CPU
Vault
Vault
DRAM
Notes: For example, one viable model

## Slide 6: Data Structures + Hardware
Tight integration between algorithmic design
and hardware characteristics
Memory becomes an active component in managing data
Managing data structures in PIM
  Old work: pointer chasing for sequential data structures
  Our work: concurrent data structures
Notes: This new technology promises to revolutionize the interaction
between computation and data, as it enables memory to become
an active component in managing the data. Therefore, it invites
a fundamental rethinking of basic data structures and promotes
a tighter dependency between algorithmic design and hardware
characteristics.
PIM is sequential; single core per vault; prior work looked at sequential data structures
We are the first to look at concurrent data structures, and compare PIM data structures with state-of-the-art concurrent data structures.

## Slide 7: CONTENTION
LOW
HIGH
Cacheable
Pointer-chasing
Goals: PIM Concurrent Data Structures
1. How do PIM data structures compare to state-of-the-art concurrent data structures?
2. How to design efficient PIM data structures?

## Slide 8: CONTENTION
LOW
HIGH
Cacheable
Pointer-chasing
Goals: PIM Concurrent Data Structures
1. How do PIM data structures compare to state-of-the-art concurrent data structures?
2. How to design efficient PIM data structures?
e.g., uniform distribution skiplist & linkedlist

## Slide 9: Pointer Chasing Data Structures
1
1
1
1
3
4
6
7
8
10
11
14
4
4
7
10
10
10
8
12
14
12
14
7
16
16
16
16
Notes: Explain skiplist
Explain pointer chasing
Explain why PIM is good for pointer chasing

## Slide 10: CONTENTION
LOW
HIGH
Cacheable
Pointer-chasing
Goals: PIM Concurrent Data Structures
1. How do PIM data structures compare to state-of-the-art concurrent data structures?
2. How to design efficient PIM data structures?
e.g., uniform distribution skiplist & linkedlist

## Slide 11: Naïve PIM Skiplist
CPU
CPU
CPU
add(30)
add(5)
delete(80)
PIM Memory Vault
PIM core
1
1
1
1
3
4
6
7
8
10
11
14
4
4
7
10
10
10
8
12
14
12
14
7
16
16
16
16
Low Latency

## Slide 12: Concurrent Data Structures
CPU
CPU
CPU
add(30)
add(5)
delete(80)
1
1
1
1
3
4
6
7
8
10
11
14
4
4
7
10
10
10
8
12
14
12
14
7
16
16
16
16
DRAM
High Latency
Notes: Concurrent (w/ coarse locks, fine-grain locks or lock-free)
Sequential Skiplist CPU – done before
Concurrent skiplist
Lock free skiplist

## Slide 13: Flat Combining
CPU
CPU
CPU
add(30)
add(5)
delete(80)
1
1
1
1
3
4
6
7
8
10
11
14
4
4
7
10
10
10
8
12
14
12
14
7
16
16
16
16
Sequential access
Combiner lock
DRAM
High Latency

## Slide 14: Skiplist Throughput
Chart: 
| 1.0 | 4.0 | 7.0 | 10.0 | 13.0 | 16.0 | 19.0 | 22.0 | 25.0 | 28.0
naiveFC 33/33/33 | 712347 | 684537 | 685470 | 731177 | 718907 | 723619 | 712691 | 702736 | 679801 | 657210
parallel 33/33/33 | 533519 | 1915433 | 3450566 | 4753588 | 6144909 | 6962714 | 7743386 | 8208266 | 9141183 | 9074593
Lock-free
FC
Ops/s
Threads
Intel Xeon E7-4850v3 28 hardware threads, 2.2 GHz

## Slide 15: PIM Performance
N | Size of the skiplist
p | Number of processes
LCPU | Latency of a memory access from the CPU
LLLC | Latency of a LLC access
LATOMIC | Latency of an atomic instruction (by the CPU)
LPIM | Latency of a memory access from the PIM core
LMSG | Latency of a message from the CPU to the PIM core
Notes: Performance Model
  To do so we have to develop a simple model to reason about the performance of these algorithms

## Slide 16: PIM Performance
LCPU = r1 LPIM = r2 LLLC
LMSG = LCPU
r1 = r2 = 3

## Slide 17: PIM Performance
Algorithm | Throughput
Lock-free | p / ( B * LCPU )
Flat Combining (FC) | 1 / ( B * LCPU )
PIM | 1 / ( B * LPIM + LMSG )
B = average number of nodes accessed during a skiplist operation

## Slide 18: Skiplist Throughput
Chart: 
| 1.0 | 4.0 | 7.0 | 10.0 | 13.0 | 16.0 | 19.0 | 22.0 | 25.0 | 28.0
naiveFC 33/33/33 | 712347 | 684537 | 685470 | 731177 | 718907 | 723619 | 712691 | 702736 | 679801 | 657210
parallel 33/33/33 | 533519 | 1915433 | 3450566 | 4753588 | 6144909 | 6962714 | 7743386 | 8208266 | 9141183 | 9074593
expected native PIM | 2137041 | 2053611 | 2056410 | 2193531 | 2156721 | 2170857 | 2138073 | 2108208 | 2039403 | 1971630
Lock-free
Ops/s
Threads
PIM (expected)
FC

## Slide 19: CONTENTION
LOW
HIGH
Cacheable
Pointer-chasing
Goals: PIM Concurrent Data Structures
1. How do PIM data structures compare to state-of-the-art concurrent data structures?
2. How to design efficient PIM data structures?
e.g., uniform distribution skiplist & linkedlist

## Slide 20: New PIM algorithm: Exploit Partitioning
CPU
Crossbar Network
CPU
PIM core
Vault
PIM memory
PIM core
PIM core
CPU
CPU
Vault
Vault
DRAM
Notes: We need parallelism, exploit the structure of the hardware

## Slide 21: PIM Skiplist w/ Partitioning
1
1
1
1
3
4
6
7
8
10
11
20
26
4
4
7
10
10
10
8
12
20
20
12
20
7
CPU
CPU
CPU
1
10
20
CPU cache
Vault 1
Vault 2
Vault 3
PIM core
PIM core
PIM core
PIM Memory

## Slide 22: PIM Performance
Algorithm | Throughput
Lock-free | p / ( B * LCPU )
Flat Combining (FC) | 1 / ( B * LCPU )
PIM | 1 / ( B * LPIM + LMSG )
FC + k partitions | k / ( B * LCPU )
PIM + k partitions | k / ( B * LPIM + LMSG )
B = average number of nodes accessed during a skiplist operation

## Slide 23: Skiplist Throughput
Chart: 
| 1.0 | 4.0 | 7.0 | 10.0 | 13.0 | 16.0 | 19.0 | 22.0 | 25.0 | 28.0
naiveFC 33/33/33 | 712347 | 684537 | 685470 | 731177 | 718907 | 723619 | 712691 | 702736 | 679801 | 657210
parallel 33/33/33 | 533519 | 1915433 | 3450566 | 4753588 | 6144909 | 6962714 | 7743386 | 8208266 | 9141183 | 9074593
FC w/ 4 partitions 33/33/33 | 713106 | 1486058 | 1830860 | 2109016 | 2218555 | 2247405 | 2238411 | 2232732 | 2233450 | 2225234
FC w/ 8 partitions 33/33/33 | 718690 | 1832279 | 2504398 | 2975474 | 3260773 | 3394861 | 3478395 | 3559995 | 3604142 | 3654547
FC w/ 16 partitions 33/33/33 | 729705 | 2095177 | 3050554 | 3798302 | 4287650 | 4553113 | 4755603 | 4956537 | 5118947 | 5252542
Lock-free
FC
Ops/s
Threads
FC w/ 16 partitions
FC w/ 8 partitions
FC w/ 4 partitions

## Slide 24: Skiplist Throughput
Chart: 
| 1.0 | 4.0 | 7.0 | 10.0 | 13.0 | 16.0 | 19.0 | 22.0 | 25.0 | 28.0
naiveFC 33/33/33 | 712347 | 684537 | 685470 | 731177 | 718907 | 723619 | 712691 | 702736 | 679801 | 657210
parallel 33/33/33 | 533519 | 1915433 | 3450566 | 4753588 | 6144909 | 6962714 | 7743386 | 8208266 | 9141183 | 9074593
FC w/ 4 partitions 33/33/33 | 713106 | 1486058 | 1830860 | 2109016 | 2218555 | 2247405 | 2238411 | 2232732 | 2233450 | 2225234
FC w/ 8 partitions 33/33/33 | 718690 | 1832279 | 2504398 | 2975474 | 3260773 | 3394861 | 3478395 | 3559995 | 3604142 | 3654547
FC w/ 16 partitions 33/33/33 | 729705 | 2095177 | 3050554 | 3798302 | 4287650 | 4553113 | 4755603 | 4956537 | 5118947 | 5252542
expected PIM w/ 8 partitions 33/33/33 | 2156069 | 5496838 | 7513195 | 8926421 | 9782319 | 10184583 | 10435186 | 10679985 | 10812427 | 10963640
expected PIM w/ 16 partitions 33/33/33 | 2189114 | 6285530 | 9151663 | 11394907 | 12862951 | 13659338 | 14266808 | 14869612 | 15356840 | 15757626
Lock-free
FC
Ops/s
Threads
FC w/ 16 partitions
FC w/ 8 partitions
FC w/ 4 partitions
PIM w/ 8 partitions (expected)
PIM w/ 16 partitions (expected)

## Slide 25: CONTENTION
LOW
HIGH
Cacheable
Pointer-chasing
Goals: PIM Concurrent Data Structures
1. How do PIM data structures compare to state-of-the-art concurrent data structures?
2. How to design efficient PIM data structures?
e.g., FIFO queue

## Slide 26: FIFO Queue
HEAD
TAIL
enqueue
dequeue
Notes: Explain high contention + why they don’t seem to be a good fit for PIM – cache locality BUT contention hurts concurrent data structures

## Slide 27: PIM FIFO Queue
Tail
CPU
CPU
PIM core
Deq()
Deq()
1
dequeues a node
2
retrieves request
3
sends back
the node
1
retrieves request
PIM Memory Vault

## Slide 28: Pipelining
1
2
Timeline
3
Deq()
Deq()
Deq()
1
2
3
1
2
3
Can overlap the execution of the next request

## Slide 29: Parallelize Enqs and Deqs
Head
Tail
CPU
CPU
CPU
Vault 2
PIM core
Vault 1
PIM core
enqs
deqs

## Slide 30: Conclusion
PIM is becoming feasible in the near future
We investigate Concurrent Data Structures (CDS) for PIM
Results:
Naïve PIM data structures are less efficient than CDS
New PIM algorithms can leverage PIM features
  They outperform efficient CDS
  They are simpler to design and implement
Notes: The memory wall prompts moving computation to data
PIM is becoming feasible in the near future which makes
Memory an active component in managing data
This results in a tight integration between algorithmic design and hardware characteristics
We investigate Concurrent Data Structures for PIM
In particular we look at concurrent data structures
Naïve PIM data structures are less efficient than
efficient concurrent data structures
Despite the lower latency accesses from the PIM core

## Slide 31
Thank you!
https://research.vmware.com/
icalciu@vmware.com

## Slide 32: Concurrent Data Structures for Near-Memory Computing
Zhiyu Liu (Brown)
Irina Calciu (VMware Research)
Maurice Herlihy (Brown)
Onur Mutlu (ETH)

## Slide 33
Notes: The memory wall: Speed gap between memory and CPU, the “memory wall”
Moving computation closer to memory to solve this problem
  (This is an idea that has been extensively studied for a long time, but it is recently becoming a possibility using 3D stacking)
Near Memory Computing: Architecture
Revolutionize interaction between computation and data; Rethink basic data structures and tight integration between algorithmic design and hardware characteristics
PIM is sequential; single core per vault; prior work looked at sequential data structures
In this work: concurrent data structures
  What are concurrent data structures
  Concurrent data structures are used everywhere but difficult to design
  Concurrent data structures are hard
  We show that optimized concurrent data structures are better than PIM sequential
  So we need parallelism, we develop new algorithms to leverage the characteristics of the hardware
Performance Model
  To do so we have to develop a simple model to reason about the performance of these algorithms