## Slide 1
Continuous Runahead: Transparent Hardware Acceleration for Memory Intensive Workloads
Milad Hashemi, Onur Mutlu, and Yale N. Patt
1) Runahead requests are overwhelmingly accurate:
2) Runahead has very low prefetch coverage:
3) Runahead intervals are short, dramatically limiting runahead performance gain:
Our Proposal: Continuous Runahead
Goal: Run ahead for longer intervals.
Dynamically identify the chains of operations that cause the most critical cache misses.
These dependence chains are then renamed to execute in a loop and migrated to a specialized compute engine in the memory controller where they can run ahead continuously.
This Continuous Runahead Engine (CRE) leads to a 21.9% single-core performance gain over prior state-of-the-art techniques on the memory intensive SPEC CPU2006 benchmarks. In a quad-core system, the CRE leads to a 13.2% gain over the highest performing prefetcher (GHB) in our evaluation. When the CRE is combined with a GHB prefetcher, the result is a 23.5% gain over a baseline with GHB prefetching alone.
Runahead execution effectively expands the reorder buffer of an out-of-order processor to generate MLP during a full-window stall. We make 3 observations about traditional runahead:
Continuous Runahead Performance Results:
Chart: Request Accuracy
| zeusmp | cactus | wrf | GemsFDTD | leslie | omnetpp | milc | soplex | sphinx | bwaves | libquantum | lbm | mcf | Mean
Runahead | 0.97 | 0.98 | 0.97 | 0.99 | 0.98 | 0.93 | 0.95 | 0.93 | 0.91 | 0.98 | 0.94 | 0.78 | 0.98 | 0.95
GHB | 0.75 | 0.99 | 0.97 | 0.95 | 0.99 | 0.37 | 0.38 | 0.82 | 0.7 | 0.99 | 0.99 | 0.99 | 0.71 | 0.82
Stream | 0.71 | 0.91 | 0.97 | 0.94 | 0.99 | 0.13 | 0.33 | 0.76 | 0.62 | 0.99 | 0.99 | 0.93 | 0.62 | 0.76
Markov + Stream | 0.85 | 0.4 | 0.94 | 0.93 | 0.85 | 0.2 | 0.23 | 0.79 | 0.63 | 0.99 | 0.99 | 0.8 | 0.3 | 0.69
Chart: % Independent Cache Misses
| zeusmp | cactus | wrf | GemsFDTD | leslie | omnetpp | milc | soplex | sphinx | bwaves | libquantum | lbm | mcf | Mean
% Independent Misses | 0.09 | 0.1 | 0.09 | 0.08 | 0.09 | 0.09 | 0.19 | 0.07 | 0.18 | 0.18 | 0.28 | 0.1 | 0.1 | 0.13
Chart: Cycles Per Runahead Interval
| zeusmp | cactus | wrf | GemsFDTD | leslie | omnetpp | milc | soplex | sphinx | bwaves | libquantum | lbm | mcf | Mean
128 ROB | 36.86 | 111.26 | 48.2 | 25.31 | 46.31 | 96.83 | 34.02 | 71.25 | 82.15 | 29.42 | 112.6 | 70.57 | 116.64 | 67.8
256 ROB | 32.12 | 91.06 | 47.56 | 18.63 | 41.54 | 91.71 | 32.83 | 66.13 | 78.38 | 21.54 | 60.06 | 70.64 | 101.93 | 57.93
512 ROB | 28.23 | 80.45 | 45.99 | 17.56 | 40.35 | 87.97 | 30.8 | 51.75 | 66.02 | 18.78 | 32.94 | 67.59 | 100.73 | 51.55
1024 ROB | 26.9 | 69.68 | 37.55 | 15.51 | 30.41 | 83.27 | 30.57 | 53.95 | 64.72 | 11.01 | 30.01 | 62.48 | 88.67 | 46.52
Chart: % Independent Cache Misses Prefetched
| zeusmp | cactus | wrf | GemsFDTD | leslie | omnetpp | milc | soplex | sphinx | bwaves | libquantum | lbm | mcf | Mean
 | 0.89 | 0.45 | 0.66 | 0.69 | 0.85 | 0.54 | 0.96 | 0.57 | 0.82 | 0.93 | 0.92 | 0.92 | 0.38 | 0.71
Chart: Normalized Bandwidth
| zeusmp | cactus | wrf | GemsFDTD | leslie | omnetpp | milc | soplex | sphinx | bwaves | libquantum | lbm | mcf | Mean
Continuous Runahead | 1.0208 | 1.0124 | 1.0025 | 1.001 | 1.0002 | 1.1463 | 1.33 | 1.0578 | 1.27 | 1 | 1 | 1.0063 | 1.0647 | 1.0702
Stream PF | 1.0839 | 1.0004 | 1.0411 | 1.0681 | 1.0129 | 1.9121 | 2.0246 | 1.2063 | 1.4334 | 1.0011 | 1.0001 | 1.0526 | 1.0488 | 1.2219
GHB PF | 1.0406 | 1.0142 | 1.0381 | 1.0553 | 1.0092 | 1.5034 | 1.2708 | 1.2745 | 1.3202 | 1.0003 | 1.0001 | 1.0055 | 1.0036 | 1.1181
Chart: % IPC Improvement over No-Prefetching Baseline
| zeusmp | cactus | wrf | GemsFDTD | leslie | omnetpp | milc | soplex | sphinx | bwaves | libquantum | lbm | mcf | GMean
Runahead Buffer | 16.16 | 12.1 | 15.71 | 16.44 | 14.07 | 22.36 | 16.79 | 14.41 | 6 | 71.26 | 86.5 | 44.21 | 13.93 | 20.1
Continuous Runahead | 24.97 | 18.21 | 21.19 | 26.34 | 28.35 | 32.27 | 25.12 | 28.25 | 27.42 | 90.11 | 112.69 | 68.9 | 29.51 | 34.3666
Stream PF | 7.45 | 0.07 | 55.47 | 76.87 | 56.72 | 0.32 | 5.03 | 58.51 | 63.19 | 97.22 | 87.35 | 18.41 | 8.04 | 14.1874
GHB PF | 2.73 | 74.6 | 49.2 | 63.54 | 67.37 | 1.38 | 3.69 | 58.19 | 57.95 | 93.94 | 98.29 | 74.22 | 0.72 | 22.4285
Chart: Update Interval (Instructions Retired)
| 1k | 5k | 10k | 25k | 50k | 100k | 250k | 500k | 1M | 2M
Continuous Runahead Request Accuracy | 0.78 | 0.84 | 0.87 | 0.88 | 0.87 | 0.86 | 0.83 | 0.76 | 0.7 | 0.65
GMean Performance Gain | 0.3 | 0.365 | 0.368 | 0.365 | 0.355 | 0.354 | 0.351 | 0.29 | 0.28 | 0.25