## Slide 1: Continuous Runahead: Transparent Hardware Acceleration for Memory Intensive Workloads
Milad Hashemi, Onur Mutlu, Yale N. Patt
UT Austin/Google, ETH Zürich, UT Austin
October 19th, 2016

## Slide 2: Continuous Runahead Outline
Overview of Runahead
Runahead Limitations
Continuous Runahead Dependence Chains
Continuous Runahead Engine
Continuous Runahead Evaluation
Conclusions
2

## Slide 3: Continuous Runahead Outline
Overview of Runahead
Runahead Limitations
Continuous Runahead Dependence Chains
Continuous Runahead Engine
Continuous Runahead Evaluation
Conclusions
3

## Slide 4: Runahead Execution Overview
Runahead dynamically expands the instruction window when the pipeline is stalled [Mutlu et al., 2003]
  The core checkpoints architectural state
  The result of the memory operation that caused the stall is marked as poisoned in the physical register file
  The core continues to fetch and execute instructions
  Operations are discarded instead of retired
  The goal is to generate new independent cache misses
4

## Slide 5: Traditional Runahead Accuracy
Chart: Request Accuracy
| zeusmp | cactus | wrf | GemsFDTD | leslie | omnetpp | milc | soplex | sphinx | bwaves | libquantum | lbm | mcf | Mean
Runahead | 0.97 | 0.98 | 0.97 | 0.99 | 0.98 | 0.93 | 0.95 | 0.93 | 0.91 | 0.98 | 0.94 | 0.78 | 0.98 | 0.95
GHB | 0.75 | 0.99 | 0.97 | 0.95 | 0.99 | 0.37 | 0.38 | 0.82 | 0.7 | 0.99 | 0.99 | 0.99 | 0.71 | 0.82
Stream | 0.71 | 0.91 | 0.97 | 0.94 | 0.99 | 0.13 | 0.33 | 0.76 | 0.62 | 0.99 | 0.99 | 0.93 | 0.62 | 0.76
Markov + Stream | 0.85 | 0.4 | 0.94 | 0.93 | 0.85 | 0.2 | 0.23 | 0.79 | 0.63 | 0.99 | 0.99 | 0.8 | 0.3 | 0.69
5

## Slide 6: Traditional Runahead Accuracy
Chart: Request Accuracy
| zeusmp | cactus | wrf | GemsFDTD | leslie | omnetpp | milc | soplex | sphinx | bwaves | libquantum | lbm | mcf | Mean
Runahead | 0.97 | 0.98 | 0.97 | 0.99 | 0.98 | 0.93 | 0.95 | 0.93 | 0.91 | 0.98 | 0.94 | 0.78 | 0.98 | 0.95
GHB | 0.75 | 0.99 | 0.97 | 0.95 | 0.99 | 0.37 | 0.38 | 0.82 | 0.7 | 0.99 | 0.99 | 0.99 | 0.71 | 0.82
Stream | 0.71 | 0.91 | 0.97 | 0.94 | 0.99 | 0.13 | 0.33 | 0.76 | 0.62 | 0.99 | 0.99 | 0.93 | 0.62 | 0.76
Markov + Stream | 0.85 | 0.4 | 0.94 | 0.93 | 0.85 | 0.2 | 0.23 | 0.79 | 0.63 | 0.99 | 0.99 | 0.8 | 0.3 | 0.69
6
Runahead is 95% Accurate

## Slide 7: Traditional Runahead Prefetch Coverage
Chart: % Independent Cache Misses
| zeusmp | cactus | wrf | GemsFDTD | leslie | omnetpp | milc | soplex | sphinx | bwaves | libquantum | lbm | mcf | Mean
% Independent Misses | 0.09 | 0.1 | 0.09 | 0.08 | 0.09 | 0.09 | 0.19 | 0.07 | 0.18 | 0.18 | 0.28 | 0.1 | 0.1 | 0.13
7

## Slide 8: Traditional Runahead Prefetch Coverage
Chart: % Independent Cache Misses
| zeusmp | cactus | wrf | GemsFDTD | leslie | omnetpp | milc | soplex | sphinx | bwaves | libquantum | lbm | mcf | Mean
% Independent Misses | 0.09 | 0.1 | 0.09 | 0.08 | 0.09 | 0.09 | 0.19 | 0.07 | 0.18 | 0.18 | 0.28 | 0.1 | 0.1 | 0.13
8
Runahead has only 13% Prefetch Coverage

## Slide 9: Traditional Runahead Performance Gain
Chart: % IPC Improvement over No-Prefetching Baseline
| zeusmp | cactus | wrf | GemsFDTD | leslie | omnetpp | milc | soplex | sphinx | bwaves | libquantum | lbm | mcf | Mean
Runahead Performance Gain | 0.1 | 0.13 | 0.09 | 0.07 | 0.08 | 0.11 | 0.15 | 0.11 | 0.14 | 0.18 | 0.28 | 0.03 | 0.1 | 0.12
Oracle Performance Gain | 0.34 | 0.44 | 0.3 | 0.46 | 0.48 | 0.39 | 0.96 | 0.49 | 0.67 | 1.01 | 3.1 | 1.1 | 1.25 | 0.85
9

## Slide 10: Traditional Runahead Performance Gain
Chart: % IPC Improvement over No-Prefetching Baseline
| zeusmp | cactus | wrf | GemsFDTD | leslie | omnetpp | milc | soplex | sphinx | bwaves | libquantum | lbm | mcf | Mean
Runahead Performance Gain | 0.1 | 0.13 | 0.09 | 0.07 | 0.08 | 0.11 | 0.15 | 0.11 | 0.14 | 0.18 | 0.28 | 0.03 | 0.1 | 0.12
Oracle Performance Gain | 0.34 | 0.44 | 0.3 | 0.46 | 0.48 | 0.39 | 0.96 | 0.49 | 0.67 | 1.01 | 3.1 | 1.1 | 1.25 | 0.85
10
Runahead has a 12% Performance Gain
Runahead Oracle has an 85% Performance Gain

## Slide 11: Traditional Runahead Interval Length
Chart: Cycles Per Runahead Interval
| zeusmp | cactus | wrf | GemsFDTD | leslie | omnetpp | milc | soplex | sphinx | bwaves | libquantum | lbm | mcf | Mean
128 ROB | 36.86 | 111.26 | 48.2 | 25.31 | 46.31 | 96.83 | 34.02 | 71.25 | 82.15 | 29.42 | 112.6 | 70.57 | 116.64 | 67.8
256 ROB | 32.12 | 91.06 | 47.56 | 18.63 | 41.54 | 91.71 | 32.83 | 66.13 | 78.38 | 21.54 | 60.06 | 70.64 | 101.93 | 57.93
512 ROB | 28.23 | 80.45 | 45.99 | 17.56 | 40.35 | 87.97 | 30.8 | 51.75 | 66.02 | 18.78 | 32.94 | 67.59 | 100.73 | 51.55
1024 ROB | 26.9 | 69.68 | 37.55 | 15.51 | 30.41 | 83.27 | 30.57 | 53.95 | 64.72 | 11.01 | 30.01 | 62.48 | 88.67 | 46.52
11

## Slide 12: Traditional Runahead Interval Length
Chart: Cycles Per Runahead Interval
| zeusmp | cactus | wrf | GemsFDTD | leslie | omnetpp | milc | soplex | sphinx | bwaves | libquantum | lbm | mcf | Mean
128 ROB | 36.86 | 111.26 | 48.2 | 25.31 | 46.31 | 96.83 | 34.02 | 71.25 | 82.15 | 29.42 | 112.6 | 70.57 | 116.64 | 67.8
256 ROB | 32.12 | 91.06 | 47.56 | 18.63 | 41.54 | 91.71 | 32.83 | 66.13 | 78.38 | 21.54 | 60.06 | 70.64 | 101.93 | 57.93
512 ROB | 28.23 | 80.45 | 45.99 | 17.56 | 40.35 | 87.97 | 30.8 | 51.75 | 66.02 | 18.78 | 32.94 | 67.59 | 100.73 | 51.55
1024 ROB | 26.9 | 69.68 | 37.55 | 15.51 | 30.41 | 83.27 | 30.57 | 53.95 | 64.72 | 11.01 | 30.01 | 62.48 | 88.67 | 46.52
12
Runahead Intervals are Short Low Performance Gain

## Slide 13
Which instructions to use during Continuous Runahead?
  Dynamically target the dependence chains that lead to critical cache misses
What hardware to use for Continuous Runahead?
  How long should chains pre-execute for?
Continuous Runahead Challenges
13

## Slide 14: Dependence Chains
LD [R6] -> R8
ADD R9, R1 -> R6
ADD R4, R5 -> R9
LD [R3] -> R5
Cache Miss
14

## Slide 15
Experiment with 3 policies to determine the best policy to use for Continuous Runahead:
PC-Based Policy
  Use the dependence chain that has caused the most misses for the PC that is blocking retirement
Maximum Misses Policy
  Use a dependence chain from the PC that has generated the most misses for the application
Stall Policy
  Use a dependence chain from the PC that has caused the most full-window stalls for the application
Dependence Chain Selection Policies
15

## Slide 16
Chart: % IPC Improvement
| zeusmp | cactus | wrf | GemsFDTD | leslie | omnetpp | milc | soplex | sphinx | bwaves | libquantum | lbm | mcf | Mean
Runahead Buffer | 11.5 | 12.1 | 12.29 | 13.8 | 8.46 | 0.6 | 13.17 | 13.44 | 9.26 | 16.28 | 29.35 | 12.82 | 12.19 | 12.56
PC-Policy | 12.5 | 14.4 | 13 | 6.59 | -8.52 | -3.45 | 28.29 | 16.31 | -10.02 | 69.54 | 89.95 | 38.84 | 10.11 | 18.46
Maximum-Misses Policy | 15 | 16 | 14.5 | 16.93 | 14.97 | 23.23 | 16.79 | 16.57 | -7.25 | 74 | 89.64 | 55.47 | 8.3 | 24.77
Stall Policy | 18 | 17 | 16.5 | 19.23 | 15.87 | 24.23 | 22.22 | 17.31 | 15.31 | 72.27 | 89.6 | 49 | 15.3 | 28.33
Dependence Chain Selection Policies
16

## Slide 17
Chart: Number of PCs
| zeusmp | cactus | wrf | GemsFDTD | leslie | omnetpp | milc | soplex | sphinx | bwaves | libquantum | lbm | mcf | Mean
90% of Stalls | 95 | 23 | 43 | 19 | 21 | 81 | 10 | 11 | 14 | 8 | 2 | 4 | 8 | 26
All Stalls | 380 | 118 | 110 | 64 | 69 | 313 | 30 | 162 | 176 | 21 | 6 | 32 | 68 | 119
All Misses | 727 | 580 | 294 | 252 | 215 | 950 | 113 | 559 | 823 | 60 | 46 | 144 | 282 | 388
Why does Stall Policy Work?
17

## Slide 18
Chart: Number of PCs
| zeusmp | cactus | wrf | GemsFDTD | leslie | omnetpp | milc | soplex | sphinx | bwaves | libquantum | lbm | mcf | Mean
90% of Stalls | 95 | 23 | 43 | 19 | 21 | 81 | 10 | 11 | 14 | 8 | 2 | 4 | 8 | 26
All Stalls | 380 | 118 | 110 | 64 | 69 | 313 | 30 | 162 | 176 | 21 | 6 | 32 | 68 | 119
All Misses | 727 | 580 | 294 | 252 | 215 | 950 | 113 | 559 | 823 | 60 | 46 | 144 | 282 | 388
Why does Stall Policy Work?
18
19 PCs cover 90% of all Stalls

## Slide 19
Chart: Normalized Performance
| zeusmp | cactus | wrf | GemsFDTD | leslie | omnetpp | milc | soplex | sphinx | bwaves | libquantum | lbm | mcf | Mean
1 Chain | 0.9258 | 1 | 0.9085 | 1.0082 | 1 | 0.89 | 0.9988 | 0.917 | 1.0323 | 0.888 | 0.967 | 1.0013 | 0.8671 | 0.95415
2 Chains | 1 | 1 | 0.909 | 1.0119 | 1 | 0.8972 | 0.999 | 0.945 | 1.017 | 0.89 | 0.967 | 1 | 0.8758 | 0.96245
4 Chains | 1 | 1 | 1 | 1.0273 | 1 | 0.916 | 1 | 1 | 1.0173 | 0.892 | 1 | 1 | 0.8921 | 0.98036
8 Chains | 1 | 1 | 1 | 1 | 1 | 0.9399 | 1 | 1 | 0.999 | 1 | 1 | 1 | 1 | 0.9953
16 Chains | 1 | 1 | 1 | 1 | 1 | 0.98 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.99846
32 Chains | 1 | 1 | 1 | 1 | 1 | 0.982 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.99862
Constrained Dependence Chain Storage
19

## Slide 20
Chart: Normalized Performance
| zeusmp | cactus | wrf | GemsFDTD | leslie | omnetpp | milc | soplex | sphinx | bwaves | libquantum | lbm | mcf | Mean
1 Chain | 0.9258 | 1 | 0.9085 | 1.0082 | 1 | 0.89 | 0.9988 | 0.917 | 1.0323 | 0.888 | 0.967 | 1.0013 | 0.8671 | 0.95415
2 Chains | 1 | 1 | 0.909 | 1.0119 | 1 | 0.8972 | 0.999 | 0.945 | 1.017 | 0.89 | 0.967 | 1 | 0.8758 | 0.96245
4 Chains | 1 | 1 | 1 | 1.0273 | 1 | 0.916 | 1 | 1 | 1.0173 | 0.892 | 1 | 1 | 0.8921 | 0.98036
8 Chains | 1 | 1 | 1 | 1 | 1 | 0.9399 | 1 | 1 | 0.999 | 1 | 1 | 1 | 1 | 0.9953
16 Chains | 1 | 1 | 1 | 1 | 1 | 0.98 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.99846
32 Chains | 1 | 1 | 1 | 1 | 1 | 0.982 | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 0.99862
Constrained Dependence Chain Storage
20
Storing 1 Chain provides 95%
of the Performance

## Slide 21
Maintain two structures:
  32-entry cache of PCs to track the operations that cause the pipeline to frequently stall
  The last dependence chain for the PC that has caused the most full-window stalls
At every full window stall:
  Increment the counter of the PC that caused the stall
  Generate a dependence chain for the PC that has caused the most stalls
Continuous Runahead Chain Generation
21

## Slide 22: Runahead for Longer Intervals
22

## Slide 23
No Front-End
No Register Renaming Hardware
32 Physical Registers
2-Wide
No Floating Point or Vector Pipeline
4kB Data Cache
CRE Microarchitecture
23

## Slide 24
SHIFT P1 -> P9
ADD P7 + 1 -> P1
ADD P9 + P1 -> P3
SHIFT P3 -> P2
LD [P2] -> P8
Cycle:
0
1
2
3
4
5
Register Remapping Table:
ADD E5 + 1 -> E3
SHIFT E3 -> E4
ADD E4 + E3 -> E2
SHIFT E2 -> E1
LD [E1] -> E0
Core Physical
Register
CRE Physical
Register
Search List:
P2
First CRE Physical
Register
EAX
EBX
ECX
P8
E0
E0
P2
E1
E1
P3
E2
P3
P1
E3
E3
P9
E4
P9, P1
P1
P7
P7
E5
MAP E3 -> E5
Dependence Chain Generation
24

## Slide 25
Dependence Chain Generation
25

## Slide 26
Chart: Update Interval (Instructions Retired)
| 1k | 5k | 10k | 25k | 50k | 100k | 250k | 500k | 1M | 2M
Continuous Runahead Request Accuracy | 0.78 | 0.84 | 0.87 | 0.88 | 0.87 | 0.86 | 0.83 | 0.76 | 0.7 | 0.65
GMean Performance Gain | 0.3 | 0.365 | 0.368 | 0.365 | 0.355 | 0.354 | 0.351 | 0.29 | 0.28 | 0.25
Interval Length
26

## Slide 27
Single-Core/Quad-Core
  4-wide Issue
  256 Entry Reorder Buffer
  92 Entry Reservation Station
Caches
  32 KB 8-Way Set Associative L1 I/D-Cache
  1MB 8-Way Set Associative Shared Last Level Cache per Core
Non-Uniform Memory Access Latency DDR3 System
  256-Entry Memory Queue
  Batch Scheduling
Prefetchers
  Stream, Global History Buffer
  Feedback Directed Prefetching: Dynamic Degree 1-32
CRE Compute
  2-wide issue
  1 Continuous Runahead issue context with a 32-entry buffer and 32-entry physical register file
  4 kB Data Cache
System Configuration
27

## Slide 28
Chart: % IPC Improvement over No-Prefetching Baseline
| zeusmp | cactus | wrf | GemsFDTD | leslie | omnetpp | milc | soplex | sphinx | bwaves | libquantum | lbm | mcf | GMean
Runahead Buffer | 16.16 | 12.1 | 15.71 | 16.44 | 14.07 | 22.36 | 16.79 | 14.41 | 6 | 71.26 | 86.5 | 44.21 | 13.93 | 20.1
Continuous Runahead | 24.97 | 18.21 | 21.19 | 26.34 | 28.35 | 32.27 | 25.12 | 28.25 | 27.42 | 90.11 | 112.69 | 68.9 | 29.51 | 34.3666
Single-Core Performance
28

## Slide 29
Chart: % IPC Improvement over No-Prefetching Baseline
| zeusmp | cactus | wrf | GemsFDTD | leslie | omnetpp | milc | soplex | sphinx | bwaves | libquantum | lbm | mcf | GMean
Runahead Buffer | 16.16 | 12.1 | 15.71 | 16.44 | 14.07 | 22.36 | 16.79 | 14.41 | 6 | 71.26 | 86.5 | 44.21 | 13.93 | 20.1
Continuous Runahead | 24.97 | 18.21 | 21.19 | 26.34 | 28.35 | 32.27 | 25.12 | 28.25 | 27.42 | 90.11 | 112.69 | 68.9 | 29.51 | 34.3666
Single-Core Performance
29
21% Single Core Performance Increase over prior State of the Art

## Slide 30
Chart: % IPC Improvement over No-Prefetching Baseline
| zeusmp | cactus | wrf | GemsFDTD | leslie | omnetpp | milc | soplex | sphinx | bwaves | libquantum | lbm | mcf | GMean
Runahead Buffer | 16.16 | 12.1 | 15.71 | 16.44 | 14.07 | 22.36 | 16.79 | 14.41 | 6 | 71.26 | 86.5 | 44.21 | 13.93 | 20.1
Continuous Runahead | 24.97 | 18.21 | 21.19 | 26.34 | 28.35 | 32.27 | 25.12 | 28.25 | 27.42 | 90.11 | 112.69 | 68.9 | 29.51 | 34.3666
Stream PF | 7.45 | 0.07 | 55.47 | 76.87 | 56.72 | 0.32 | 5.03 | 58.51 | 63.19 | 97.22 | 87.35 | 18.41 | 8.04 | 14.1874
GHB PF | 2.73 | 74.6 | 49.2 | 63.54 | 67.37 | 1.38 | 3.69 | 58.19 | 57.95 | 93.94 | 98.29 | 74.22 | 0.72 | 22.4285
Continuous Runahead + Stream | 27.52 | 15.42 | 60.32 | 83.89 | 57.89 | 16.46 | 17.2 | 63.21 | 67.21 | 116.04 | 121.47 | 89.06 | 37.81 | 47.9527
Continuous Runahead + GHB | 26.66 | 79.21 | 56.77 | 73.96 | 74.45 | 29.21 | 25.71 | 65.31 | 67.21 | 122.53 | 124.12 | 91.03 | 33.38 | 58.8054
Single-Core Performance + Prefetching
30

## Slide 31
Chart: % IPC Improvement over No-Prefetching Baseline
| zeusmp | cactus | wrf | GemsFDTD | leslie | omnetpp | milc | soplex | sphinx | bwaves | libquantum | lbm | mcf | GMean
Runahead Buffer | 16.16 | 12.1 | 15.71 | 16.44 | 14.07 | 22.36 | 16.79 | 14.41 | 6 | 71.26 | 86.5 | 44.21 | 13.93 | 20.1
Continuous Runahead | 24.97 | 18.21 | 21.19 | 26.34 | 28.35 | 32.27 | 25.12 | 28.25 | 27.42 | 90.11 | 112.69 | 68.9 | 29.51 | 34.3666
Stream PF | 7.45 | 0.07 | 55.47 | 76.87 | 56.72 | 0.32 | 5.03 | 58.51 | 63.19 | 97.22 | 87.35 | 18.41 | 8.04 | 14.1874
GHB PF | 2.73 | 74.6 | 49.2 | 63.54 | 67.37 | 1.38 | 3.69 | 58.19 | 57.95 | 93.94 | 98.29 | 74.22 | 0.72 | 22.4285
Continuous Runahead + Stream | 27.52 | 15.42 | 60.32 | 83.89 | 57.89 | 16.46 | 17.2 | 63.21 | 67.21 | 116.04 | 121.47 | 89.06 | 37.81 | 47.9527
Continuous Runahead + GHB | 26.66 | 79.21 | 56.77 | 73.96 | 74.45 | 29.21 | 25.71 | 65.31 | 67.21 | 122.53 | 124.12 | 91.03 | 33.38 | 58.8054
Single-Core Performance + Prefetching
31
Increases Performance over and
In-Conjunction with Prefetching

## Slide 32
Chart: % Independent Cache Misses Prefetched
| zeusmp | cactus | wrf | GemsFDTD | leslie | omnetpp | milc | soplex | sphinx | bwaves | libquantum | lbm | mcf | Mean
 | 0.89 | 0.45 | 0.66 | 0.69 | 0.85 | 0.54 | 0.96 | 0.57 | 0.82 | 0.93 | 0.92 | 0.92 | 0.38 | 0.71
Independent Miss Coverage
32

## Slide 33
Chart: % Independent Cache Misses Prefetched
| zeusmp | cactus | wrf | GemsFDTD | leslie | omnetpp | milc | soplex | sphinx | bwaves | libquantum | lbm | mcf | Mean
 | 0.89 | 0.45 | 0.66 | 0.69 | 0.85 | 0.54 | 0.96 | 0.57 | 0.82 | 0.93 | 0.92 | 0.92 | 0.38 | 0.71
Independent Miss Coverage
33
70% Prefetch Coverage

## Slide 34
Chart: Normalized Bandwidth
| zeusmp | cactus | wrf | GemsFDTD | leslie | omnetpp | milc | soplex | sphinx | bwaves | libquantum | lbm | mcf | Mean
Continuous Runahead | 1.0208 | 1.0124 | 1.0025 | 1.001 | 1.0002 | 1.1463 | 1.33 | 1.0578 | 1.27 | 1 | 1 | 1.0063 | 1.0647 | 1.0702
Stream PF | 1.0839 | 1.0004 | 1.0411 | 1.0681 | 1.0129 | 1.9121 | 2.0246 | 1.2063 | 1.4334 | 1.0011 | 1.0001 | 1.0526 | 1.0488 | 1.2219
GHB PF | 1.0406 | 1.0142 | 1.0381 | 1.0553 | 1.0092 | 1.5034 | 1.2708 | 1.2745 | 1.3202 | 1.0003 | 1.0001 | 1.0055 | 1.0036 | 1.1181
Bandwidth Overhead
34

## Slide 35
Chart: Normalized Bandwidth
| zeusmp | cactus | wrf | GemsFDTD | leslie | omnetpp | milc | soplex | sphinx | bwaves | libquantum | lbm | mcf | Mean
Continuous Runahead | 1.0208 | 1.0124 | 1.0025 | 1.001 | 1.0002 | 1.1463 | 1.33 | 1.0578 | 1.27 | 1 | 1 | 1.0063 | 1.0647 | 1.0702
Stream PF | 1.0839 | 1.0004 | 1.0411 | 1.0681 | 1.0129 | 1.9121 | 2.0246 | 1.2063 | 1.4334 | 1.0011 | 1.0001 | 1.0526 | 1.0488 | 1.2219
GHB PF | 1.0406 | 1.0142 | 1.0381 | 1.0553 | 1.0092 | 1.5034 | 1.2708 | 1.2745 | 1.3202 | 1.0003 | 1.0001 | 1.0055 | 1.0036 | 1.1181
Bandwidth Overhead
35
Low Bandwidth Overhead

## Slide 36
Chart: % Weighted Speedup Improvement
| H1 | H2 | H3 | H4 | H5 | H6 | H7 | H8 | H9 | H10 | GMean
Continuous Runahead | 48.94 | 51.1 | 41.77 | 44.84 | 55.91 | 49.49 | 49.97 | 34.9 | 29.13 | 35.42 | 43.32
Stream PF | 36.4 | 39.3 | 38.2 | 25.58 | 54.96 | 49.75 | 39.63 | 24.63 | 11.08 | 13.22 | 29.76
GHB PF | 34.52 | 43.21 | 35.9 | 19.14 | 56.13 | 51.78 | 38.83 | 16.99 | 12.41 | 25.12 | 30.11
Multi-Core Performance
36

## Slide 37
Chart: % Weighted Speedup Improvement
| H1 | H2 | H3 | H4 | H5 | H6 | H7 | H8 | H9 | H10 | GMean
Continuous Runahead | 48.94 | 51.1 | 41.77 | 44.84 | 55.91 | 49.49 | 49.97 | 34.9 | 29.13 | 35.42 | 43.32
Stream PF | 36.4 | 39.3 | 38.2 | 25.58 | 54.96 | 49.75 | 39.63 | 24.63 | 11.08 | 13.22 | 29.76
GHB PF | 34.52 | 43.21 | 35.9 | 19.14 | 56.13 | 51.78 | 38.83 | 16.99 | 12.41 | 25.12 | 30.11
Multi-Core Performance
37
43% Weighted Speedup Increase

## Slide 38
Chart: % Weighted Speedup Improvement
| H1 | H2 | H3 | H4 | H5 | H6 | H7 | H8 | H9 | H10 | GMean
Continuous Runahead | 48.94 | 51.1 | 41.77 | 44.84 | 55.91 | 49.49 | 49.97 | 34.9 | 29.13 | 35.42 | 43.32
Stream PF | 36.4 | 39.3 | 38.2 | 25.58 | 54.96 | 49.75 | 39.63 | 24.63 | 11.08 | 13.22 | 29.76
GHB PF | 34.52 | 43.21 | 35.9 | 19.14 | 56.13 | 51.78 | 38.83 | 16.99 | 12.41 | 25.12 | 30.11
Continuous Runahead + Stream | 66.3 | 65.16 | 58.51 | 55.9 | 76.04 | 66.91 | 66.17 | 44.56 | 37.57 | 47.45 | 57.24
Continuous Runahead + GHB | 67.61 | 66.39 | 67.29 | 64.07 | 80.81 | 73.12 | 76.23 | 56.99 | 44.7 | 51.46 | 63.94
Multi-Core Performance + Prefetching
38

## Slide 39
Chart: % Weighted Speedup Improvement
| H1 | H2 | H3 | H4 | H5 | H6 | H7 | H8 | H9 | H10 | GMean
Continuous Runahead | 48.94 | 51.1 | 41.77 | 44.84 | 55.91 | 49.49 | 49.97 | 34.9 | 29.13 | 35.42 | 43.32
Stream PF | 36.4 | 39.3 | 38.2 | 25.58 | 54.96 | 49.75 | 39.63 | 24.63 | 11.08 | 13.22 | 29.76
GHB PF | 34.52 | 43.21 | 35.9 | 19.14 | 56.13 | 51.78 | 38.83 | 16.99 | 12.41 | 25.12 | 30.11
Continuous Runahead + Stream | 66.3 | 65.16 | 58.51 | 55.9 | 76.04 | 66.91 | 66.17 | 44.56 | 37.57 | 47.45 | 57.24
Continuous Runahead + GHB | 67.61 | 66.39 | 67.29 | 64.07 | 80.81 | 73.12 | 76.23 | 56.99 | 44.7 | 51.46 | 63.94
Multi-Core Performance + Prefetching
39
13% Weighted Speedup Gain over
GHB Prefetching

## Slide 40
Chart: Energy Normalized to No-Prefetching Baseline
| H1 | H2 | H3 | H4 | H5 | H6 | H7 | H8 | H9 | H10 | Mean
Continuous Runahead | 0.6501 | 0.6248 | 0.7019 | 0.6929 | 0.6319 | 0.663 | 0.6424 | 0.7613 | 0.7644 | 0.7981 | 0.69065
Stream PF | 0.7508 | 0.7708 | 0.8035 | 0.8548 | 0.7094 | 0.7701 | 0.7868 | 0.8886 | 0.9222 | 0.9449 | 0.81687
GHB PF | 0.6787 | 0.683 | 0.6944 | 0.8485 | 0.6534 | 0.6369 | 0.6879 | 0.8949 | 0.9439 | 0.8079 | 0.74597
Continuous Runahead + Stream | 0.5007 | 0.4728 | 0.6616 | 0.6667 | 0.5589 | 0.5232 | 0.467 | 0.5965 | 0.729 | 0.6965 | 0.58014
Continuous Runahead + GHB | 0.4914 | 0.4701 | 0.5813 | 0.6039 | 0.5177 | 0.5315 | 0.5252 | 0.6234 | 0.7397 | 0.7523 | 0.57665
Multi-Core Energy Evaluation
40

## Slide 41
Chart: Energy Normalized to No-Prefetching Baseline
| H1 | H2 | H3 | H4 | H5 | H6 | H7 | H8 | H9 | H10 | Mean
Continuous Runahead | 0.6501 | 0.6248 | 0.7019 | 0.6929 | 0.6319 | 0.663 | 0.6424 | 0.7613 | 0.7644 | 0.7981 | 0.69065
Stream PF | 0.7508 | 0.7708 | 0.8035 | 0.8548 | 0.7094 | 0.7701 | 0.7868 | 0.8886 | 0.9222 | 0.9449 | 0.81687
GHB PF | 0.6787 | 0.683 | 0.6944 | 0.8485 | 0.6534 | 0.6369 | 0.6879 | 0.8949 | 0.9439 | 0.8079 | 0.74597
Continuous Runahead + Stream | 0.5007 | 0.4728 | 0.6616 | 0.6667 | 0.5589 | 0.5232 | 0.467 | 0.5965 | 0.729 | 0.6965 | 0.58014
Continuous Runahead + GHB | 0.4914 | 0.4701 | 0.5813 | 0.6039 | 0.5177 | 0.5315 | 0.5252 | 0.6234 | 0.7397 | 0.7523 | 0.57665
Multi-Core Energy Evaluation
41
22% Energy Reduction

## Slide 42
Runahead prefetch coverage is limited by the duration of each runahead interval
To remove this constraint, we introduce the notion of Continuous Runahead
We can dynamically identify the most critical LLC misses to target with Continuous Runahead by tracking the operations that cause the pipeline to frequently stall
We migrate these dependence chains to the CRE where they are executed continuously in a loop
Conclusions
42

## Slide 43
Continuous Runahead greatly increases prefetch coverage
Increases single-core performance by 34.4%
Increases multi-core performance by 43.3%
Synergistic with various types of prefetching
Conclusions
43

## Slide 44: Continuous Runahead: Transparent Hardware Acceleration for Memory Intensive Workloads
Milad Hashemi, Onur Mutlu, Yale N. Patt
UT Austin/Google, ETH Zürich, UT Austin
October 19th, 2016
44