## Slide 1
Anup Das
Shihao Song, Onur Mutlu, and Nagarajan Kandasamy
DATACON
Improving Phase Change Memory Performance
via Data Content Aware Access

## Slide 2: Executive Summary
Observations
  During PCM write, latency and energy are sensitive to the data to be written as well as the content that is overwritten, which is unknown at the time to write
  Overwriting known all-0s or all-1s content improves both latency and energy by programming the PCM cells only in one direction, i.e., using SET or RESET operations, not both
Idea: Data Content Aware PCM Writes
  Overwrite unknown content only when necessary, and otherwise overwrite all-0s and all-1s content reduces latency and energy
Two Key Mechanisms
  Address translation: to translate the write address to a physical address within memory that contains the best type of content to overwrite
  Re-Initialization: to methodically re-initialize unused memory locations with known all-0s and all-1s content in a manner that does not interfere with regular read and write accesses
Performance Evaluation
  Significant improvement of system performance (27%) and reduction of energy (43%) for SPEC CPU2017, NAS Parallel, and Tensorflow Benchmarks

## Slide 3: Asymmetry in PCM SET and RESET Operations
PCM stores data as resistance of its cells
RESET operation (1–> 0): fast and high energy
SET operation (0 —> 1): slow and low energy

## Slide 4: Baseline PCM Write Operation
Use both SET and RESET operations
Program and Verify (P&V) Scheme

## Slide 5: PreSET and PreRESET
Use either SET and RESET operations, not both
PreSET or PreRESET is decided at design-time and used for all PCM writes, independent of the write data
PreSET: Overwrite all-1s
PreRESET: Overwrite all-0s
  Qureshi et al., “PreSET: Improving performance of phase change memories by exploiting asymmetry in write times,” in ISCA, 2012

## Slide 6: PCM Write Related Key Observations (I)
Energy benefit of PreSET vs. PreRESET depends on the fraction of SET bits in the write data

## Slide 7: PCM Write Related Key Observations (I)
Energy benefit of PreSET vs. PreRESET depends on the fraction of SET bits in the write data
Idea: Use PreRESET when the fractions of SET bits in the write data is less than 60%, otherwise use PreSET

## Slide 8: PCM Write Related Key Observations (II)
The fraction of SET bits in the write data is workload dependent

## Slide 9: PCM Write Related Key Observations (II)
The fraction of SET bits in the write data is workload dependent
Idea: Re-initialize unused memory locations with all-0s or all-1s based on the the PCM writes in a workload

## Slide 10: Data Content Aware PCM Writes
Key Idea
  To serve PCM writes
    Overwrite known all-0s or all-1s content: to improve performance and energy
    Overwrite unknown content: only when is no all-0s or all-1s initialized location available in PCM
Three components
  Analysis of write data
    Analyze the fraction of SET bits in write data and estimate the energy-latency trade-offs for SET and RESET operations in PCM
  Address translation
    Translate the write address to a physical address within memory that contains the best type of content to overwrite, and record this translation in a table for future accesses.
  Re-initialization
    Re-initialize unused memory locations with known all-0s or all-ones content in a manner that does not interfere with regular read and write accesses

## Slide 11: Outline
Introduction
Detailed design of DATACON
Address translation
Overwritten content selection
Re-initialization
Evaluation
Conclusion

## Slide 12: System Overview
DRAM-PCM hybrid memory with embedded DRAM (eDRAM) as write cache to PCM main memory

## Slide 13: System Overview
DRAM-PCM hybrid memory with embedded DRAM (eDRAM) as write cache to PCM main memory
One eDRAM cache line maps to
eight memory lines in a PCM rank

## Slide 14: Detailed Design of DATACON
DATACON adds four new components to the baseline design
  Address Translation Table (AT): to record logical-to-physical address translations, which are needed to redirect write requests to the best overwritten content in PCM
  Lookup Table (LUT): to cache recently-used address translation information in the memory controller
  Address Status Unit (SU): to select an all-0s or all-1s initialized physical address for the logical address of a write request
  Initialization Queue (InitQ): to record unused physical locations in PCM, such that they can be re-initialized methodically

## Slide 15: Address Translation (I): Read
read
0x30a
0x11fe
0x30a
0x910b
0x1078
LUT

## Slide 16: Outline
Introduction
Detailed design of DATACON
Address translation
Overwritten content selection
Re-initialization
Evaluation
Conclusion

## Slide 17: Address Translation (I): Read
read
0x30a
logical address

## Slide 18: Address Translation (I): Read
read
0x30a
0x11fe
0x30a
LUT
logical address

## Slide 19: Address Translation (I): Read
read
0x30a
0x11fe
0x30a
LUT
read
0x11fe
logical address
physical address

## Slide 20: Address Translation (II): Write
write
0x1078
0x0005
logical address
write
data

## Slide 21: Address Translation (II): Write
write
0x1078
0x0005
logical address
write
data
Overwritten Content Selection

## Slide 22: Address Translation (II): Write
write
0x1078
0x0005
logical address
write
data
Overwritten Content Selection
overwrite
all-0s

## Slide 23: Address Translation (II): Write
write
0x1078
0x0005
logical address
write
data
Overwritten Content Selection
overwrite
all-0s
0x910b
ResetQ
SetQ
SU

## Slide 24: Address Translation (II): Write
write
0x1078
0x0005
logical address
write
data
Overwritten Content Selection
overwrite
all-0s
0x910b
ResetQ
SetQ
write
0x910b
0x0005
physical address
write
data
SU

## Slide 25: Address Translation (II): Write
write
0x1078
0x0005
logical address
write
data
Overwritten Content Selection
overwrite
all-0s
0x910b
ResetQ
SetQ
write
0x910b
0x0005
physical address
write
data
0x11fe
0x30a
0x910b
0x1078
LUT
SU

## Slide 26: Address Translation (II): Write
write
0x1078
0x0005
logical address
write
data
Overwritten Content Selection
overwrite
all-0s
0x910b
ResetQ
SetQ
write
0x910b
0x0005
physical address
write
data
0x11fe
0x30a
0x910b
0x1078
LUT
0x1078
InitQ
SU

## Slide 27: Address Translation

## Slide 28: Outline
Introduction
Detailed design of DATACON
Address translation
Overwritten content selection
Re-initialization
Evaluation
Conclusion

## Slide 29: Overwritten Content Selection

## Slide 30: Overwritten Content Selection
DATACON overwrites unknown content only when there is no all-0s or all-1s initialized content available in PCM

## Slide 31: Outline
Introduction
Detailed design of DATACON
Address translation
Overwritten content selection
Re-initialization
Evaluation
Conclusion

## Slide 32: Re-initialization Requests
Two queues to record the address of all-0s and all-1s content in PCM
  SetQ and ResetQ
Thresholding to initiate re-initialization requests
  Re-initialization requests stored in the InitQ
Re-initialization requests serviced when
  Read and the write queues are both empty, or
  Write queue is empty and read request is to a memory partition different from the re-initialization request
    Exploit’s PCM’s partition-level parallelism (PALP)
  Song et al., “Enabling and Exploiting Partition-Level Parallelism (PALP) in Phase Change Memories,” in CASES, 2019

## Slide 33: Outline
Introduction
Detailed design of DATACON
Address translation
Overwritten content selection
Re-initialization
Evaluation
Conclusion

## Slide 34: System Configuration
A cycle-level in-house x86 multi-core simulator, whose front-end is based on Pin
  To simulate 8 out-of-order cores
A main memory simulator, closely matching the JEDEC Nonvolatile Dual In-line Memory Module (NVDIMM)- N/F/P Specifications
  Ramulator to simulate DRAM
  NVMain to simulate PCM
Ramulator: Kim et al. “Ramulator: A fast and extensible DRAM simulator” CAL, 2016.
NVMain: Poremba et al. “Nvmain 2.0: A user-friendly memory simulator to model (non-) volatile memory systems” CAL, 2015

## Slide 35: Simulation Parameters

## Slide 36: Simulation Parameters

## Slide 37: Evaluated Systems
Baseline: services PCM writes by overwriting unknown content
  Lee et al., “Architecting phase change memory as a scalable DRAM alternative,” in ISCA, 2009
PreSET: services PCM writes by always overwriting all-1s
  Qureshi et al., “PreSET: Improving performance of phase change memories by exploiting asymmetry in write times,” in ISCA, 2012
Flip-N-Write: services PCM writes by finding out the memory content using additional reads and programming only bits that are different from the write data
  Cho et al., “Flip-N-Write: a simple deterministic technique to improve PRAM write performance, energy and endurance,” in MICRO, 2009

## Slide 38: Workloads
SPEC CPU2017
NAS Parallel Benchmarks
Tensorflow workloads

## Slide 39: Overall System Performance
Execution time normalized to Baseline

## Slide 40: Overall System Performance
Average Execution time of DATACON is
40% lower than Baseline,
47% lower than Flip-N-Write, and
27% lower than PreSET

## Slide 41: Memory System Energy
Energy normalized to Baseline

## Slide 42: Memory System Energy
Energy normalized to Baseline
Average Energy of DATACON is
27% lower than Baseline,
26% lower than Flip-N-Write, and
43% lower than PreSET

## Slide 43: Overwritten Content
Overwritten content in DATACON and PreSET

## Slide 44: Overwritten Content
Overwritten content in DATACON and PreSET
DATACON overwrites unknown content for only 4% of PCM writes. PreSET overwrites unknown content for 59% of PCM writes.

## Slide 45: Re-initialization Overhead
Total PCM energy distributed into energy to service reads, writes, and re-initialization requests in DATACON

## Slide 46: Re-initialization Overhead
Total PCM energy distributed into energy to service reads, writes, and re-initialization requests in DATACON
Re-initialization requests constitute, on average,
11% of the total PCM energy

## Slide 47: LUT Sizing
Execution time normalized to Baseline for three different LUT sizes

## Slide 48: LUT Sizing
Execution time normalized to Baseline for three different LUT sizes
Caching the address translations of 2 recently-used partitions
is sufficient to provide high performance.
There is marginal performance improvement from caching more partitions.

## Slide 49: Outline
Introduction
Detailed design of DATACON
Address translation
Overwritten content selection
Re-initialization
Evaluation
Conclusion

## Slide 50: Conclusion
Observations
  During PCM write, latency and energy are sensitive to the data to be written as well as the content that is overwritten, which is unknown at the time to write
  Overwriting known all-0s or all-1s content improves both latency and energy by programming the PCM cells only in one direction, i.e., using SET or RESET operations, not both
Idea: Data Content Aware PCM Writes
  Overwrite unknown content only when necessary, and otherwise overwrite all-0s and all-1s content reduces latency and energy
Two Key Mechanisms
  Address translation: to translate the write address to a physical address within memory that contains the best type of content to overwrite
  Re-Initialization: to methodically re-initialize unused memory locations with known all-0s and all-1s content in a manner that does not interfere with regular read and write accesses
Performance Evaluation
  Significant improvement of system performance (27%) and reduction of energy (43%) for SPEC CPU2017, NAS Parallel, and Tensorflow Benchmarks

## Slide 51
Anup Das
Shihao Song, Onur Mutlu, and Nagarajan Kandasamy
Contact: shihao.song@drexel.edu
DATACON
Improving Phase Change Memory Performance
via Data Content Aware Access