## Slide 1: Isolating CPU and IO Traffic by Leveraging a Dual-Data-Port DRAM
Donghyuk Lee
Lavanya Subramanian, Rachata Ausavarungnirun, Jongmoo Choi, Onur Mutlu
Decoupled Direct Memory Access
Notes: Hello, my name is Donghyuk Lee.
Today, I will talk about “Decoupled Direct Memory Access, which Isolates CPU and IO Traffic by Leveraging a Dual-Data-Port DRAM”.
This work is done in collaboration with Jongmoo Choi from Dankook University, and Lavanya Subramanian, Rachata Ausavarungnirun, and my advisor Onur Mutlu from Carnegie Mellon Universiy

## Slide 2
processor
Logical System Organization
main memory
IO devices
CPU access
IO access
Main memory connects processor and IO devices as an intermediate layer
Notes: In logical organization, system consists of processor, main memory and IO devices.
Processor accesses main memory to get data for executing instructions, called CPU access.
IO devices transfer data to main memory, called IO access.
Therefore, the main memory connects processor and IO devices as an intermediate layer.

## Slide 3
processor
Physical System Implementation
main memory
IO devices
CPU access
IO access
IO access
High Pin Cost
in Processor
High Contention
in Memory Channel
Notes: In physical implementation, however, IO devices are connected to processor,
and DMA in the processor manages the IO traffic through memory channel.
This difference between logical and physical organization leads to
High contention in memory channel,
High pin count in processor chip.

## Slide 4
processor
Our Approach
main memory
IO devices
CPU access
Enabling IO channel, decoupled & isolated from CPU channel
IO access
IO access
Notes: To avoid these problems, our approach is providing a direct connection between IO devices and main memory, which enables IO access without interfering CPU access.
We call this new memory system architecture – Decouple Direct Memory Access

## Slide 5
Executive Summary
Problem
  CPU and IO accesses contend for the shared memory channel
Our Approach: Decoupled Direct Memory Access (DDMA)
  Design new DRAM architecture with two independent data ports
   Dual-Data-Port DRAM
  Connect one port to CPU and the other port to IO devices
   Decouple CPU and IO accesses
Application
  Communication between compute units (e.g., CPU – GPU)
  In-memory communication (e.g., bulk in-memory copy/init.)
  Memory-storage communication (e.g., page fault, IO prefetch)
Result
  Significant performance improvement (20% in 2 ch. & 2 rank system)
  CPU pin count reduction (4.5%)
Notes: This is the summary of today’s talk.
The problem is that CPU and IO accesses contend for memory channel.
To mitigate this problem, we design new DRAM which has two independent data port, called dual-data-port DRAM.
We connect one port to CPU and the other port to IO devices, thereby isolating CPU and IO traffic.
We call this Decoupled Direct Memory Access (DDMA).
We can use this new memory system for
Communication between compute units,
In-memory communication, and
Memory-storage communication.
We evaluate our DDMA-based memory system and show that it provides significant performance improvement with reduction in CPU pin count.

## Slide 6
Outline
1. Problem
3. Dual-Data-Port DRAM
5. Evaluation
4. Applications for DDMA
2. Our Approach
1. Problem
Notes: This is the outline of today’s talk.
We first describe more details of the problem in conventional memory system.
Then we provide the overview of our proposed memory system.
Then we introduce one of major component, dual-data-port DRAM.
We explain how we can leverage our new memory system.
We, then, provide our evaluation methodology and results.

## Slide 7
main memory
CPU
DMA
graphics
network
storage
USB
IO interface
memory controller
Memory Channel Contention
DRAM
Chip
Processor
Chip
Problem 1: Memory Channel Contention
DMA
IO interface
Notes: This is more detailed view of a system.
CPU is connected to main memory over memory channel and
the memory controller manages accesses to the main memory.
IO devices are connected the CPU over IO interface in CPU chip.
Direct memory access unit (DMA) controls the IO traffic.
When there is a request for data in IO devices,
the requested data is first transferred to the main memory over both IO interface and the memory channel.
Then CPU accesses the main memory again to bring the requested data.
When there is a request for data in main memory,
the requested data is also transferred over the main memory.
In today’s multi-core system, all these data transfer can be happen concurrently, leading to memory channel contention.

## Slide 8
Chart: 
| CORR | SYR2K | GRAMSCHM | COVAR | SYRK | FDTD2D | 2MM | 3MM | GEMM | MVT | GESUMMV | BICG | ATAX | 3DCONV | 2DCONV
Time Spent on CPU-GPU Communication | 0.00056984 | 0.00095816 | 0.0015094 | 0.0018979 | 0.0060775 | 0.015924 | 0.027459 | 0.078553 | 0.10453 | 0.38899 | 0.39085 | 0.39323 | 0.3986 | 0.89039 | 0.91692
33.5%
on average
Fraction of Execution Time
A large fraction of the execution time is spent on IO accesses
Problem 1: Memory Channel Contention
Notes: To see the potential memory channel contention, we observe the IO traffic in GPGPU workloads.
X-axis shows the GPGPU workloads.
Y-axis shows the fraction of execution time that consume for IO accesses.
As we can see, some of GPGPU workloads mostly consumes for its execution time for computation,
however, many workloads spent significant fraction of the total execution time for transferring data between CPU and GPU. For example 33.5% on average of 8 GPGPU workloads.
Therefore, there is high demand of IO bandwidth, leading to high memory channel contention.

## Slide 9
Integrating IO interface on the processor chip leads to high area cost
Chart: 
| Others | IO Interface | Memory Channel | Power
Pin Count | 98 | 117 | 288 | 600
Chart: 
| Others | IO Interface | Memory Channel
Pin Count | 98 | 117 | 288
Processor Pin Count
(w/o power pins)
power
memory
(2 ch)
IO interface
(10.6%)
others
IO interface
(28.4%)
others
memory
(2 ch)
(w/ power pins)
Processor Pin Count
959 pins in total
359 pins in total
Problem 2: High Cost for IO Interfaces
Notes: Second problem is high area cost for IO interfaces in processor chip.
The chart shows the processor pin count of an Intel i7 processor.
As we can see, 10.6% of total pins are used for IO interfaces.
In the right chart, without counting power pints,
we see that about 19.5% of total pins are used for IO interfaces.
Therefore, integrating IO interface on processor chip leads to high processor pin count, potentially large processor chip area.

## Slide 10
Shared Memory Channel
Memory channel contention for IO access and CPU access
High area cost for integrating IO interfaces on processor chip
Notes: In summary,
IO and CPU accesses contend for memory channel.
Integrating more IO interfaces for higher bandwidth leads to high area cost on processor chip.

## Slide 11
Outline
1. Problem
3. Dual-Data-Port DRAM
5. Evaluation
4. Applications for DDMA
2. Our Approach
Notes: This is the outline of today’s talk.
We first describe more details of the problem in conventional memory system.
Then we provide the overview of our proposed memory system.
Then we introduce one of major component, dual-data-port DRAM.
We explain how we can leverage our new memory system.
We, then, provide our evaluation methodology and results.

## Slide 12
Our Approach
CPU
DMA
graphics
network
storage
USB
DRAM
Chip
main memory
?
DMA
CTRL.
DMA control
Processor
Chip
control channel
Dual-Data-
Port DRAM
Port 1
Port 2
memory controller
IO interface
DMA
Chip
DMA IO interface
Notes: As explained, our approach is directly connecting IO devices to main memory.
To this end, we first migrate IO interfaces and fraction of DMA unit out of processor chip,
we call this chip DMA IO.
DMA control unit is still existing within the processor chip, which manages off-chip DMA-IO.
To connect this off-chip DMA-IO to the main memory,
we devise a new DRAM architecture, Dual-Data-Port DRAM, which has two independent data ports,
both of which are managed by memory controller.

## Slide 13
Our Approach
?
CPU
graphics
network
storage
USB
DRAM
Chip
DMA
CTRL.
DMA control
Processor
Chip
control channel
Dual-Data-
Port DRAM
Port 1
Port 2
memory controller
DMA
Chip
DMA IO interface
IO ACCESS
Decoupled Direct Memory Access
CPU ACCESS
Notes: As explained, our approach is directly connecting IO devices to main memory.
To this end, we first migrate IO interfaces and fraction of DMA unit out of processor chip,
we call this chip DMA IO.
DMA control unit is still existing within the processor chip, which manages off-chip DMA-IO.
To connect this off-chip DMA-IO to the main memory,
we devise a new DRAM architecture, Dual-Data-Port DRAM, which has two independent data ports,
both of which are managed by memory controller.

## Slide 14
Outline
1. Problem
3. Dual-Data-Port DRAM
5. Evaluation
4. Applications for DDMA
2. Our Approach
Notes: This is the outline of today’s talk.
We first describe more details of the problem in conventional memory system.
Then we provide the overview of our proposed memory system.
Then we introduce one of major component, dual-data-port DRAM.
We explain how we can leverage our new memory system.
We, then, provide our evaluation methodology and results.

## Slide 15
peripherallogic
bank
Background: DRAM Operation
memory channel
data channel
control channel
control port
data port
control port
data port
bank
activate
read
bank
bank
READY
DRAM peripheral logic: i) controls banks, and ii) transfers data over memory channel
memory controller at CPU
Notes: We first explain the conventional DRAM organization and its operation.
DRAM consists of multiple banks and peripheral logic.
This DRAM chip is connected to the processor chip over memory channel.
This memory channel consists of a control channel and a data channel.
The DRAM peripheral logic connects these control and data channel to DRAM bank,
which are called control path and data path.
Accessing DRAM starts from activating a bank.
The bank are ready to be transfer data.
When receiving a read command, data is transferred over both data path and data channel.
In summary, DRAM periphery logic, control banks and transfer data over memory channel.

## Slide 16
bank
Problem: Single Data Port
periphery
Requests are served serially due to single data port
data channel
control channel
control port
data port
read
control port
data port
bank
READY
bank
READY
data port
read
Many
Banks
Single Data Port
memory controller at CPU
Notes: This figure shows the access scenario of multiple banks.
Now, both banks are ready to serve data and memory controller has requests for both banks.
When receiving a read command of a bank, the bank transfer data.
After finishing the data transfer, the memory controller issues another read commands, leading to transferring data.
Even though there are multiple banks which are ready to transfer data,
the peripheral logic only transfer data one after another.
Therefor, requests for multiple banks are served in serial due to limited peripheral logic.

## Slide 17
Problem: Single Data Port
RD
DATA
RD
DATA
Control Port
Data Port
time
RD
DATA
RD
Control Port
Data Port 1
time
DATA
Data Port 2
What about a DRAM with two data ports?
Notes: Specifically,
issuing a command takes one clock cycle in control channel.
However, transferring data takes multiple cycles in data channel, for example, 4 cycles for 8 data burst.
Therefore, peripheral logic for data traffic leads to more serialization for accessing DRAM.

## Slide 18
bank
periphery
twice the bandwidth & independent data ports with low overhead
data channel
control channel
data port 1
bank
bank
control port
to Port 1 (upper)
to Port 2 (lower)
bank
data bus
port select signal
data port 2
data channel
mux
mux
Overhead
Area: 1.6% ↑
Pins: 20 ↑
Dual-Data-Port DRAM
Notes: We add additional data data port and data path.
To manage the connections between bank and these two data port, we add a multiplexer per each bank.
The multiple makes any connection in the three nodes – bank data bus, upper data port, and lower data port.
To manage the multiplexer, we add a control signal, port select, in the control channel.
We called this new DRAM architecture, Dual-Data-Port DRAM, which has twice bandwidth and two independent data ports.

## Slide 19
DDP-DRAM Memory System
bank
periphery
CPU channel
control channel
with port select
data port 1
bank
bank
control port
data port 2
IO channel
mux
mux
DDMA IO interface
memory controller at CPU
Notes: We integrate this Dual-Data-Port DRAM in a system by connecting a data port to CPU and the other to DDM-IO.
In our architecture, Both data ports and DDMA-IO are controlled by the memory controller in the processor.

## Slide 20
Three Data Transfer Modes
CPU Access: Access through CPU channel
  DRAM read/write with CPU port selection
IO Access: Access through IO channel
  DRAM read/write with IO port selection
Port Bypass: Direct transfer between channels
  DRAM access with port bypass selection
Notes: Our Dual-Data-Port DRAM supports three access mode, CPU access, IO access, and Port Bypass.
Let us take a look at more details of these three modes.

## Slide 21
1. CPU Access Mode
bank
periphery
CPU channel
bank
control port
data port 2
IO channel
DDMA IO interface
control channel
with port select
mux
mux
data port
bank
READY
memory controller at CPU
read
control port
CPU channel
data port 1
control channel
with CPU channel
Notes: In CPU access mode, memory controller simply issues read command with CPU port selection.
Then, DRAM periphery builds the connection between bank and CPU port,
and transfer data to CPU, which is same as DRAM access in conventional systems.

## Slide 22
2. IO Access Mode
bank
periphery
CPU channel
bank
control port
IO channel
DDMA IO interface
control channel
with port select
mux
mux
data port 1
control channel
with IO channel
memory controller at CPU
IO channel
data port
data port 2
bank
READY
read
control port
Notes: In IO Access mode, memory controller issues read/write command with IO port selection.
Then, DRAM peripheral logic builds the connection between bank and IO port,
and transfer data to IO channel.
DDMA-IO, then, read data from IO channel.

## Slide 23
3. Port Bypass Mode
bank
periphery
CPU channel
bank
control port
IO channel
control channel
with port select
mux
mux
control channel
with port bypass
IO channel
bank
data port
data port
data port 2
data port 1
CPU channel
DDMA IO interface
memory controller at CPU
Notes: In Port Bypass mode, memory controller issues read/write command with both ports selection.
Then, DRAM peripheral logic builds the connection between these two ports,
then memory controller and DDMA-IO directly communicate over DRAM peripheral logic.

## Slide 24
Outline
1. Problem
3. Dual-Data-Port DRAM
5. Evaluation
4. Applications for DDMA
2. Our Approach
Notes: This is the outline of today’s talk.
We first describe more details of the problem in conventional memory system.
Then we provide the overview of our proposed memory system.
Then we introduce one of major component, dual-data-port DRAM.
We explain how we can leverage our new memory system.
We, then, provide our evaluation methodology and results.

## Slide 25
Three Applications for DDMA
Communication b/w Compute Units
  CPU-GPU communication
In-Memory Communication and Initialization
  Bulk page copy/initialization
Communication b/w Memory and Storage
  Serving page fault/file read & write
Notes: First, DDMA supports communication between compute units.
For example, CPU-GPU communication.
Second, DDMA supports In-memory communication and initialization.
For example, bulk page copy and initialization can perform through DDMA.
Third, DDMA support communication between memory and storage.
For example, page fault, file read and write.
This feature also enables aggressive IO prefetching.
Let us take a look at more details of these mechanisms.

## Slide 26
ctrl. channel
DDMA ctrl.
read
with IO sel.
CPU → GPU
1. Compute Unit ↔ Compute Unit
CPU
DDMA
ctrl.
memory controller
DDP-DRAM
DDMA IO interface
GPU
DDMA
ctrl.
memory controller
DDP-DRAM
DDMA IO interface
ctrl. channel
DDMA ctrl.
destination
DDMA IO interface
source
Ack.
destination
DDMA IO interface
write
with IO sel.
Transfer data through DDMA without interfering w/ CPU/GPU memory accesses
CPU
memory controller
GPU
memory controller
Notes: This figure shows two systems, CPU system and GPU system that has their own memory system.
The communication scenario is transferring data from CPU memory to GPU memory.
To this end,
CPU memory controller issues read commands to transfer data to CPU DDMA-IO.
Then, CPU DDMA-IO transfers data to GPU DDMA-IO.
GPU DDMA-IO lets GPU knows about the data transfer.
Then, GPU memory controller issues write commands to transfer data to DRAM.

## Slide 27
ctrl. chan.
read
with IO sel.
write
with IO sel.
2. In-Memory Communication
DDMA ctrl.
CPU
DDMA
ctrl.
memory controller
DDP-DRAM
DDMA IO interface
source
destination
Transfer data in DRAM through DDAM without interfering with CPU memory accesses
CPU
memory controller
Notes: The communication scenario is migrating data from one location to the other location within DRAM.
To this end,
The memory controller first issues read command with IO port select to transfer data to DDMA-IO.
The memory controller, then, issues write command with IO port select to transfer data to DRAM.

## Slide 28
DDMA ctrl.
Acc. Storage
Ack.
3. Memory ↔ Storage
ctrl. chan.
write
with IO sel.
CPU
DDMA
ctrl.
memory controller
DDP-DRAM
DDMA IO interface
Storage
Storage (source)
destination
DDMA IO interface
Transfer data from storage through DDMA without interfering with CPU memory accesses
destination
CPU
memory controller
Notes: The communication scenario in this figure is transferring data from storage to main memory.
To this end,
DDMA-IO first brings data from storage.
Then, DDMA-IO lets CPU know the data traffic from storage.
The memory controller, then, issues write command to transferring the data to DRAM.

## Slide 29
Outline
1. Problem
3. Dual-Data-Port DRAM
5. Evaluation
4. Applications for DDMA
2. Our Approach
Notes: This is the outline of today’s talk.
We first describe more details of the problem in conventional memory system.
Then we provide the overview of our proposed memory system.
Then we introduce one of major component, dual-data-port DRAM.
We explain how we can leverage our new memory system.
We, then, provide our evaluation methodology and results.

## Slide 30
Evaluation Methods
System
  Processor: 4 – 16 cores
  LLC: 16-way associative, 512KB private cache-slice/core
  Memory: 1 – 4 ranks and 1 – 4 channels
Workloads
  Memory intensive: SPEC CPU2006, TPC, stream (31 benchmarks)
  CPU-GPU communication intensive: polybench (8 benchmarks)
  In-memory communication intensive: apache, bootup, compiler, filecopy, mysql, fork, shell, memcached (8 in total)
Notes: We model systems that have 4 to 16 cores and memory systems that have 1 to 4 ranks and 1 to 4 channels.
We builds workloads by randomly selecting from three benchmark categories.
Memory intensive benchmark from SPEC CPU 20016, TPC, stream
CPU-GPU communication benchmarks from Polybench
In-memoy intensive benchmarks,

## Slide 31
Chart: 
| 4-Core | 8-Core | 16-Core
C2R2 | 0.079197 | 0.14666 | 0.20091
Chart: 
| 4-Core | 8-Core | 16-Core
C4R1 | 0.052178 | 0.11706 | 0.20439
Performance Improvement
Performance Improvement
CPU-GPU Comm.-Intensive
In-Memory Comm.-Intensive
More performance improvement at higher core count
High performance improvement
Performance (2 Channel, 2 Rank)
Notes: We first observe the performance improvement in 2 rank and 2 channel memory systems.
Left figure shows the case for CPU-GPU communication-intensive workloads.
X axis shows the number of cores and Y axis are weighted speedup improvement.
As we can see, our mechanism provides significant performance improvement and provide more performance improvement in more core counts. More core systems provide more inflight requests the main memory, leading to higher contention in memory channel. By decoupling IO accesses from the memory channel, our mechanism provides more performance improvement at more core systems.
We observe similar results for in-memory communication-intensive workloads.
We conclude that our mechanism provide more performance improvement for more core systems.

## Slide 32
Performance on Various Systems
Chart: 
| 1 rank | 2 rank | 4 rank
16-Core | 0.23101 | 0.27317 | 0.31961
Chart: 
| 1 ch | 2 ch | 4 ch
16-Core | 0.23101 | 0.14869 | 0.080779
Channel Count
Rank Count
Performance Improvement
Performance Improvement
Performance increases with rank count
Notes: Now we vary the memory system configuration of the number of ranks and channels.
X axis shows channel and rank count.
Y axis are weighted speedup improvement.
When increasing the number of channels, our mechanism provides less benefits in performance mainly due to the reduced memory channel conflicts in more-channel memory systems.
When increasing the number of ranks, our mechanism provides more benefits in performance mainly due to higher conflicts in more-rank memory system.
In summary, our mechanism provides more performance improvement at more memory ranks and less memory channels.

## Slide 33
Chart: 
| 1 ch | 1 ch DDMA | 2 ch
16-Core | 959 | 915 | 1103
Chart: 
| 1 ch | 1 ch DDMA | 2 ch
16-Core | 1 | 1.3226 | 1.5952
Performance
Processor Pin Count
DDMA achieves higher performance at lower processor pin count
959
915
1103
DDMA vs. Doubling Channel
Notes: We compare our mechanism to the case, simply increasing channel counts.
Left figure shows performance comparison of three memory system, baseline – 1 channel memory system, our proposal – 1 channel with DDMA, and 2 channel memory system.
Our mechanism provides significant performance improvement over the baseline 1 channel memory system. but, less performance benefit than 2 channel memory system.
However, increasing channel count leads to significant increase in processor pins.
We compare this trade off in right figure. Y axis are package pin count. Adding one more memory channel requires significant additional processor pins (144 pins per channel). On the other hand, using DDMA reduces processors pins mainly due to migrated IO interfaces out of processors chip.
Therefore, our mechanism achieves higher performance at lower processor pin count.

## Slide 34
Conclusion
Problem
  CPU and IO accesses contend for the shared memory channel
Our Approach: Decoupled Direct Memory Access (DDMA)
  Design new DRAM architecture with two independent data ports
   Dual-Data-Port DRAM
  Connect one port to CPU and the other port to IO devices
   Decouple CPU and IO accesses
Application
  Communication between compute units (e.g., CPU – GPU)
  In-memory communication (e.g., bulk in-memory copy/init.)
  Memory-storage communication (e.g., page fault, IO prefetch)
Result
  Significant performance improvement (20% in 2 ch. & 2 rank system)
  CPU pin count reduction (4.5%)
Notes: This is the summary of today’s talk.
The problem is that CPU and IO accesses contend for memory channel.
To mitigate this problem, we design new DRAM which has two independent data port, called dual-data-port DRAM.
We connect one port to CPU and the other port to IO devices, thereby isolating CPU and IO traffic.
We call this Decoupled Direct Memory Access (DDMA).
We can use this new memory system for
Communication between compute units,
In-memory communication, and
Memory-storage communication.
We evaluate our DDMA-based memory system and show that it provides significant performance improvement with reduction in CPU pin count.

## Slide 35: Isolating CPU and IO Traffic by Leveraging a Dual-Data-Port DRAM
Donghyuk Lee
Lavanya Subramanian, Rachata Ausavarungnirun, Jongmoo Choi, Onur Mutlu
Decoupled Direct Memory Access
Notes: Hello, my name is Donghyuk Lee.
Today, I will talk about “Decoupled Direct Memory Access, which Isolates CPU and IO Traffic by Leveraging a Dual-Data-Port DRAM”.
This work is done in collaboration with Jongmoo Choi from Dankook University, and Lavanya Subramanian, Rachata Ausavarungnirun, and my advisor Onur Mutlu from Carnegie Mellon Universiy

## Slide 36
System Overhead
DDMA reduces more expensive on-chip area, while increasing less expensive off-chip area
processor
DRAM
IO devices
Conventional System
processor
DDP-DRAM
IO devices
DDMA-IO
Proposed System
Low Cost High
Notes: To avoid these problems, our approach is providing a direct connection between IO devices and main memory, which enables IO access without interfering CPU access.
We call this new memory system architecture – Decouple Direct Memory Access

## Slide 37
Chart: 
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 Channel | 2 Channel | 2 Channel | 1 Rank | 2 Rank | 4 Rank
Both Channels Busy | 0 | 0.26603 | 0.26603 | 0 | 0 | 0.15977 | 0.15977 | 0 | 0 | 0.073127 | 0.073127 | 0 | 0 | 0.26603 | 0.26603 | 0 | 0 | 0.3196 | 0.3196 | 0 | 0 | 0.34056 | 0.34056 | 0
Single Channel Busy | 0 | 0.52812 | 0.14788 | 0 | 0 | 0.51975 | 0.15359 | 0 | 0 | 0.43631 | 0.13644 | 0 | 0 | 0.52812 | 0.14788 | 0 | 0 | 0.52645 | 0.099813 | 0 | 0 | 0.50368 | 0.087344 | 0
Channel Utilization Analysis
Simultaneous Channel Utilization  Performance Improvement
CPU-GPU Communication-Intensive
Channel Utilization
CPU
IO
CPU
IO
CPU
IO
CPU
IO
CPU
IO
CPU
IO
Chart: 
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 Channel | 2 Channel | 2 Channel | 1 Rank | 2 Rank | 4 Rank
Both Channels Busy | 0 | 0.26603 | 0.26603 | 0 | 0 | 0.15977 | 0.15977 | 0 | 0 | 0.073127 | 0.073127 | 0 | 0 | 0.26603 | 0.26603 | 0 | 0 | 0.3196 | 0.3196 | 0 | 0 | 0.34056 | 0.34056 | 0
Single Channel Busy | 0 | 0.52812 | 0.14788 | 0 | 0 | 0.51975 | 0.15359 | 0 | 0 | 0.43631 | 0.13644 | 0 | 0 | 0.52812 | 0.14788 | 0 | 0 | 0.52645 | 0.099813 | 0 | 0 | 0.50368 | 0.087344 | 0
Chart: 
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 Channel | 2 Channel | 2 Channel | 1 Rank | 2 Rank | 4 Rank
Both Channels Busy | 0 | 0.26603 | 0.26603 | 0 | 0 | 0.15977 | 0.15977 | 0 | 0 | 0.073127 | 0.073127 | 0 | 0 | 0.26603 | 0.26603 | 0 | 0 | 0.3196 | 0.3196 | 0 | 0 | 0.34056 | 0.34056 | 0
Single Channel Busy | 0 | 0.52812 | 0.14788 | 0 | 0 | 0.51975 | 0.15359 | 0 | 0 | 0.43631 | 0.13644 | 0 | 0 | 0.52812 | 0.14788 | 0 | 0 | 0.52645 | 0.099813 | 0 | 0 | 0.50368 | 0.087344 | 0
Chart: 
|  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 Channel | 2 Channel | 2 Channel | 1 Rank | 2 Rank | 4 Rank
Both Channels Busy | 0 | 0.26603 | 0.26603 | 0 | 0 | 0.15977 | 0.15977 | 0 | 0 | 0.073127 | 0.073127 | 0 | 0 | 0.26603 | 0.26603 | 0 | 0 | 0.3196 | 0.3196 | 0 | 0 | 0.34056 | 0.34056 | 0
Single Channel Busy | 0 | 0.52812 | 0.14788 | 0 | 0 | 0.51975 | 0.15359 | 0 | 0 | 0.43631 | 0.13644 | 0 | 0 | 0.52812 | 0.14788 | 0 | 0 | 0.52645 | 0.099813 | 0 | 0 | 0.50368 | 0.087344 | 0
4
Notes: To see where the performance benefit come from, we evaluated the channel utilization.
Y axis shows channel utilization.
In X axis, there are multiple evaluation cases with different channel and rank count.
In each evaluation case, there are two bars, left one represent CPU channel and right one represents IO channel.
Each bar consists of two portions, bottom dark bar shows the fraction of execution time when both CPU and IO channel transfers data, and upper light bar shows the fraction of execution time when either CPU or IO channels transfers data.
Intuitively, our mechanism gets benefits only when transferring data in both channels (in dark bar).
We observe that similar trend of both channel utilization when varying memory channel and rank counts.
We conclude that simultaneous channel utilization leads to performance improvement.