## Slide 1: The Dirty-Block Index
Vivek Seshadri
Abhishek Bhowmick ∙ Onur Mutlu
Phillip B. Gibbons ∙ Michael A. Kozuch ∙ Todd C. Mowry
Today – 4:15PM – Session 3A
Notes: For any piece of information, if there is a mismatch in the way it is organized and they way it is queried, inefficiency creeps in.

## Slide 2
Mismatch: Representation and Query
A
B
C
Z
…
Sorted by Title
Get all the books written by author X
Notes: For example, sorting a set of books based on the title is a bad approach if we frequently query for books written by specific authors.

## Slide 3
Breadth First
Search
List all edges
adjacent to
vertex ‘a’
0 | 1 | 0 | 0 | 0
1 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 0 | 1
0 | 0 | 0 | 1 | 0
a
c
b
d
e
Mismatch: Representation and Query
Notes: Similarly, representing a graph as a adjacency matrix is bad if we frequently perform breadth first search on the graph.

## Slide 4
Tag
Tag
Tag
Tag
Tag
Tag
Tag
Tag
D
D
D
D
D
D
D
D
Cache Tag Store
Dirty Bit
Is block X
dirty?
List all dirty blocks of DRAM row R.
Mismatch: Representation and Query
Notes: In this work, we find that there is a similar mismatch in the way the dirty bit information is organized in existing caches and the way it is queried.

## Slide 5
Tag
Tag
Tag
Tag
Tag
Tag
Tag
Tag
Cache Tag Store
DBI
Dirty-Block Index
Is block X
dirty?
List all dirty blocks of DRAM row R.
Notes: We propose a new way of organizing the dirty bit information in a structure called the Dirty-block index.

## Slide 6
DBI
Many Optimizations
DRAM-aware writeback
Bypassing cache lookups
Reducing ECC overhead
Efficient cache flushing
Load balancing memory accesses
Bulk DMA
Efficient write scheduling
...
Notes: By eliminating the mismatch, our new organization enables simpler and more efficient implementations of several previously proposed optimizations.

## Slide 7
Many Optimizations
DRAM-aware writeback
Bypassing cache lookups
Reducing ECC overhead
Efficient cache flushing
Load balancing memory accesses
Bulk DMA
Efficient write scheduling
...
DBI
31% performance over baseline
6% over best previous mechanism
8% cache area reduction
Notes: With just three optimizations, our organization can improve performance by 31% compared to the baseline, 6% over the best previous mechanism while reducing overall cache area by 8% --- all with one structure.

## Slide 8: The Dirty-Block Index
Vivek Seshadri
Abhishek Bhowmick ∙ Onur Mutlu
Phillip B. Gibbons ∙ Michael A. Kozuch ∙ Todd C. Mowry
Today – 4:15PM – Session 3A
Notes: So what is this mismatch? How does DBI eliminate the mismatch? Attend my talk to find out the answers!