## Slide 1: The Dirty-Block Index
Vivek Seshadri
Abhishek Bhowmick ∙ Onur Mutlu
Phillip B. Gibbons ∙ Michael A. Kozuch ∙ Todd C. Mowry

## Slide 2: Summary
Problem: Dirty bit organization in caches does not match queries
  Inefficiency and performance loss
The Dirty-Block Index (DBI)
  Remove dirty bits from cache tag store
  DRAM row-oriented organization of dirty bits
Efficiently respond to queries
  Get all dirty blocks of a DRAM row; Is block B dirty?
Enables efficient implementation of many optimizations
  DRAM-aware writeback, bypassing cache lookup, reducing ECC cost, …
Improves performance while reducing overall cache area
  28% performance over baseline, 6% over state-of-the-art (8-core)
  8% cache area reduction

## Slide 3: Information: Organization and Query
Organization
Mismatch leads to inefficiency
Query
Get all the files belonging to males with first name starting with “Q”.
Get all files between 2013 and 2014.
?
?
?
?
?

## Slide 4: Mismatch between Organization and Query
A
B
C
Z
…
Sorted by title
Get all the books written by author X
Bad organization
for the query

## Slide 5: Metadata: Information About a Cache Block
Block Address
V
Valid Bit
D
Dirty Bit
(Writeback cache)
Sh
Sharing Status
(Multi-cores)
Error Correction
(Reliability)
ECC
Repl
Replacement Policy
(Set-associative cache)

## Slide 6: Block-Oriented Metadata Organization
Valid Bit
Dirty Bit
(Writeback cache)
Sharing Status
(Multi-cores)
Error Correction
(Reliability)
V
Block Address
D
Sh
Repl
ECC
Replacement Policy
(Set-associative cache)

## Slide 7: Block-Oriented Metadata Organization
V
Block Address
D
Sh
Repl
ECC
Cache
Tag Store
Tag Entry
 Simple to Implement
 Scalable
Any metadata query requires
an expensive tag store lookup
Is this the best organization?

## Slide 8: Block-Oriented Metadata Organization
V
Block Address
D
Sh
Repl
ECC
Cache
Tag Store
Tag Entry
 Simple to Implement
 Scalable
Any metadata query requires
an expensive tag store lookup
Is this the best organization?

## Slide 9: Focus of This Work
V
Block Address
D
Sh
Repl
ECC
Cache
Tag Store
Tag Entry
D
Dirty Bit
Is putting the dirty bit
in the tag entry
the best approach?
Queried by many operations
and optimizations

## Slide 10: Outline
Introduction
Shortcomings of Block-Oriented Organization
The Dirty-Block Index (DBI)
Optimizations Enabled by DBI
Evaluation
Conclusion

## Slide 11: DRAM-Aware Writeback
Last-Level Cache
Memory Controller
DRAM
Channel
Write Buffer
1. Buffer writes and flush them in a burst
2. Row buffer hits are faster and more efficient than row misses
Row Buffer
Virtual Write Queue [ISCA 2010], DRAM-Aware Writeback [TR-HPS-2010-2]

## Slide 12: DRAM-Aware Writeback
Dirty Block
Proactively write back
all other dirty blocks from
the same DRAM row
Last-Level Cache
Significantly increases the DRAM write row hit rate
Get all dirty blocks of DRAM row ‘R’
Memory Controller
R
R
R
R
R
Virtual Write Queue [ISCA 2010], DRAM-Aware Writeback [TR-HPS-2010-2]

## Slide 13: Shortcoming of Block-Oriented Organization
Get all dirty blocks of DRAM row ‘R’

## Slide 14: Shortcoming of Block-Oriented Organization
Get all dirty blocks of DRAM row ‘R’
Cache
Tag Store
Set of blocks co-located in DRAM
~8KB = 128 cache blocks
Is block 1 of Row R dirty?
Is block 2 of Row R dirty?
Is block 3 of Row R dirty?
Is block 128 of Row R dirty?
…

## Slide 15: Shortcoming of Block-Oriented Organization
Get all dirty blocks of DRAM row ‘R’
Cache
Tag Store
Requires many expensive
(possibly unnecessary) tag lookups
Significantly increases
tag store contention
Inefficient

## Slide 16: Many Cache Optimizations/Operations
DRAM-aware Writeback
Bulk DMA
Bypassing Cache Lookup
Load Balancing Memory Accesses
Cache Flushing
DRAM Write Scheduling
Metadata for Dirty Blocks

## Slide 17: Queries for the Dirty Bit Information
DRAM-aware Writeback
Bulk DMA
Bypassing Cache Lookup
Load Balancing Memory Accesses
Cache Flushing
DRAM Write Scheduling
Metadata for Dirty Blocks
Get all dirty blocks that belong to a coarse-grained region
Is block ‘B’ dirty?
Block-based dirty bit organization is inefficient for both queries

## Slide 18: Outline
Introduction
Shortcomings of Block-Oriented Organization
The Dirty-Block Index (DBI)
Optimizations Enabled by DBI
Evaluation
Conclusion

## Slide 19: The Dirty-Block Index
V
Block Address
Sh
Repl
ECC
Cache
Tag Store
Tag Entry
D
DBI
DRAM row-oriented organization
of dirty bits

## Slide 20: The Dirty-Block Index
V
Block Address
Sh
Repl
ECC
Cache
Tag Store
Tag Entry
DBI
D
D
D
D
Dirty bit vector
(one bit per block)
DRAM row address
V
DBI entry valid bit
DBI Entry

## Slide 21: DBI Semantics
A block in the cache is dirty if and only if
1. The DBI has a valid entry for the DRAM row
that contains the block, and
2. The dirty bit for the block in the bit vector
of the corresponding DBI entry is set

## Slide 22: DBI Semantics by Example
DBI
0
1
0
0
100
1
DBI entry valid bit
DBI Entry
Dirty Block
Even if it is present in the cache, it is not dirty.
DRAM row address
Dirty bit vector
(one bit per block)

## Slide 23: Benefits of DBI
Get all dirty blocks of DRAM row ‘R’
Is block ‘B’ dirty?
A single lookup to Row R in the DBI
DBI is faster than the tag store
Compared to 128 lookups with existing organization

## Slide 24: Outline
Introduction
Shortcomings of Block-Oriented Organization
The Dirty-Block Index (DBI)
Optimizations Enabled by DBI
Evaluation
Conclusion

## Slide 25: DRAM-Aware Writeback
1
Dirty Block
Proactively write back
all other dirty blocks from the same DRAM row
1
0
0
0
R
1
1
0
1
0
Look up the cache only for these blocks
Last-Level Cache
DBI
Virtual Write Queue [ISCA 2010], DRAM-Aware Writeback [TR-HPS-2010-2]
DBI achieves the benefit of DRAM-aware writeback without increasing contention for the tag store!

## Slide 26: Bypassing Cache Lookups
2
Cache
Tag Store
If an access is likely to miss, we can bypass the tag lookup!
Miss Predictor
Read
No
Yes
Forward to next level
Dirty Block
DBI
Yes
No
1. No false negatives
2. Write through
Mostly-No Monitors [HPCA 2003], SkipCache [PACT 2012]
Reduces access latency/energy; Reduces tag store contention
Not desirable
DBI seamlessly enables
simpler and more aggressive miss predictors!

## Slide 27: Reducing ECC Overhead
3
ECC-Cache [IAS 2009], Memory-mapped ECC [ISCA 2009], ECC-FIFO [SC 2009]
Dirty block – Requires error correction
Clean block – Requires only error detection
Dirty
Cache
ECC
EDC
ECC for dirty blocks in some other structure.
Complex mechanism to identify location of ECC.

## Slide 28: Reducing ECC Overhead
3
Cache
EDC
DBI
ECC
tracks far fewer blocks than
the cache!
DBI enables a simpler mechanism to reduce ECC cost.
8% reduction in overall cache area!
ECC-Cache [IAS 2009], Memory-mapped ECC [ISCA 2009], ECC-FIFO [SC 2009]
Dirty block – Requires error correction
Clean block – Requires only error detection

## Slide 29: DBI – Other Optimizations
Load balancing memory accesses in hybrid memory
Better DRAM write scheduling
Fast cache flushing
Bulk DMA coherence
…
(Discussed in paper)

## Slide 30: Outline
Introduction
Shortcomings of Block-Oriented Organization
The Dirty-Block Index (DBI)
Optimizations Enabled by DBI
Evaluation
Conclusion

## Slide 31: Evaluation Methodology
2.67 GHz, single issue, OoO, 128-entry instruction window
Cache Hierarchy
  32 KB private L1 cache, 256 KB private L2 cache
  2MB/core Shared L3 cache
DDR3-1066 DRAM
  1 channel, 1 rank, 8 banks, 8KB row buffer, FR-FCFS, open row policy
SPEC CPU2006, STREAM
Multi-core
  102 2-core, 259 4-core, and 120 8-core workloads
  Multiple metrics for performance and fairness

## Slide 32: Mechanisms
Dynamic Insertion Policy (Baseline) (ISCA 2007, PACT 2008)
DRAM-Aware Writeback (DAWB) (TR-HPS-2010-2 UT Austin)
Virtual Write Queue (ISCA 2010)
Skip Cache (PACT 2012)
Dirty-Block Index
  + No Optimization
  + Aggressive Writeback
  + Cache Lookup Bypass
  + Both Optimizations (DBI+Both)
Difficult to combine

## Slide 33: Effect on Writes and Tag Lookups
Chart: Normalized to Baseline
| Memory Writes | Write Row Hits | Tag Lookups
Baseline | 1 | 1 | 1
DAWB | 1.14 | 2.51 | 1.95
DBI
+AWB
+CLB
DBI+Both | 1.17 | 2.31 | 0.86
DBI achieves almost all the benefits of DAWB
with significantly lower tag store contention

## Slide 34: System Performance
Chart: System Performance
| 1-Core | 2-Core | 4-Core | 8-Core
Baseline | 1 | 1.46 | 1.8 | 2.62
DAWB | 1.13 | 1.73 | 2.29 | 3.17
DBI
+AWB
+CLB
DBI+Both | 1.13 | 1.8 | 2.43 | 3.36
13%
0%
23%
4%
35%
6%
28%
6%
Reduced tag store contention due to DBI
translates to significant performance improvement

## Slide 35: Other Results in Paper
Detailed cache area analysis (with and without ECC)
DBI power consumption analysis
Effect of individual optimizations
Other multi-core performance/fairness metrics
Sensitivity to DBI parameters
Sensitivity to cache size/replacement policy

## Slide 36: Conclusion
The Dirty-Block Index
  Key Idea: DRAM-row oriented dirty-bit organization
Enables efficient implementation of several optimizations
  DRAM-Aware writeback, cache lookup bypass, Reducing ECC cost
  28% performance over baseline, 6% over best previous work
  8% reduction in overall cache area
Wider applicability
  Can be applied to other caches
  Can be applied to other metadata (e.g., coherence)

## Slide 37: The Dirty-Block Index
Vivek Seshadri
Abhishek Bhowmick ∙ Onur Mutlu
Phillip B. Gibbons ∙ Michael A. Kozuch ∙ Todd C. Mowry

## Slide 38: Backup Slides

## Slide 39: Cache Coherence
M
O
E
S
I
Exclusive modified
Shared modified
Exclusive unmodified
Shared Unmodified
Invalid
D

## Slide 40: Operation of a Cache with DBI
Cache
Tag Store
DBI
1. Read Access
2. Writeback
3. Cache Eviction
4. DBI Eviction
Look up tag store
Update tag store. Update DBI to indicate the block is dirty.
Check DBI. Write back if block is dirty
Write back all blocks marked dirty by the entry

## Slide 41: DBI Design Parameters
DBI
1
0
0
0
R
1
1
0
1
0
DBI Size (α)
Total number of blocks tracked by the DBI
Represented as a fraction of number of blocks in cache
DBI Granularity (g)
Number of blocks tracked by each entry
Notes: R -> Row Addr

## Slide 42: DBI Design Parameters – Example
1MB Cache
64B Blocks
DBI
α = ¼
g = 64
Cache tracks 16384 blocks
DBI tracks 4096 blocks
Each entry tracks 64 blocks
DBI has 64 entries

## Slide 43: Effect on Writes and Tag Lookups
Chart: Normalized to Baseline
| Memory Writes | Write Row Hits | Tag Lookups
Baseline | 1 | 1 | 1
DAWB | 1.14 | 2.51 | 1.95
DBI | 1.16 | 2.11 | 1
+AWB | 1.17 | 2.31 | 1.2
+CLB | 1.16 | 2.14 | 0.62
+Both | 1.17 | 2.31 | 0.86

## Slide 44: System Performance
Chart: System Performance
| 1-Core | 2-Core | 4-Core | 8-Core
Baseline | 1 | 1.46 | 1.8 | 2.62
DAWB | 1.13 | 1.73 | 2.29 | 3.17
DBI | 1.11 | 1.75 | 2.33 | 3.23
+AWB | 1.13 | 1.77 | 2.36 | 3.27
+CLB | 1.11 | 1.79 | 2.39 | 3.3
+Both | 1.13 | 1.8 | 2.43 | 3.36
Notes: Percent improvement over baseline
Percent improvement over DAWB