## Slide 1: Evanesco: Architectural Support for Efficient Data Sanitization in Modern Flash-Based Storage Systems
Myungsuk Kim*, Jisung Park*, Geonhee Cho, Yoona Kim, Lois Orosa, Onur Mutlu, and Jihong Kim
Seoul National University
SAFARI Research Group, ETH Zürich
ASPLOS 2020
*M. Kim and J. Park equally contributed.

## Slide 2: Executive Summary
Motivation: Secure deletion is essential in storage systems as modern computing systems process a large amount of security-sensitive data.
Problem: It is challenging to support data sanitization in NAND flash-based SSDs.
  Erase-before-write property  no overwrite on stored data
  Physical data destruction  high performance & reliability overheads
Evanesco: A low-cost data-sanitization technique w/o reliability issues
  Uses on-chip access-control mechanisms instead of physically destroying data
  Manages access-permission (AP) flags inside a NAND flash chip
    Data is not accessible once the flash controller sets the data’s AP flag to disabled.
    An AP flag cannot be reset before erasing the corresponding data.
Results
  Provides the same level of reliability as an unmodified SSD (w/o data-sanitization support)
    Validated w/ 160 real state-of-the-art 3D NAND flash chips
  Significantly improves performance and lifetime over existing data-sanitization techniques
    Provides comparable (94.5%) performance with an unmodified SSD

## Slide 3: Outline
Secure Deletion in NAND Flash-Based SSDs
Evanesco: Lock-Based Data Sanitization
  pageLock: Page-Level Data Sanitization
  blockLock: Block-Level Data Sanitization
  SecureSSD: An Evanesco-Enabled SSD
Evaluation
Conclusion
Secure Deletion in NAND Flash-Based SSDs
Evanesco: Lock-Based Data Sanitization
  pageLock: Page-Level Data Sanitization
  blockLock: Block-Level Data Sanitization
  SecureSSD: An Evanesco-Enabled SSD
Evaluation
Conclusion

## Slide 4: Secure Deletion in Storage Systems
Security-sensitive data is increasing in modern storage systems.
Private Message
2003.12.03
Private Photo
Confidential Data (e.g., Medical Record)
Once a user deletes security-sensitive data,
a storage system should guarantee its irrecoverability

## Slide 5: Data Versioning Problem
Obsolete data in NAND flash-based solid-state drives (SSDs)
  Old versions of updated or deleted files can remain in the SSD for a long time.
Time (in disk writes)
1.25
2.5
3.75
0
Number of pages [103]
20
0
5
10
15
f: a heavily-updated DB file
# of valid pages of file f
# of invalid pages of file f
: running out of free space
Updated or deleted data of a file can remain in SSDs
due to unique features of NAND flash memory

## Slide 6: NAND Flash Memory Organization & Operations
NAND String
Page(s): Unit of read and program (e.g., 131,072 cells: 16-KiB page)
Block: Erase unit (e.g., 576 pages: 9-MiB block)
Erase-before-write: A block needs to be erased
before programming a page (i.e., no overwrite on a page)
1
…
BL0
1
0
0
1
BL1
…
0
1
0
0
BL2
…
1
1
1
1
BLn-1
…
0
0
0
…
Peripherals
(Page Buffer, Decoder, …)
Block#1
Block#2
…
Flash Cell
BitLine
Erased (1)
Programmed (0)

## Slide 7: NAND Flash-Based SSD
Flash-Based SSD
Chip#0
Chip#1
File System
CTRL
DRAM
NAND
NAND
0
1
2
3
4
5
6
7
8
…
0
1
2
3
Block#0
4
5
6
Page
7
Block#1
8
9
10
Block#2
12
13
14
15
Block#3
A0
A2
B1
A1
B0
B2
A0
A1
A2
B0
B
1
B2
Flash Controller
Flash Translation Layer (FTL)
Address translation
  Distributes host writes to fully exploit internal parallelism
  Out-of-place updates
   Logical-to-physical (L2P) mappings (e.g., LPA 1  PPA 8)
Garbage collection (GC)
  Reclaims free pages for future host writes
  Selects a victim block w/ the smallest number of valid pages
  Additional copy operations to move valid pages
   Page-status information (e.g., B0: invalid)
A1
B2’
Logical Page Address
Physical Page Address
A.png
B.db
A0
A1
A2
B
1
A0
A2
B1
A1
B0
B2
B0
B2
B2’
B0’
11
B0’
B2’
B0’
B2’
B2’
B0’
NAND
NAND
Logical block-device view
that supports overwrites
Update B0 and B2
GC Victim
Copy valid pages

## Slide 8: Data Deletion in NAND Flash-Based Storage Systems
Flash-Based SSD
Chip#0
Chip#1
File System
CTRL
DRAM
NAND
NAND
0
1
2
3
4
5
6
7
8
…
0
1
2
3
Block#0
4
5
6
7
Block#1
8
9
10
Block#2
12
13
14
15
Block#3
A0
A2
B1
Flash Controller
Flash Translation Layer (FTL)
A1
B2’
A.png
B.db
A0
A1
A2
B
1
A0
A2
B1
11
B0’
B0’
B2’
B0’
A.png
A0
A1
A2
LPA
PPA
0
0
L2P Mapping Table
Page Status Table
1
4
2
1
3
4
2
5
12
…
…
11
N/A
PPA
Status
0
valid
1
valid
2
valid
3
4
valid
5
…
…
15
free
N/A
N/A
N/A
A1
A0
A2
invalid
invalid
invalid
5
invalid
B
1’
N/A
N/A
N/A
A0
A2
A0
A1
A2
invalid
invalid
A1
invalid
B
1’
B1’
B1’
B1
B1
3
5
valid
invalid
free
Delete A
NAND
NAND
Update mapping & status
Update
status
Update
mapping
Out-of-place update
Update B1
A1
Invalid data remains in NAND flash chips
until GC erases the corresponding block(s)

## Slide 9: Security Vulnerability of NAND Flash-Based SSDs
ADVERSARY
Flash-Based SSD
Chip#0
Chip#1
File System
CTRL
DRAM
NAND
NAND
0
1
2
3
4
5
6
7
8
…
0
1
2
3
Block#0
4
5
6
7
Block#1
8
9
10
Block#2
12
13
14
15
Block#3
A0
A2
B1
Flash Controller
Flash Translation Layer (FTL)
A1
B2’
A.png
B.db
A0
A2
B1
11
B0’
B0’
B2’
B0’
A.png
LPA
PPA
0
0
L2P Mapping Table
Page Status Table
1
4
2
1
3
4
2
5
12
…
…
11
N/A
PPA
Status
0
valid
1
valid
2
valid
3
4
valid
5
…
…
15
free
N/A
N/A
N/A
A0
A2
invalid
invalid
invalid
5
invalid
N/A
N/A
N/A
A0
A1
A2
invalid
invalid
invalid
B
1’
B1’
B1’
B1
3
5
valid
invalid
free
A1
?
Direct access to SSD
No mappings
to invalid PPAs
NAND
NAND
Custom Flash Controller
Direct access
to raw NAND chips
Forensic Tool
A0
A1
A2
B1
De-solder
A.png
B.db
Entire Deleted File
Previous Ver. of Updated File
Deleted or updated files can be recovered by directly accessing raw NAND flash chips

## Slide 10: Existing Solution: Immediate Block Erasure
Immediately erases the block that stores data to be sanitized
  High performance and lifetime overheads due to Erase-before-write property
    Needs to copy all the valid pages stored in the same block
Target Block
576 Pages
Valid
Invalid
Free
Wasted
Hundreds of Copies:
Free Block
…
Target Page
…
Immediate block erasure:
High performance and lifetime overheads

## Slide 11: Existing Solution: Reprogramming the Page
Scrubbing [Wei+, FAST’2011]: Reprograms all the flash cells storing an invalid page
  Destroys the page data w/o block erasure
  Performance and lifetime overheads in Multi-level cell (MLC) NAND flash memory
    Needs to copy all the valid pages stored in the same flash cells
  Reliability issues: cell-to-cell interference
Target Block
Target Page
…
Cell-to-cell interference
Share
flash cells
Existing solutions incur
performance, lifetime, and reliability problems
in modern NAND flash memory
Valid
Invalid
Free
Scrubbed

## Slide 12: Outline
Secure Deletion in NAND Flash-Based SSDs
Evanesco: Lock-Based Data Sanitization
  pageLock: Page-Level Data Sanitization
  blockLock: Block-Level Data Sanitization
  SecureSSD: An Evanesco-Enabled SSD
Evaluation
Conclusion

## Slide 13: Evanesco: Access Control-Based Sanitization
Key idea: Allow a NAND flash chip to be aware of data validity
  Prevent access to invalid data at the chip level w/o destroying the data
     Low overhead: No copy operation to move valid pages stored in the same cells
     High reliability: No cell-to-cell interference to other valid pages
Two new NAND flash commands: pageLock (pLock) and blockLock (bLock)
  pLock: disables access to a page
  bLock: disables access to all the page in a block
read(2)
00…0
(all-zero data)
pLock(3)
bLock(0)
0
1
2
3
Block#0
4
5
6
7
Block#1
B0’
A0
A1
A2
NAND
B0
B0
E
E
E
E
E
E
E
E
D
D
D
D
Flags#1
Flags#0
EVANESCO!
YOU ARE
ALREADY VANISHED.
B0
A0
A1
A2
A0
A1
A2
E:Enabled, D:Disabled

## Slide 14: Outline
Secure Deletion in NAND Flash-Based SSDs
Evanesco: Lock-Based Data Sanitization
  pageLock: Page-Level Data Sanitization
  blockLock: Block-Level Data Sanitization
  SecureSSD: An Evanesco-Enabled SSD
Evaluation
Conclusion

## Slide 15: pLock: Page-Level Data Sanitization
Implements page access-permission (pAP) flags using spare cells
  A disabled page cannot be enabled until the entire block is erased.
  No additional command to access a pAP flag: read with the page data at the same time
Prevents transfer of data from a disabled page
  The bridge transistor disconnects the page buffer from the data-out circuitry.
Data Area
Spare Area
(for metadata)
Page Buffer
⋯
Page#1
Page#2
⋮
Page#N–1
Page#0
Block
Flash Cell
Erased (1)
Programmed (0)
Bitline (BL)
Flag Cell
Enabled (1)
Disabled (0)
Bridge Transistor
pLock(2)
Flag-cell programming
Read(2)
1
0
1
0
0
1
0
0: off (disconnect)
0000…000 (all-zero data)
Page Buffer
Data Out

## Slide 16: pLock: Implementation Details
Problem 1: Multiple pages are stored in the same flash cell.
  Solution: Use multiple flags for each row (e.g., 3 flags for triple-level cell (TLC) NAND)
Problem 2: A flag cell can misbehave  unintentional disabling or enabling of a page
  Solution: Use multiple flag cells for each pAP flag (k-modular redundancy scheme)
Reliability issues
1. Cell-to-cell interference b/w flag cells in the same NAND strings
2. Program disturbance due to high program voltage to the other cells at the same row
Solutions
1. Use flag cells in single-level cell (SLC) mode
- More robust to interference and disturbance
- Reduces pLock latency
2. One-shot programming w/ low voltage
- Reduces interference and disturbance
Data Out
Bridge Transistor
Data Cells
MSB
CSB
LSB
pAP Flags
Majority Circuit
k
BLn-1
BLn+2k
BLn
BLn+k
BLn+3k-1
LSB
0
CSB
1
MSB
2
LSB
3
Block#k
4
5
⋮
Page Buffer
CSB
MSB
⋮
No cell-to-cell interference
AP Flag Selector
k
LSB
pLock: Prevents data transfer for a disabled page
 Reliable and copy-free per-page sanitization

## Slide 17: Outline
Secure Deletion in NAND Flash-Based SSDs
Evanesco: Lock-Based Data Sanitization
  pageLock: Page-Level Data Sanitization
  blockLock: Block-Level Data Sanitization
  SecureSSD: An Evanesco-Enabled SSD
Evaluation
Conclusion

## Slide 18: Problem with Page-Level Sanitization
Nontrivial performance overhead in invalidating an entire block
  Deleting a 1-GiB video  65,536 pLock operations (page size = 16 KiB)
  Invalidating blocks in SSD management tasks (GC, wear-leveling, …)
Immediate block erasure is not feasible in 3D NAND flash memory.
  Open-block problem: Reliability degradation due to a long time interval b/w erasing and programming a block  A block should be erased lazily.
Chart: 
| 0 | 0.5 | 1 | 2 | 3 | 5
 | 1 | 1.01 | 1.015 | 1.03 | 1.05 | 1.06
 | 1 | 1.02 | 1.05 | 1.09 | 1.16 | 1.2
 | 1 | 1.06 | 1.14 | 1.23 | 1.29 | 1.34
Length of open interval
Zero
Very short
Short
Medium
Long
Very long
Normalized RBER
(Raw Bit Error Rate)
No P/E cycling
After P/E cycling
After P/E cycling + retention

## Slide 19: bLock: Block-Level Sanitization
Vref
(activate)
VCC
(activate)
Key idea: Program the string-select line (SSL) of a block
  3D NAND flash memory implements an SSL using flash cells.
  SSL programming: Disconnects all the pages from bitlines (i.e., from the page buffer)
Block#k
BL0
BLn-1
SSL#0
SSL#k
SSL#N
No voltage
(deactivate)
No voltage
(deactivate)
bLock(k)
⋮
⋮
SSL programming
Disconnected from BLs
Block#0
Block#N-1
BL0
BLn-1
Data Out
Page Buffer
0
0
0
0
0
0
0
0
All-zero data
Cannot activate
w/ normal voltage
0
0
1
0
1
1
0
1
page read
 No current through strings
Flash Cell
bLock: Programs the SSL of block
Disconnects all the pages from bitlines
until the block is physically erased

## Slide 20: Outline
Secure Deletion in NAND Flash-Based SSDs
Evanesco: Lock-Based Data Sanitization
  pageLock: Page-Level Data Sanitization
  blockLock: Block-Level Data Sanitization
  SecureSSD: An Evanesco-Enabled SSD
Evaluation
Conclusion

## Slide 21: SecureSSD: An Evanesco-Enabled SSD
⋮
Block#m
Multiple invalid pages +
no valid pages in the block
⋮
Block#k
Valid
Invalid
An SSD that supports immediate data sanitization of updated or deleted data
  Lock manager issues pLock and bLock commands depending on the block’s status.
Delete A
Trim (discard) LPAs
bLock
pLock
File System
A.png
B.doc
Application
SecureSSD
Evanesco-Aware FTL
L2P
Mapping
Table
Page
Status
Table
Lock
Manager
Flash Chip
Flash Chip
Flash Chip
A.png
B.doc
pLock
bLock
⋯
A.png
A.png
Lock
Manager

## Slide 22: SecureSSD: Selective Data Sanitization
SecureSSD avoids unnecessary pLock and bLock for security-insensitive data.
  A user sets the security requirements of written data w/ extended I/O interfaces.
Delete B
Trim (discard) LPAs
File System
A.png
B.doc
Application
SecureSSD
Evanesco-Aware FTL
L2P
Mapping
Table
Page
Status
Table
Lock
Manager
Flash Chip
Flash Chip
Flash Chip
A.png
B.doc
⋯
A.png
A.png
Extended
PG Status
Table
fd = open(“B.doc”, O_CREATE|O_INSEC);
// create security-insensitive file B.doc
bio->bi_of =| REQ_OP_INSEC_WRITE;
// set low security requirement
Set page status to INSECURE
B.doc
Invalidation w/o pLock or bLock
SecureSSD minimizes data-sanitization overheads

## Slide 23: Outline
Secure Deletion in NAND Flash-Based SSDs
Evanesco: Lock-Based Data Sanitization
  pageLock: Page-Level Data Sanitization
  blockLock: Block-Level Data Sanitization
  SecureSSD: An Evanesco-Enabled SSD
Evaluation
Conclusion

## Slide 24: Methodology
Design space exploration for pLock and bLock
  Using 160 real state-of-the-art 3D triple-level-cell (TLC) NAND flash chips
  To find the best operation parameters w/o reliability degradation
    pLock: 100-us latency w/ 9 flag cells per page
    bLock: 300-us latency
    tREAD = 100 us, tPROG = 700 us, tBERS = 3.5 ms
Simulator: Open SSD-development platform (FlashBench [Lee+, RSP’2012])
  32-GiB storage capacity
  576 pages per block
  16-KiB page size
Compared SSDs
  erSSD: Erases the entire block after copying valid pages in the block
  scrSSD: Performs scrubbing after copying valid pages in the same cells [Wei+, FAST’2011]
Workloads
  Three server workloads: MailServer, DBServer, FileServer
  Mobile workload collected from an Android smartphone (Samsung Galaxy S2)

## Slide 25: Results: Performance
Normalized IOPS
Chart: 
| MailServer | DBServer | FileServer | Mobile
erSSD | 0.0040514 | 0.0037037 | 0.0006891 | 0.034454
scrSSD | 0.44049 | 0.20679 | 0.20397 | 0.56471
secSSD | 0.9803 | 0.89198 | 0.96164 | 0.95462
erSSD
scrSSD
secSSD
SecureSSD significantly reduces performance overhead of data sanitization (11% slowdown at most)
0.98
0.96
0.95
0.89
0.004
0.003
0.0007
0.034
0.44
0.21
0.2
0.56

## Slide 26: Results: Lifetime
Normalized WAF
Chart: 
| MailServer | DBServer | FileServer | Mobile
erSSD | 184.9203 | 285.3769 | 254.4159 | 320.159
scrSSD | 2.9415 | 3.3282 | 4.4166 | 1.4928
secSSD | 0.99777 | 1.0006 | 1.0045 | 1.0066
erSSD
scrSSD
secSSD
No additional copy in SecureSSD: No lifetime overhead
Write Amplification Factor
184.9
285.3
245.4
320.2
2.9
3.3
4.4
1.5

## Slide 27: Results: Effect of Selective Data Sanitization
Normalized IOPS
Chart: 
| MailServer | DBServer | FileServer | Mobile
60% | 0.98591 | 0.93812 | 0.97496 | 0.9923
70% | 0.98176 | 0.92964 | 0.97084 | 0.9858
80% | 0.97763 | 0.91449 | 0.96757 | 0.97487
90% | 0.97695 | 0.90511 | 0.96432 | 0.96148
100% | 0.973 | 0.89198 | 0.9589 | 0.95462
Selective data sanitization minimizes performance overheads
(6% slowdown at most with 60% security-sensitive data)
0.99
0.97
0.94
0.89
0.97
0.96
0.99
0.95

## Slide 28: Other Analyses in the Paper
Empirical Study on Invalid Data in SSDs
Reliability Issues in Physical Data Destruction
Design Space Exploration for pLock and bLock
Effectiveness of bLock command

## Slide 29: Outline
Secure Deletion in NAND Flash-Based SSDs
Evanesco: Lock-Based Data Sanitization
  pageLock: Page-Level Data Sanitization
  blockLock: Block-Level Data Sanitization
  SecureSSD: An Evanesco-Enabled SSD
Evaluation
Conclusion

## Slide 30: Conclusion
Challenges of data sanitization in NAND flash-based SSDs:
  Erase-before-write property  no overwrite on stored data
  Physical data destruction  high performance & reliability overheads
Evanesco: Uses on-chip access-control mechanisms
  pLock: Page-level data sanitization
    Implements the access-permission flag of each page using spare cells
  bLock: Block-level data sanitization
    Programs the SSL of a block to disconnect all pages
  SecureSSD: An Evanesco-Enabled SSD
    Supports selective data sanitization to reduce performance overheads
Results
  Provides the same level of reliability of an unmodified SSD
    Validated w/ 160 real state-of-the-art 3D NAND flash chips
  Significantly improves performance and lifetime over existing data-sanitization techniques
    Provides comparable (94.5%) performance with an unmodified SSD

## Slide 31: Evanesco: Architectural Support for Efficient Data Sanitization in Modern Flash-Based Storage Systems
Myungsuk Kim*, Jisung Park*, Geonhee Cho, Yoona Kim, Lois Orosa, Onur Mutlu, and Jihong Kim
Seoul National University
SAFARI Research Group, ETH Zürich
ASPLOS 2020
*M. Kim and J. Park equally contributed.