## Slide 1: MinBD: Minimally-Buffered Deflection Routing for Energy-Efficient Interconnect
Chris Fallin, Greg Nazario, Xiangyao Yu*, Kevin Chang, Rachata Ausavarungnirun, Onur Mutlu
Carnegie Mellon University
*CMU and Tsinghua University

## Slide 2: Motivation
In many-core chips, on-chip interconnect (NoC) consumes significant power
  Intel Terascale: ~28% of chip power
  Intel SCC: ~10%
  MIT RAW: ~36%
Recent work1 uses bufferless deflection routing to reduce power and die area
Core
L1
L2 Slice
Router
1Moscibroda and Mutlu, “A Case for Bufferless Deflection Routing in On-Chip Networks.” ISCA 2009.

## Slide 3: Bufferless Deflection Routing
Key idea: Packets are never buffered in the network. When two packets contend for the same link, one is deflected.
Removing buffers yields significant benefits
  Reduces power (CHIPPER: reduces NoC power by 55%)
  Reduces die area (CHIPPER: reduces NoC area by 36%)
But, at high network utilization (load), bufferless deflection routing causes unnecessary link & router traversals
  Reduces network throughput and application performance
  Increases dynamic power
Goal: Improve high-load performance of low-cost deflection networks by reducing the deflection rate.

## Slide 4: Outline: This Talk
Motivation
Background: Bufferless Deflection Routing
MinBD: Reducing Deflections
  Addressing Link Contention
  Addressing the Ejection Bottleneck
  Improving Deflection Arbitration
Results
Conclusions

## Slide 5: Outline: This Talk
Motivation
Background: Bufferless Deflection Routing
MinBD: Reducing Deflections
  Addressing Link Contention
  Addressing the Ejection Bottleneck
  Improving Deflection Arbitration
Results
Conclusions

## Slide 6: Bufferless Deflection Routing
Destination
Key idea: Packets are never buffered in the network. When two packets contend for the same link, one is deflected.1
1Baran, “On Distributed Communication Networks.” RAND Tech. Report., 1962 / IEEE Trans.Comm., 1964.

## Slide 7: Bufferless Deflection Routing
Input buffers are eliminated: flits are buffered in pipeline latches and on network links
North
South
East
West
Local
North
South
East
West
Local
Deflection Routing Logic
Input Buffers

## Slide 8: Deflection Router Microarchitecture
Inject/Eject
Reassembly
Buffers
Inject
Eject
Stage 1: Ejection and injection of local traffic
Stage 2: Deflection arbitration
Fallin et al., “CHIPPER: A Low-complexity Bufferless Deflection Router”, HPCA 2011.

## Slide 9: Issues in Bufferless Deflection Routing
Correctness: Deliver all packets without livelock
  CHIPPER1: Golden Packet
  Globally prioritize one packet until delivered
Correctness: Reassemble packets without deadlock
  CHIPPER1: Retransmit-Once
Performance: Avoid performance degradation at high load
  MinBD
1 Fallin et al., “CHIPPER: A Low-complexity Bufferless Deflection Router”, HPCA 2011.

## Slide 10: Key Performance Issues
1. Link contention: no buffers to hold traffic  any link contention causes a deflection
 use side buffers
2. Ejection bottleneck: only one flit can eject per router per cycle  simultaneous arrival causes deflection
 eject up to 2 flits/cycle
3. Deflection arbitration: practical (fast) deflection arbiters deflect unnecessarily
 new priority scheme (silver flit)

## Slide 11: Outline: This Talk
Motivation
Background: Bufferless Deflection Routing
MinBD: Reducing Deflections
  Addressing Link Contention
  Addressing the Ejection Bottleneck
  Improving Deflection Arbitration
Results
Conclusions

## Slide 12: Outline: This Talk
Motivation
Background: Bufferless Deflection Routing
MinBD: Reducing Deflections
  Addressing Link Contention
  Addressing the Ejection Bottleneck
  Improving Deflection Arbitration
Results
Conclusions

## Slide 13: Addressing Link Contention
Problem 1: Any link contention causes a deflection
Buffering a flit can avoid deflection on contention
But, input buffers are expensive:
  All flits are buffered on every hop  high dynamic energy
  Large buffers necessary  high static energy and large area
Key Idea 1: add a small buffer to a bufferless deflection router to buffer only flits that would have been deflected

## Slide 14: How to Buffer Deflected Flits
Baseline Router
Eject
Inject
1 Fallin et al., “CHIPPER: A Low-complexity Bufferless Deflection Router”, HPCA 2011.
Destination
Destination
DEFLECTED

## Slide 15: How to Buffer Deflected Flits
Side-Buffered Router
Eject
Inject
Step 1. Remove up to one deflected flit per cycle from the outputs.
Step 2. Buffer this flit in a small FIFO “side buffer.”
Step 3. Re-inject this flit into pipeline when a slot is available.
Side Buffer
Destination
Destination
DEFLECTED

## Slide 16: Why Could A Side Buffer Work Well?
Buffer some flits and deflect other flits at per-flit level
  Relative to bufferless routers, deflection rate reduces (need not deflect all contending flits)
   4-flit buffer reduces deflection rate by 39%
  Relative to buffered routers, buffer is more efficiently used (need not buffer all flits)
     similar performance with 25% of buffer space

## Slide 17: Outline: This Talk
Motivation
Background: Bufferless Deflection Routing
MinBD: Reducing Deflections
  Addressing Link Contention
  Addressing the Ejection Bottleneck
  Improving Deflection Arbitration
Results
Conclusions

## Slide 18: Addressing the Ejection Bottleneck
Problem 2: Flits deflect unnecessarily because only one flit can eject per router per cycle
In 20% of all ejections, ≥ 2 flits could have ejected  all but one flit must deflect and try again
 these deflected flits cause additional contention
Ejection width of 2 flits/cycle reduces deflection rate 21%
Key idea 2: Reduce deflections due to a single-flit ejection port by allowing two flits to eject per cycle

## Slide 19: Addressing the Ejection Bottleneck
Single-Width Ejection
Eject
Inject
DEFLECTED

## Slide 20: Addressing the Ejection Bottleneck
Dual-Width Ejection
Eject
Inject
For fair comparison, baseline routers have dual-width ejection for perf. (not power/area)

## Slide 21: Outline: This Talk
Motivation
Background: Bufferless Deflection Routing
MinBD: Reducing Deflections
  Addressing Link Contention
  Addressing the Ejection Bottleneck
  Improving Deflection Arbitration
Results
Conclusions

## Slide 22: Improving Deflection Arbitration
Problem 3: Deflections occur unnecessarily because fast arbiters must use simple priority schemes
Age-based priorities (several past works): full priority order gives fewer deflections, but requires slow arbiters
State-of-the-art deflection arbitration (Golden Packet & two-stage permutation network)
  Prioritize one packet globally (ensure forward progress)
  Arbitrate other flits randomly (fast critical path)
Random common case leads to uncoordinated arbitration

## Slide 23: Fast Deflection Routing Implementation
Let’s route in a two-input router first:
Step 1: pick a “winning” flit (Golden Packet, else random)
Step 2: steer the winning flit to its desired output
and deflect other flit
   Highest-priority flit always routes to destination

## Slide 24: Fast Deflection Routing with Four Inputs
Each block makes decisions independently
  Deflection is a distributed decision
N
E
S
W
N
S
E
W

## Slide 25: Unnecessary Deflections in Fast Arbiters
How does lack of coordination cause unnecessary deflections?
  1. No flit is golden (pseudorandom arbitration)
  2. Red flit wins at first stage
  3. Green flit loses at first stage (must be deflected now)
  4. Red flit loses at second stage; Red and Green are deflected
Destination
Destination
all flits have
equal priority
unnecessary
deflection!

## Slide 26: Improving Deflection Arbitration
Key idea 3: Add a priority level and prioritize one flit to ensure at least one flit is not deflected in each cycle
Highest priority: one Golden Packet in network
  Chosen in static round-robin schedule
  Ensures correctness
Next-highest priority: one silver flit per router per cycle
  Chosen pseudo-randomly & local to one router
  Enhances performance

## Slide 27: Adding A Silver Flit
Randomly picking a silver flit ensures one flit is not deflected
  1. No flit is golden but Red flit is silver
  2. Red flit wins at first stage (silver)
  3. Green flit is deflected at first stage
  4. Red flit wins at second stage (silver); not deflected
Destination
Destination
At least one flit
is not deflected
red flit has
higher priority
all flits have
equal priority

## Slide 28: Minimally-Buffered Deflection Router
Eject
Inject
Problem 1: Link Contention
Solution 1: Side Buffer
Problem 2: Ejection Bottleneck
Solution 2: Dual-Width Ejection
Problem 3: Unnecessary Deflections
Solution 3: Two-level priority scheme

## Slide 29: Outline: This Talk
Motivation
Background: Bufferless Deflection Routing
MinBD: Reducing Deflections
  Addressing Link Contention
  Addressing the Ejection Bottleneck
  Improving Deflection Arbitration

## Slide 30: Outline: This Talk
Motivation
Background: Bufferless Deflection Routing
MinBD: Reducing Deflections
  Addressing Link Contention
  Addressing the Ejection Bottleneck
  Improving Deflection Arbitration
Results
Conclusions

## Slide 31: Methodology: Simulated System
Chip Multiprocessor Simulation
  64-core and 16-core models
  Closed-loop core/cache/NoC cycle-level model
  Directory cache coherence protocol (SGI Origin-based)
  64KB L1, perfect L2 (stresses interconnect), XOR-mapping
  Performance metric: Weighted Speedup (similar conclusions from network-level latency)
  Workloads: multiprogrammed SPEC CPU2006
    75 randomly-chosen workloads
    Binned into network-load categories by average injection rate

## Slide 32: Methodology: Routers and Network
Input-buffered virtual-channel router
  8 VCs, 8 flits/VC [Buffered(8,8)]: large buffered router
  4 VCs, 4 flits/VC [Buffered(4,4)]: typical buffered router
  4 VCs, 1 flit/VC [Buffered(4,1)]: smallest deadlock-free router
  All power-of-2 buffer sizes up to (8, 8) for perf/power sweep
Bufferless deflection router: CHIPPER1
Bufferless-buffered hybrid router: AFC2
  Has input buffers and deflection routing logic
  Performs coarse-grained (multi-cycle) mode switching
Common parameters
  2-cycle router latency, 1-cycle link latency
  2D-mesh topology (16-node: 4x4; 64-node: 8x8)
  Dual ejection assumed for baseline routers (for perf. only)
1Fallin et al., “CHIPPER: A Low-complexity Bufferless Deflection Router”, HPCA 2011.
2Jafri et al., “Adaptive Flow Control for Robust Performance and Energy”, MICRO 2010.

## Slide 33: Methodology: Power, Die Area, Crit. Path
Hardware modeling
  Verilog models for CHIPPER, MinBD, buffered control logic
    Synthesized with commercial 65nm library
  ORION 2.0 for datapath: crossbar, muxes, buffers and links
Power
  Static and dynamic power from hardware models
  Based on event counts in cycle-accurate simulations
  Broken down into buffer, link, other

## Slide 34: Reduced Deflections & Improved Perf.
Deflection
Chart: Weighted Speedup
| AVG
Baseline | 13.3104
B (Side-Buf) | 12.7312
D (Dual-Eject) | 13.8075
S (Silver Flits) | 13.402
B+D | 14.0867
B+S+D (MinBD) | 14.1847
Rate
28%
17%
22%
27%
11%
10%
All mechanisms individually reduce deflections
2. Side buffer alone is not sufficient for performance (ejection bottleneck remains)
3. Overall, 5.8% over baseline, 2.7% over dual-eject by reducing deflections 64% / 54%
5.8%
2.7%

## Slide 35: Overall Performance Results
Chart: Injection Rate
| 0.0 - 0.15 | 0.15 - 0.30 | 0.30 - 0.40 | 0.40 - 0.50 | > 0.50 | AVG
Buffered (8,8) | 16.0051 | 15.8617 | 15.1919 | 14.2118 | 11.8768 | 14.6295
Buffered (4,4) | 16.0049 | 15.8602 | 15.1612 | 14.1471 | 11.7073 | 14.5761
Buffered (4,1) | 15.9983 | 15.8027 | 14.8748 | 13.5043 | 10.4798 | 14.132
CHIPPER | 15.9451 | 15.4841 | 14.5144 | 13.1601 | 9.9339 | 13.8075
AFC (4,4) | 15.9907 | 15.8249 | 15.1374 | 14.1132 | 10.872 | 14.3876
MinBD-4 | 15.919 | 15.5898 | 14.893 | 13.7518 | 10.7399 | 14.1787
Improves 2.7% over CHIPPER (8.1% at high load)
Similar perf. to Buffered (4,1) @ 25% of buffering space
2.7%
8.1%
2.7%
8.3%
Within 2.7% of Buffered (4,4) (8.3% at high load)

## Slide 36: Overall Power Results
Chart: Network Power (W)
| Buffered (8,8) | Buffered (4,4) | Buffered (4,1) | CHIPPER | AFC(4,4) | MinBD-4
static | 1.6291 | 1.047 | 0.74594 | 0.52767 | 0.86902 | 0.55326
dynamic | 0.92052 | 0.79869 | 0.70841 | 0.92607 | 0.84745 | 0.70553
Chart: Network Power (W)
| Buffered (8,8) | Buffered (4,4) | Buffered (4,1) | CHIPPER | AFC(4,4) | MinBD-4
buffer | 1.0994 | 0.40037 | 0.04931 | 0 | 0.24432 | 0.023553
non-buffer | 1.4502 | 1.4453 | 1.405 | 1.4537 | 1.4721 | 1.2352
Chart: Network Power (W)
| Buffered (8,8) | Buffered (4,4) | Buffered (4,1) | CHIPPER | AFC(4,4) | MinBD-4
static buffer | 0.91433 | 0.3323 | 0.031218 | 0 | 0.13325 | 0.020768
static link | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115
static other | 0.60323 | 0.60323 | 0.60323 | 0.41617 | 0.62427 | 0.42099
dynamic buffer | 0.18502 | 0.068074 | 0.018092 | 0 | 0.11107 | 0.0027846
dynamic link | 0.59769 | 0.59372 | 0.56097 | 0.71132 | 0.59769 | 0.53927
dynamic other | 0.13782 | 0.1369 | 0.12935 | 0.21475 | 0.13869 | 0.16348
Buffers are significant fraction of power in baseline routers
Buffer power is much smaller in MinBD (4-flit buffer)
Dynamic power increases with deflection routing
Dynamic power reduces in MinBD relative to CHIPPER

## Slide 37: Performance-Power Spectrum
Chart: Network Power (W)
| 2.549584000000001 | 2.248441 | 2.085126000000001 | 1.522975 | 2.000121000000003 | 1.845714 | 1.753193 | 1.454351 | 1.723579 | 1.637617 | 1.57499 | 1.401160999999999 | 1.578871 | 1.463406 | 1.520311 | 1.344364
 | 14.6295 | 14.612 | 14.5288 | 14.3117 | 14.6259 | 14.5761 | 14.4304 | 14.132 | 14.6045 | 14.4883 | 14.247 | 13.8303 | 14.523 | 13.9062 | 14.304 | 13.3269
 | 14.3876
 | 13.8075
 | 14.1787
Most energy-efficient (perf/watt) of any evaluated network router design
Buf (4,4)
Buf (4,1)
More Perf/Power
Less Perf/Power
Buf (8,8)
AFC
CHIPPER
MinBD

## Slide 38: Die Area and Critical Path
Chart: Normalized Die Area
| Buffered (8,8) | Buffered (4,4) | Buffered (4,1) | CHIPPER | MinBD
Area | 2.06 | 1.69 | 1.6 | 1 | 1.03
Chart: Normalized Critical Path
| Buffered (8,8) | Buffered (4,4) | Buffered (4,1) | CHIPPER | MinBD
Critical Path | 0.99 | 0.99 | 0.99 | 1 | 1.07
Only 3% area increase over CHIPPER (4-flit buffer)
Reduces area by 36% from Buffered (4,4)
Increases by 7% over CHIPPER, 8% over Buffered (4,4)
+3%
-36%
+7%
+8%

## Slide 39: Conclusions
Bufferless deflection routing offers reduced power & area
But, high deflection rate hurts performance at high load
MinBD (Minimally-Buffered Deflection Router) introduces:
  Side buffer to hold only flits that would have been deflected
  Dual-width ejection to address ejection bottleneck
  Two-level prioritization to avoid unnecessary deflections
MinBD yields reduced power (31%) & reduced area (36%) relative to buffered routers
MinBD yields improved performance (8.1% at high load) relative to bufferless routers  closes half of perf. gap
MinBD has the best energy efficiency of all evaluated designs with competitive performance

## Slide 40: Thank You!

## Slide 41: MinBD: Minimally-Buffered Deflection Routing for Energy-Efficient Interconnect
Chris Fallin, Greg Nazario, Xiangyao Yu*, Kevin Chang, Rachata Ausavarungnirun, Onur Mutlu
Carnegie Mellon University
*CMU and Tsinghua University

## Slide 42: Backup Slides

## Slide 43: Correctness: Golden Packet
The Golden Packet is always prioritized long enough to be delivered (hop latency * (max # hops + serialization delay))
  “Epoch length”: e.g. 4x4: 3 * (7 + 7) = 42 cycles (pick 64 cyc)
Golden Packet rotates statically through all packet IDs
  E.g. 4x4: 16 senders, 16 transactions/sender  256 choices
Max latency is GP epoch * # packet IDs
  E.g., 64*256 = 16K cycles
Flits in Golden Packet are arbitrated by sequence # (total order)

## Slide 44: Correctness: Retransmit-Once
Finite reassembly buffer size may lead to buffer exhaustion
What if a flit arrives from a new packet and no buffer is free?
Answer 1: Refuse ejection and deflect  deadlock!
Answer 2: Use large buffers  impractical
Retransmit-Once (past work): operate opportunistically & assume available buffers
  If no buffer space, drop packet (once) and note its ID
  Later, reserve buffer space and retransmit (once)
End-to-end flow control provides correct endpoint operation without in-network backpressure

## Slide 45: Correctness: Side Buffer
Golden Packet ensures delivery as long as flits keep moving
What if flits get “stuck” in a side buffer?
Answer: buffer redirection
  If buffered flit cannot re-inject after Cthreshold cycles, then:
  1. Force one input flit per cycle into buffer (random choice)
  2. Re-inject buffered flit into resulting empty slot in network
If a flit is golden, it will never enter a side buffer
If a flit becomes golden while buffered, redirection will rescue it after Cthreshold * BufferSize (e.g.: 2 * 4 = 8 cyc)
Extend Golden epoch to account for this

## Slide 46: Why does Side Buffer Alone Lose Perf.?
Adding a side buffer reduces deflection rate
  Raw network throughput increases
But ejection is still the system bottleneck
  Ejection rate remains nearly constant
Side buffers are utilized  more traffic in flight
Hence, latency increases (Little’s Law): ~10%

## Slide 47: Overall Power Results
Chart: Network Power (W)
| Buf(8,8) | Buf(4,4) | Buf(4,1) | CHIPPER | AFC(4,4) | MinBD-4 | Buf(8,8) | Buf(4,4) | Buf(4,1) | CHIPPER | AFC(4,4) | MinBD-4 | Buf(8,8) | Buf(4,4) | Buf(4,1) | CHIPPER | AFC(4,4) | MinBD-4 | Buf(8,8) | Buf(4,4) | Buf(4,1) | CHIPPER | AFC(4,4) | MinBD-4 | Buf(8,8) | Buf(4,4) | Buf(4,1) | CHIPPER | AFC(4,4) | MinBD-4 | Buf(8,8) | Buf(4,4) | Buf(4,1) | CHIPPER | AFC(4,4) | MinBD-4
static buffer | 0.91433 | 0.3323 | 0.031218 | 0 | 0.0050791 | 0.020768 | 0.91433 | 0.3323 | 0.031218 | 0 | 0.036222 | 0.020768 | 0.91433 | 0.3323 | 0.031218 | 0 | 0.14399 | 0.020768 | 0.91433 | 0.3323 | 0.031218 | 0 | 0.21283 | 0.020768 | 0.91433 | 0.3323 | 0.031218 | 0 | 0.26813 | 0.020768 | 0.91433 | 0.3323 | 0.031218 | 0 | 0.13325 | 0.020768
static link | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115 | 0.1115
static other | 0.60323 | 0.60323 | 0.60323 | 0.41617 | 0.62427 | 0.42099 | 0.60323 | 0.60323 | 0.60323 | 0.41617 | 0.62427 | 0.42099 | 0.60323 | 0.60323 | 0.60323 | 0.41617 | 0.62427 | 0.42099 | 0.60323 | 0.60323 | 0.60323 | 0.41617 | 0.62427 | 0.42099 | 0.60323 | 0.60323 | 0.60323 | 0.41617 | 0.62427 | 0.42099 | 0.60323 | 0.60323 | 0.60323 | 0.41617 | 0.62427 | 0.42099
dynamic buffer | 0.0090543 | 0.0032847 | 0.0012275 | 0 | 0.0011914 | 0.00017472 | 0.050803 | 0.018461 | 0.006483 | 0 | 0.015529 | 0.00089341 | 0.1705 | 0.063334 | 0.018805 | 0 | 0.10077 | 0.0027897 | 0.27505 | 0.10177 | 0.027342 | 0 | 0.17978 | 0.0042221 | 0.41969 | 0.15352 | 0.0366 | 0 | 0.25808 | 0.0058433 | 0.18502 | 0.068074 | 0.018092 | 0 | 0.11107 | 0.0027846
dynamic link | 0.11833 | 0.11833 | 0.11808 | 0.097674 | 0.12465 | 0.090063 | 0.3901 | 0.39005 | 0.38812 | 0.3488 | 0.41631 | 0.30623 | 0.65875 | 0.65674 | 0.6358 | 0.71217 | 0.68658 | 0.57357 | 0.81622 | 0.81152 | 0.76467 | 1.007 | 0.83146 | 0.76111 | 1.005 | 0.99196 | 0.89817 | 1.391 | 0.92943 | 0.96537 | 0.59769 | 0.59372 | 0.56097 | 0.71132 | 0.59769 | 0.53927
dynamic other | 0.027285 | 0.027284 | 0.027228 | 0.029488 | 0.029141 | 0.027303 | 0.089949 | 0.089938 | 0.089493 | 0.1053 | 0.097209 | 0.092834 | 0.15189 | 0.15143 | 0.1466 | 0.21501 | 0.15958 | 0.17388 | 0.1882 | 0.18712 | 0.17632 | 0.304 | 0.19269 | 0.23073 | 0.23174 | 0.22873 | 0.2071 | 0.41995 | 0.21484 | 0.29266 | 0.13782 | 0.1369 | 0.12935 | 0.21475 | 0.13869 | 0.16348
0.00 – 0.15
0.15 – 0.30
0.30 – 0.40
0.40 – 0.50
> 0.50
AVG

## Slide 48: MinBD vs. AFC
AFC:
  Combines input buffers and deflection routing
  In a given cycle, all link contention is handled by buffers or by deflection (global router mode)
  Mode-switch is heavyweight (drain input buffers) and takes multiple cycles
  Router has area footprint of buffered + bufferless, but could save power with power-gating (assumed in Jafri et al.)
  Better performance at highest loads (equal to buffered)
MinBD:
  Combines deflection routing with a side buffer
  In a given cycle, some flits are buffered, some are deflected
  Smaller router and no mode switching
  But, loses some performance at highest load

## Slide 49: Related Work
Baran, 1964
  Original “hot potato” (deflection) routing
BLESS (Moscibroda and Mutlu, ISCA 2009)
  Earlier bufferless deflection router
  Age-based arbitration  slow (did not consider critical path)
CHIPPER (Fallin et al., HPCA 2011)
  Assumed baseline for this work
AFC (Jafri et al., MICRO 2010)
  Coarse-grained bufferless-buffered hybrid
SCARAB (Hayenga et al., MICRO 2009), BPS (Gomez+08)
  Drop-based deflection networks
  SCARAB: dedicated circuit-switched NACK network