## Slide 1: A Large-Scale Study of Flash Memory Errors in the Field
      Justin Meza
Qiang Wu
Sanjeev Kumar
Onur Mutlu

## Slide 2
Overview
First study of flash reliability:
at a large scale
in the field

## Slide 3
Access pattern dependence
SSD lifecycle
Read disturbance
Temperature
Overview
New reliability trends

## Slide 4
Access pattern dependence
Read disturbance
Temperature
New reliability trends
SSD lifecycle
Overview
Early detection lifecycle period distinct from hard disk drive lifecycle.

## Slide 5
Access pattern dependence
Temperature
New reliability trends
SSD lifecycle
Read disturbance
Overview
We do not observe the effects of read disturbance errors in the field.

## Slide 6
Access pattern dependence
New reliability trends
SSD lifecycle
Read disturbance
Temperature
Overview
Throttling SSD usage helps mitigate temperature-induced errors.

## Slide 7
New reliability trends
SSD lifecycle
Read disturbance
Temperature
Access pattern dependence
Overview
We quantify the effects of the page cache and write amplification in the field.

## Slide 8
background and motivation
server SSD architecture
error collection/analysis methodology
SSD reliability trends
summary
Outline

## Slide 9
Background and
motivation

## Slide 10
persistent
high performance
hard disk alternative
used in solid-state drives (SSDs)
Flash memory

## Slide 11
persistent
high performance
hard disk alternative
used in solid-state drives (SSDs)
prone to a variety of errors
    wearout, disturbance, retention
Flash memory

## Slide 12
Our goal
Understand SSD reliability:
at a large scale
    millions of device-days, across four years
in the field
    realistic workloads and systems

## Slide 13
Server SSD architecture

## Slide 14
Notes: Here is a schematic of a server SSD. Unlike the SSD in your computer, server SSDs are connected over PCIe to enable high bandwidth.

## Slide 15
PCIe

## Slide 16
Flash chips

## Slide 17
SSD controller
translates addresses
schedules accesses
performs wear leveling

## Slide 18
10011111 11001111 11000011 00001101
10101110 11100101 11111001 01111011
00011001 11011101 11100011 11111000
11011111 01001101 11110000 10111111
00000001 11011110 00000101 01010110
00001011 10000010 11111110 00011100
...
01001100 01001101 11010010 01000000
10011100 10111111 10101111 11000101
User data
ECC metadata
Notes: Because bit flips are common in flash memory, the SSD controller stores error correcting code metadata alongside user data on the flash chips.

## Slide 19
Types of errors
Small errors
10's of flipped bits per KB
silently corrected by SSD controller
Large errors
100's of flipped bits per KB
corrected by host using driver
referred to as SSD failure

## Slide 20
Small errors
Large errors
Types of errors
~10's of flipped bits per KB
silently corrected by SSD controller
~100's of flipped bits per KB
corrected by host using driver
refer to as SSD failure
We examine large errors (SSD failures) in this study.

## Slide 21
Error collection/ analysis methodology

## Slide 22
SSD data measurement
metrics stored on SSDs
measured across SSD lifetime

## Slide 23
SSD characteristics
6 different system configurations
    720GB, 1.2TB, and 3.2TB SSDs
    servers have 1 or 2 SSDs
    this talk: representative systems
6 months to 4 years of operation
15TB to 50TB read and written
Notes: 6 different system configurations
this talk: representative systems
analysis of all systems in paper

## Slide 24
Bit error rates (BER)
BER = bit errors per bits transmitted
1 error per 385M bits transmitted to 1 error per 19.6B bits transmitted
    averaged across all SSDs in each system type
10x to 1000x lower than prior studies
    large errors, SSD performs wear leveling

## Slide 25
A few SSDs cause most errors

## Slide 26
A few SSDs cause most errors

## Slide 27
A few SSDs cause most errors
What factors contribute to SSD failures in the field?

## Slide 28
Analytical methodology
not feasible to log every error
instead, analyze lifetime counters
snapshot-based analysis
Notes: Because errors occur so frequently in SSDs, it is not feasible for us to log every error that occurs.
Instead, we analyze lifetime counters that are present in the SSDs we examine that track various metrics such as number of errors that have been corrected, the number of bits read from or written to the SSD and so on.
To account for this, we analyze data by taking a "snapshot" of the current statistics throughout the fleet, group devices by similar characteristics, and examine the error rates of devices in each group. Here's an example.

## Slide 30
Errors | 54,326 | 0 | 2 | 10
Data written | 10TB | 2TB | 5TB | 6TB

## Slide 31
Errors | 54,326 | 0 | 2 | 10
Data written | 10TB | 2TB | 5TB | 6TB
2014-11-1

## Slide 32
Errors | 54,326 | 0 | 2 | 10
Data written | 10TB | 2TB | 5TB | 6TB
2014-11-1
Data written
Errors

## Slide 33
Errors | 54,326 | 0 | 2 | 10
Data written | 10TB | 2TB | 5TB | 6TB
2014-11-1
Data written
Buckets
Errors

## Slide 34
Errors | 54,326 | 0 | 2 | 10
Data written | 10TB | 2TB | 5TB | 6TB
2014-11-1
Data written
Errors

## Slide 35
Errors | 54,326 | 0 | 2 | 10
Data written | 10TB | 2TB | 5TB | 6TB
2014-11-1
Data written
Errors

## Slide 36
SSD reliability trends

## Slide 37
Access pattern dependence
SSD lifecycle
Read disturbance
Temperature
New reliability trends

## Slide 38
Access pattern dependence
Read disturbance
Temperature
SSD lifecycle
New reliability trends

## Slide 39
bathtub curve
Storage lifecycle background:
the
[Schroeder+,FAST'07]
for disk drives
Usage
Failure
rate

## Slide 40
bathtub curve
Storage lifecycle background:
the
[Schroeder+,FAST'07]
for disk drives
Failure
rate
Usage
Early failure period
Useful life period
Wearout period

## Slide 41
bathtub curve
Storage lifecycle background:
the
[Schroeder+,FAST'07]
for disk drives
Failure
rate
Usage
Early failure period
Useful life period
Wearout period
Do SSDs display similar lifecycle periods?

## Slide 42
Use
data written to flash
to examine SSD lifecycle
(time-independent utilization metric)
Notes: We use data written to flash to examine SSD lifecycle trends.
This is because data written to flash is a time-independent metric for SSD utilization.

## Slide 43
720GB, 1 SSD
720GB, 2 SSDs
0
40
80
Data written (TB)

## Slide 44
720GB, 1 SSD
720GB, 2 SSDs
0
40
80
Data written (TB)
Early failure period
Useful life period
Wearout period

## Slide 45
720GB, 1 SSD
720GB, 2 SSDs
0
40
80
Data written (TB)
Early failure period
Useful life period
Wearout period
Early detection period

## Slide 46
Access pattern dependence
Read disturbance
Temperature
New reliability trends
SSD lifecycle
Early detection lifecycle period distinct from hard disk drive lifecycle.

## Slide 47
Access pattern dependence
Temperature
SSD lifecycle
Read disturbance
New reliability trends

## Slide 48
Read disturbance
reading data can disturb contents
failure mode identified in lab setting
under adversarial workloads

## Slide 49
Read disturbance
reading data can disturb contents
failure mode identified in lab setting
under adversarial workloads
Does read disturbance affect SSDs in the field?

## Slide 50
Examine SSDs with
flash R/W
to understand read effects
(isolate effects of read vs. write errors)
ratios
most data read
and
high

## Slide 51
3.2TB, 1 SSD (average R/W = 2.14)
0
100
200
Data read (TB)

## Slide 52
1.2TB, 1 SSD (average R/W = 1.15)
0
100
200
Data read (TB)
Notes: In both of these examples we observe that there is no large statistically-significant deviation in failure rate between devices that have read a small amount of data and those that have read a large amount of data.
One reason for this could be that the read intensity of a variety of real workloads is not sufficient to induce read disturbance in the SSDs we analyzed.
In addition, this could be due to the fact that the controller on the flash devices we examine is able to detect and tolerate these type of errors before they cause a larger error to occur.

## Slide 53
Access pattern dependence
Temperature
New reliability trends
SSD lifecycle
Read disturbance
We do not observe the effects of read disturbance errors in the field.

## Slide 54
Access pattern dependence
SSD lifecycle
Read disturbance
Temperature
New reliability trends

## Slide 56
Temperature sensor

## Slide 57
720GB, 1 SSD
720GB, 2 SSDs

## Slide 58
High temperature:
may throttle or
shut down

## Slide 59
1.2TB, 1 SSD
3.2TB, 1 SSD
Throttling

## Slide 60
Access pattern dependence
New reliability trends
SSD lifecycle
Read disturbance
Temperature
Throttling SSD usage helps mitigate temperature-induced errors.

## Slide 61
Temperature
SSD lifecycle
Read disturbance
Access pattern dependence
New reliability trends

## Slide 62
Access pattern effects
System buffering
data served from OS caches
decreases SSD usage
Write amplification
updates to small amounts of data
increases erasing and copying

## Slide 63
Access pattern effects
Write amplification
updates to small amounts of data
increases erasing and copying
System buffering
data served from OS caches
decreases SSD usage

## Slide 65
OS

## Slide 66
OS
Page cache

## Slide 67
OS
Page cache

## Slide 68
OS
Page cache

## Slide 69
OS
Page cache

## Slide 70
OS
Page cache

## Slide 71
OS
Page cache

## Slide 72
OS
Page cache

## Slide 73
OS
the impact of SSD writes
System caching reduces
Page cache

## Slide 74
1.2TB, 2 SSDs
3.2TB, 2 SSDs
0
15
30
Data written to OS (TB)

## Slide 75
720GB, 2 SSDs
0
15
30
Data written to OS (TB)
Data written to flash cells (TB)
60
20

## Slide 76
Access pattern effects
System buffering
data served from OS caches
decreases SSD usage
Write amplification
updates to small amounts of data
increases erasing and copying

## Slide 77
OS
Flash devices use a
translation layer
to locate data

## Slide 78
OS
Logical
address
space
Translation layer
Physical
address
space
<offset1, size1>
<offset2, size2>
...

## Slide 79
Sparse data layout
more translation metadata
potential for higher write amplification
Notes: Example: reading/writing a large number of small files.

## Slide 80
Dense data layout
less translation metadata
potential for lower write amplification
Notes: Example: reading/writing a large file.

## Slide 81
Use
translation data size
to examine effects of data layout
(relates to application access patterns)

## Slide 82
0
1
2
Translation data (GB)
Sparser
Denser
720GB, 1 SSD

## Slide 83
0.25
0.45
Translation data (GB)
0.25
0.45
Translation data (GB)
Graph search
Key-value store
Write amplification in the field

## Slide 84
New reliability trends
SSD lifecycle
Read disturbance
Temperature
Access pattern dependence
We quantify the effects of the page cache and write amplification in the field.

## Slide 85
Access pattern dependence
SSD lifecycle
Read disturbance
Temperature
New reliability trends

## Slide 86
Block erasures and discards
Page copies
Bus power consumption
More results in paper

## Slide 87
Summary

## Slide 88
Large scale
In the field

## Slide 89
Access pattern dependence
SSD lifecycle
Read disturbance
Temperature
Summary
New reliability trends

## Slide 90
Access pattern dependence
Read disturbance
Temperature
New reliability trends
SSD lifecycle
Summary
Early detection lifecycle period distinct from hard disk drive lifecycle.

## Slide 91
Access pattern dependence
Temperature
New reliability trends
SSD lifecycle
Read disturbance
Summary
We do not observe the effects of read disturbance errors in the field.

## Slide 92
Access pattern dependence
New reliability trends
SSD lifecycle
Read disturbance
Temperature
Summary
Throttling SSD usage helps mitigate temperature-induced errors.

## Slide 93
New reliability trends
SSD lifecycle
Read disturbance
Temperature
Access pattern dependence
Summary
We quantify the effects of the page cache and write amplification in the field.

## Slide 94: A Large-Scale Study of Flash Memory Errors in the Field
      Justin Meza
Qiang Wu
Sanjeev Kumar
Onur Mutlu

## Slide 95
Backup slides

## Slide 96
System characteristics
SSD capacity | PCIe | Average age (years) | SSDs per server | Average written (TB) | Average read (TB)
720GB | v1, x4 | 2.4 | 1 | 27.2 | 23.8
 |  |  | 2 | 48.5 | 45.1
1.2TB | v2, x4 | 1.6 | 1 | 37.8 | 43.4
 |  |  | 2 | 18.9 | 30.6
3.2TB | v2, x4 | 0.5 | 1 | 23.9 | 51.1
 |  |  | 2 | 14.8 | 18.2
Notes: So let's take a look at some of the baseline reliability metrics.

## Slide 97
720GB
1.2TB
3.2TB
Devices:
1
2
1
2
1
2

## Slide 98
720GB
1.2TB
3.2TB
Devices:
1
2
1
2
1
2

## Slide 99
Channels
operate in parallel

## Slide 100
DRAM buffer
stores address translations
may buffer writes

## Slide 101
1.2TB, 2 SSDs
3.2TB, 2 SSDs
Early detection
+ throttling