## Slide 1: Vulnerabilities in MLC NAND Flash Memory Programming: Experimental Analysis, Exploits, and Mitigation Techniques
Yu Cai, Saugata Ghose, Yixin Luo, Ken Mai, Onur Mutlu, Erich F. Haratsch
February 6, 2017

## Slide 2: Executive Summary
MLC (multi-level cell) NAND flash uses two-step programming
We find new reliability and security vulnerabilities
  In between two steps, cells are in a partially-programmed state
  Program interference, read disturb much worse for partially-programmed cells than for fully-programmed cells
We experimentally characterize vulnerabilities using real state-of-the-art MLC NAND flash memory chips
We show that malicious programs can exploit vulnerabilities to corrupt data of other programs and reduce flash memory lifetime
We propose three solutions that target vulnerabilities
  One solution completely eliminates vulnerabilities, at the expense of 4.9% program latency increase
  Two solutions mitigate vulnerabilities, increasing flash lifetime by 16%
Notes: Fix image of partially-programmed cell

## Slide 3: Presentation Outline
Executive Summary
NAND Flash Background
Characterizing New Vulnerabilities in Two-Step Programming
Example Sketches of Security Exploits
Protection and Mitigation Mechanisms
Conclusion

## Slide 4: Storing Data in NAND Flash Memory
Flash cell uses the threshold voltage of a floating-gate transistor to represent the data stored in the cell
Per-bit cost of NAND flash memory has greatly decreased
  Aggressive process technology scaling
  Multi-level cell (MLC) technology
NAND Flash
Chip
MSB: Most Significant Bit
LSB: Least
Significant Bit
11
Flash Cell
Notes: Animate: interference arrows, increase as scaling, two steps of programming
Add MSB/LSB
Add partially-programmed, fully-programmed

## Slide 5: Programming Data to a Multi-Level Cell
Cell programmed by pulsing a large voltage on the transistor gate
Cell-to-cell program interference
  Threshold voltage of a neighboring cell inadvertently increases
  Worsens as flash memory scales
Mitigation: two-step programming
00
??
01
00
Program
00
10
??
?0
00
Step 1
Step 2
01
10
Notes: Animate: interference arrows, increase as scaling, two steps of programming
Add MSB/LSB
Add partially-programmed, fully-programmed

## Slide 6: Reading Data from a Multi-Level Cell
Threshold voltages represented as a probability distribution
  Due to process variation
  Each two-bit value corresponds to a state (a range of threshold voltages)
Read reference voltages (Va, Vb, Vc)
  Identify the state a cell belongs to
  Applied to the transistor gate to see if a cell turns on
Probability
Density
ER 11
P1 01
P2 00
P3 10
Va
Vb
Vc
MSB
LSB
Threshold Voltage (Vth)

## Slide 7: NAND Flash Memory Errors and Lifetime
During a read, raw bit errors occur when the cell threshold voltage incorrectly shifts to a different state
Controller employs sophisticated ECC to correct errors
If errors exceed ECC limit, flash memory has exhausted its lifetime
Raw Bit Error Rate
(RBER)
Program/Erase (P/E) Cycles
ECC Correction Capability
Lifetime
OUR GOAL
Understand how two-step programming
affects flash memory errors and lifetime
(and what potential vulnerabilities it causes)

## Slide 8: Presentation Outline
Executive Summary
NAND Flash Background
Characterizing New Vulnerabilities in Two-Step Programming
  How Can Two-Step Programming Introduce Errors?
  Program Interference
  Read Disturb
Example Sketches of Security Exploits
Protection and Mitigation Mechanisms
Conclusion

## Slide 9: How Can Two-Step Programming Introduce Errors?
Cell starts in the erased state
Step 1 – LSB: Partially program the cell to a temporary state
Errors are introduced into the partially-programmed LSB data
Step 2 – MSB: Program the cell to its final state
  LSB data is read with errors into internal LSB buffer, not corrected by ECC
  MSB data comes from controller to internal MSB buffer
Flash Memory
LSB
MSB
MSB 0
LSB 0
MSB 1
LSB 1
MSB n
LSB n
. . .
. . .
Read
Without
Errors
Controller
MSB data
Read
With
Errors
. . .
ECC Engine
Internal
Buffers
MSB
LSB
LSB data
Errors in internal LSB buffer data cause the cell to be programmed to an incorrect state
Notes: Update image with new labels, animate, add X’s to LSB
Collapse distributions to a single graph

## Slide 10: Cell-to-Cell Program Interference
Flash cells are grouped into multiple wordlines (rows)
Two-step programming interleaves LSB, MSB steps of neighboring wordlines
Steps interleaved using shadow program sequencing
. . .
. . .
. . .
Wordline
Wordline 1
Wordline 0
Wordline 2
Vth
A: LSB of Wordline 1 programmed: no interference
C: After programming LSB of Wordline 2
Vref
B: After programming MSB of Wordline 0
ER
TP
Probability
Density
D: Error when programming MSB of Wordline 1
Wordline 1
LSB
MSB
LSB
MSB
Steps for neighboring wordlines cause interference on partially-programmed cells
How bad is this interference?

## Slide 11: Characterizing Errors in Real NAND Flash Chips
We perform experiments on real state-of-the-art 1x-nm (i.e., 15-19nm) MLC NAND flash memory chips
More info: Cai et al., FPGA-Based Solid-State Drive Prototyping Platform, FCCM 2011
FPGA
Flash
Controller
NAND Flash Daughterboard

## Slide 12: Measuring Errors Induced by Program Interference
Error rate increases with each programming step
  A: Before interference (LSBs in Wordline n just programmed)
  B: After programming pseudo-random data to MSBs in Wordline n-1
  C: After programming pseudo-random data to MSBs in Wordline n-1 and LSBs in Wordline n+1
Interference depends on the data value being programmed
  Higher voltage  more programming pulses  more interference
  W: After programming worst-case data pattern to Wordlines n-1 and n+1
Program interference with worst-case data pattern increases the error rate of partially-programmed cells by 4.9x
Chart: 
| A | B | C | W
 | 1 | 1.4455 | 2.8151 | 4.9273
Raw Bit Error Rate (Normalized to A)
4.9x

## Slide 13: Read Disturb
Flash block: cells from multiple wordlines connected together on bitlines (columns)
Reading a cell from a bitline
  Apply read reference voltage (Vref) to cell
  Apply a pass-through voltage (Vpass) to turn on all unread cells
Pass-through voltage has a weak programming effect
. . .
. . .
. . .
Bitline
Wordline 0
Wordline 2
ER
TP
ER
P1
P2
P3
Vth
ER
LARGER GAP 
GREATER EFFECT
Unprogrammed
Partially
Programmed
Fully
Programmed
Vpass
Wordline 1
Vref
Vpass
Vpass
Partially-programmed and unprogrammed cells more susceptible to read disturb errors

## Slide 14: Measuring Errors Induced by Read Disturb
Chart: Wordline Number




Induce read disturbs on:
  A: Fully-programmed cells
  B: Partially-programmed cells
  C: Unprogrammed cells
After read disturb, program remaining data and check error rate
10-1
10-2
10-3
10-4
Read Disturb Count
A
B
C
LSB Data Raw Bit Error Rate
Order of Magnitude Increase
Errors in Data Not Programmed When Read Disturb Occurs
LSB data in partially-programmed and unprogrammed cells most susceptible to read disturb
Notes: Todo: make graphs bigger

## Slide 15: Presentation Outline
Executive Summary
NAND Flash Background
Characterizing New Vulnerabilities in Two-Step Programming
Example Sketches of Security Exploits
  Program Interference Based Exploit
  Read Disturb Based Exploit
Protection and Mitigation Mechanisms
Conclusion

## Slide 16: Sketch of Program Interference Based Exploit
Malicious program targets a piece of data that belongs to a victim program
Goal: Maximize program interference induced on victim program’s data
Write worst-case data pattern to neighboring wordlines (WL)
  Wordlines 0/1: all 1s to keep at lowest possible threshold voltage
  Wordline 2: victim program writes data
  Wordlines 1 and 3: all 0s to program to highest possible threshold voltage
In the paper
  More details on why this works
  Procedure to work around data scrambling
WL 0
Malicious File A (all 1s)
WL 1
Malicious File B (all 0s)
Malicious File A (all 1s)
WL 2
Data Under Attack
WL 3
Malicious File B (all 0s)
MSB
2
1
3a
3b
LSB
MSB
LSB
MSB
LSB
MSB
LSB

## Slide 17: Presentation Outline
Executive Summary
NAND Flash Background
Characterizing New Vulnerabilities in Two-Step Programming
Example Sketches of Security Exploits
  Program Interference Based Exploit
  Read Disturb Based Exploit: in the paper
Protection and Mitigation Mechanisms
Conclusion

## Slide 18: Presentation Outline
Executive Summary
NAND Flash Background
Characterizing New Vulnerabilities in Two-Step Programming
Example Sketches of Security Exploits
Protection and Mitigation Mechanisms
  Buffering LSB Data in the Controller
  Multiple Pass-Through Voltages
  Adaptive LSB Read Reference Voltage
Conclusion

## Slide 19: 1. Buffering LSB Data in the Controller
Key Observation: During MSB programming, LSB data is read from flash cells with uncorrected interference and read disturb errors
Key Idea: Keep a copy of the LSB data in the controller
Flash Memory
LSB
MSB
MSB 0
LSB 0
MSB 1
LSB 1
MSB n
LSB n
. . .
. . .
Controller
MSB data
. . .
ECC Engine
Read
Without
Errors
Read
With
Errors
LSB data
Completely eliminates vulnerabilities to program interference and read disturb
Typical case: 4.9% increase in programming latency
Internal
Buffers

## Slide 20: 2. Multiple Pass-Through Voltages
Key Observation: Large gap between threshold voltage and pass-through voltage (Vpass) increases errors due to read disturb
Key Idea: Minimize gap by using three pass-through voltages
Reduces raw bit error rate by 72%
Increases flash lifetime by 16%
ER
TP
ER
P1
P2
P3
Vth
ER
Vpass
Vpass
partial
Vpass
erase
LARGE GAP
Unprogrammed
Partially
Programmed
Fully
Programmed
Mitigates vulnerabilities to read disturb
No increase in programming latency

## Slide 21: Presentation Outline
Executive Summary
NAND Flash Background
Characterizing New Vulnerabilities in Two-Step Programming
Example Sketches of Security Exploits
Protection and Mitigation Mechanisms
  Buffering LSB Data in the Controller
  Multiple Pass-Through Voltages
  Adaptive LSB Read Reference Voltage: in the paper
Conclusion

## Slide 22: Presentation Outline
Executive Summary
NAND Flash Background
Characterizing New Vulnerabilities in Two-Step Programming
Example Sketches of Security Exploits
Protection and Mitigation Mechanisms
Conclusion

## Slide 23: Executive Summary
We find new reliability and security vulnerabilities in MLC NAND flash memory
  In between two steps, cells are in a partially-programmed state
  Program interference, read disturb much worse for partially-programmed cells than for fully-programmed cells
We experimentally characterize vulnerabilities using real state-of-the-art MLC NAND flash memory chips
We show that malicious programs can exploit vulnerabilities to corrupt data of other programs and reduce flash memory lifetime
We propose three solutions that target vulnerabilities
  One solution completely eliminates vulnerabilities, at the expense of 4.9% program latency increase
  Two solutions mitigate vulnerabilities, increasing flash lifetime by 16%
Notes: Fix image of partially-programmed cell

## Slide 24: Vulnerabilities in MLC NAND Flash Memory Programming: Experimental Analysis, Exploits, and Mitigation Techniques
Yu Cai, Saugata Ghose, Yixin Luo, Ken Mai, Onur Mutlu, Erich F. Haratsch
February 6, 2017

## Slide 25: Backup Slides

## Slide 26: NAND Flash Memory Scaling
SSDs use NAND flash memory chips, which contain billions of flash cells
Per-bit cost of NAND flash memory has greatly decreased thanks to scaling
Aggressive process technology scaling
  Flash cell size decreases
  Cells placed closer to each other
Multi-level cell (MLC) technology
  Each flash cell represents data using a threshold voltage
  MLC stores two bits of data in a single cell
128GB NAND Flash
256GB NAND Flash
01
11
11
10
11
00
00
10
MSB: Most Significant Bit
LSB: Least
Significant Bit
Notes: Animate: smaller cells, closer together, SLC  TLC
Color MSB/LSBs

## Slide 27: Two-Step Programming
Per-bit cost of NAND flash memory has greatly decreased
  Aggressive process technology scaling
  Multi-level cell (MLC) technology
Flash cell programmed by pulsing a large voltage to the cell transistor
Cell-to-cell program interference
  Threshold voltage of a neighboring cell inadvertently increases
  Worsens as flash memory scales
Mitigation: two-step programming
NAND Flash
Chip
01
11
11
10
11
00
00
10
MSB: Most Significant Bit
LSB: Least
Significant Bit
11
??
10
00
10
Program
11
10
??
?0
00
Step 1
Step 2
Notes: Animate: interference arrows, increase as scaling, two steps of programming
Add MSB/LSB
Add partially-programmed, fully-programmed

## Slide 28: Representing Data in MLC NAND Flash Memory
Flash cell uses floating-gate transistor threshold voltage to represent the data stored in the cell
Threshold voltages represented as a probability distribution
  Each two-bit value corresponds to a state (a range of threshold voltages)
  Read reference voltages (Va, Vb, Vc) identify the state a cell belongs to
Probability
Density
ER 11
P1 01
P2 00
P3 10
Va
Vb
Vc
MSB
LSB
Threshold Voltage (Vth)

## Slide 29: Threshold Voltage Distributions During Programming
Unprogrammed
1. Program LSB
2. Program MSB
Temporary Vth
Starting Vth
ER 11
P1 01
P2 00
P3 10
ER XX
Final Vth
ER X1
TP X0
Probability
Density
Probability
Density
MSB
LSB
Probability
Density

## Slide 30: Characterizing NAND Flash Memory Reliability
Raw bit errors occur when the cell threshold voltage incorrectly shifts to a different state
Raw Bit
Error Rate
Program/Erase (P/E) Cycles
ECC Correction Capability
Lifetime
We experimentally characterize RBER, lifetime of state-of-the-art 1x-nm (i.e., 15-19nm) MLC NAND flash memory chips

## Slide 31: Malicious Program Behavior
Raw Bit Error Rate
P/E Cycles
ECC Error Correction Capability
Normal Usage
Malicious Usage
Normal
Lifetime
Reduced
Lifetime

## Slide 32: How Can Two-Step Programming Introduce Errors?
Step 1: Program only the LSB data
Errors are introduced into the partially-programmed LSB data
Step 2: Program the MSB data
  LSB data is read with errors directly into internal LSB buffer, not corrected by ECC
  MSB data comes from controller to internal MSB buffer
Partially
Programmed
Vth
Erased Vth
ER 11
P1 01
P2 00
P3 10
ER ??
Final Vth
ER ?1
TP ?0
Probability Density
MSB
LSB
Flash Memory
LSB
MSB
MSB 0
LSB 0
MSB 1
LSB 1
MSB n
LSB n
. . .
. . .
Read
Without
Errors
Controller
MSB data
Read
With
Errors
. . .
ECC Engine
Errors in LSB data cause cell to be programmed to an incorrect state
Notes: Update image with new labels, animate, add X’s to LSB
Collapse distributions to a single graph

## Slide 33: Data Scrambler Workaround
Some flash controllers employ XOR-based data scrambling
Workaround to write worst-case data pattern
  Recreate scrambler logic in software
  Scramble data in software with the same seed
  Hardware scrambler descrambles data using the same seed
  Descrambled data written to flash memory
Scrambler
SEED Linear Feedback Shift Register
+
Logical Block Address
Output
Input
Malicious Program
Unscrambled Worst-Case Data
Software Scrambler
SSD Controller
Hardware Scrambler
ECC Engine
SCRAMBLED DATA
DESCRAMBLED
DATA
Flash
Memory
DESCRAMBLED DATA
1
2
3
4
KEY

## Slide 34: Sketch of Read Disturb Based Exploit
Malicious program wants to induce errors into unprogrammed and partially-programmed wordlines in an open block
Rapidly issues large number of reads to the open block
  Write data to the open block
  Issues ~10K reads per second directly to the SSD using syscalls
Induces errors in partially-programmed data
Induces errors in data not yet programmed
  Programming can only increase threshold voltage
  Exploit increases threshold voltage before programming, preventing cell from storing some data values
In the paper: working around SSD caches
Notes: To do: diagram?

## Slide 35: 1. Buffering LSB Data in the Controller
When LSB data is initially programmed, keep a copy in the controller DRAM
During MSB programming, send both LSB and MSB data from controller to internal LSB/MSB buffers in flash memory
Procedure to retrieve, correct data from flash memory if DRAM loses data (e.g., after power loss)
Flash Memory
LSB
MSB
MSB 0
LSB 0
MSB 1
LSB 1
MSB n
LSB n
. . .
. . .
Controller
MSB data
. . .
ECC Engine
Read
Without
Errors
Read
With
Errors
LSB data
Completely eliminates vulnerabilities to interference, read disturb
Typical case: 4.9% increase in programming latency

## Slide 36: Algorithm for Buffering LSB Data
A: Send LSB data to internal LSB buffer
YES
Step 1
Step 2
B: Keep copy of LSB in DRAM buffer
Program LSB page
C: Is LSB in DRAM buffer?
E: Send LSB data to internal LSB buffer
D: Retrieve LSB data from DRAM buffer
F: Send MSB data to internal MSB buffer
G: Retrieve LSB data from flash chip
NO
H: Correct LSB data using ECC engine
Program MSB page

## Slide 37: Latency Impact of Buffering
Vary the speed of the interface between the controller and the flash memory
Assumes 8KB page size
Baseline Latency
LSB Page in DRAM
LSB Page Not in DRAM
Chart: Interface Speed (MB/s)
| 100 | 200 | 300 | 400
Existing | 1681.92 | 1640.96 | 1627.3067 | 1620.48
Our Normal | 1763.84 | 1681.92 | 1654.6133 | 1640.96
First power | 1945.76 | 1822.88 | 1781.92 | 1761.44

## Slide 38: Error Rate with Multiple Pass-Through Voltages
Chart: Read Disturb Count
| 1 | 500 | 1000 | 2000 | 5000 | 8000 | 16000 | 20000 | 30000 | 40000 | 45000 | 50000
LSB-Full | 0.0008604 | 0.0008664 | 0.0008256 | 0.0008004 | 0.0008226 | 0.0008334 | 0.0008634 | 0.0008562 | 0.000906 | 0.0009342 | 0.0009228 | 0.0009402
MSB-Full | 0.0015341 | 0.0017253 | 0.0017561 | 0.0018182 | 0.0020288 | 0.0021956 | 0.0025888 | 0.0028285 | 0.003254 | 0.0037498 | 0.0039328 | 0.0042493
LSB Erase/Half Single Pass | 0.0016092 | 0.002034 | 0.0021024 | 0.0022404 | 0.0027084 | 0.0030792 | 0.0039528 | 0.0044856 | 0.0054312 | 0.0065328 | 0.0069396 | 0.0076428
MSB Erase/Half Single Pass | 0.0013274 | 0.00144 | 0.0014581 | 0.0014947 | 0.0016187 | 0.001717 | 0.0019485 | 0.0020897 | 0.0023403 | 0.0026322 | 0.00274 | 0.0029263
Chart: Read Disturb Count
| 1 | 500 | 1000 | 2000 | 5000 | 8000 | 16000 | 20000 | 30000 | 40000 | 45000 | 50000
LSB-Full | 0.0008604 | 0.0008664 | 0.0008256 | 0.0008004 | 0.0008226 | 0.0008334 | 0.0008634 | 0.0008562 | 0.000906 | 0.0009342 | 0.0009228 | 0.0009402
MSB-Full | 0.0015341 | 0.0017253 | 0.0017561 | 0.0018182 | 0.0020288 | 0.0021956 | 0.0025888 | 0.0028285 | 0.003254 | 0.0037498 | 0.0039328 | 0.0042493
LSB Erase/Half Multiple Pass | 0.00070092 | 0.0007434 | 0.00075024 | 0.00076404 | 0.00081084 | 0.00084792 | 0.00093528 | 0.00098856 | 0.0010831 | 0.0011933 | 0.001234 | 0.0013043
MSB Erase/Half Multiple Pass | 0.0012505 | 0.0012717 | 0.0012751 | 0.001282 | 0.0013254 | 0.001364 | 0.0014176 | 0.0014643 | 0.0015316 | 0.0015966 | 0.001617 | 0.0017521
Single Pass-Through Voltage
Multiple Pass-Through Voltages
Limit
LSB: unprogrammed,
partially programmed
MSB: fully programmed
MSB: unprogrammed,
partially programmed
LSB: fully programmed
Limit

## Slide 39: 3. Adaptive LSB Read Reference Voltage
Adapt the read reference voltage used to read partially-programmed LSB data
  Compensates for threshold voltage shifts caused by program interference, read disturb
  Maintain one read reference voltage per die
  Relearn voltage once a day by checking error rate of test LSB data
Reduces error count, but does not completely eliminate errors
Chart: P/E Cycles
| 5000 | 1
Adaptive Vref | 0.001366 | 0.000562
Baseline | 0.00173 | 0.000804
Baseline: Fixed Vref
Adaptive Vref
-30%
-21%

## Slide 40: 3. Adaptive LSB Read Reference Voltage
Adapt the read reference voltage for partially-programmed LSB data to compensate for voltage shifts
  Program reference data value to LSBs of test wordlines
  Relearn voltage once a day by checking error rate of test data
Reduces error count by 21-30%, but does not completely eliminate errors
Vth
After interference, read disturb
Vref
Before interference, read disturb
ER
TP
Probability
Density
Mitigates, but doesn’t fully eliminate, vulnerabilities
No increase in programming latency

## Slide 41: Conclusion
Two-step programming used in MLC NAND flash memory
  Introduces new reliability and security vulnerabilities
  Partially-programmed cells susceptible to program interference and read disturb
We experimentally characterize vulnerabilities using real NAND flash chips
Malicious programs can exploit vulnerabilities to corrupt data belonging to other programs, and reduce flash memory lifetime
Solution | Protects Against | Latency Overhead | Error Rate Reduction
1. Buffering LSB in the Controller | program interference read disturb | 4.9% | 100%
2. Adaptive LSB Read Reference Voltage | program interference read disturb | 0.0% | 21-33%
3. Multiple Pass-Through Voltages | read disturb | 0.0% | 72% 16% lifetime increase
Notes: Fix image of partially-programmed cell