## Slide 1: FPGA-accelerated Dense Linear Machine Learning: A Precision-Convergence Trade-off
Kaan Kara, Dan Alistarh, Gustavo Alonso, Onur Mutlu, Ce Zhang

## Slide 2
What is the most efficient way of training dense linear models on an FPGA?
FPGAs can handle floating-point, but they are certainly not the best choice.
We have tried: On par with a 10-core Xeon, not a clear win.
Yet!
How about some recent developments in the machine research?
Low-precision data EXACTLY the same end-result.
In theory
leads to

## Slide 3: Stochastic Gradient Descent (SGD)
while not converged do
for i from 1 to M do
end
end
N features
M samples
x
=
Data Set
Labels
Model
Computation
CPU, GPU, FPGA
Memory
CPU Cache,
DRAM,
FPGA BRAM
Data Source
DRAM, SSD,
Sensor
Data Ar
Model x
Gradient: dot(Ar, x)Ar

## Slide 4: Advantage of Low-Precision Data + FPGA
while not converged do
for i from 1 to M do
end
end
x
=
Data Set
Labels
Model
Computation
CPU, GPU, FPGA
Memory
CPU Cache,
DRAM,
FPGA BRAM
Data Source
DRAM, SSD,
Sensor
Data Ar
Model x
Gradient: dot(Ar, x)Ar
Compress!
N features
M samples

## Slide 5: Key Takeaway
Iterations
Training
Loss
Naïve rounding
Stochastic rounding
Full-precision
Using an FPGA, we can increase the hardware efficiency while maintaining the statistical efficiency of SGD for dense linear models.
Execution Time
Training
Loss
faster
same quality
In practice, the system opens up a multivariate trade-off space:
Data properties, FPGA implementation, SGD parameters…

## Slide 6: Outline for the Rest…
Stochastic quantization. Data layout
Target platform: Intel Xeon+FPGA
Implementation: From 32-bit to 1-bit SGD on FPGA.
Evaluation: Main results. Side effects.
Conclusion

## Slide 7: Stochastic Quantization [1]
[…. 0.7 ….]
0
1
Naive solution: Nearest rounding (=1)
=> Converge to a different solution.
Stochastic rounding: 0 with probability 0.3, 1 with probability 0.7
=> Expectation remains the same. Converge to the same solution.
Gradient
We need 2
independent samples
…and each iteration of the algorithm needs fresh samples.
[1] H Zhang, K Kara, J Li, D Alistarh, J Liu, C Zhang: ZipML: An End-to-end Bitwise Framework for Dense Generalized Linear Models, arXiv:1611.05402

## Slide 8: Before the FPGA: The Data Layout
32-bit float value
1. Feature
1. Sample
32-bit float value
2. Feature
32-bit float value
3. Feature
32-bit float value
n. Feature
32-bit float value
m. Sample
32-bit float value
32-bit float value
32-bit float value
Quantize to 4-bit.
We need 2 independent quantizations!
4-bit | 4-bit
1. Feature
1. Sample
2. Feature
m. Sample
4x compression!
3. Feature
4-bit | 4-bit
4-bit | 4-bit
n. Feature
4-bit | 4-bit
4-bit | 4-bit
4-bit | 4-bit
4-bit | 4-bit
4-bit | 4-bit
For each iteration
A new index!
1 quantization index
Currently slow!

## Slide 9: Target Platform
Intel Xeon+FPGA
Ivy Bridge, Xeon E5-2680 v2
10 cores, 25 MB L3

## Slide 10: Full Precision SGD on FPGA
32-bit floating-point: 16 values
Processing rate: 12.8 GB/s
Computation
Custom Logic
Storage Device
FPGA BRAM
Data Source
DRAM, SSD,
Sensor

## Slide 11: Scale out the design for low-precision data!
How can we increase the internal parallelism while maintaining the processing rate?

## Slide 12: Challenge + Solution
8-bit: 32 values Q8
4-bit: 64 values Q4
2-bit: 128 values Q2
1-bit: 256 values Q1
=> Scaling out is not trivial!
We can get rid of floating-point arithmetic.
We can further simplify integer arithmetic for lowest precision data.

## Slide 13: Trick 1: Selection of quantization levels
U
L
Select the lower and upper bound [L,U]
Select the size of the interval ∆
All quantized values are integers!
∆

## Slide 14: This is enough for Q4 and Q8
8-bit: 32 values Q8
4-bit: 64 values Q4
2-bit: 128 values Q2
1-bit: 256 values Q1

## Slide 15: Trick 2: Implement Multiplication using Multiplexer
Q2 multiplier
Q1 multiplier

## Slide 16: Support for all Qx
Circuit for Q8, Q4 and Q2 SGD
Processing rate: 12.8 GB/s
Circuit for Q1 SGD
Processing rate: 6.4 GB/s

## Slide 17: Support for all Qx
Circuit for Q8, Q4 and Q2 SGD
Processing rate: 12.8 GB/s
Circuit for Q1 SGD
Processing rate: 6.4 GB/s
Data Type | Logic | DSP | BRAM
float | 38% | 12% | 7%
Q8 | 35% | 25% | 6%
Q4 | 36% | 50% | 6%
Q2, Q1 | 43% | 1% | 6%

## Slide 18: Data sets for evaluation
Name | Size | # Features | # Classes
MNIST | 60,000 | 780 | 10
GISETTE | 6,000 | 5,000 | 2
EPSILON | 10,000 | 2,000 | 2
SYN100 | 10,000 | 100 | Regression
SYN1000 | 10,000 | 1,000 | Regression
Following the Intel legal guidelines on publishing performance numbers, we would like to make the reader aware that results in this publication were generated using preproduction hardware and software, and may not reﬂect the performance of production or future systems.

## Slide 19: SGD Performance Improvement
SGD on Synthetic100,
4-bit works
SGD on Synthetic1000,
8-bit works

## Slide 20: 1-bit also works on some data sets
SGD on MNIST, Digit 7
1-bit works
MNIST
multi-classification accuracy

## Slide 21: Naïve Rounding vs. Stochastic Rounding
Bias
Stochastic quantization results in unbiased convergence.

## Slide 22: Effect of Step Size
Large step size + Full precision
vs.
Small step size +
Low precision

## Slide 23: Conclusion
Highly scalable, parametrizable FPGA-based stochastic gradient descent implementations for doing linear model training.
Open source: www.systems.ethz.ch/fpga/ZipML_SGD
The way to train linear models on FPGA should be through the usage of stochastically rounded, low-precision data.
Multivariate trade-off space: Precision vs. end-to-end runtime, convergence quality, design complexity, data and system properties.
Key Takeaways:

## Slide 25: Backup
Why do dense linear models matter?
Workhorse algorithm for regression and classification.
Sparse, high dimensional data sets can be converted into dense ones.
Transfer Learning
Random Features
Why is training speed important?
Often a human-in-the-loop process.
Configuring parameters, selecting features, data dependency etc.
Train
Evaluate

## Slide 26: Effect of Reusing Indexes
In practice 8 indexes are enough!