## Slide 1: Kilo-NOC: A Heterogeneous Network-on-Chip Architecture for Scalability and Service Guarantees
Boris Grot, Joel Hestness, Stephen W. Keckler 1 The University of Texas at Austin 1 NVIDIA Research | Onur Mutlu Carnegie Mellon University

## Slide 2: Motivation
Extreme-scale chip-level integration
  Cores
  Cache banks
  Accelerators
  I/O logic
  Network-on-chip (NOC)
10-100 cores today
1000+ assets in the near future

## Slide 3: This talk
On-chip networks for the kilo-node era
Kilo-NOC

## Slide 4: Kilo-NOC requirements
High efficiency
  Area
  Energy
Good performance
Strong service guarantees

## Slide 5: Outline
Limitations of existing NOC technologies
Contributions
  Topology-aware QOS support
  Hybrid flow control
Select results
Summary

## Slide 6: Technologies & Limitations (1/2)
Technology: Low-diameter topologies
  Rich connectivity improves performance & energy
  E.g.: flattened butterfly [Micro 07], MECS [HPCA 09]
Scalability obstacle: Buffer demands
  Growth in router radix with network radix
  More buffers per port due to slower wires
Cost: area, energy, delay

## Slide 7: Technologies & Limitations (2/2)
Technology: NOC QOS architectures
  No per-flow buffering (shared pool of VCs)
  Simple prioritization and scheduling
  E.g.: GSF [ISCA 08], PVC [Micro 09]
Scalability obstacle: VC demands
  Many VCs to cover long links with slow wires
Cost: buffering, arbitration complexity

## Slide 8: Outline
Limitations of existing NOC technologies
Contributions
  Topology-aware QOS support
  Optimized flow control
Select results
Summary

## Slide 9: Baseline QOS-enabled CMP
Multiple VMs
sharing a die
Shared resources
(e.g., memory controllers)
VM-private resources
(cores, caches)
QOS-enabled router
Q

## Slide 10: Conventional NOC QOS
Contention scenarios:
Shared resources
  memory access
Intra-VM traffic
  shared cache access
Inter-VM traffic
  VM page sharing

## Slide 11: Conventional NOC QOS
Contention scenarios:
Shared resources
  memory access
Intra-VM traffic
  shared cache access
Inter-VM traffic
  VM page sharing
Network-wide guarantees without network-wide QOS support

## Slide 12: Kilo-NOC QOS
Insight: leverage rich network connectivity
  Naturally reduce interference among flows
  Limit the extent of hardware QOS support
Requires a low-diameter topology
  This work: Multidrop Express Channels (MECS)
  Grot et al., HPCA 2009

## Slide 13: Topology-Aware QOS
Dedicated, QOS-enabled regions
  Rest of die: QOS-free
Richly-connected topology
  Traffic isolation
Special routing rules
  Manage interference
QOS-free

## Slide 14: Topology-Aware QOS
Dedicated, QOS-enabled regions
  Rest of die: QOS-free
Richly-connected topology
  Traffic isolation
Special routing rules
  Manage interference

## Slide 15: Topology-Aware QOS
Dedicated, QOS-enabled regions
  Rest of die: QOS-free
Richly-connected topology
  Traffic isolation
Special routing rules
  Manage interference

## Slide 16: Topology-Aware QOS
Dedicated, QOS-enabled regions
  Rest of die: QOS-free
Richly-connected topology
  Traffic isolation
Special routing rules
  Manage interference

## Slide 17: Kilo-NOC view
Topology-aware QOS support
  Limit QOS complexity to a fraction of the die
Optimized flow control
  Reduce buffer requirements in QOS-free regions
QOS-free

## Slide 18: Traditional Buffer Flow Control
Router-side buffering
  Enough storage to cover the round-trip credit time
E.g.: wormhole, virtual channel flow control

## Slide 19: Elastic Buffer Flow Control
Integrate storage directly into links
Kodi et al. [ISCA ’08], Michelogiannakis et al. [HPCA ’09]
  No virtual channels
  Reduced router complexity

## Slide 20: Elastic Buffer Flow Control
Integrate storage directly into links
Kodi et al. [ISCA ’08], Michelogiannakis et al. [HPCA ’09]
  Multiple networks for deadlock avoidance
  No savings in end-to-end storage with p2p links

## Slide 21: MECS + EB flow control
Insight: EB flow control reduces storage requirements in a MECS network
  Each EB shared by all downstream nodes
Problem: performance suffers

## Slide 22: MECS + EB flow control
Chart: Load (%)
MECS | 20.9091 | 21.0421 | 21.2307 | 21.407 | 21.6134 | 21.8416 | 22.0821 | 22.332 | 22.6169 | 22.97 | 23.3071 | 23.7356 | 24.1778 | 24.7414 | 25.326 | 26.0449 | 26.9402 | 27.9266 | 29.1728 | 30.6446 | 32.868 | 35.6893 | 40.3963 | 49.2916 | 69.3038 | 176.2594 | 450.6665 | 853.3067
MECS EB | 20.4297 | 20.5857 | 20.7988 | 20.9975 | 21.2331 | 21.4895 | 21.7658 | 22.0562 | 22.3973 | 22.8411 | 23.3037 | 23.9118 | 24.6885 | 26.1316 | 27.8237 | 32.1529 | 61.9601 | 195.6294 | 429.1887 | 797.3519 | 1309.0212 | 1865.1743 | 2422.9072 | 3011.4829 | 3621.1658 | 4213.2046 | 4794.7319 | 5389.2378
32%

## Slide 23: Hybrid flow control
Combine EB and VC flow control
Long flight time  many buffers/VCs at router port
Allocate VC

## Slide 24: Hybrid flow control
Combine EB and VC flow control
Novel JIT VC allocation strategy
  Allocate a VC from an elastic buffer
Allocate VC

## Slide 25: Hybrid flow control
Combine EB and VC flow control
Novel JIT VC allocation strategy
  Allocate a VC from an elastic buffer
Benefits
  Shallow, per-message class VCs
  Deadlock freedom without multiple networks
  Performance improvement
Special rules for deadlock avoidance

## Slide 26: MECS + hybrid flow control
Chart: Load (%)
MECS | 20.9091 | 21.0421 | 21.2307 | 21.407 | 21.6134 | 21.8416 | 22.0821 | 22.332 | 22.6169 | 22.97 | 23.3071 | 23.7356 | 24.1778 | 24.7414 | 25.326 | 26.0449 | 26.9402 | 27.9266 | 29.1728 | 30.6446 | 32.868 | 35.6893 | 40.3963 | 49.2916 | 69.3038 | 176.2594 | 450.6665 | 853.3067
MECS EB | 20.4297 | 20.5857 | 20.7988 | 20.9975 | 21.2331 | 21.4895 | 21.7658 | 22.0562 | 22.3973 | 22.8411 | 23.3037 | 23.9118 | 24.6885 | 26.1316 | 27.8237 | 32.1529 | 61.9601 | 195.6294 | 429.1887 | 797.3519 | 1309.0212 | 1865.1743 | 2422.9072 | 3011.4829 | 3621.1658 | 4213.2046 | 4794.7319 | 5389.2378
MECS hybrid | 19.9239 | 20.0694 | 20.2674 | 20.4497 | 20.6582 | 20.8893 | 21.1275 | 21.3684 | 21.6464 | 21.9841 | 22.3031 | 22.6993 | 23.0985 | 23.6046 | 24.1333 | 24.7642 | 25.5264 | 26.4208 | 27.4713 | 28.8565 | 31.4303 | 36.225 | 89.6307 | 304.5989 | 665.3123 | 1117.7197 | 1711.025 | 2148.1375
8%
8x less buffering

## Slide 27: Outline
Limitations of existing NOC technologies
Contributions
  Topology-aware QOS support
  Hybrid flow control
Select results
Summary

## Slide 28: Evaluation Methodology
Parameter | Value
Technology | 15 nm
Vdd | 0.7 V
System | 1024 tiles: 256 concentrated nodes (64 shared resources)
Networks: | 
MECS+PVC | VC flow control, QOS support (PVC) at each node
MECS+TAQ | VC flow control, QOS support only in shared regions
MECS+TAQ+EB | EB flow control outside of SRs, Separate Request and Reply networks
K-MECS | Proposed organization: TAQ + hybrid flow control

## Slide 29: Area comparison
Chart: Area (mm2)
| MECS+PVC | MECS+TAQ | MECS+ TAQ+EB | K-MECS
Links | 3.4102 | 3.4102 | 4.8488 | 3.4102
Link EBs | 0 | 0 | 0.82232 | 0.52629
Routers | 26.4729 | 15.0498 | 5.9396 | 5.9081
SR Routers | 0 | 6.6182 | 6.6182 | 6.6182

## Slide 30: Energy comparison
Chart: Network energy/packet (pJ)
| MECS+PVC | MECS+TAQ | MECS+EB+TAQ | K-MECS
Links | 39.4392 | 39.4392 | 39.4392 | 39.4392
Link EBs | 0 | 0 | 2.3102 | 2.3102
Routers | 40.7651 | 26.5255 | 6.1589 | 9.3178
SR Routers | 0 | 6.2175 | 6.2175 | 6.2175

## Slide 31: Summary
Kilo-NOC: a heterogeneous NOC architecture for kilo-node substrates
Topology-aware QOS
  Limits QOS support to a fraction of the die
  Leverages low-diameter topologies
  Improves NOC area- and energy-efficiency
  Provides strong guarantees

## Slide 32: Summary
Kilo-NOC: a heterogeneous NOC architecture for kilo-node substrates
Topology-aware QOS
Hybrid flow control
  Enabled by Topology-aware QOS
  Couples VC and EB flow control
  JIT VC allocation
  Reduces VC & buffer requirements

## Slide 33: Summary
Kilo-NOC: a heterogeneous NOC architecture for kilo-node substrates
Topology-aware QOS
Hybrid flow control
Bottom line vs MECS+PVC
  45% improvement in area-efficiency
  29% improvement in energy-efficiency
  Comparable QOS strength, performance