## Slide 1: Topology-aware QOS Support in Highly Integrated CMPs
Boris Grot (UT-Austin)
Stephen W. Keckler (NVIDIA/UT-Austin)
Onur Mutlu (CMU)

## Slide 2: Motivation
Highly integrated chip multiprocessors
  Tilera Tile GX – up to 100 cores
  Intel Knight’s Corner – 50 x86-64 cores (next year)
Infrastructure-level monetization of CMPs
  Server consolidation
  Cloud computing
New challenges & vulnerabilities
  Performance isolation
  Information leakage [Ristenpart et al., CCCS ‘09]
  Denial-of-service
SW solutions are insufficient

## Slide 3: Hardware QOS Support
Shared caches
  [Iyer, ICS ‘04] [Nesbit et al., ISCA ‘07]
Memory controllers
  [Mutlu & Moscibroda, Micro ‘07, ISCA ’08]
Network-on-chip (NOC)
  [Lee et al., ISCA ‘08] [Grot et al., Micro ’09]

## Slide 4: Scalability of Shared Resource QOS
Shared caches
  Way-level QOS: difficult to scale
  Bank-level: scales, if (# banks ≥ # cores)
  Requires network QOS to ensure fair access
Memory controllers, accelerators
  Requires end-point QOS support
  Requires network QOS to ensure fair access
Network-on-chip (NOC)
  Area, energy, performance overheads due to QOS
  Overheads grow with network size

## Slide 5: Baseline CMP Organization
4 tiles per network node (core & cache banks)
Shared memory controllers (MCs) with own QOS mechanism
Hardware QOS support at each router
Our target: 64 nodes (256 tiles)

## Slide 6: Scalability Challenges of NOC QOS
Conventional
  Weighted Fair Queing [Demers et al., SIGCOMM ’89]
  Per-flow buffering at each router node
  Complex scheduling/arbitration
On-Chip
  Preemptive Virtual Clock (PVC) [Grot et al., Micro ’09]
    Buffers are shared among all flows
    Priority inversion averted through preemption of lower-priority packets
    Preemption recovery: NACK + retransmit
  Sources of overhead
    Flow tracking (area, energy, delay)
    Preemptions (energy, throughput)
    Buffer overhead in low-diameter topologies (area, energy)

## Slide 7: Topology-aware On-chip QOS
Shared resources isolated into dedicated regions (SR)
Low-diameter topology for single-hop SR access
  MECS [Grot et al., HPCA ‘08]
Convex domain for each application/VM
  Enables shared caches without cache-level QOS
  Downside: potential resource fragmentation

## Slide 8: This Work: Shared Region Organization
Focus: interaction between topology and QOS
Three different topologies
  MECS
  Mesh
  Destination Partitioned Subnets (DPS)
Preemptive QOS (PVC)
Detailed evaluation
  Area
  Energy
  Performance
  Fairness
  Preemption resilience

## Slide 9: Topologies
MECS
Mesh
DPS
Mesh
  + Low complexity
  − Low bandwidth
  − Inefficient multi-hop transfers
MECS
  + Efficient “multi-hop” transfers
  − Buffer requirements
  − Arbitration complexity
DPS
  + Low buffer overhead
  + Low arbitration complexity
  + Efficient multi-hop transfers
  − High crossbar complexity

## Slide 10: Experimental Methodology
CMP | 64 nodes (256 terminals): 8x8 with 4-way concentration
Network (SR) | 8 nodes (1 column), 16 byte links, 1 cycle wire delay b/w neighbors
QOS | Preemptive Virtual Clock (PVC): 50K cycle frame
Workloads | uniform-random, tornado, hotspot, & adversarial permutations; 1- and 4-flit packets, stochastically generated
Topologies | mesh_x1, mesh_x2, mesh_x4, MECS, DPS
Mesh | 6 VCs/port, 2 stage pipeline (VA, XT)
MECS | 14 VCs/port, 3 stage pipeline (VA-local, VA-global, XT)
DPS | 5 VCs/port, 2 stage pipeline at source/dest (VA, XT), 1 cycle at intermediate hops
Common | 4 flits/VC; 1 injection VC, 2 ejection VCs, 1 reserved VC at each network port

## Slide 11: Performance: Uniform Random
Chart: Injection rate (%)
mesh_x1 | 12.9103 | 13.616 | 14.8589 | 17.7465 | 67.225 | 1551.9258 | 1817.6034 | 1885.8402 | 1913.9338 | 1924.4552 | 1939.5742 | 1952.5792 | 1954.5171 | 1955.754 | 1966.7262
mesh_x2 | 12.7512 | 13.0911 | 13.5121 | 14.0785 | 14.8537 | 15.8701 | 17.5358 | 20.2708 | 29.14 | 440.6394 | 843.6034 | 957.8115 | 999.0167 | 1021.1498 | 1040.4559
mesh_x4 | 12.7269 | 12.9216 | 13.2015 | 13.4978 | 13.8677 | 14.3354 | 14.858 | 15.496 | 16.3195 | 17.4084 | 18.8937 | 20.9158 | 196.1869 | 459.0423 | 562.6569
mecs | 11.1534 | 11.3929 | 11.6898 | 12.0179 | 12.42 | 12.9143 | 13.5159 | 14.3016 | 15.3415 | 16.8529 | 19.3685 | 24.42 | 62.1174 | 277.0058 | 453.162
dps | 11.018 | 11.2134 | 11.4616 | 11.7549 | 12.113 | 12.5374 | 13.0655 | 13.7989 | 14.7835 | 16.2321 | 18.564 | 24.4789 | 68.8255 | 211.5966 | 339.9368

## Slide 12: Performance: Tornado
Chart: Injection rate (%)
mesh_x1 | 17.3059 | 19.5431 | 56.1816 | 3165.2859 | 3282.5217 | 3321.4397 | 3342.385 | 3352.668 | 3360.2417 | 3366.1072 | 3371.6821 | 3376.2519 | 3377.7083 | 3379.5698 | 3382.2561
mesh_x2 | 16.886 | 17.4599 | 18.3541 | 19.9401 | 23.6036 | 71.3253 | 1546.6704 | 1654.7905 | 1689.5487 | 1705.5934 | 1717.975 | 1724.9872 | 1732.0907 | 1736.715 | 1738.9445
mesh_x4 | 16.7378 | 17.0277 | 17.3812 | 17.8146 | 18.3886 | 19.1355 | 20.2858 | 241.7394 | 332.6196 | 374.8287 | 635.6576 | 654.2339 | 702.9138 | 889.0618 | 1036.0254
mecs | 12.6472 | 12.8328 | 13.0376 | 13.2899 | 13.6133 | 14.0489 | 14.6189 | 15.504 | 16.8068 | 19.0649 | 24.5735 | 51.7259 | 517.5838 | 722.1749 | 770.0458
dps | 13.6472 | 13.8328 | 14.0407 | 14.2856 | 14.6048 | 15.0401 | 15.6275 | 16.5108 | 17.8156 | 20.2278 | 25.6575 | 53.7423 | 512.5926 | 726.7414 | 770.759

## Slide 13: Preemption Resilience
Chart: Preemption rate (%)
| mesh_x1 | mesh_x2 | mesh_x4 | mecs | dps
Packets | 20.6402 | 32.3529 | 28.1087 | 10.8397 | 21.4895
Hops | 9.4086 | 27.5823 | 24.021 | 10.8172 | 8.904

## Slide 14: Fairness & Performance Impact
Chart: 
| mesh_x1 | mesh_x2 | mesh_x4 | mecs | dps
avg deviation | 0.0031628 | 0.0060047 | 0.0033992 | 0.0071385 | 0.005447
slowdown | 0.015759 | 0.031076 | 0.034615 | 0.043944 | 0.014934

## Slide 15: Area Efficiency
Chart: Topology
| mesh_x1 | mesh_x2 | mesh_x4 | mecs | dps
Input buffers | 0.023867 | 0.0272 | 0.033864 | 0.044807 | 0.032063
Crossbar | 0.015735 | 0.030841 | 0.076158 | 0.015735 | 0.03147
Flow state | 0.0017525 | 0.0033434 | 0.0063949 | 0.0020131 | 0.0016002

## Slide 16: Energy Efficiency
Chart: Router component energy (nJ)
| src | intermediate | dest | 3 hops | src | intermediate | dest | 3 hops | src | intermediate | dest | 3 hops | src | intermediate | dest | 3 hops | src | intermediate | dest | 3 hops | mesh_x1 | mesh_x2 | mesh_x4 | mecs | dps
buffers | 3.7582 | 2.5134 | 2.5134 | 11.2984 | 3.7582 | 2.5134 | 2.5134 | 11.2984 | 3.7582 | 2.5134 | 2.5134 | 11.2984 | 3.7582 | 0 | 5.0077 | 8.766 | 3.7582 | 2.2036 | 2.2036 | 10.3691
xbar | 1.2407 | 1.2407 | 1.2407 | 4.9629 | 1.593 | 1.593 | 1.593 | 6.372 | 2.3214 | 2.3214 | 2.3214 | 9.2858 | 2.6552 | 0 | 2.6552 | 5.3103 | 1.77 | 0.084288 | 1.6858 | 3.6244
flow table | 0.27055 | 0.61319 | 0.61319 | 2.1101 | 0.34967 | 0.61319 | 0.61319 | 2.1892 | 0.42089 | 0.61319 | 0.61319 | 2.2605 | 0.27055 | 0 | 0.2472 | 0.51775 | 0.42089 | 0 | 0.90008 | 1.321

## Slide 17: Summary
Scalable QOS support for highly integrated CMPs
Topology-aware QOS approach
  Isolate shared resources into dedicated regions (SRs)
  Low-diameter interconnect for single-hop SR access
  App’n/VM domains avoid the need for QOS outside SRs
This paper: Shared Region organization
  Interaction between topology and QOS
  New topology: Destination Partitioned Subnets (DPS)
  DPS & MECS: efficient, provide good isolation
Topology/QOS interaction: promising direction
  More research needed!