## Slide 1: Accelerating Pointer Chasing in 3D-Stacked Memory: Challenges, Mechanisms, Evaluation
Kevin Hsieh
Samira Khan, Nandita Vijaykumar, Kevin K. Chang,
Amirali Boroumand, Saugata Ghose, Onur Mutlu

## Slide 2: Executive Summary
Our Goal: Accelerating pointer chasing inside main memory
Challenges: Parallelism challenge and Address translation challenge
Our Solution: In-Memory PoInter Chasing Accelerator (IMPICA)
  Address-access decoupling: enabling parallelism in the accelerator with low cost
  IMPICA page table: low cost page table structure
Key Results:
  1.2X – 1.9X speedup for pointer chasing operations, +16% database throughput
  6% - 41% reduction in energy consumption

## Slide 3: Linked Data Structures
Linked data structures are widely used in many important applications
Database
B-Tree
Hash Table
Key-value stores
Linked data structures are
connected by pointers

## Slide 4: The Problem: Pointer Chasing
Traversing linked data structures requires chasing pointers
MEM
H
E
A
F
Q
M
Find(A)
Addr (H)
Data (H)
Addr (E)
Data (E)
Addr (A)
Data (A)
Serialized and irregular access pattern
6X cycles per instruction in real workloads

## Slide 5: Our Goal
DRAM layers
Accelerating pointer chasing inside main memory
H
E
A
F
Q
M
Find(A)
MEM
Data (A)
Logic layer
Find
(A)

## Slide 6: Outline
Motivation and Our Approach
Parallelism Challenge
IMPICA Core Architecture
Address Translation Challenge
IMPICA Page Table
Evaluation
Conclusion

## Slide 7: Parallelism Challenge
Time
Memory
access
CPU core
In-Memory Accelerator
Comp
Memory access
CPU core
Comp
Comp
Comp
Memory
access
Comp
Comp
Comp
Memory access
Comp
Faster for one operation
Slower for two operations

## Slide 8: Parallelism Challenge and Opportunity
A simple in-memory accelerator can still be slower than multiple CPU cores
Opportunity: a pointer-chasing accelerator spends a long time waiting for memory
CPU core
Accelerator
CPU core
CPU core
Comp
Memory access (10-15X of Comp)
Comp

## Slide 9: Our Solution: Address-Access Decoupling
Time
Comp
Memory access
Comp
Comp
Address Engine
Access Engine
Comp
Memory access
Memory
access
CPU core
CPU core
Comp
Comp
Memory
access
Comp
Comp
Address-access decoupling enables parallelism in both engines with low cost

## Slide 10: IMPICA Core Architecture
DRAM Dies
Address
Engine
Access
Engine
Memory Controller
DRAM
Logic Layer
DRAM Layers
Request Queue
To/From CPU
Access Queue
Response Queue
IMPICA Cache
Traversal 1
Traversal 2

## Slide 11: Outline
Motivation and Our Approach
Parallelism Challenge
IMPICA Core Architecture
Address Translation Challenge
IMPICA Page Table
Evaluation
Conclusion

## Slide 12: Address Translation Challenge
TLB/MMU
Pointer (VA)
Pointer (PA)
Page table walk
PTW
PTW
PTW
PTW
PTW
No TLB/MMU on the memory side
Duplicating it is costly and creates compatibility issue
The page table walk requires multiple memory accesses

## Slide 13: Our Solution: IMPICA Page Table
Completely decouple the page table of IMPICA from the page table of the CPUs
IMPICA Region
Physical Address Space
Virtual Page
Physical Page
Physical Page
Virtual Page
CPU Page Table
Virtual Address Space
IMPICA Page Table
Map linked data structure into IMPICA regions
IMPICA page table is a partial-to-any mapping

## Slide 14: IMPICA Page Table: Mechanism
Bit [47:41]
Bit [40:21]
Bit [20:12]
Bit [11:0]
Region Table
Flat Page Table (2MB)
Small Page Table (4KB)
+
+
Virtual Address
+
Physical Address
Tiny region table is almost always in the cache
Flat page table
saves one memory access

## Slide 15: Outline
Motivation and Our Approach
Parallelism Challenge
IMPICA Core Architecture
Address Translation Challenge
IMPICA Page Table
Evaluation
Conclusion

## Slide 16: Evaluated Workloads
Microbenchmarks
  Linked list (from Olden benchmark)
  Hash table (from Memcached)
  B-tree (from DBx1000)
Application
  DBx1000 (with TPC-C benchmark)

## Slide 17: Evaluation Methodology
Simulator: gem5
System Configuration
  CPU
    4 OoO cores, 2GHz
    Cache: 32KB L1, 1MB L2
  IMPICA
    1 core, 500MHz, 32KB Cache
  Memory Bandwidth
    12.8 GB/s for CPU, 51.2 GB/s for IMPICA
Our simulator code will be released in Dec.
  https://github.com/CMU-SAFARI

## Slide 18: Result – Microbenchmark Performance
Chart: Speedup
| Linked List | Hash Table | B-Tree
Baseline + extra 128KB L2 | 1.0261 | 1.0135 | 1.0205
IMPICA | 1.9236 | 1.2865 | 1.1848
1.9X
1.3X
1.2X

## Slide 19: Result – Database Performance
Chart: Database Throughput
| Baseline + extra 128KB L2 | Baseline + extra 1MB L2 | IMPICA
Throughput | 1.0101 | 1.054 | 1.1601
+2%
+5%
+16%
Chart: Database Latency
| Baseline + extra 128KB L2 | Baseline + extra 1MB L2 | IMPICA
Latency | 1.001 | 0.95911 | 0.86934
-4%
-13%
-0%

## Slide 20: Energy Consumption
Chart: Normalized Energy
| Linked List | Hash Table | B-Tree | DBx1000
Baseline + extra 128KB L2 | 0.97087 | 0.99077 | 0.98072 | 0.9731
IMPICA | 0.59474 | 0.77144 | 0.90116 | 0.94365
-41%
-24%
-6%
-10%

## Slide 21: More in the Paper
Interface and design considerations
  CPU interface and programming model
  Page table management
  Cache coherence
Area and power overhead analysis
Sensitivity to IMPICA page table design

## Slide 22: Conclusion
Performing pointer-chasing inside main memory can greatly speed up the traversal of linked data structures
Challenges: Parallelism challenge and Address translation challenge
Our Solution: In-Memory PoInter Chasing Accelerator
  Address-access decoupling: enabling parallelism with low cost
  IMPICA page table: low cost page table structure
Key Results:
  1.2X – 1.9X speedup for pointer chasing operations, +16% database throughput
  6% - 41% reduction in energy consumption
Our solution can be applied to a broad class of in-memory accelerators

## Slide 23: Accelerating Pointer Chasing in 3D-Stacked Memory: Challenges, Mechanisms, Evaluation
Kevin Hsieh
Samira Khan, Nandita Vijaykumar, Kevin K. Chang,
Amirali Boroumand, Saugata Ghose, Onur Mutlu

## Slide 24: Microarchitecture Metrics
Chart: TLB MPKI
| Linked List | Hash Table | B-Tree
Baseline + addititional cache | 153.5429 | 57.94 | 34.4795
PICA | 77.9474 | 13.0269 | 5.0202
Chart: Normalized cache miss latency
| Linked List | Hash Table | B-Tree
Baseline + extra 128KB L2 | 1.0108 | 0.99741 | 0.979
IMPICA | 0.61455 | 0.71986 | 0.71749

## Slide 25: Sensitivity to IMPICA TLB size & Page Table Design
Chart: Address Translation Speedup
| Linked List | Hash Table | B-Tree | DBx1000
32 TLB | 1 | 1 | 1 | 1
64 TLB | 1 | 1.0017 | 1.0108 | 1.0324
32 TLB + RPT | 1.0961 | 1.073 | 1.0473 | 1.2837
64 TLB + RPT | 1.0961 | 1.0752 | 1.0551 | 1.3008

## Slide 26: Full IMPICA Core Architecture
DRAM Dies
Address
Engine
Access
Engine
Memory Controller
DRAM
Logic Layer
DRAM Layers
Request Queue
To/From CPU
Access Queue
Response Queue
IMPICA Cache
Inst RAM
Data RAM

## Slide 27: CPU Interface
We use packet-based interface between CPU and IMPICA
Execution steps
  CPU sends function call and parameter to IMPICA
  The packet is written to IMPICA data RAM
  IMPICA loads the function into inst RAM
  IMPICA writes results to the data RAM, from which the CPU polls the results.

## Slide 28: Programming Model
An IMPICA program is written as a function in the application code with a compiler directive
The compiler compiles these functions into IMPICA instructions and wraps the function calls with communication codes

## Slide 29: Page Table Management
The application allocates the memory for its linked data structures with a special API
The OS reserves a portion of the virtual address space as IMPICA regions
The OS maintains the coherence between CPU page table and IMPICA page table in the page fault handler

## Slide 30: IMPICA Page Table Size
Region Table
  4 entries (covers a 2TB memory range)
  68 B
Flat page table (each)
  220 entries
  8 MB
Small page table (each)
  29 entries
  4 KB

## Slide 31: Handling of Multiple Memory Stacks
The OS knows the IMPICA region because of our page table management
The OS always maps the IMPICA region of the same application into the same memory stack, including the corresponding IMPICA page table

## Slide 32: Cache Coherence
We execute every function that operates on the IMPICA regions in the accelerator
It can be extended with more advanced cache coherence mechanism.

## Slide 33: Limit of Parallelism
The parallelism of IMPICA is limited by
  Data RAM size (for call stacks)
  Memory access time vs. address computation time
  The size of the queues
Each IMPICA core can easily parallelize 10 – 15 pointer chasing requests.

## Slide 34: Area and Power Overhead
Power overhead: average power increases by 5.6%
CPU (Cortex-A57) | 5.85 mm2 per core
L2 Cache | 5 mm2 per MB
Memory Controller | 10 mm2
IMPICA (+32KB cache) | 0.45 mm2