## Slide 1: Mitigating Prefetcher-Caused Pollution Using Informed Caching Policies for Prefetched Blocks
Vivek Seshadri
Samihan Yedkar ∙ Hongyi Xin ∙ Onur Mutlu
Phillip B. Gibbons ∙ Michael A. Kozuch ∙ Todd C. Mowry

## Slide 2: Summary
Existing caching policies for prefetched blocks result in cache pollution
Accurate Prefetches (ICP Demotion)
  95% of useful prefetched blocks are used only once!
  Track prefetched blocks in the cache
  Demote prefetched block on cache hit
Inaccurate Prefetches (ICP Accuracy Prediction)
  Existing accuracy prediction mechanisms get stuck in positive feedback
  Self-tuning Accuracy Predictor
ICP (combines both mechanisms)
  Significantly reduces prefetch pollution
  6% performance improvement over 157 2-core workloads

## Slide 3: Caching Policies for Prefetched Blocks
Problem: Existing caching policies for prefetched blocks result in significant cache pollution
Cache Set
MRU
LRU
Cache Miss:
Insertion Policy
Cache Hit:
Promotion Policy
Are these insertion and promotion policies good for prefetched blocks?

## Slide 4: Prefetch Usage Experiment
CPU
L1
L2
L3
Prefetcher
Off-Chip Memory
Monitor L2 misses
Prefetch into L3
Classify prefetched blocks into three categories
1. Blocks that are unused
2. Blocks that are used exactly once before evicted from cache
3. Blocks that are used more than once before evicted from cache

## Slide 5: Usage Distribution of Prefetched Blocks
Chart: Fraction of Prefetched Blocks
| milc | omnetpp | mcf | twolf | bzip2 | gcc | xalancbmk | soplex | vpr | apache20 | tpch17 | art | ammp | tpcc64 | tpch2 | sphinx3 | astar | galgel | tpch6 | GemsFDTD | swim | facerec | zeusmp | cactusADM | leslie3d | equake | lbm | lucas | libquantum | bwaves
Unused | 0.88 | 0.79 | 0.77 | 0.75 | 0.65 | 0.65 | 0.64 | 0.64 | 0.63 | 0.52 | 0.51 | 0.44 | 0.37 | 0.32 | 0.31 | 0.29 | 0.27 | 0.23 | 0.16 | 0.08 | 0.07 | 0.05 | 0.04 | 0.03 | 0.03 | 0.02 | 0.01 | 0.01 | 0 | 0
Used Once | 0.12 | 0.2 | 0.21 | 0.1 | 0.2 | 0.35 | 0.35 | 0.32 | 0.26 | 0.43 | 0.48 | 0.51 | 0.53 | 0.53 | 0.66 | 0.71 | 0.72 | 0.77 | 0.69 | 0.92 | 0.83 | 0.88 | 0.89 | 0.97 | 0.92 | 0.97 | 0.99 | 0.99 | 1 | 1
Used > Once | 0 | 0.01 | 0.02 | 0.15 | 0.15 | 0 | 0.01 | 0.04 | 0.11 | 0.05 | 0.01 | 0.05 | 0.1 | 0.15 | 0.03 | 0 | 0.01 | 0 | 0.15 | 0 | 0.1 | 0.07 | 0.07 | 0 | 0.05 | 0.01 | 0 | 0 | 0 | 0
Many applications have a significant fraction of inaccurate prefetches.
95% of the useful prefetched blocks are used only once!
Typically, large data structures benefit repeatedly from prefetching. Blocks of such data structures are unlikely to be
used more than once!

## Slide 6: Outline
Introduction
ICP – Mechanism
  ICP promotion policy
  ICP insertion policy
Prior Works
Evaluation
Conclusion

## Slide 7: Shortcoming of Traditional Promotion Policy
D
D
D
P
P
D
P
D
Cache Set
MRU
LRU
P
Cache Hit!
Promote to MRU
This is a bad policy. The block is unlikely to be reused in the cache.
This problem exists with state-of-the-art
replacement policies (e.g., DRRIP, DIP)

## Slide 8: ICP Demotion
D
D
D
P
P
D
P
D
Cache Set
MRU
LRU
P
Cache Hit!
Demote to LRU
Ensures that the block is evicted from
the cache quickly after it is used!
Only requires the cache to distinguish between
prefetched blocks and demand-fetched blocks.

## Slide 9: Outline
Introduction
ICP – Mechanism
  ICP promotion policy
  ICP insertion policy
Prior Works
Evaluation
Conclusion

## Slide 10: Cache Insertion Policy for Prefetched Blocks
Cache Set
MRU
LRU
Prefetch Miss:
Insertion Policy?
Good (Accurate prefetch)
Bad (Inaccurate prefetch)
Good (Inaccurate prefetch)
Bad (accurate prefetch)

## Slide 11: Predicting Usefulness of Prefetch
Cache Set
MRU
LRU
Prefetch Miss
Predict Usefulness
of Prefetch
Accurate
Inaccurate
Fraction of Useful Prefetches

## Slide 12: Shortcoming of “Fraction of Useful Prefetches”
Cache Set
MRU
LRU
Prefetch Miss
Accurate
Inaccurate
b
b
b
b
b
b
Threshold
The predictor may get stuck in a state where all prefetches are predicted to be inaccurate!
Accurate prefetches predicted as inaccurate and evicted before use

## Slide 13: ICP Accuracy Prediction
MRU
LRU
Evicted Prefetch Filter
Recently-evicted
Predicted-inaccurate
Prefetched Blocks
P
Demand Request
Miss
Hit
Accurate prefetch mispredicted as inaccurate
Self-tuning Accuracy Predictor.
Reduces error in prediction from 25% to 14%!

## Slide 14: ICP – Summary
ICP Demotion (ICP-D)
  Track prefetched blocks in the cache
  Demote prefetched block to LRU on cache hit
ICP Accuracy Prediction (ICP-AP)
  Maintain accuracy counter for each prefetcher entry
  Evicted Prefetch Filter (EPF): tracks recently-evicted predicted-inaccurate prefetches
  Bump up accuracy counter on cache miss + EPF hit
Hardware Cost: only 12KB for a 1MB cache

## Slide 15: Outline
Introduction
ICP – Mechanism
  ICP promotion policy
  ICP insertion policy
Prior Works
Evaluation
Conclusion

## Slide 16: Prior Works
Feedback Directed Prefetching (FDP) (Srinath+ HPCA-07)
  Use pollution filter to determine degree of prefetch pollution
  Insert all prefetches at LRU if pollution is high
  Can insert accurate prefetches at LRU
Prefetch-Aware Cache Management (PACMan) (Wu+ MICRO-11)
  Insert prefetches both into L2 and L3
  Accesses to L3 filtered by L2 (directly insert at LRU in L3)
  Does not mitigate pollution at L2!

## Slide 17: Outline
Introduction
ICP – Mechanism
  ICP promotion policy
  ICP insertion policy
Prior Works
Evaluation
Conclusion

## Slide 18: Methodology
Simulator (released publicly) http://www.ece.cmu.edu/~safari/tools/memsim.tar.gz
  1-8 cores, 4Ghz, In-order/Out-of-order
  32KB private L1 cache, 256KB private L2 cache
  Aggressive stream prefetcher (16-entries/core)
  Shared L3 cache (1MB/core)
  DDR3 DRAM Memory
Workloads
  SPEC CPU2006, TPCC, TPCH, Apache
  157 2-core, 20 4-core, and 20 8-core workloads
Metrics
  Prefetch lifetime (measure of prefetch pollution)
  IPC, Weighted Speedup, Harmonic Speedup, Maximum Slowdown

## Slide 19: Single Core – Prefetch Lifetime
Chart: Prefetch Lifetime (Number of misses)
| libquantum | omnetpp | art | gmean
Baseline | 16 | 15.49 | 16 | 13.81
PACMan | 15.99 | 4.99 | 14.97 | 10.74
ICP-D | 1 | 12.5 | 8.12 | 4.6
ICP-AP | 15.97 | 4.42 | 11.61 | 7.74
ICP | 1 | 2.08 | 4.73 | 2.06
0%
7%
24%
3%
Performance Improvement of ICP over Baseline
ICP significantly reduces prefetch pollution without losing the benefit of prefetching!

## Slide 20: 2-Core Performance
Chart: Weighted Speedup Improvement
| Type-1 | Type-2 | Type-3 | Type-4 | Type-5 | All
PACMan | 0.2 | 0.2 | 0.2 | 1 | 1 | 0.5
ICP-D | 0.2 | 10 | 7 | 6 | 1 | 5
ICP-AP | 0.2 | 0.2 | 0 | 2 | 2 | 1
ICP | 1 | 10 | 7 | 8 | 2 | 6
Inaccurate
Inaccurate & Accurate
Accurate
No Pollution
ICP significantly improves system performance!
6% across 157 2-core workloads

## Slide 21: Other Results in the Paper
Sensitivity to cache size and memory latency
Sensitivity to number of cores
Sensitivity to cache replacement policy (LRU, DRRIP)
Performance with out-of-order cores
Benefits with stride prefetching
Comparison to other prefetcher configurations

## Slide 22: Conclusion
Existing caching policies for prefetched blocks result in cache pollution
Accurate Prefetches (ICP Demotion)
  95% of useful prefetched blocks are used only once!
  Track prefetched blocks in the cache
  Demote prefetched block on cache hit
Inaccurate Prefetches (ICP Accuracy Prediction)
  Existing accuracy prediction mechanisms get stuck in positive feedback
  Self-tuning Accuracy Predictor
ICP (combines both mechanisms)
  Significantly reduces prefetch pollution
  6% performance improvement over 157 2-core workloads

## Slide 23: Mitigating Prefetcher-Caused Pollution Using Informed Caching Policies for Prefetched Blocks
Vivek Seshadri
Samihan Yedkar ∙ Hongyi Xin ∙ Onur Mutlu
Phillip B. Gibbons ∙ Michael A. Kozuch ∙ Todd C. Mowry