## Slide 1: OWL: Cooperative Thread Array (CTA) Aware Scheduling Techniques for Improving GPGPU Performance
Adwait Jog, Onur Kayiran, Nachiappan CN, Asit Mishra, Mahmut Kandemir, Onur Mutlu, Ravi Iyer, Chita Das
Notes: This work is jointly performed with my collaborators at Penn State, Intel and CMU.

## Slide 2
Source: nVIDIA
GPUs are everywhere!
Super Computers
Desktops
Laptops
Tablets
Smartphones
Gaming Consoles
Notes: GPUs are used from smart-phones to supercomputers.
They are getting popular as they are capable of executing graphics as well as general
purpose applications.
In this talk, I will be presenting a series of scheduling techniques to improve
GPGPU performance.

## Slide 3: Executive Summary
Limited DRAM bandwidth is a critical performance bottleneck
Thousands of concurrently executing threads on a GPU
  May not always be enough to hide long memory latencies
  Access small size caches  High cache contention
Proposal: A comprehensive scheduling policy, which
  Reduces Cache Miss Rates
  Improves DRAM Bandwidth
  Improves Latency Hiding Capability of GPUs
Notes: To start with, let us understand the critical issues we have to deal with. In this paper, we show that limited DRAM b/w is a critical bottleneck for many GPGPU apps.
Although thousands of threads can be executed concurrently on a GPU, it may not always be enough to hide long memory latencies.
Also, these threads access small caches of GPUs, leading to high cache contention, and high miss rates
making the cache not very effective.
There are many ways to overcome this issue, but in this paper, we propose scheduling policy,
Which improves cache performance, DRAM b/w and latency hiding capability.

## Slide 4: Off-chip Bandwidth is Critical!
Percentage of total execution cycles wasted waiting for the data to come back from DRAM
Chart: 
| SAD | PVC | SSC | BFS | MUM | CFD | KMN | SCP | FWT | IIX | SPMV | JPEG | BFSR | SC | FFT | SD2 | WP | PVR | BP | CON | AES | SD1 | BLK | HS | SLA | DN | LPS | NN | PFN | LYTE | LUD | MM | STO | CP | NQU | CUTP | HW | TPAF | AVG | AVG-T1
 | 0.90269 | 0.86445 | 0.82241 | 0.6484 | 0.71382 | 0.60663 | 0.60584 | 0.43943 | 0.47385 | 0.64708 | 0.64635 | 0.51687 | 0.46336 | 0.4493 | 0.29411 | 0.28971 | 0.47774 | 0.26293 | 0.24463 | 0.16514 | 0.18735 | 0.13915 | 0.15322 | 0.094841 | 0.11532 | 0.1988 | 0.10324 | 0.10689 | 0.048452 | 0.13028 | 0.088976 | 0.041891 | 0.012271 | 0.011149 | 0.00013977 | 0.0053883 | 0.0050535 | 0.0021302 | 0.31524 | 0.54577
Type-1
Applications
55%
AVG: 32%
Type-2
Applications
GPGPU Applications
Notes: So off-chip b/w is critical.
We characterize 38 GPGPU applications taken from various application suites and calculated the percentage of execution cycles wasted waiting for the data to come back
from main memory.
Average across all 38 GPGPU apps considered is 32%.
For Applications on the left, which are termed as Type-1 applications, suffer the most because of limited off-chip b/w. The average percentage is about 55%.
For Applications on the right, which are termed as Type-2 applications, seem to perform well on GPUs, as the percentages are lower.
In this paper, we focus on Type-1 applications (without hurting the performance of Type-2) application and propose scheduling schemes to improve their
Performance.

## Slide 5: Outline
Introduction
Background
CTA-Aware Scheduling Policy
  1. Reduces cache miss rates
  2. Improves DRAM Bandwidth
Evaluation
Results and Conclusions
Notes: Before going into details of our scheduling scheme, let us revisit some of the background

## Slide 6: High-Level View of a GPU
DRAM
SIMT Cores
…
Scheduler
ALUs
L1 Caches
Threads
…
W
W
W
W
W
W
Warps
L2 cache
Interconnect
CTA
CTA
CTA
CTA
Cooperative
Thread
Arrays
(CTAs)
Notes: In a GPU, there are multiple SIMT cores.
The memory requests generated via these cores are then served by memory channels each attached with L2 cache.
Each SIMT core is associated with L1 caches and ALUs. There are 10s of thousands of thread than can be launched on a core.
A scheduler Associated with each core schedules these threads onto the SIMT units at the core.
These Cores are then grouped into warps which in turn group as CTAs or thread blocks.

## Slide 7: CTA-Assignment Policy (Example)
Warp Scheduler
ALUs
L1 Caches
Warp Scheduler
ALUs
L1 Caches
Multi-threaded CUDA Kernel
SIMT Core-1
SIMT Core-2
CTA-1
CTA-2
CTA-3
CTA-4
CTA-2
CTA-4
CTA-1
CTA-3
Notes: Lets us understand how these thread blocks / CTAs are assigned on multiple SIMT cores on a GPU.
A CUDA kernel, which consists of multiple CTAs is shown.
A Breadth first policy is used, where CTA – 1 goes to core 1 and CTA 2 goes to core 2 etc.

## Slide 8: Warp Scheduling Policy
All launched warps on a SIMT core have equal priority
  Round-Robin execution
Problem: Many warps stall at long latency operations roughly at the same time
W
W
CTA
W
W
CTA
W
W
CTA
W
W
CTA
All warps compute
All warps have equal priority
W
W
CTA
W
W
CTA
W
W
CTA
W
W
CTA
All warps compute
All warps have equal priority
Send Memory Requests
SIMT Core Stalls
Time
Notes: Traditional warp scheduling is round robin and have equal priority. These warps are executed
by the scheduler in round-robin fashion. The problem is that, many warps stall at long latency operations (memory accesses)
roughly at the same time. So how it works is;
Four CTAs on a core and all warps have equal priority and execute in round-robin
Fashion.
After they stall, they send memory requests and core has nothing to
Execute while waiting for the data.
As soon as data of warps of some CTAs
Come back and execution can proceed

## Slide 9: Solution
W
W
CTA
W
W
CTA
W
W
CTA
W
W
CTA
W
W
CTA
W
W
CTA
W
W
CTA
W
W
CTA
Send Memory Requests
Saved Cycles
W
W
CTA
W
W
CTA
W
W
CTA
W
W
CTA
All warps compute
All warps have equal priority
W
W
CTA
W
W
CTA
W
W
CTA
W
W
CTA
All warps compute
All warps have equal priority
Send Memory Requests
SIMT Core Stalls
Time
Form Warp-Groups
(Narasiman MICRO’11)
CTA-Aware grouping
Group Switch is Round-Robin
Notes: One of the solution proposed is to make warp groups.
In this paper, as a starting point, we use CTA-aware grouping where warp groups are formed with CTA boundaries into
Consideration.
So what it means in this figure is that , One group = 1 CTA and each CTA has enough warps to fill the Pipeline.
So, now warps of first group are prioritized over others and as soon as they stall and send memory Request, scheduler moves to another group.
Note that, the group switch is round-robin here.
With this policy, the advantage is that memory requests of some groups are sent earlier and
Hence cycles can be saved as shown.

## Slide 10: Outline
Introduction
Background
CTA-Aware Scheduling Policy "OWL"
  1. Reduces cache miss rates
  2. Improves DRAM bandwidth
Evaluation
Results and Conclusions
Notes: Okay, we are now all set to understand our scheduling scheme, called OWL.
This policy is based on two philosophies.

## Slide 11: OWL Philosophy (1)
OWL focuses on "one work (group) at a time"
Notes: OWL based on one group at a time of philosophy and does one work at a time (Unlike this person)

## Slide 12: OWL Philosophy (1)
What does OWL do?
  Selects a group (Finds food)
  Always prioritizes it (Focuses on food)
Group switch is NOT round-robin
Benefits:
  Lesser Cache Contention
  Latency hiding benefits via grouping are still present
Notes: Here, I am talking about the bird owl. Not the scheduler.
When an owl is flying, and when it finds a lot of food – it focuses on a particular food and catches it and ignores the others
Similar to that – our scheduling policy. Selects a group. And always prioritizes it.
Group switch is now not round robin (I will explain that it in a second)
Benefits:

## Slide 13: Objective 1: Improve Cache Hit Rates
CTA 1
CTA 3
CTA 5
CTA 7
CTA 1
CTA 3
CTA 5
CTA 7
Data for CTA1 arrives.
No switching.
CTA 3
CTA 5
CTA 7
CTA 1
CTA 3
C5
CTA 7
CTA 1
C5
Data for CTA1 arrives.
T
No Switching: 4 CTAs in Time T
Switching: 3 CTAs in Time T
Fewer CTAs accessing the cache concurrently  Less cache contention
Time
Switch to CTA1.
Notes: Four CTAs are launched on a core. Assume that one group = 1 CTA. In the previous
Default two-level policy (CTA-grouping), the CTA group switch is round robin.
So,
As soon as data for the group 1 comes back from DRAM, it continues to schedule
Groups in round robin fashion.
What OWL does it , it schedules back to CTA 1. The advantage of doing that is,
That in time T, there are 4 CTAs executing in time T, but only 3 CTAs execute in
Time T.
Fewer CTAs access the cache concurrently  Less cache contention

## Slide 14: Reduction in L1 Miss Rates
Limited benefits for cache insensitive applications
Additional analysis in the paper.
Chart: Normalized L1 Miss Rates
| SAD | SSC | BFS | KMN | IIX | SPMV | BFSR | AVG.
Round Robin | 1 | 1 | 1 | 1 | 1 | 1 | 1 | 1
CTA-Aware | 0.94271 | 0.99326 | 0.99321 | 0.73362 | 0.72977 | 1.0029 | 0.98306 | 0.91123
CTA-Aware-Locality | 0.58145 | 0.92471 | 0.82816 | 0.50542 | 0.03893 | 0.92099 | 0.83576 | 0.6622
8%
18%
Round-Robin
CTA-Grouping
CTA-Grouping-Prioritization
Notes: CTA-grouping leads to 8% L1 miss rate across all type-1 apps
And OWL techniques leads to 18% over RR.
Only Cache Sensitive applications

## Slide 15: Outline
Introduction
Background
CTA-Aware Scheduling Policy "OWL"
  1. Reduces cache miss rates
  2. Improves DRAM bandwidth (via enhancing bank-level parallelism and row buffer locality)
Evaluation
Results and Conclusions
Notes: Now let us understand how it improves DRAM b/w.
So, in this paper, we improve DRAM b/w by improving bLP and row locality.
Before going to that,
Let us revisit some CTA properties.

## Slide 16: More Background
Independent execution property of CTAs
  CTAs can execute and finish in any order
CTA DRAM Data Layout
  Consecutive CTAs (in turn warps) can have good spatial locality
  (more details to follow)
Notes: CTA properties:
CTA can execute and finish in any order.

## Slide 17: CTA Data Layout (A Simple Example)
A(0,0) | A(0,1) | A(0,2) | A(0,3)
 | : |  | 
 | : |  | 
DRAM Data Layout (Row Major)
Bank 1
Bank 2
Bank 3
Bank 4
A(1,0) | A(1,1) | A(1,2) | A(1,3)
 | : |  | 
 | : |  | 
A(2,0) | A(2,1) | A(2,2) | A(2,3)
 | : |  | 
 | : |  | 
A(3,0) | A(3,1) | A(3,2) | A(3,3)
 | : |  | 
 | : |  | 
Data Matrix
A(0,0) | A(0,1) | A(0,2) | A(0,3)
A(1,0) | A(1,1) | A(1,2) | A(1,3)
A(2,0) | A(2,1) | A(2,2) | A(2,3)
A(3,0) | A(3,1) | A(3,2) | A(3,3)
mapped to Bank 1
CTA 1
CTA 2
CTA 3
CTA 4
mapped to Bank 2
mapped to Bank 3
mapped to Bank 4
Average percentage of consecutive CTAs (out of total CTAs) accessing the same row = 64%
Notes: To understand this consider a simple example. This is very simplified view of the CTA
DRAM layout. Assume that CTA 1 requires the left quadrant of the data matrix CTA 2 on
The 2nd quadrant etc. If you see how this data is mapped to the banks, the row 1
Is mapped to bank-1 , row 2 to bank 2 etc. Which means that data for CTA 1 and
CTA 2 (consecutive CTAs) are mapped to the same banks. We calculate this
Consecutive CTA percentage across all these apps, it turned out to be very
High (64). It contains many irregular apps.

## Slide 18: Implications of high CTA-row sharing
L2 Cache
W
CTA-1
W
CTA-3
W
CTA-2
W
CTA-4
SIMT Core-1
SIMT Core-2
Bank-1
Bank-2
Bank-3
Bank-4
Row-1
Row-2
Row-3
Row-4
Idle Banks
W
W
W
W
CTA Prioritization Order
CTA Prioritization Order
Notes: Let us understand, what are the implication of high row sharing.
If at core 1, CTA 1 is being priortized at core 1 and CTA 2 at core 2
Because of high CTA row sharing, the CTAs will be accessing
Smaller set of DRAM banks, rather than all the banks.
To understand this better, let us consider this cartoon

## Slide 19: Analogy
THOSE WHO HAVE TIME:
STAND IN LINE HERE
THOSE WHO DON’T HAVE TIME:
STAND IN LINE HERE
Counter 1
Counter 2
Which counter will you prefer?
Notes: One counter is titled as…
One counter is titled as …
Since, we are very busy…

## Slide 20: Which counter will you prefer?
THOSE WHO HAVE TIME:
STAND IN LINE HERE
THOSE WHO DON’T HAVE TIME:
STAND IN LINE HERE
Counter 1
Counter 2
Notes: Many up land in counter 2, thinking that their work will be done faster.

## Slide 21
High Row Locality
Low Bank Level Parallelism
Bank-1
Row-1
Bank-2
Row-2
Bank-1
Row-1
Bank-2
Row-2
Req
Req
Req
Req
Req
Req
Req
Req
Req
Req
Lower Row Locality
Higher Bank Level Parallelism
Req
Notes: Coming back to computer science, we see that one of the banks is swamped up with lot
Of requests. Although they might have good row locality, they might not exploit
The bank-level parallelism. So it will be better, if BLP is improved and load can be
Balanced with some sacrifice on row locality

## Slide 22: OWL Philosophy (2)
What does OWL do now?
  Intelligently selects a group (Intelligently finds food)
  Always prioritizes it (Focuses on food)
OWL selects non-consecutive CTAs across cores
  Attempts to access as many DRAM banks as possible.
Benefits:
  Improves bank level parallelism
  Latency hiding and cache hit rates benefits are still preserved
Notes: Now OWL has become more intelligent
I will explain it in a second

## Slide 23: Objective 2: Improving Bank Level Parallelism
L2 Cache
W
CTA-1
W
CTA-3
W
CTA-2
W
CTA-4
SIMT Core-1
SIMT Core-2
Bank-1
Bank-2
Bank-3
Bank-4
Row-1
Row-2
Row-3
Row-4
W
W
W
W
11% increase in bank-level parallelism
14% decrease in row buffer locality
CTA Prioritization Order
CTA Prioritization Order
Notes: Blp Increases, locality decreases, by changing the priortization order.
To mitigate the effects of 14%loss of row locality, we propose a simple memory side
prefetching

## Slide 24: Objective 3: Recovering Row Locality
L2 Cache
W
CTA-1
W
CTA-3
W
CTA-2
W
CTA-4
SIMT Core-2
Bank-1
Bank-2
Bank-3
Bank-4
Row-1
Row-2
Row-3
Row-4
W
W
W
W
Memory Side
Prefetching
L2 Hits!
SIMT Core-1
Notes: Which will mitigate the effects of lost row locality

## Slide 25: Outline
Introduction
Background
CTA-Aware Scheduling Policy "OWL"
  1. Reduces cache miss rates
  2. Improves DRAM bandwidth
Evaluation
Results and Conclusions
Notes: How to mitigate this problem:
By improving cache performance, improving DRAM bandwidth.

## Slide 26: Evaluation Methodology
Evaluated on GPGPU-Sim, a cycle accurate GPU simulator
Baseline Architecture
  28 SIMT cores, 8 memory controllers, mesh connected
  1300MHz, SIMT Width = 8, Max. 1024 threads/core
  32 KB L1 data cache, 8 KB Texture and Constant Caches
  GDDR3 800MHz
Applications Considered (in total 38) from:
  Map Reduce Applications
  Rodinia – Heterogeneous Applications
  Parboil – Throughput Computing Focused Applications
  NVIDIA CUDA SDK – GPGPU Applications
Notes: We used GPGPU-Sim and details on baseline architecture is listed.
We consider in total 38 apps which are selected from various app suites..

## Slide 27: IPC results (Normalized to Round-Robin)
Chart: Normalized IPC
| SAD | PVC | SSC | BFS | MUM | CFD | KMN | SCP | FWT | IIX | SPMV | JPEG | BFSR | SC | FFT | SD2 | WP | PVR | BP | AVG - T1
CTA-Aware-Locality | 1.4907 | 2.5914 | 1.0703 | 1.0784 | 1.0242 | 1.0456 | 1.6365 | 1.1854 | 1.1239 | 2.028 | 1.0952 | 1.1297 | 1.0838 | 1.0112 | 1.073 | 1.0729 | 1 | 1.0057 | 1.0722 | 1.2536
CTA-Aware-Locality-BLP | 1.6508 | 2.8029 | 1.0822 | 1.0893 | 1.1031 | 1.0581 | 1.7363 | 1.2388 | 1.1342 | 2.2665 | 1.1403 | 1.2317 | 1.1098 | 1.0118 | 1.1674 | 0.97198 | 1 | 1.0269 | 1.1318 | 1.3134
OWL | 1.6508 | 2.8029 | 1.0822 | 1.1 | 1.14 | 1.11 | 1.7363 | 1.2388 | 1.16 | 2.2665 | 1.18 | 1.38 | 1.1098 | 1.0321 | 1.1674 | 1.02 | 1 | 1.0269 | 1.13 | 1.3334
Perfect-L2 | 1.6654 | 2.8371 | 1.0845 | 1.1273 | 1.3129 | 1.12 | 1.9889 | 1.7176 | 1.4083 | 2.2721 | 1.2074 | 1.5803 | 1.1712 | 1.1373 | 1.1789 | 1.2282 | 1.088 | 1.0615 | 1.1889 | 1.4399
11% within Perfect L2
More details in the paper
44%
Notes: Labeling
Performance improvement  scheme 1

## Slide 28: Conclusions
Many GPGPU applications exhibit sub-par performance, primarily because of limited off-chip DRAM bandwidth
OWL scheduling policy improves –
  Latency hiding capability of GPUs (via CTA grouping)
  Cache hit rates (via CTA prioritization)
  DRAM bandwidth
  (via intelligent CTA scheduling and prefetching)
33% average IPC improvement over round-robin warp scheduling policy, across type-1 applications

## Slide 29: Thanks! QUESTIONS?

## Slide 30: OWL: Cooperative Thread Array (CTA) Aware Scheduling Techniques for Improving GPGPU Performance
Adwait Jog, Onur Kayiran, Nachiappan CN, Asit Mishra, Mahmut Kandemir, Onur Mutlu, Ravi Iyer, Chita Das

## Slide 31: Related Work
Warp Scheduling: (Rogers+ MICRO 2012, Gebhart+, ISCA 2011, Narasiman+ MICRO 2011)
DRAM scheduling: (Ausavarungnirun+ ISCA 2012, Lakshminarayana+ CAL 2012, Jeong+ HPCA 2012, Yuan+ MICRO 2009)
GPGPU hardware prefetching: (Lee+, MICRO 2009)

## Slide 32: Memory Side Prefetching
Prefetch the so-far-unfetched cache lines in an already open row into the L2 cache, just before it is closed
What to prefetch?
  Sequentially prefetches the cache lines that were not accessed by demand requests
  Sophisticated schemes are left as future work
When to prefetch?
  Opportunsitic in Nature
  Option 1: Prefetching stops as soon as demand request comes for another row. (Demands are always critical)
  Option 2: Give more time for prefetching, make demands wait if there are not many. (Demands are NOT always critical)

## Slide 33: CTA row sharing
Our experiment driven study shows that:
  Across 38 applications studied, the percentage of consecutive CTAs (out of total CTAs) accessing the same row is 64%, averaged across all open rows.
  Ex: if CTAs 1, 2, 3, 4 all access a single row, the CTA row sharing percentage is 100%.
  The applications considered include many irregular applications, which do not show high row sharing percentages.