## Slide 1: Orchestrated Scheduling and Prefetching for GPGPUs
Adwait Jog, Onur Kayiran, Asit Mishra, Mahmut Kandemir, Onur Mutlu, Ravi Iyer, Chita Das

## Slide 2
Multi-threading
Caching
Prefetching
Main Memory
Improve
Replacement Policies
  Parallelize your code!
  Launch more threads!
Improve Memory Scheduling Policies
Improve Prefetcher
(look deep in the future, if you can!)
Is the Warp Scheduler
aware of these techniques?
Notes: What are some of the classic ways to improve the memory performance of almost any computing system. First is Multithreading. You attempt to parallelize your code as much as possible, so that you can launch all those threads! Second is Caching: Various interesting cache replacement polices and cache architectures have been proposed for effective caching.
Third is Improving DRAM bandwidth utilization. One of the ways is to improve memory scheduling policies. Fourth is prefetching techniques. Many sophisticated prefetching schemes are proposed to predict future accesses…
So a question we ask ourselves In the context of GPGPUs, “Is the warp scheduler at the core aware of these techniques?”
It turns out that an aware warp scheduler can shape the memory access patterns in such a manner
that can complement the above techniques and improve their effectiveness.

## Slide 3
Multi-threading
Caching
Prefetching
Main Memory
Cache-Conscious Scheduling, MICRO’12
Two-level Scheduling
MICRO’11
Thread-Block-Aware Scheduling (OWL)
ASPLOS’13
?
Aware
Warp
Scheduler
Notes: Some of the previous works have developed aware warp schedulers. Two Level warp Scheduler was proposed to improve the latency tolerance further in GPGPUs. We will discuss this in detail later in my talk. To improve the caching efficiency, cache conscious scheduling was proposed. To improve the DRAM bandwidth utilization our previous work has proposed thread-block aware warp scheduling policies. In this talk, we propose a prefetch aware
Warp scheduler to improve the prefetching effectiveness

## Slide 4: Our Proposal
Prefetch Aware Warp Scheduler
Goals:
  Make a Simple prefetcher more Capable
  Improve system performance by orchestrating scheduling and prefetching mechanisms
25% average IPC improvement over
  Prefetching + Conventional Warp Scheduling Policy
7% average IPC improvement over
  Prefetching + Best Previous Warp Scheduling Policy
Notes: The goal of this scheduler is to: make simple prefetcher more capable. Also, it improves the system performance by orchestrating scheduling and prefetching mechanisms. We observe 25% IPC improvement over the case when prefetching is orchestrated with conventional round-robin policy.
And 7% when prefetching is orchestrated with best previous warp scheduling policy.

## Slide 5: Outline
Proposal
Background and Motivation
Prefetch-aware Scheduling
Evaluation
Conclusions
Notes: This is the outline of my talk. I will first give some background on GPUs and typical scheduling policies. Further, I will motivate the need of Prefetch aware warp scheduler followed by its details. I will discuss some of the evaluated metrics associated with this work and wrap-up with final conclusions. Lets start with the background.

## Slide 6: High-Level View of a GPU
DRAM
Streaming Multiprocessors (SMs)
…
Scheduler
ALUs
L1 Caches
Threads
…
W
W
W
W
W
W
Warps
L2 cache
Interconnect
CTA
CTA
CTA
CTA
Cooperative
Thread Arrays
(CTAs) Or
Thread Blocks
Prefetcher
Notes: In a GPU, there are multiple streaming multiprocessors, shown as SMs in the figure. The memory requests generated via these SMs are then served by memory channels each attached with L2 cache.
Each SM is associated with L1 caches and ALUs. Thousands of thread than can be launched on a SM. A scheduler associated with each SM schedules these threads onto the SIMT units of the SM. These threads are then grouped into warps which in turn group as CTAs or thread blocks. In this work, we have assumed a L1 prefetcher with each SM, which prefetches data to the L1 data cache.

## Slide 7: Warp Scheduling Policy
Equal scheduling priority
  Round-Robin (RR) execution
Problem: Warps stall roughly at the same time
SIMT Core Stalls
Time
Compute Phase (2)
W1
W2
W3
W4
W5
W6
W7
W8
W1
W2
W3
W4
W5
W6
W7
W8
Compute
Phase (1)
DRAM
Requests
D1
D2
D3
D4
D5
D6
D7
D8
Notes: Traditional warp scheduling is round robin and have equal priority. These warps are executed by the scheduler in round-robin fashion.
<CLICK> The problem is that, many warps stall at long latency operations (memory accesses) roughly at the same time. To understand how it works, consider a simple example:
Let us assume that 8 warps are launched on a SM, and they have associated compute phase 1. As all of them have equal scheduling priority, many of them stall and send their corresponding DRAM requests. The DRAM requests are marked as D1 to D8, where D1 is DRAM request for Warp 1. During this time SM has nothing to execute, as shown in the figure. As soon as data of some warps come back to the SM execution can proceed and compute phase (2) can start. This policy severely decreases SM utilization as it has no useful work to do, while waiting for the data.

## Slide 8
Time
SIMT Core Stalls
Compute Phase (2)
W1
W2
W3
W4
W5
W6
W7
W8
W1
W2
W3
W4
W5
W6
W7
W8
Compute
Phase (1)
DRAM
Requests
D1
D2
D3
D4
D5
D6
D7
D8
Compute
Phase (1)
Compute
Phase (1)
Group 2
Group 1
W1
W2
W3
W4
W5
W6
W7
W8
DRAM
Requests
D1
D2
D3
D4
Comp. Phase (2)
Group 1
W1
W2
W3
W4
D5
D6
D7
D8
Comp. Phase (2)
Group 2
W5
W6
W7
W8
Saved
Cycles
TWO LEVEL (TL) SCHEDULING
Notes: One of the solution proposed is two level scheduling, where warp groups are formed. For example, in this case <CLICK>
So, now warps of first group are prioritized over others and as soon as they stall and send their corresponding memory requests,
scheduler moves to another group. Note that, the group switch is round-robin here. With this policy, the advantage is that memory
requests of some groups are sent earlier and, hence cycles can be saved as shown.

## Slide 9
Accessing DRAM …
Idle for a
period
W1
W2
W3
W4
W5
W6
W7
W8
Bank 1
Bank 2
Memory Addresses
X
X + 1
X + 2
X + 3
Y
Y + 1
Y + 2
Y + 3
Group 1
Bank 1
Bank 2
W1
W2
W3
W4
W5
W6
W7
W8
Group 2
Legend
Low Bank-Level Parallelism
High Row Buffer Locality
High Bank-Level Parallelism
High Row Buffer Locality
Notes: This shows how DRAM is accessed when RR scheduling is employed. As all requests are given equal priority, most of the requests all received by the banks roughly at the same time.
Also, lets see what are the memory addresses generated by these warps. <<<>>>>
It is known that there is significant high spatial locality among consecutive warps, and hence data of first four warps are mapped to bank-1, but as we go across many warps, these patches of spatial locality can be completely unrelated. For example, as shown in the figure, the data of first four warps Is mapped to bank-1 shown by X through X + 3. Similarly, for the next group, let us assume that it is mapped to bank-2.
When RR scheduling is employed both bank-level parallelism and Row buffer locality is high. BLP is high because, both the banks are being accessed. Row buffer locality is also high as the all the data copied to DRAM row associated with a bank has potential to be highly utilized.
When two level scheduling is used, because of the higher priority given to First group, only of the banks is accessed, thereby other bank has idle time. This lowers the bank-level parallelism, but row buffer locality is still high. For bank-1 as all associated requests are issued together in this example.

## Slide 10: Warp Scheduler Perspective (Summary)
Warp Scheduler | Forms Multiple Warp Groups? | DRAM Bandwidth Utilization | 
 |  | Bank Level Parallelism | Row Buffer Locality
Round- Robin (RR) | ✖ | ✔ | ✔
Two-Level (TL) | ✔ | ✖ | ✔
Notes: Now, let us evaluate our warp schedulers against the perfect case, when all the memory
Requests hit in L1 cache.

## Slide 11: Evaluating RR and TL schedulers
Chart: 
| SSC | PVC | KMN | SPMV | BFSR | FFT | SCP | BLK | FWT | JPEG | GMEAN
Round-robin (RR) | 6.8705 | 6.2469 | 3.2741 | 2.3168 | 1.6432 | 1.5 | 1.4654 | 1.3922 | 1.3223 | 1.2206 | 2.1988
Two-level (TL) | 6.3562 | 2.6245 | 2.2269 | 2.276 | 1.629 | 1.7657 | 1.4505 | 1.1159 | 1.2387 | 1.1402 | 1.8815
IPC Improvement factor with Perfect L1 Cache
Can we further reduce this gap?
Via Prefetching ?
2.20X
1.88X
Notes: This graph shows the performance gap between perfect L1 cache and RR scheduler.
Y axis is shown as in terms of IPC improvement factor. X axis are set of evaluated applications coming
From various suites. These suites are described later. Second, bar
Shows the gap between perfect L1 cache and TL scheduler.
The two-level warp scheduler reduces the performance impact of L1 cache misses on
performance, as shown by the lower IPC improvement obtained,
So, the question is it useful to incorporate another memory latency tolerance
technique – prefetching, to support these schedulers and reduce this gap
Further?

## Slide 12
Time
DRAM
Requests
Compute
Phase (1)
D1
D2
D3
D4
D5
D6
D7
D8
(1) Prefetching: Saves more cycles
Compute
Phase (1)
Comp. Phase (2)
Comp. Phase (2)
Compute
Phase (1)
DRAM
Requests
D1
D2
D3
D4
Compute
Phase (1)
Comp. Phase (2)
Saved
Cycles
RR
TL
P5
P6
P7
P8
Prefetch Requests
Saved
Cycles
Compute Phase-2 (Group-2) Can Start
Comp. Phase (2)
(A)
(B)
Notes: So, lets see if prefetching works with the better of two schedulers, Two level scheduler. We have the same setup again, from the
Background. We observe that SM is idle between two groups of compute phase 2, shown by (A) and (B)

## Slide 13
Bank 1
Bank 2
X
X + 1
X + 2
X + 3
Y
Y + 1
Y + 2
Y + 3
Memory Addresses
Idle for
a period
(2) Prefetching: Improve DRAM Bandwidth Utilization
W1
W2
W3
W4
W5
W6
W7
W8
Bank 1
Bank 2
W1
W2
W3
W4
W5
W6
W7
W8
Prefetch
Requests
No Idle period!
High Bank-Level Parallelism
High Row Buffer Locality
Notes: If done accurately

## Slide 14
X
X + 1
X + 2
X + 3
Y
Y + 1
Y + 2
Y + 3
Memory Addresses
Challenge: Designing a Prefetcher
Bank 1
Bank 2
W1
W2
W3
W4
W5
W6
W7
W8
Prefetch
Requests
X
Y
X
Sophisticated Prefetcher
Y
Notes: We observe that prefetching can save cycles but potentially requires a sophisctaed prefetcher
To determine address Y. In fact, there might be no relation between X and Y, which makes it
More difficult to design.

## Slide 15: Our Goal
Keep the prefetcher simple, yet get the performance benefits of a sophisticated prefetcher.
To this end, we will design a prefetch-aware warp scheduling policy
A simple prefetching does not improve performance with existing scheduling policies.
Why?

## Slide 16
Time
DRAM
Requests
D1
D2
D3
D4
D5
D6
D7
D8
P2
D3
P4
P6
D5
D7
P8
Simple Prefetching + RR scheduling
Compute
Phase (1)
Time
D1
DRAM
Requests
Compute
Phase (1)
Compute Phase (2)
No Saved Cycles
Overlap with D2 (Late Prefetch)
Compute Phase (2)
RR
Overlap with D4
(Late Prefetch)
Notes: When one warp issues its memory request, a prefetch request is generated based on its address.

## Slide 17
Time
DRAM
Requests
D1
D2
D3
D4
D5
D6
D7
D8
Simple Prefetching + TL scheduling
P2
D3
P4
Saved
Cycles
Group 2
Group 1
Group 2
Group 1
Compute
Phase (1)
Compute
Phase (1)
D1
Group 2
Group 1
Compute
Phase (1)
Compute
Phase (1)
Comp. Phase (2)
Group 1
Comp. Phase (2)
Comp. Phase (2)
RR
TL
Overlap with D2 (Late Prefetch)
Overlap with D4 (Late Prefetch)
D5
P6
D7
P8
Group 2
Comp. Phase (2)
No Saved Cycles (over TL)
Notes: Focus on late prefetches
Also doesn’t affect DRAM utilizate requests are overlap

## Slide 18: Let’s Try…
X
Simple
Prefetcher
X + 4

## Slide 19
X
X + 1
X + 2
X + 3
Y
Y + 1
Y + 2
Y + 3
Memory Addresses
Simple Prefetching with TL scheduling
Bank 1
Bank 2
Idle for a period
W1
W2
W3
W4
W5
W6
W7
W8
X + 4
May not be equal to
Y
UP1 UP2 UP3 UP4
Bank 1
Bank 2
W1
W2
W3
W4
W5
W6
W7
W8
Useless Prefetches
Useless Prefetch
(X + 4)

## Slide 20
Time
DRAM
Requests
D1
D2
D3
D4
D5
D6
D7
D8
Simple Prefetching with TL scheduling
DRAM
Requests
D1
D2
D3
D4
Saved
Cycles
D5
D6
D7
D8
Compute
Phase (1)
Compute
Phase (1)
Compute
Phase (1)
Compute
Phase (1)
Comp. Phase (2)
Comp. Phase (2)
Comp. Phase (2)
Comp. Phase (2)
TL
RR
No Saved Cycles (over TL)
U5
U6
U7
U8
Useless Prefetches
Notes: For better visualization, Useless Prefetches are shown together. In reality, they can be interleaved with demand requests.

## Slide 21: Warp Scheduler Perspective (Summary)
Warp Scheduler | Forms Multiple Warp Groups? | Simple Prefetcher Friendly? | DRAM Bandwidth Utilization | 
 |  |  | Bank Level Parallelism | Row Buffer Locality
Round-Robin (RR) | ✖ | ✖ | ✔ | ✔
Two-Level (TL) | ✔ | ✖ | ✖ | ✔

## Slide 22: Our Goal
Keep the prefetcher simple, yet get the performance benefits of a sophisticated prefetcher.
To this end, we will design a prefetch-aware warp scheduling policy
A simple prefetching does not improve performance with existing scheduling policies.

## Slide 23
Sophisticated Prefetcher
Simple
Prefetcher
Prefetch Aware (PA) Warp Scheduler
Notes: The goal is to keep the prefetcher simple yet get the performance benefits of a
sophisticated, difficult to design prefetcher.

## Slide 24
W1
W3
W5
W7
Prefetch-aware
Scheduling
Non-consecutive warps are associated with one group
X
X + 1
X + 2
X + 3
Y
Y + 1
Y + 2
Y + 3
Prefetch-aware (PA) warp scheduling
Group 1
W1
W2
W3
W4
W5
W6
W7
W8
Round Robin Scheduling
X
X + 1
X + 2
X + 3
Y
Y + 1
Y + 2
Y + 3
W1
W2
W3
W4
W5
W6
W7
W8
Two-level
Scheduling
Group 2
X
X + 1
X + 2
X + 3
Y
Y + 1
Y + 2
Y + 3
W2
W4
W6
W8
See paper for generalized algorithm of PA scheduler
Notes: In RR, all warps are grouped in a single group.
In TL, first four consecutive warps are grouped into first group, and other four in another
In PA, we group non-consecutive warps in first group, and second group contains the
Remaining warps (as shown). I will explain the reasoning behind this in a second.
The generalized version of this grouping is detailed in the paper.

## Slide 25
Simple Prefetching with PA scheduling
W1
W2
W3
W4
W6
W8
W5
W7
Bank 1
Bank 2
X
X + 1
X + 2
X + 3
Y
Y + 1
Y + 2
Y + 3
X
Simple
Prefetcher
X + 1
Reasoning of non-consecutive warp grouping is that groups can (simple) prefetch for each other
(green warps can prefetch for red warps using simple prefetcher)
Notes: Reasoning of non-consecutive warp grouping is that they can prefetch for each other

## Slide 26
Simple Prefetching with PA scheduling
Bank 1
Bank 2
W1
W2
W3
W4
W6
W8
W5
W7
X + 1
X + 3
Y + 1
Y + 3
Cache Hits!
X
X + 2
Y
Y + 2
X
Simple
Prefetcher
X + 1

## Slide 27
Time
DRAM
Requests
Compute
Phase (1)
D1
D3
D5
D7
D2
D4
D6
D8
Simple Prefetching with PA scheduling
Compute
Phase (1)
Comp. Phase (2)
Comp. Phase (2)
Compute
Phase (1)
DRAM
Requests
D1
D3
D5
D7
Compute
Phase (1)
Comp. Phase (2)
Saved
Cycles
RR
TL
P2
P4
P6
P8
Prefetch Requests
Saved
Cycles
Compute Phase-2 (Group-2) Can Start
Comp. Phase (2)
Saved Cycles!!! (over TL)
(A)
(B)
Notes: So, lets see if prefetching works with the better of two schedulers, Two level scheduler. We have the same setup again, from the
Background. For better visualization, Prefetches are shown together. In reality, they can be interleaved with demand requests.

## Slide 28
DRAM Bandwidth Utilization
Bank 1
Bank 2
W1
W2
W3
W4
W6
W8
W5
W7
X + 1
X + 3
Y + 1
Y + 3
X
X + 2
Y
Y + 2
High Bank-Level Parallelism
High Row Buffer Locality
X
Simple
Prefetcher
X + 1
18% increase in bank-level parallelism
24% decrease in row buffer locality

## Slide 29: Warp Scheduler Perspective (Summary)
Warp Scheduler | Forms Multiple Warp Groups? | Simple Prefetcher Friendly? | DRAM Bandwidth Utilization | 
 |  |  | Bank Level Parallelism | Row Buffer Locality
Round-Robin (RR) | ✖ | ✖ | ✔ | ✔
Two-Level (TL) | ✔ | ✖ | ✖ | ✔
Prefetch-Aware (PA) | ✔ | ✔ | ✔ | ✔ (with prefetching)

## Slide 30: Outline
Proposal
Background and Motivation
Prefetch-aware Scheduling
Evaluation
Conclusions
Notes: Before going into details of why one needs prefetch-aware scheduler, let us understand some background
and limitations of current scheduling polcies

## Slide 31: Evaluation Methodology
Evaluated on GPGPU-Sim, a cycle accurate GPU simulator
Baseline Architecture
  30 SMs, 8 memory controllers, crossbar connected
  1300MHz, SIMT Width = 8, Max. 1024 threads/core
  32 KB L1 data cache, 8 KB Texture and Constant Caches
  L1 Data Cache Prefetcher, GDDR3@1100MHz
Applications Chosen from:
  Mapreduce Applications
  Rodinia – Heterogeneous Applications
  Parboil – Throughput Computing Focused Applications
  NVIDIA CUDA SDK – GPGPU Applications
Notes: We used GPGPU-Sim and details on baseline architecture is listed.
We consider applications from these suites. The evaluated applications
Are those application where multithreading is not enough to hide the long memory latency

## Slide 32: Spatial Locality Detector based Prefetching
MACRO BLOCK | 
X | 
X + 1 | 
X + 2 | 
X + 3 | 
Prefetch:- Not accessed (demanded) Cache Lines
Prefetch-aware Scheduler Improves effectiveness of this simple prefetcher
D
D
D = Demand, P = Prefetch
P
P
See paper for more details

## Slide 33: Improving Prefetching Effectiveness
Chart: 
| RR+Prefetching | TL+Prefetching | PA+Prefetching
Prefetch Accuracy | 0.85 | 0.89 | 0.9
Chart: 
| RR+Prefetching | TL+Prefetching | PA+Prefetching
Late Prefetches | 0.89 | 0.86 | 0.69
Chart: 
| RR+Prefetching | TL+Prefetching | PA+Prefetching
Miss Rate Reduction(%) | 0.02 | 0.04 | 0.16
Fraction of Late Prefetches
Reduction in L1D Miss Rates
Prefetch Accuracy
RR+Prefetching
TL+Prefetching
PA+Prefetching
Notes: In addition to that, our scheme also improves DRAM BLP by 18%

## Slide 34: Performance Evaluation
Chart: 
| SSC | PVC | KMN | SPMV | BFSR | FFT | SCP | BLK | FWT | JPEG | GMEAN
RR+Prefetching | 1.0014 | 0.98298 | 0.98552 | 0.99871 | 1.0184 | 1.0057 | 1.0221 | 1.0065 | 0.98897 | 1.028 | 1.01
TL | 1.0809 | 2.3802 | 1.4702 | 1.0179 | 1.0087 | 0.84951 | 1.0103 | 1.2477 | 1.0674 | 1.0704 | 1.164
TL+Prefetching | 1.0778 | 2.4624 | 1.5457 | 1.0169 | 1.0236 | 0.86786 | 1.0112 | 1.2658 | 1.0757 | 1.1584 | 1.19
Prefetch-aware (PA) | 1.1097 | 2.293 | 1.442 | 1.0317 | 1.0272 | 1.1161 | 0.99763 | 1.27 | 1.0476 | 1.1432 | 1.204
PA+Prefetching | 1.1128 | 2.5437 | 1.6917 | 1.041 | 1.0294 | 1.1468 | 1.0399 | 1.3106 | 1.0901 | 1.1695 | 1.264
1.01
1.16
1.19
1.20
1.26
Results are Normalized to RR scheduling
25% IPC improvement over
  Prefetching + RR Warp Scheduling Policy (Commonly Used)
7% IPC improvement over
  Prefetching + TL Warp Scheduling Policy (Best Previous)
See paper for Additional Results
Notes: This graph shows the IPC improvement normalized to RR scheduling.
The Y axis has all the evaluated benchmarks chosen from various
Application suites described before.
First is when RR + prefetching. We do not expect much improvement
As it doesn’t improve the latency tolerance further.
Second is TL, TL provides signficiant improvement because of
Grouping of warps.
Third is TL+Prefetching, provides on does provide modest improvement
Because some of the prefetches by spatial locality detector based prefetcher
Are timely.
Fourth is PA, which is our propose warp scheduler.
While working alone it does improve Bank level parallelism
But at the cost of row buffer locality. Hence, the performance
is restrained by loss in row buffer locality
Last one is our orchestrated scheduling and prefetching, which not
Only incorporates a simple prefetching for latency tolerance benefits
But also improves the row buffer locality

## Slide 35: Conclusions
Existing warp schedulers in GPGPUs cannot take advantage of simple prefetchers
  Consecutive warps have good spatial locality, and can prefetch well for each other
  But, existing schedulers schedule consecutive warps closeby in time  prefetches are too late
We proposed prefetch-aware (PA) warp scheduling
  Key idea: group consecutive warps into different groups
  Enables a simple prefetcher to be timely since warps in different groups are scheduled at separate times
Evaluations show that PA warp scheduling improves performance over combinations of conventional (RR) and the best previous (TL) warp scheduling and prefetching policies
  Better orchestrates warp scheduling and prefetching decisions
Notes: Existing warp schedulers in GPGPUs cannot take advantage of simple prefetchers
It is because consecutive warps have good spatial locality ….
But problem we saw is that existing scheduler schedule these consecutive warps close by
in time which leads to many late prefetches
-In this regard prefetch aware scheduler. The key idea is to group these consecutive warps
Into different groups so that since groups are scheduled at separate times, prefeteches
Are likely to be late. We also showed that prefetching + PA scheduling can also
Improve DRAM b/w utilization
Evaluations show that PA scheduler can improve performance over many combinations of
Conventional and previously best known schedulers
As a part of future work, we are looking into further better orchestration of warp
Scheduling and prefetching mechanisms.

## Slide 36: Thanks! QUESTIONS?

## Slide 37: BACKUP

## Slide 38: Effect of Prefetch-aware Scheduling
Chart: 
| Two-level | Prefetch-aware
1 miss | 0.3805 | 0.3775
2 misses | 0.2617 | 0.4545
3-4 misses | 0.3578 | 0.168
Chart: 
| Two-level | Prefetch-aware
1 miss | 0.08052 | 0.11598
2 misses | 0.36632 | 0.51582
3-4 misses | 0.55316 | 0.36819
Percentage of DRAM requests (averaged over group) with:
to a macro-block
High Spatial Locality Requests
Recovered by Prefetching
High Spatial Locality Requests

## Slide 39: Working (With Two-Level Scheduling)
MACRO BLOCK | 
X | 
X + 1 | 
X + 2 | 
X + 3 | 
MACRO BLOCK | 
Y | 
Y + 1 | 
Y + 2 | 
Y + 3 | 
D
D
D
D
D
D
D
D
High Spatial Locality Requests

## Slide 40: Working (With Prefetch-Aware Scheduling)
MACRO BLOCK | 
X | 
X + 1 | 
X + 2 | 
X + 3 | 
MACRO BLOCK | 
Y | 
Y + 1 | 
Y + 2 | 
Y + 3 | 
D
D
D
D
P
P
P
P
High Spatial Locality Requests

## Slide 41
MACRO BLOCK | 
X | 
X + 1 | 
X + 2 | 
X + 3 | 
MACRO BLOCK | 
Y | 
Y + 1 | 
Y + 2 | 
Y + 3 | 
Cache
Hits
D
D
D
D
Working (With Prefetch-Aware Scheduling)

## Slide 42: Effect on Row Buffer locality
Chart: Row Buffer Locality
| SSC | PVC | KMN | SPMV | BFSR | FFT | SCP | BLK | FWT | JPEG | AVG
TL | 5.1731 | 9.0467 | 8.1748 | 2.1866 | 1.6282 | 6.4418 | 4.1725 | 4.2649 | 7.9394 | 5.683 | 5.4711
TL+Prefetching | 5.3589 | 9.9494 | 8.6953 | 4.8278 | 1.7434 | 6.3928 | 5.9514 | 4.6542 | 8.2943 | 4.9485 | 6.0816
PA | 4.7089 | 6.1649 | 7.6516 | 1.8937 | 1.5941 | 3.5801 | 3.1464 | 2.5149 | 5.9162 | 4.2995 | 4.147
PA+Prefetching | 4.7798 | 8.4123 | 8.1366 | 4.4695 | 1.7084 | 3.834 | 4.0925 | 4.0423 | 6.5059 | 4.94 | 5.0921
24% decrease in row buffer locality over TL

## Slide 43: Effect on Bank-Level Parallelism
Chart: Bank Level Parallelism
| SSC | PVC | KMN | SPMV | BFSR | FFT | SCP | BLK | FWT | JPEG | AVG
RR | 5.3149 | 4.9642 | 15.3531 | 4.9824 | 10.8957 | 7.858 | 9.9656 | 8.2509 | 15.9868 | 4.9167 | 8.8488
TL | 5.2422 | 3.1456 | 16.2947 | 4.4627 | 9.6429 | 5.9386 | 9.3484 | 7.6965 | 15.5669 | 4.6651 | 8.2004
PA | 5.6991 | 5.1051 | 19.9972 | 4.8695 | 10.5728 | 9.3654 | 10.2727 | 9.1487 | 17.2408 | 5.1579 | 9.7429
18% increase in bank-level parallelism over TL

## Slide 44
Bank 1
Bank 2
Bank 1
Bank 2
Memory Addresses
Simple Prefetching + RR scheduling
X
X + 1
X + 2
X + 3
Y
Y + 1
Y + 2
Y + 3
W1
W2
W3
W4
W5
W6
W7
W8
W1
W2
W3
W4
W5
W6
W7
W8

## Slide 45
Bank 1
Bank 2
X
Bank 1
Bank 2
X + 1
X + 2
X + 3
Y
Y + 1
Y + 2
Y + 3
Memory Addresses
Idle for a period
Idle for a period
Simple Prefetching with TL scheduling
Group 1
Group 2
Legend
W1
W2
W3
W4
W5
W6
W7
W8
W1
W2
W3
W4
W5
W6
W7
W8

## Slide 46: CTA-Assignment Policy (Example)
Warp Scheduler
ALUs
L1 Caches
Warp Scheduler
ALUs
L1 Caches
Multi-threaded CUDA Kernel
SIMT Core-1
SIMT Core-2
CTA-1
CTA-2
CTA-3
CTA-4
CTA-3
CTA-4
CTA-1
CTA-2
Notes: Lets us understand how these thread blocks / CTAs are assigned on multiple SIMT cores on a GPU.
A CUDA kernel, which consists of multiple CTAs is shown.